## Slide 1: Multi-objective River Management (MRM)
Name: Anna Murgatroyd
Date: May 2020
The Transformation by Innovation in Distance Education (TIDE) project is enhancing distance learning in Myanmar by building the capacity of Higher Education staff and students, enhancing programmes of study, and strengthening systems that support Higher Educational Institutions in Myanmar. TIDE is part of the UK-Aid-funded Strategic Partnerships for Higher Education Innovation and Reform (SPHEIR) programme(www.spheir.org.uk). SPHEIR is managed on behalf of FCDO by a consortium led by the British Council that includes PwC and Universities UK International. The TIDE project will close in May 2021.

## Slide 2: Anna Murgatroyd
BA Geography
PhD Climate Adaptation and Water Management
4+ Years Academic Research
Assistant in Flood Management Research

## Slide 3: Part 1: Water Resources

## Slide 4
97% Salt Water
68.7% Glaciers and Ice
31% Groundwater
0.3% Surface Water
3% Fresh Water
"Fishing" (Public Domain) by Pixabay.com - Free Public Domain Images
"Oriental Smallclawed Otter" (CC BY-SA 2.0) by suneko
"duck" (CC BY-NC-ND 2.0) by Pimthida
"Night Rainbow" (CC BY-NC-ND 2.0) by judhi

## Slide 5
Resources We Seek to Consume
Why do we Consume?
Health
Happiness
Reproduction
Critical Questions
Which resources are renewable?
Which resources do we deplete faster then they are renewed?
Do the renewable resources degrade?
Water Rivers Lakes Groundwater | Energy Fossil Fuels Biomass (plants) Hydropower Generation Wind/Solar
Food Plants Animals | Minerals Metals Industrial Materials

## Slide 6
Environmental Conditions
Environmental Conditions
Environmental Conditions
Environmental Conditions
Economic Development
Public Welfare
Political Stability
Why Resource Consumption?

## Slide 7
Simple Water Cycle
Evapo-transpiration
Precipitation
Runoff
Public Domain - NASA

## Slide 8
Public Domain - John Evans and Howard Periman, USGS
More Complex Water Cycle

## Slide 9: Water Supply Water Demand
(CC BY-SA 4.0) by Kantabon
(CC BY-SA 3.0 de) By Stefan Brending, Lizenz:
"The Rice Fields of Inle Lake"
(CC BY-NC 2.0 by virtualwayfarer
(CC BY-NC-ND 2.0) by Aaron T. Goodman
"Fresh caught fish"
(CC BY-ND 2.0) by rainy city
Groundwater
Surface water

## Slide 10: Too Much, Too Little
"Southern Africa drought - Mozambique" (CC BY-NC-ND 2.0) by IFRC
"Flooded Road" (CC BY-NC 2.0) by onbangladesh

## Slide 11
Colorado
Nile
Irrawaddy

## Slide 12
Planetary Boundaries:
An assessment of major global impacts
Is Freshwater Scarce?
Globally? – No
Regionally? – Sometimes
Rockstrom et. al 2009

## Slide 14
Baseline water stress measures the ratio of total annual water withdrawals to total available annual renewable supply, accounting for upstream consumptive use. Higher values indicate more competition among users.

## Slide 15
Physical risks related to water quantity identify areas of concern (e.g. droughts or floods) that may impact short or long term water availability.

## Slide 16
Physical risks related to water quality identify areas of concern that may impact short or long term water availability.

## Slide 17: But what about competing uses?
Agriculture
Energy Production
Public Health / Hygiene
Fisheries
Environmental Conditions
Recreation / Tourism
Cultural Value
Intrinsic / Aesthetic Value
1
2
3
6
5
4
7
8
Assigned Priorities?
(CC BY-SA 4.0) by Kantabon
(CC BY-SA 3.0 de) By Stefan Brending, Lizenz:
"The Rice Fields of Inle Lake"
(CC BY-NC 2.0 by virtualwayfarer
(CC BY-NC-ND 2.0) by Aaron T. Goodman
"Fresh caught fish"
(CC BY-ND 2.0) by rainy city

## Slide 18
Economic Benefits?
Societal Values?
Legal - Water Rights System?
Political dynamics?
External vs. Internal influences
What determines priorities?
Everything may change with time!

## Slide 19: Water for Agriculture
Flood Irrigation
Sprinkler Irrigation
Drip Irrigation
Low Cost
High Evaporation Losses
Low Maintenance
High Labour
Low Efficiency
High Cost
Medium Evaporation Losses
High Maintenance
Low Labour
Medium Efficiency
High Cost
Low Evaporation Losses
High Maintenance
High Labour
High Efficiency
"Wheat Cultivation" (CC BY 2.0) by eutrophication&hypoxia
"La huerta orgánica" (CC BY 2.0) by Sustainable sanitation
"Spray irrigation of fields, mists, rows"
(CC BY 2.0) by Wonderlane

## Slide 20
Water for Hydropower
CGIAR
Water, Land and Ecosystems

## Slide 21
Is there enough water? When does is flow?
Not just minimum continuous flow requirements
  Minimum flood flow requirements - Wet flood plain
  Maximum dry season flow requirements – Allow natural fish habitat
Fish migration pathways
Water quality standards
Water for Environmental Maintenance
http://www.thelivingriver.org
"Salmon" (CC BY 2.0) by AER Wilmington DE

## Slide 22
Time
Flow
(m3/sec)
Dry Season
Wet Season
Dry Season
Hydrograph – Flows over time
Reduce high flows
Increase Low flows
Increase Low flows
Natural flow pattern
Simple Dammed flow pattern
(CC BY-SA 4.0) by Kantabon
Bad for environment
Bad for dependencies on the environment
Good for energy
Good for transport

## Slide 23
Courtesy Clint Dillard
Courtesy Clint Dillard
How to operate a multi-objective reservoir
  Agricultural
  Energy generation
  Municipal
  Environmental
  Recreational
  Flood control
  Water quality
Question: Who can get the needed water?
Answer: Maybe everyone/some/nobody!
Approach: Explore different reservoir operations
Typical Management Question:
Can you manage many needs together?
"Spray irrigation of fields, mists, rows"
(CC BY 2.0) by Wonderlane
"untitled-167-Edit" (CC BY-NC 2.0) by ccutler
"East Bundaberg ... 29th Jan 2013" (CC BY-NC 2.0) by srv007
(CC BY-SA 4.0) by Kantabon

## Slide 24
Multi-use Reservoir Operation
Engineered Design Flows:
Try to meet human needs and replicate natural flows!
Time
Flow
(m3/sec)
Number of floods reduced
Magnitude of floods reduced
Low flows increased

## Slide 25
Models to Simulate Water Movement
Built using:
An understanding of the physical river
+
An understanding of policies
+
Computers, software and programming logic

## Slide 26
Analyse the possible implications of dam construction
Test various operational policies among stakeholders
Show benefits of cooperation
Create a discussion space to understand both benefits and impacts
Models to Simulate Water Movement

## Slide 27: Keys to Sustainable Development
Information
Infrastructure
Institutions
Do you have the necessary knowledge?
Can you physically meet the needs of the population?
Can the needs be met by properly managing the resources?

## Slide 28: Part 2. Case Studies

## Slide 29: Colorado River
“Hammersmith Bridge" (londonist.com)
Thames Basin

## Slide 30
Thames River Basin
12,935 square kilometres
+13 million people
Flows 235km
Average of 690 mm rainfall per year: one of the driest parts of the UK
40% water supply from groundwater

## Slide 31
Thames River Basin
12,935 square kilometres
+13 million people
Flows 235km
Average of 690 mm rainfall per year: one of the driest parts of the UK
40% water supply from groundwater

## Slide 32
“Thames Water WRMP2014" (corporate.thameswater.co.uk)

## Slide 33
By 2045 there will be an additional two million people living in the basin.
Less rain when it’s needed most, with more extreme weather events.
Abstractions must be more sustainable i.e. need to balance the water taken for customers with what is left in the environment.
Planning challenges

## Slide 34
“Thames Water WRMP2014" (corporate.thameswater.co.uk)
Supply Augmentation – Add More Water

## Slide 35
15 years to build
Supply 300 Ml/d

## Slide 36
Reduce the amount of water leaking from pipes
Install “smart water meters” to improve customer understanding of water use
Provide water saving advice
Demand Management – Reduce uses
Croydon Guardian (yourlocalguardian.co.uk)
“Smart Meter” (wwtonline.co.uk)

## Slide 37: Colorado River
“Hammersmith Bridge" (londonist.com)
Thames Basin
Water is in short supply!
Maintaining supply demand balance is a major challenge
Cooperation among customers, water companies and policy makers is key
Short term solutions are only temporary
Long term investments are necessary

## Slide 38: Colorado River
"Colorado Recreational River, Utah" (CC BY 2.0) by mypubliclands

## Slide 39
Colorado River Basin
Alpine to Desert to Sea
2 countries
7 USA States
2 Mexico States
40 million people
22 recognized tribes
7 wildlife refuges
11 national parks
5.5 million acres (2.2 m ha)
4,200 MW electrical capacity
Colorado
New Mexico
Wyoming
Utah
Nevada
Arizona
California
Baja California
Sonora
"JuneCO-6548" (CC BY-NC-SA 2.0)
"Colorado Recreational River, Utah" (CC BY 2.0)
"Hoover Dam" (CC BY-SA 2.0)”
"Denver in morning light" (CC BY-NC 2.0)”
"Culver delta hawk 2" (CC BY-NC 2.0)

## Slide 40
1.5 maf
7.5 maf
7.5 maf
1922 – Colorado River Compact
1944 – USA-Mexico Treaty
1964 – Arizona vs. California
Water Allocations
4.4 maf
2.8 maf
0.3 maf
16.5 maf - Total Allocation
7.5 maf – USA Upper Basin
+7.5 maf – USA Lower Basin
+1.5 maf – Mexico

## Slide 42: How much water is available?

## Slide 43: Effects of Dams on the River

## Slide 44: Colorado River Reaches Basin Closure
US Bureau of Reclamation

## Slide 45: Historical Drought Begins
Drought?
Over-consumption?
Climate Change?

## Slide 47: How to Address Future Shortages?
Negotiated Reduction of uses within the United States
Shortage sharing agreements between USA and Mexico
Exploratory “Basin Study” of alternatives
  Possible Future Supplies
  Possible Future Demands
  Solicit Possible Solutions

## Slide 48
Wyoming
Networks of Policy Makers
+
Networks of Lawyers
+
Networks of Modellers
+
Stakeholder
Input
Negotiated Solutions
Negotiated Compromises

## Slide 49
Water sharing between United States
Water sharing between Countries
River management during drought conditions
River management during floods conditions
2007- 2012 Negotiated Agreements Between Parties
U.S Department of the Interior

## Slide 50: Colorado River “Basin Study”
Evaluate Possible Future Supplies
Evaluate Possible Future Demands
Solicit Potential Solutions
Assemble ‘portfolios’ of solutions with possible timelines

## Slide 51
Desalination
Wastewater Reuse
Import Water
Watershed Management
"Carlesbad Desal. Plant" (CC BY 2.0) by vanderhe1
"Moorefield, W.Va. Wastewater Treatment P" (CC BY-NC 2.0) by chesbayprogram
Supply Augmentation – Add More Water
"Tamarisk Trees" (CC BY-NC 2.0) by rocor

## Slide 52
Increase Municipal Efficiency
Increase Agricultural Efficiency
Energy Production Efficiency
Demand Management – Reduce uses
"Shower" (CC BY 2.0) by andrewmalone
"sprinkler" (CC BY-NC-ND 2.0) by OpenThreads
"sprinkler" (CC BY-NC 2.0) by cdn-pix
"Crystal River 3 Nuclear Power Plant" (CC BY-SA 2.0) by GorissM

## Slide 53: Colorado River Conclusions:
The River Is Overused!
Even in wealthy countries, water can be a major challenge
Cooperation among stakeholders is necessary
"Colorado Recreational River, Utah" (CC BY 2.0) by mypubliclands
Environmental Engineering
+
Environmental Policy Solutions
are required to manage the future!

## Slide 54: Part 3: Multi Objective Water Resource Planning

## Slide 55: Hydropower in Myanmar
“Irrawaddy River, Myanmar" by Alamy/ Getty pictures

## Slide 57
What are the main issues?
Who are the main stakeholders?
What are the interests of the stakeholders?
What are the opportunities?
What are the risks?
Who are the decision-makers in the basin?
How can these problems be approached?
What are the alternatives to the Myitsone Dam?
Discussion:
The Myitsone Dam

## Slide 58: Hydropower Sustainability Principles
Whole Basin Planning
Balanced Natural Resource Utilization
Natural Resource Capacity-based Development
Retention of Intact Rivers/Sub-basins

## Slide 59
High - provides an important contribution to basin processes (such as high flows or a large sediment load), and/or has unique natural values for at least two biophysical factors;
Medium - no high conservation value features over a notable area for two biophysical factors, although may contain notable values for a single factor or pockets of such values;
Low - no high conservation value features over a notable area for any biophysical factor, although may contain pockets of high value.
Proposed Approach
Sub-basin “Zoning”

## Slide 60: Water resources game Divide into groups of 4 or 5 people

## Slide 61: Water Supply Water Demand
(CC BY-SA 4.0) by Kantabon
(CC BY-SA 3.0 de) By Stefan Brending, Lizenz:
"The Rice Fields of Inle Lake"
(CC BY-NC 2.0 by virtualwayfarer
(CC BY-NC-ND 2.0) by Aaron T. Goodman
"Fresh caught fish"
(CC BY-ND 2.0) by rainy city
Groundwater
Surface water

## Slide 62
Planning and management game
City
Nature Reserve
Factory
Farming
Needs 10 water units
Needs water 10 units
Needs 15 water units
Needs 10 water units

## Slide 63
Desalination:
  $$$$
  +20
Import water:
  $$
  +10
Reservoir
  $$$
  +15
"Carlesbad Desal. Plant" (CC BY 2.0) by vanderhe1
Supply Augmentation – Add More Water
Increase City Efficiency:
  $$$
  +10 in city
Increase agricultural efficiency:
  $$
  +10 in farm
Increase industry efficiency
  $$$$
  +10 in farm
Demand Management
– Reduce Use
"Shower" (CC BY 2.0) by andrewmalone
"sprinkler" (CC BY-NC 2.0) by cdn-pix

## Slide 64
Questions?
Comments?