## Slide 1: bioenergy & sustainable development
Exploring
Dr Angela Minas, Tyndall Centre for Climate Change Research, The University of Manchester
angelamae.minas@manchester.ac.uk
Notes: mingalaba

## Slide 2: Mingalarpar

## Slide 3: Today’s
agenda

## Slide 4: Learning outcomes
describe the benefits and challenges of achieving sustainable bioenergy systems; and
understand the relevance of developing sustainable bioenergy systems within Myanmar’s context

## Slide 5: Biomass & bioenergy
Session 1a

## Slide 6: Biomass
Biological material such as
Agricultural crops and residues
Forestry crops and residues
Animal residues
Industrial residues
Municipal solid waste
Sewage
Energy produced from the chemical conversion of biomass
Bioenergy can be in form of
  Generated electricity and heat
  Liquid fuels to run vehicles and machines
  Gas to run vehicles and machines, and generate energy (electricity, heat)
Bioenergy
Notes: https://www.powtoon.com/embed/fPaUt89u3th/

## Slide 7: energy crop: Canola
All images are free for non-commercial re-use and/or under Creative Commons Public Domain Licence
feedstock
energy crop: Jatropha
agricultural residue: rice husk
fuelwood
solid waste
animal waste

## Slide 8: Question
Which feedstock is the largest source of bioenergy?

## Slide 9: Shares of global primary bioenergy sources
Source: Chum, H. et al. 2011. IPCC Special Report on Renewable Energy Sources and Climate Change Mitigation, Cambridge University Press. Figure 2.1
Fuelwood is the largest primary bioenergy resource (67%) in the world

## Slide 10: Traditional bioenergy vs Modern bioenergy
Use of feedstock such as fuelwood, charcoal, manure and crop residues for household heating and cooking
Main energy source in low- and middle-income countries in the Global South
Advantages: low technology, available, affordable
Disadvantages: inefficient use, high pollution, often very time intense to source (collecting)
Wikimedia/Wambui Mwangi

## Slide 11: Traditional bioenergy vs Modern bioenergy
Alternative to traditional biomass
Use of modern technologies to convert feedstock from crops and residues to electricity, heat or biofuels and biochemicals
Advantages: more efficient use of resource, less polluting than traditional bioenergy
Disadvantage: high cost compared to traditional uses
Flickr/ILRI

## Slide 12: Different feedstocks use different conversion technologies
Feedstock conversion chain
Source: Bauen, et al. (2009)
Notes: https://hub.globalccsinstitute.com/publications/bioenergy-review/chapter-1-what-bioenergy

## Slide 13: Conversion routes and technologies for modern bioenergy
Thermo-chemical
Combustion (Widely deployed)
Gasification (Early market development)
Pyrolysis
(Early market development)
Mechanical extraction
Transesterification
(Widely deployed)
Bio-chemical
Anaerobic digestion (widely deployed)
Fermentation
(Widely deployed)
Combustion
(Widely deployed)
Gasification
(Early market development)
Anaerobic digestion
(Widely deployed)
Notes: Bio-chemical routes:
Intervention of bacteria or enzymes to break down biomass molecules
Slower pace process compared to thermo-chemical conversion routes
Require less external (heat) energy input
Manages biomass feedstock with higher moisture content (> 50% wt)
Thermo-chemical conversion routes:
Produce a gas (flue gases or high-energy content gases) for direct utilization to generate power and/or heat, or for upgrading into biofuels (advanced bioenergy routes)
Processes with faster pace
Require external heat input
Require biomass with lower moisture content

## Slide 14: Combustion
Burning feedstock in the presence of air
Gas needs to be cleaned before exhausting to atmosphere
Gasification
Burning feedstock in an oxygen-deficient environment (partial oxidation of biomass)
Produces cleaner gas that can be used in turbines, engines and boilers for power or heat generation, or for upgrade into biofuel and biochemicals
Anaerobic digestion
Anaerobic micro-organisms biologically degrade organic waste, in the absence of oxygen
Produces biogas and digestate that can be used as fertiliser
Notes: Pyrolysis:
Thermal decomposition of biomass in the absence of oxygen
Produces a bio-oil (for fast-pyrolysis) and gas and solid charcoal (for slow-pyrolysis)
Promising for conversion of biomass waste into liquid fuel

## Slide 15: Combustion
Can be small or large scale; Can be decentralised or part of the gas grid; Can be low-cost and high-flexible technology
Can be done at micro-scale or large scale; Requires high investment cost
Gasification
Anaerobic digestion
Can be done at small- or medium- scale; Power generation can be decentralised or part of the grid
Source: Chinagate.cn
Source: Husk Power System

## Slide 16: Question
What percentage of global primary energy supply comes from bioenergy?

## Slide 17: Bioenergy makes up 9.4% of the world’s primary energy supply
Fuel share in world total primary energy supply (2015)
Source: IEA (2017)
Notes: https://www.iea.org/publications/freepublications/publication/RenewablesInformation2017Overview.pdf

## Slide 18: 63.7% of renewable energy comes from solid biofuels for traditional bioenergy uses (e.g., use of firewood for heating and cooking)
Product share in world renewable energy supply (2015)
Source: IEA (2017)
Notes: https://www.iea.org/publications/freepublications/publication/RenewablesInformation2017Overview.pdf

## Slide 19
2.3 billion people
continue to use traditional biomass for cooking
(IEA, 2015)
Notes: 2.7 billion people continue to use traditional biomass for cooking and 1.2 billion have no access to electricity (IEA, 2015)
The consensus from research and industry now is that bioenergy has a role to play in achieving sustainable development

## Slide 20
(Souza et al., 2015a; Cushion et al., 2010)
Ensure access to affordable, reliable, sustainable and modern energy for all
Sustainable bioenergy
promotes of efficient uses of biomass
have reduced environmental impacts (e.g., deforestation and land degradation)
reinforces socio-economic and social benefits that could be provided by bioenergy
Notes: Sustainable bioenergy = promotion of efficient uses of biomass and having reduced environmental impacts (e.g., deforestation and land degradation), but also the reinforcement of economic and social benefits that could be provided by bioenergy
Sustainable bioenergy very much aligns with the UN SDG 7 but certainly also have value in terms of climate action, poverty action (especially in rural agricultural communities), achieving sustainability in cities, among others.
Bioenergy sits across agriculture, poverty, environmental management, energy

## Slide 21: Bioenergy in the Global South
Session 1b: Activity

## Slide 22: Global South
refers to nations classified by the World Bank as low- and middle- income that are in Africa, Asia, Latin America and the Caribbean
the term is not geographically accurate nor does it truly reflect the state of development among countries in the region
Mitlin and Satterthwaite, 2013
Notes: For the purpose of this presentation

## Slide 23
NASA Climate Projection, 2015 (global temperature change by 2100); UNDP, 2008
Asia
Africa
Latin America and the Carribean

## Slide 24
70% of world’s poor continue to rely on agriculture for income and employment
(Souza et al., 2015; World Bank, 2016)

## Slide 25
1.1 billion people
have no access to electricity
(IEA, 2017)

## Slide 26: Group activity
Review examples of bioenergy in the Global South, and discuss:
Flickr/Sustainable Sanitation Alliance
What are the benefits or positive aspects of the bioenergy project?
What are the challenges or issues that were identified (and how were they solved)?
What factors should be considered to make bioenergy sustainable?

## Slide 27
Trade-offs and synergies in bioenergy development (Souza et al., 2015)

## Slide 28: Examples of bioenergy sustainability indicators
Infrastructure development
Land ownership
Local income
Employment
Training workforce
Price & supply of food
Value added to resources
Competition for biomass resource
Water use & water quality
Land use & land-use change
Changes in fossil fuel use
Source: Global Bioenergy Partnership

## Slide 29: activity wrap-up

## Slide 30
Advantages
Partnerships
Biomass feedstock easily available
Low-cost
Potential income
Energy can support agriculture and education
Challenges
Cost and payment might be expensive
Lack of information
Issues of trust
Meeting the demand for electricity

## Slide 31
Maintenance might be difficult
Not easy to construct
Lack of training
Sustainability factors
Government support
Community involvement
Outputs of conversion can be used for other purposes
Company supports local activities
Capacity building and training

## Slide 32: Challenges in sustainable bioenergy
Provide social and economic benefits, alongside energy access
Encourage community ownership and participation
Integrate social and cultural considerations in deployment
Raise awareness and educate locals about the project
Have supportive policies, enabling institutions, financial mechanisms
Build trust between locals and technology developers

## Slide 33: Considerations in sustainable bioenergy
Open communication and consultation
Locals have access to information and financial resources
Stakeholders are in a form of partnership
Local institutions and actors have roles and responsibilities
Technology developers and funders take into account needs and wants of end-users, and understand socio-cultural context

## Slide 34: Benefits of bioenergy systems
Globally large resources of biomass feedstocks
Can fit in existing energy/fuel supply infrastructure
Is very flexible as a large variety of feedstocks can be used for a large variety of applications (electricity, heat, fuels, chemicals)
Provides energy even if the sun doesn’t shine, the wind doesn’t blow
Alternative fuel to fossil fuels – potentially reducing emissions from energy, transport
Helps reducing/manage waste

## Slide 35: Benefits of bioenergy systems
Deals with residues and wastes – instead of landfill, and open-field burning
Can be stored efficiently in form of feedstocks
Provides energy, especially to provide a baseload
Improves energy security
Creates resilience, income and jobs in related sectors like agricultural and forestry, waste management

## Slide 36: Challenges of bioenergy systems
Biomass resources are not necessarily in the place where energy is required
Sourcing much more scattered than e.g. coal, oil
Less energy dense than fossil fuels – larger amounts are required with effect on logistics (transport, handling, storage) and land requirement to produce it
Often more expensive than fossil fuels
High risk of unsustainable sourcing and deforestation
Majority of global biomass is used with inefficient technologies
Non-uniform/inconsistent feedstock
Health impacts mainly when using traditional applications