## Slide 1: Practical Workshop
Dr. Cecilia Medupin & Professor Amanda Bamford
© C. Medupin
© A. Bamford
By Marc Veraart - Myanmar Inle Lake, CC BY 2.0
Aquascience: Assessing the health of rivers and lakes

## Slide 2: Objectives of the practical workshop
By end of workshop you should be able to …….
take water and biological samples in the field from rivers and lakes
measure physical/chemical parameters of rivers and lakes
assess the biodiversity of rivers and lakes (benthic invertebrates, phytoplankton & zooplankton)
collate the data and record results in workbook
Then finally……interpret the results and come to a conclusion!

## Slide 3: Methodology & Approach
Activity 1: Field work (mornings) visit to sample sites
  Collection of samples
Activity 2: In the Laboratory (afternoons)
  Sorting of samples, nutrient analysis & record data
Final session: Discussion of class results & conclusions

## Slide 4: Activity 1: Fieldwork

## Slide 5: River Biomonitoring
Collect benthic macroinvertebrates with 3 minute kick samples
https://www.nhbs.com/professional-hand-net-with-wooden-handle-250mm-wide
© A. Bamford

## Slide 6
Dr. Medupin demonstrating kick sampling
Video copyright A.Bamford & C. Medupin

## Slide 7: Lake Biomonitoring
https://www.nhbs.com/plankton-net-250mm-frame-32mm-filter
Phytoplankton net (50µm) and Zooplankton net (250µm)
Collect 3 x 1 litre water samples to take back to lab.
http://www.benzermultitech.com/distilled-water.html
http://www.elkaylabs.com/30ml-universal-container-with-cap-unlabelled-sterile-ps-pr-811.php
© A. Bamford

## Slide 8: Physical & chemical monitoring
1. Measure in situ……pH, temperature and electrical conductivity
2. Collect 3 x 1litre water samples to take back to lab.
© C. Medupin
https://www.hydroponics.eu/digital-meter-hanna-instruments-phec-c-mod-combo-waterproof-~1112.html
https://www.ysi.com/proplus

## Slide 9: Activity 2: In the Laboratory

## Slide 10: Sorting & Identification Benthic macroinvertebrates
http://www.visio-tek.net/public/files/16-VISIO-S.pdf
© C. medupin
© A. Bamford
Sarah Greenwood, CC BY-SA 4.0
© C. Medupin

## Slide 11: Identification of lake organisms- Phytoplankton & zooplankton
Dieter Ebert, Basel, Switzerland, CC BY-SA 4.0

## Slide 12: Nutrient analyses
Vacuum pump with 0.45µm filter
https://reefbuilders.com/2017/04/25/water-testing-nitrates-phosphates/
Nutrient testing kits for phosphate and nitrates/ion electrodes
https://www.stellarscientific.com/vacuum-filtration-unit-250ml-pes-with-45um-filter-individually-wrapped-sterile-12-cs/

## Slide 13: Collation of results - Discussion & Conclusion

## Slide 15: Thanks for listening!