## Slide 1
Flood Management in Myanmar MOOC
Module 2 Lecture

## Slide 2: Lecture 2: Flood Risk Warnings & Modelling
This lecture will cover the following topics:
  What are flood risk warning systems?
  How can flood risks be assessed?
  Introduction to flood risk modelling – techniques & tools

## Slide 3: What are flood risk warning systems?

## Slide 4
What is a flood warning system?
Image – On May 14 2013 – US Navy Joint Typhoon Warning Center (JTWC) captures this natural-color image of Typhoon Mahasen – within 48 hours – high wind speeds expected to increase to 70 knots; warning forecast map showed Mahasen would hit Bangladesh, northeastern India and Myanmar on May 17!
Ahead of storm – government authorities ordered mass evacuations of low-lying areas, 12,000 people living in flood-prone areas were vulnerable – particularly for people living in refugee camps in western Myanmar.
Notes: Source of image: http://earthobservatory.nasa.gov/NaturalHazards/view.php?id=81125 (from creative commons wiki – https://commons.wikimedia.org/wiki/File:Mahasen_2013-05-14_0535Z.jpg)
Source of text in first bullet: http://earthobservatory.nasa.gov/NaturalHazards/view.php?id=81125

## Slide 5
What is a flood warning system?
Early warning systems for floods are one of the first critical tools for flood risk management (Required Reading 1 – UNDHI Water Adaptation Technology Brief)
Main purpose of a flood early warning system: issue warnings when a flood is about to occur or is already occurring
Flood early warning systems have 4 inter-connected components:
  Assessments, data gathering on rainfall levels, knowledge of flood risks in the area
  Local hazard monitoring (forecasts) and a warning service
  Flood risk dissemination and communication service
  Community response capabilities
Why important:
  Improves community preparedness for extreme weather events such as floods – saves lives & minimizes loss of infrastructure and assets!
  Increased understanding of risks and appropriate flood responses
Notes: Source of text: https://www.ctc-n.org/sites/www.ctc-n.org/files/resources/early_warning_systems_for_floods_0.pdf

## Slide 6
Core Elements to Implement a Flood Early Warning System
Risk knowledge: establish a system/agreement to collect and share data, figures, maps, etc on flood risks and vulnerability in the area (Required Reading 2 – UNISDR (2006) - Developing Early Warning Systems – A Checklist)
Monitoring & warning service: design and implement sensors or related equipment for measuring water levels at selected hotspots in local water courses and vulnerable water infrastructure and link to local database; accurate and timely data is crucial.
Dissemination and communication: dissemination roles and responsibilities should be clear (the core govt, civil society, private sector, community institutions and agencies involved); technologies for sharing information quickly to multiple groups in multiple locations will need to be developed or upgraded.
Response capability: Education – reaching out to related stakeholders by means of training centres and information kiosks – to improve the community disaster preparedness is important!
Notes: Source of text: https://www.unisdr.org/2006/ppew/info-resources/ewc3/checklist/English.pdf

## Slide 7
Data Communication in Flood Management: Case Study Bago River Basin
Flood-prone Bago River Basin had severe floods in 2011 and 2015
Events revealed the need for the improvement of disaster responses for risk reduction
In order to develop efficient decision-making, study finds that (Source: Required Reading 3 – Shirai et al., (2018))
  Myanmar government needs to strengthen the data observation networks
  Strengthen the design of communication scheme for flood hazard warning among all stakeholders
Data communication:
  Not only needed in emergencies but also normal situations
  Important for daily monitoring of status of rivers and river management facilities
  Researchers suggest the need for stakeholders to understand the trends of hydrological and hydrological phenomena so that these trends are reflected in the design of water management plans.
  Research aimed to propose data communication scheme that enables stakeholders to receive data tailored to each agency individually – details in Module 3 Lecture

## Slide 8: Flood Hazard & Flood Risk Maps

## Slide 9: What is Flood Hazard Map?
One of the methods to prevent and reduce losses from floods and other water-related disasters is to provide reliable information to citizens about flood risk – this is best done using a flood inundation map (Source Required Reading 4 – Zin Win et al., (2015)
Flood hazard mapping is an effective non-structural measure for sustainable urban planning, protecting humans, property, and core component of disaster risk reduction.
Zin win et al., (2015) Case study – researchers develop a flood inundation map of the Bago river basin – by coupling a hydrological and hydraulic model with Geographical Information Systems (GIS)
Image shows example of multi-hazard map of Indian state of Kerala: "W/C" = Wind/Cyclone, "E" = Earthquake, "F" = Flood, "H" = High risk, "L" = Low risk, "M" = Medium risk.
Notes: Source of image: https://commons.wikimedia.org/wiki/File:Kerala_India_multi_hazard_zones_map.PNG#/media/File:Kerala_India_multi_hazard_zones_map.PNG

## Slide 10: Flood Modeling
Flood modeling is made up of two components (source Zin Win et al. (2015):
  Hydrological simulation – quantifies the size, duration, and probability of the flood event
  Hydraulic simulation – using the propagation of the flood wave across the river channel and mapping of inundated areas
Hydrological simulation is performed through a rainfall–runoff model that quantifies flood peak dis- charges or a flow hydrograph in the given return period.
Hydraulic analysis conducted using a one- dimensional hydraulic model in a steady state condition or an unsteady one-dimensional or two-dimensional flood routing algorithm for the accurate spatially distributed evaluation of flow and velocity dynamics (Zin Win et al., (2015))
Notes: Source of image: https://commons.wikimedia.org/wiki/File:Kerala_India_multi_hazard_zones_map.PNG#/media/File:Kerala_India_multi_hazard_zones_map.PNG

## Slide 11: Flood Risk Modelling
Tools and Techniques

## Slide 12: Why is modelling important?
Under flood risk management – ability to predict flood hazard and risk under internal (landuse) and climate scenarios plays an important role in flood risk management (Source Required Reading 5 – Ngo et al., (2018))
Previously – in flood risk management – there was a need for developing detailed flood models – conducting several flood simulation exercises - this basically ignored the uncertainty of parameters
Probabilistic forecasts – requirement for quantitative flood risk assessments – aid urban planners and decision-makers – to develop informed risk reduction strategies – saves lives! (source Ngo et al., (2018))
Hydraulic models simulate river flow and flooding – needed to estimate water level changes – under future scenarios
Notes: Source of image: <a data-flickr-embed="true" href="https://www.flickr.com/photos/nasaearthobservatory/6750278049/in/photolist-c64qV5-bhuWui-dMLUHX-H3323R-RauRDh-x5A2Zd-wNHTms" title="Tsunami Damage near Ishinomaki, Japan"><img src="https://farm8.staticflickr.com/7010/6750278049_5f9884e7c2_b.jpg" width="720" height="480" alt="Tsunami Damage near Ishinomaki, Japan"></a><script async src="//embedr.flickr.com/assets/client-code.js" charset="utf-8"></script>

## Slide 13: Why is modelling important?
Examples of hydrodynamic models developed to address complex real-world hydraulic problems including flood forecasting: MIKE11, MIKEFLOOD, ISIS, HEC-RAS, SOBEK, LISFLOOD-FP, Delft 3D
Probabilistic flood forecasting requires flood models – simple and fast – fit-for-purpose by being fast in execution – involves running thousands of realizations of the model for a given scenario
Notes: Source of image: <a data-flickr-embed="true" href="https://www.flickr.com/photos/nasaearthobservatory/6750278049/in/photolist-c64qV5-bhuWui-dMLUHX-H3323R-RauRDh-x5A2Zd-wNHTms" title="Tsunami Damage near Ishinomaki, Japan"><img src="https://farm8.staticflickr.com/7010/6750278049_5f9884e7c2_b.jpg" width="720" height="480" alt="Tsunami Damage near Ishinomaki, Japan"></a><script async src="//embedr.flickr.com/assets/client-code.js" charset="utf-8"></script>

## Slide 14: Why is modelling important?
Ngo et al. (2018) used daily upstream flow data and hourly downstream sea level in 2000 for the Mekong River Delta -
This study shows that it is possible to simulate river water levels – with acceptable levels of accuracy in a deltaic river system like the lower Mekong in Vietnam
Simple SWMM model developed to simulate drainage/ sewerage system – was achieved by simplifying a complex hydraulic model
Objective is to use it for probabilistic flood simulations and for stakeholder based co-design applications – this model is feasible solution for low cost applications and can be run in an hour (compared to hours for traditional models
Notes: Source of image: <a data-flickr-embed="true" href="https://www.flickr.com/photos/nasaearthobservatory/6750278049/in/photolist-c64qV5-bhuWui-dMLUHX-H3323R-RauRDh-x5A2Zd-wNHTms" title="Tsunami Damage near Ishinomaki, Japan"><img src="https://farm8.staticflickr.com/7010/6750278049_5f9884e7c2_b.jpg" width="720" height="480" alt="Tsunami Damage near Ishinomaki, Japan"></a><script async src="//embedr.flickr.com/assets/client-code.js" charset="utf-8"></script>

## Slide 15: Next Module: Flood Risk Management Techniques in Myanmar