## Slide 1
LECTURE 5 BASE YEAR RECONSTRUCTION using the INDUSTRY SECTOR EXAMPLE
Version 2.0
Model for Analysis of Energy Demand
Notes: Lecture 7: the sectors.

## Slide 2: Intended Learning Outcomes (ILOs)
5.1 Industry Sector and its sub-sectors
5.2 Base Year Reconstruction (1/3) – Collection of Raw Data
5.3 Base Year Reconstruction (2/3) - MAED Input Data calculation for the base year
5.4 Base Year Reconstruction (3/3): Run, Results, Check for Accuracy
2
This lecture has four Intended Learning Outcomes (ILOs):
ILO1: learn about the industry sector and its subsectors
ILO2: learn how to collect the raw data needed for the base year reconstruction
ILO3: learn how to calculate the MAED input data for the base year
ILO4: learn how to check that the Base year was successfully reconstructed.
Notes: This lecture has four Intended Learner Outcomes:
ILO1: learn about the industry sector and its subsectors
ILO2: learn how to collect the raw data needed for the base year reconstruction
ILO3: learn how to calculate the MAED input data for the base year
ILO4: learn how to check that the Base year was successfully reconstructed.

## Slide 3
3
Lecture 5.1 End-use categories
Sectors
Subsectors
End-use
Category of Final Energy Demand (FED)
Motor Fuels
Modern Biomass
Fossil Fuels
Electricity
Traditional Fuels
Solar Thermal
Industry
Transport
Service
Household
Manufacturing
Construction
Mining
Agriculture
Motive power: Conveyer, drilling, etc.
Thermal use: Vapor, water heat, etc.
Specific use of electricity, Appliances , etc.
            5.1.1. The Industry Sector, Subsectors, End-use and Final Energy Demands
Notes: In MAED, the structure of the final energy consumption of the country is broken down in a consistent manner, dividing the consumption into 4 major consuming sectors: industry, service, household, and transport. We will now look more in detail into the Industry sector and its four subsectors: Agriculture, Construction, Mining and Manufacturing.

## Slide 4
4
Lecture 5.1 Base Year Reconstruction (1/3)
            5.1.2. Base year selection and reconstruction
Calculate MAED Input Data for the base year
Check accuracy of MAED results for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
1. Base year reconstruction
2. Scenario development
3. Results Analysis
            The base year must be selected from a most recent year in the past for which energy and economic statistics are available, reliable, and consistent.
            The base year should represent stable conditions of energy consumption.
            Unusual situations should prevent a year from being selected.
Notes: As was already pointed out, the value of specific energy consumption for the base year is a crucial parameter for estimation of the future energy demand. This makes the selection of the base year a very important issue.
There are several criteria for the selection of the base year. Firstly, the base year should be selected as the most recent year for which energy and economic statistics are available, reliable, and consistent. Secondly, the base year should be selected to represent stable conditions of energy consumption. Finally, If unusual situations like an economic crisis, extreme climatic conditions, or a political crisis occurred during a given year, it should not be selected as a baseline and a previous year should be used.
To reconstruct the base year, an iterative process is adopted. First, statistical data on energy consumption by sectors, by end-use, and by fuels for the selected base year should be gathered. Then, MAED input data for the base year are calculated on the basis of this information. The MAED model is in turn run with this input data. The MAED results are compared with statistical values for that year. In case of discrepancy, the procedure should be repeated, with adjusted MAED parameters.
The objective of this phase is to establish a benchmark and to validate the programme for the energy system of the specific country.

## Slide 5
5
Lecture 5.1 Base Year Reconstruction (1/3)
            5.1.3. Base year reconstruction
Calculate MAED Input Data for the base year
Check accuracy of MAED results for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
1. Base year reconstruction
2. Scenario development
3. Results Analysis
            The base year must be selected from a most recent year in the past for which energy and economic statistics are available, reliable, and consistent.
            The base year should represent stable conditions of energy consumption.
            Unusual situations should prevent a year from being selected.
Notes: To reconstruct the base year, an iterative process is adopted. First, statistical data on energy consumption by sectors, by end-use, and by fuels for the selected base year should be gathered. Then, MAED input data for the base year are calculated on the basis of this information. The MAED model is in turn run with this input data. The MAED results are compared with statistical values for that year. In case of discrepancy, the procedure should be repeated, with adjusted MAED parameters.
The objective of this phase is to establish a benchmark and to validate the programme for the energy system of the specific country.

## Slide 6
6
Lecture 5.1 Base Year Reconstruction (1/3)
            5.1.4. Gather MAED Parameters for the Base Year
Calculate MAED Input Data for the base year
Check accuracy of MAED results for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
1. Base year reconstruction
2. Scenario development
3. Results Analysis
            To reconstruct the Base Year we need to gather the following data:
            Final Energy Demand/Consumption (FED) by sectors, by end-use, and by fuels for the selected base year
            Thermodynamic Energy Efficiency ( of the process/of the equipment used.
            Driving Parameter (DP) for each end-use (i.e. industry, transport, service, and household uses)
Notes:             To reconstruct the Base Year we need to gather the following data:
            Final Energy Demand/Consumption (FED) by sectors, by end-use, and by fuels for the selected base year
            Thermodynamic Energy Efficiency ( of the process/of the equipment used.
            Driving Parameter (DP) for each end-use (i.e. industry, transport, service, and household uses).
            We have to make sure that units are consistent across MAED. We will see an example later in this lecture.
            To reconstruct the Base Year we need to gather the following data:
            Final Energy Demand/Consumption (FED) by sectors, by end-use, and by fuels for the selected base year
            Thermodynamic Energy Efficiency (𝛈) of the process/of the equipment used.
            Driving Parameter (DP) for each end-use (i.e. industry, transport, service, and household uses).
            We have to make sure that units are consistent across MAED. We will see an example later in this lecture.

## Slide 7
7
Lecture 5.1 Base Year Reconstruction (1/3)
            5.1.5. Gather MAED Parameters for the Base Year - Example
Calculate MAED Input Data for the base year
Check accuracy of MAED results for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
            To reconstruct the Base Year we need to gather the following data:
            Final Energy Demand/Consumption (FED) by sectors, by end-use, and by fuels for the selected base year
            Thermodynamic Energy Efficiency ( of the process/of the equipment used.
            Driving Parameter (DP) for each end-use (i.e. industry, transport, service, and household uses)
Notes:             To reconstruct the Base Year we need to gather the following data:
            Final Energy Demand/Consumption (FED) by sectors, by end-use, and by fuels for the selected base year
            Thermodynamic Energy Efficiency ( of the process/of the equipment used.
            Driving Parameter (DP) for each end-use (i.e. industry, transport, service, and household uses).
            We have to make sure that units are consistent across MAED.
            To reconstruct the Base Year we need to gather the following data:
            Final Energy Demand/Consumption (FED) by sectors, by end-use, and by fuels for the selected base year
            Thermodynamic Energy Efficiency (𝛈) of the process/of the equipment used.
            Driving Parameter (DP) for each end-use (i.e. industry, transport, service, and household uses).
            We have to make sure that units are consistent across MAED.

## Slide 8
8
Lecture 5.2 Base Year Reconstruction (2/3)
            5.2.1. Calculate MAED Input Data for the Base Year
Calculate MAED Input Data for the base year
Check accuracy of MAED results for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
With the Final Energy Consumption data and the Efficiency we calculate the Useful Energy and then the Market Penetration.
The ratio of the Useful Energy and the Driving Parameter will give us the Specified Energy Consumption (or Energy Intensity).
Notes:             To reconstruct the Base Year we need to gather the following data:
            Final Energy Demand/Consumption (FED) by sectors, by end-use, and by fuels for the selected base year
            Thermodynamic Energy Efficiency ( of the process/of the equipment used.
            Driving Parameter (DP) for each end-use (i.e. industry, transport, service, and household uses).
            We have to make sure that units are consistent across MAED.
            To reconstruct the Base Year we need to gather the following data:
            Final Energy Demand/Consumption (FED) by sectors, by end-use, and by fuels for the selected base year
            Thermodynamic Energy Efficiency (𝛈) of the process/of the equipment used.
            Driving Parameter (DP) for each end-use (i.e. industry, transport, service, and household uses).
            We have to make sure that units are consistent across MAED.

## Slide 9: Lecture 5.2 Base Year Reconstruction (2/3)
Calculate MAED Input Data for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
Check accuracy of MAED results for the base year
            5.2.2. Calculate MAED Input Data for the Base Year
9
Notes: To calculate the Useful Energy demand we need to multiply the Efficiencies by the Final Energy Demands.

## Slide 10: Lecture 5.2 Base Year Reconstruction (2/3)
Calculate MAED Input Data for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
Check accuracy of MAED results for the base year
            5.2.3. Calculate MAED Input Data for the Base Year
10
Notes: Once we got the Energy Forms penetration (market penetration) and the Useful energy demand we can calculate the Specified Energy Consumption for each end-use.

## Slide 11: Lecture 5.2 Base Year Reconstruction (2/3)
Calculate MAED Input Data for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
Check accuracy of MAED results for the base year
Agriculture MAED Input Data
We still need to calculate these data
            5.2.4. Calculate MAED Input Data for the Base Year
11

## Slide 12: Lecture 5.2 Base Year Reconstruction (2/3)
Calculate MAED Input Data for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
Check accuracy of MAED results for the base year
Agriculture MAED Input Data
We have calculated percentages of the original data for:
- Penetration of Energy Forms in ACM - Agriculture
- Efficiencies in ACM - Agriculture
The data are now ready to be input in MAED.
            5.2.5. Calculate MAED Input Data for the Base Year
12

## Slide 13: Lecture 5.2 Base Year Reconstruction (2/3)
Calculate MAED Input Data for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
Check accuracy of MAED results for the base year
Agriculture MAED Input Data
Sectoral Shares of GDP for Agriculture
Total GDP
Sectoral Shares of GDP for Agriculture (%)
=
Agriculture Raw Data
10
            5.2.6. Calculate MAED Input Data for the Base Year
13
Notes: Another set of Raw data needed for the reconstruction are the Social Economic Data, in this case for the agriculture sector.

## Slide 14: Lecture 5.3 Base Year Reconstruction (3/3)
            5.3.1. How does MAED calculate the Final Energy Demands for the various energy sources? What happens inside the MAED model?
Where:
Calculate MAED Input Data for the base year
Check accuracy of MAED results for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
14
Notes: We have seen how it works the reconstruction of the base year, which follows an opposite direction of the way in which MAED software operates. MAED goes from the Driving Parameter to the Final Energy Calculations.

## Slide 15: Lecture 5.3 Base Year Reconstruction (3/3)
5.3.2. An illustrative example: from UED to FED
Where:
Coal Furnace
Fossil Fuel
30 %
70 %
Electric
Furnace
Electricity
100 % Process Heat
Calculate MAED Input Data for the base year
Check accuracy of MAED results for the base year
Run the MAED model
Gather/Adjust MAED parameters for the base year
15
Notes: The final energy demand of a specific energy source (the quantity of energy purchased by end users, that reaches the final consumer's door) is given by the product of the inverse of the efficiency of the process where energy is used, the market penetration of the given energy source type, and the final useful energy demand.
In the model, energy demand of the ultimate consumers is calculated in terms of the useful energy wherever possible.
Useful energy demand can be provided either by only one energy form, or by two or more energy forms, according to market penetration. This fact is used in MAED to consider fuel substitutions.
Sometimes various energy forms, for example, electricity and fossil fuels, are competing for a given end-use category of energy demand. This demand is calculated first in terms of useful energy and then converted into final energy, taking into account the penetration into the given market and the efficiency of each alternative energy source. Market penetration and efficiencies are specified as scenario parameters.

## Slide 16: Lecture 5.3 Base Year Reconstruction (3/3)
Gather/Adjust MAED parameters for the base year
Check accuracy of MAED results for the base year
Agriculture Expected MAED Output
We need to check that these numbers from MAED are the same as our raw data for the total final energy demand
            5.3.3. Calculate MAED Input Data for the Base Year
Calculate MAED Input Data for the base year
Run the MAED model
16

## Slide 17: Lecture 5.3 Base Year Reconstruction (3/3)
Gather/Adjust MAED parameters for the base year
Check accuracy of MAED results for the base year
Agriculture reconstruction
First we need to calculate the Total Specific Final Energy Demand, summing up the Final Energy Demand per each end-use
            5.3.4. Calculate MAED Input Data for the Base Year
Calculate MAED Input Data for the base year
Run the MAED model
Then we convert these numbers (by dividing them by 8760) in Gwyr the unit of the MAED output data, and check if they are identical. If so, we have successfully reconstructed the Base Year.
17

## Slide 18
18
Lecture 5.4 Other Industry Sub-sector
Sectors
Subsectors
End-use
Category of Final Energy Demand (FED)
Motor Fuels
Modern Biomass
Fossil Fuels
Electricity
Traditional Fuels
Solar Thermal
Industry
Transport
Service
Household
Manufacturing
Construction
Mining
Agriculture
Motive power: Conveyer, drilling, etc.
Thermal use: Vapor, water heat, etc.
Specific use of electricity, Appliances , etc.
            5.4.1. The Industry Sector, Subsectors, End-use and Final Energy Demands
Notes: As seen before the Industry sector can be further broken down into four subsectors: agriculture, construction, mining and manufacturing. We have covered the Agriculture sub-sector. Let’s now see what needs to be done for the other ones.

## Slide 19: Lecture 5.4 Other Industry Sub-sector
            5.4.2. Construction and Mining Subsectors
In MAED, the Construction and Mining Subsectors follow the same structure of the Agriculture subsector.
Source: https://www.freepik.com/free-photo/construction-site-silhouettes_1243080.htm#query=construction&position=7&from_view=search&track=sph, Image by evening_tao</a> on Freepik.
Source: https://www.freepik.com/free-photo/yellow-excavator-digging-ore-rich-rock-open-pit-mine_17344806.htm#query=mining%20sector&position=34&from_view=search&track=ais, Image by wirestock</a> on Freepik
19

## Slide 20: Lecture 5.4 Other Industry Sub-sector
            5.4.3. Manufacturing Subsector
            As done previously, to reconstruct the Base Year we need to gather the following data:
            Final Energy Demand/Consumption (FED) by sectors, by end-use, and by fuels for the selected base year.
            The Final Energy Demand and the Efficiencies for Thermal Uses are split into three levels to better represent Low, Medium and High Temperature processes.
            Thermodynamic Energy Efficiency ( of the process/of the equipment used.
            Driving Parameter (DP) for each end-use
20
Notes: In the manufacturing subsector, the thermal use of heat can be further divided into low, medium, and high temperature. The driving parameter is still the value added of the subsector.
The specific energy consumption is now the product of the specific energy intensity of the subsector and the share of thermal use at that temperature.

## Slide 21: Lecture 5.4 Other Industry Sub-sector
            5.4.4. Manufacturing Subsector
Additional steps compared to the Agriculture Subsector
21

## Slide 22: Lecture 5.4 Other Industry Sub-sector
            5.4.5. Manufacturing Subsector
Additional steps compared to the Agriculture Subsector
22
Notes: In the manufacturing subsectors we have additional steps compared to the agriculture subsector, namely related to the split of the temperature into three levels.

## Slide 23: Lecture 5.4 Other Industry Sub-sector
            5.4.6. Manufacturing Extras
In the Manufacturing subsector is possible to model both Cogeneration power plants and heat pumps.
Source: https://www.flaticon.com/free-icons/power-plant" title="power plant icons, Power plant icons created by photo3idea_studio - Flaticon</a>.
Source: https://www.freepik.com/free-photo/close-up-heat-pump-outside-home_22118722.htm#query=heat%20pump&position=24&from_view=search&track=ais, Freepik</a>
Electricity (Power)
Steam (Heat)
23

## Slide 24
CCG courses (this will take you to the website link http://www.ClimateCompatibleGrowth.com/teachingmaterials)
24
Cannone, C., Collett, K.A., Charbonnier F., Ahsan A., Halloran C., Vijay,A.,Berdellans I., Hasanovic S., Gritsevskyi A,Stankeviciute L., Tot M.; Welsch M., Hirmer S., 2023. Lecture 5: "BASE YEAR RECONSTRUCTION using the INDUSTRY SECTOR EXAMPLE" , Energy Demands Projections with MAED (Model for Analysis of Energy Demand). Release Version 2.0. [online presentation]. Climate Compatible Growth & Programme and International Atomic Energy Agency.