## Slide 1: LECTURE 3 FOUNDATIONS OF INPUT-OUTPUT ANALYSIS
Input-Output analysis and modelling with MARIO
Supported by and in collaboration with
Politecnico di Milano
by Lorenzo Rinaldi, Nicolò Golinucci, Matteo Vincenzo Rocco and Emanuela Colombo

## Slide 2
By the end of this lecture, you will:
Understand the basics of Input-Output Analysis
Understand the meaning of Leontief Inverse matrix
Define and use basic Input-Output quantity and price models
Understand the fundamental structure of national economic accounts
Learning Outcomes
Please be aware you find supporting files for this lecture on Zenodo at the following link: https://doi.org/10.5281/zenodo.8308515

## Slide 3
3.1 Quantitative Impact Assessment
From the previous lecture…
  Synthesis approach versus systems approach
  Sustainability and impact as property of systems rather than single processes
  Mathematical models of Socio-Economic Metabolism are needed to formulate informed policy decisions
Practical issues
  How to define a common mathematical structure to quantify the impact of products and processes?
  How to set time and space boundaries of the analyzed system?
  How to test if changes in technology lead to an overall environmental impact reduction?

## Slide 4
3.1 Quantitative Impact Assessment
Early development
  End of 1930s: USA Government need for a conversion plan of its industry to a war footing
  Need for estimating the final bill of goods, flows of steel, aluminum, energy, etc. for each industry in upcoming years, required to produce the required war items (airplanes, tanks, guns, …)
  Knowing such quantities essential to plan for adequate investments in capital stocks to expand sectors productive capacities and to avoid lack in supplies
  Direct supplies of goods and services are not enough!
  For any product, a direct, indirect and total demand of inputs can be defined
Tank manufacturing
1 Tank
Energy sector
Steel sector
Services sector
Other inputs
Steel
Energy
Services
Energy sector
Steel sector
Services sector
Steel
Energy
Services
Other inputs
Energy sector
Steel sector
Services sector
Steel
Energy
Services
Other inputs
Supply chains TIERS
1
2
3
…
DIRECT demand
INDIRECT demand
References: [1]

## Slide 5
3.1 Quantitative Impact Assessment
Early development
  W. Leontief set up an analytical approach to quantify the direct + indirect demand of products by each industry to meet wartime demand
  Given a complex productive system, bottom-up calculation of total impact is complex, implying difficulties in defining systems boundaries
  For a given nation, technical features of all industries can be arranged in a matrix shape, mapping the structure of national supply chains.
  Fundamental idea: behavior of the system and its reaction to exogenous shocks can be quantified once the features of its single components (industries) and the linkages among them are known
References: [1]
US economy
Steel industry
Energy industry
Services industry
Steel industry
Energy industry
Services industry
Households’ demand (B$, GDP)
Raw materials (kton) Primary energy (MJ) Workforce (workers) …
War items (B$)
Additional resources requirements

## Slide 6
3.1 Quantitative Impact Assessment
Early development
  Findings: production capacity of major industries were inadequate to satisfy materials and energy demand for war items production, while keeping the current levels of households’ demand satisfied.
  A feasible transition to a wartime economy:
    Massive construction programs to expand industries production capacity (i.e. investments in capital stocks)
    Identification of industries to be converted to production of war items
    Reduction of personal households’ consumptions (rationings)
References: [1]
US economy
Steel industry
Energy industry
Services industry
Steel industry
Energy industry
Services industry
Households’ demand (B$, GDP)
Raw materials (kton) Primary energy (MJ) Workforce (workers) …
War items (B$)
Additional resources requirements

## Slide 7
3.2 Fundamental notation and definitions
Activity
activity that transforms inputs into outputs
synonyms: unit process, process, technology, industry, sector
transforms multiple inputs into one or multiple outputs
represented by a “black box”
Energy (J)
Raw wood (kg)
Furniture (units)
System
collection of processes enclosed within a boundary, and linked by exchanges of inputs and outputs
a system may be composed by a single process
synonyms: product system
Environment
all things outside the boundary of the system (e.g. natural environment, other systems)
it may interact with the system by exchanging flows of inputs and outputs
Environment
System boundary
Services (€)
Labor (h)
Scrap (kg)
Air emissions (kg)
i
Activity
1
2
System
Activity

## Slide 8
3.2 Fundamental notation and definitions
Commodity
any goods or service, inputs or outputs of processes
synonyms: flow, product
quantifiable by physical or monetary units (e.g. kg, Joule, €, …)
represented by arrowed lines
intermediate demand
products exchanged among processes inside system boundaries (also named “intermediate transaction”)
final demand
products delivered as output of the system (also named “useful product” or “functional unit”)
environmental transaction
material or energy inputs/outputs crossing system boundary different from the final demand.
if there are not previous/subsequent human transformations, these are named “elementary flows”, usually represented by dotted line.
Environment
System boundary
1
2
System
Final demand
Environmental transaction
Activity
Intermediate demand
Product classification

## Slide 9
3.2 Fundamental notation and definitions
Total activity production
products may satisfy both intermediate and final demand.
total output equals intermediate and final demands.
synonyms: total output
one production balance can be defined for each activity.
In vector form:
1
2
System
Final demand
Activity
Intermediate demand
Total production of 1
i
Total production of 2
Total production vector
Intermediate transactions matrix
Final demand vector

## Slide 10
3.2 Input-Output Analysis: bottom-up
Assumptions
  Let us consider a simplified productive system S composed by 2 activity: Goods production (G) and Energy production (E)
  G and E produce one unique homogeneous output (goods and energy, respectively)
  Each unit of activity output implies a set of inputs and outputs transactions, assumed as constant
Goods
(G)
Energy
(E)

## Slide 11
3.2 Input-Output Analysis: bottom-up
Questions
  Calculate the total production of Energy and Goods produced by the system in delivering a net amount of 15 tons of goods as final demand
  Calculate the total CO2 emissions caused by the system in delivering the same final demand
Goods
(G)
Energy
(E)

## Slide 12
3.2 Input-Output Analysis: bottom-up
Pen on paper…
  Demand of inputs and emissions caused by 15 tons of goods can be determined in each tier of the supply chain based by analyzing the supply chain in each tier
  Production (Cumulated production) of inputs/outputs
Goods
(G)
Energy
(E)
Goods
(G)
Energy
(E)
Goods
(G)
Tier 2
+0 (15)
+60 (60)
+1200 (1260)
 | Tier 1
Goods [ton] | +15 (15)
Energy [MWh] | +0 (0)
CO2 [ton] | +60 (60)
Tier 3
+6 (21)
+0 (60)
+24 (1284)
Tier 5
+2 (23)
+0 (84)
+9.6 (1774)
Tier 4
+0 (21)
+24 (84)
+480 (1764)
…

## Slide 13
3.2 Input-Output Analysis: bottom-up
Takeaways
  Mathematical complexity. Calculation process is complex and prone to mistakes.
  Physical complexity. Real-life productive systems are much more complex than the two-processes system analyzed:
    Supply chains are usually composed by more than two activities
    Each activity may produce multiple outputs, consume several resources, discharge multiple wastes
    Each activity inputs and outputs per unit of useful product may not be constant
    Selection of system boundaries is ambiguous: it is difficult to understand when contributions in upstream tiers are negligible
  Data mining and activity characterization
    Inputs and outputs per unit of commodity by each activity may be not constant
    Characterization of production activity is complex and labor intensive

## Slide 14
3.2 Input-Output Analysis: bottom-up
The neat way…
  The previous problem can be easily solved by neatly arrange data in a system of linear equations
  The following items are defined:
Technical coefficients matrix
Each column represents the intermediate inputs directly required by the i-th process from all the others to deliver one unit of i-th output.
Final demand vector
Represent the net products delivered out of system’s boundaries by each i-th activity
Total output (total activity)
Overall production by each activity
Exogenous variables
Endogenous variable

## Slide 15
3.2 Input-Output Analysis: bottom-up
The neat way…
  Define total production as a function of technical coefficients and final demand:
  Since intermediate demand is defined per unit of total output, a production balance can be defined as follows:
Total output intermediate demand final demand
Leontief Inverse matrix (or Total requirements matrix)
Leontief quantity model (or “primal” model)
Quantifies the total production of each activity of a system once technical coefficients and final demand are defined
i

## Slide 16
3.2 Input-Output Analysis: bottom-up
The neat way…
  Calculate the total production of Energy and Goods by the system in delivering a net amount of 15 tons of goods as final demand
  Once total production has determined, total intermediate transactions can be also quantified
Bottom-up approach implies cutoff errors!
 | Tier 1
Goods [ton] | +15 (15)
Energy [MWh] | +0 (0)
Tier 5
+2 (23)
+0 (84)

## Slide 17
3.2 Input-Output Analysis: bottom-up
Meaning of the Leontief Inverse matrix (1/2): Technical VS Leontief coefficients
Column: direct inputs invoked by i-th activity to provide one unit of its own of output
Column: total (direct + indirect) inputs invoked by i-th activity to provide one unit of its own net output (final demand)

## Slide 18
3.2 Input-Output Analysis: bottom-up
Meaning of the Leontief Inverse matrix (2/2): the power series expansion
Goods
(G)
Energy
(E)
Goods
(G)
Contributions of upstream tiers converge to the Leontief Inverse matrix!
=

## Slide 19
3.2 Input-Output Analysis: bottom-up
Back to the initial questions:
  Calculate the total CO2 emissions caused by the system in delivering the same final demand
  Once the Leontief quantity model has solved, environmental transactions can be consequently determined
  Given a same productive system, environmental transactions can be seen from two different perspectives:
Production-based accounting
Transactions directly caused by each activity
CO2 emissions directly produced by power plants
Water use of agriculture sector
Energy use by service sector
Consumption-based accounting (CBA)
Transactions embodied in final demand commodity
CO2 emissions embedded in manufactured goods
Virtual water embedded in food products
Energy embodied in services products

## Slide 20
3.2 Input-Output Analysis: bottom-up
Back to the initial questions:
  Calculate the total CO2 emissions caused by the system in delivering the same final demand
Environmental transactions coefficients matrix
Columns represent the direct exogenous transactions with the environment per unit of each i-th activity output.
Production-based accounting (PBA)
Goods
Energy

## Slide 21
3.2 Input-Output Analysis: bottom-up
Back to the initial questions:
  Calculate the total CO2 emissions caused by the system in delivering the same final demand
Environmental transactions coefficients matrix
Columns represent the direct exogenous transactions with the environment per unit of each i-th activity output.
Consumption-based accounting (CBA)
“footprint” of the final demand unit
Goods
Energy
Goods
Energy

## Slide 22
3.2 Input-Output Analysis: bottom-up
Exogenous parameters
Endogenous parameters
Technical coefficients matrix
Environmental transactions coefficients matrix
Leontief coefficients matrix
Final demand vector
Total production (Leontief quantity model)
Total environmental transactions (Production-based account)
Unit Process
Functional Unit
Total environmental transactions (Consumption-based account)
Total intermediate transactions
Perturbation in activity or demand scenarios
Effects of perturbations
Shock analysis

## Slide 23
3.3 Input-Output Analysis: top-down
Top-down approach based on national accounts
  A set of products transactions across technologies in a defined time span is needed
  Such transactions are observed data for a particular area (regions, countries, cluster of countries), separated in different segments (producing sectors)
  Segments are classified based on international standards and with different aggregation levels ( manufacturing, steel manufacturing, nails and spikes) (more on course module 3…)
  Transactions of goods and services between production and consumption sectors are collected considering a defined time frame (1 year)
  Transactions are usually collected in monetary units (but in principle physical units can be used). Advantages and drawbacks?
  Economic accounts are complemented with “environmental extensions”
Country
Production activities
(Industries)
Consumption activities
(Households, govern, trades, …)
Intermediate transactions
Final demand
Environmental transactions
Environment

## Slide 24
3.3 Input-Output Analysis: top-down
National economic accounts for a simple economy with 2 industries
Production activities
Production activities
Consumption activities
Labor
Households
Investments
Govern
Exports
Capital, taxes, …
Imports
For production activities, total output equals total outlays
Gross output of the economy
Deriving value of net output
Row sum
Column sum
Gross national income
Gross national product

## Slide 25
3.3 Input-Output Analysis: top-down
A focus on Value Added
  What “adds” value to intermediate inputs, which would otherwise be just a bunch of unfinished products
  Together with other inputs (e.g., imports) they are known as “factors of production”
  Value (€) of activity production output equals value of intermediate production plus “factors of production”
  Value added is usually disaggregated into 3 main categories:
    Labor compensation: workers provide intrinsic fundamental value to products (design, assembly, …)
    Capital consumption and operational margins: amortization of infrastructure required to support the production process (machinery, buildings, …); deficits or surplus of the economic activity
    Taxes: compensation paid to government to take advantage of public services (streets, other infrastructures)
Production activities
Production activities
Labor
Capital, taxes, …
Imports

## Slide 26
3.3 Input-Output Analysis: top-down
Deriving technical and Value Added coefficients
  Fundamental assumption: in a given time window (say 1 year, ), input flows consumed by a sector depends entirely on the output of such sector. Fixed relationships between sectors inputs and outputs, assumed as constants (hp: constant return to scale)
  Technical coefficients: ratio between i-th inputs to sector j-th, and sector j-th total output.
  Value added coefficients: ratio between factor inputs to sector j-th and sector j-th total output.
Production activities
Production activities
Consumption activities
Technical coefficients
Production activities
Value added
Value added coefficients
Value added

## Slide 27
3.3 Input-Output Analysis: top-down
Environmental transactions coefficients
  National economic accounts may be complemented with “environmental extensions” (also named “satellite accounts”), representing the link between each sector and the environment in terms of emissions and resource uses (in physical units)
  Environmental transactions coefficients: ratio between i-th transactions to sector j-th, and sector j-th total output.
Production activities
Production activities
Consumption activities
Value added
Environmental transactions coefficients
Environmental transactions
Environmental transactions
  Leontief quantity model (primal model): derives prospective changes in total output, value added and environmental transactions if changes in final demand or sectors activity occur.

## Slide 28
3.4 Takeaways, assumptions and limitations
Takeaways
  Once coefficients tables () are derived from national accounts in a given time frame (), Leontief quantity and price models can be defined.
  Once total output is derived, value added and environmental transactions are derived as consequences based on Production-based and Consumption-based paradigms.
  IOA is a general mathematical scheme that can be applied at different scales and based on different approaches:
    Bottom-up: technologies are characterized based on engineering or process-related data, leading to direct definition of coefficients tables
    Top-down: technologies are characterized starting from national accounts, hence quantified based on total transactions in a given time frame.

## Slide 29
3.4 Takeaways, assumptions and limitations
General assumptions and limitations
  Constant return to scale (Input-Output Analysis assumes linearity throughout)
  Supplies of resources and primary inputs fully elastic
  Definition of the final demand fully exogenous and non-reactive to structural change in activity
  Changes in prices indices are just kickstarts: nothing is said about the effects induced by such changes (are products prices really changing? Or such shocks will be absorbed by changing cost of factors (e.g. reducing firms surplus?) What will be the effect on demand?

## Slide 30
Fundamental literature
Hannon B (2012). Early development of Input-Output Analysis of energy and ecologic systems. In Thermodynamics and Destruction of Resources, Cambridge University Press.
Miller R E, Blair P D. (2009). Foundations of Input-Output Analysis. In Input-output analysis: foundations and extensions. Cambridge university press.
Duchin F, Steenge A E (2007). Mathematical models in Input-Output economic. Rensselaer Working Papers in Economics.
Kitzes J (2013). An Introduction to Environmentally-Extended Input-Output Analysis. Resources, MDPI.
Heijungs R, Suh S (2002). The Computational Structure of Life Cycle Assessment. Springer.
Peters G (2007). Efficient algorithms for life cycle assessment, input-output analysis and Monte-Carlo analysis. International Journal of Life Cycle Assessment.
Duchin F, Levine S (2017). Choosing among alternative technologies - conditions for assuring the feasibility of an input-output database or scenario. Economic Systems Research.

## Slide 31
Rinaldi R., Golinucci N., Rocco M. V., Colombo E., 2023. Lecture 3: Input-Output analysis and modelling with MARIO. Release Version 1.0 [online presentation]. Climate Compatible Growth Programme, Politecnico di Milano
Supported by and in collaboration with
Politecnico di Milano
Consolidated by Lorenzo Rinaldi, Nicolò Golinucci, Matteo Vincenzo Rocco and Emanuela Colombo from Politecnico di Milano