## Slide 1: LECTURE 2 COST-BENEFIT ANALYSIS THEORY
Supported by and in collaboration with Sustainable Energy for All. Consolidated by KTH
Geospatial Clean Cooking access modelling using OnStove
by B. Khavari and C. Ramirez

## Slide 2
ILO1: Be able to define Cost-Benefit Analysis (CBA)
ILO2: Be able to list different costs and benefits categories in clean cooking modelling
ILO3: Differentiate between social and private views
ILO4: Explain the different steps needed to conduct a CBA
Learning Outcomes
By the end of this lecture, you will:

## Slide 3
2.1 What is Cost Benefit Analysis (CBA)?
CBA is a policy assessment method that quantifies in monetary terms the value of
all consequences of a policy to all members of society” – Boardman et al. 2018
Net-benefit is defined as benefits minus costs
Time saved
Health impacts
GHG emissions
Investments
Fuel costs
Maintenance
Learning costs
Reduced deforestation
(Boardman et al., 2018)
Notes: When looking at the benefits of clean cooking, there is often a monetary value attached to inaction. For example, in the latest version of the Tracking SDG 7 report it is stated that the cost of inaction in the clean cooking sector amounts to 2.4 trillion USD. This means that the benefits we talked about in presentation 1 (health, reduced time, and the environment) have gotten a monetary amount assigned to it. But how do we go about monetizing improvements with regards to health, time spent and environment?
One way of doing this is applying a CBA. CBA can be defined as a policy assessment method quantifying in monetary terms the value of all consequences of a policy to all members of society. The idea is to identify the benefits and costs of an action (or a lack there of), valuing the impacts of the defined benefits and costs in a monetary value (for example USD) and then determining the net-benefits. Net-benefits would then be defined as the incremental benefits minus the incremental costs in comparison to a benchmark. The benchmark tends to be equated to a situation where no policy changes are applied. The monetary value applied to the benefits and costs can be viewed as a weight indicating the emphasis of different benefits in the net-benefit equation.
The costs and benefits have to be treated slightly differently depending on their characteristics. If the cost or benefit is included in the market, say a cylinder of LPG, market data may be used. If we are dealing with benefits or costs that do not exist in the market, say health impacts or time saved, markets can not be depended on. In these cases we can instead use stated or revealed preferences. A stated preferences is when you ask a respondents, so you could for example ask a respondent how highly he or she values a risk reduction with regards to health. When using revealed preference you assess a persons market transactions or behavior.

## Slide 4
2.1 What is Cost Benefit Analysis (CBA)?
CBA is a policy assessment method that quantifies in monetary terms the value of
all consequences of a policy to all members of society” – Boardman et al. 2018
(Boardman et al., 2018)
Private
Social
vs
Notes: CBA is viewed as a social measure, with the main purpose of identifying the benefits and costs for the wider society. Therefore, it can be a viable tool for policy makers in deciding whether an investment or policy is worth going through with. However, by omitting or altering certain benefits and costs the measure can be modified to apply in the private situation as well. For clean cooking, an example of this could be to remove the environmental benefits from the calculations and take into account only the benefits that are felt directly by the private households themselves, such as health impacts and time savings. This way we exclude externalities that are not directly affecting the private users (households in this case).

## Slide 5
2.1 What is Cost Benefit Analysis (CBA)?
CBA is a policy assessment method that quantifies in monetary terms the value of
all consequences of a policy to all members of society” – Boardman et al. 2018
(Boardman et al., 2018)
Policy implementation
Ex ante:
Is the policy a good idea?
Ex post:
Was the policy a good idea?
Notes: A CBA can also be conducted at different times during a process. Ex ante is when a CBA is conducted before the policy is implemented, answering the question “is the policy change worth it?. Ex post is done after the policy is already implemented, answering the question “was the policy a good idea”. The ex post analysis does not allow for a change in policy, but it can provide information on a specific type of interventions. For long-term projects spanning across long time a third category, “in media res”, can be used. In these cases the CBA is conducted during the project to answer the question of whether it make sense to go forward with a given policy or if it should be aborted.

## Slide 6
Step-by-step to conducting a CBA
Explain the purpose
Identify alternatives
Decide how benefits and costs are counted
Identify impact categories
Predict the impacts during the projects lifetime
Monetize impacts
Discount costs and benefits to present value
Determine net present value of each alternative
Perform a sensitivity analysis
Make a recommendation
(Boardman et al., 2018)
Notes: Boardman in his book summarizes CBA into a workflow of ten-steps. We will briefly look into each of them and what they mean.

## Slide 7
2.2 Step-by-step to conducting a CBA
Why are you doing the project?
Market failures: inefficient distribution of goods and services in the free market
1. Explain the purpose
(Boardman et al., 2018)
Notes: The first step is to identify the purpose of the project. Why are you doing the project? Through the lens of clean cooking you would answer that the transition costs a large amount of money, but that it also brings with it a large number of benefits. We are interested in weighing these against each other. Typically a CBA is a good tool when dealing with market failures. Market failure can be defined as inefficient distribution of goods and services in the free market. When markets work well private interest ensures that the optimal solution is adapted. In other words if markets are working well, there would be no reason for people to use traditional cooking fuels as we know they have negative impact on health, environment and gender equality. When dealing with a market failure it is usually a good idea for the government to intervene in a way that tries to correct the failure. A CBA then helps understanding if the costs of intervening are sensible when compared to the benefits.

## Slide 8
2.2 Step-by-step to conducting a CBA
2. Identify alternatives
(Boardman et al., 2018)
Alternative
Current
Alternative
Current
Alternative
Current
Notes: The second step is to identify alternative projects. In the case clean cooking this can refer to continuing on with traditional cooking rather than transitioning to cleaner or clean options. This is why calculating the incremental benefits and costs that we saw on the previous slide is so important, we are interested in reduced damages rather than an absolute value.

## Slide 9
2.2 Step-by-step to conducting a CBA
3. Decide how benefits and costs are counted (system boundaries)
(Boardman et al., 2018)
Country
Sub-region
Society
Household
or
Notes: The third step is to decide how to calculate the costs and benefits. This relates to how you draw your system boundaries (do you calculate the costs and benefits for your whole country or only a sub-region of it). It also relates to some extent which view of net-benefits you use. From a social perspective a subsidy may be an additional cost (as society has to pay for a decreased price to the consumer), but from a private net-benefit perspective it is a reduction in cost alleviating some of the affordability constraints that may exist.

## Slide 10
2.2 Step-by-step to conducting a CBA
4. Identify impact categories
(Boardman et al., 2018)
HEALTH
CLIMATE & ENVIRONMENT
GENDER & LIVELIHOODS
DEFORESTATION
INVESTMENTS
FUEL COSTS
PROGRAME
COST
LEARNING COST
Notes: The fourth step is to identify impacts and categorize them as either benefits or costs. For clean cooking benefits could be reduced morbidity and mortality, time saved and emissions avoided, while the costs could be investment costs, fuel costs and cost of promoting the new stoves. As mentioned earlier these benefits and costs are always compared to the business-as-usual case. While you want to include as many costs and benefits as possible it is often a trade-off between accuracy and what is manageable (it may be difficult or even impossible to include all benefits and costs).

## Slide 11
2.2 Step-by-step to conducting a CBA
5. Predict the impacts during the projects lifetime
(Boardman et al., 2018)
  Clean stoves emit lower quantities of PM2.5s reducing health impacts
  ICS stoves have better efficiencies than traditional ones reducing fuel consumption
  Transitioning to cleaner stoves reduce wood consumption leading to potential reductions in deforestation
  Cleaner stoves reduce time needed for cooking and collecting fuels
  Cleaner stoves reduce greenhouse gases emitted to the atmosphere
Notes: In the fifth step we predict the impacts of the policy change during the lifetime of the project. If the goal of the cooking transition is to improve health, environment and gender issues, this step would include calculating reduced number of cases and death, reduced greenhouse gases and time saved cooking and collecting fuels. In order to do this it is important to understand the cause and effect relationships connected to the cooking transition. In other words it is important to understand why cleaner cooking solutions save time (higher efficiencies and lower (or no) cooking times) etc.

## Slide 12
2.2 Step-by-step to conducting a CBA
6. Monetize impacts
(Boardman et al., 2018)
  Costs of loosing a live
  Costs of a disease
  Cost of GHG emissions
  Cost of deforestation
  Opportunity cost (time spent cooking and collecting fuels)
Notes: After determining the impacts they are monetized which is done by assigning a dollar amount to each impact. Some benefits are controversial to assign value to. For example how do you value avoided deaths due to household air pollution? The values that are used in a cost-benefit analysis should not be seen as an actual valuation, but rather as a willingness to pay for said benefit. We will discuss this more at a later point

## Slide 13
2.2 Step-by-step to conducting a CBA
7. Discount costs and benefits to present value
(Boardman et al., 2018)
Notes: Next all benefits and costs are discounted to present value. This is especially important when benefits of an investment are delayed and the project or its effects cover several years. People may be more reluctant to invest for potential benefits that are coming later and the discounted values can help taking this into account.

## Slide 14
2.2 Step-by-step to conducting a CBA
8. Determine net present value of each alternative
(Boardman et al., 2018)
Firewood to Electricity
Firewood to ICS
ICS to Electricity
LPG to Electricity
Firewood to LPG
Notes: In step eight we determine the net-present value of each alternative. This is equivalent to the present value of each benefit minus the present value of all costs, in other words what we defined as the net-benefit on the previous slide.

## Slide 15
2.2 Step-by-step to conducting a CBA
9. Perform a sensitivity analysis
(Boardman et al., 2018)
Adapted from (Voros, J., 2003)
Adapted from (Quist, J., 2016)
Notes: It is important to recognize that the benefits and their valuations of any transition are uncertain. To make up for the uncertainty a sensitivity analysis is usually preformed to asses what would happen to the net-benefits if the absolute benefits or their valuation changes.

## Slide 16
2.2 Step-by-step to conducting a CBA
10. Make a recommendation
(Boardman et al., 2018)
Chart: Technology shares
| Biogas | LPG | Electricity
Sales | 2 | 6 | 5
Spatial distribution
Notes: Once the preceding steps are done a recommendation can be made for the problem based on the CBA. In the case of clean cooking the recommendation can be to invest in a specific stove in a specific settlement.

## Slide 17
References
Boardman, A., Greenberg, D., Vining, A., & Weimer, D. (2018). Cost-Benefit Analysis: Concepts and Practice, 5th edition.
Voros, J. (2003). A generic foresight process framework. Foresight, 5(3), 10–21. https://doi.org/10.1108/14636680310698379
Quist, J. (2016). Deliverable 4.3: Report on future lifestyle scenarios and backcasting vision workshops.

## Slide 18
Thank you for your attention in this lecture!

## Slide 19
Khavari B., Ramirez C., 2023. Lecture 2: Geospatial Clean Cooking access modelling using OnStove. Release Version 1.0 [online presentation]. Climate Compatible Growth Programme, Sustainable Energy for All, KTH
Supported by and in collaboration with
Sustainable Energy for All
Consolidated by Babak Khavari and Camilo Ramirez from the Royal Institute of Technology (KTH) in Stockholm