## Slide 1
Supported by and in collaboration with
Politecnico di Milano
Off-Grid Energy Systems Modelling with MicroGridsPy
LECTURE 3
Energy System Modelling
Version 1.0

## Slide 2
1
Learning Outcomes of the Lesson
Understanding Energy System Models
Learners will be able to understand what energy system models are, including their purpose and how they function. This will involve grasping the concept that these models are mathematical representations of physical phenomena or collections of processes and acquiring the basic glossary.
Optimization Techniques in Energy Modelling
Students will learn about various optimization techniques, including constrained optimization and linear programming, and their application in energy modelling
Temporal and Geo-Spatial Resolution in Modelling
Learners will understand the importance of temporal and geo-spatial resolutions in energy system modelling, crucial for managing renewable energy variability and understanding local energy dynamics for strategic planning
Understanding the Attributes of MicroGridsPy
Learners will develop an understanding of the attributes, characteristics, and features of MicroGridsPy as an energy systems modeling tool

## Slide 3
2
Energy System Models
Mathematical representation of a physical phenomenon or ensemble of processes, in order to perform analytical experiments by assessing different scenarios and inform with sound scientific data the policy making process.
Definition
Global Energy Transition
Environmental dimension
Social dimension
Social equity
Governance
Challenges
High share of variable sources
Need of flexibility and storage
Cross-Sectorial Linkages
Inter or intra-national connections
Complex energy systems

## Slide 4
3
Brief History of Energy Modelling
1972
International Institute for Applied System Analysis (IIASA) - MESSAGE
1970s
Oil Crisis
1974
International Energy Agency (IEA)
1976
IEA-ETSAP – MARKAL, TIMES
Nowadays
Limited complexity of energy systems
Low temporal resolution
Low spatial resolution
High interest in policy/economy feedbacks
Focus on macro-economic interactions
Affordability, resilience and environment
High penetration of renewables
Decentralized generation
New-generation models
High spatial and temporal resolution
High technological detail

## Slide 5
4
General Glossary
Top-down
Bottom-up
Aim at modelling the economy as a whole at national or regional level (macroeconomic models) and at assessing the aggregated effects of energy and/or climate change policies in monetary units.
Aim at modelling more specific and narrowed energy systems with high-degree of technological detail but usually without taking into account broader macroeconomic aspects.
Application to feedback loops to welfare, employment and economic growth
Low technological characterization
Give a detailed representation of energy systems and technological options
Do not take into consideration complex socio-economical dynamics
“How much a given energy price (environmental tax) increase will reduce demand (emissions) and consumption (GDP growth)?”
“How can a given energy demand (emission reduction target) be achieved with minimal (energy systems) costs?”

## Slide 6
5
General Glossary
Simulation
Optimization
Aim to replicate the rules and linkages that describe the interactions among different elements of the analysed system, simulating the behaviour of energy producers and consumers in response to factors like prices, income, and other parameters.
Identify an optimal mix of technologies under certain constraints to achieve specific targets, assuming that real-world decisions align with the objective function to obtain a theoretically ideal solution.
Realism: Accurately mirrors real-world energy systems, capturing complex interactions
Limited Predictive Power: Not as effective for future planning
Efficient Decision-Making: Finds the most efficient solutions within set constraints.
Over-simplification: May produce impractical solutions due to simplified assumptions
“Instead of generating possible futures, focus on predicting the system’s likely evolution”
“Mathematical optimization is the selection of a best element (with regard to some criterion) from some set of available alternatives”

## Slide 7
6
Constrained Optimization
Objective Function
min [cost/emissions/others...]
Energy Balance
Power Balance
Mass Balance
Technological Constraints
Environmental Constraints
Economical Constraints
In energy model constrained optimization, the objective function is bound by constraints that mirror the system's physical behaviour and specific policy or regulatory directives, ensuring solutions are economically sound, technically viable, and policy-compliant.

## Slide 8
7
Linear programming (LP) – a method for optimization
LP optimisation is a deterministic optimisation method that allows to find the exact absolute optimum solution within the given domain. The most common type of application involves the general problem of allocating limited resources among competing activities in a best possible (i.e., optimal) way.
Subject to (constraints)
Maximize Z=(c1x1 + c2x2)
b 1=4; b 2=12; b3 =18
c 1= 3; c 2 = 5
a1 x1 + a2 x2 ≤ b 3
0≤ x1 ≤ b1; 0 ≤ 2x2 ≤ b2
a 1= 3; a2 = 2
With given
SIMPLEX Method
The simplex method is an algebraic procedure. In linear programming constraints define a polyhedron in n dimensions: if an optimal solution exists, it will be at a corner point feasible solution (vertex) of the latter. Starting from any feasible solution, one can find the optimal solution by following the edges of the polyhedron .
Example of feasible solution domain

## Slide 9
8
Optimization Modelling Frameworks
Basic Terminology
Parameter: a fixed and constant value in model equations, often linked to real-world costs, efficiencies, or physical traits of the energy system
Variable: elements of a model that are unknown and changeable, such as decisions or system outcomes. Their values, known as the solution, emerge from the optimization
Set: index used in the algebraic structure of equations, serving to categorize and organize variables and parameters within the model
Constraint: an expression, either equal or inequal, that limits the possible values of one or more variables within the model.
Objective function: mathematical expression that defines the goal of the optimization, such as maximizing profits or minimizing costs. It is formulated in terms of the model's variables and parameters and is the key component the solver aims to optimize given the constraints.
Open-source Python package for formulating and solving various optimization models, compatible with both commercial and open-source solvers, defining general symbolic problems, create specific problem instances, and solve them
PYOMO
Optimization problems require a specific terminology and robust frameworks for modelling and solving complex mathematical challenges.
Python-embedded modelling language for convex optimization problems. It provides an intuitive syntax and automatic transformations of complex problems into standard forms
A high-level General Algebraic Modelling Language for mathematical optimization problems. It allows for easy model formulation, management, and solves problems using various solvers
A powerful language designed specifically for large-scale optimization. It is particularly adept at handling complex problems and provides a clear, concise syntax for specifying optimization models.

## Slide 10
9
General Glossary
Static
Dynamic
Offer an instantaneous snapshot of an energy system at a specific point in time, either present or future. They can depict immediate adjustments to shocks, transitioning from old to new equilibriums without involving time or transition phases.
Explicitly incorporate time, illustrating how system properties evolve. They are recursive, forming a sequence of static equilibria where the output of one time slice becomes the input for the next.
Straightforward, less complex and easier interpretation of results
Exclude energy systems dynamics, such as technological evolution, policy impacts over time, or long-term environmental effects
More comprehensive view of the energy system's evolution over time.
Complex and resource-intensive, requiring detailed data and sophisticated modelling

## Slide 11
10
General Glossary
Time Resolution
Geo-Spatial Resolution
Refers to the granularity with which time is represented in the model. It can range from hourly intervals to annual aggregates.
Refers to the geographical detail within the model. This can vary from a single, aggregated national level to a more detailed regional or even local level.
Higher time resolution allows for detailed analysis of fluctuations in energy demand and supply, crucial for modelling systems with significant renewable energy sources
Lower time resolution may be sufficient for long-term planning and policy assessment as well as modelling fossil fuels systems which are less dependent on time
Higher geo-spatial resolution provides insights into local variations in energy demand and supply and environmental impacts, crucial for distributed energy resources like solar and wind power
Lower geo-spatial resolution are useful for national policy-making and strategic decisions as well as centralized systems which are not dependent on location
Source for Images: [1]

## Slide 12
11
Time Resolution
The crucial role of high-resolution temporal data in system modelling cannot be overstated, particularly for the accurate representation of renewable energy sources. It ensures that the intermittent and variable nature of renewables is captured effectively, enabling more reliable and efficient energy system planning
Low Time Resolution
A coarse spatial and temporal resolution is necessary to keep computational effort manageable and useful for situations where temporal fluctuations are not important: fossil fuel-fired or nuclear plants
High Time Resolution
Renewable energy can be highly variable in time. Therefore, with their rising importance, resolving time and space becomes important to accurately answer questions about the energy system.
Computational balance
Notes: Aryanpur et al. 2021

## Slide 13
12
Geo-Spatial Resolution
Regional demand variabilities and inflexibilities
Regional consumer preferences
Impact of climate conditions on demand
Population demographics
Regional responsibilities
Political acceptability
Local actors & stakeholders
Regional income level & wealth distribution
VRE generation potential
Transmission development
Diversification of Generation
Regional resource endowment
1
2
3
Demand Side Implications
Supply Side Implications
Socio-economic, environmental
& political motivations
Regional environmental issues
Energy consumption habits
Regional consumer affordability
Regional willingness to pay
Region-specific financial incentives
Need for equitable generation
Trade-offs between environmental impacts and energy security
Social resistance against new installations
Correlation between VRE generation and fluctuating demand
Requirements for load-following and storage technologies
Analysis of centralized vs de-centralized energy supply
Source for Image: adaptation from [2]
Notes: Aryanpur et al. 2021

## Slide 14
13
Main Modelling Frameworks
Main modelling frameworks in terms of geographical and temporal resolution
PyPSA
URBS
MESSAGE
MARKAL
TIMES
Global
Continental
National
Regional
Local
Single Project
Geographical Coverage
Seconds
Minutes
Hours
Days
Years
Decades
Temporal Resolution
Energy modelling encompasses a range of tools tailored for different scopes, from local to global, with varying temporal detail, supporting decision-making in energy system development and planning.

## Slide 15
14
What is MicroGridsPy?
MicroGridsPy is an open-source bottom-up, stochastic optimization model for sizing and dispatching energy in microgrids, particularly in isolated areas, with high time resolution and time-evolving load demand.
It’s Python-based, running on Pyomo and it relies mainly on linear programming formulation.
Bottom-up, dynamic, optimization model
High time resolution, Linear programming
MicroGridsPy model scheme visualization
Notes: Aryanpur et al. 2021

## Slide 16
15
Towards OPEN-SOURCE modelling
PyPSA
URBS
Hilpert et al. (2018)
Pfenninger (2017)
Brown et al. (2018)
Quoilin et al. (2017)
Dorfner et al. (2016)
Lund (2007), Garegnani et al. (2016)
Howells et al. (2011)
Balderrama et al. (2019)
Most of the new-generation modelling frameworks arose within the Open Energy Modelling Initiative (OpenMod) in response to the increasing advocacy for openness and transparency of codes and datasets.
GitHUB
Notes: Aryanpur et al. 2021

## Slide 17
16
"All models are wrong, but some are useful“
George Box – British Statistician
Notes: Aryanpur et al. 2021

## Slide 18
4
References
[1] Prina et al., Classification and challenges of bottom-up energy system models - A review, Renewable and Sustainable Energy Reviews 2020, https://doi.org/10.1016/j.rser.2020.109917
[2] Aryanpur et al., A review of spatial resolution and regionalisation in national-scale energy systems optimisation models, Energy Strategy Reviews, https://doi.org/10.1016/j.esr.2021.100702

## Slide 19
CCG courses (this will take you to the website link http://www.ClimateCompatibleGrowth.com/teachingmaterials)
Moksnes N., Sahlberg A., Khavari B. 2021. Lecture 1: OnSSET/Global Electrification Platform. Release Version 1.0. [online presentation]. Climate Compatible Growth Programme, Energy Sector Management Assistance Program and World Bank Group
Stevanato, N., Onori, A., Mereu, R., & Colombo, E., 2024. Lecture 3: Off-Grid Energy Systems Modelling with MicroGridsPy. Release Version 1.0 [online presentation]. Climate Compatible Growth Programme, Politecnico di Milano
Supported by and in collaboration with
Politecnico di Milano
Consolidated by Nicolò Stevanato, Alessandro Onori, Riccardo Mereu and Emanuela Colombo from Politecnico di Milano