## Slide 1: LECTURE 3 INTRODUCTION TO OnSSET
OnSSET/Global Electrification Platform
Version 1.0

## Slide 2
Course Name
Learning Outcomes
ILO1: Describe the basic datasets used in OnSSET
ILO2: Explain how energy resources are distributed in sub-Saharan Africa
ILO3: List key features of Geographical Information Systems (GIS)
ILO4: Describe the role of geospatial data and the Sustainable Development Goals
By the end of this lecture, you will be able to:
Notes: This lecture has four Intended Learner Outcomes. After this lecture you will be able to:
Describe the basic datasets used in OnSSET
Explain how energy resources are distributed in sub-Saharan Africa
List key features of Geographical Information Systems (G I S)
Describe the role of geospatial data and the Sustainable Development Goals
These learning outcomes will be important for the basic understanding of the OnSSET tool.

## Slide 3
3.1 Introduction to OnSSET
A new medium-term power system optimization model
Identifies a least-cost plan for universal electrification through a mix of
  Grid network extension
  Mini-grid systems
  Stand-alone systems
Incorporates in a spatially explicit manner resources, infrastructure, technologies, and demand
Aiming at ensuring full access to affordable, reliable, sustainable and modern electricity for all by 2030
Korkovelos et al., 2019, Mentis et al. 2017
Open-Source Spatial Electrification Tool (OnSSET)
Source: Mentis et al. 2021
Notes: The model that KTH Royal Institute of technology has developed, and that we will use in this course, is the Open Source Spatial Electrification Tool (OnSSET). OnSSET draws on the geospatial dimension to develop electrification investment scenarios for every settlement in a country or region. It calculates the lowest cost scenario for universal access to electricity. OnSSET considers grid extension, mini-grids, and stand-alone technologies. It was first developed focusing on SDG7, namely to create universal energy access by 2030. Today it can also be customized to look at different timelines and different access rate targets.

## Slide 4
Key aspects of OnSSET
3.1 Introduction to OnSSET
Korkovelos et al., 2019
Source: Mentis et al. 2021
Implemented in Python and QGIS
Country specific electrification analysis (National–subnational level)
Spatial resolution that can vary as per input data and needs
Customized inputs according to country specific characteristics
  Social indicators (e.g., population growth, urbanization level, different demand patterns)
  Technical factors (e.g., T&D losses for national grid, alternative technologies available)
  Cost elements (e.g., Investment cost, O&M , Fuel cost)
  Energy Access targets
Notes: As the name suggests, OnSSET is an open source model, which means anyone can access it through our GitHub repository (where repository is a directory or storage space online where your projects can live). And in order to run an analysis using OnSSET, you also need two other open source tools. The first tool is Python, which is a programming language that's needed to run the OnSSET code itself. And the second one is Q.G.I.S, which is a geospatial information system. This is software that is used to collect and process the geospatial data that is needed as input to the OnSSET code. It should be noted that you don’t have to be a programmer to use the OnSSET tool – it is only about having Python available on your computer. Also, the Q.G.I.S process could be replaced using other G I S software, such as Arc G.I.S or GeoPandas.
This tool is suited for national analysis, where every settlement is modelled individually. However, this tool does not provide a solution down to every single household. Instead, it provides the overall solution for every single settlement. Finally, the model can be customized to reflect the different contexts that might apply to different countries. There are around 15 geospatial datasets and 150 other input variables that can easily be updated for the specific country or region you're studying. This includes population and population growth, information on urbanization trends, the expected demand for electricity and target access rates, the costs of different technology options, and other technical factors such as loss of transmission and distribution (or T&D) networks. We will cover all of these aspects during the course of this training.

## Slide 5
OnSSET contribution
3.1 Introduction to OnSSET
Source: Adapted from Mentis et al. 2021
Open-source
Underlying methodologies/algorithms published in peer reviewed journals
Used by teams at different universities (e.g., University of British Columbia, Kabul Polytechnic University, University of Cape Town, Imperial College London)
Used to inform International reports such as (e.g., IEA’s World Energy Outlook (2017, 2019)
Used to build capacity over geospatial electrification planning in different institutions & countries
Adopted by international organizations
  The Global Electrification Platform (GEP) -- World Bank
  Modelling tools for sustainable development -- UNDESA
Notes: Since its development in 2015, OnSSET has contributed to research studies, online platforms, and capacity building events. The methodology and the new additions to the tool are peer reviewed and published in scientific journals. OnSSET is open source and free to use and modify to your needs. The tool is also used by researchers in other universities from Canada to Afghanistan to South Africa. The results from the OnSSET tool can also be seen in international reports, such as the International Energy Agency's World Energy Outlook. And we also want to mention that the core focus in our work is also capacity building activities. Together with international partners, we have organized trainings in Italy, Benin, Ethiopia, South Africa, and others places to ensure that the models can be used by energy practitioners in areas where access to electricity needs to be increased. Finally, there are also platforms where anyone can go and explore electrification scenarios for countries around the world without the need to do any modelling work of their own, such as the UNDESA (United Nations Department of Economic and Social Affairs) modelling tools for sustainable development, or the World Bank and ESMAPs (Energy Sector Management Assistance Program) the Global Electrification Platform.

## Slide 6
6
Geospatial electrification models
3.1 Introduction to OnSSET
The different tools have different purposes, strengths, and weaknesses:
Rural vs. National electrification planning
Open-source vs licensed
Varying levels of detail and computational time
Varying number of electricity generation technology options
Moner‐Girona et al., 2018, Morissey, 2018
Source: Mentis et al. 2021
Picture source: Moner‐Girona et al., 2018, image, license under CC-BY 4.0
Notes: Models that take account of geospatial information on how things vary throughout the region to study how to increase access to electricity are what we call geospatial electrification models.
In recent years, many models and initiatives have been developed to take into account the geospatial dimension to improve electrification planning as seen in the figure. The different tools has different degrees of SDG integration where OnSSET has a very strong focus on SDG7. As mentioned, there are many aspects to take into consideration in the planning: economical, technological, environmental, and political. The different models and initiatives have different focuses and different strengths and weaknesses. It is important to select a model or a tool that is suited to answer the specific questions that you wish to study or that you need to answer. We will mention some notable differences between the models. First of all, models can have different objectives such as focusing on rural or national electrification. Second, a model can be open source or licensed. Third, you can see varying levels of detail and computational time. Finally, there are different levels of richness of technology choices.

## Slide 7
Key messages
3.1 Introduction to OnSSET
The suitability of different technology options (grid-extension, mini-grids, stand-alone technologies) to supply electricity depends on many factors that vary geographically within a country
In recent years, several models have been developed that take into account the geographical dimension to examine technology options for increasing access to electricity: these are so-called geospatial electrification models
Different geo-spatial electrification models are used for different purposes, each with its own strengths and weaknesses
Source: Mentis et al. 2021
Notes: Now to summarize the three key messages of this part of the lecture. First of all, we need to include the geospatial dimension in energy access planning to know where to deploy different technologies, depending on population, resource availability, and distance to infrastructure. Second, to cover this spatial dimension, several different models, tools, and initiatives have been developed in recent years that we call geospatial electrification models. Finally, one must note that each model has its own strengths and weaknesses. They are suited to answer different questions or to inform different kinds of projects. The OnSSET tool is an open source model with low running times and a lower level of detail than some of the others, which has been used in many different applications and training events.

## Slide 8
Course Name
Lecture 3.1 References
Korkovelos, A., Khavari, B., Sahlberg, A., Howells, M., Arderne, C., 2019. The Role of Open Access Data in Geospatial Electrification Planning and the Achievement of SDG7. An OnSSET-Based Case Study for Malawi. Energies 12, 1395. https://doi.org/10.3390/en12071395
Mentis, D., Howells, M., Rogner, H., Korkovelos, A., Arderne, C., Zepeda, E., Siyal, S., Taliotis, C., Bazilian, M., de Roo, A., Tanvez, Y., Oudalov, A., Scholtz, E., 2017. Lighting the World: the first application of an open source, spatial electrification tool (OnSSET) on Sub-Saharan Africa. Environmental Research Letters 12, 085003. https://doi.org/10.1088/1748-9326/aa7b29
Mentis, D., Korkovelos, A., Sahlberg, A., Khavari, B., n.d. Lecture 1: Introduction to geospatial electrification modelling [WWW Document]. OnSSET Teaching Kit. URL https://onsset.github.io/teaching_kit/courses/module_1/Lecture_1/ (accessed 2.18.21).
Moner‐Girona, M., Puig, D., Mulugetta, Y., Kougias, I., AbdulRahman, J., Szabó, S., 2018. Next generation interactive tool as a backbone for universal access to electricity. WIREs Energy and Environment 7, e305. https://doi.org/10.1002/wene.305
Morrissey, J., 2018. Achieving Universal Electricity Access at the Lowest Cost. Oxfam, OXFAM’S RESEARCH BACKGROUNDERS 113.

## Slide 9
Identify geospatial energy related data
3.2 Key datasets used in OnSSET
Administrative boundaries
Road network
Nighttime light
Power plants
Mines
Existing Grid Network
Current population
Projected population and Grid Network
Wind power capacity factor
Global Horizontal Irradiance
Mini and small hydropower potential
Spatial cost of Diesel gensets
Source: Mentis et al. 2021
Korkovelos et al., 2019, Mentis et al. 2017
Existing Grid Network
Picture source: Khavari et al. 2021, image, license under CC-BY 4.0
Notes: In this mini-lecture we will look at an example of an electrification analysis, using the OnSSET tool, for all of sub-Saharan Africa. To start with we need to collect all geospatial datasets. First of all, we need to look at the administrative boundaries which delineate the area or the country that we are studying. In this case, we're studying all countries in sub-Saharan Africa. Another important dataset is the road network, which indicates how well connected each settlement is. Nighttime lights show the light that's detectable by a satellite that passes over the globe during nighttime. We can through that assume that there's probably some access to electricity or something that emits this light. We can also look at power plants and mines, the former is the producer of electricity, the latter is a consumer of electricity. Another key dataset is information about where the existing grid network is, which affects the cost of extending to new settlements (as seen in the picture). This dataset is also used to identify the currently electrified settlements. Of course, we also need to take into account how the population is distributed. And then we also look at the projections of these. How do we expect population to grow in different areas and are there already committed grid network extensions that we should include in our analysis? In the next slide we will discuss the energy resource layers.

## Slide 10
Energy resources in sub-Saharan Africa
3.2 Key datasets used in OnSSET
Korkovelos et al., 2018, Mentis et al. 2017
Source: Adapted from Mentis et al. 2021
Picture Source: Mentis et al. 2017, image licensed under CC-BY 3.0
Picture Source: Mentis et al. 2017, image licensed under CC-BY 3.0
Picture Source: Korkovelos et al. 2018, image licensed under CC-BY 4.0
Notes: In Sub-Saharan Africa the wind potential is high in West and East Africa. For the solar energy resource, or the global horizontal irradiance, you can see that there are variations across the continent with some areas with very high potential (seen in darker red). Generally the solar potential in sub-Saharan Africa is quite high. We also included hydropower potential as seen in the lower blue picture. In red and blue you can see the different locations that that we found that we could connect mini- and small hydropower across sub-Saharan Africa. In addition to that we also have information about the cost of diesel. The cost varies throughout the country (low cost in red and higher cost in green), but also between countries as you can see in the top right-hand corner, illustrating a high and low diesel cost scenario.
The geospatial variation depends on the diesel
Availability;
Whether the country an importer or an exporter;
And the cost for transporting the diesel to more remote settlements.

## Slide 11
Multi-tier framework
3.2 Key datasets used in OnSSET
ESMAP, 2015; Fuso Nerini et al., 2016
Source: Mentis et al. 2021
Picture source: Khavari et al. 2021, image, license under CC-BY 4.0
Notes: Once you have collected the geospatial data sets, we also need to estimate the future electricity demand. And we do this using the multi-tier framework. The multi-tier framework has five levels of access, and it is not just about having electricity or not having electricity, but also about how much electricity you need. Tier 1 is the lowest level of electricity access. And this is just enough electricity to power a few light bulbs or maybe phone charging or a radio. If we move up to tier 2, we add some other appliances, for example a TV or a fan or other low consumption appliances. Then as we go towards tiers three to four to five there are more electricity services up to refrigerators, air conditioners, and electric cook stoves. And depending on the tier you are aiming for, of course, the electricity requirements differ. To power just a few light bulbs and some phone charging a few kilowatt hours per capita per year is enough. While, if you want to power electricity for cook stoves and air conditioners you might need several hundred kilowatt hour per person per year. In OnSSET we define electricity demand for every single settlement based on the population in the settlement and then multiply this by the electrification tier.

## Slide 12
What are the options for electrification?
3.2 Key datasets used in OnSSET
Source: Mentis et al. 2021
GRID
STAND-ALONE
TECHNOLOGIES
MINI-GRID
Picture Source: International Renewable Energy Agency (IRENA) CC BY-NC-ND 2.0
Notes: Now we will look at the electrification options that can supply this demand. If we look at all the off-grid options we have four mini-grid options by default and two stand-alone options in OnSSET. The mini-grid options can be powered by either solar PV, diesel generation, wind, or hydro. Stand-alone options can be powered by solar PV or diesel generation. After collecting all of these datasets we summarize these geospatial datasets in a database. In addition we include economic parameters to choose which is the least-cost electricity supply option among the off-grid technologies.

## Slide 13: 3.2 Key datasets used in OnSSET
Levelized cost of electricity (LCOE)
Mentis et al. 2017
Source: Mentis et al. 2021
Picture Source adapted from: Mentis et al. 2017, image licensed under CC-BY 3.0
Notes: The optimization in OnSSET to identify the least-cost option is through the levelized cost of generating electricity (L.C.O.E). The L.C.O.E takes into account all of the costs over the project lifetime from investment costs, but also operation and maintenance costs that are recurring for every year and the fuel costs (for diesel generators). The technologies that are dependent on renewable resources like solar and wind have no fuel costs. We compare this cost to all of the electricity that is generated by the system over its lifetime. If we take into account all of these costs divided by all of the energy, we get the lowest cost of generating electricity, which is measured in U.S dollars per kilowatt hour. All the above can be represented by the formula on the slide. The L.C.O.E is a good measure to compare different technologies that have different cost structures. As an example we can look at a solar PV system that might have a very high investment cost in the beginning but no fuel costs. If you instead look at a diesel system, we have much lower investment costs in the beginning, but much higher running costs or fuel costs throughout each year. If we take into account all of these different costs and compare them, we'll get a good measure to decide which is the least-cost supply option in every settlement. In the next mini-lecture we will look at some results for all of sub-Saharan Africa.

## Slide 14
Mini Lecture Learning Objective
Lecture 3.2 References
Bhatia, Mikul, Angelou, Niki, 2015. Beyond Connections : Energy Access Redefined (TECHNICAL REPORT No. 008/15), Working paper.
Korkovelos, A., Khavari, B., Sahlberg, A., Howells, M., Arderne, C., 2019. The Role of Open Access Data in Geospatial Electrification Planning and the Achievement of SDG7. An OnSSET-Based Case Study for Malawi. Energies 12, 1395. https://doi.org/10.3390/en12071395
Korkovelos, A., Mentis, D., Siyal, S.H., Arderne, C., Rogner, H., Bazilian, M., Howells, M., Beck, H., De Roo, A., 2018. A Geospatial Assessment of Small-Scale Hydropower Potential in Sub-Saharan Africa. Energies 11, 3100. https://doi.org/10.3390/en11113100
Mentis, D., Howells, M., Rogner, H., Korkovelos, A., Arderne, C., Zepeda, E., Siyal, S., Taliotis, C., Bazilian, M., de Roo, A., Tanvez, Y., Oudalov, A., Scholtz, E., 2017. Lighting the World: the first application of an open source, spatial electrification tool (OnSSET) on Sub-Saharan Africa. Environmental Research Letters 12, 085003. https://doi.org/10.1088/1748-9326/aa7b29
Mentis, D., Korkovelos, A., Sahlberg, A., Khavari, B., n.d. Lecture 1: Introduction to geospatial electrification modelling
[WWW Document]. OnSSET Teaching Kit. URL https://onsset.github.io/teaching_kit/courses/module_1/Lecture_1/ (accessed 2.18.21).
Nerini, F.F., Broad, O., Mentis, D., Welsch, M., Bazilian, M., Howells, M., 2016. A cost comparison of technology approaches for improving access to electricity services. Energy 95, 255–265. https://doi.org/10.1016/j.energy.2015.11.068

## Slide 15
Electrification results
3.3 Electricity access in sub-Saharan Africa
Mentis et al. 2017
Source: Mentis et al. 2021
Picture Source: Mentis et al. 2017, image licensed under CC-BY 3.0
Notes: In this mini-lecture we will look at some results for sub-Saharan Africa. In the slide you can see in the first scenario all population are electrified with a Tier 1 demand. We can see that the grid, in blue, is the most suitable option close to the existing network and in the high densely populated areas around West Africa and in South Africa. You can see a lot of blue around Addis Ababa in Ethiopia. But stand-alone technologies are less costly in less densely populated areas and areas farther away from the existing networks. If everyone would get access to a Tier 3 level of electricity access, on the other hand, we'll see a different mix of technologies. This scenario is in the top right-hand map. Now, this grid would be the least-cost option for about 45 percent of the population in sub-Saharan Africa. Stand-alone technologies are reduced to about half of the population. We also see that mini-grid would play a more important role, reaching 7 percent of the population. The mini-grids (in green) are located often in areas that are further away from the existing networks, but still have a relatively high population density. This is also what we called the “mini-grid space” in the introductory lecture.
If we were to achieve low oil price for tier 5 (lower left corner) for all of the population in sub-Saharan Africa, the grid becomes the main supply option, reaching 7 out of 10 people. Mini-grid increases to about a quarter of the population while stand-alone will only supply electricity for seven percent of the population in the most remote and less densely populated areas. The demand has a large effect and we see different solutions, depending on different demands. In reality, we'll have a mix of tiers within a country and within the continent, so we might see a higher tier in urban areas, for example, and a lower tier in rural areas.

## Slide 16
Investment cost
3.3 Electricity access in sub-Saharan Africa
Mentis et al. 2017
Source: Mentis et al. 2021
Picture Source: Mentis et al. 2017, image licensed under CC-BY 3.0
Notes: If providing tier 1 for all of the population in sub-Saharan Africa, in this analysis the investment cost is approximately 50 billion U.S dollars. Providing electricity demand at Tier 5 level for all of the population in sub-Saharan Africa, the cost is approximately 855 billion dollars. There's almost a factor 20 in difference between these two scenarios. We see the technology split with stand-alone technologies in yellow, grid in blue and mini-grid in green as a share of the total population (overall technology split percentage). In tier 1 we see, as we described earlier, grid and stand-alone technologies. As we move to higher consumption targets we see a lot more focus on grid and mini-grid is introduced at tier 3. At the same time we see the decreasing role of stand-alone technologies.

## Slide 17
Example results of electrification analysis of sub-Saharan Africa
3.3 Electricity access in sub-Saharan Africa
Mentis et al. 2017
Source: Adapted from Mentis et al. 2021
Picture Source: Mentis et al. 2017, image licensed under CC-BY 3.0
Notes: There are many different aspects we can visualize from our results, which is very useful when we discuss electrification options. What we have shown before is the scenarios in which grid, mini-grid, and stand-alone technologies are the least-cost solution. We can further break it down into which type of mini-grid, and which energy resources it will be supplied by. Other things we can visualize are the cost of electricity. To the left we see in the green the areas in which we have a low cost of electricity per kilowatt hour, while in the darker shades of red we have a much higher cost of electricity. What we can see here, for example, is that the cost is much lower in the same areas have high population density and are close to existing grid. Conversely we see a higher cost of electricity in less densely populated areas, especially in rural areas. In the picture to the right we see the Market Assistance Need Index (known as MANI). Countries in red, such as Liberia, Democratic Republic of Congo, Somalia, and Burundi, rank highest in assistance need, while other countries such as South Africa, Botswana, and Namibia score very low on this index. Combining these two can give insight into where the need for assistance is high in combination with a high cost for electricity.

## Slide 18
Investment needs in sub-Saharan Africa
Source: Mentis et al. 2021
3.3 Electricity access in sub-Saharan Africa
Picture source: Khavari et al. 2021, image, license under CC-BY 4.0
Notes: Another aspect that we can visualize is the investment costs per area. You see some regional values here where the darker colour is higher cost and lighter colour is lower cost. The same trend as we saw with the lower cost of electricity in the densely populated areas is apparent here, as we can see that these same areas have a high investment cost. The larger cities can decrease the overall cost of electricity through the economy of scale. There are many different aspects you can visualize in G.I.S apart from just which technology is to be used.

## Slide 19
Key messages
Grid extension is favourable in areas with high demands, which often correlates with high population density and close distance (<50 km) to the grid network
Mini-grids are favourable in medium to high demand levels, which normally correlates with the density of population in areas located further away from existing grid lines
Stand-alone systems are favourable in areas where demand levels are low, typically in small rural settlements and/or sparsely populated areas
Increased electricity demand (Tier 1 → Tier 5) moves the least-cost option gradually from Stand-alone → Mini-Grid → Grid.
Source: Mentis et al. 2021
3.3 Electricity access in sub-Saharan Africa
Notes: Some key take away messages from this mini-lecture:
First of all, grid extension is often favourable in areas with high demand, which often correlates with high population density, which is frequently close to the current network. The cost, in such areas, of extending the grid is therefore not so high per person. Mini-grids are usually the technology option for high to medium demand levels, typically in densely populated areas, but quite far away from the existing grid where the cost of extending the grid network would be too high. Stand-alone technologies are most favourable where the demand is low, typically in rural areas and sparsely populated areas that are far away from the grid network. However, we see that this mix of technologies changes depending on demand levels. For tier 1 demand the optimal technology mix has a high share of stand-alone technologies, but as we move towards tier 5 we move gradually from stand-alone options to mini-grid and grid.

## Slide 20
Lecture 3.3 References
Mentis, D., Howells, M., Rogner, H., Korkovelos, A., Arderne, C., Zepeda, E., Siyal, S., Taliotis, C., Bazilian, M., de Roo, A., Tanvez, Y., Oudalov, A., Scholtz, E., 2017. Lighting the World: the first application of an open source, spatial electrification tool (OnSSET) on Sub-Saharan Africa. Environmental Research Letters 12, 085003. https://doi.org/10.1088/1748-9326/aa7b29
Mentis, D., Korkovelos, A., Sahlberg, A., Khavari, B., n.d. Lecture 1: Introduction to geospatial electrification modelling
[WWW Document]. OnSSET Teaching Kit. URL https://onsset.github.io/teaching_kit/courses/module_1/Lecture_1/ (accessed 2.18.21).

## Slide 21
What is GIS and why is it useful?
3.4 Geospatial data and the SDGs
GIS can relate information from different sources, using two key index variables space (or location) and time.
A Geographic Information System (GIS) is an integrated set of hardware and software tools, designed to capture, store, manipulate, analyse, manage, and digitally present spatial (or geographic) data and related attribute information.
Source: Sahlberg et al. 2021
Notes: Geographic Information System (G.I.S) can relate information from different sources, using two key index variables: space (or location) and time. G.I.S stands for Geographic Information System, and, just like any other information system, they consists of a set of integrated tools designed to capture or store, manipulate, and analyse data. What sets G.I.S apart from other information systems is that the data has a spatial and temporal dimension. The spatial dimension describes how data changes based on location while the temporal dimension describes how it changes based on time. An example of this is solar irradiation. Solar irradiation changes based on where you are, that is the spatial dimension. But it also changes based on time of day which is the temporal dimension. The spatial and temporal dimensions make G.I.S very useful for energy modelling.

## Slide 22
3.4 Geospatial data and the SDGs
Geographical Information System (GIS)
The use of GIS serves multiple purposes:
Location based assessments: GIS tools enable assessments to analyse energy related geospatial information.
Remote sensing: The use of GIS tools facilitates the integration of remote sensing techniques to derive resource availability & energy potentials in cases where such data are not (publicly) available.
Illustration of results: GIS is used to illustrate results in interactive maps, providing an effective science–policy interface.
Source: Sahlberg et al. 2021
Notes: We have listed three of the main purposes of using G.I.S here.
First of all, the spatial dimension gives us the ability to do location based assessments. Using G.I.S we can tailor solutions to different parts of the study area, down to a settlement level and basically say Solution A works best in settlement B, and solution X works best on settlement Y. This is difficult to do using tools that do not have a spatial dimension incorporated. The spatial and temporal dimensions also help us diversify our energy mix using remote sensing. Furthermore, we can estimate where we have resources such as solar, wind, and hydro. Lastly, G.I.S is very important when it comes to illustrating results in interactive maps. These maps can provide an effective science–policy interface by communicating key indicators for electrification planning, ensuring that the results are easily understood.

## Slide 23
Spatial solar and wind availability
3.4 Geospatial data and the SDGs
Wind Power Capacity factor map of the African continent
Areas with high potential for Wind Power projects deployment
Area with high potential for PV systems deployment
Global Horizontal Irradiation (GHI) map of sub-Saharan Africa
Source: Sahlberg et al. 2021
Picture source: Global Solar Atlas 2.0, https://globalsolaratlas.info
Picture source: Global Wind Atlas version 3.0, https://globalwindatlas.info/
Notes: On this slide, you can see two maps that shows the power of the spatial dimension of G.I.S. We have the global horizontal irradiation on the left-hand side. That is a good G.I.S dataset if you're interested in PV potential. On the right-hand side you have the wind power capacity. This G.I.S dataset is good if you're interested in knowing where you should install wind turbines. By looking at these maps, you can identify areas with higher potential for PV panels and wind turbines. This information is related to the spatial dimension.

## Slide 24
Geospatial data and the SDGs
3.4 Geospatial data and the SDGs
“It has been estimated that approximately 20% of the SDG indicators can be interpreted and measured either through direct use of geospatial data itself or through integration with statistical data.”
Arnold et al., 2019
Notes: As geospatial data describes the spatial as well as the temporal aspects of our Earth, it has important value in helping realize and implement the 17 Sustainable Development Goals (SDGs) and Agenda 2030.
“It has been estimated that approximately 20% of the SDG indicators can be interpreted and measured either through direct use of geospatial data itself or through integration with statistical data.”
Finding reliable geospatial data is an important task for countries which are developing their national plans for the 17 SDGs. Access to open source and high resolution data is an important part of that. The quality of geospatial data increases if it is developed with local knowledge. These local datasets can then be aggregated if needed to regional and global levels and compared to independent international (global) data sources. Certain types of fundamental geospatial data, for example elevation, transportation networks, and settlements should be collected and create a foundation for the Sustainable Development Goals indicators.
However, to make the data collection robust, the geospatial data needs to be in certain formats in terms of spatial resolutions, thematic detail, and temporal periodicity. In many countries this can be a challenge as the knowledge and capacity is not there to provide the long-term consistent data. The capacity shortage can be in terms of core geospatial data as well as the lack of the required data capture capacities.

## Slide 25
Key messages
3.4 Geospatial data and the SDGs
GIS are large systems describing how data change over time and space
The use of GIS in energy planning is important as it gives us the ability to adapt solutions based on location specific attributes
GIS can play a crucial role in filling data gaps and communicating results
GIS is important for the planning and tracking of the Sustainable Development Goals.
Source: Sahlberg et al. 2021
Notes: Some key takeaway messages:
G.I.S are large systems describing how data changes based on time and location. The use of G.I.S and energy planning is important as it gives us the ability to do location based systems. And G.I.S can play a crucial a role when it comes to filling in the gaps and communicating our results. In addition, G.I.S can play an important role in follow up and support for achieving the Agenda 2030.

## Slide 26
Lecture 3.4 References
Arnold, S., Chen, J., Eggers, O., 2019. Global and Complementary (Non-authoritative) Geospatial Data for SDGs: Role and Utilisation.
Sahlberg, A., Khavari, B., Korkovelos, A., Mentis, D., n.d. Lecture 3: Application of GIS in electrification analysis in the OnSSET tool [WWW Document]. OnSSET Teaching Kit. URL https://onsset.github.io/teaching_kit/courses/module_2/Lecture%203/ (accessed 2.18.21).

## Slide 27
22
Thank you for your attention in this lecture!

## Slide 28
CCG courses (this will take you to the website link http://www.ClimateCompatibleGrowth.com/teachingmaterials)
Moksnes N., Sahlberg A., Khavari B. 2021. Lecture 1: OnSSET/Global Electrification Platform. Release Version 1.0. [online presentation]. Climate Compatible Growth Programme, Energy Sector Management Assistance Program and World Bank Group
Take Quiz

## Slide 29
This document was updated on 01.11.2024