## Slide 1: Maximum 32 point Arial in white
LECTURE 4 ENERGY ACCESS EXPLORER FRONT-END
Supported by and in collaboration with World Resources Institute

## Slide 2
2
Learning Outcomes
ILO1: Differentiate the key functions of the EAE front-end
ILO2: Explore the categories, layers and features of the data
ILO3: Conduct multi-criteria analysis based on different scenarios
ILO4: Export the analysis results for generating reports and presentations
By the end of this lecture, you will:
Notes: This lecture has four Intended Learning Outcomes. By the end of this lecture, you will:
​
Differentiate the key functions of the EAE front-end
Explore the categories, layers and features of the data
Identify the analytical indices and results of EAE
Make multi-criteria analysis based on different scenarios
​
These learning outcomes will be important to understand the context of the course.

## Slide 3
3
4.1 EAE Front-End Interface
The EAE front-end interface allows users to visualize and carry out multi-criteria spatial analysis with user-selected datasets on energy demand and supply to generate high priority areas for energy access interventions.
For EAE's front-end applications, users do not require any prior GIS or programming expertise. Anyone can use it!
Introduction
Notes: Beyond its visualization and analytical capabilities, EAE functions as a dynamic geographic information system and data repository which reduces software engineering and data transaction costs for both data providers and users. Its unique backend infrastructure comes with an easy to navigate Content Management System and allows administrative users with limited or no GIS and programming expertise to add data and metadata in a simple manner.

## Slide 4
4
Key Functionalities:
Select and visualize geospatial data
User friendly interface
Overlay data
Apply queries, filters and buffers
High resolution multi-criteria analysis
Map high-priority areas
View on desktop and mobile phone internet browsers
Customizable base maps (e.g., satellite, light, dark plus labels)
View in a public version
View in a password protected version
Zoom-in feature to select smaller administrative division and see custom versions of the app
Search for and summarize the top 20 locations in terms of the select indicators or the analytical outputs
Develop custom summary reports and dashboards
Search for coordinates or areas of interest
Save and download analysis
Visualize temporal data to track progress
4.1 EAE Front-End Interface
Notes: The EAE front-end comprises a range of essential functionalities designed to allow users ...

## Slide 5
5
SOURCE: EAE
4.2 Data view
Data, features and map functions menu
Map Functions​ Menu
Data & Features Menu
Add Layers
Active Layers
Search Features
Top Locations
Search POI's
Change geographies
Activate information cursor
Zoom in
Zoom out
Base map change
Map projection type
Map view

## Slide 6
6
EAE Features:
Add Layers: select from available datasets in EAE
Active Layers
  View all currently selected layers
  Change the order in which layers are displayed in EAE
  Filter values and change the dataset’s weight in the analysis
Search Features: search for a specific feature within a dataset
  Example: ‘Makerere University’ in Schools
  Note: not all datasets are searchable
Top Locations: provides a ranked list of the top 20 locations (sq km pixels) based on user-selected criteria
Search POIs: search for a point of interest (city/town, subnational division, national park) within the country
Change Geographies: select a particular subnational unit to focus your analysis
4.2 Data view
Notes: The EAE front-end comprises a range of essential functionalities designed to allow users ...

## Slide 7
7
SOURCE: EAE
Data categories and subcategories
Data categories and subcategories
4.2 Data view
Notes: The EAE front-end comprises

## Slide 8
8
SOURCE: EAE
Active later
Active layer
Layer value adjustment
Activate & adjust layer weighting values
Clear active layer
Dataset information
Adjust dataset opacity
4.2 Data view
Notes: The EAE front-end comprises

## Slide 9
9
SOURCE: EAE
4.3 Analysis View
Analysis View
Analysis view
Criteria and filter applied in the analysis
Multicriteria Analysis Index
Summary reports and dashboards

## Slide 10
10
Analytical Indices
There are 4 indices available in the analysis view:
  Energy Access Potential: areas with highest potential for electrification in the short-term, based on both supply and demand indicators; areas with high values on this index are the ‘low hanging fruits’
  Demand Index: focuses on demand indicators to identify where demand for energy services is highest
  Supply Index: focuses on supply indicators to identify sites with high potential for developing electricity generation
  Assistance Need Index: areas where demand and supply indicators are weaker, but where there is nevertheless an ongoing need for electrification; areas scoring high on the Assistance Need Index may require donor-supported interventions
  For more details on the analytical indices, please refer to Module 2.4
4.3 Analysis View

## Slide 11
11
Unit of Analysis
The index scores generated by EAE can be presented at different scales:
  Raster Analysis: The default unit of analysis in Energy Access Explorer is Raster Analysis, which provides granular analysis down to the pixel level
  Administrative Priority: Summarizes results for subnational administrative divisions; available at different levels/tiers
4.3 Analysis View

## Slide 12
12
High-Level Summaries
4.4 Applying EAE Analysis Results
In addition to identifying key areas, EAE also calculates the area and population affected in the user’s custom analysis
These values are displayed in summary charts within the analysis view
More detailed results can be found in the Summary Report
Notes: Source raster files may come in a higher resolution (finer pixel size) than what is supported in the Energy Access Explorer
Resampling the raster reduces the file size by adjusting the pixel size.
  You may need to install the GRASS plugin to access r.resamp.stats

## Slide 13
13
Summary Reports
The Summary Report in EAE provides detailed information for all indices in both chart and table format
The report can be exported for use in reports and presentations
4.4 Applying EAE Analysis Results
Notes: Source raster files may come in a higher resolution (finer pixel size) than what is supported in the Energy Access Explorer
Resampling the raster reduces the file size by adjusting the pixel size.
  You may need to install the GRASS plugin to access r.resamp.stats

## Slide 14: Thank you
www.climatecompatiblegrowth.com
Woldeamanuel, A. A., Khalid, A., Anand, S., Sahar, T., Saklani, A., Sinclair-Lecaros, S., Mentis, D., Ronoh, D., & Stockman, J., 2024. Lecture 1: Energy Access Explorer. Release Version 2.0 [online presentation]. Climate Compatible Growth Programme, World Resource Institute
Supported by and in collaboration with
World Resources Institute
Consolidated by Alemayehu Agizew Woldeamanuel, Abdul Khalid, Shikha Anand, Tarannum Sahar, Akansha Saklani, Santiago Sinclair-Lecaros, Dimitris Mentis, Douglas Ronoh and Jake Stockman from the World Resources Institute

## Slide 15
This document was updated on 01.11.2024