## Slide 1: Lecture 6 Enabling Technologies
The Electricity Transition Playbook
Version 1.0
Supported by and in collaboration with CCG and Green Grids Initiative

## Slide 2: “Enabling technologies”
This title has at least two possible meanings in the context of this course:
1. Enabling as an adjective
e.g. How can technologies enable society to reach net-zero emissions targets
2. Enabling as a verb
e.g. How can society enable people to adopt these technologies
This chapter will try to address both of these.
Notes: In this chapter we explore the importance of adopting different technologies for achieving pathways to zero emissions. Technologies can themselves enable these pathways, but we must also think about how to enable people and societies to adopt the necessary technologies in the first place, not to mention integrating and maintaining them.

## Slide 3: Technologies
Enabling technologies
that can enable the energy transition

## Slide 4: Technology example: Electric vehicles
N.B. This map just shows one particular kind of legislation that may drive change. Many countries have different kinds of zero-emission vehicle targets.
Graphic:
The Zero Emission Vehicles Transition Council
https://zevtc.org/tracking-progress/light-duty-vehicle-map
https://www.iea.org/data-and-statistics/data-product/global-ev-outlook-2023 - global-ev-policies
Notes: For perhaps the most familiar day-to-day example of such a technology, we could begin by mentioning zero-emission vehicles, the most prolific of which being battery-powered “electric” vehicles. A significant number of countries have already committed to phasing-out the sale of combustion engines in the relatively near future – many in the coming decade - and in the most progressive case as soon as two years time. Phase-out targets are just one kind of legislative approach; many countries have different methods of encouraging or enforcing a transition to zero-emission vehicle targets that are too numerous to list but can be found in the link above.

## Slide 5: Technology example: Electric vehicles
COP26 declaration signed by 39 countries:
https://acceleratingtozero.org/the-declaration/
“Together, we will work towards all sales of new cars and vans being zero emission globally by 2040, and by no later than 2035 in leading markets.”
Notes: A degree of international consistency was reached however in the COP26 declaration, aiming for 100% of vehicle sales to be electric or zero in leading markets in just 12 years time.

## Slide 6: Technology example: Electric vehicles
Worldwide share = 14%
Notes: These targets can be compared with current data on actual sales, for example what was sold last year. This figure shows the share of electric vehicles in new car sales by country. Though the running cost of electric vehicles can be much lower than combustion equivalents, the upfront cost is usually still higher. It might not be surprising, therefore, that this map picks out mostly countries where average individual wealth is higher, and a greater fraction of car-buyers might have the additional upfront cost at their disposal.

## Slide 7: Technology example: Electric vehicles
Notes: For comparison, this map shows countries with GDP per capita higher than $2000, which ensures that all the countries in the previous slide are included. This does indeed have some similarities with the previous map, but many differences. For example, China and India are much further advanced in EV share that countries with comparable GDP per capita. Meanwhile, a number of countries with the highest GDP per capita (USA, Australia) are not among the highest for share of electric vehicles. So the uptake of this technology is not simply down to the personal wealth of the people in the region; there are other factors enabling or preventing adoption. Regions that seem to be exceptions to this trend may provide valuable examples of how societies can enable individuals to adopt a technology despite the barrier of upfront cost.
[Note that the EV list is not comprehensive, so we can only comment on higher-GDP countries that make both lists.]

## Slide 8: Technology example: Electric vehicles
Notes: Zero-emission vehicles can enable huge improvements of air-quality in cities; a life-changing (and, for some, life-saving) benefit that the technology can provide, whatever the source of the energy that is used to charge them.

## Slide 9: Technology example: Electric vehicles
Initial cost of gasoline cars is typically still lower
But energy consumption can be over 3 times higher.
And running costs over $1000 more each year.
Notes: Contribution to overall emissions reduction is also guaranteed due the much greater energy efficiency of electric vehicles which can drive over 3 times further on the same amount of energy. So they reduce total system emissions even if the source of electricity is not renewable.

## Slide 10: Technology example: Solar PV generation
https://globalsolaratlas.info/map
Notes: To maximize this contribution, though, the transition to emission-free vehicles must be accompanied by a plan to transition to emission-free electricity, for example Solar PV generation which as this slide illustrates still has so much potential in many regions of the world.

## Slide 11: Technology example: Hydrogen storage
https://www.bighit.eu
https://www.emec.org.uk/facilities/hydrogen/
https://www.youtube.com/watch?v=Rybpaqhg5Qg
Notes: However, because solar and also wind energy are variable sources of power, additional technologies may need to be adopted to enable that energy to be stored and reused to match demand. In this example, excess renewable electricity generated in the Orkney islands is used by electrolysers to produce hydrogen, by electrolysis of water. This hydrogen is then stored as high-pressure gas in the tube trailers, which can be transported to mainland Orkney, for a variety of end uses including auxiliary power and heat for ferries in Kirkwall harbour, fuelling a fleet of hydrogen range-extended light vehicles, and heating for buildings in the Kirkwall area.
Generation exceeding demand becomes an issue earlier in the transition for smaller or more isolated systems like these islands but will occur in ever larger systems as renewable generation shares increase around the world.

## Slide 12: Smart grids and devices
Enabling technologies

## Slide 13: Smart grids and devices
Graphic: Bartz/Stockmar, CC BY 4.0
https://en.wikipedia.org/wiki/Smart_grid#/media/File:Staying_big_or_getting_smaller.jpg
Example of demand side management / energy flexibility by Hicham Johra et al. 2019 J. Phys.: Conf. Ser. 1343 012064
https://iopscience.iop.org/article/10.1088/1742-6596/1343/1/012064/pdf
Notes: Solar and wind generation are variable sources of power, but an increasing number of end uses for the electricity can also be varied, in principle.
These include routine charging of vehicles and devices, dishwashers, washing machines, heating, cooling, and some manufacturing processes.
If these can be switched on when renewable energy is being generated, and switched off when it isn’t, this can reduce the fuel burned in the system, or losses to storage which would otherwise be required to fill the demand gap.
Enabling more renewable energy to be sold (rather than stored) also helps incentivise further generation.

## Slide 14: Data
Enabling technologies

## Slide 15: Data availability
In January 2012, the USA’s Green Button initiative was launched,
allowing energy customers securely download their own detailed
energy usage with a simple click on electric utilities' websites.
In June 2019, the UK’s Energy Data Taskforce published this report, which presents five key recommendations:
1: Digitalisation of the Energy System
2: Maximising the Value of Data
3: Visibility of Data
4: Coordination of Asset Registration
5: Visibility of Infrastructure and Assets
https://www.gov.uk/government/groups/energy-data-taskforce
https://www.energy.gov/data/green-button
Notes: For demand to be adjusted to match renewable supply, thousands and potentially millions of distributed devices need to receive instructions from the grid, and/or access to current and forecast energy generation data.
So data availability and internet connection become critical for enabling zero-emission electricity.
End-user data may also need to be made available to the system, bringing privacy and data security also into consideration.

## Slide 16: Data - humans working with technology
https://www.uts.edu.au/human-technology-institute
Notes: However, the quality of the decision is not proportional to the quantity of data!
Data acquisition and particularly storage can create huge legislative challenges, as well as becoming extremely expensive!
It may be that existing open data, if processed and interpreted with modern tools, is more than sufficient to inform the key decisions
Centers of expertise for managing these new challenges are already being established and are valuable resources for governments and industry.

## Slide 17: Internet access
Notes: But in many cases, the challenges for data- and connection-dependent technologies are much more fundamental. For most, it has become hard to imagine not having access to the internet. But if we cast our minds back to the 1990s (for those of us who were there), we can remember that life did exist without it, as this map illustrates. In 1990, the internet existed but almost no-one used it. Moving forwards in time, we can see usage spreading around the world over the course of 3 decades, but even today over a third of people still do not use the internet. In some regions, internet access itself may be the technology most needed to enable the energy transition to start.

## Slide 18: Enabling people
Enabling technologies
to adopt technologies

## Slide 19: Enabling people – financing
Though many energy-efficient and zero-emission technologies may actually save money in the long term, the upfront purchase cost can be an impossibly high barrier for many people. We saw this trade of already in the above example of electric vehicles.
Heating and cooling technologies are another familiar example. Even in wealthier, developed countries, the initial cost of switching from gas heating to a more energy-efficient heat pump is still financially prohibitive for the majority of households.
Futhermore, adopting energy saving technologies can require other building modifications, sometimes substantial ones, putting them out of reach of yet more households and businesses.
And lastly, there may be buildings where such modifications would not even be permitted under current regulations, for example for older buildings or those in historic areas.
Notes: A common challenge for many low-emission technologies is the higher upfront cost, sometimes accompanied by other costs associated with the change, such as the larger radiators and improved insulation needed for heat-pumps.

## Slide 20: Enabling people – financing
2 billion people have access to electricity but still cook with biomass. Load shedding, weak grids, affordability of electricity, accessibility of liquid petroleum gas (LPG), tradition, perceptions, and a lack of suitable cooking appliances all act as barriers to scaling up the use of electricity or gas for cooking – clean cooking.
https://m-kopa.com
https://https://mecs.org.uk
Notes: Where there is the business case and/or the desire to make the change to a decarbonizing technology, it can be possible - in principle - to get around the upfront cost with financing.
For many homeowners and businesses, they would at least have the option to borrow against the future saving the technology can provide. For billions around the world, however, no matter how compelling the case - or need - to purchase more efficient equipment, loans may simply be not available, and they are stuck.
But there are a growing number of programs and companies, like the examples in this slide, which address this problem and prevent people being locked-out of technology access.

## Slide 21: Safety and public perception
Enabling technologies

## Slide 22: Safety and public perception
https://www.authentikusa.com/uploads/images/orig/blog/visiter-death-valley-national-park.jpg
https://en.wikipedia.org/wiki/Dalton_Highway#/media/File:Dalton_truck_and_Sukakpak_Mountain.jpg
Notes: The financial implications of new technologies are of course not the only factor that effects adoption rates. As well as convenience, there is of course their relative safety.
In the case of the electrification of personal transport, there is the genuine safety consideration over the range of vehicles.
In some places, being “out of gas” is an inconvenience; in other places, it can be life-threatening.

## Slide 23: Safety and public perception
https://www.gov.uk/government/statistics/reported-road-casualties-great-britain-annual-report-2021
…but it is not normalised!
This graphic seems to show that travelling by car is the most risky….
This table is normalised by vehicle miles, indicating that safety of low-energy transport needs to be improved.
N.B. Normalisation by “urban passenger miles” would be a more relevant comparison, or limiting data to short journeys, but this data could not be found. Bus/coach travel safety should also not be interpreted from the above order (presumably, casualty rates per passenger mile would be much lower for this category).
Notes: An even more effective switch for decarbonising personal transport is of course to travel without a car altogether. But riding bicycles, e-bikes and taking public transport all have different safety profiles than driving a car.
Even if the statistical chances of an accident or incident were similar, people may still feel safer inside their own vehicle. The nature of typical dangers while driving (e.g. damage or theft of the car) may also be less frightening than those on public transport or bicycle (e.g. personal exposure to violence and theft).
Building affordable and effective public transport and cycle networks may sometimes not be sufficient. For people to leave their cars, trains and buses also need to be safe from crime, and the streets and air quality safe for bicycles.

## Slide 24: Enabling people who build and use technologies
Enabling technologies

## Slide 25: Enabling people - education
Rice University, 1962:
“We choose to go to the moon” 1
https://upload.wikimedia.org/wikipedia/commons/thumb/5/56/John_F._Kennedy_speaks_at_Rice_University.jpg/220px-John_F._Kennedy_speaks_at_Rice_University.jpg
https://cdn.cnn.com/cnnnext/dam/assets/190628104016-apollo-11-mission-control-super-169.jpg 3. https://www.bbc.co.uk/programmes/w3csz4dk
20 July 1969:
Mission control room during moon landing2
when this target was set,
most of these people
were still at school!
(average age 27) 3
..and their job titles did not exist!
Notes: Growth in new technologies needs to be accompanied by growth in people who have the skills to build, maintain and repair them. Some of the expertise needed may require entirely new education pathways, and new courses - like this one you are attending right now, where people are attempting to tell others how to do something that has never been done. But the people who trained the flight controllers in this image had not landed a spacecraft on the moon before either.
As well as new skillsets, any transition will also require huge growth in many existing areas of expertise in related infrastructures and technologies. For example, for the transition from horses to cars a century ago, it would be all very well to have a mechanic available in the nearest town, but if no-one had paved the roads to get there, they wouldn’t be much use. Similarly, the growth in a country’s adoption of hydrogen as a clean fuel in the future could become limited by the availability of traditional welders, or builders, rather than by lack of experts in the hydrogen production itself.

## Slide 26: Enabling people – motivation
“…without repeating the mistakes that man has made in extending his writ around this globe of ours”
…that goal will serve to organize and measure
the best of our energies and skills,
“We choose to go to the moon…
Speech given by John F. Kennedy, largely written by presidential advisor and speechwriter Ted Sorensen
https://web.archive.org/web/20180315230845/https://er.jsc.nasa.gov/seh/ricetalk.htm
because that challenge is one that we are willing to accept,
one we are unwilling to postpone…”
Notes: As well as the scientific training to enable them to adopt clean technologies, belief that the transition is going to happen may be just as critical, as well as some sense of broad agreement within society that it is a good thing. Those elements are unfortunately beyond the scope of this course, but we can borrow further form the example of the Apollo program, and hope that the same sense of purpose can be generated for what is a much more critical situation for humanity than that was.

## Slide 27: Enabling the Energy Transition
“…without repeating the mistakes that man has made in extending his writ around this globe of ours”
…that goal will serve to organize and measure
the best of our energies and skills,
Speech given by John F. Kennedy, largely written by presidential advisor and speechwriter Ted Sorensen
https://web.archive.org/web/20180315230845/https://er.jsc.nasa.gov/seh/ricetalk.htm
because that challenge is one that we are willing to accept,
one we are unwilling to postpone…”
Taken by Apollo 8 astronaut William Anders:
"We set out to explore the moon and instead discovered the Earth”
https://en.wikipedia.org/wiki/Earthrise
Notes: This photo of the Earth taken from orbit around the Moon has been described as “the most influential environmental photograph ever taken” and as marking “the beginning of the environmental movement”. It showed the Earth in its isolation and vulnerability. When the crew of a later apollo mission, Apollo 13, were at this point, they were famously in a damaged spacecraft which was filling up with carbon dioxide, and even if they solved that problem there had insufficient energy to run the spacecraft for re-entry to Earth. Yet the flight control team (some of whom were in the previous photo), working with thousands of industry contractors, found a way to re-design the way the spacecraft’s power and environmental systems could work, and the crew made it. Today, over 50 years on, it is not a 3-person spacecraft that needs to be re-designed and repowered, it is one that holds 8-billion. But we have 8 billion people to do it.

## Slide 28
Stringer M. J., 2023. Lecture 6: Enabling Technologies.
The Electricity Transition Playbook. Release Version 1.0 [online presentation]. Climate Compatible Growth Programme, Green Grids Initiative
Supported by and in collaboration with CCG and Green Grids Initiative
Consolidated by Martin Stringer from CCG and Green Grids Initiative

## Slide 29
This document was updated on 01.11.2024