## Slide 1: LECTURE 5 TIME IN ENERGY SYSTEM MODELS
Introduction to CLEWs

## Slide 2: Learning outcomes
ILO1: Reflect upon the variability of energy demands over time and its effect on the planning of energy infrastructure
ILO2: Reflect upon the variability of energy supply over time and its effect on the planning of energy infrastructure
ILO3: Describe how the variability of energy demand and supply can be captured in the structure of a model
ILO4: Describe the main time-dependent parameters in OSeMOSYS and their use
By the end of this lecture, you will be able to:
Notes: This lecture describes the role of time in energy planning and how time may be represented in energy system models.
By the end of the lecture, you will be able to:
1) Reflect upon the variability of energy demands over time and its effect on the planning of energy infrastructure; 2) Reflect upon the variability of energy supply over time and its effect on the planning of energy infrastructure;
3) Describe how the variability of energy demand and supply can be captured in the structure of a model;
4) Describe the main time-dependent parameters in OSeMOSYS and their use.

## Slide 3: 5.1 Time-dependent demand
Overview
Supply
Demand
Notes: The previous lectures explained what we mean by the energy system and the description of energy supply chains. As such, they presented mostly static pictures of what energy systems look like in specific moments. However, the energy system evolves continuously. There are changes happening both on the supply side and on the demand side. This module focuses on the latter. Changes on the demand side happen at various time scales, within minutes, days, seasons, and years. An example of changes within minutes or hours is when a multitude of people returns home after work every day and starts, at similar times, turning on lights, heating or cooling, stoves, et cetera. In a matter of minutes, the demand for energy in a city or even a country can change significantly. An example on the scale of days can be that during weekends people mostly stay home and do not use energy-consuming appliances from the offices. Therefore, the nature of the energy demand during weekdays or weekends is different. And an example on the scale of seasons is the use of air conditioning when the hot season comes. This can significantly increase demands for electricity. Finally, an example on the scale of years is the change in overall electricity demand due to the slow growth of population and the size of the economy.

## Slide 4: 5.1 Time-dependent demand
A daily life example
Picture source: search.creativecommons.org, image, image, image, image, licensed under CC 0 1.0; SimpleIcon, image, licensed under CC BY 3.0
Notes: The best way to illustrate the concept of variation of the energy demand in an energy system is by starting at the smallest scale and the one closest to us: the energy uses in households. For everyday activities in households, energy is often needed. There is not one constant level of energy use. It rather depends on what activities are performed, when, and for how long. For example, in some moments of the day energy is needed for cooking; in other moments energy is needed to produce hot water; in other moments it is needed for charging phones or for recreational activities. For maintaining a warm space during cold winters or a cool space during hot summers energy will be needed rather constantly through the day. In other words, each appliance or service in a household uses energy with a certain profile that changes in time. Sometimes an appliance is not working and therefore uses no energy, sometimes it uses little energy, and sometimes it uses a significant amount of energy.

## Slide 5: 5.1 Time-dependent demand
A daily life example
Notes: Here a few examples are given on how the use of energy in a household could change during a typical day, according to when different appliances are activated. The profiles of use shown in the figure are fictitious but representative of reality. At the top, the typical use of electricity by a fridge is shown. There is always a certain use of electricity, due to the fact that the fridge needs to be always active. The use is roughly constant through the day, apart from the moments when the fridge needs to run defrosting processes. In the middle, the use of energy by a washing machine is shown, assuming it is activated when coming back home from work in the evening. The cycle of a washing machine lasts a few hours, but there are moments where a great amount of energy is needed to heat the water. At the bottom, the energy use profile of a kettle is shown, assuming it is activated in the morning and after dinner to prepare tea. The time of use is very short, in the order of minutes, but again the water heating can require a great amount of energy in those minutes.

## Slide 6: 5.1 Time-dependent demand
A daily life example
Picture source: Heredia Roberto, image, licensed under CC BY 4.0
Notes: Patterns of use of appliances and services like the ones shown in the previous slide happen in many households across villages, cities, regions, and entire countries. The sum of the energy uses in all the households in a country makes up the country’s residential energy demand. Since the profiles of energy use in the households vary in time, the total residential energy demand also varies in time. The left side of the figure shows a typical daily energy demand profile in the residential sector, for four hypothetical regions in a country. The numbers are based on reality but are fictitious. The profile shows what one would expect considering the average activities in one household. During the night time, when most people are asleep, the energy use is at its minimum. During the day, the energy use settles on an intermediate level, with a small peak in the morning. Finally, the energy use is highest in the evening, when most people come back from work. Similarly, energy use profiles can be constructed for the commercial and industrial sectors by summing up all commercial and industrial uses, respectively. Sample profiles are shown in the centre and right-hand side of the figure. The energy use profile for the commercial sector shows, for example, that most of the energy is used during the day, when most commercial activities are open.

## Slide 7: 5.1 Time-dependent demand
In the longer term
Picture source: Heredia Roberto, image, licensed under CC BY 4.0
Notes: As mentioned at the beginning of this module, the energy demand varies not only on the time scale of minutes or hours. It also varies across seasons and years. The figure shows an example, again based on realistic but fictitious numbers. In the figure, the energy demands for the residential, commercial, and industrial sector are shown again, but this time over several years. Picking, for instance, the line at the top, representing the residential sector, two main types of variations can be seen. One is seasonal, where the energy demand seems higher during the winter and lower during the summer, on average. This is probably due to the need for energy for heating during winters and lower need for cooling during summers. The second type of variation is a trend of steep increase over the years. This may be due to increasing population and increasing economic activity. Similar trends are seen for the industrial and commercial sectors, even though in these cases the seasonal variability is not clear. The variability of demand over time, both in the short and long term, is very important for planning purposes. The reason will become clear in the next modules.

## Slide 8: Lecture 5.1 References
Taliotis, C., et al., Time representation in OSeMOSYS, 2018. Zenodo. http://doi.org/10.5281/zenodo.4585695

## Slide 9: 5.2 Time-dependent supply
Overview
Supply
Demand
Notes: This module continues the discussion about the evolution of the energy system over time and it focuses on changes on the energy supply side. As for demand, changes on the supply side happen at different time scales, from seconds, to minutes, days, seasons, and years. Changes happening within seconds and minutes may include supply–demand imbalances happening on the electricity transmission and distribution networks, which need to be corrected swiftly. Changes happening within hours and days may relate to maintenance interventions on power plants, which force the power plants to be turned down for some time. A change happening over seasons could be, for example, the variation of hydropower electricity output due to lower or higher availability of water during summer. Finally, an example of changes happening over years could be the decommissioning of old power plants or the construction of new ones. There are even changes on the time scale of decades, like the depletion of fossil fuel resources or the integration of power systems at a continental level.

## Slide 10: 5.2 Time-dependent supply
Example: solar photovoltaic
Picture source: Delphi234, photo, licensed under CC 0 1.0, Solargis, photo, licensed under CC BY 4.0
Notes: One cause of changes in the energy supply patterns over seconds, hours, days, and seasons is the electricity supply from variable renewable technologies. This is increasingly important, because variable renewables like solar photovoltaic or wind are responsible for growing shares of electricity supply worldwide, and they are expected to provide the largest share in a few decades. The figure on the left shows how the electricity supplied by one solar photovoltaic panel in a certain location may change during a day and across days. At night, the electricity output is typically zero because sun does not shine. In the central part of the day the output is highest. However, it could change significantly between days and be highest in a clear-sky summer day – see the blue line – lowest in a clear-sky winter day, or highly inconstant during a spring day with unstable weather. It must also be taken into account that the electricity supply potential of a photovoltaic panel and the electricity supply profile change also depending on the location in a region and within a country. The figure on the right shows the high variability of solar electricity supply potential across the world.

## Slide 11: 5.2 Time-dependent supply
Example: wind
Picture source: Roberto Heredia, image, licensed under CC BY 4.0
Reference: Staffell, I., Pfenninger, S., Using bias-corrected reanalysis to simulate current and future wind power output, Energy, 2016, pp. 1224-1239
Notes: This slide shows another example of the variability of electricity supply, related to wind. The electricity output of wind turbines depends on their characteristics, but also on the availability and intensity of wind. As we experience every day, the availability and intensity of wind can change significantly in time and in space. These figures show a series of recorded values of electricity supply by several turbines in a region. The figure on the left shows raw data, which typically span across a range but have a statistical distribution. The figures in the centre and on the left show monthly and hourly average values, with ranges of error. Different types of variations in the supply emerge. There are longer-term trends and shorter-term oscillations. The longer-term trends are, for example, monthly variations, where the supply is significantly higher in some months, due to higher wind speeds. The shorter-term variations can be hourly but also across just a few minutes. They are less predictable. Solar and wind power are not the only time-dependent energy supply options. Other renewable energy supply options are normally subject to variations, like hydropower or geothermal. The electricity supply by biomass power plants or fossil fuel power plants is usually more controllable. However, it may vary for different reasons than the availability of input. It could vary due to market dynamics, or due to outages and maintenance. The same can be said about the supply of energy through storable commodities (such as fuels for transportation or gas for heating). This is controllable, but it could vary due to multiple reasons.

## Slide 12: 5.2 Time-dependent supply
Aggregating to the system level
Picture source: Queenwe, image, image, image, image, licensed under CC BY-SA 4.0
Notes: Like the energy demand, also the energy supply by all assets in a city, region, or country can be summed. The sum of the supply by all assets in a country and the net imports constitute the energy supply of the country. Since the energy supply by the individual assets is variable, the overall energy supply in the considered region or country can also vary over the same time scales, from seconds to years. The figures show, for example, the overall electricity supply by different sources in the United States, across two sample years. By looking at different months, clear seasonal trends in supply from wind – in the top left figure – and hydro power – in the top right – can be identified. On the contrary, the supply from geothermal and biomass power plants – in the bottom left and bottom right figures respectively – seems more insensitive to seasonal changes. If one were to look at variations across days or years, other trends would emerge. Within a period of a few days, variations due to the daily availability of renewables would likely emerge. Across years, variations due to new policies, technological developments, and changes in fuel prices would likely emerge.

## Slide 13: 5.2 Time-dependent supply
Supply–demand matching
Seasonal resource-demand mismatch
Picture source: Roberto Heredia, image, licensed under CC BY 4.0
Notes: It has now been established that both energy demand and supply change with time. But why are these changes important? And why should they be taken into account when modelling the energy system? As seen in the previous slides, energy is used for providing services in different sectors of the economy. Therefore, the demand for energy must be met exactly when the need comes. For example, every time we press the switch for turning on the lights, we expect and need the lights to actually turn on. We certainly do not expect them to turn on an hour later. However, energy resources are not always available exactly to the extent there is need for them. For instance, the figure shows a mismatch in seasonal profiles of water availability for hydropower generation and electricity demand. If the electricity demand in this case were to be met only by means of hydropower, then problems would arise. For the energy demands to be matched exactly when they arise, the supply of energy needs to be planned carefully, both in the short-term and in the long-term. In the short-term planners need to make sure that the existing infrastructure is functional. In the long-term, planners need to make sure that new infrastructure investments are made to meet future (potentially increasing) energy demands. Modellers can create energy system models that calculate how it is possible to match the demands with supply options at all time scales.

## Slide 14: Lecture 5.2 References
Taliotis, C., et al., Time representation in OSeMOSYS, 2018. Zenodo. http://doi.org/10.5281/zenodo.4585695
Staffell, I., Pfenninger, S., Using bias-corrected reanalysis to simulate current and future wind power output, Energy, 2016, pp. 1224-1239, https://doi.org/10.1016/j.energy.2016.08.068

## Slide 15: 5.3 Representing all time scales
Overview
2019
2022
Model horizon
Annual
Seasonal
Summer
Winter
Daily
Day
Night
Day
Night
Notes: This lecture describes how energy system models can be structured so that changes in energy demand and supply over time may be represented. Different energy system modelling tools may look at different time scales. In this case, time scales relevant for OSeMOSYS or similar tools will be targeted. That is, time scales that are relevant for planning. Therefore, changes in the energy system that occur over several years as well as within each year need to be represented. The first item the user should decide on is the model horizon. That is, the start and end year of the period for which the evolution of the energy system is to be analysed. Within this model horizon, the changes in the energy system will be modelled for each year separately. This type of representation looking at consecutive years is called dynamic. The user can decide to further divide each year into several seasons. This is useful for capturing seasonal changes in demand and supply. The example shows a separation of summer and winter. This will allow, for instance, representation of higher demand for cooling during summer and higher demand for heating during winter. The user can also decide to further divide each season into one typical day, split into daytime and night-time. This split may allow the user, for instance, to represent the complete unavailability of solar resource during the night.

## Slide 16: 5.3 Representing all time scales
Years
2019
2022
Model horizon
Annual
Seasonal
Summer
Winter
Daily
Day
Night
Day
Night
SETs:
Year: Years included in the time domain of the model
TimeSlice: Representative time periods that each year is divided into
Notes: Normally, in energy system models the time domain of the model (that is, the number of years) and the resolution of the model (that is, the intra-annual time slices or time steps) are part of the model structure. This means that they are one of the first characteristics that the modeller decides, and they are fixed for a certain model. Different scenarios may be produced with the same model, using different numerical inputs, but the years and the time slices of the model remain the same. In OSeMOSYS, these structural and unchanging characteristics of a model are provided as sets. For refreshing the concept of sets, you may look at lecture 3. The modeller needs to provide the list of all years to be modelled in the set called ‘year’. The decision of which years and time slices to model influences all the following steps regarding the search for model inputs. For example, the modeller may decide to model the evolution of the energy system from 2019 and 2022. This implies that the modeller will have to look for numerical data regarding energy demand and supply for each of the four years, starting from some time in the past, in this case 2019, and creating a projection up to 2022.

## Slide 17: 5.3 Representing all time scales
Years
2019
2022
Model horizon
Annual
Seasonal
Summer
Winter
Daily
Day
Night
Day
Night
SETs:
Year: Years included in the time domain of the model
TimeSlice: Representative time periods that each year is divided into
Notes: Like the modelled years, the intra-annual time slices (or time steps) are also decided at the very beginning of the modelling process and become part of the unchanging structure of the model. The inputs and outputs of the model will be specific to each time slice. In OSeMOSYS, the modeller needs to include the list of all desired time slices in the set called TimeSlice. Referring to the case in the figure, the modeller is splitting each year into four time slices: one that represents a typical summer day, one that represents a typical summer night, one for a winter day, and one for a winter night. Here comes one of the most complicated concepts in energy system modelling. This type of representation of time is not sequential. That is, it does not represent moments in one year that follow each other. It represents portions of the time of one year having similar characteristics of demand and/or supply. For instance, the time slice representing summer days aggregates together all the daytime hours of all summer days, because they have similar characteristics of demand and supply. This aggregate of hours has the duration of roughly one fourth of a year.

## Slide 18: 5.3 Representing all time scales
Calculating the duration of a time slice
Chart: Hourly demand (TJ)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Summer | 4.0984 | 4.0984 | 4.0984 | 4.0984 | 4.0984 | 4.0984 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 4.0984 | 4.0984
Winter | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 28.9256
Notes: The concept of TimeSlice may become clearer through one example. You will be guided through all these calculations in the hands-on material and acquire more familiarity thereof. Let us imagine that we want to create a model capturing average seasonal variations of the electricity demand in a country. The demand varies as in the diagram. During summer, it is higher in the daytime hours due to the need for air conditioning. During winter, it is higher in the night-time hours due to the need for electricity. Looking at the graph, we notice that we can roughly capture these variations by dividing each year of the model time domain into four TimeSlices: a Winter-Night TimeSlice lasting from 8 pm to 8 am; a Winter-Day TimeSlice lasting from 8 am to 8 pm; a Summer-Night TimeSlice lasting from 11 pm to 7 am; a Summer-Day TimeSlice lasting from 7 am to 11 pm. The next slide describes how the duration of these TimeSlices can be calculated.

## Slide 19: 5.3 Representing all time scales
Calculating the duration of a time slice
SUMMER |  | WINTER | 
Apr, May, Jun, Jul, Aug, Sep, Oct, Nov 8 months 244 days |  | Dec, Jan, Feb, Mar 4 months 121 days | 
Day: 7:00 – 23:00 16 hours | Night: 23:00 – 7:00 8 hours | Day: 8:00 – 20:00 12 hours | Night: 20:00 – 8:00 12 hours
= (16 x 244) / 8760 = 0.4457 | = (8 x 244) / 8760 = 0.2228 | = (12 x 121) / 8760 = 0.1657 | = (12 x 121) / 8760 = 0.1657
* No. of hours in a year: 8760
Notes: The duration of each TimeSlice can be calculated as a ratio of the entire duration of one year. One year lasts 8,760 hours. Starting from the Summer-Day TimeSlice, we know that, for each day, it lasts from 7 am to 11 pm. That is, it lasts 16 hours every day. However, the Summer-Day TimeSlice needs to include all summer days. Assuming that summer lasts from April to November (in a very warm country!), it is 244 days long. The total number of hours aggregated under the Summer-Day TimeSlice is calculated by multiplying the number of daytime hours per day by the number of summer days. This means 16 times 244. If the aim is calculating the duration of the TimeSlice as a ratio of the total duration of one year, this number needs to be divided by 8,760 hours. The calculation is shown at the bottom left of the table and delivers 0.4457, that is 44.57% of the duration of one year. You may repeat the same calculation for the other three TimeSlices. Notice that the sum of the four fractions calculated is 1. That is, the summation of the duration of the four TimeSlices needs to add up to one year.

## Slide 20: Lecture 5.2 References
Taliotis, C., et al., Time representation in OSeMOSYS, 2018. Zenodo. http://doi.org/10.5281/zenodo.4585695

## Slide 21: 5.4 Time-dependent parameters
Accumulated Annual Demand: A type of demand that is defined for each year
Specified Annual Demand: A type of demand that is defined for each TimeSlice
Specified Demand Profile: Fraction of Specified Annual Demand for a commodity in each TimeSlice
Capacity Factor: Fraction of a technology’s capacity that can be utilized in each TimeSlice
Annual demand
Notes: Once the structure of the model is set and the number of years and time slices are decided, the modeller may move to filling in values for a series of time-dependent parameters. As seen in previous lectures, the parameters are all those characteristics for which the user can input numerical values. Almost all parameters in a long-term energy system model are dependent on time, but here the focus will be on some of them that need defining early on. You will become familiarized with these in the hands-on exercises. The first parameter is the annual demand. This can be of two types: either accumulated demand or specified demand. The accumulated demand is defined for one year and can be met in any moment during that year. It is typically defined for commodities that can be stored and do not need to be procured in specific moments during a year. For example, a country may have an annual demand for oil products. There will surely be a need for these oil products in different quantities during the year. However, as long as there are enough of them stored in bunkers, when they are bought does not matter. The specified demand is defined for one year and for each time slice. This is typically defined for commodities that cannot be stored and are needed in different quantities during different moments of the year. The best example for this is electricity. As seen before, there is a time-varying profile of electricity demand that needs meeting at every moment.

## Slide 22: 5.4 Time-dependent parameters
Accumulated Annual Demand: A type of demand that is defined for each year
Specified Annual Demand: A type of demand that is defined for each TimeSlice
Specified Demand Profile: Fraction of Specified Annual Demand for a commodity in each TimeSlice
Capacity Factor: Fraction of a technology’s capacity that can be utilized in each TimeSlice
Demand profile
Notes: The demand profile is defined by the user only for those commodities for which a specified annual demand has been defined. It is defined as the fraction of specified annual demand for a commodity that needs to be met in each time slice. The sum of all fractions in a year needs to be 1. As mentioned in the previous slide, this applies well to electricity. For electricity, a modeller needs to define first a value of specified annual demand, which may vary year by year. The annual demand needs to be met by the annual supply of electricity. On top of this, the modeller needs to define also how large a part of the annual electricity demand will come in different moments of the year, through the specified demand profile. For instance how much demand could occur during daytime and night-time in winter and during daytime and night-time in summer. It might happen that 50% of the total annual demand for electricity is concentrated during daytime in summer due to the very high demand for air conditioning. This highly uneven profile of the demand has to be taken into account, because it will affect significantly how the supply is planned.

## Slide 23: 5.4 Time-dependent parameters
Demand profile
Total annual demand (TJ) = 164 * N summer days + 496 * N winter days = 100,000 TJ
*Note that decimals in the table are not shown, therefore the values are approximated
Chart: Hourly demand (TJ)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Summer | 4.0984 | 4.0984 | 4.0984 | 4.0984 | 4.0984 | 4.0984 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 8.1967 | 4.0984 | 4.0984
Winter | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 12.3967 | 28.9256 | 28.9256 | 28.9256 | 28.9256 | 28.9256
Notes: Defining the demand profile for a certain commodity is not trivial. Firstly, it requires data. Often, values for the overall annual consumption of a commodity are publicly available for some years in the past, in reports presenting annual energy balances. However, for understanding when this consumption happened during one year requires much more detailed data, often available only to relevant agencies or utilities. Secondly, the calculation might seem a bit confusing for the modeller, in the first instance. Let us take the example shown in part 5.3 of this lecture. There, the demand for a commodity for each hour of a typical summer day and a typical winter day was available. This is reported again in the graph at the top. Based on that data, the modeller had decided to divide each year in four time slices: summer day, summer night, winter day, and winter night. In part 5.3 we had shown how to calculate the duration of each time slice. That was independent of the demand. Now, we show how to calculate the ratio of demand happening in each time slice. Bear in mind that this ratio can be very different from the duration of the time slice. The table at the bottom helps with the calculation. It presents the numerical value of the demand (in energy units) for every hour of a typical summer and winter day. On the right the summation of all these values is shown. At the bottom the total annual demand in petajoules is calculated.

## Slide 24: 5.4 Time-dependent parameters
Demand profile
TimeSlice | Calculation of value
SD | = (16 * 8.2) * 244 / 100,000 TJ ~ 0.32
SN | = (8 x 4.1) * 244 / 100,000 TJ ~ 0.08
WD | = (12 x 12.4) * 121 / 100,000 TJ ~ 0.18
WN | = (12 x 28.9) * 121 / 100,000 TJ ~ 0.42
Total annual demand (TJ) = 164 * N summer days + 496 * N winter days = 100,000 TJ
*Note that decimals in the table are not shown, therefore the values are approximated
Notes: The demand profile, that is, the ratio of demand occurring in each time slice, needs to be calculated for every time slice. Starting from the time slice representing daytime hours in summer (named SD), one first needs to sum up all the 16 values in yellow in the table. These are then multiplied by the number of summer days (244) and divided by the total demand. The result is 0.32. That is, 32% of the total demand occurs during daytime in summer. The same calculation can be repeated for the other time slices. Be aware that there can be a difference between the duration of the time slice and the fraction of demand occurring in that time slice. For example, in this case, as calculated in part 5.3, the summer daytime time slice takes around 45% of the time in one year. However, it accounts for only 32% of the demand in that year. On the contrary, the winter night-time time slice takes around 17% of the time in one year, but it accounts for 42% of the demand. This shows that, per unit of time, in this example at least, the demand during night-time in winter is much higher than the demand during daytime in summer. Other very different cases can occur and, once more, each can have very different implications for the planning of the supply.

## Slide 25: 5.4 Time-dependent parameters
Accumulated Annual Demand: A type of demand that is defined for each year
Specified Annual Demand: A type of demand that is defined for each TimeSlice
Specified Demand Profile: Fraction of Specified Annual Demand for a commodity in each TimeSlice
Capacity Factor: Fraction of a technology’s capacity that can be utilized in each TimeSlice
Capacity factor
  Solar profile in winter and summer months
Notes: The last time-dependent parameter that is worth mentioning in this lecture is the capacity factor. This is defined as the fraction of a technology’s capacity that can be utilized in each time slice. As described in lecture 4, not all the existing capacity of a technology can be used in every moment, due to a certain frequency of unplanned outages. If 5 gigawatt of gas power plants are in place in a country, it may happen that on average during the month of January only 4.8 gigawatt can be used, because 0.2 gigawatt here and there experience some outages during the same month. This means that, on average, during the month of January, at most 96% of the installed gas capacity can be used. Less can be used, but not more. This is expressed by the parameter capacity factor, which can be defined for all technologies in a model. The capacity factor is particularly important for renewable technologies, but in that case it is used in a slightly different way. It does not express necessarily when the technologies are not available because of outages, but rather when they are not available because the resource is not available. For instance, if the modeller intends to model a solar photovoltaic plant, the modeller knows that the supply profile of the plant will be similar to the one in the figure, which depicts the location’s solar supply profile. Thus, the plant will not produce during the night-time because there is no sun. So, for the time slices representing night-time, the user can set the capacity factor of the solar technology to 0. Calculating the capacity factor is not trivial, especially for renewables. You will familiarize with this in the hands-on exercises. This concludes the part of the course on the energy system. In the next lecture you will be introduced to the land system.

## Slide 26
Gardumi F. (KTH), Shivakumar A. (UNDESA)., Niet T. (SFU)., Sridharan V., Ramos E.P. (KTH)., Alfstad T., (UNDESA) 2021. Lecture 5: Time in energy system models. Release Version 1.0. [online presentation]. Climate Compatible Growth Programme, United Nations Development Program and United Nations Department of Economic and Social Affairs.
CCG courses (this will take you to the website link http://www.ClimateCompatibleGrowth.com/teachingmaterials)
Take Quiz

## Slide 27
This document was updated on 01.11.2024