## Slide 1: Lecture 8 Supply Chain and the Workforce
The Electricity Transition Playbook
Version 1.0
Supported by and in collaboration with CCG and Green Grids Initiative
This material was produced by Ben Marshall at The National HVDC Centre in July 2023.
Notes: Welcome to this presentation on supply chains and the workforce.
As we envision a future that is sustainable, efficient, and environmentally responsible, it becomes really important to address the complex web of activities involved in the procurement, production, and distribution of energy resources. This is where supply chains come into play.
Supply chains encompass the interconnected network of organizations, resources, technologies, and processes that collaborate to deliver goods and services to end consumers. In the context of the energy sector, supply chains play a vital role in ensuring the reliable and efficient flow of energy resources from their source to the point of consumption. This brings us to the second focus of the lecture
the workforce is the driving force behind the successful implementation and operation of any energy system. A well-equipped and skilled workforce is crucial to navigate the complexities of energy supply chains. We must ensure that the workforce is equipped with the necessary knowledge, skills, and training to adapt to these evolving demands. The workforce needs to be agile, capable of harnessing the potential of new technologies, and embracing innovative solutions that drive the energy transition forward.
From engineers and technicians who design and maintain infrastructure to logistics professionals who optimize transportation and storage, every role within the workforce contributes to the smooth functioning of the energy ecosystem.
Getting to net zero will require astonishing growth in solar, wind, and other renewables, plus systems to store energy and feed the grid. This clean energy boom will mean manufacturing new technology in enormous quantities. Supply chains—material, production, and distribution networks—are only as strong as their weakest links. So this kind of brings us to the next slide on making sure that our future supply chains are sustainable, resilient and reliable.

## Slide 2: Overview of the HVDC Centre
The National HVDC Centre is part of Scottish & Southern Electricity Networks. Scottish and Southern Electricity Networks is a trading name of Scottish Hydro Electric Transmission plc, Registered in Scotland No. SC213461, having its Registered Office at Inveralmond House, 200 Dunkeld Road, Perth, PH1 3AQ; and is a member of the SSE Group www.ssen.co.uk
part of
together with
and
The National HVDC Centre is Great Britain’s simulation and training facility for HVDC; supporting the integration and successful operation of all HVDC schemes connecting to the GB Network (including Offshore Wind connections).
The Centre is also the National hub for HVDC knowledge exchange, expertise and innovation.
Notes: Ben Marshall, the technology manager at the UK National HVDC centre based in Glasgow, will provide a case study on supply chain challenges. The National HDVC centre supports transmission owners and electricity system operators across the UK and also integrates a variety of offshore connections. You can see in the blue outlines, the offshore transmission operators and their various connections across the coastlines of GB and it is also one of the many bootstraps reinforcements of HVDC connections to the onshore connections you can see in green and grey. Ben will cover HVDC, what it is, why it is a thing in terms of supply to hit net zero and a bit about the role played by the HVDC Centre.

## Slide 3: Working with stakeholders involved in HVDC
2020-2023 Co-ordinated offshore in GB & supply chain+ R&D strategy that supports it
2021- 2027 R&D strategy Delivery
Engagement, support and collaboration to deliver HVDC networks and individual projects 2013- present
Multi-terminal Multivendor demonstration & specification & design International Advisory and consultancy 2022- present
Notes: HVDC works across a lot of things:
they advise electricity system operators on coordinated offshore solutions to connect all of the windfarms required for net zero policy to be met in GB, via solutions which avoid the status quo, developing the network with onshore connections across the various communities and deliver more than twice the infrastructure we would be able to deliver via much more sophisticated integration
Highlighted the research and development needs, in order to get there
Also highlighted the supply chain challenges in engaging and growing, the majority of future assets which are HVDC
Involved in international initiatives, some in the past, some are ongoing such as our interfaces with the Department for energy in the US
Fundamentally, the HVDC centre knows this space, and advises countries such as South Korea, and advised our own first in a world multiterminal, multivendor demonstration of the Peterhead of a DC network which involves control systems and specifications which the centre has actively contributed and developed over the last 18 months.

## Slide 4: HVDC- what is it, how is it used?
Back to Back HVDC Link (been around for 50+ years in transmission systems):
  Connect asynchronous AC grid
  Transfer power
Point-to-Point HVDC Transmission line link (been around even longer- 60+ years):
  To transmit power to very long distance
  HVDC is employed because of economical reasons and low losses.
HVDC very effective solution to underground/submarine cable-ed systems over long distance:
  Less losses and voltage issues compared to AC
  Can support weak power islands (VSC-HVDC), such as offshore connections/ systems with high renewables in the right places.
Notes: What is HVDC? You have a convertor which the far right is showing, simply it is chopping a DC signal so that you have got plus and minus voltages but you do it in the arrays that you see below it so you are developing something that looks a lot like a sine wave. This is quite a basic amination, in practise you have got hundreds of these semiconductor devises switching to change a voltage which is DC into AC or back again into AC. So that is what the convertor terminals are doing. So you have one of those, a back-to-back between two networks, installed on the network in Sweden, GB and France.
Why is it being used? It is extremely effective over long distances, the reason for that is you don’t have the same voltage challenges that you do with AC so you don’t need as much power to be reserved for charging the cables that you would in an AC system and you don’t need to have intermediate points where you’re regulating the voltage, energising the cables, and switching them on for the first time is also a lot more straight forward than it would be for an AC system of comparable size. So it is a great way of getting over long distances. Also with voltage source control you can almost say that DC stands for direct control because you can control the power islands in a way that even a synchronous power island wouldn’t have been able to do as quickly, directly or accurately. So this means that if you have a load of wind farms connecting into a platform then , which you can see on the slide and is real connecting German system about 700 MW in scale, these collections of assets all need a frequency and voltage to connect to and that’s generated by your convertor on the platform. Convertors are very fast and intelligent, and can do many things but can’t do them all at the same time, they need to be ordered with a hierarchy, unlike your AC system which is all about the physics of big rotating coal, oil and gas generators. Your DC system is all about your control which is firing the valves on the right, and it is about getting that to complement your system to deliver the support and services that are needed.

## Slide 5: We need HVDC- at pace and scale
2) To improve network transmission capability to get electricity from where it is generated, to where it is consumed
3) To interconnect to different Transmission System Operator areas of Europe together to pool intermittent power.
We need HVDC to meet our 2030 (and 2050) commitments:
Source: National Grid Interconnector Register 2021
We are not the only ones- these are worldwide problems!!
1) To connect offshore Wind Farms
Notes: Why are we doing this? We need to deliver at pace and scale, so we need the HVDC systems to connect to wind farms and communicate the power across the networks and we also need them to deliver between different transition system operators areas, so communicate between otherwise asynchronous networks separately operated and controlled where other pools of intermittent resources are in place, so you can get your solar from Spain to GB and you can get your wind to Spain, and harvest the hydro around Europe etcetera. The point about these challenges, they’re all challenges of transitioning to a renewable-dominated system, and the GB aren’t the only ones doing that.

## Slide 6: The problem and a global HVDC response
HND
US wind
Solar,
wind
Sun-cable, Bass link 2, offshore wind
NEDO
Future geo thermal/ solar?
US Macro-grid
X-link, ONEE, Solar
Hydro, solar, wind
Grids, wind
Energy islands, wind
US Macro-grid
Notes: So we are all dealing with the challenges of global warming and COP26 outlined a path towards conversion of electricity to be delivered by renewable sources. But those resources aren’t where the old resources were and the old networks are, and we need to grow our networks to connect to those resources and communicate the power to different places. We also need to pool these networks together so we are insulated from the effects of an intermittent power source, when the wind is not blowing we harvest the solar and hydro etcetera.
You can see on the slide there are lots of things going on in the world, the problem is the supply chain has grown from a project-by-project intermittent activity where you might have a few projects in Europe in every given year, to a situation where in Europe you have got multiple tens of projects going on at the same time. And as you can see there is a lot going on elsewhere.

## Slide 7: HVDC orders in Europe
40 VSC projects in delivery between 2025-2030;
In one week, forward order of 22 converters by one TSO
EU have requested information from SET group on critical components and vendors for consideration of further block-booking of capacity in response to US Inflation reduction act.
Notes: Power islands in Europe, there are lots of areas where there are concentrated artificial islands or convertors bringing wind together- it is mainly about offshore wind in Europe- and then communicating those across international boundaries. So connecting those to lots of different places on the onshore system, or you are connecting between nations so that the resources which are already onshore can be harvested and distributed where they need to be. So that means a lot of interconnections and a lot of networks in the middle of the North Sea, so there is a need for over 40 HVDC projects between now and 2030. There are even more beyond that, Europe has ambition for about 450 GW worth of offshore wind by 2050.

## Slide 8: HVDC orders in the US
Overall aim for 54 + HVDC converters by 2040s
Notes: In the states, similar picture, they have started development engineering on the inset in the left which is the US macro-grid. So all the yellow and blue are HVDC solutions, onshore and offshore, some involving lines, some involving submarine cables. That will be beginning to be built in the 2030s, and towards the late 2030s most of this would be in place, so by the 2040s you’ve got 54 plus convertors coming into being.
The inset on the right is just a bit more detail about the concentrator loops you can see on the East cost, connecting wind into that arrangement. And this is the beginning of other areas having similar integration as well.

## Slide 9: HVDC in South East Asia & Australasia
Japan 1GW only Australasia- Sun cable, plus 3 further major projects.
of extra VSC HVDC. NEDO project has strong similarities to Aquila objectives.
KEPCO up to 12GW of offshore wind, but around 4GW likely as VSC HVDC.
India- new LCC HVDC planned, no new VSC HVDC as yet, but large offshore wind bid zone areas about to be announced.
Notes: In southeast Asia, one of the longest and most ambitious HVDC cables is going into it’s end financing at the moment. So you have solar, batteries and wind going across Singapore and Australia being connected together via an HVDC system.
In Japan, there is a project called NEDO which is looking to build a multiterminal, multivendor offshore spine, connecting wind and reinforcing the network.
And India is beginning the process, KEPCO in South Korea is also doing quite a lot, you can see the scale of what is being done above.

## Slide 10: Areas of support needed for HVDC
Activity 4 – Specifying what you need to de-risk your project(s)- replicas etc
Activity 12 – Replica Hosting and operational support/ investigation
Activity 9 – Commissioning Support
Activity 3 –Initial Design Review
Activity 1 – Training- what do you need to know!
HVDC project- typical timeline
Activity 5 – Detailed Design Review – and understanding the consequences of that!
Activity 2 –
“Art of the possible” analysis
Activity 6 –being able to model what you want and describe “what good looks like”
Activity 7 – FAT results review
Activity 8 –”enhanced” FST- checking your risks too!
Activity 11 –Operator training
Activity 13–Interaction analysis, integration with other delivered/ commissioned projects
Activity10 – protection Co-ordination testing
Feasibility & Options
Planning & Development
Tender/
Bid phase
Base Design
Detailed Design
FST/ FAT
Commis-sion
Operation& support
Upgrades
Refurbishment
Areas of vendor
support needed
Notes: To highlight, there are many things you need to support HVDC. So the suppliers are providing outputs across a typical HVDC project outline, and you can see there even in the early stages there are outputs into activities which you need to make sure you are doing to make sure a HVDC system works for you, and sits alongside other things.
And then when you get into base design and detail design, there are even more activities you need to consider and get information out of the vendors.
Whilst there has been block booking of factory slots, in Europe 22 slots have been taken up, most of that within a month and complemented 18 pre-existing factory slots being booked up. There is a lot of work going beyond that to try and make sure that factory slots are translated into real projects that work for real systems.
Some of the other things you need to do before you get to commissioning, and these are all important because you are trying to marry some programmable logic of what you want HVDC to do, with a system that behaves with physics at the moment. So you are trying to make sure that you have a specification of a control that works well with your network, and that the kit works, and is then supported, upgraded and refurbished as it goes through it’s life.
So you don’t want any of these yellow points of interface to become another sticking point along the road in delivering for net zero your HVDC projects

## Slide 11: Key take-aways
World-wide pressures on HVDC supply chain
  If we are not careful; we compete within a limited pool of resources, and do not send the signals that grow its capability
Forward orders have already saturated many of the vendors order books
  We need to broaden supply chains and get the most out of the existing ones- how do we make things easy for ourselves, and the vendors?
  Standardise, modularise, focus on what vendors are best at!
Existing activity is “tip of the iceberg”- even more is on the horizon
  How do we work collaboratively to avoid “road blocks in the supply chain
  We need to be growing capability now ahead of later growth.
To stimulate supply chain growth we need to provide clear investment certainty, signals & incentives
  Anticipatory decision making to enable long term Supply chain
  benefits.
Notes: Some of the key takeaways are around the worldwide pressures, so we are moving from a project-by-project incremental activity on HVDC to something that is much more industrial line production basis. And if we are not careful we will all end up competing for a very limited pool of resources, and we won’t send the right messages out to the vendor that he needs to grow his capability.
So what are these messages? Part of it is broadening the supply chain, making sure we have the most actors we can who are all cooperating and collaborating together. We can’t expect these future solutions to all be dominated by one vendor's solution and design. That also pushes the point about standardising and modularising what you do, so if we were building an AC system we wouldn’t have bespoke products for every new overhead cable and transformer. The same thing applies here, HVDC is beginning to be much more standardised in the capacities you get, the voltages it operates at and how it is being specified, and then the control system is tuned to the individual projects needs but again in a much more standardised way.
And you focus on the vendors delivering that and as an entity; whether you are a government, a developer or a operator you focus on doing the most you can to make the vendors road that much easier. So if that means building the site that the convertor sits on, if that means handling the integration of a convertor contract with a cable contract, these are the sorts of things that you need to grasp and be comfortable with. It needs to be really collaborative working, we need to be growing our capacity to manage this. The convertors aren’t best placed to do everything so we have got to be able to step in and do the things that we need to do which is specific to the projects and systems that we are building.
The other point the vendors need is clarity, they need to see that pathway to future capacity is required, they need that direction and comfort that any decisions they make now are not going to be stranded assets in the future; they’re not going to be driving huge recruitment now only to need large lay-offs in the future, so we need to give them that visibility of what is coming down the line.

## Slide 12
Marshall, B., Luscombe, H., 2023. Lecture 8: Supply Chain and Workforce – Case Study. The Electricity Transition Playbook. Release Version 1.0 [online presentation]. Climate Compatible Growth Programme, Green Grids Initiative
Supported by and in collaboration with CCG and Green Grids Initiative
Consolidated by Ben Marshall and Hannah Luscombe from CCG and Green Grids Initiative

## Slide 13
This document was updated on 01.11.2024