## Slide 1: Lecture 3: Collecting infrastructure data
Sapphire Vital, Oxford University

## Slide 2: Learning Outcomes
By the end of this lecture, you will:
Know the key principles for collecting infrastructure data
Collecting infrastructure data is the first step in evidence-based infrastructure development processes. It is the foundation for estimating future infrastructure needs, setting targets, developing scenarios, and ultimately choosing optimal infrastructure development pathways.
Know the types of data that need to be collected, research methodologies, and infrastructure carbon emission estimation
The last mini-lecture illustrates the application of best practices in a case study of Curaçao
2

## Slide 3: 3.1 Overview of needed infrastructure data
Learning Objectives
Indicate critical data fields needed to assess current infrastructure systems
Describe the utility of each type of data needed
3

## Slide 4: 3.1 Overview of needed infrastructure data
Introduction
Evaluating the status of current infrastructure systems is the first step in the evidence-based infrastructure development process (Adshead, Fuldauer, et al. 2018)
The collected data enables the analysis of future infrastructure needs and informs infrastructure development strategies
The needed data covers key technical, social, economic, and environmental features of infrastructure systems
4
Evidence-based infrastructure development process (Adshead, Fuldauer, et al. 2018)

## Slide 5: 3.1 Overview of needed infrastructure data
Technical features of infrastructure systems: Supply versus demand
Infrastructure systems consist of supply and demand components
Supply infrastructure provides the specific infrastructure service
Demand elements drive how much of the service is needed
The most common demand components include domestic, commercial, industry, and system losses
Specific areas within these categories may also be considered
For instance, for the waste sector, demand data may be collected based on the disposal protocol for different materials
5
Networked infrastructure system | Supply infrastructure | 
Electricity | Diesel generation Nuclear reactors Natural gas power plants Coal power plants Solar thermal or photovoltaic systems | On and offshore wind farms Hydropower generation facility Geothermal plant Biomass energy generation Waste to energy facilities
Transport | Modes: cars, trucks, buses, trains, aircrafts, boats Route infrastructure: road networks, railroads | Terminal infrastructure: bus and train stations, airports, freight ports, cruise ship terminals Fueling stations: gas stations, electric vehicle charging ports
Water (including wastewater) | Water and wastewater treatment plants Desalination plants Raw intakes Water distribution systems | Sewerage networks Septic tanks Pit latrines
Waste | Landfills Dumps | Recycling facilities Waste to energy facilities
Digital communication | Fixed telephone networks Mobile networks | Fixed broadband networks Data centres
Inexhaustive examples of supply assets of network infrastructure systems (Adshead, Roman, et al. 2018; Adshead et al. 2020; Malmodin and Lunden 2018)

## Slide 6: 3.1 Overview of needed infrastructure data
Technical features of infrastructure systems: Capacity and design life
Important to capture the capacity of each infrastructure system
Capacity refers to the quantity of service each infrastructure component can supply
The units used should be uniform
It is also important to note the design life or lifespan of each infrastructure component in order to assess their operation statuses
For instance, a diesel electricity generation plant may provide a significant portion of electricity to a community but be aged and in need of replacement within two years
The facility would therefore be a critical consideration when projecting future infrastructure needs
6
Networked infrastructure system | Capacity Description
Electricity | Power generation ability: Static generation is measured in Watts (W) while generation over a period of time is measured in Watt hours (Wh)
Transport | Number of transportation modes in the country by type Length of transportation routes measured in kilometres or miles Estimated number of transportation modes accommodated by transportation routes Number of transportation terminals Number of modes (buses, airplanes, boats etc.) accommodated by transportation terminals
Water (including wastewater) | Volume of water supplied over a period of time often measured in cubic metres per year
Waste | Weight of waste disposed often measured in tonnes
Digital Communication | Number of static network towers Length of network transmission infrastructure
Examples of infrastructure capacity descriptors in networked infrastructure systems (Adshead, Roman, et al. 2018)

## Slide 7: 3.1 Overview of needed infrastructure data
Social features of infrastructure systems: Population served
The number of people served by infrastructure system assets indicates the coverage of that particular service
Comparing the percentage of population with access to services to national targets illuminates the gaps that need to be filled and the underserved proportion of the population (given the location of the service provision is also specified)
This knowledge is needed to design country specific infrastructure development strategies
For instance, a country may be 100% electrified but has wastewater treatment facilities that only cover its capital. This country therefore would allocate more resource towards improving the wastewater system
7

## Slide 8: 3.1 Overview of needed infrastructure data
Economic features of infrastructure systems: monetary value
The capital and expenditure costs of infrastructure assets are needed to evaluate the cost-effectiveness of varying infrastructure development strategies
For example varying types of electricity interventions have different price points over their lifespans: geothermal energy generation plants have high initial costs but high energy generation at low implementation costs over a long design life, while a diesel energy generation plant may initially cost less but incur high fuel bills over its lifespan
Long-term infrastructure strategies that maximise sustainable development and consider the Paris Agreement are the most cost-effective (Adshead et al. 2021)
Such strategies take advantage of interdependencies between infrastructure systems as well as low-hanging fruit such as improving system efficiency
8

## Slide 9: 3.1 Overview of needed infrastructure data
Environmental features of infrastructure systems: Carbon emissions
The carbon emissions from each infrastructure component should be estimated to capture the contribution of the infrastructure systems to climate change
Other environmental attributes of infrastructure systems, such as landfill versus recycling and conventional vehicles versus electric vehicles, are captured in the data on systems’ technical features
Estimating carbon emissions can be approached via a variety of methodologies
Data on the carbon intensity of infrastructure assets may be obtained from national greenhouse gas inventories whose methodologies should reflect the recommendations and guidelines of the United Nations Framework Convention on Climate Change
9

## Slide 10: 3.1 Overview of needed infrastructure data
Summary
Overview of the data required to assess the current performance of infrastructure systems
The data required, inclusive of technical, social, economic, and environmental components, is needed to evaluate infrastructure gaps, project future needs, and ultimately devise infrastructure development strategies in line with national priorities and global agendas such as the Sustainable Development Goals and the Paris Agreement
10

## Slide 11: 3.1 Overview of needed infrastructure data
Bibliography
Adshead, D., L. Fuldauer, S. Thacker, A. Hickford, G. Rouhet, W. S. Muller, and J. W. Hall. 2018. “Evidence-based infrastructure: Curacao. National infrastructure systems modelling to support sustainable and resilient infrastructure development.” Copenhagen, Demark: United Nations Office for Project Services. https://www.unops.org/expertise/.
Adshead, D., L. Fuldauer, S. Thacker, O. Roman, S. Vital, F. Felix, C. Roberts, et al. 2020. “Saint Lucia: National Infrastructure Assessment.” August. United Nations Office for Project Services.
Adshead, D., O. Roman, S. Thacker, F. Felix, L. Fuldauer, and A. J. Hickford. 2018. “Long-term strategic infrastructure planning model for Saint Lucia: Version 1.0.” University of Oxford; United Nations Office for Project Services.
Adshead, D., O. Roman, S. Thacker, and J. W. Hall. 2021. “Infrastructure Strategies for Achieving the Global Development Agendas in Small Islands.” Earth’s Future 9 (2). https://doi.org/10.1029/2020EF001699.
Malmodin, J., and D. Lunden. 2018. “The energy and carbon footprint of the global ICT and E & M sectors 2010-2015.” Sustainability (Switzerland) 10 (9). https://doi.org/10.3390/su10093027.
11

## Slide 12: 3.2 Methods of gathering infrastructure data
Learning objectives
Describe and utilise effective methods to gather infrastructure information
12

## Slide 13: 3.2 Methods of gathering infrastructure data
Introduction
Research has shown that evidence-based infrastructure planning rooted in participatory processes yield the best results (Fuldauer et al. 2019)
Infrastructure planning has often been fragmented; stakeholders from each infrastructure system have operated in their silos and missed sustainable development opportunities that arise from collective action
Participatory research facilitates integrated cross-sectoral infrastructure planning by involving key stakeholders throughout the planning process (Fuldauer et al. 2019)
Two key aspects of participatory research:
Desktop studies: Involves extracting key information from key documents and conducting stakeholder mapping
Stakeholder engagement: Involves interviewing key stakeholders across the public and private sector and civil society
13

## Slide 14: 3.2 Methods of gathering infrastructure data
Participatory research in the evidence-based infrastructure development process
14
Participatory engagement involvement in the evidence-based infrastructure development process (Fuldauer et al. 2019)
Participatory research methods can be utilised throughout evidence-based infrastructure development process from data collection to scenario planning, modelling and evaluating infrastructure strategies, and developing action plans
Involving key stakeholders throughout the planning process enables the stakeholders to take ownership of the development plans
It facilitates commitment to implementation through interdisciplinary collaboration and coordinated efforts (Fuldauer et al. 2019)
Stakeholders play a critical role in collecting the data needed to evaluate the performance of current infrastructure
This can be achieved through desktop studies, stakeholder interviews, and workshops

## Slide 15: 3.2 Methods of gathering infrastructure data
Desktop studies
Desktop studies consist of conducting research to capture physical infrastructure data as well as develop a multi-level stakeholder map
Conducting a multi-level stakeholder map involves identifying influential stakeholders in each infrastructure system
Target stakeholders who can influence or be affected by the infrastructure planning process (Fuldauer et al. 2019)
Information on infrastructure data and stakeholders can be obtained through open-source policy documents, strategies, plans, assessments, studies, and reports
These documents can often be found on the websites of relevant government ministries and departments, utilities, regional and international research institutions, and international development agencies, among others
Primary or secondary data, or point towards the source of primary data
15

## Slide 16: 3.2 Methods of gathering infrastructure data
Stakeholder engagement
Stakeholders should be consulted to verify the information found, provide the most up-to-date information, and/or to fill any data gaps
If the key stakeholders identified are not able to access the most recent data, they are often able to direct towards another actor who can
While there are different ways of engaging with stakeholders, semi-structured interviews and workshops through snowball sampling are most efficient when the stakeholders’ roles are not clearly defined or easily identified externally (Fuldauer et al. 2019)
Snowball sampling involves identifying a core group of stakeholders and asking them to point you towards other stakeholders you should speak to
For semi-structured interviews researchers develop broad topics and sample questions they would like to ask but leave room for changes depending on the direction of conversations
16
Questions used to guide semi-structured interviews on infrastructure development in line with the Paris Agreement and the Sustainable Development Goals (Vital 2019)

## Slide 17: 3.2 Methods of gathering infrastructure data
Summary
Overview of methods to gather infrastructure information, grounded in participatory processes
The mini-lecture highlighted the use of desktop studies and stakeholder engagement
Further application of participatory processes is addressed in subsequent lectures
17

## Slide 18: 3.2 Methods of gathering infrastructure data
Bibliography
Fuldauer, L. I., M. C. Ives, D. Adshead, S. Thacker, and J. W. Hall. 2019. “Participatory planning of the future of waste management in small island developing states to deliver on the Sustainable Development Goals.” Journal of Cleaner Production 223: 147–62. https://doi.org/10.1016/j.jclepro.2019.02.269.
Vital, S. 2019. “Infrastructure Development through the Lens of Mitigation and Sustainable Development: The St . Lucia Case Study.” MSc, University of the West Indies.
18

## Slide 19: 3.3 Estimating infrastructure carbon emissions
Learning objectives
Estimate gross carbon emissions of infrastructure systems
19

## Slide 20: 3.3 Estimating infrastructure carbon emissions
Gross carbon emissions calculation method
Step 1 - Identify the carbon emissions per unit for each type of infrastructure asset (capacity factor).
For example, the capacity factor of a hydropower system would be measured in tCO2eq/kWh (tonnes of carbon dioxide equivalent per kilo watt hour)
Step 2 - Identify the capacity of the infrastructure assets
Step 3 - Conduct any unit conversion needed.
Following on from the previous example, if the given capacity factor of a hydropower plant is reported to be 25 gCO2eq/kWh (grams of carbon dioxide equivalent per kilo watt hour) and its capacity is 10 GWh (giga watt hour), unit conversion needs to take place to ensure correct calculation. The conversion would be as follows:
1g = 0.000001 tonnes
Therefore: 25 gCO2eq/kWh= 0.000025 tCO2eq/kWh
1 GWh= 1,000,000 kWh
Therefore: 10 GWh= 10,000,000 kWh
Step 4 - Multiply the capacity factor by the capacity of an infrastructure asset to determine its gross emissions:
Gross Carbon Emissions (tCO2eq) = Capacity Factor ×Capacity
For instance, the hydropower plant:
Gross Carbon Emissions= 0.000025 x 10,000,000 = 250 tCO2eq annually
20

## Slide 21: 3.3 Estimating infrastructure carbon emissions
Identifying capacity factors
Emissions capacity factors can be sourced from a variety of academic and institutional research
Intergovernmental Panel on Climate Change (2014), provides a summary assessment of capacity factors for various sectors as well as more detailed methodologies for determining carbon emissions
Availability and quality of carbon emission data vary significantly across sectors
The following sections present the available capacity factors for the energy, transportation, wastewater and waste infrastructure systems. Where minimum, median, and/or maximum factors are given, estimates can be made using the median or average value
21

## Slide 22: 3.3 Estimating infrastructure carbon emissions
Energy
22
Emissions of electricity supply technologies. The capacity factors for the energy system are described as the lifecycle emissions and are measured in gCO2eq/kWh (Intergovernmental Panel on Climate Change 2014)

## Slide 23: 3.3 Estimating infrastructure carbon emissions
Transport
23
The capacity factor for the transportation system is noted as gCO2eq/p-km (grams of carbon dioxide equivalent per passenger kilometre)
The capacity would therefore be the number of kilometres traversed by passengers using a particular transportation mode
Intergovernmental Panel on Climate Change (2014) specified data for commercially available technologies, and expected future passenger and freight transportation
Passenger transport emissions factors for commercially available technologies (Intergovernmental Panel on Climate Change 2014)

## Slide 24: 3.3 Estimating infrastructure carbon emissions
Waste and wastewater
Intergovernmental Panel on Climate Change (2014) notes several capacity factors for Municipal Solid Waste (MSW) given the two common greenhouse gases emitted from landfills:
Methane emissions: Measured in gCH4/kg MSW (grams of methane per kilogram of Municipal Solid Waste)
Nitrous oxide emissions: Measured in gN2O/kg MSW (grams of nitrous oxide per kilogram of Municipal Solid Waste)
These values are then combined and converted to tCO2eq/t MSW (tonne of carbon dioxide equivalent per tonne of Municipal Solid Waste). This factor would be used to calculate gross carbon emissions
The capacity factor for wastewater is stated in tCO2eq/tBOD5 (tonnes of carbon dioxide equivalent per tonne of biological oxygen demand)
24
Wastewater capacity factor (Intergovernmental Panel on Climate Change 2014)
Depiction of the capacity factors for waste treatment technologies (Intergovernmental Panel on Climate Change 2014)

## Slide 25: 3.3 Estimating infrastructure carbon emissions
Summary
Mini-lecture 3.3 illustrated a simple method for estimating the carbon emissions of infrastructure systems in lieu of detailed in-country data
The mini-lecture further pointed towards a good source of carbon emission capacity factors: Intergovernmental Panel on Climate Change (2014)
25

## Slide 26: 3.3 Estimating infrastructure carbon emissions
Bibliography
Adshead, D., O. Roman, S. Thacker, F. Felix, L. Fuldauer, and A. J. Hickford. 2018. “Long-term strategic infrastructure planning model for Saint Lucia: Version 1.0.” University of Oxford; United Nations Office for Project Services.
Intergovernmental Panel on Climate Change. 2014. “Technology-specific Cost and Performance Parameters.” Climate Change 2014 Mitigation of Climate Change, 1329–56. https://doi.org/10.1017/cbo9781107415416.025.
26

## Slide 27: 3.4 Case study: Curaçao
Learning objectives
Apply best practice data collection methods to a specific country context
27

## Slide 28: 3.4 Case study: Curaçao
Introduction
Infrastructure planning conducted for the island of Curaçao in 2018 (Adshead et al. 2018)
Focus on the island’s solid waste system as elaborated by Fuldauer et al. (2019)
Curaçao is a Small Island Developing State (SIDS) off the coast of Venezuela
The island’s main economic activity is tourism
150,000 residents + 750,000 tourists annually (Fuldauer et al. 2019)
The strain of this high volume of tourists on Curaçao’s infrastructure systems leads to high per-capita infrastructure costs
Sustainable infrastructure development, particularly in the solid waste system, is a challenge for the island (Fuldauer et al. 2019)
28

## Slide 29: 3.4 Case study: Curaçao
29
Solid waste data collected
Two main sources and complemented by other resources: the Central Bureau of Statistics Curaçao and the Waste Management Processing Plant Curaçao Design Feasibility Study
Municipal solid waste as well as commercial, stay-over tourist-generation, and cruise-ship tourist-generated waste
Capacity, cost, and carbon emissions of infrastructure assets
Additional information on the population and per capita waste production
Some data was locally sourced while other data was sourced from international studies
Average per capita waste generation in the Caribbean of 1.1kg/capita/day
The most up to date data was obtained along with the lifespans of infrastructure assets
Core data collected on waste infrastructure assets’ capacity and cost (Fuldauer et al. 2019)
Population and per capita data collected on Curaçao’s waste sector (Fuldauer et al. 2019)
Graphical depiction of Curaçao’s solid waste sector (Adshead et al. 2018)
Notes: There are now several open-source hazard products at global scales which are being used widely for vulnerability and risk analysis. A few resources include:
Global river and coastal flood maps: Historical and future hazard maps at different return periods (2, 5, 1, 25, 50, 10, 250, 500, 100 years). All data is available at a 30 arc-seconds resolution (~1km at equator) (Gassert et al. 2015).
Global hazard maps for earthquakes for different return periods (250, 475, 975, 1500, 2475 years) both Peak Ground Acceleration and spectral acceleration. Data is available at 0.072 degrees (~8km at equator).
Global dataset of 1,000 synthetic tropical cyclones paths with cyclone characteristics (e.g., wind speed, pressure) on a global scale. Wind speed probabilities are derived globally (1 metre, 1 minutes sustained speed) for different return periods (1 to 1,000 years) at 1km resolution (Bloemendaal et al. 2019).

## Slide 30: 3.4 Case study: Curaçao
Stakeholder engagement
Stakeholder consultation was conducted to complement the data obtained from the desktop study
The desktop study brought about a list of key stakeholders: 20 priority stakeholders were specified based on their organisation, and level and field of education (Fuldauer et al. 2019)
The Ministry of Health, Environment and Nature: holds jurisdiction over waste management and related policies
Slikor: Curaçao’s main waste management company that collects domestic waste, manages the island’s sole landfill, incinerates special wastes such as chemicals, and cleans up unmanaged waste
Greenforce: a recycling company
The Caribbean Recycling Company: a recycling company
Antillean Scrap Co: a recycling company
Stakeholders were engaged to provide context for the waste sector and fill any data gaps via semi-structured stakeholder interviews. The broad range of stakeholders enabled the researchers to capture a wide variety of views. Most of the stakeholders agreed that Curaçao’s existing waste sector is unsustainable and action is particularly required to ensure environmentally safe recycling practices and disposal of chemical waste
30

## Slide 31: 3.4 Case study: Curaçao
Resulting map of Curaçao’s waste management system
31
Curaçao generated 257,000 million tonnes of waste, in decreasing order, by commercial entities, residential homes, stay-over tourists and cruise-ship tourists
Only tourists’ waste was collected by the island’s sole waste company Selikor
Most of the island's waste was disposed of in the landfill
The balance of the waste, in decreasing order, was recycled, incinerated, reused or exported.
Curaçao’s existing waste management system; MT=million tonnes (Fuldauer et al. 2019)

## Slide 32: 3.4 Case study: Curaçao
Summary
Mini-lecture 3.4 provided an insight into the application of the principles laid out in mini-lectures 3.1- 3.3 to a specific country context
The mini-lecture provided useful insights on data collection and stakeholder engagement from an infrastructure development perspective of the waste sector in the island of Curaçao
32

## Slide 33: 3.4 Case study: Curaçao
Bibliography
Adshead, D., L. Fuldauer, S. Thacker, A. Hickford, G. Rouhet, W. S. Muller, and J. W. Hall. 2018. “Evidence-based infrastructure: Curacao. National infrastructure systems modelling to support sustainable and resilient infrastructure development.” Copenhagen, Demark: United Nations Office for Project Services. https://www.unops.org/expertise/.
Fuldauer, L. I., M. C. Ives, D. Adshead, S. Thacker, and J. W. Hall. 2019. “Participatory planning of the future of waste management in small island developing states to deliver on the Sustainable Development Goals.” Journal of Cleaner Production 223: 147–62. https://doi.org/10.1016/j.jclepro.2019.02.269.
33

## Slide 34: Thank you
www.climatecompatiblegrowth.com