## Slide 1: Lecture 4: Future infrastructure demand
Orlando Roman, Oxford University

## Slide 2: Learning Outcomes
By the end of this lecture, you will:
Understand important concepts for infrastructure demand estimation, including main drivers and important scenario analysis methods, such as the Shared Socio-economic Pathways (SSPs)
Know the specific drivers and considerations for the process of demand forecasting and have clear the learning outcomes through practical applications in developing country contexts
2

## Slide 3: 4.1 Overview of future infrastructure demand and drivers
Learning Objectives
Recognise the importance of defining uncertainty in future infrastructure planning
Identify potential drivers of infrastructure demand
3

## Slide 4: 4.1 Overview of future infrastructure demand and drivers
Introduction
Demand for infrastructure is driven by complex future social, economic and technological changes, which are highly uncertain and difficult to estimate
Demographic changes, urbanisation, migration, environmental factors, institutional development, etc.
A lack of infrastructure is a major problem for developing countries, exacerbated in the coming decades due to significant population growth
In this lecture:
Methodologies to forecast investment/policy needs, usually developed for climate change adaptation and mitigation, to understand how uncertainties are considered in other contexts
Nature of infrastructure as long-lived assets, and why it is important not to follow a predict-then-act approach, but to predict a range of possible futures, recognising uncertainty
Main future trends in developing countries and their consequences for infrastructure demand
4
World Population Forecast by 2100 (based on data from United Nations Department of Economic and Social Affairs (2019))

## Slide 5: 4.1 Overview of future infrastructure demand and drivers
Infrastructure as long-lived assets
Emerging markets and developing economies will require annual infrastructure investments of around USD1 trillion (Ruiz-Nuñez and Wei 2015)
Electricity and roads account for more than 66% of the total investment needed by 2040
Furthermore, from 2016 to 2040, approximately USD 94 trillion (USD 3.7 trillion per year) will be needed globally
Appropriate infrastructure projections and decision-making processes important to prevent locking countries in unsustainable and irreversible development patterns and huge infrastructure challenge that the developing world needs to tackle over the next decades
Infrastructure lasts for decades so the decisions made in the present need to recognise the future demand. The nature of these long-term trends is uncertain and hard to predict (Thoung et al. 2016). Therefore, a predict-then-act approach is not recommended for these long-lived assets, but rather to predict a range of possible futures in recognition of this uncertainty
5
Growing annual infrastructure investment requirements by sector (based on data from Global Infrastructure Hub (2020))

## Slide 6: 4.1 Overview of future infrastructure demand and drivers
Scenario analysis for infrastructure investments
Scenario: internally consistent view of what the future might turn out to be - not a forecast, but one possible future outcome (Porter 1985)
One method crafted with the intention of including societal, environmental and economic uncertainty/complexity is the Integrated Assessment Modelling (IAM) approach, which has been used to inform policymaking in the context of climate change (Beek et al. 2020)
Shared Socio-Economic Pathways (SSPs): project global scenarios of socio-economic change to the end of the century with the intention of characterising uncertainty in mitigation, adaptation and impacts of climate change
Socio-economic and environmental challenges are classified as pertaining to adaptation or mitigation
This way of characterising uncertainty and its implications of mitigation or adaptation, enables the exploration of future socio-economic pathways that make these processes harder or easier (O’Neill et al. 2014)
Exploratory nature of this forecasting exercise (presenting multiple future scenarios) as opposed to normative scenarios (building toward one vision of the future)
6
The challenge space of SSPs (O’Neill et al. 2014)

## Slide 7: 4.1 Overview of future infrastructure demand and drivers
Shared Socio-economic Pathways (SSPs)
SSP1: Sustainability – Taking the Green Road, in which the world shifts gradually toward a more sustainable path. This scenario has low challenges to mitigation and adaptation
SSP2: Middle of the Road in which historical trends in social, economic and technological changes continue. This scenario has medium challenges to mitigation and adaptation
SSP3: Regional Rivalry – A Rocky Road, in which nationalism and regional conflicts push countries to focus on their own goals and needs. This scenario has high challenges to mitigation and adaptation
SSP4: Inequality – A Road Divided, in which there are high inequalities and technological disparities between different regions. This scenario has low challenges to mitigation and high challenges to adaptation
SSP5: Fossil-fuelled Development – Taking the Highway, in which there is rapid technological progress and growth by exploitation of natural resources. This scenario has high challenges to mitigation and low challenges to adaptation
7

## Slide 8: 4.1 Overview of future infrastructure demand and drivers
Infrastructure drivers
When confronting with the difficult task of forecasting infrastructure demand, there are many drivers that may have a potential impact on the future. Some of the most important drivers that can influence infrastructure demand are described as follows:
Population growth, is the most common driver of infrastructure demand. There are many global, regional and local population forecasts and the proportional growth of population and demand is easy to compute
Economic Development, can modify future demand given that there is a close relationship between economic development and level of consumption. On the other hand, infrastructure can produce economic development as well
Consumption patterns, are related to economic development but are also influenced by changes in culture or behaviour. For example, an increase in recycling and efficient use of energy and water will shape the future demand of infrastructure
Technology, is usually related to the supply side (new ways of production) but can also influence demand (efficiency, new transportation modes).
Urbanisation, migration and tourism, are of particular importance in developing countries in which an important increase of rural-to-urban migration is expected
Demographics (age and gender), can influence consumption patterns and shape the overall demand for infrastructure
8
Forecasting of different drivers under the SSPs (Riahi et al. 2017)

## Slide 9: 4.1 Overview of future infrastructure demand and drivers
Summary
In this mini-lecture, the complexity that the future poses on infrastructure was described
This mini-lecture explains the concept of Shared Socio-economic Pathways (SSPs) as a tool to project global scenarios
This concept is also used to introduce some basic ideas about infrastructure demands and drivers
9

## Slide 10: 4.1 Overview of future infrastructure demand and drivers
Bibliography
Beek, Lisette van, Maarten Hajer, Peter Pelzer, Detlef van Vuuren, and Christophe Cassen. 2020. “Anticipating Futures Through Models: The Rise of Integrated Assessment Modelling in the Climate Science-Policy Interface Since 1970.” Global Environmental Change 65 (November): 102191.
Global Infrastructure Hub. 2020. “Infrastructure Monitor.”
O’Neill, Brian C., Elmar Kriegler, Kristie L. Ebi, Eric Kemp-Benedict, Keywan Riahi, Dale S. Rothman, Bas J. van Ruijven, et al. 2017. “The Roads Ahead: Narratives for Shared Socioeconomic Pathways Describing World Futures in the 21st Century.” Global Environmental Change 42 (January): 169–80.
O’Neill, Brian C., Elmar Kriegler, Keywan Riahi, Kristie L. Ebi, Stephane Hallegatte, Timothy R. Carter, Ritu Mathur, and Detlef P. van Vuuren. 2014. “A New Scenario Framework for Climate Change Research: The Concept of Shared Socioeconomic Pathways.” Climatic Change 122 (October): 387–400.
Porter, Michael E. 1985. Competitive Advantage : Creating and Sustaining Superior Performance. Free Press ; Collier Macmillan.
Riahi, Keywan, Detlef P. van Vuuren, Elmar Kriegler, Jae Edmonds, Brian C. O’Neill, Shinichiro Fujimori, Nico Bauer, et al. 2017. “The Shared Socioeconomic Pathways and Their Energy, Land Use, and Greenhouse Gas Emissions Implications: An Overview.” Global Environmental Change 42 (January): 153–68.
Ruiz-Nuñez, Fernanda, and Zichao Wei. 2015. “Infrastructure Investment Demands in Emerging Markets and Developing Economies.”
Thoung, Chris, Rachel Beaven, Chengchao Zuo, Mark Birkin, Peter Tyler, Douglas Crawford-Brown, Edward J. Oughton, and Scott Kelly. 2016. “Future Demand for Infrastructure Services.” The Future of National Infrastructure: A System-of-Systems Approach. Cambridge University Press.
United Nations Department of Economic and Social Affairs. 2019. “World Population Prospects - Population Division - United Nations.”
10

## Slide 11: 4.2 Infrastructure demand across sectors
Learning objectives
Recognise the current state of infrastructure demand across different sectors
Explain the main trends and challenges in future infrastructure demand across different sectors
11

## Slide 12: 4.2 Infrastructure demand across sectors
Energy demand
Energy is an input in almost all goods and services we need, starting with the production of food, through heating, cooking, lighting, communications and transportation (Baruah et al. 2016)
Our current energy system is also one of the main factors of climate change; therefore, the future challenges of meeting the energy demand sustainably are huge and considered in the Sustainable Development Goal (SDG) 7 “Affordable and Clean Energy.”
The growing level of industrialisation, technological advancement and population growth will increase demand and challenge the global energy systems. This increase will be more notorious in developing economies throughout the first stages of industrialisation
Some energy forecasts predicted that energy consumption in non-OECD (Organisation for Economic Co-operation and Development) countries will increase by 41% between 2015 and 2040, in contrast to a 9% increase in OECD countries (U.S. Energy Information Administration 2017)
Looking to the near future, the electrification of transport is expected to restructure the global energy demand, reducing fossil fuel consumption and pushing electricity demand even further
On the other hand, environmental consciousness can potentially reduce our energy consumption through the selection of more efficient appliances or renewable energy sources
12
Forecasted Non-OECD energy consumption (U.S. Energy Information Administration 2017)

## Slide 13: 4.2 Infrastructure demand across sectors
Transportation demand
Transportation systems: roads, railways, airports, ports, and all related infrastructure
Carbon emissions of the system depend on vehicles’ fuel type and consumption
Some transportation networks are usually congested at peak hours and transportation managers try to improve the efficiency of the system by using better scheduling of public transport or policies
Expansion of the transportation infrastructure is required to serve the increasing demand
The phenomenon of induced demand is the auto-generated demand produced by the capacity expansion (Cervero and Hansen 2002)
Transportation demand is expected to increase due to population growth and the need for more interconnected urban centres
Some trends can challenge and modify this demand, such as the potential use of automated vehicles or an increase in working from home
The demand for different transportation modes might change towards more sustainable mobility or public transport if the adequate incentives are given in the planning process
13
Demand for passenger transport by type (ITF 2019)

## Slide 14: 4.2 Infrastructure demand across sectors
Water demand
Water use has been increasing worldwide at a rate of 1% annually since the 1980s, driven by population growth, socio-economic development and consumption (UNESCO World Water Assessment Programme 2019)
This global demand is expected to grow by 20% to 30% until 2050 in comparison with current water use (Burek et al. 2016)
Approximately four billion people experience severe water scarcity at least one month of the year (Mekonnen and Hoekstra 2012), two billion do not have access to safely-managed drinking water and 785 million lack basic services (WHO/UNICEF 2019)
Future options to meet water demand in the developing world include making the system more efficient, for example, by reducing water losses, increasing the reuse, and recycling wastewater
Developing countries have estimated water losses of about 40% to 50% while developed countries are increasingly using tertiary treatment of wastewater, reducing pollution and producing a new form of water supply The supply side of water will also be challenged by climate change: while an increment in precipitation will increase the risk of flooding and erosion, a decrease will reduce our ability to supply water
14
Change in net precipitation, 2010–2050 (UNESCO World Water Assessment Programme 2019)

## Slide 15: 4.2 Infrastructure demand across sectors
Solid waste demand
A poor waste management can contaminate our environment and oceans and can cause respiratory problems and spread diseases
Solid waste management is typically provided at the municipality level, and consists of collection, transfer stations, processing facilities, landfills and incinerators
Current waste management policies prioritise a more circular economy approach by reusing, recycling and recovering waste based on the widespread waste hierarchy which was (included in SDG 12)
Prevention is considered the most preferred option while disposal is the least preferred
15
Our waste management systems still depend on landfills
This is more profound in low-income countries in which 93% of waste is dumped
Current technologies are recovering resources and energy (methane) from landfills, helping to reduce the need for raw materials
Waste generation is correlated with economic development and waste generation in low and middle-income countries is expected to increase by 40% by 2050
Future waste management will require careful handling of rising electronic and chemical waste through proper treatment and disposal facilities
Waste Hierarchy (Bugge, Fevolden, and Klitkou 2019)
Waste Generation per capita per day (kg) (Kaza et al. 2018)

## Slide 16: 4.2 Infrastructure demand across sectors
Summary
In this mini-lecture we have explored the differences between four of the main important infrastructure sectors in terms of their future demand
We also reviewed current states of demand and highlighted how current challenges can persist or increase into the future
It is important to note that these four infrastructure sectors will not necessarily be the most important in every location, for instance, digital communications are now a critical sector for international development
Other contexts might consider irrigation (e.g. agriculture-based economies) or ports (e.g. islands) as vital infrastructure systems that need special attention
Furthermore, some countries are including health and educational services in their infrastructure plans, which imply further differing challenges and approaches
It’s important to note that different sectors have different demand trends so different strategies might apply. On the other hand, most of the sectors have interdependencies between them, so collaborative plans and system-of-systems thinking will provide great value for infrastructure planners
16

## Slide 17: 4.2 Infrastructure demand across sectors
Bibliography
Baruah, Pranab, Modassar Chaudry, Meysam Qadrdan, Nick Eyre, and Nick Jenkins. 2016. “Energy Systems Assessment.” The Future of National Infrastructure: A System-of-Systems Approach. Cambridge University Press.
Blainey, Simon P., and John M. Preston. 2016. “Transport Systems Assessment.” The Future of National Infrastructure: A System-of-Systems Approach. Cambridge University Press.
Bugge, Markus M., Arne Martin Fevolden, and Antje Klitkou. 2019. “Governance for System Optimization and System Change: The Case of Urban Waste.” Research Policy 48 (May): 1076–90.
Burek, Peter, Yusuke Satoh, Günther Fischer, Mohammed Taher Kahil, Angelika Scherzer, Sylvia Tramberend, Luzma Fabiola Nava, et al. 2016. “Water Futures and Solution Fast Track Initiative-Final Report.”
Cervero, Robert, and Mark Hansen. 2002. “Induced Travel Demand and Induced Road Investment: A Simultaneous Equation Analysis.” Source: Journal of Transport Economics and Policy 36: 469–90.
ITF. 2019. “ITF Transport Outlook 2019.” OECD.
Kaza, Silpa, Lisa C. Yao, Perinaz Bhada-Tata, and Frank Van Woerden. 2018. What a Waste 2.0: A Global Snapshot of Solid Waste Management to 2050. What a Waste 2.0: A Global Snapshot of Solid Waste Management to 2050. Washington, DC: World Bank.
Kingdom, Bill, Roland Liemberger, and Philippe Marin. 2006. “The Challenge of Reducing Non-Revenue Water (NRW) in Developing Countries How the Private Sector Can Help: A Look at Performance-Based Service Contracting.” World Bank, Washington, DC.
Mekonnen, Mesfin M., and Arjen Y. Hoekstra. 2012. “A Global Assessment of the Water Footprint of Farm Animal Products.” Ecosystems 15 (April): 401–15.
Pires, Ana, and Graça Martinho. 2019. “Waste Hierarchy Index for Circular Economy in Waste Management.” Waste Management 95 (July): 298–305.
U.S. Energy Information Administration. 2017. “EIA - International Energy Outlook 2017.” Report Number: DOE/EIA-0484(2017).
UNESCO World Water Assessment Programme. 2019. “The United Nations World Water Development Report 2019: Leaving No One Behind.”
Watson, Geoff V. R., Anne M. Stringfellow, William Powrie, David A. Turner, and Jon Coello. 2016. “Solid Waste Systems Assessment.” The Future of National Infrastructure: A System-of-Systems Approach. Cambridge University Press.
WHO/UNICEF. 2019. “WHO | Progress on Household Drinking Water, Sanitation and Hygiene 2000-2017:” World Health Organization.
17

## Slide 18: 4.3 Determining main infrastructure drivers
Learning objectives
List different infrastructure drivers that might be considered for demand forecasting
Describe how different contexts might require a different set of demand drivers
18

## Slide 19: 4.3 Determining main infrastructure drivers
Key considerations
This mini-lecture will continue exploring the main infrastructure drivers and some of their specific features
As we have seen with the example of Shared Socio-economic Pathways (SSPs), the nature of the future narratives we want to explore are crucial in the development of forecasts:
In its simplest form, we can assume that current consumption patterns will remain unchanged in the future and infrastructure demand will be driven only by population growth
The complexity of the estimation increases when we assume long-term trends on economic development, urbanisation and demographics
This entails not only an interdependent analysis of infrastructure and the economy, but potentially an explicit spatial analysis for the urban development driver
The considered time span is also of importance, given that the more distant the future, the higher the uncertainty:
A projection of a couple of decades in the future might hold some assumptions of current technologies and patterns
A forecast toward the end of the century might need assumptions about disruptive technological and socio-economic changes that can fundamentally restructure our relationship with infrastructure services
19

## Slide 20: 4.3 Determining main infrastructure drivers
Population trends
Population forecasts can be typically found in national or regional statistics authorities with different levels of detail and features
The United Nations regularly publishes World Population Prospects (United Nations Department of Economic and Social Affairs 2019), with detailed population estimations
It provides estimations for 235 countries by using two demographic trends: population growth and population ageing
Several Population Scenarios: low, medium and high variants
Different narratives: “constant fertility,” “instant replacement,” “zero migration,” “constant mortality” and “no change”
Probabilistic estimations including prediction intervals that can help with uncertainty quantification and detailed analysis for infrastructure planning
20
Population Forecasting for Ghana under different scenarios (based on data from United Nations Department of Economic and Social Affairs (2019))

## Slide 21: 4.3 Determining main infrastructure drivers
Per capita consumption rates and seasonal effects
21
Per capita consumption rates can be found in the literature, policy documents and utilities´ reports, or can be discussed with policy makers according to their visions and expectations to the future
Some useful per capita consumption rates of energy and water can be found in the World Bank Development indicators (World Bank 2021) for different countries and regions
These consumption rates might change with the socio-economic development of the region (Thoung et al. 2016)
One simple way of forecasting infrastructure demand is by doing annual aggregates and looking at year-over-year changes
However, our needs, and consequently infrastructure demand, is not uniform but seasonal
While our infrastructure should provide services over the whole year, it is particularly important to provide a reliable service when it’s needed the most
Seasonal energy demand in the UK. This seasonal pattern persists in the projections of the future. (Staffell and Pfenninger 2018)

## Slide 22: 4.3 Determining main infrastructure drivers
Spatially distributed demand
The spatial distribution of infrastructure needs might be crucial for several applications
This is clearer with the development of mega urban centres in which infrastructure demand is high
The potential rural-urban migration, or the development of satellite urban settlements, play a role in how we perform our infrastructure planning
Scenario narratives might also influence the spatial distribution of demand
These different spatial changes will also bring different challenges for the coverage that our distribution networks need to reach
Regional-dependent infrastructures such as water and waste will need a more granular analysis of the future local and regional needs
22
Spatial population change in Nordic municipalities by 2040 (Gassen and Heleniak 2019)

## Slide 23: 4.3 Determining main infrastructure drivers
Other chronic effects and climate change
Alongside the importance of adaptation and mitigation, climate change might have an impact on our ability to meet infrastructure demand:
Can modify our consumption patterns in terms of heating, cooling and demand for services (Clarke et al. 2018)
It will certainly increase the seasonal variability of demand and have major impacts on our supply systems. For instance, changes in temperature, wind and rainfall patterns will affect the functioning of renewable energy (solar and wind) and water supplies (Urich and Rauch 2014)
Another chronic effect is the inevitable ageing of infrastructure assets, or the slow deterioration of our systems, which can be mitigated by good maintenance programmes
Also, strong demographic changes (increasing elderly population and variation in gender profiles) can play a role in modified consumption patterns into the future
23

## Slide 24: 4.3 Determining main infrastructure drivers
Summary
In this mini-lecture we explored in more detail some infrastructure demand drivers such as population growth and per capita consumption rates
We also comment on seasonal effects and spatially distributed demand as important features to take into account in different contexts
24

## Slide 25: 4.3 Determining main infrastructure drivers
Bibliography
Clarke, Leon, Jiyong Eom, Elke Hodson Marten, Russell Horowitz, Page Kyle, Robert Link, Bryan K. Mignone, Anupriya Mundra, and Yuyu Zhou. 2018. “Effects of Long-Term Climate Change on Global Building Energy Expenditures.” Energy Economics 72 (May): 667–77.
Gassen, Nora Sánchez, and Timothy Heleniak. 2019. “THE NORDIC POPULATION IN 2040-Analysis of Past and Future Demographic Trends.”
Haasnoot, Marjolijn, Jan H. Kwakkel, Warren E. Walker, and Judith ter Maat. 2013. “Dynamic Adaptive Policy Pathways: A Method for Crafting Robust Decisions for a Deeply Uncertain World.” Global Environmental Change 23 (April): 485–98.
Lempert, Robert J., and David G. Groves. 2010. “Identifying and Evaluating Robust Adaptive Policy Responses to Climate Change for Water Management Agencies in the American West.” Technological Forecasting and Social Change 77 (July): 960–74.
Staffell, Iain, and Stefan Pfenninger. 2018. “The Increasing Impact of Weather on Electricity Supply and Demand.” Energy 145 (February): 65–78.
Thoung, Chris, Rachel Beaven, Chengchao Zuo, Mark Birkin, Peter Tyler, Douglas Crawford-Brown, Edward J. Oughton, and Scott Kelly. 2016. “Future Demand for Infrastructure Services.” The Future of National Infrastructure: A System-of-Systems Approach. Cambridge University Press.
United Nations Department of Economic and Social Affairs. 2019. “World Population Prospects - Population Division - United Nations.”
Urich, Christian, and Wolfgang Rauch. 2014. “Exploring Critical Pathways for Urban Water Management to Identify Robust Strategies Under Deep Uncertainties.” Water Research 66 (December): 374–89.
World Bank. 2021. “World Development Indicators | DataBank.”
25

## Slide 26: 4.4 Infrastructure demand forecasts in practice
Learning objectives
Describe forecast estimation for different contexts
Identify differences in future demand across infrastructure sectors in practice
26

## Slide 27: 4.4 Infrastructure demand forecasts in practice
Overview of demand projections in practice
This mini-lecture will showcase different applications of the National Infrastructure Systems MODel – International (NISMOD-Int) for demand forecasting
Infrastructure demand forecasting was used in a range of international contexts including Curaçao, Saint Lucia, Palestine, Ghana and others
The specific details and differences between countries will arise by describing the rationale and the process followed in each of these cases - different contexts require different infrastructure drivers
The cases studied here cover the aforementioned four countries and three infrastructure sectors: waste, electricity and water
Additionally, infrastructure needs are also discussed in terms of future performance of current systems and why they need to be restructured
27

## Slide 28: 4.4 Infrastructure demand forecasts in practice
28
Waste generation projections for Curaçao
Population, tourism and economic growth were used as future demand drivers
Low, moderate and high waste generation scenarios were constructed
The projections show a broad range of waste generation by 2050
Waste management in Curaçao currently depends heavily on landfills
At the current rate of waste generation landfills will be full by 2030
Waste management will need new options, such as waste treatment and recycling plants, waste reduction programmes and, as the last option, new landfills for final disposal
Waste Generation Projections for Curaçao (Fuldauer et al. 2019)
Waste demand and current supply (Adshead et al. 2018)
Notes: There are now several open-source hazard products at global scales which are being used widely for vulnerability and risk analysis. A few resources include:
Global river and coastal flood maps: Historical and future hazard maps at different return periods (2, 5, 1, 25, 50, 10, 250, 500, 100 years). All data is available at a 30 arc-seconds resolution (~1km at equator) (Gassert et al. 2015).
Global hazard maps for earthquakes for different return periods (250, 475, 975, 1500, 2475 years) both Peak Ground Acceleration and spectral acceleration. Data is available at 0.072 degrees (~8km at equator).
Global dataset of 1,000 synthetic tropical cyclones paths with cyclone characteristics (e.g., wind speed, pressure) on a global scale. Wind speed probabilities are derived globally (1 metre, 1 minutes sustained speed) for different return periods (1 to 1,000 years) at 1km resolution (Bloemendaal et al. 2019).

## Slide 29: 4.4 Infrastructure demand forecasts in practice
Electricity demand in Saint Lucia
Energy demand was estimated based on population and tourism growth
Per capita consumption rates in the island were estimated with current consumption
Residents consume on average 1.4 MWh/resident/year and 0.2KW/resident at peak time
Tourists consume 12.2 MWh/tourist/year and 1.9KW/tourist over the peak period: seasonal tourism is an important driver when it comes to future infrastructure planning
Per capita consumption rates in Saint Lucia might increase alongside economic development
Diesel can meet future demand, but emission goals, high costs, and import dependence require system restructuring and new energy alternatives
29
Residential and peak tourism scenarios (Adshead et al. 2020)
Future energy needs for a moderate scenario (Adshead et al. 2020)

## Slide 30: 4.4 Infrastructure demand forecasts in practice
Population forecasts for Palestine were developed by combining population growth expected for both Gaza and the West Bank
The sum of these two projections resulted in a range of between 10.7 and 16.3 million people by 2050, for the High and Low scenarios, respectively, equivalent to average annual growth rates of 2.3% and 3.6%, respectively, which are in line with the average growth rate of 2.6% for Palestine between 2007 and 2016 (Ives et al. 2018)
Economic forecasts were also developed for Palestine for the baseline economic scenario, the optimistic scenario and the pessimistic scenario by using annual GDP growth rates of 3.5%, 5.5% and 1.5%, respectively (Ives et al. 2018)
Three socio-economic scenarios were created: (1) “balanced prosperity” by combining the low population growth with the optimistic economic scenario, (2) “central” by combining the central population growth and the baseline economic scenario, and (3) “unstable adversity” by combining the high population growth and the pessimistic economic scenario
Combining socio-economic projections and expectations in Palestine
30
Population projections for Palestine (Ives et al. 2018)
Economic projections for Palestine (Ives et al. 2018)
Water demand projections for Palestine (Ives et al. 2018)

## Slide 31: 4.4 Infrastructure demand forecasts in practice
Population growth and socio-economic development for Ghana
31
Population Growth Scenarios: UN forecasts were used to create three scenarios - medium, upper, and lower estimates
Current Consumption: Ghana's per capita electricity consumption is 351 KWh, lower than similar middle-income countries
Comparison with Other Countries: Middle-income nations consume 2044 KWh per capita, while high-income countries average 8929 KWh
Development Impact: Ghana, despite its middle-income status, has lower per capita consumption than its peers
Future Projections: By 2050, Ghana aims for middle-income consumption in a pessimistic scenario and high-income levels in an optimistic scenario
Electricity demand projections for Ghana (based on data from United Nations Department of Economic and Social Affairs (2019) and World Bank (2021))

## Slide 32: 4.4 Infrastructure demand forecasts in practice
Summary
In this mini-lecture we described the forecasting process for infrastructure demand in four different countries in which the NISMOD-International tool has been applied
With this approach, we have illustrated the details, considerations and challenges of infrastructure demand forecasting in developing regions
32

## Slide 33: 4.4 Infrastructure demand forecasts in practice
Bibliography
Adshead, D., L. I. Fuldauer, S. Thacker, O. Román, S. Vital, F. Felix, C. Roberts, et al. 2020. “Saint Lucia: National Infrastructure Assessment.” United Nations Office for Project Services.
Adshead, D., L. Fuldauer, S. Thacker, A. Hickford, G. Rouhet, W. S. Muller, J. W. Hall, and R. Nicholls. 2018. “Evidence-Based Infrastructure: Curacao. National Infrastructure Systems Modelling to Support Sustainable and Resilient Infrastructure Development.” United Nations Office for Project Services.
Fuldauer, Lena I., Matthew C. Ives, Daniel Adshead, Scott Thacker, and Jim W. Hall. 2019. “Participatory Planning of the Future of Waste Management in Small Island Developing States to Deliver on the Sustainable Development Goals.” Journal of Cleaner Production 223 (June): 147–62.
Ives, Matthew C, Scott Thacker, Daniel Adshead, Jim W Hall, Adrian J Hickford, Robert J Nicholls, Trevor Sway Muwafaq, Abu Ayyash, Rob Jones, and Nicholas O’regan. 2018. “A Fast Track Analysis of Infrastructure Provision in Palestine.”
United Nations Department of Economic and Social Affairs. 2019. “World Population Prospects - Population Division - United Nations.”
World Bank. 2014. “Electric Power Consumption (kWh Per Capita) | Data.” IEA Statistics © OECD/IEA.
———. 2021. “World Development Indicators | DataBank.”
33

## Slide 34: Thank you
www.climatecompatiblegrowth.com