## Slide 1: Lecture 7: Decision analysis for long-term infrastructure planning
Orlando Roman, Oxford University

## Slide 2: Learning Outcomes
By the end of this lecture, you will:
Have an introduction of the several concepts of decision-making under different contexts applicable to infrastructure
These include multiple stakeholders, infrastructure interdependencies and deep uncertainties in future forecasts
Have seen real applications of the NISMOD-Int tool to developing countries
2

## Slide 3: 7.1 Key considerations for infrastructure decision-making
Learning Objectives
List key considerations for infrastructure decision-making
Explain why each of them are important
3

## Slide 4: 7.1 Key considerations for infrastructure decision-making
Overview of performance evaluation
Following previous lectures, we are already able to:
Establish the current state of infrastructure systems
Develop forecasts of future infrastructure demands
Establish a vision, performance metrics and goals for the future
Develop strategic alternatives for future infrastructure provision
In this lecture we will set the basis for decision-making on evaluating what strategies perform better under future forecasts to achieve our defined goals
Infrastructure, as a high-cost long-lived asset, needs to take into account a variety of factors, scenarios, objectives, stakeholders and interdependencies with other sectors
4
(Anheier, Lorentz, and Fratzscher 2016; OECD 2017)

## Slide 5: 7.1 Key considerations for infrastructure decision-making
Multiple objectives
5
Making decisions about infrastructure today, needs to take into account a variety of different aspects and goals
Multiple goals in the decision-making process
Common multiple objectives:
Costs
Emissions (mainly for energy and transport)
Reliability of the service
Access (mainly for water and wastewater in low-income settings)
Air and water quality
Other environmental impacts
Often converted into monetary values to be comparable
An alternative can be multi-criteria decision-making, in which every metric can be analysed with its own value, and trade-off evaluations can be performed
Natural infrastructure for multiple objectives (Cohen-Shacham et al. 2016)
(Bhardwaj et al. 2019; Saha 2018)

## Slide 6: 7.1 Key considerations for infrastructure decision-making
Interdependencies between infrastructure sectors
Types of interactions: Intra-network (within the same sector), inter-network and human-centric communication
Direct interdependencies:
Energy and water sectors
hydropower plants (which generate water and energy at the same time)
energy needed for water treatment and desalination
Energy and transportation sectors
fossil fuels used for vehicles
electrification of transport
Waste and energy
waste-to-energy projects such as incinerators or anaerobic digesters as well as the methane collection in landfills
Indirect dependencies:
if infrastructure is planned centrally, one common budget might be distributed for different sectors, therefore the budget spent in one sector might affect another
demand-management strategy such as increasing environmental awareness can have an impact on all sectors and can be considered a cross-sectoral intervention
6
Interdependent infrastructure systems (Amini, Imteaj, and Pardalos 2020)
(Hamiche, Stambouli, and Flazi 2016; Artioli, Acuto, and McArthur 2017)

## Slide 7: 7.1 Key considerations for infrastructure decision-making
Uncertainty on infrastructure forecasts
7
The longer the planning timeframe, the more uncertain the forecasts
When facing that range of uncertainty, different approaches are commonly used:
Simple statistic estimations (average or the median of the forecasts) - not considered a good uncertainty management
Evaluate the probability distribution of the forecasts + evaluate the likelihood of different scenarios + estimate an expected value – good if the only goal is to maximise the overall expected value of the decision
Worst-case scenario (conservative approach) - the solution might be expensive but will always work
More specialised approaches intending to evaluate the performance of different strategies under the whole range of scenarios, can result in robust decisions in the present, and propose adaptive approaches through time
Different forecasts of sea level rise for the Thames river in London (Hall, Harvey, and Manning 2019)

## Slide 8: 7.1 Key considerations for infrastructure decision-making
Multiple stakeholders
Infrastructure is costly and its impacts are widespread decisions are usually taken by a group of stakeholders
Infrastructure governance entails the social and institutional factors that create and sustain infrastructure relationships
Uncertainty:
there are many viable alternatives to follow
the problem depends upon people’s unpredictable behaviour
the uncertainty of the decision-making process itself, where various stakeholders with different worldviews do not agree on a strategy
The variety and sometimes conflicting opinions need to be accounted for from the framing of the problem, the development of a vision and objectives, and the metrics that should be used.
This will lead to consensus-based decision-making, often entailing a complex and iterative process
8
A framework for the participatory decision-making process (Pira et al. 2015)
(Groves and Lempert 2007; Turner 2018)

## Slide 9: 7.1 Key considerations for infrastructure decision-making
Summary
In this mini-lecture we reviewed key considerations for infrastructure decision-making
Infrastructure normally has multiple objectives, interdependencies, future uncertainty and multiple stakeholders involved
Making infrastructure decisions is therefore a complex process
9

## Slide 10: 7.1 Key considerations for infrastructure decision-making
Bibliography
Amini, M. Hadi, Ahmed Imteaj, and Panos M. Pardalos. 2020. “Interdependent Networks: A Data Science Perspective.” Patterns 1 (April): 100003. https://doi.org/10.1016/j.patter.2020.100003.
Anheier, H. K., B. Lorentz, and M. Fratzscher. 2016. “Governance of Infrastructure: International Best Practices and Innovations Executive Summary.” Hertie School of Governance. https://www.hertie-school.org/fileadmin/2_Research/2_Research_directory/Research_projects/Governance_of_infrastructure/HSoG_Policy_Paper_Best_Practice_Summary_2016_24_online.pdf.
Artioli, Francesca, Michele Acuto, and Jenny McArthur. 2017. “The Water-Energy-Food Nexus: An Integration Agenda and Implications for Urban Governance.” Political Geography 61 (November): 215–23. https://doi.org/10.1016/j.polgeo.2017.08.009.
Bhardwaj, Ankit, Madhura Joshi, Radhika Khosla, and Navroz K. Dubash. 2019. “More Priorities, More Problems? Decision-Making with Multiple Energy, Development and Climate Objectives.” Energy Research and Social Science. Elsevier Ltd. https://doi.org/10.1016/j.erss.2018.11.003.
Cohen-Shacham, E., C. Janzen, S. Maginnis, and G. Walters. 2016. Nature-Based Solutions to Address Global Societal Challenges. Nature-Based Solutions to Address Global Societal Challenges. IUCN International Union for Conservation of Nature. https://doi.org/10.2305/iucn.ch.2016.13.en.
Groves, David G., and Robert J. Lempert. 2007. “A New Analytic Method for Finding Policy-Relevant Scenarios.” Global Environmental Change 17 (February): 73–85. https://doi.org/10.1016/j.gloenvcha.2006.11.006.
Hall, Jim W., Hamish Harvey, and Lucy J. Manning. 2019. “Adaptation Thresholds and Pathways for Tidal Flood Risk Management in London.” Climate Risk Management 24 (January): 42–58. https://doi.org/10.1016/j.crm.2019.04.001.
Hamiche, Ait Mimoune, Amine Boudghene Stambouli, and Samir Flazi. 2016. “A Review of the Water-Energy Nexus.” Renewable and Sustainable Energy Reviews. Elsevier Ltd. https://doi.org/10.1016/j.rser.2016.07.020.
OECD. 2017. Getting Infrastructure Right: A Framework for Better Governance. Getting Infrastructure Right. OECD. https://doi.org/10.1787/9789264272453-en.
Pira, Michela Le, Giuseppe Inturri, Matteo Ignaccolo, and Alessandro Pluchino. 2015. “Analysis of AHP Methods and the Pairwise Majority Rule (PMR) for Collective Preference Rankings of Sustainable Mobility Solutions.” In Transportation Research Procedia, 10:777–87. Elsevier. https://doi.org/10.1016/j.trpro.2015.09.031.
Saha, D. 2018. “Low-Carbon Infrastructure: An Essential Solution to Climate Change?” World Bank Blogs. https://blogs.worldbank.org/ppps/low-carbon-infrastructure-essential-solution-climate-change.
Turner, Colin. 2018. “The Governance of Polycentric National Infrastructure Systems: Evidence from the UK National Infrastructure Plan.” Environment and Planning C: Politics and Space 36 (May): 513–29. https://doi.org/10.1177/2399654417717068.
10

## Slide 11: 7.2 Principles of decision analysis under uncertainty
Learning objectives
Describe the types of uncertainty and when deep uncertainty arises
Describe some approaches of MCDA
Explain the difference between robust and adaptive plans
11

## Slide 12: 7.2 Principles of decision analysis under uncertainty
Overview on decision analysis
One of the bases of decision theory is the concept of expected utility as formulated by (Savage 1954):
One can formulate a personal utility function, which is a function about how one values different aspects, and is by nature, subjective
One can also formulate a probability distribution of the potential outcomes of a certain decision to then optimise the expected value of the utility function under the probability distribution of outcomes and obtain the best decision
Sometimes this approach is not applicable to infrastructure decision-making:
Given the variety of stakeholders and objectives, it’s not easy to compute a single expected utility function infrastructure decisions don’t only focus on optimising benefits, but also on reducing losses from worst-case scenarios
An infrastructure that performs well on average but loses functionality for an entire year is normally not considered acceptable
“Flaw of Averages”: the analysis is carried out for a “most likely” scenario or using a “best prediction” instead of using a deeper uncertainty evaluation
The concepts elaborated in this mini-lecture will therefore tackle the challenges of making decisions under uncertainty using a participatory and adaptive approach
12

## Slide 13: 7.2 Principles of decision analysis under uncertainty
Types of risk and uncertainty
13
Different types of uncertainty (Buurman and Babovic 2016)

## Slide 14: 7.2 Principles of decision analysis under uncertainty
Multi-criteria decision analysis
A decision-making process evaluates a set of alternatives by using different criteria, including attributes and objectives
Attributes = measurable properties of the model (cost, capacity and emissions of specific infrastructure options or strategies) as well as related or dependent characteristics (location or lifetime)
Objectives = statements about the desired state of the system, visions or goals
“a priori” approach uses a set of relative weights to build an objective function for optimisation (Drobne and Lisec 2009)
A decision-maker can say that reducing emissions has a 50% importance (weight), while cost and reliability have 30% and 20% importance, respectively
“a posteriori” approach does not need to provide relative weights beforehand, it tries to explore the whole set of alternatives and evaluate the trade-offs between different and conflicting objectives (Malczewski 1999)
an energy plan can have low cost and high emissions by continuing to use fossil fuels, or high cost and low emissions by changing to renewables
the decision-maker does not need to decide how much they prefer to reduce emissions or costs by, instead they can look at the whole set of options, evaluate the trade-offs and potentially make a compromised decision
The set of optimal solutions is commonly referred to as a Pareto Frontier (Cohon 1978)
Several methods used in the industry that use MCDA approaches, such as the Analytic Hierarchy Process (AHP) ELECTRE or PROMETHEE
14

## Slide 15: 7.2 Principles of decision analysis under uncertainty
Robustness in decision making
Robustness is the concept of making decisions in the present that will also achieve objectives in the future
Decision-makers try to explore a broad range of future scenarios and select the strategy that performs best in most of them
The two most commonly used performance indicators are:
robustness, or selecting the strategy that performs best in most futures
regrets, minimising the potential losses under all potential futures.
15
Projected mean changes in annual temperature (°C) and precipitation (%) for a hydropower project from different climate models. The range of values evident is between +20% to -30%, resulting in a huge challenge for the project design. Given the non-flexible nature of a hydropower dam, in this case, a robust decision that minimises possible regrets is critical. (Taner, Ray, and Brown 2017)

## Slide 16: 7.2 Principles of decision analysis under uncertainty
Flexibility and adaptation in decision making
Flexibility takes a sequential decision-making approach
Flexibility does not try to make only the best decisions in the present, but intends to also provide options so the system can adapt through time
Adaptive management and the value of flexibility, as the capability to adapt over time, is a well-known concept developed in recent techniques for making decisions under uncertainty
Flexibility is an important advantage for two main reasons:
Adaptive strategies do not usually require a large capital investment and are more attractive because they postpone investments
Postponing decisions into the future has the advantage that in the future there may be much more information and less uncertainty than in the present
16
Drawdown threshold for the decision to expand or not in a reservoir dam (Fletcher et al. 2019)

## Slide 17: 7.2 Principles of decision analysis under uncertainty
Summary
In this mini-lecture we introduced the Flaw of Averages to illustrate the mistake of making decisions based on average performance
Then we explored the types of uncertainty that exist in different problems and some concepts of multi-criteria decision analysis (MCDA)
Finally, we described the concepts of robustness and flexibility and their importance for infrastructure planning
17

## Slide 18: 7.2 Principles of decision analysis under uncertainty
Bibliography
Buurman, Joost, and Vladan Babovic. 2016. “Adaptation Pathways and Real Options Analysis: An Approach to Deep Uncertainty in Climate Change Adaptation Policies.” Policy and Society 35 (January): 137–50. https://doi.org/10.1016/j.polsoc.2016.05.002.
Cohon, J. L. 1978. Multiobjective Programming and Planning. Academic Press. https://www.elsevier.com/books/multiobjective-programming-and-planning/cohon/978-0-12-178350-1.
Drobne, Samo, and Anka Lisec. 2009. “Multi-Attribute Decision Analysis in GIS: Weighted Linear Combination and Ordered Weighted Averaging.” Informatica 33: 459. http://www.informatica.si/index.php/informatica/article/view/263.
Fletcher, Sarah, Kenneth Strzepek, Adnan Alsaati, and Olivier De Weck. 2019. “Learning and Flexibility for Water Supply Infrastructure Planning Under Groundwater Resource Uncertainty.” Environmental Research Letters 14 (November): 114022. https://doi.org/10.1088/1748-9326/ab4664.
Gärdenfors, Peter, and Nils Eric Sahlin. 1982. “Unreliable Probabilities, Risk Taking, and Decision Making.” Synthese 53 (December): 361–86. https://doi.org/10.1007/BF00486156.
Holling, C. S. 1978. Adaptive Environmental Assessment and Management. John Wiley & Sons. http://pure.iiasa.ac.at/id/eprint/823/.
Malczewski, Jacek. 1999. GIS and Multicriteria Decision Analysis. Wiley. https://www.wiley.com/en-us/GIS+and+Multicriteria+Decision+Analysis-p-9780471329442.
Malczewski, Jacek, and Claus Rinner. 2015. Multicriteria Decision Analysis in Geographic Information Science. Springer Berlin Heidelberg. https://doi.org/10.1007/978-3-540-74757-4.
Savage, L. J. 1954. The Foundations of Statistics. John Wiley & Sons. https://psycnet.apa.org/record/1955-00117-000.
Taner, Mehmet Ümit, Patrick Ray, and Casey Brown. 2017. “Robustness-Based Evaluation of Hydropower Infrastructure Design Under Climate Change.” Climate Risk Management 18 (January): 34–50. https://doi.org/10.1016/j.crm.2017.08.002.
18

## Slide 19: 7.3 Methods for decision making under uncertainty
Learning objectives
List and describe some DMDU methods
Explain when a particular method is preferred
19

## Slide 20: 7.3 Methods for decision making under uncertainty
Introduction
Evaluating a deeply uncertain future through a traditional scenario technique has important challenges:
In complex systems, it is difficult to clearly visualise the relationship between inputs and outputs. These are often non-linear, with regions of extreme sensitivity to particular assumptions, and threshold points that are difficult to identify
The number of possible scenarios that can be analysed are limited, even for visualisation purposes. Normally, the entire spectrum of the problem cannot be evaluated
It is difficult to establish monitoring criteria, decision rules or triggering points for decision-making, as these rely on how the future unfolds
The decision-making community is using innovative decision support methods: they combine creative thinking of scenario techniques, the capabilities of stress testing and the deliberative process of decision-making in a systematised fashion, thus reducing possible biases
20

## Slide 21: 7.3 Methods for decision making under uncertainty
Exploratory analysis
21
Exploratory Analysis is a wide exploration of many alternative scenarios (Bankes 1993) opening up a range of plausible future states
Normative approach is based on the best forecast
Predictive approach intends to account for variability in the future state
Exploratory approach takes a wider look into the future alternatives asking “what if” questions and evaluating all plausible alternatives
exploration of potential futures might guide the decision-making process by finding vulnerabilities and best strategies
when the future proves hard to predict, plans ought to be robust and flexible (Lempert 2019)
Two approaches of exploration:
Evaluate future states to find robust decisions that remain effective regardless of outcomes
Identify key decision points to adapt over time, promoting flexibility for managing uncertainty
The Exploratory Modelling Analysis (EMA) Workbench (Kwakkel 2017) connects models from different languages and software to analyze uncertainty, identify sensitivity regions, and optimize strategies
Types of future scenario approaches (McGowan, Jay, and Kidd 2019)

## Slide 22: 7.3 Methods for decision making under uncertainty
Robust decision-making (RDM)
22
Robust decision-making (RDM) is an analytical approach that evaluates strategies against various potential futures to identify vulnerabilities and refine plans
Decision framing is where stakeholders identify the alternatives, uncertainties and performance indicators they wish to evaluate (wider range)
Evaluate strategy across futures is a systematic development of the entire spectrum of possible scenarios, generating a range of futures, against which the performance of the originally proposed alternatives will be evaluated.
Vulnerability analysis is where data mining and machine learning algorithms are used to identify the vulnerabilities of each alternative, which allow modification or unifying alternatives, thus creating new ones. This feedback loop is the most creative process and where the method generates the most value
Trade-off analysis is where the different alternatives generated are compared based on their performance, such as their robustness (best in most futures), regrets (the difference between the chosen and the optimal solution) or others identified. This step allows a transparent decision-making process for the different stakeholders.
Based on the results, the process allows to develop new futures and strategies to be evaluated in a new round of analysis.
The RDM method allows iteration and learning in each round of analysis until a satisfactory robust strategy is found
Iterative steps in RDM (Lempert 2019)

## Slide 23: 7.3 Methods for decision making under uncertainty
Real/engineering options analysis
Real Options Analysis emphasizes flexibility and adaptability over time, similar to the Dynamic Adaptive Planning approach
The Real or Engineering Options methodology allows for a deeper exploration of technical alternatives compared to other Decision-Making Under Uncertainty (DMDU) methods
This methodology is particularly effective for evaluating engineering projects amidst uncertainty
Real Options evaluates the cost of adding flexibility and estimates whether the benefits outweigh these costs given future uncertainties
23
Distribution of desalination capacity added over 1,000 simulations (Fletcher et al. 2019)

## Slide 24: 7.3 Methods for decision making under uncertainty
Dynamic Adaptive Planning
The RDM (Robust Decision Making) and Real Options methods can be complemented with a dynamic adaptive approach, helping to understand systems and their vulnerabilities while allowing for transparent option comparisons
Adaptive planning focuses on the need for dynamic adaptation over time, highlighting the importance of responding to changes in circumstances
Tipping points represent moments when current strategies become ineffective, necessitating new actions; for example, Actions A and D are long-term effective but may lead to changes in strategy later due to various pressures
Identifying tipping points or adaptation triggers is challenging but essential for generating flexible pathways that facilitate timely adaptations to better strategies
24
Adaptation pathways map (Haasnoot et al. 2013)

## Slide 25: 7.3 Methods for decision making under uncertainty
Summary
In this mini-lecture we explained the need of more sophisticated methods when facing complex systems and a huge range of possible scenarios
Then we described four of the most used methods in practice: exploratory analysis, robust decision making (RDM), real/engineering options and dynamic adaptive pathways
25

## Slide 26: 7.3 Methods for decision making under uncertainty
Bibliography
Bankes, Steve. 1993. “Exploratory Modeling for Policy Analysis.” Operations Research 41 (June): 435–49. https://doi.org/10.1287/opre.41.3.435.
de Neufville, Richard, and S. Scholtes. 2011. Flexibility in Engineering Design. 2011. MIT Press. https://mitpress.mit.edu/books/flexibility-engineering-design.
de Neufville, Richard, and Kim Smet. 2019. “Engineering Options Analysis (EOA).” Decision Making Under Deep Uncertainty. Springer International Publishing. https://doi.org/10.1007/978-3-030-05252-2_6.
Fletcher, Sarah, Kenneth Strzepek, Adnan Alsaati, and Olivier De Weck. 2019. “Learning and Flexibility for Water Supply Infrastructure Planning Under Groundwater Resource Uncertainty.” Environmental Research Letters 14 (November): 114022. https://doi.org/10.1088/1748-9326/ab4664.
Groves, David G., and Robert J. Lempert. 2007. “A New Analytic Method for Finding Policy-Relevant Scenarios.” Global Environmental Change 17 (February): 73–85. https://doi.org/10.1016/j.gloenvcha.2006.11.006.
Haasnoot, Marjolijn, Jan H. Kwakkel, Warren E. Walker, and Judith ter Maat. 2013. “Dynamic Adaptive Policy Pathways: A Method for Crafting Robust Decisions for a Deeply Uncertain World.” Global Environmental Change 23 (April): 485–98. https://doi.org/10.1016/j.gloenvcha.2012.12.006.
Hall, Jim W., Hamish Harvey, and Lucy J. Manning. 2019. “Adaptation Thresholds and Pathways for Tidal Flood Risk Management in London.” Climate Risk Management 24 (January): 42–58. https://doi.org/10.1016/j.crm.2019.04.001.
Kwakkel, Jan H. 2017. “The Exploratory Modeling Workbench: An Open Source Toolkit for Exploratory Modeling, Scenario Discovery, and (Multi-Objective) Robust Decision Making.” Environmental Modelling and Software 96 (October): 239–50. https://doi.org/10.1016/j.envsoft.2017.06.054.
Kwakkel, Jan H., Marjolijn Haasnoot, and Warren E. Walker. 2016. “Comparing Robust Decision-Making and Dynamic Adaptive Policy Pathways for Model-Based Decision Support Under Deep Uncertainty.” Environmental Modelling and Software 86 (December): 168–83. https://doi.org/10.1016/j.envsoft.2016.09.017.
Lempert, R. J. 2019. “Robust Decision Making (RDM).” Decision Making Under Deep Uncertainty. Springer International Publishing. https://doi.org/10.1007/978-3-030-05252-2_2.
McGowan, Lynne, Stephen Jay, and Sue Kidd. 2019. “Scenario-Building for Marine Spatial Planning.” Maritime Spatial Planning: Past, Present, Future. Springer International Publishing. https://doi.org/10.1007/978-3-319-98696-8_14.
26

## Slide 27: 7.4 Strategic evaluation of infrastructure in practice
Learning objectives
List different indicators used to evaluate strategies in practice
Identify infrastructure interdependencies between sectors
27

## Slide 28: 7.4 Strategic evaluation of infrastructure in practice
Overview of infrastructure strategy evaluation in practice
This mini-lecture will showcase different applications of the National Infrastructure Systems MODel – International (NISMOD-Int) for strategy evaluation in infrastructure planning
Strategy evaluation and decision-making were used in a range of international contexts including Curaçao, Saint Lucia and Palestine and will be described in detail here
Furthermore, the evaluations include waste and water sectors and a cross-sectoral analysis that provides an overview of infrastructure interdependencies in the long-term
The different potential strategies and the different indicators used in each country will provide insight on the participatory nature of this process and how different contexts, needs and priorities shape the infrastructure planning process
28

## Slide 29: 7.4 Strategic evaluation of infrastructure in practice
29
Waste management strategy evaluation in Curaçao (part I)
Waste treatment by strategy (Fuldauer et al. 2019)
Performance of waste strategies on SDG indicators (Fuldauer et al. 2019)
Landfill capacity will be depleted by 2026 and without other interventions, the waste generated thereafter might remain unmanaged
Half of the “baseline” strategy still depends on landfills
“circular economy” strategy proposes 60% of recycling
“technology-led” strategy includes a new option of producing energy from waste and anaerobic digestion
The technology-led strategy is the only one able to treat 100% of the waste until 2050. However, the circular economy approach shows a better performance on employment and recycling
Notes: There are now several open-source hazard products at global scales which are being used widely for vulnerability and risk analysis. A few resources include:
Global river and coastal flood maps: Historical and future hazard maps at different return periods (2, 5, 1, 25, 50, 10, 250, 500, 100 years). All data is available at a 30 arc-seconds resolution (~1km at equator) (Gassert et al. 2015).
Global hazard maps for earthquakes for different return periods (250, 475, 975, 1500, 2475 years) both Peak Ground Acceleration and spectral acceleration. Data is available at 0.072 degrees (~8km at equator).
Global dataset of 1,000 synthetic tropical cyclones paths with cyclone characteristics (e.g., wind speed, pressure) on a global scale. Wind speed probabilities are derived globally (1 metre, 1 minutes sustained speed) for different return periods (1 to 1,000 years) at 1km resolution (Bloemendaal et al. 2019).

## Slide 30: 7.4 Strategic evaluation of infrastructure in practice
Waste management strategy evaluation in Curaçao (part II)
30
Performance of waste strategies against cost and cumulative carbon (Fuldauer et al. 2019)
Waste management pathway (Adshead et al. 2018)

## Slide 31: 7.4 Strategic evaluation of infrastructure in practice
Strategic performance for water provision in Palestine
31
Strategic Performance for Water Supply in Gaza (Ives et al. 2018)
Five infrastructure strategies for Palestine were developed based on varying levels of investment: "No build" (benchmark), "Status Quo," "Infrastructure-led development," "Pipeline," and "Efficiency with Scarcity“
The analysis indicates that only the "Infrastructure-led development" strategy meets future water demand under the central scenario, while the "Status Quo" and "Efficiency with Scarcity" strategies do not suffice
The analysis assumes 100 litres/capita/day as the baseline (WHO standard), but in a pessimistic "unstable adversity" scenario, only 30 litres/capita/day may be achievable

## Slide 32: 7.4 Strategic evaluation of infrastructure in practice
Infrastructure interdependencies in Saint Lucia
32
The National Infrastructure Assessment for Saint Lucia evaluated key sectors: electricity, water, wastewater, and solid waste, highlighting strong interdependencies, particularly between transport and tourism and between water and wastewater management
Significant interdependencies were noted, such as the utilization of treated wastewater for irrigation and the connections among various sectors that are crucial for national planning
The anticipated expansion of ports and airports could lead to an increased demand for electricity, water, wastewater, and solid waste, with projections showing rises between 9% and 36% by 2050
Projects like anaerobic digestion and waste-to-energy could divert 26% to 35% of waste while potentially generating 6% to 33% of the electricity demand, alongside strategies for water efficiency that might reduce demand by 7.6% to 20%
Cross-sectoral infrastructure interdependencies in Saint Lucia (Adshead et al. 2020)
Quantification of cross-sectoral infrastructure interdependencies for Saint Lucia by 2050 (Adshead et al. 2020)

## Slide 33: 7.4 Strategic evaluation of infrastructure in practice
Summary
In this mini-lecture we illustrate previous concepts with practical applications of strategic evaluation on real cases
We explored waste management, water systems and infrastructure interdependencies in Curacao, Palestine and Saint Lucia, respectively
In this way we review the differences between contexts, assumptions and sectors
33

## Slide 34: 7.4 Strategic evaluation of infrastructure in practice
Bibliography
Adshead, D., L. I. Fuldauer, S. Thacker, O. Román Garcı́a, S. Vital, F. Felix, C. Roberts, et al. 2020. “Saint Lucia: National Infrastructure Assessment.” United Nations Office for Project Services. https://content.unops.org/publications/Saint-Lucia-National-Infrastructure-Assessment.pdf.
Adshead, D., L. Fuldauer, S. Thacker, A. Hickford, Rouhet G., Muller W. S., Hall J. W., and Nicholls R. 2018. “Evidence-Based Infrastructure: Curacao. National Infrastructure Systems Modelling to Support Sustainable and Resilient Infrastructure Development.” United Nations Office for Project Services. https://www.itrc.org.uk/wp-content/uploads/2019/09/UNOPS-ITRC_EBI_Curacao_2018-Full-report.pdf.
Fuldauer, Lena I., Matthew C. Ives, Daniel Adshead, Scott Thacker, and Jim W. Hall. 2019. “Participatory Planning of the Future of Waste Management in Small Island Developing States to Deliver on the Sustainable Development Goals.” Journal of Cleaner Production 223 (June): 147–62. https://doi.org/10.1016/j.jclepro.2019.02.269.
Ives, Matthew C, Scott Thacker, Daniel Adshead, Jim W Hall, Adrian J Hickford, Robert J Nicholls, Trevor Sway Muwafaq, Abu Ayyash, Rob Jones, and Nicholas O’regan. 2018. “A Fast Track Analysis of Infrastructure Provision in Palestine.” https://www.itrc.org.uk/wp-content/PDFs/PalestineFTA_online.pdf.
34

## Slide 35: Thank you
www.climatecompatiblegrowth.com