## Slide 1: Lecture 16: Nature-based solutions for climate risk adaptation
Yu Mo and Amelie Paszkowski, Oxford University

## Slide 2: Learning Outcomes
By the end of this lecture, you will:
Know how different nature-based solutions can be used for climate risk adaptation
Have knowledge of portfolios of natural solutions for water regulation, coastal protection, landslides, soil erosion and urban cooling
Have seen case studies that illustrate how such solutions can be implemented in practice, with all examples from the Global South
Understand the co-benefits that nature-based solutions provide and compared to typical grey infrastructure
Have a base understanding of the role that nature can play as a green or blue infrastructure for climate risk mitigation
2

## Slide 3: 16.1 Nature-based solutions for water regulation
Learning Objectives
To identify a portfolio of nature-based solutions for water regulation in extreme situations of flooding and drought
To illustrate how nature-based solutions have been used in conjunction with hard infrastructure to regulate flood extremes
To recognise the value of nature-based solutions in adapting to and mitigating water extremes
3

## Slide 4: 16.1 Nature-based solutions for water regulation
Introduction to regulation of water extremes
At present, an estimated 4 billion people live in areas of water scarcity and approximately 2.3 billion people are affected by flooding
These figures are expected to rise in the face of climate change. Appropriate water regulation underpins the majority of the SDGs (1, 2, 3, 6, 8, 9, 11, 13, 15, and 17)
Under a changing climate, hard engineering infrastructures constructed in the past is now being tested like never before
Nature is able to adapt itself to changing environmental conditions, and therefore nature-based solutions have become more attractive for sustainable development and longer-term climate resilience
The fundamental concept that underpins nature-based solutions in water management is to mimic the inherent natural water cycle as much as possible
4
Nature-based solutions for water regulation (Cohen-Shacham et al. 2016)
(Damania et al. 2017; GEF 2018)

## Slide 5: 16.1 Nature-based solutions for water regulation
Nature-based solutions for flood regulation
Traditional engineered solutions have often disconnected floodplains from their rivers or tidal channels, and have contributed to a great loss of ecosystem services from these systems
Nature-based solutions allow these ecosystems to thrive, and also offer flexibility and adaptability to further environmental change that built solutions do not provide
These alternative solutions typically address multiple climate challenges at once and can generate larger economic returns because of the co-benefits they create
Salt marshes can reduce non-storm wave heights by an average of 72%, coral and oyster reef systems by 70%, mangroves by 31% and seagrass by 36%
It can be two to five times cheaper to restore coastal wetlands and reef systems than to construct submerged breakwaters
5
Flood type | Hard Engineering options | Nature-based solutions | Co-benefits
Fluvial | Dams Levees/ embankments Flood walls Improved pumping, piping and storage systems Channel modifications | Re-/af- forestation and forest conservation – uses natural ability to retain water, slowing down and absorbing some of the storm flow Riparian buffers: restoring and renaturing areas surrounding rivers and watercourses will increase flood storage capacity Reconnecting rivers to their floodplains Wetland restoration / conservation Constructed wetlands Establishing flood bypasses | Stabilising riverbanks, reducing impacts of flooding, land erosion and landslides Improved water quality through natural filtration Carbon sequestration and storage Increased availability of wild-sourced food (including freshwater fish) and other products Protection of agricultural crops from flooding, safeguarding food supplies (e.g. agroforestry) Pollination services
Pluvial/Urban | Expansion of drainage infrastructure Engineered flood protection | Urban watercourse restoration and ‘re-naturing’ to reduce risk of assets and secure riverbanks Restoration and maintenance of urban greenspaces to improve rainwater infiltration and reduce runoff Swales Green roofs Rain garden Permeable pavements | Improved physical and mental health in urban populations Moderate urban temperatures Create ecological networks which support biodiversity Air purification Noise reduction
Coastal/Tidal | Coastal dykes and levees Sea walls Temporary storm barriers Breakwaters | Mangrove protection and restoration to anchor sediments and dissipate wave energy Coastal marsh and dune management and restoration to dissipate wave energy Coral reef and/or oyster reef restoration and management to attenuate wave energy Sea grass stabilises sediment and reduces storm wave heights | Improved fish stocks Biodiversity conservation Carbon sequestration and storage Sediment accretion and stabilisation of coastline Tourism and recreation
(Bertule et al. 2014; Kapos et al. 2019; Watkins et al. 2019; McDonald and Shemie 2014; Kapos et al. 2019)

## Slide 6: 16.1 Nature-based solutions for water regulation
Nature-based solutions for flood regulation: Case study in China
6
Sponge City Concept (introduced by the Chinese Central Government in 2013): Shift from discharging stormwater to capturing and utilizing it for urban resilience
Key Strategies: Rainwater harvesting, permeable pavements, green spaces, green roofs, and water recycling
2030 Goal of sponge cities: Retain 70% of rainwater across 80% of urban areas to mitigate flooding and enhance sustainability
Jinhua City Example: Yanwei Island Park repurposed former sand quarries with native wetland plants, permeable paving, and flood-adaptive terraces
Urban-Nature Integration: Mimics natural processes to improve flood resilience, reduce runoff, and enhance ecological sustainability
Application of China’s sponge city concept in Jinhuan Yanwei Island Park (Turenscape 2014)
(Hall et al. 2019)

## Slide 7: 16.1 Nature-based solutions for water regulation
Nature-based solutions for drought regulation
Drought Impacts: Wide-reaching environmental, social, and economic effects, including famine, human mortality, agricultural losses, and wildlife deaths
Limited Evidence on NbS: Nature-based solutions (NbS) for drought management are underexplored, with more focus on water supply than demand reduction
Key NbS Strategies: Improve soil quality and vegetation to enhance groundwater recharge, optimizing water availability during dry periods
Green Belt Restoration: Planting native vegetation provides shade to water bodies, reducing evaporation and increasing soil infiltration
Hybrid Approaches: Combining NbS with small-scale grey infrastructure (e.g., water harvesting depressions) can maximize drought resilience
7
Example Impacts | Hard Engineering Options | Nature-based solutions | Potential Co-benefits
Reduced harvests, livestock losses, damage to livelihoods and interruption to supplies of agricultural commodities Water shortages affecting lives, sanitation and economic activity Disruption to transport and industrial processes (e.g., hydropower) | Reservoirs and/or dams Concrete catchments Desalination plants Aqueducts | Management and restoration of watershed vegetation to regulate flows, enhance infiltration and recharge groundwater storage Establish “Green Belts” to increase water availability , retain sediments and nutrients, improve soil quality, and provide shade to minimise evaporation Climate resilient grazing and livestock management to regenerate vegetation and improve soil quality Ecosystems help to reduce sedimentation in reservoirs, increasing their lifespan and reducing cost of dredging Larger-scale rainwater harvesting supporting water resources management Bioswales to replenish groundwater in urban areas Removal of water-thirsty species and replanting with native vegetation Coastal vegetation (mangroves, reefs, salt marshes) can protect water resources from saltwater intrusion | Biodiversity conservation Carbon sequestration and storage Improved soil fertility Increased availability of wild-sourced food (including freshwater fish) and other products Prevent/mitigate damage, preserving longevity of built infrastructure Reduce requirement for built infrastructure Pollination services
Nature-based solutions for addressing drought impacts (Kapos et al. 2019; Watkins et al. 2019)
(United Nations 2018)

## Slide 8: 16.1 Nature-based solutions for water regulation
Nature-based solutions for drought regulation: Case study in India
1985-86 Rajasthan Drought: Unusually low rainfall and excessive logging caused the worst drought in the region’s history, leading to critical groundwater depletion and "dark zones" restricting groundwater use
Community-Led Restoration: NGO Tarun Bharat Sangh helped local communities, especially women, restore natural water storage through small-scale water harvesting, forest regeneration, and soil restoration
Impressive Outcomes: Water returned to 1,000+ villages, five rivers that previously dried up post-monsoon now flow year-round, and fisheries were re-established
Groundwater & Agriculture Revival: Groundwater levels rose by ~6 meters, increasing productive farmland from 20% to 80% of the catchment
Ecosystem Benefits: Forest cover increased by 33%, improving soil integrity, water retention, and providing habitat for wildlife, including antelopes and leopards
Key Takeaway: Working with natural cycles rather than against them yields vast ecological, social, and economic benefits
8
(United Nations 2018)

## Slide 9: 16.1 Nature-based solutions for water regulation
Summary
This mini-lecture has provided an introduction to nature-based solutions for regulating water extremes
A portfolio of options has been provided for both regulating floods and droughts, and case studies have demonstrated how such natural solutions have succeeded in practice
9

## Slide 10: 16.1 Nature-based solutions for water regulation
Bibliography
Bertule, Maija, James Lloyd, Louise Korsgaard, James Dalton, Rebecca Welling, Stefano Barchiesi, and Mark Smith. 2014. Green Infrastructure Guide for Water Management: Ecosystem-Based Management Approaches for Water-Related Infrastructure Projects.
Cohen-Shacham, E., G. Walters, C. Janzen, and S. Maginnis. 2016. “Nature-Based Solutions to Address Global Societal Challenges.” IUCN. https://portals.iucn.org/library/sites/library/files/documents/2016-036.pdf.
Damania, Richard, Sébastien Desbureaux, Marie Hyland, Asif Islam, Scott Moore, Aude-Sophie Rodella, Jason Russ, and Esha Zaveri. 2017. “Uncharted Waters: The New Economics of Water Scarcity and Variability.”
GEF. 2018. “Small Island Developing States and the GEF: Building Lasting Partnerships.” www.thegef.org.
Hall, Jim W., Jeroen C. J. H. Aerts, Bilal M. Ayyub, Stephane Hallegatte, Mark Harvey, Xi Hu, Elco Koks, et al. 2019. “Adaptation of Infrastructure Systems.” Global Commission on Adapatation. https://gca.org/reports/adaptation-of-infrastructure-systems/.
Kapos, Valerie, Sylvia Wicander, Tania Salvaterra, Katie Dawkins, and Charlotte Hicks. 2019. “The Role of the Natural Environment in Adaptation.” Global Commission on Adaptation. https://gca.org/reports/the-role-of-the-natural-environment-in-adaptation/.
McDonald, R. I., and D. Shemie. 2014. “URBAN WATER BLUEPRINT: Mapping Conservation Solutions to the Global Water Challenge.” The Nature Conservancy.
Turenscape. 2014. “Yanweizhou Park in Jinhua City.” https://www.turenscape.com/en/project/detail/4629.html.
United Nations. 2018. “World Water Development Report 2018: Nature-Based Solutions for Water.” United Nations. https://www.unwater.org/publications/world-water-development-report-2018/.
Watkins, Graham, Mariana Silva, Amanda Rycerz, Katie Dawkins, John Firth, Val Kapos, Laura Canevari, Barney Dickson, and Amal-Lee Amin. 2019. “Nature-Based Solutions: Scaling Private Sector Uptake for Climate Resilient Infrastructure in Latin America and the Caribbean.” Inter-American Development Bank. https://publications.iadb.org/publications/english/document/Nature-based_Solutions_Scaling_Private_Sector_Uptake_for_Climate_Resilient_Infrastructure_in_Latin_America_and_the_Caribbean.pdf.
10

## Slide 11: 16.2 Nature-based solutions for coastal protection
Learning objectives
Recognise the value of nature-based solutions for coastal protection
Obtain a basic understanding of how nature-based solutions will adjust and adapt to future climate along the coast
11

## Slide 12: 16.2 Nature-based solutions for coastal protection
Vital coastal ecosystems
Over 40% of the world’s population lives within 100 km of the coastline
The coastal urban population has doubled in the last 40 years and seven of the world’s 10 largest cities are coastal
Various coastal ecosystems, such as coastal wetlands including mangroves and marshes, coral and oyster reefs, sand beaches and dunes, and seagrass, are located around different regions of the world
These coastal ecosystems provide vital provisioning, regulation, supporting, and cultural services:
Provisioning service: products generated from the ecosystem, such as fish, shellfish, and wood
Regulating service: the regulation of ecosystem processes, such as erosion control, flood regulation, storm protection, water purification, and climate regulation
Supporting service: the support of all other ecosystem services, such as soil formation, primary production, and nutrient cycling
Cultural service: the spiritual and emotional benefits people obtain from ecosystems, such as cultural heritage values, tourism, and recreation
These services can be vital to coastal communities, such as food provision and storm protection, and to the global society, such as biodiversity conservation and climate mitigation
12
Global population grid in 3D (Martino et al. 2016)
Global distribution of kelp forests, mangroves, salt marsh, and seagrass (Krause-Jensen, Duarte, and Frigstad 2018)
(Martinez et al. 2007; Martino et al. 2016)

## Slide 13: 16.2 Nature-based solutions for coastal protection
Nature-based solutions for coastal protection
Coastal Climate Threats: Rising sea levels and stronger tropical cyclones threaten coastal communities, with 600 low-lying cities at risk by 2050, potentially causing USD 1 trillion in economic losses
Storm Intensity & Sea-Level Rise: Storm intensity may increase by 2–11% by 2100, with storm surges worsening due to rising sea levels
NbS for Coastal Protection: Restoring and managing mangroves, coral reefs, and wetlands reduces coastal flooding, shoreline erosion, and storm damage
Impact of Coastal Ecosystems: Mangroves reduce coastal flooding impacts by 39% and property damage by 16%.Coral reefs prevent flooding-related damages from doubling, and severe storm damages could rise by 90% without them
Sustainability of NbS: Nature-based solutions offer long-term, ecologically sound alternatives to conventional coastal engineering while providing co-benefits
Decision-Making Tools: Models like InVEST, ARIES, and MIMES help assess the role of natural habitats in coastal protection and risk reduction
13
Hazards | Hard Engineering options | Nature-based solutions | Co-benefits
Flooding | Seawall/dyke Levees | Coastal wetlands such as mangroves and marshes can provide areas of extra water storage and prevent storm surges from reaching inland areas | Provision of fishery and forest products Opportunity for tourism and recreation opportunities Enhancement of biodiversity and habitats for economically or ecologically important species Carbon sequestration for climate mitigation
Shoreline erosion | Seawall/dyke Breakwaters | Protect remaining intertidal ecosystems such as muds, saltmarshes, mangrove, seagrass, and vegetated dunes from further degradation, fragmentation, and loss Coastal wetlands can trap sediment Coastal ecosystems can reduce energy of tidal waves and storm surges, and thus reduce their height and velocity | 
Storm damage | Seawall/dyke Levees | Coastal marsh and dune management and restoration can dissipate wave energy and storm winds | 
Sea-level rise | Seawall/dyke Levee Pumping stations | Coastal wetlands such as mangroves and marshes trap sediment and increase elevation | 
Pollution, eutrophication hypoxia | Wastewater treatment plant | Re- establishment and restoration of coastal wetlands to reduce nutrients and other pollutants in coastal waters Restoration or creation of shellfish reefs to restore active filtration of suspended sediments and removal of nutrients and other pollutants | 
Salinisation | Irrigation | Coastal wetlands can stabilise shoreline and prevent sea water reaching inland areas | 
Nature-based solutions for coastal protection and their co-benefits (Kapos et al. 2019; World Bank 2016)
(Knutson et al. 2010; Smith et al. 2010; Losada et al. 2018)

## Slide 14: 16.2 Nature-based solutions for coastal protection
The flexibility and adaptation of nature-based solutions under climate change
14
Coastal Ecosystem Resilience: Unlike conventional grey infrastructure, coastal ecosystems can self-adjust to changing climates by accreting organic and inorganic material, expanding land area despite rising sea levels
Climate Change Mitigation: Coastal vegetation, particularly wetlands and marshes, plays a crucial role in sequestering CO2, contributing significantly to the global carbon budget
High Carbon Storage: Coastal marshes store more carbon per unit area than forests, with carbon remaining for millennia, unlike forests where it lasts for decades or centuries
Threats from Human Activities: Land conversion and urban expansion can restrict the ability of coastal ecosystems to adapt naturally, reducing their effectiveness in mitigating climate change
Effective NbS Strategies: Nature-based solutions should consider both natural dynamics and human constraints to ensure long-term resilience and functionality
Key processes of vegetated coastal habitats for climate change mitigation and adaptation (Duarte et al. 2013)
Processes that affect the capacity for climate change mitigation (CO2 sinks) and adaptation (shoreline protection from rising sea level) are shown for seagrass meadows (upper panel), salt marshes (middle panel) and mangrove forests (lower panel)
Blue arrows indicate transport of atmospheric or dissolved material, red arrows show transport of particulates and purple arrows indicate vegetative growth.
(World Bank 2016; Zhai et al. 2019; McLeod et al. 2011; Nellemann and Corcoran 2009; Windham-Myers, Crooks, and Troxler 2018; Duarte et al. 2013; Richards and Friess 2016)

## Slide 15: 16.2 Nature-based solutions for coastal protection
Nature-based solutions for storm protection: Case study in Bangladesh
15
Mangroves & Cyclone Protection: Bangladesh, highly vulnerable to hurricanes, has the world’s largest mangrove forests, which reduce water velocity by 29–92% and storm surge height by 4–16.5 cm
Coastal Afforestation Programs: Since 1966, Bangladesh has implemented mangrove restoration efforts to mitigate cyclone impacts, stabilize coastal areas, and support the economy
Key Benefits: Mangrove conservation provides cyclone protection, timber resources, employment, and habitats for wildlife and fisheries
Challenges: Mangrove survival rates are low due to dynamic coastal changes, requiring replanting every 3 years, while human activities like shrimp farming and settlement encroach on new land before it fully matures
Land cover maps of the Sundarban mangrove forest, obtained from Landsat image classification for (a) 1975/1977, (b) 1989, (c) 2000 and (d) 2010. Cyclone tracks of November 1970, November 1988, and that of cyclone SIDR in November 2007 are shown on classified image of 1975, 1989 and 2010 respectively (Quader, Agrawal, and Kervyn 2017)
(Dasgupta et al. 2019; Iftekhar and Islam 2004; Saenger and Siddiqi 1993)

## Slide 16: 16.2 Nature-based solutions for coastal protection
Nature-based solutions for coastal resilience: Case study in Uruguay
16
Coastal Vulnerability in Uruguay: Over 10% of Uruguay’s population lives in low-lying coastal areas; Kiyú suffered USD 1 million in damages from a 2012 storm
Nature-Based Adaptation Program: The Departmental Office of Climate Change (DOCC) led a pilot adaptation program integrating coastal management, vulnerability assessments, and ecosystem-based solutions
Key Adaptation Measures:
Captor fences (1,200m) to trap sand and reduce erosion
Reforestation with native shrubs after removing non-native eucalyptus trees
600m of storm drains and re-profiled roads to manage rainwater and prevent erosion
Scaling Up Success: After success in 2013-2014, Uruguay expanded coastal management projects along San José’s coastline from 2015 onward
Schematic representation of the beach profile (a) before, and (b) after the implementation of soft interventions. Panel (c) shows the desired near-future state, illustrating an ideal rebuilding of both beach profile and ridge of dunes (Carro et al. 2018)

## Slide 17: 16.2 Nature-based solutions for coastal protection
Summary
Nature-based solutions provide effective coastal protection
More importantly, nature-based solutions offer extra flexibility and adaptation to a changing climate compared to traditional grey engineering options
The case studies of restoring mangroves in Bangladesh for storm protection and of planting native shrubs in Uruguay for preventing shoreline erosion have demonstrated how nature-based solutions can be implemented to protect coastal communities in the real world
17

## Slide 18: 16.2 Nature-based solutions for coastal protection
Bibliography
Carro, Inti, Leonardo Seijo, Gustavo J. Nagy, Ximena Lagos, and Ofelia Gutirrez. 2018. “Building Capacity on Ecosystem-Based Adaptation Strategy to Cope with Extreme Events and Sea-Level Rise on the Uruguayan Coast.” Journal Article. International Journal of Climate Change Strategies and Management 10 (4): 504–22. https://doi.org/10.1108/IJCCSM-07-2017-0149.
Dasgupta, Susmita, Md Saiful Islam, Mainul Huq, Zahirul Huque Khan, and Md Raqubul Hasib. 2019. “Quantifying the Protective Capacity of Mangroves from Storm Surges in Coastal Bangladesh.” Journal Article. PLoS ONE 14 (3). https://doi.org/10.1371/journal.pone.0214079.
Duarte, Carlos M., I�igo J. Losada, Iris E. Hendriks, In�s Mazarrasa, and N�ria Marb�. 2013. “The Role of Coastal Plant Communities for Climate Change Mitigation and Adaptation.” Journal Article. Nature Climate Change 3 (11): 961–68. https://doi.org/10.1038/nclimate1970.
Iftekhar, M. S., and M. R. Islam. 2004. “Managing Mangroves in Bangladesh: A Strategy Analysis.” Journal Article. Journal of Coastal Conservation 10 (1): 139–46. https://doi.org/10.1652/1400-0350(2004)010[0139:Mmibas]2.0.Co;2.
Kapos, Valerie, Sylvia Wicander, Tania Salvaterra, Katie Dawkins, and Charlotte Hicks. 2019. “The Role of the Natural Environment in Adaptation.” Global Commission on Adaptation. https://gca.org/reports/the-role-of-the-natural-environment-in-adaptation/.
Knutson, Thomas R., John L. McBride, Johnny Chan, Kerry Emanuel, Greg Holland, Chris Landsea, Isaac Held, James P. Kossin, A. K. Srivastava, and Masato Sugi. 2010. “Tropical Cyclones and Climate Change.” Journal Article. Nature Geoscience 3: 157–63. https://doi.org/10.1038/ngeo779.
Krause-Jensen, Dorte, Carlos Duarte, and Helene Frigstad. 2018. “Marine Forests - Nature’s Own Carbon Capture and Storage.” Report. Science Nordic. https://sciencenordic.com/climate-change-climate-solutions-denmark/marine-forests---natures-own-carbon-capture-and-storage/1458305.
Losada, I. J., P. Men�ndez, A. Espejo, S. Torres, P. D�az-Simal, S. Abad, M. W. Beck, S. Narayan, D. Trespalacios, and K. Pfliegner. 2018. “The Global Value of Mangroves for Risk Reduction.” Journal Article. Technical Report.
Martinez, M. L., A. Intralawan, G. V�zquez, O. Perez-Maqueo, P. Sutton, and R. Landgrave. 2007. “The Coasts of Our World: Ecological, Economic and Social Importance.” Journal Article. Ecological Economics 63 (2-3): 254–72. https://doi.org/10.1016/j.ecolecon.2006.10.022.
Martino, Pesaresi, Michele Melchiorri, Alice Siragusa, and Thomas Kemper. 2016. “Atlas of the Human Planet 2016: Mapping Human Presence on Earth with the Global Human Settlement Layer.” Journal Article. European Commission.
McLeod, Elizabeth, Gail L. Chmura, Steven Bouillon, Rodney Salm, Mats Bj�rk, Carlos M. Duarte, Catherine E. Lovelock, William H. Schlesinger, and Brian R. Silliman. 2011. “A Blueprint for Blue Carbon: Toward an Improved Understanding of the Role of Vegetated Coastal Habitats in Sequestering Co2.” Journal Article. Frontiers in Ecology and the Environment 9 (10): 552–60.
Nellemann, Christian, and Emily Corcoran. 2009. Blue Carbon: The Role of Healthy Oceans in Binding Carbon: A Rapid Response Assessment. Book. UNEP/Earthprint.
Quader, Mohammad Abdul, Shefali Agrawal, and Matthieu Kervyn. 2017. “Multi-Decadal Land Cover Evolution in the Sundarban, the Largest Mangrove Forest in the World.” Journal Article. Ocean & Coastal Management 139: 113–24. https://doi.org/10.1016/j.ocecoaman.2017.02.008.
Richards, D. R., and D. A. Friess. 2016. “Rates and Drivers of Mangrove Deforestation in Southeast Asia, 2000-2012.” Journal Article. Proc Natl Acad Sci U S A 113 (2): 344–49. https://doi.org/10.1073/pnas.1510272113.
Saenger, Peter, and N. A. Siddiqi. 1993. “Land from the Sea: The Mangrove Afforestation Program of Bangladesh.” Journal Article. Ocean & Coastal Management 20 (1): 23–39.
Smith, Jane Mc Kee, Mary A. Cialone, Ty V. Wamsley, and Tate O. McAlpin. 2010. “Potential Impact of Sea Level Rise on Coastal Surges in Southeast Louisiana.” Journal Article. Ocean Engineering 37 (1): 37–47. https://doi.org/10.1016/j.oceaneng.2009.07.008.
Villamizar, Alicia, Maria E. Guti�rrez, Gustavo J. Nagy, Ruben M. Caffera, and Walter Leal Filho. 2016. “Climate Adaptation in South America with Emphasis in Coastal Areas: The State-of-the-Art and Case Studies from Venezuela and Uruguay.” Journal Article. Climate and Development 9 (4): 364–82. https://doi.org/10.1080/17565529.2016.1146120.
Windham-Myers, Lisamarie, Stephen Crooks, and Tiffany G. Troxler. 2018. A Blue Carbon Primer: The State of Coastal Wetland Carbon Science, Practice and Policy. Book. CRC Press.
World Bank. 2016. “Managing Coasts with Natural Solutions: Guidelines for Measuring and Valuing the Coastal Protection Services of Mangroves and Coral Reefs.” Report.
Zhai, Lu, Bo Zhang, Shouraseni Sen Roy, Douglas O. Fuller, and Leonel da Silveira Lobo Sternberg. 2019. “Remote Sensing of Unhelpful Resilience to Sea Level Rise Caused by Mangrove Expansion: A Case Study of Islands in Florida Bay, USA.” Journal Article. Ecological Indicators 97: 51–58. https://doi.org/10.1016/j.ecolind.2018.09.063.
18

## Slide 19: 16.3 Nature-based solutions for erosion and landslide control
Learning objectives
Obtain a portfolio of nature-based solutions for both erosion and landslide mitigation
Appreciate the value of nature-based solutions in addressing the hazards of erosion and landslides
19

## Slide 20: 16.3 Nature-based solutions for erosion and landslide control
Introduction
Impacts of Intense Rainfall: Heavy precipitation can trigger soil erosion and landslides, severely affecting livelihoods and infrastructure
Global Landslide Fatalities: Between 2004–2016, nearly 56,000 people died from landslides, with India, China, the Philippines, and Nepal being most affected
Economic Costs of Soil Erosion: Soil erosion causes USD 400 billion in annual losses, damaging agriculture, increasing sedimentation in reservoirs, and weakening riverbanks
Causes of Increased Landslides: Extreme rainfall, deforestation, overexploitation, land-use changes, and construction drive the rising frequency of landslides
Nature-Based Solutions (NbS): The lecture will explore NbS for erosion control in Bangladesh and landslide management in Nepal as sustainable approaches to these challenges
20
(Kapos et al. 2019; Stokes et al. 2014; European Environment Agency 2015; Stokes et al. 2014; )

## Slide 21: 16.3 Nature-based solutions for erosion and landslide control
21
Nature-based solutions for erosion control
Erosion & Waterbodies: Climate-related erosion mainly occurs near coastlines and riverbanks, where water exerts pressure on unstable soils
Vegetation as a Key Solution: Planting vegetation along riverbanks and coastlines stabilizes soil, reduces erosion risk, and provides protective ground cover
Coastal Erosion Control: Mangroves are a well-known NbS for reducing coastal erosion, while in non-mangrove regions like the UK, seagrass helps stabilize sediments
Riverine Erosion Control: Vegetation along river catchments minimizes soil exposure, stabilizes banks, and reduces sediment loss into waterways
Erosion type | Hard Engineering options | Nature-based solutions | Co-benefits
Riverine | River walls Concrete river embankments Riverine groynes Sandbags (not truly hard engineering) | Riparian buffers- vegetate riverbanks to stabilise the soils from erosion Agroforestry and/or “conservation agriculture” within watershed – enhance canopy interception of rainfall reducing soil exposure and erosion | Reduced fluvial flood risk Improved water quality through natural filtration Carbon sequestration and storage Pollination services Biodiversity conservation
Coastal / Tidal | Coastal dykes and levees Sea walls Temporary storm barriers Breakwaters | Mangrove protection and restoration to anchor sediments and dissipate wave energy Coastal marsh and dune management and restoration to dissipate wave energy Coral reef and/or oyster reef restoration and management to attenuate wave energy Sea grass – stabilises sediment and regulates water currents that contribute to coastal erosion | Reduced coastal flood risk Improved fish stocks Biodiversity conservation Carbon sequestration and storage Tourism and recreat
Nature-based solutions for riverine and coastal erosion (Kapos et al. 2019)
Notes: There are now several open-source hazard products at global scales which are being used widely for vulnerability and risk analysis. A few resources include:
Global river and coastal flood maps: Historical and future hazard maps at different return periods (2, 5, 1, 25, 50, 10, 250, 500, 100 years). All data is available at a 30 arc-seconds resolution (~1km at equator) (Gassert et al. 2015).
Global hazard maps for earthquakes for different return periods (250, 475, 975, 1500, 2475 years) both Peak Ground Acceleration and spectral acceleration. Data is available at 0.072 degrees (~8km at equator).
Global dataset of 1,000 synthetic tropical cyclones paths with cyclone characteristics (e.g., wind speed, pressure) on a global scale. Wind speed probabilities are derived globally (1 metre, 1 minutes sustained speed) for different return periods (1 to 1,000 years) at 1km resolution (Bloemendaal et al. 2019).

## Slide 22: 16.3 Nature-based solutions for erosion and landslide control
Case study of nature-based solutions for erosion control: Bangladesh
Riverine erosion in Bangladesh is a major driver of poverty, threatening 15–20 million people, with 870 km² of land lost along the Brahmaputra River only since 1973
It has become evident that engineering structures are not able to control the dynamic nature of these vast river systems
A mosaic of nature-based solutions in different local areas along riverbanks and coastal regions have shown to be effective with erosion management:
Planting vetiver grass (Chrysopogon zizanoides) to protect the surface of existing earthen embankments from erosion (Zaman et al. 2016)
Encouraging farmers to leave a few centimetres of stem from their crops during harvest in order to trap suspended sediments and prevent soil erosion (Khalequzzaman 1994)
Breaching of existing embankments (locally termed Tidal River Management) in order to re-establish the natural sedimentation patterns between river and floodplain and reduce the scouring on existing erosion and flood infrastructure
The solution is a combination of localised mitigation measures, and strong collaboration between decision-makers, researchers, engineers, local authorities and local communities
22
(Rahman, Islam, and Rahman 2015)

## Slide 23: 16.3 Nature-based solutions for erosion and landslide control
Nature-based solutions for landslides
Vegetation can also be used to stabilise slopes that are prone to landslides
Thick roots act like nails in the soil on slopes, reinforcing the soil
The effectiveness of vegetation in protecting slopes depends on the architecture and extent of the root system; root depth and distribution have been identified as the most important properties for slope stabilisation
Vegetation can therefore stabilise soil through its roots, but also protect the soil surface from surface erosion as well as from gully formation
Vegetating slopes for stabilisation is predominantly done by planting live cuttings and rooted plants into the ground in various arrangements and geometric arrays, in a way that will reinforce soil and create barriers to earth movement
Drain excess water from the slope, enhancing drainage and avoiding soil saturation and slumping of earth materials
23
(Stokes et al. 2014; ADPC 2020)

## Slide 24: 16.3 Nature-based solutions for erosion and landslide control
Case study of nature-based solutions for landslides: Nepal
24
Due to monsoon rainfall and frequent earthquakes, Nepal is highly prone to landslides, with over 4,000 landslides recorded since the 2015 earthquake
High-Risk Terrain: Shallow landslides (top 2m of soil) are common on hillslopes, worsened by poorly secured roads that make slopes more vulnerable
Nature-Based Stabilization: Vegetating slopes using grass lines, jute netting, bamboo fencing, and vegetated stone pitching is a cost-effective erosion control method
Amriso (Broom Grass) as a Key Solution: This fast-growing plant stabilizes soil with a strong root network while providing fodder, fuel, and broom-making material, reducing landslides in rural areas
The success of these nature-based solutions relies on local community participation in implementing and maintaining slope stabilization measures
Local communities planting Amriso along unstable steep slopes (WWF 2013)
(IUCN 2021)

## Slide 25: 16.3 Nature-based solutions for erosion and landslide control
Summary
This mini-lecture provided an overview of the challenges faced with erosion and landslides and how nature-based solutions can provide alternative options to traditional hard-engineering measures
Two case studies were presented: natural riverine erosion management in Bangladesh and natural landslide management in Nepal
25

## Slide 26: 16.3 Nature-based solutions for erosion and landslide control
Bibliography
ADPC. 2020. “Nature-Based Solutions (NbS) for Landslide Risk Management.” ADPC. http://www.adpc.net/igo/category/ID1643/doc/2020-pULw5B-ADPC-Nature_based_Soltutions_for_Landslide_Risk_Management_ADPC.pdf.
European Environment Agency. 2015. “Exploring Nature-Based Solutions — the Role of Green Infrastructure in Mitigating the Impacts of Weather- and Climate Change-Related Natural Hazards.” European Environment Agency. https://www.eea.europa.eu/publications/exploring-nature-based-solutions-2014.
IUCN. 2014. “Community-Based Bio-Engineering for Eco-Safe Roadsides in Nepal.”
———. 2021. “NEPAL | IUCN.” https://www.iucn.org/theme/ecosystem-management/our-work/environment-and-disasters/ecosystems-protecting-infrastructure-and-communities-epic/nepal.
Kapos, Valerie, Sylvia Wicander, Tania Salvaterra, Katie Dawkins, and Charlotte Hicks. 2019. “The Role of the Natural Environment in Adaptation.” Global Commission on Adaptation. https://gca.org/reports/the-role-of-the-natural-environment-in-adaptation/.
Khalequzzaman, MD. 1994. “Recent Floods in Bangladesh: Possible Causes and Solutions.” Natural Hazards. Vol. 9.
Rahman, Mirza A. T. M. Tanvir, Shofiul Islam, and Syed Hafizur Rahman. 2015. “Coping with Flood and Riverbank Erosion Caused by Climate Change Using Livelihood Resources: A Case Study of Bangladesh.” Climate and Development 7 (March): 185–91. https://doi.org/10.1080/17565529.2014.910163.
Stokes, Alexia, Grant B Douglas, Thierry Fourcaud, Filippo Giadrossich, Clayton Gillies, Thomas Hubble, John H Kim, et al. 2014. “Ecological Mitigation of Hillslope Instability: Ten Key Issues Facing Researchers and Practitioners.” Plant Soil 377: 1–23. https://doi.org/10.1007/s11104-014-2044-6.
WWF. 2013. “Broom Grass — a Boon for Communities and Ecosystems | WWF.” https://wwf.panda.org/?212732/broom-grass--a-boon-for-communities-and-ecosystems.
Zaman, Md Wasif, Tansir Zaman Asik, Md Yousuf Rumi, and H M Shahin. 2016. “GEOTECHNICAL HAZARD ANALYSIS OF RIVER EMBANKMENT OF BANGLADESH AND ITS PROTECTABILITY.” International Journal of GEOMATE. Vol. 10. Online.
26

## Slide 27: 16.4 Nature-based solutions for urban cooling
Learning objectives
Understand why and how the urban heat island occurs
Recognise the importance of nature-based solutions in addressing urban heat island effects
Obtain a portfolio of nature-based solutions for urban cooling
27

## Slide 28: 16.4 Nature-based solutions for urban cooling
Introduction to the need for cooling
Rising Urban Temperatures: Over 140,000 deaths from 83 heatwaves in Europe since 2000, with 1,000 cities expected to reach 25°C summer highs by 2050, exposing 800% more people to extreme heat
Energy Demand Surge: Cooling demand will triple by 2050, increasing from 2,020TWh to 6,200TWh, leading to higher electricity consumption and emissions
Economic Costs: High temperatures could cost the global economy USD 2 trillion by 2030, while air conditioning use creates a vicious cycle of warming and cooling
Urban Heat Island Effect: Cities face worsened heat impacts due to dense buildings, air pollution, and limited green spaces, exacerbating health risks
Nature-Based Solutions (NbS): Urban greening, canopy cover, and evaporative cooling can reduce local temperatures and mitigate health risks from rising urban heat
28
Introduction to natural solutions for heat mitigation in urban settings
(UNEP 2020; Kapos et al. 2019; Hall et al. 2019; Bowler et al. 2010)

## Slide 29: 16.4 Nature-based solutions for urban cooling
The urban heat island (UHI) effect
Urban Heat Island (UHI) Effect: Cities retain heat due to impervious surfaces (roads, buildings), low albedo, and minimal green cover, exacerbating warming
Additional Heat Sources: Waste heat from industry, air conditioning, and transportation further increases urban temperatures and air pollution
Rising Heat Risks: UHI, combined with global warming, is increasing extreme heat events, disproportionately affecting poorer neighbourhoods with limited cooling access
Challenges of Cooling: Large-scale air conditioning is costly and energy-intensive, worsening emissions and heat buildup
Nature-Based Solutions (NbS): Blue and green infrastructure provide cost-effective cooling through shade and evapotranspiration, mitigating heat risks
29
Conceptualisation of the urban heat island effect (Wong et al. 2021)
(UNEP 2020; Makido, Hellman, and Shandas 2019; Wong et al. 2021; Bowler et al. 2010; Depietri, Welle, and Renaud 2013)

## Slide 30: 16.4 Nature-based solutions for urban cooling
Nature-based solutions for UHI mitigation
30
Urban areas can be up to 4°C hotter than natural areas due to limited vegetation, exacerbating the Urban Heat Island (UHI) effect
Cooling Potential of NbS: Urban trees can reduce air conditioning costs by 10%, and water bodies can lower temperatures by up to 0.9°C
Increasing canopy cover, expanding green spaces, restoring forests and wetlands, and implementing green roofs and agroforestry help cool cities
Using light-colored roofs, walls, and pavements enhances cooling by reflecting sunlight and reducing heat absorption (complementary solutions)
Co-benefits of nature-based solutions are carbon sequestration, biodiversity, pollution control, soil fertility, tourism, and improved physical and mental health
(a) Proposed framework for implementing nature-based solutions in urban environments at different scales; and (b) a summary of cooling benefits from nature-based solutions (Wong et al. 2021)
(Kapos et al. 2019; Bowler et al. 2010; Gill et al. 2007)

## Slide 31: 16.4 Nature-based solutions for urban cooling
Nature-based solutions for cooling at the building scale
31
Nature-based solutions for heat mitigation at the building scale (Wong et al. 2021)
In dense urban environments, large greenspaces are difficult to create, requiring innovative green and blue infrastructure solutions
Green roofs and walls enhance thermal insulation, evapotranspiration, shade, and albedo, reducing heat inside and around buildings
Placement matters—self-shading and overshadowing from buildings can impact cooling efficiency, which is highest in summer due to increased evapotranspiration
Green walls inside buildings can regulate air temperature, improve air quality, and enhance well-being
(Wong et al. 2021; Gill et al. 2007)

## Slide 32: 16.4 Nature-based solutions for urban cooling
Case study of urban greening: Singapore
32
With one of the highest population densities globally, Singapore experiences summer temperatures up to 7°C higher in urban centres than surrounding areas
A government-funded project collaborates with researchers to implement nature-based solutions across buildings, landscapes, and infrastructure
Green roofs, walls, and upper-level greenery are now required to expand green and blue infrastructure in the densely urbanized city
High sun intensity makes green roofs effective, while high humidity enhances vegetation growth with minimal water use
Studies show urban parks reduce temperatures by 4°C, demonstrating the effectiveness of Singapore’s innovative and aesthetic green urban design
Singapore’s use of nature-based solutions in mitigating the urban heat island effect.
(Vahanvati and Keating 2020)

## Slide 33: 16.4 Nature-based solutions for urban cooling
Summary
This mini-lecture has introduced the challenges of rising urban temperatures, defined the urban heat island effect, and provided nature-based solutions for mitigating urban heat at both the city and building scale
Through the “Cooling Singapore” project, these nature-based solutions are shown in practice
33

## Slide 34: 16.4 Nature-based solutions for urban cooling
Bibliography
Bowler, Diana E., Lisette Buyung-Ali, Teri M. Knight, and Andrew S. Pullin. 2010. “Urban Greening to Cool Towns and Cities: A Systematic Review of the Empirical Evidence.” Landscape and Urban Planning. Elsevier. https://doi.org/10.1016/j.landurbplan.2010.05.006.
Depietri, Yaella, Torsten Welle, and Fabrice G. Renaud. 2013. “Social Vulnerability Assessment of the Cologne Urban Area (Germany) to Heat Waves: Links to Ecosystem Services.” International Journal of Disaster Risk Reduction 6 (December): 98–117. https://doi.org/10.1016/j.ijdrr.2013.10.001.
Gill, Susannah E., John F. Handley, Adrian Roland Ennos, and Stephan Pauleit. 2007. “Adapting Cities for Climate Change: The Role of the Green Infrastructure.” Built Environment 33: 115–33. https://doi.org/10.2148/benv.33.1.115.
Hall, Jim W., Jeroen C. J. H. Aerts, Bilal M. Ayyub, Stephane Hallegatte, Mark Harvey, Xi Hu, Elco Koks, et al. 2019. “Adaptation of Infrastructure Systems.” Global Commission on Adapatation. https://gca.org/reports/adaptation-of-infrastructure-systems/.
Kapos, Valerie, Sylvia Wicander, Tania Salvaterra, Katie Dawkins, and Charlotte Hicks. 2019. “The Role of the Natural Environment in Adaptation.” Global Commission on Adaptation. https://gca.org/reports/the-role-of-the-natural-environment-in-adaptation/.
Makido, Yasuyo, Dana Hellman, and Vivek Shandas. 2019. “Nature-Based Designs to Mitigate Urban Heat: The Efficacy of Green Infrastructure Treatments in Portland, Oregon.” Atmosphere 10 (May): 282. https://doi.org/10.3390/atmos10050282.
Ruefenacht, Lea A., and Juan Angel Acero. 2017. “Strategies for Cooling Singapore: A Catalogue of 80+ Measures to Mitigate Urban Heat Island and Improve Outdoor Thermal Comfort.” Str. https://doi.org/10.3929/ethz-b-000258216.
UNEP. 2020. “How Cities Are Using Nature to Keep Heatwaves at Bay.” https://www.unep.org/news-and-stories/story/how-cities-are-using-nature-keep-heatwaves-bay.
Vahanvati, Mittul, and Adriana Keating. 2020. “What Australia Can Learn from Singapore about Designing Our Cities to Reduce Urban Heat | the Fifth Estate.” https://thefifthestate.com.au/articles/what-australia-can-learn-from-singapore-about-designing-our-cities-to-reduce-urban-heat/.
Wong, Nyuk Hien, Chun Liang Tan, Dionysia Denia Kolokotsa, and Hideki Takebayashi. 2021. “Greenery as a Mitigation and Adaptation Strategy to Urban Heat.” Nature Reviews Earth & Environment 2 (January): 166–81. https://doi.org/10.1038/s43017-020-00129-5.
Wong, Nyuk Hien, and Chen Yu. 2005. “Study of Green Areas and Urban Heat Island in a Tropical City.” Habitat International 29 (September): 547–58. https://doi.org/10.1016/j.habitatint.2004.04.008.
34

## Slide 35: Thank you
www.climatecompatiblegrowth.com