## Slide 1: Transport decarbonization and data-to-deal Lecture 2: Mobility, Accessibility and Transport Demand
Notes: Hello and welcome to this lecture on mobility, accessibility and travel demand.

## Slide 2: Lecture 2: Learning Outcomes
By the end of this lecture, you will be able to:
Discuss the main drivers of transport demand
Describe concepts of mobility and accessibility
Discuss and compare the main measures of accessibility
Place this into context of sustainable transport planning and building decarbonisation pathways
Notes: By the end of this lecture, you will be able to:
Discuss the main drivers of transport demand
Describe concepts of mobility and accessibility
Discuss and compare the main measures of accessibility
Place this into context of sustainable transport planning and building decarbonisation pathways

## Slide 3: 1. Mobility and accessibility
Key concepts

## Slide 4: Revision: Transport moves people or goods from A to B
For example: you are at point A, and you are hungry
Getting to point B unlocks some sort of value that you don’t have at part A (food)
Transport is a derived demand: generally, transport users don’t get value from the act of travelling itself, they do the travelling to abstract some value out of being at their destination
A
B
0.6 km
5,561 km
Restaurant, Ingram St, Glasgow
Restaurant, Turusbekov St, Bishkek
Home
“DISTANCE”
Notes: Revision from last time: The purpose of a transport system is to move people or goods between points in space. For example: you are at point A, and you are hungry.
Getting to point B unlocks some sort of value that you don’t have at part A (food). This demonstrates a fundamental assumption about transport, that transport is a derived demand. This means that, generally speaking, transport users don’t get value from the act of travelling itself, they do the travelling to abstract some value out of being at their destination.

## Slide 5: Mobility
Mobility = the ease of movement of a passenger or unit of freight
When mobility is high, activities are less constrained by distance
New York Times.
Notes: Time now to introduce a fundamental concept in transport systems. Mobility, like the name implies, is the ability of movement. It’s how easy it is for a passenger or a unit of freight to overcome a unit of physical difference. Therefore, when mobility is high, activities are less constrained by distance.

## Slide 6: Mobility ~ “cost per kilometre”
In Nairobi, travelling 11 km across the city takes 64 min by public transport (matatu)
In Tokyo, travelling 11 km across the city takes 17 min by public transport (subway)
Nairobi, Kenya
Tokyo, Japan
Notes: Mobility can therefore be thought of as ‘cost per kilometre’. Recall from last lecture that we are now talking in terms of generalised cost – this is not just a ticket price or a fuel price but it is the sum total of monetary costs, journey time, any discomfort, any additional costs imparted on the user. Let’s consider these two examples. In Nairobi, if we travel 11 km through the city by public transport, then it will take 64 min by matatu. In Tokyo, if we want to travel the same distance through the city by public transport, then it will take 17 minutes by subway. We could conclude on the basis of this comparison that public transport users in Tokyo enjoy greater mobility than public transport users in Nairobi.

## Slide 7: Accessibility
Accessibility is the potential for interaction, both social and economic. (Handy, 1994)
A basic dimension of city performance (Lynch, 1984)
When accessibility is high, transport system users have greater opportunities to participate in value-returning activities
Handy, S. (1994). Highway blues: nothing a little accessibility can’t cure. Access. https://escholarship.org/uc/item/66k8b8bz
Lynch, K. (1981). Good city form. MIT Press. https://mitpress.mit.edu/9780262620468/good-city-form/
What determines accessibility?
Travel cost: the lower the travel cost, the greater the amount of destinations that can be reached in a given budget – and the greater the accessibility
Travel choice: the wider the variety of modes for getting to a particular destination, the greater the accessibility
Destination choice: the more destinations, and the more varied the destinations, the greater the accessibility
Notes: Now let’s consider another fundamental concept in transport systems: accessibility. If mobility was the ability to move, then it stands to reason that accessibility is the ability to access. Indeed that’s what we have: Susan Handy defines it was the potential for interaction, both social and economic. Lynch cites accessibility as a basic dimension of city performance. When accessibility is high, transport system users have greater opportunities to participate in value-returning activities.

## Slide 8: Mobility vs. Accessibility
Mobility ~ cost per kilometre
  How easy is it to overcome physical distance?
Accessibility ~ cost per unit of destination
  How many value-returning activities can you get per unit of travelling?
Mobility is a property of a transport system, determined by the spatial structure of its network and the level of quality of its service
Accessibility is a property of a human settlement, determined by mobility and the built environment
Notes: Mobility tells us how easy it is to overcome physical distance, but accessibility tells us how many value-returning activites we can get per unit of travelling.
Therefore, mobility is a property of a transport system determined by the spatial structure of its network and the level of quality of its service. Accessibility is a property of a human settlement, determined by mobility and the built environment

## Slide 9: Does good mobility mean good accessibility?
Mobility is determined by road capacity, design speed, and (in the case of automobile mobility) how many other people are using the road
Mobility is also driven by travel costs and their relation to individuals’ budgets
US-95 and I-15 interchange in downtown Las Vegas, Nevada. | trekandphoto / Adobe Stock
This wide, high-speed highway intersection in downtown Las Vegas represents high mobility to individuals with access to a vehicle that can use it (except under high traffic conditions!)
That mobility will help individuals overcome distance and thus reach more destinations (increasing accessibility).
But where are the destinations?
Notes: Does good mobility mean good accessibility? For example, for automobiles, mobility is determined by road capacity, design speed and how many other people are using the road at that time. Mobility is also driven by travel costs and how much people can budget for.
Good mobility makes it easier to move, so naturally that means it is easier to access more opportunities. But it’s not the whole story. For example – see the picture on the right. This wide, high-speed highway intersection in downtown Las Vegas represents high mobility to individuals with access to a vehicle that can use it (except under high traffic conditions!) That mobility will help individuals overcome distance and thus reach more destinations (increasing accessibility). But where are the destinations?

## Slide 10: Good mobility vs. good accessibility
Good mobility usually contributes to good accessibility because it means easier travel between two points
But poor mobility doesn’t necessarily mean poor accessibility if goods, services and activities can be accessed without vehicular travel
Shibuya, downtown Tokyo | Google Maps
High diversity in land use means more destinations (commercial, employment, social) are nearby to where people live
High density means travel distances shorter (and therefore required speed is lower for a given level of accessibility)
Mobility provided for pedestrians (shorter distance  lower design speed) and public transport users (metro railway)
Metro
Notes: Good mobility usually contributes to good accessibility because it means easier travel between two points.
But poor mobility doesn’t necessarily mean poor accessibility if goods, services and activities can be accessed without vehicular travel
Consider the picture on the right. High diversity in land use means more destinations (commercial, employment, social) are nearby to where people live. High density means travel distances shorter (and therefore required speed is lower for a given level of accessibility)

## Slide 11: Accessibility – summary
Accessibility acknowledges that the demand for travel is derived from the demand for activities
Mobility ignores the derived nature of travel demand, focusing instead on the ability to travel (as if movement was the goal)
“Mobility is only the means – activities are the end and accessibility is the key” (Handy, 2020)
Handy, S. (2020). Is accessibility an idea whose time has finally come? Transportation Research Part D. vol 83. https://doi.org/10.1016/j.trd.2020.102319
Notes: In summary:
Accessibility acknowledges that the demand for travel is derived from the demand for activities
Mobility ignores the derived nature of travel demand, focusing instead on the ability to travel (as if movement was the goal)
“Mobility is only the means – activities are the end and accessibility is the key” (Handy, 2020)

## Slide 12: 2. Travel demand and the built environment
Drivers of passenger travel demand, time budgets, land use, induced demand and the cycle of congestion

## Slide 13: The D’s of (urban) travel demand
3 D’s (Cervero, 1997):
  Density
  Diversity (of land use)
  Design (of networks)
7 D’s (Ewing, 2010):
  (The 3 above plus…)
  Destination accessibility
  Distance to transit
  Demand management
  Demographics
Cervero, R., & Kockelman, K. (1997). Travel demand and the 3Ds: Density, diversity, and design. Transportation Research Part D: Transport and Environment, 2(3)
Ewing, R., & Cervero, R. (2010). Travel and the built environment: A meta-analysis. Journal of the American Planning Association, 76(3)
Handy, S., Cao, X., & Mokhtarian, P. (2005). Correlation or causality between the built environment and travel behavior? Evidence from Northern California. Transportation Research Part D.
“Cities don’t promote density for its own sake — they promote density to increase accessibility. Using accessibility as the performance measure by which we assess current conditions and proposed policies could shift the public debate away from the scary idea of density, which often provokes hostile responses…
…It’s time to be done with the Ds and get back to A.”
– Prof Susan Handy (UC Davis) https://bit.ly/3J4f8bV
Notes: What defines travel demand? So far we have spoken that travel demand comes from the demand to take part in activities, or to procure goods or services. But the spatial distribution of those things we want to access, and how easy it is to access them, clearly influences our travel demand.
Cervero established the 3 D’s of urban travel demand as the density (of opportunities), the diversity of land use and the design of networks.
In 2010 Ewing introduced 7 more Ds. On the right we have a statement contradicting that. “Cities don’t promote density for its own sake — they promote density to increase accessibility. Using accessibility as the performance measure by which we assess current conditions and proposed policies could shift the public debate away from the scary idea of density, which often provokes hostile responses…
…It’s time to be done with the Ds and get back to A.”

## Slide 14
Metz, D. (2004). Travel time constraints on transport policy, Proceedings of ICE, Transport, 157, Issue TR2, pp99-105
Time budgets and passenger transport
Notes: This is another way of framing travel demand. Marchetti’s constant is based on some fundamental transport analysis, that ever since antiquity humans have tended to travel around an hour per day. This remains remarkably stable in the present day where measurement of such things is more reliable, as shown on the right. What this means is that whereas in ancient cities an hour a day would mean our daily radius would not generally exceed a few kilometres, with the advent of technologies like trams, subways and cars we have the ability to travel much further on the same time budget. This comes back to our earlier discussion on mobility. Mobility makes it easier to overcome distance, but if our budget for time stays roughly the same, then our distance will naturally increase.

## Slide 15
Sources: Adams, 1970
What this means for land use
Notes: This can be linked directly to land use in our cities. This is a model of many cities that have been around for over 200 years or so. In each zone we have a different dominant mode of passenger travel, and it goes to say that the cost of transport between those zones is a strong influence in that land is developed:
I (1800 – 1890) Walking/horsecar
II (1890 -1920) Electric Streetcar
III (1920 – 1945) Recreational Auto
IV (1945 – 1970) Motorway

## Slide 16: What this means for land use (II)
Notes: We can see this in real life – I have chosen the US city of Detroit but this could be many places. You can see the industrial clusters along the main road, which benefit from reduced travel costs associated with being near the road. You can also see residential areas far away from areas of employment. These high-capacity, high-speed roads between the suburbs and the city centre allow for the land to be developed in this way.

## Slide 17
Cost of travel
Travel Demand
A
B
Jevon’s paradox
A reduction in the cost of any commodity will result in an increased demand for that commodity. Reduce the cost of motoring (e.g. fuel price) and more people will drive!
Notes: This observed phenomenon that travel simply increases if it becomes easier to overcome distance is an example of the Jevons Paradox. Jevons Paradox occurs when technological improvements that increase the efficiency of resource use (e.g. vehicles that cost less to run, or move further in a given time) lead to higher overall consumption rather than savings. First observed by economist William Stanley Jevons in the 19th century with coal use, this paradox highlights the unintended consequences of efficiency gains in economics and sustainability. A reduction in the cost of any commodity will result in an increased demand for that commodity. Reduce the cost of motoring (e.g. fuel price) and more people will drive!

## Slide 18
Eyre, N and Killip, G. (eds). 2019. Shifting the focus: energy demand in a net-zero carbon UK. Centre for Research into Energy Demand Solutions. Oxford, UK. ISBN: 978-1-913299-04-0
Jevon’s paradox in practice
The UK Department for Transport anticipates that large-scale switch to zero-emission vehicles (ZEVs) will increase vehicle use because of falling motoring costs
Notes: Jevon’s paradox is accounted for in policy and planning. This graph shows traffic growth scenarios by the UK Department for Transport. The largest traffic growth scenario occurs from the biggest switch to zero emissions vehicles. This happens because the cost of motoring in electric vehicles is significantly lower than their petrol counterparts; therefore, the government anticipates that this will increase travel demand as a result of the cost falling.

## Slide 19
British Rail advert, 1979
Induced demand
Notes: Why is Jevon’s paradox important for transport planning and policy? Induced demand is an observed phenomenon associated with building transport infrastructure. For example, if a road is widened, it reduces the ‘cost’ of travel. Therefore, according to Jevon’s paradox, the demand for travel will increase. This ‘induced’ demand highlights how infrastructure development in transport often has unintended consequences.

## Slide 20: Vicious spiral of congestion
Rodrigue, J. P. (2020). The Geography of Transport Systems (Fifth Edition). New York: Routledge.
Notes: The result of induced demand is often called the ‘vicious spiral of congestion’. A local transport authority sees that their roads are congested, and faces pressure to increase capacity. They build new capacity, which results in a lower friction to mobility. Therefore, using Marchetti’s constant theory, people will simply travel further for the same time budget and thus urban sprawl is incited. The length and number of journeys then increases, adding demand to the network, until you are at the point of congestion once more.

## Slide 21: Externalities of car use
This (non-exhaustive) list describes some of the negative externalities of car-centric transport systems (and how they relate to non-communicable diseases)
Electrification will reduce air pollution and climate impacts but will do little for many other impacts!
https://transformative-mobility.org/multimedia/health-impacts-of-automobility/
Notes: But what’s the problem? What’s wrong with extra car traffic? If we can continue building, then at some point surely true demand will be realised and car travel demand will be satisfied? Well, that may satisfy the demand for travel amongst the car users, but we also must think about externalities (external ‘costs’) that are not taken into account by thinking just of travel times and fuelling costs. This (non-exhaustive) list describes some of the negative externalities of car-centric transport systems (and how they relate to non-communicable diseases). Electrification will reduce air pollution and climate impacts but will do little for many other impacts!

## Slide 22: 4. Freight demand and vehicle ownership
Drivers of freight demand and vehicle ownership

## Slide 23
Freight activity correlated with income (higher disposable incomes  higher demand for consumption  more freight activity)
Slide courtesy of Pierpaolo Cazzola (UC Davis) – data originally from IEA, 2017
Road freight demand is strongly correlated with income
Notes: Freight activity correlated with income (higher disposable incomes lead to higher demand for consumption, which leads to more freight activity)

## Slide 24
Slide courtesy of Pierpaolo Cazzola (UC Davis) – data originally from UNECE, 2012
Structural effect
Income effect
Car ownership per capita is partially explained by income
Notes: Higher income leads to higher propensity to own vehicles, but there are also structural effects that influence how many people own vehicles in a society. Can you think of what they might be?

## Slide 25
Structural effect
Income effect
Slide courtesy of Pierpaolo Cazzola (UC Davis) – data originally from IEA, 2008
Structural effects of public transport usage play more of a role
Notes: Wealth is also an explainer of public transport usage, but here structural effects play even more of a roll. For example, residents of Amsterdam and Phoenix are similarly wealthy in terms of GDP per capita, but the mode share of those cities is vastly different. Can you think what these structural effects could be that explain this difference?

## Slide 26: 5. Transport planning and policy
Objectives, methods and progress

## Slide 27: Transport as a (super) wicked problem…
Wicked problem
Unique with no standardised solutions
Persistent and insoluble with no definitive problem formulation
Symptomatic of deeper problems
Characterised by contradictions
Redistributive implications for entrenched interests
Super-wicked problem
Time is running out
Those seeking to end the problem are also causing it
No central authority
Policies discount the future irrationally
Rittel & Webber (1973), Rayner (2006) and Levin et al. (2012)
Notes: Before we talk about methods used in planning transport, let us first introduce transport as a super wicked problem. Firstly, a wicked problem is defined as something that is:
Unique with no standardised solutions (no one size fits all)
Persistent and insoluble with no definitive problem formulation (for ever changing problem and solution space)
Symptomatic of deeper problems (e.g. inequalities in access)
Characterised by contradictions (e.g. solving one problem may make another worse)
Redistributive implications for entrenched interests (policies may redistribute resources in a way that affects powerful groups, potentially leading to pushback or resistance)
A super wicked problem is all of this, but furthermore:
Time is running out
Those seeking to end the problem are also causing it
There is no central authority
Policies discount the future irrationally

## Slide 28: Transport planning & policy
Strategic goals set by government
Long-term strategies
Potential conflicts
Strategic goals elicited from stakeholders
Buy-in from the beginning
Lobbyists/opportunists may limit vision
Rodrigue, J. P. (2020). The Geography of Transport Systems (Fifth Edition). New York: Routledge.
Notes: Be that as it may, let us consider a framework by which we can understand general approaches in transport planning. This slide provides an overview of transport planning and policy, focusing on decision-making approaches and time horizons.
Decision-Making:
  Transport planning can follow a top-down, bottom-up, or hybrid approach.
  Governments set strategic goals, which can involve long-term strategies but may also create potential conflicts.
  Stakeholders play a key role in shaping policies, ensuring buy-in from the beginning, but lobbyists or opportunists may also influence or limit the vision.
Time Horizons in Transport Planning:
  Strategic (5–10 years): Focuses on implementing a vision and major infrastructure projects.
  Tactical (2–5 years): Involves business plans and specific activities to support strategic goals.
  Operational (less than 2 years): Deals with practical problems and managing mobile assets.

## Slide 29: Traditional (urban) transport planning
Transport planning since ~1940s has largely relied on mathematical modelling
  These tend to predict traffic growth in line with historical projections
  They ‘tell’ planners to provide more road space
= ‘predict and provide’
4 step transport demand model
Rodrigue, J. P. (2020). The Geography of Transport Systems (Fifth Edition). New York: Routledge.
Notes: Traditional urban transport planning has relied on mathematical models since the 1940s, primarily using a four-step demand model. These models predict future traffic growth based on historical trends and suggest expanding road capacity to accommodate demand. This approach, known as 'predict and provide,' assumes that increasing road space will solve congestion. However, as we have discussed, this often leads to induced demand, where more road capacity encourages more traffic.

## Slide 30: The problem
TUMI
Traditional transport planning forecasts a most likely mobility future
It tends to replicate and reinforce the status quo (build more roads for cars)
It fails to acknowledge that supply affects demand
Lyons, G. and Davidson, C. (2016). Guidance for transport planning and policymaking in the face of an uncertain future. Transportation Research Part A: Policy and Practice, 88, 104-116. http://dx.doi.org/10.1016/j.tra.2016.03.012
Notes: Traditional transport planning predicts a ‘most likely’ mobility future, often reinforcing existing trends by expanding road infrastructure for cars. This approach overlooks the fact that increasing road supply can induce more demand, leading to congestion rather than solving it. By failing to consider alternative transport solutions, it locks cities into car dependency instead of promoting more sustainable mobility options.

## Slide 31: Supply affects demand
Beyond serving society, transport infrastructure shapes society
What are the opportunities for social and economic activity in a digitally connected society?
What kind of transport system do we actually want?
People using transport infrastructure to access goods, services and activities: Paris (above); Los Angeles (below)
Notes: What do we mean by “supply affects demand”?
Transport infrastructure doesn’t just serve society—it actively shapes it. Expanding roads encourages more car use, while investing in other modes can shift mobility patterns. In a digitally connected world, we must ask: what opportunities for social and economic activity do we want to enable? Instead of defaulting to past trends, we should rethink and design a transport system that truly aligns with our future needs and aspirations. In these two pictures we see People using transport infrastructure to access goods, services and activities: Paris (above); Los Angeles (below).

## Slide 32: The Decide & Provide paradigm
Decide & Provide (D&P) aims to plan for the future in a vision-led planning approach using scenarios
D&P relies on input from all stakeholders to create those scenarios:
  What sort of place are we creating?
  What kind of activities do we need access to?
  How will we provide access to those activities (in terms of spatial proximity, physical mobility and digital connectivity)?
Importantly D&P still uses models and data to inform decisions! The key distinction between the two approaches is their purpose.
https://www.trics.org/decideandprovideguidance.html
Notes: The Decide & Provide (D&P) paradigm is an alternative framework to predict & provide (P&P). D&P takes a vision-led approach to transport planning, moving beyond predicting past trends. Instead of just forecasting traffic growth, it engages all stakeholders to shape future scenarios: What kind of places do we want? What activities need access? And how do we enable that access—through spatial design, mobility, and digital connectivity? This approach ensures planning is proactive, not just reactive.
However, can you think of the potential vulnerabilities of using this approach? For one, clearly it requires a fair representation of stakeholders in the scenario development.

## Slide 33: Decide & Provide case study: Cheonggyecheon, Seoul
Cheonggyecheon stream, Seoul
1960s  elevated expressway to relieve traffic through the city
2003  mayor proposed a project to demolish the highway and restore the stream, with pedestrian walkways
2025
  Air pollution (NO2) dropped 35%
  Designed to cope with floods (resilience)
  “Initially, everyone thought it would cause gridlock. But people adapted. Now we can’t imagine the highway ever being here” – local resident
Notes: Seoul’s Cheonggyecheon stream illustrates the Decide & Provide approach in action. Originally covered by an elevated expressway in the 1960s to ease congestion, the city took a bold step in 2003 to remove the highway and restore the stream with pedestrian-friendly spaces. Despite initial fears of gridlock, people adapted. By 2025, air pollution (NO₂) had dropped 35%, and the area became a model for resilience, even managing floods effectively. The transformation shows how proactive planning can reshape urban mobility for the better.

## Slide 34: Another outcome of contemporary transport planning: Superblocks, Barcelona
Eggimann, S. The potential of implementing superblocks for multifunctional street use in cities. Nat Sustain 5, 406–414 (2022)
Metropolis.org
Notes: Superblocks (or "superilles") are a key element of Barcelona's innovative urban mobility strategy. These are designated areas where several city blocks are closed off to through traffic, prioritizing pedestrians, cyclists, and public transport. The initiative aims to reduce air pollution, improve public space, and enhance quality of life by creating quieter, safer, and greener urban environments. Superblocks have been a significant outcome of Barcelona’s efforts to reimagine urban spaces for more sustainable and livable cities.

## Slide 35: Summary
In this lecture, we have explored mobility, accessibility and transport demand in the context of transport policy and planning.
In the next lecture, we will focus on how this demand translates to energy, and different options we have for decarbonising transport energy demand.
Questions – james.dixon@strath.ac.uk
Notes: In this lecture, we have explored mobility, accessibility and transport demand in the context of transport policy and planning.
In the next lecture, we will focus on how this demand translates to energy, and different options we have for solving it.

## Slide 36: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Dr James Dixon
University of Strathclyde
Glasgow, UK
e: james.dixon@strath.ac.uk