## Slide 1: Transport decarbonization and data-to-deal Lecture 3: Clean Transport Systems Energy and emissions considerations
Notes: Welcome to this lecture on clean transport systems, including considerations of energy and emissions of transport systems.

## Slide 2: Lecture 3: Learning Outcomes
By the end of this lecture, you will be able to:
Describe the Activity, Share, Intensity, (emissions) Factor (ASIF) framework of modelling transport energy demand
Describe the Avoid, Shift, Improve framework for transport decarbonisation
Describe the fundamentals of transport-energy modelling and discuss the fundamentals of optimisation models (using OSeMOSYS as an example)
Compare different options for transport decarbonisation pathways, including supply-side and demand-side interventions.
Notes: By the end of this lecture, you will be able to:
Describe the Activity, Share, Intensity, (emissions) Factor (ASIF) framework of modelling transport energy demand
Describe the Avoid, Shift, Improve framework for transport decarbonisation
Describe the fundamentals of transport-energy modelling and discuss the fundamentals of optimisation models (using OSeMOSYS as an example)
Compare different options for transport decarbonisation pathways, including supply-side and demand-side interventions, and be familiar with how these are used to build decarbonisation pathways

## Slide 3: 1. Transport: the emissions problem
Global emissions and transport climate mitigation

## Slide 4: Global transport emissions
Ritchie, H. and Roser, M. (2024). CO2 and greenhouse gas emissions. [Online]. Available: https://ourworldindata.org/co2-emissions-from-transport
Chart: Global emissions by sector Total = 49.4 GtCO2e
| Energy use in industry | Agriculture, forestry & land use | Energy use in buildings | Transport | Other energy | Industry | Waste
GtCO2e | 0.242 | 0.184 | 0.175 | 0.162 | 0.153 | 0.052 | 0.032
Chart: Global transport emissions by mode Total = 8 GtCO2e
| Road, passenger | Road, freight | Aviation, passenger | Aviation, freight | Shipping | Rail | Other
GtCO2 | 3.608 | 2.352 | 0.75168 | 0.17632 | 0.848 | 0.08 | 0.176
Notes: Global transport emissions are significant: In 2023, transport contributed 16% of global emissions. When we explore that as an individual pie chart on the right, three quarters are from road transport. Passenger road vehicles in themselves are the biggest cause, constituting 45% of transport sector emissions.

## Slide 5: There is significant disparity in per-capita emissions, mostly driven by wealth
Chart: Population share by country income status
| Low | Lower-middle | Upper-middle | High
 | 0.703 | 3.19 | 2.78 | 1.24
Chart: Transport sector emissions by country income status
| Low | Lower-middle | Upper-middle | High
 | 0.0611 | 0.967 | 1.97 | 3.12
Notes: Predictably, this is not shared equitably round the globe. Whilst only 16% of the global population live in high income countries, they are responsible for 51% of transport emissions. Low and lower-middle income countries constitute nearly half (49%) of the global population, but are responsible for only 17% of global transport emissions. This frames a lot of the discussion around ‘decarbonisation’ in transport. Put simply, many countries around the world never ‘carbonised’ to begin with. The issue then becomes more around the delivery of transport sector pathways that will reduce the impacts of damaging and increasingly expensive fossil-fuel technologies in the future.

## Slide 6: Countries who contribute most emissions generally suffer least from climate change
Our World in Data - https://ourworldindata.org/grapher/co2-emissions-transport?time=2019
Notre Dame Global Adaptation Initiative - https://gain.nd.edu/our-work/country-index/
Notes: Aside from low and lower middle income countries not having a large share of responsibility for climate change, they are generally speaking not the ones who will suffer the most from its outcomes. The map on the right shows the Notre Dame institute GAIN index, which scores how vulnerable a country is to climate change. There is a direct negative correlation between the emissions produced and the vulnerability suffered (the most vulnerable countries are often the least responsible).

## Slide 7: Climate mitigation policy – how’s it going?
Notes: How is climate mitigation policy going? I recommend checking out the climate action tracker online, that highlights countries’ commitments in climate change. This is based on NDC submissions, in which clearly there are no countries shown as being compatible with the 1.5C target. Many countries, including Russia and Mexico are ‘critically insufficient’.

## Slide 8: Revision: Avoid  Shift  Improve
Creutzig, F., Roy, J., Lamb, W.F. et al. Towards demand-side solutions for mitigating climate change. Nature Clim Change 8, 260–263 (2018). https://doi.org/10.1038/s41558-018-0121-1
Notes: In lecture 1 we established the Avoid Shift Improve (ASI) hierarchy of environmental sustainability in transport. It is used as a way of categorising interventions. ASI was developed as a framework for sustainable transportation and urban mobility planning. It aims to reduce environmental impacts, improve efficiency, and enhance accessibility by focusing on three key strategies:
Avoid (Reduce the need for travel): Encourages urban planning, digitalization, and policies that minimize the necessity for long-distance travel or frequent trips. Examples: Mixed-use development, remote work, e-commerce, and telemedicine.
Shift (Promote sustainable modes of transport): Focuses on moving people and goods towards more sustainable transportation options like public transit, cycling, and walking. Examples: Expanding metro and bus networks, building pedestrian-friendly infrastructure, and implementing bike-sharing programs.
Improve (Enhance efficiency and sustainability):Aims to make existing transport systems cleaner and more efficient through technological and operational advancements. Examples: Electrification of vehicles, fuel efficiency improvements, smart traffic management, and better logistics.

## Slide 9: Transport and Nationally Determined Contributions (NDCs)
UNFCCC NDC Registry. https://unfccc.int/NDCREG
SLOCAT, 2021. Transport in NDCs. https://slocat.net/ndcs
166 NDCs (up to COP26, Nov 2021)
76% highlight transport as a source of mitigation
8% have transport-specific mitigation targets
Of transport-specific mitigation targets, the majority are based on improve measures. Only 7% based on avoid and 28% based on shift
Notes: Transport is represented in Nationally Determined Contributions (NDCs) to the Paris Agreement as a key sector for reducing greenhouse gas (GHG) emissions and achieving climate goals under the Paris Agreement. Since transport is a major source of CO₂ emissions, it is very important that transport is included in NDCs. However, as of the submission of 1st NDCs (COP26), whilst 76% of the NDCs highlight transport as a source of mitigation, only 8% have transport-specific mitigation targets. Of those transport-specific mitigation targets, the majority are based on improve measures. Only 7% based on avoid and 28% based on shift.

## Slide 10: 2. Transport-energy modelling
Key concepts

## Slide 11: Building low-carbon transport energy pathways
Pathways are used to explore the range of plausible outcomes
Including:
  Techno-economic scenarios
  Socio-economic scenarios
  Policy decisions
There are generally many routes to a desired outcome – but who gets to decide which one we take?
Notes: Pathways are tools used to explore a range of possible futures by considering various scenarios. These include:
Techno-economic scenarios: Assessing the impact of technology and economic trends.
Socio-economic scenarios: Understanding the social and economic implications of different paths.
Policy decisions: Evaluating how political choices influence outcomes.
There are typically many routes to achieve a desired outcome, but a key question remains: who gets to decide which pathway we follow?

## Slide 12: Energy for transport
People don’t consume energy for the sake of it
  Rather, they do so to satisfy demand for energy services (Schipper & Marie-Lilliu, 1999)
E = total GHG emissions of transport
A = total vehicle activity (expressed in vehicle-km, vkm)
Si = sectoral structure (share of vkm, at an arbitrary level of detail –service, modes, vehicle class, powertrain)
Ii = energy intensity of sector i (average energy consumption for that service)
Fij = emissions factor of energy carrier j for sector i
Three people consuming energy services
The ASIF framework (Schipper et al., 2000) provides a way of linking services to emissions
Image: Sustrans
Notes: In past lectures we have discussed drivers of transport demand, and how transport is a derived demand – derived from human activities associated with accessing stuff: goods, services and activities. At a wider level, people don’t consume energy for the sake of it. They do so to satisfy demand for energy services. This framing results in the equation on the top left, which was developed by Lee Schipper at the turn of the millennium. The ASIF framework (not to be confused with the ASI hierarchy!) provides a way of linking transport service demand to emissions. In the equation,
E = total GHG emissions of transport
A = total vehicle activity (expressed in vehicle-km, vkm)
Si = sectoral structure (share of vkm, at an arbitrary level of detail –service, modes, vehicle class, powertrain)
Ii = energy intensity of sector i (average energy consumption for that service)
Fij = emissions factor of energy carrier j for sector i

## Slide 13: A taxonomy of models
Transport-energy models can be distinguished along three main axes (Krey, 2014):
  the mathematical solution concepts (e.g., whether optimisation or simulation, partial or general equilibrium);
  the system boundaries (e.g., whether sectoral or temporal);
  the level of detail (e.g., technology, spatial resolution).
The first bit of a (non-exhaustive) list of energy models (LEAP)
The 4th axis?
The audience!
Notes: Transport-energy models can be distinguished along three main axes (Krey, 2014):
  the mathematical solution concepts (e.g., whether optimisation or simulation, partial or general equilibrium);
  the system boundaries (e.g., whether sectoral or temporal);
  the level of detail (e.g., technology, spatial resolution).
A fourth axis that I consider useful is the audience: is this for other academics, or is it for influencing policy?

## Slide 14: OSeMOSYS
“Open Source Energy Modelling System”
Based on an optimisation framework, the model:
  Returns the least-cost set of technologies to supply energy service demand in a given year
  Represents every end-use sector, including transport
http://www.osemosys.org/
Howells, M. et al. (2011). OSeMOSYS: The Open Source Energy Modeling System: An introduction to its ethos, structure and development. Energy Policy.
Notes: The modelling framework you will be using to develop a transport-energy model later in the course is OSeMOSYS, which stands for the Open Source Energy Modelling System.
Based on an optimisation framework, the model:
  Returns the least-cost set of technologies to supply energy service demand in a given year
  Represents every end-use sector, including transport

## Slide 15: Optimisation models
Optimisation models (like OSeMOSYS) identify least-cost resources and technology deployment pathways towards a desired set of outcomes (e.g. net-zero emissions by year Y)
Demand-side and supply-side interventions are modelled by including constraints or changing technology costs
Minimise an objective function, usually the total financial cost of the system
Constraints bound the solution space (e.g. ‘supply must equal demand’, ‘emissions must be equal to zero by 2050’, ‘50% of new cars by 2030 must be battery electric’, …)
Notes: Optimisation models (like OSeMOSYS) identify least-cost resources and technology deployment pathways towards a desired set of outcomes (e.g. net-zero emissions by year Y)
Demand-side and supply-side interventions are modelled by including constraints or changing technology costs
Mathematically, they are represented by an objective function to be minimised, which is usually the total cost of the system. That is constrained to make the solution make sense in the context of whatever scenario is being developed – e.g. ‘supply must equal demand’, ‘emissions must be equal to zero by 2050’, ‘50% of new cars by 2030 must be battery electric’

## Slide 16: Decarbonisation: what are our options?
Flexing the I (energy intensity) and the F (emissions factor):
-Technologies
-Fuel switching
Flexing the A (activity) and the S (mode share):
-Planning reform
-Public transport
-Active travel
Notes: So, revisiting the ASIF framework: what are our options for transport decarbonisation?
We can flex the A (activity) and the S (mode share), which includes planning reform, public transport and active travel (Avoid and Shift)
Or we can flex the I (energy intensity) and F (emissions factor), which includes technologies and fuel switching (Improve).

## Slide 17: 3. Supply-side options for transport decarbonisation
Flexing the I and the F

## Slide 18: Vehicle powertrain decarbonisation: electrification vs. low carbon liquid fuels
Or we could:
Upscale renewable generation
Manufacture low carbon fuels from carbon (captured from the air) and hydrogen (produced from electrolysis)…
…and we wouldn’t have to change any of our infrastructure! So why don’t we do this? (Next slide)
We could:
Upscale renewable generation
Charge batteries, and use those batteries to power motors in electric vehicles
India Times (2019). https://bit.ly/365QXWJ
…but this requires the shift of transport energy demand from the petrochemical system to the electrical system
Notes: First let us consider flexing the I and the F by fuel switching. Let’s take the case of vehicle powertrain decarbonisation, which has two main options: battery electrification or the use of low carbon liquid fuels.
For the first option, we could:
Upscale renewable generation
Charge batteries, and use those batteries to power motors in electric vehicles… but this requires the shift of transport energy demand from the petrochemical system to the electrical system
Alternatively, we could
upscale renewable generation
Manufacture low carbon fuels from carbon (captured from the air) and hydrogen (produced from electrolysis… and we wouldn’t have to change any of our infrastructure!
So why don’t we do this?

## Slide 19
LOSSES
~20%
MOTION
~80%
~10%
LOSSES
ELECTRICITY
RENEWABLE ELECTRICITY
100 TWh energy (renewable electricity)
Battery, motor & transmission
ELECTROLYSIS
Water
DIRECT AIR CAPTURE
Air
Fischer- Tropsch
Refining/cracking
LOSSES1
~55%
Synfuel (CxHx)
45 TWh of energy (low carbon fuel)
CO2
IC engine & transmission
LOSSES
~80%
~20%
MOTION
Water
100 TWh energy (renewable electricity)
RENEWABLE ELECTRICITY
(Reverse) Water Gas Shift
H2
~72% (overall)
1 Hanggi et al. (2019) A review of synthetic fuels for passenger vehicles. Energy Reports, vol. 5.
~9% (overall)
1) ELECTRIFICATION
2) SYNTHETIC FUELS
x 8
Notes: It all comes down to thermodynamics. Let’s explore these options in comparison.
Firstly let’s run through the electrification route. Let’s say we start with some renewable electricity produced from solar or wind electricity, and we can consider this our primary energy source. Let’s say we have 100 TWh of energy as renewable electricity. If we put that through a power system, we may lose approximately 10% between the generator, transmitting long distances, stepping down to a plug socket in a home. Then using that electricity in a battery, motor and transmission of an electric vehicle (say, a car or a bus) will result in a further 20% of losses (mostly as heat and noise). In other words, we keep 80% of the energy as motion. That means from our original 100 units of renewable electricity, we get to keep 72% of them.
Now let’s run through the synthetic fuels route. Say we have the same original 100 units of renewable electricity. We can use that energy to power electrolysis and direct air capture processes to harvest hydrogen and carbon dioxide. We can combine these to create a synthetic hydrocarbon fuel – as on the last slide, something that could be chemically identical to gasoline. In those processes, we’ve lost around 55% of our original energy, so out of our 100 units we have 45 left as synthetic fuel. Now we run that through an internal combustion engine and transmission, and we lose the vast majority of it (around 80%). 20% gets carried through as motion, and as it’s 20% of our 45 TWh, we’re left with 9% of our original energy from the renewable electricity we had to start with.
Clearly, the thermodynamics of electrification look to be superior.

## Slide 20: Energy for EVs
278 billion vehicle miles
Department for Transport, Road Traffic Estimates: Great Britain [Online]. Available: https://bit.ly/3724per
Department for Transport, Energy consumption by transport mode and source of energy: United Kingdom.
US Department of Energy, “Fuel Properties Comparison.” https://goo.gl/eU1bvK
Private cars, per year – UK
~25 million tonnes petroleum
~300 TWh energy
~0.3 kWh/mile
~80 TWh energy
Notes: Consider this another way. If we take service demand for transport as our starting point. Using the UK as an example, we have a transport demand of 278 billion vehicle miles per year in private cars. If we look at the energy consumption statistics, that uses around 25 million tonnes of petroleum, or 300 TWh of energy. However, if we were to take the same energy service demand and consider a typical efficiency of a battery electric car of approx. 0.3 kWh/mile, then the energy we would need to supply that demand is 80 TWh of electrical energy. Of course, we must consider upstream processes required to produce that 80 TWh of electricity, and indeed upstream processes to produce 300 TWh of energy from petroleum.
In summary, it is widely recognised that the thermodynamics of electrification are far superior. But what’s the catch?

## Slide 21: So why not electrify everything?
Batteries are far less energy dense than hydrocarbon fuels! – not feasible for sectors like mid/long-haul aviation and shipping
“Even assuming huge advances in battery technology, with batteries that are 30 times more efficient and ‘energy-dense’ than they are today, it would only be possible to fly an A320 airliner for a fifth of its range with just half of its payload” – Grazia Vittadini (CTO, Airbus)
https://www.bbc.co.uk/news/business-48630656
Royal Society, “Sustainable synthetic carbon-based fuels”
Notes: Why not electrify everything?
Batteries are far less energy dense than hydrocarbon fuels! – not feasible for sectors like mid/long-haul aviation and shipping
“Even assuming huge advances in battery technology, with batteries that are 30 times more efficient and ‘energy-dense’ than they are today, it would only be possible to fly an A320 airliner for a fifth of its range with just half of its payload” – Grazia Vittadini (CTO, Airbus)
The chart on the right shows the energy density per unit mass and volume of lithium batteries (bottom left corner) and traditional hydrocarbon fuels including petrol (gasoline), diesel, etc. at the top right.

## Slide 22: Biofuels
Biofuels are combustible fuels derived from biological material in waste or crops
(Soon to be) waste cooking oil
Miscanthus (a high-yield energy crop)
Chart: Miles travelled
| Car, first gen. biofuels | Car, second gen. biofuels | Solar PV + EV | Solar PV + E-bike
 | 1 | 5 | 1081 | 21243
Car and bike miles travelled on 1 m2 of land covered in biofuels or solar panels
“The wheat required to meet today’s global aviation demand equates to almost as much as the planet’s total human calorie requirement”
M. Berners-Lee, There is no Planet B: A Handbook for the Make or Break Years. Cambridge University Press, 2019.
Notes: Biofuels are one alternative to consider. Biofuels are combustible fuels derived from biological material in waste or crops, which could include energy crops like Miscanthus or waste cooking oil.
Biofuels can meet some demand for transport. However, from a thermodynamic point of view, they are clearly not as good as battery electrification. The top right chart show the car and bike miles that could be travelled using 1 square metre of land covered in biofuels or solar panels. First generation biofuel (e.g. ethanol made from corn) from that land can power a car for 1 mile; second generation (e.g. cellulosic ethanol made from miscanthus) biofuels could power one for 5 miles, but covering that same land in a solar PV cell and using the electricity to power a battery would provide over 1000 miles. If we instead did the same for an electric bike, we could get over 21,000 miles.
Therefore, the role of biofuels needs to be judged carefully: clearly, a lot of land is required to produce energy on the scale we require. We also need that land for other purposes like food production.
“The wheat required to meet today’s global aviation demand equates to almost as much as the planet’s total human calorie requirement”

## Slide 23: Hydrogen for aviation
Hydrogen is ~3 times more energy dense than jet fuel by mass
But ~4 times less energy dense than jet fuel by volume
Figures: Finlay Asher (Green Sky Thinking); Airbus; Royal Society, “Sustainable synthetic carbon-based fuels”
Notes: Hydrogen is another alternative. Often times this is discussed as a potential low-carbon liquid fuel for aviation. At first glance, it looks pretty good: hydrogen is 3 times more energy dense than jet fuel per unit mass. However, it is 4 times less energy dense than jet fuel by unit volume. This means that either you need larger aircraft, which increase drag at a given speed, or the same size aircraft but reduced number of passengers, or you completely redesign the aircraft to accompany for these different requirements.
Hydrogen storage tanks, especially those for liquid hydrogen, are heavy and bulky. This adds weight to aircraft, reducing fuel efficiency and increasing the complexity of aircraft design and operation.

## Slide 24: Hydrogen-derived fuels for ships, planes…
Hydrogen and nitrogen (from the air) can be combined to form ammonia (NH3)
  This is already common practice for fertiliser production!
Ammonia is around 50% more energy dense per unit volume than hydrogen and easier to liquefy – so it’s more suitable for some transport applications
Ammonia can be burned or used in a fuel cell to generate electricity
But it carries a significant energy penalty for making it!
Hydrogen can be combined with carbon (from biomass or captured from the air) to produce synthetic hydrocarbons (CXHX)
The appeal is that they can be burned in the same engines as fossil fuels and they don’t have the same scaling limitations as biofuels
So what’s the catch?
https://royalsociety.org/topics-policy/projects/low-carbon-energy-programme/sustainable-synthetic-carbon-based-fuels-for-transport/
ICAO cost projections for synthetic fuels
Notes: Hydrogen and nitrogen (from the air) can be combined to form ammonia (NH3)
  This is already common practice for fertiliser production!
Ammonia is around 50% more energy dense per unit volume than hydrogen and easier to liquefy – so it’s more suitable for some transport applications
Ammonia can be burned or used in a fuel cell to generate electricity
But it carries a significant energy penalty for making it!

## Slide 25: 4. Demand-side options for transport decarbonisation
Flexing the A and the S

## Slide 26: Planning and x-minute neighbourhoods
X-minute neighbourhoods (where X = 15, 20, 30, …) are designed such that residents’ daily needs are met within an X-minute walk or cycle from their home
Designing x-minute neighbourhoods reduces travel demand, making it easier to meet decarbonisation targets
https://www.tsu.ox.ac.uk/news/x-minute-city-improving-quality-life-across-whole-urban-area
Notes: Reforming planning has significant potential for reducing travel demand and promoting use of lower-energy intensity means of transport.
X-minute neighbourhoods focus on designing urban spaces where residents can access essential services (e.g., work, education, shopping, healthcare) within a short walk or bike ride—typically under 15 minutes. This planning concept aims to reduce travel demand by promoting local living, minimizing reliance on cars, and enhancing sustainability. By prioritizing mixed-use development, pedestrian-friendly infrastructure, and public transport, X-minute neighbourhoods contribute to better quality of life, lower traffic congestion, and reduced carbon emissions.

## Slide 27: Modal shift
Promoting the use of energy-efficient modes of transport (bus, train, bike, etc.) over private car use reduces the energy demanded by the transport system
This can be done by incentivising these modes and/or disincentivising car travel
Mobility-as-a-service can reduce asset (car) ownership, reducing car reliance and promoting use of other modes
Notes: Encouraging modal shift involves promoting the use of more sustainable transport options, such as walking, cycling, and public transit, over private car use. This can be achieved through policies and infrastructure improvements that make alternatives more accessible, affordable, and convenient. By investing in bike lanes, public transport networks, and pedestrian-friendly streets, cities can reduce congestion, lower emissions, and improve public health. A successful modal shift not only contributes to sustainability but also fosters more vibrant, livable urban environments

## Slide 28: Mobility as a Service
Incentives to use non-car modes don’t have to be purely financial
Streamlined services reduce ‘friction’ of their use and increase their attractiveness
Mobility as a Service (MaaS): users can access multiple modes from one integrated service provider (e.g. a smartphone app)
https://futuremobilityfinland.fi/vision/mobility-as-a-service/
Notes: Mobility as a Service (MaaS) is a concept that integrates various transportation options (e.g., buses, trains, bikes, car-sharing) into a single accessible and customer-friendly service. Through MaaS platforms, users can plan, book, and pay for multi-modal journeys via one app, offering greater convenience and flexibility. MaaS aims to reduce the reliance on private cars, improve transport efficiency, and make urban mobility more sustainable. By offering seamless connectivity and personalized travel options, MaaS can help reduce traffic congestion, lower emissions, and enhance overall mobility.

## Slide 29: Revision: Avoid  Shift  Improve
Creutzig, F., Roy, J., Lamb, W.F. et al. Towards demand-side solutions for mitigating climate change. Nature Clim Change 8, 260–263 (2018). https://doi.org/10.1038/s41558-018-0121-1
Notes: You’ve seen this many times by now – this is the Avoid-Shift-Improve (ASI) hierarchy. This is a framework for creating more sustainable transport systems by focusing on three key strategies: Avoiding the need to travel, Shifting to more sustainable modes, and Improving the energy efficiency of end use technologies. The key point is that we can place all the interventions we’ve discussed in this lecture in one of the parts of this hierarchy.

## Slide 30: 5. Emissions scoping and building pathways
Emissions scoping; life cycle assessment; a case study of decarbonisation pathways (UK)

## Slide 31: Scope
Well-to-tank
Production
Manufacturing
Raw materials processing
Tank-to-wheel
End-of-life
(+maintenance)
Well-to-wheel
Life Cycle Assessment (LCA)
Conversion of stored energy to motion
Recycling
Disposal
Fuel extraction
Fuel processing
Electricity generation
Notes: Emissions scoping is important: it involves understanding and measuring the full range of emissions associated with a transport system. In this case we are considering road vehicles, for which we would need to consider vehicle use fomr production to end-of-life. This includes:
Tank to wheel, which includes the conversion of the stored energy on the vehicle to motion (e.g. burning gasoline)
Well to tank, which includes fuel extraction, fuel processing or electricity generation. Together, tank to wheel and well to tank are grouped as well to wheel.
There are then production emissions, end of life emissions and maintenance.
All of this is accounted for in an LCA: life cycle assessment.

## Slide 32: Why scope matters – low emission vehicles
Using direct emissions (TTW), EVs are zero-emission
Fuel cycle, batteries & manufacturing must be accounted for too
On average EVs give ~50-70% reduction in lifecycle emissions
  But what about the remaining 30-50%??
D. Kay, N. Hill, D. Newman. Powering Ahead: The Future of Low-Carbon Cars and Fuels Ricardo-AEA for the RAC Foundation and UKPIA, London (2013)
Carbon Brief, “Factcheck: How electric vehicles help to tackle climate change,” 2019. [Online]. Available: https://bit.ly/2UHWQ82.
Chart: gCO2e/km
| Avg Euro Car (2019) | HEV (Toyota Prius Eco) | BEV, 40 kWh (Nissan Leaf) | BEV, 75 kWh (Tesla Model S)
Tailpipe | 165 | 99 | 0 | 0
Fuel cycle | 47 | 28 | 29 | 26
Other manufacturing | 46 | 38 | 38 | 38
Batteries | 0 | 3 | 27 | 50
50-70% reduction
Notes: Why does emissions scoping matter?
Using direct emissions (TTW), EVs are zero-emission
Fuel cycle, batteries & manufacturing must be accounted for too
On average EVs give ~50-70% reduction in lifecycle emissions
  But what about the remaining 30-50%??

## Slide 33: Summary
In this lecture, we have introduced transport-energy system modelling and laid out frameworks for the decarbonisation of transport.
In the next lecture, we will focus on the inequity of transport systems and how to pursue goals towards equitable access.
Questions – james.dixon@strath.ac.uk
Notes: In this lecture, we have introduced transport-energy system modelling and laid out frameworks for the decarbonisation of transport.
In the next lecture, we will focus on the inequity of transport systems and how to pursue goals towards equitable access.

## Slide 34: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Dr James Dixon
University of Strathclyde
Glasgow, UK
e: james.dixon@strath.ac.uk