## Slide 1
Energy system modelling using OSeMOSYS
LECTURE 4
KEY PARAMETERS in OSeMOSYS

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO 1: Learn the definitions of activity, capacity, capacity to activity unit in OSeMOSYS
ILO2: Learn the definition of capacity factors in OSeMOSYS and how it is used in the model
ILO3: Learn about the definitions of input activity ratios and output activity ratios in OSeMOSYS
ILO4: Learn about how demands are represented in OSeMOSYS
ILO5: Learn how demands are projected in OSeMOSYS
Notes: Welcome to Lecture 4 of this course. This lecture focuses on several important concepts including:

## Slide 3
4.1.1 Activity and Capacity
4.1 Key Parameters in OSeMOSYS
Capacity refers to the maximum output a technology can produce at any given time, usually measured in capacity units (e.g., GW, Mton/year, 1000 vehicles). It defines the installed size of a technology and limits the level of activity it can perform in each time slice.
Capacity
Activity refers to the amount of output produced by a technology in a given period, typically measured in energy service units (e.g., PJ, Mtons, passenger km). It represents how much a technology operates to meet demand and is central to calculating fuel use, emissions, and costs.
Activity
Notes: Activity refers to the amount of output produced by a technology in a given time period, typically measured in energy service units (e.g., PJ, Mtons, vehicle km). It represents how much a technology operates to meet demand and is central to calculating fuel use, emissions, and costs.
Capacity refers to the maximum output a technology can produce at any given time, usually measured in capacity units (e.g., GW, Mton/year, 1000 vehicles). It defines the installed size of a technology and limits the level of activity it can produce in each time slice.
In OSeMOSYS you can input data on activity and capacity to represent historical data or future real or hypothetical plans. The model additionally provides outputs on the activity and capacity of each technology annually, helping to support energy planning and investment strategies.

## Slide 4
4
4.1.2 Capacity & Activity for Power Plants - Example
(Taliotis et al. (2018), image, licensed under CC BY 4.0; made using images from: D Harris, image, CC BY SA 2.0; Zygimantus, image, CC BY SA 4.0; Party Pop, image, CC BY-SA 3.0)
4.1 Key Parameters in OSeMOSYS
Notes: Looking at our example of a coal power plant above, the diagram shows that the amount of coal that can be supplied to the power plant is 3500MWh per hour, and using this coal the power plant can produce 1000MWh of electricity per hour. The capacity of our coal power plant is therefore 1000MWh of electricity per hour, and the activity would be 1000MWh of electricity in one hour, 2000MWh of electricity in 2 hours, and so on. Nevertheless, there are often limits on the capacity and activity of power plants. For example, the capacity of coal power plants may be limited by budget constraints or the activity may be limited by the amount of coal available.

## Slide 5
The maximum amount of activity that one unit of capacity can produce in a year.
Capacity To Activity Unit
4.1.3 Capacity to Activity Unit
4.1 Key Parameters in OSeMOSYS
Notes: Capacity to activity unit is the maximum amount of activity 1 unit of capacity can produce in a year. For certain technologies the capacity to activity unit is set. For example, 1GW of capacity can only generate a maximum of 31.536 PJ of activity in a given year as shown in the equation above. Similarly, in industry for example if your capacity unit is Mt/year. Then you know that 1 unit of capacity will produce 1 Mt of activity in a year. The only case where things are a bit different is in the transport sector where you have a known activity (e.g. number of kilometre-metres travelled by cars) and a known capacity (e.g. total number of cars on the road) which means you would have to calculate the capacity to activity unit by dividing the activity by the capacity values.

## Slide 6
4.1.4 Capacity Factor – Part 1
4.1 Key Parameters in OSeMOSYS
Hydro power plant
0.00072 PJ
Capacity Factor (CF): Capacity available per each timeslice expressed as a fraction of the total installed capacity, with values ranging from 0 to 1.
Notes: An important parameter in the relationship between capacity and activity is the capacity factor. In OSeMOSYS, the capacity factor is the ratio of actual output of a technology to its maximum possible output over a specific time period. It reflects how much a technology is actually used compared to its full potential, accounting for availability, downtime, or resource variability (like the variability of the sun, wind, and water flow). The energy produced (activity) varies based on the capacity factor, as shown in the example.

## Slide 7
7
If a hydroelectric plant has an installed capacity of 240 MW, what level of activity can it provide in one day in MWh assuming CF equal to 0.55?
4.1.5 Capacity Factor – Part 2
4.1 Key Parameters in OSeMOSYS
Notes: In this example, the first step is to calculate the number of hours in one day. Since one day equals 24 hours, we then calculate the energy produced by multiplying the installed capacity of 240 MW by the 24-hour period and the capacity factor of 0.55. This provides us with the amount of energy production the hydroelectric plant can produce in one day, which is 3,168 MWh. If the capacity factor was 1 instead of 0.55 (the plant was able to run constantly throughout the day) then the energy production would be much higher at 5, 760 MWh. However, in reality there might not be a lot of water flow at a particular time of the day or there might be other constraints which result in the plant only being use for a little over half its full potential, resulting in a lower level of possible activity.

## Slide 8
4.1.6 Activity Ratios
4.1 Key Parameters in OSeMOSYS
Used to specify how much of an input is needed to support the Activity of a Technology. It specifies how many units of input are needed for each unit of activity.
Used to specify how much output is generated from the Activity of a Technology. It specifies how many units of output are produced for each unit of activity.
Output Activity Ratio
Input Activity Ratio
Notes: The InputActivityRatio is used to specify how much of an input is needed to support the Activity of a Technology. It specifies how many units of input are needed for each unit of activity.
As an example, consider a natural gas fired power station with a conversion efficiency of 50%. The input to the plant is natural gas and the Activity represents electricity generated. This means that for every unit of electricity generated, 2 units (1/50%) of natural gas are needed. Consequently, the InputActivityRatio should be set to 2 in this case. This parameter is time dependent and can vary from year to year.
The InputActivityRatio is specified for each technology/commodity combination. If a technology has 2 or more input commodities, then that technology would have a InputActivityRatio for each commodity that is needed.
The OutputActivityRatio is used to specify how much output is generated from the Activity of a Technology. It specifies how many units of output are produced for each unit of activity. This parameter is time dependent and can vary from year to year.
As an example, consider maize cultivation. The Activity of the maize cultivation could represent how much land is planted with maize (measured in hectares), while the output would be the number of tonnes of maize produced. If 1,000 hectares of maize cultivation yields 4,500 tonnes, then the ratio of output to activity is 4.5 (4,500/1,000). Consequently, the OutputActivityRatio should be set to 4.5 tonnes per hectare in this case.
The OutputActivityRatio is specified for each technology/commodity combination. If a technology has 2 or more output commodities, then it would have an OutputActivityRatio for each commodity.
It is important to note however, that typically if the input activity ratio has a specific value then the output activity ratio is 1 and vice versa. This helps normalize the activity and define it for 1 unit (e.g. how much input is needed for 1 unit of output or vice versa) making it easier to scale. For example, if you know that you need 1.389 PJ of biomass to produce 1 PJ of heat in a biomass heater then the input activity ratio is 1.389 and the output activity ratio is 1. This is typically how it is represented in the OSeMOSYS model.
Technologies can also have multiple input activity ratios and multiple output activity ratios as mentioned above. For example, industry plants typically need both electricity and heat to produce their product. Therefore, if you know 1.263 PJ of electricity and 6.113 PJ of heat are needed to produce 1 Mton of steel. Then your input activity ratio for electricity will be 1.263 and for heat will be 6.113 and your output activity ratio for steel will be 1. Another important example to note is the transmission technology input and output activity ratios. Transmission and distributions represent the transport of electricity and sometimes fuels from power plants to end-users. Transmission and distribution systems are never 100% efficient and there are typically always losses. This could be from heat losses, illegal wire tapping etc. Therefore, the output of the transmission technology is typically less than the input, so we model this by giving the technology an input activity ratio of 1 and an output activity ratio of 0.98 if it experiences 2% losses or 0.96 if it experiences 4% losses and so on. These examples are not exhaustive.

## Slide 9
4.1.7 Representing Efficiency in OSeMOSYS – Part 1
4.1 Key Parameters in OSeMOSYS
Notes: Although not applicable always (e.g. when modelling crops and land) – typically the relationship between the input and output activity ratios gives you the efficiency of a technology.
For example, a coal-fired power plant takes the input fuel of coal and produces the output fuel of electricity. It is important to remember that the efficiency of a power plant is equal to the Output Activity Ratio divided by the Input Activity Ratio. In OSeMOSYS it is typical to set the Output Activity Ratio to 1 and adjust the Input Activity Ratio accordingly. If the Output Activity Ratio is 1, the efficiency of a power plant is therefore equal to 1 divided by the Input Activity Ratio. One might argue that you could also set the Input Activity Ratio to 1 instead and then adjust the Output Activity Ratio to get the same efficiency. This would be correct from a fuel use point of view but it would destroy the capacity outputs of the model and the economics of that technology since the capacity of a technology in OSeMOSYS is typically determined based on the output activity ratio being set to 1.

## Slide 10
10
Let’s look at a coal power plant as an example. If the amount of electricity produced is 25 GJ, how much coal in GJ was utilized?
Coal power plant
10 GJ of coal
4 GJ of electricity
4.1.8 Representing Efficiency in OSeMOSYS – Part 2
4.1 Key Parameters in OSeMOSYS
Notes: In this example, we have data indicating that a coal power plant produces 4 GJ of electricity using 10 GJ of coal. To calculate the plant’s efficiency, we divide the output energy by the input energy, yielding a value of 0.4 or 40%. The input activity ratio is then computed as the inverse of the efficiency, which is 1 divided by 0.4, equaling 2.5. The output activity ratio remains 1.
This means that 2.5 GJ of coal is required to produce 1 GJ of electricity. To calculate the coal needed to produce 25 GJ of electricity, we use the input/output activity ratio, resulting in 62.5 GJ of coal.

## Slide 11
4.1.9 Input & Output Activity on MUIO
4.1 Key Parameters in OSeMOSYS
Notes: The input and outputs of technologies are set up in the configuration page of the OSeMOSYS interface (MUIO) under the technologies tab. The commodities you select in the Input Activity Ratio column are the commodities going into your technology (commodities the technology needs to function) and the commodities you select in the Output Activity Ratio column are the commodities going out of the technology (produced by the technology).

## Slide 12
12
12
Lecture 4.1References
Taliotis, Constantinos, Gardumi, Francesco, Shivakumar, Abhishek, Sridharan, Vignesh, Ramos, Eunice, Beltramo, Agnese, … Howells, Mark. (2018, December). Representing primary energy supply in OSeMOSYS. Zenodo. http://doi.org/10.5281/zenodo.4558799

## Slide 13
13
4.2.1 Introducing Technology Costs in OSeMOSYS
4.2 Costs
(Taliotis et al. (2018), image, licensed under CC BY 4.0)
In OSeMOSYS, costs are split into Capital Costs, Fixed Costs, and Variable Costs
Notes: As well as defining the performance of a technology, it is important to define its costs. Technologies can require initial investments, as well as have costs that occur annually. In OSeMOSYS technology costs are split into 3 categories: variable costs (occurring annually), fixed costs (occurring annually) and capital costs (initial costs of the technology). This diagram shows the units of each of these costs and some examples of what they represent - we will look at each cost in more detail in the following slides.
Another potential cost that isn’t mentioned above is emission costs. This isn’t typically applied unless a user wants to apply a cost penalty for each unit of emissions produced in the model.

## Slide 14
14
4.2.2 Capital Costs
4.2 Costs
(Pappis et al. (2019), image licensed under CC BY 4.0)
Notes: The Capital Cost represents the initial cost of buying the technology and is defined as a function of technology capacity, using the unit $/kW. This includes the costs of the initial investments for the technology up until the point where it can start running. For example, the capital cost for a power plant would typically include the costs of planning and design; parts, machinery and building; construction; and commissioning and certification. Capital costs for some technologies, for example renewable technologies like solar PV, are likely to change in the future as shown in this diagram, and so the capital cost is defined for each model year in OSeMOSYS.

## Slide 15
15
4.2.3 Fixed Costs
4.2 Costs
(Created using data from Pappis et al. (2019), report licensed under CC BY 4.0)
Notes: The Fixed Cost is an annual cost defined as a function of technology capacity per year, using the unit $/kW/yr. This includes regular costs associated with the technology every year. For example, the fixed cost for a power plant would typically include the costs of paying workers’ salaries; regular operations and maintenance; taxes and insurance. As for capital costs, fixed costs for some technologies may be expected to change in the future, and so the fixed cost is also defined for each model year in OSeMOSYS. This diagram shows the fixed costs for different power plant types used in the TEMBA energy modelling study for Africa.

## Slide 16
16
4.2.3 Variable Costs
4.2 Costs
(Pappis et al. (2019), image licensed under CC BY 4.0)
Notes: The Variable Cost is defined as a function of technology activity, using the unit $/GJ. This includes the costs only associated with the technology’s activity, namely costs only incurred when a technology produces its output fuel/commodity. For example, the variable cost for a power plant is largely the cost of the power plant’s input fuel, as well as the costs of any other consumables like chemicals that are needed for the power plant to operate. This means that wind, solar PV and hydropower technologies often have variable costs of 0 as they do not require any fuels. As we will see in the next part of this lecture, the variable cost for primary energy supply technologies is the price of the commodity/fuel being supplied. For example, a Coal Imports technology would have a variable cost equal to the price of imported coal in each year. This diagram shows example fuel cost projections, which could be used for the variable costs for primary energy supply technologies. As we can see in the diagram, variable costs, especially fuel prices, may also change over time and so are defined for each model year in OSeMOSYS.

## Slide 17
17
Lecture 4.2 References
Taliotis, Constantinos, Gardumi, Francesco, Shivakumar, Abhishek, Sridharan, Vignesh, Ramos, Eunice, Beltramo, Agnese, … Howells, Mark. (2018, December). Representing primary energy supply in OSeMOSYS. Zenodo. http://doi.org/10.5281/zenodo.4558799
Pappis, I., Howells, M., Sridharan, V., Usher, W., Shivakumar, A., Gardumi, F. and Ramos, E., Energy projections for African countries, Hidalgo Gonzalez, I., Medarac, H., Gonzalez Sanchez, M. and Kougias, I., editor(s), EUR 29904 EN, Publications Office of the European Union, Luxembourg, 2019, ISBN 978-92-76-12391-0, doi:10.2760/678700, JRC118432

## Slide 18
18
4.3.1 Parameters that Define Technologies
4.3 Parameters Defining Technologies
(Taliotis et al. (2018), image, licensed under CC BY 4.0)
Notes: There are three main groups of data that are used to define technologies. These include the input commodity, which refers to the fuel supply to the technology. Important data on the input commodity include its price, availability and impacts. For example, the greenhouse gas emissions associated with using the fuel. Secondly, we need data on the techno-economic and environmental characteristics of technologies. These include technology costs, efficiency, lifetime and availability. Finally, we need to define each technology’s output commodity, which is the commodity it produces. Important data on output commodities include their demand, energy content and impacts. All of these aspects can be incorporated using different parameters on OSeMOSYS.

## Slide 19
19
4.3.2 Considering Key Characteristics of Technologies
(Pappis et al. (2019), image licensed under CC BY 4.0)
4.3 Parameters Defining Technologies
Notes: There are several important technology characteristics that should be considered in capacity expansion planning. Models developed using OSeMOSYS have the capability to consider several of these characteristics, including:
Variation in the availability, efficiency and costs of a technology over both short and long timescales. For example, new technologies that have high costs now may be expected to become significantly cheaper in the future. This diagram, which presents capital cost projections for renewable energy technologies, shows that some technology costs are expected to fall in the future. These technologies may therefore become more important for cost-effectiveness in the future, so it is important that OSeMOSYS can consider time-variable cost data.
Models can also consider limits on production by technology and capacity constraints. For example, there is a limit to how much power can be generated by solar PV in a given country based on the intensity of the sunlight over the year. It is important that OSeMOSYS can consider this so that its results are aligned with reality.
Additionally, we can consider the emissions associated with technologies and limits that may be placed on them. For example, we may want to develop a model scenario to understand how the Carbon Dioxide emissions associated with a country’s energy system can be reduced to a certain level, so it is important that OSeMOSYS can consider the emissions associated with each technology and has the capability to impose limits on them.

## Slide 20
20
Lecture 4.3 References
Taliotis, Constantinos, Gardumi, Francesco, Shivakumar, Abhishek, Sridharan, Vignesh, Ramos, Eunice, Beltramo, Agnese, … Howells, Mark. (2018, December). Representing primary energy supply in OSeMOSYS. Zenodo. http://doi.org/10.5281/zenodo.4558799
Pappis, I., Howells, M., Sridharan, V., Usher, W., Shivakumar, A., Gardumi, F. and Ramos, E., Energy projections for African countries, Hidalgo Gonzalez, I., Medarac, H., Gonzalez Sanchez, M. and Kougias, I., editor(s), EUR 29904 EN, Publications Office of the European Union, Luxembourg, 2019, ISBN 978-92-76-12391-0, doi:10.2760/678700, JRC118432

## Slide 21
Exogenous Demand: Demands that are set by the modeller, that must be met and do not change because of the model. For example, cement production per year, railway demand per year, crop demand per year. Exogenous demands can have real historical demands in historic years and then projected demands in future years.
Endogenous Demand: Demands that are not manually set by the modeller but emerge based on interactions within the model. For example, the demand for electricity in the power sector isn’t entered directly; it arises from the electricity needs of sectors such as industry, transport, and buildings. Similarly, the demand for hydrogen and ammonia is typically not set by the modeller but is driven by the demand for fertilizers and the ratios of hydrogen and ammonia needed to produce fertilizers or the use of hydrogen in vehicles.
4.4.1 Types of Demands
4.4 Demands in OSeMOSYS
Notes: Demands are incredibly important in OSeMOSYS as they are the driver for optimisation. The model needs demands in order to have something to optimise for. E.g. If you have demand for buildings heating, the model’s objective is to choose the cheapest technologies to meet that demand while also obeying any constraints that have been applied. There are two different types of demands: exogenous and endogenous. Exogenous demand is demand that is input into the model while endogenous demand is a result of the model’s internal interactions (input and output activity ratios) and is not a demand set by the modeller.

## Slide 22
22
4.4 Demands in OSeMOSYS
4.4.2 Understanding the logic – Part 1
Notes: When defining a demand, it is important to identify:
The carrier or service which the demand arises for: e.g., electricity, passenger transportation, or cooking.
The sector the demand arises from: e.g., residential (urban and/or rural, off- or on-grid), industrial, or commercial.
The average variability of such demand within a year, which is typically expressed using average demand profiles, explained in more detail later in this lecture.
The current and expected future annual average demand.
It is hard to predict future demands, and there is naturally uncertainty in our predictions. This is one reason why we model different scenarios.

## Slide 23
23
4.4 Demands in OSeMOSYS
4.4.2 Understanding the logic – Part 2
Notes: Let’s think about what we would need to identify when defining an example demand. In this example, we will think about the electricity consumed in urban homes. So, what do we need to identify based on the previous slide?
The energy carrier which the demand arises for: in this case this is electricity.
The sector the demand arises from: in this case this is the residential sector, or the urban residential sector if we want to be more specific.
The average variability of the demand over the year: here we would look at daily and yearly electricity load profiles for a residential urban area, which will tell us how the demand varies daily and in different seasons. From what we have learnt, we might expect this residential demand to be higher in the evening, and the seasonal variation would depend on the country’s climate.
The current and expected annual demand: here we would look at an energy balance (covered in more detail later) to get data for the current and historical residential electricity demand. We could use these data, potentially combined with an estimate of population growth, to create a future projection for the demand too.

## Slide 24
24
4.4.4 Definitions
4.4 Demands in OSeMOSYS
Notes: There are several new parameters to introduce that are used to define final demands in OSeMOSYS:
Accumulated Annual Demand: This defines the total accumulated demand of a commodity that is constant throughout the year, for each modelled year.
Specified Annual Demand: This defines the total specified demand for each modelled year, linked to a specific ‘time of use’ during the year.
Specified Demand Profile: This defines the share of energy demand required in each time slice. For any demand that varies throughout the year it is crucial to use specified annual demand rather than accumulated annual demand because with accumulated annual demand the model could just choose to meet the entire demand in one time slice if it is cost-effective which would not be representative of how the demand needs to be met at specific amounts and specific times throughout the year.
It is important to note that one commodity demand cannot be defined using both Accumulated Annual Demand and Specified Annual Demand. Additionally, if a commodity demand is defined using Specified Annual Demand, data must also be entered for the Specified Demand Profile for that commodity demand because this describes how the demand entered to the ‘Specified Annual Demand’ is distributed throughout the year. Similarly, since accumulated demand means the model can literally satisfy it when it makes the most economic sense, you should only be use it when the allocation of that demand has zero effect on the economics of the entire system. For example, say you had an accumulated crop demand which would mean you’d also have an accumulated demand for agriculture motive power. The model can choose to fire up an electric sawmill in the night to balance out the load curve, which would be very unrealistic.
Additionally, always make sure you are entering demands in the correct units for OSeMOSYS, for several sectors the units are Petajoules (PJ), meaning we may need to change the units when taking demand data from other sources. For example, if we have an electricity demand profile in GWh, we would need to convert this to PJ, using a conversion factor of 1 GWh = 0.0036 PJ. Similarly, for industry we typically work in Million tonnes but you might have data in tonnes so you would have to change this.

## Slide 25
4.5.1 Example Specified Annual Demand
4.5 Demand Examples
Notes: The Specified Annual Demand parameter is used to indicate the amount of demand in each year of the model period. We usually source the data for this parameter from existing demand forecasts, which may be based on key determinants of demand such as expected population growth. If we source demand data from existing sources, we must remember to convert the data into the right units for use in OSeMOSYS.

## Slide 26
26
4.5.2 Variations in Daily Demand
4.5 Demand Examples
(Taliotis et al. 2018, image, licensed under CC BY 4.0)
Notes: In lecture 2, we learnt that demands vary on daily, weekly, and monthly timescales, mainly reflecting the schedule of consumers’ activities. In addition, this diagram also shows that demands vary by sector. We can see that the magnitude of demand varies by sector, with agricultural demand being significantly lower than residential and commercial demand in this example. In this example, this means that the commercial and residential sectors are consuming more electricity, perhaps because their activities are more energy intensive or on a larger scale. In addition, we see that the daily profile of demand varies by sector. For example, here, in the displayed graph, there is a clear evening peak in residential demand, while agricultural and industrial demands are quite consistent throughout the day. This is likely because agricultural and industrial machinery operates constantly, while energy use in homes peaks in the evening when consumers use more electricity for cooking, lighting, and appliances.
Demand can also vary seasonally because of crop cycles, holidays, or production cycles. Therefore, time variability of demands often needs to be considered.

## Slide 27
27
4.5.3 Example Specified Demand Profile for CLEWs
4.5 Demand Examples
Winter
Spring
Summer
Autumn
Night
Night
Night
Night
Night
Night
Night
Night
Day
Day
Day
Day
Notes: The Specified Annual Demand Profile parameter is used to indicate the proportion of the demand occurring in each time slice This chart shows an example specified demand profile for electricity in OSeMOSYS. There are 96 bars, 1 for each of the 96 time slices used in this OSeMOSYS model. In this example, we have four seasons (Winter, Spring, Summer, and Autumn), each represented by 24 time slices in OSeMOSYS, with 12 time slices for daytime and 12 time slices for nighttime. The Specified Demand Profile parameter is used to represent the proportion of demand occurring in each time slice. The specified demand profile values in each time slice must all add up to exactly 1.
From the chart we can see that the electricity demand in this example is highest in Winter Days, because the Winter Day time slices have the highest Specified Demand Profile values, while demand is lowest in Spring Nights. It is important to recognize that this is a simplification: in reality demand will vary within seasons and with each hour of the day. Our simplification means that we model one representative day of each season, and we assume equal demand within days and nights of those seasons. Although this is a simplification, it allows us to consider the variation in demand across seasons and day parts without having an incredibly complex model structure. Specified demand profiles can be unique such as the demand profile for electricity generation or the heating demand profile of a country. However, in most cases for modelling if country-specific data is not available we tend to keep the demand profile flat (e.g. in industry and transport sectors). Keeping a profile flat simply means making the demand profile exactly equal to the year split. This ensures that all the demand is not used up in one time slice but is distributed throughout the year, making it more realistic.

## Slide 28
4.5.4 Accumulated Annual Demand vs Specified Annual Demand
4.5 Demand Examples
We use the parameters Specified Annual Demand and Specified Annual Demand Profile when we want to consider the temporal variability of the demand within the year, e.g., electricity demand.
However, there are some demands that do not have specific temporal variability within the year. In this case, we use the parameter Accumulated Annual Demand, which allows us to specify the amount of demand for every model year, without specifying how that demand is spread throughout the year, e.g., passenger transport demand or cooking energy service.
Specified Annual Demand + Specified Annual Demand Profile
Accumulated Annual Demand
Do we need to consider demand variability within years?
Yes
No
Notes: We use the parameters Specified Annual Demand and Specified Annual Demand Profile when we want to consider the temporal variability of the demand within the year, e.g., electricity, cooking, and heating demand, since we know this varies relatively predictably across seasons and between day and night. However, there are some demands that do not have specific temporal variability within the year. In this case, we use the parameter Accumulated Annual Demand, which allows us to specify the amount of demand for every model year without specifying how that demand is spread throughout the year.

## Slide 29
29
(Olaniyan et al. (2018), image, licensed under CC BY 4.0)
4.5 Demand Examples
4.5.5 Importance of Sector-Specific Demands
Notes: The differences between sectors discussed in the previous slide mean it can sometimes be important to model demands separately by sector, so that our models can consider the specific characteristics of each demand.
Additionally, within each of these sectors, the energy demand varies over time and across different classes of consumers. For example, within the residential sector, demands may differ between rural and urban households, as shown on this diagram, or between grid-connected and off-grid areas. Energy planners must make sure that the energy demand is met at any point in time for all classes of consumers. Thus, the key characteristics of demands must be represented in energy models.

## Slide 30
Energy:
Endogenous Demand
Not set by the modeller
Buildings: Exogenous Demands
Specified Annual Demands
Specified Demand Profiles
Transport:
Exogenous Demands
Specified Annual Demands
Specified Demand Profiles
Industry:
Exogenous Demands
Specified Annual Demands
Specified Demand Profiles
Waste:
Exogenous Demands
Specified Annual Demands
Specified Demand Profiles
Agriculture:
Accumulated Annual Demands
Water:
Endogenous Demand Not set by the modeller
4.5 Demand Examples
4.5.6 Example Demands in Each Sector
Notes: This slide shows some examples of different sectors that you can model using OSeMOSYS. Other than the energy sector which has an endogenous demand for electricity, every other sub-sector has several specified demands. e.g. transport would have separate specified demands for aircrafts, cars, vans, buses, motorcycles, heavy trucks etc. Similarly, waste would have different demands for solid waste and liquid waste.
The demands for energy and fuels come from all sectors such as:
Buildings – for cooking, heating, cooling and appliances – units of activity typically in PJ
Transport – for cars, trucks and buses, aviation, shipping, and trains – units of activity typically in billion vehicle kilometres
Industry – for heating, iron and steel production, cement production, aluminum production, petrochemicals production, other chemicals production, fertilizers production and other industries – units of activity for heat is in PJ and for production quantities in Million tonnes (Mtons)
Agriculture – for tractors and machinery, processing and heating – units of activity in PJ
You may have noticed that demand units do not necessarily have to be energy units, for example, industry outputs can be the amount of product in Million tonnes and transport demands are typically in distance units such as Billion vehicle kilometres.

## Slide 31
31
4.6.1 Demands in Reference Energy Systems
4.6 Demands in Modelling
Notes: Demands are represented on the right-hand side of this simple Reference Energy System (RES), highlighted in green on this example RES.
As we can see in the diagram, there are several steps to get to the final demand split by sector. In this example there is:
The electricity from power plants, which represents the aggregated stream of electricity coming from all the power plants in the model;
Electricity after transmission, which accounts for the losses of the transmission lines;
Electricity for use or total electricity demand, which represents the electricity that arrives to final consumers after distribution.
Total demand can then be split by sector, for example in this RES we have the following demands:
  Industrial Electricity Demand
  Residential Electricity Demand
  Commercial Electricity Demand

## Slide 32
32
4.6.2 Sourcing Data for Energy Demands
4.6 Demands in Modelling
Providers of energy balance data and/or demand projections:
International Energy Agency [link]
International Renewable Energy Agency [link]
United Nations Statistics [link]
Asia-Pacific Economic Cooperation [link]
Notes: Demand data for use in models can come from several sources. Particularly useful sources include energy balances, Sankey diagrams, and sector-specific decarbonisation reports. Energy balances tell us the amount of each commodity that is used by a country or region in a given year, usually broken down by sector.

## Slide 33
33
4.7.1 Long-Term Variations in Demands
4.7 Demand Projections
Notes: One of the key challenges in energy planning is that these energy demands change over time, for example, owing to population growth or the creation of new industries. On this diagram, we can see historical variations in energy demands which are likely correlated to changes in society. For example, increases in energy demand likely reflect increased industrial activity. In planning, it is important that we think about how demands are likely to change in the future. This is often done using forecasts of demand, such as the future projections shown in this figure. To project demand you can either: - Use existing demand projections - Project base year and historical demands using drivers such as population growth rate and/or GDP growth rate - Calculate an average of how demands have changed historically and use this as a projection growth rate
This list is not exhaustive.

## Slide 34
4.8 Energy Supply Units
1 Petajoule (PJ) = 1000 Terajoules (TJ)
1 Petajoule (PJ) = 1,000,000 Gigajoules (GJ)
3.6 Petajoules (PJ) = 1 Terawatt hour (TWh)
0.0036 Petajoules (PJ) = 1 Gigawatt hour (GWh)
1 Giga-Watt (GW) = 1000 Mega-Watts (MW)
4.8.1 Reminder of Conversions
Notes: For anything energy related we typically use PJ in the MUIO for activity and GW for capacity, therefore it is important that you understand how to convert things into PJ and GW for model input. Therefore, please make a note of these conversions.

## Slide 35
35
4.9.1 The Need for A Reserve Margin
4.9 Reserve Margin in OSeMOSYS
(Taliotis et al. 2018, image, licensed under CC BY 4.0)
Notes: A reserve margin is the additional generation capacity required above the expected peak demand to ensure system reliability and account for uncertainties such as demand fluctuations or generator outages. The graph above shows several things:
1. The green line shows the capacity required to meet the demand projection – this could involve real demands in historical years and then projected demands in future years. It shows that in this example demand is increasing over time. 2. The blue line shows declining existing capacity – the country will have existing capacity for technologies that they have already invested in. Using the capacities and lifetimes of existing power plants, we can create a forecast of system capacity if there were no new capacity additions. This gives a gradually decreasing system capacity as power plants are retired. This will be covered more in the next lecture when we cover residual capacities.
3. The black line shows the demand for new capacities – it considers the existing declining system capacity and the required minimum capacity to meet demand. 3. The red line shows the capacity requirements for the future – notice how the capacity requirements are greater than the capacity needed to meet the demand projection (green line), this is to incorporate a reserve margin. By having slightly more capacity than needed a country can buffer power plant shutdowns, issues, and outages ensuring that there is still sufficient capacity to meet the demand.
Users can choose to incorporate a reserve margin to incorporate this and have a more reliable and secure energy system.

## Slide 36
Tool to create customized constraints. Flexible way to control and restrict OSeMOSYS models
Allows users to specify restrictions on relationships between variables.
Can be created for Activity, Total Capacity and New Capacity variables
Can be equalities or inequalities
Examples
Set minimum shares (i.e. replicate targets such renewable electricity, fuel blending,
Apply constraints on activity, new capacity or total capacity of group of technologies
Set reserve margin constraints
… and many more
4.9.2 Using UDCs
4.9 Reserve Margin in OSeMOSYS
Notes: This slide explains the use of User Defined Constraints (UDCs) in OSeMOSYS as a flexible tool for applying customized restrictions within energy models. UDCs allow users to define constraints on relationships between variables such as Activity, Total Capacity, and New Capacity, and can be formulated as either equalities or inequalities. They are particularly useful for setting system-specific conditions like minimum technology shares, fuel blending requirements, or capacity limits across technology groups. One important application of UDCs is for implementing reserve margin constraints, which are critical for ensuring system reliability. By using UDCs, modelers can enforce additional activity requirements above peak demand, helping to account for uncertainties such as fluctuations in demand or unexpected outages. This makes UDCs a valuable mechanism for incorporating realistic and policy-relevant conditions into OSeMOSYS models.

## Slide 37
37
4.9.3 UDC general equation
4.9 Reserve Margin in OSeMOSYS
In simple terms, UDCs have the following generation equation:
Notes: In simple terms UDCs have the following generation equation.
The sum for all technologies of the chosen variable multiplied by the mutiplier must be less than or equal to, or simply equal to, the UDC constant.
The summation symbol ( indicates that the expression in the parentheses (i.e. the multiplication of the two terms) is carried out for each technology () in the model, and then the resulting values are summed.
In simple terms UDCs have the following generation equation.
The sum for all technologies of the chosen variable multiplied by the mutiplier must be less than or equal to, or simply equal to, the UDC constant.
The summation symbol (∑▒) indicates that the expression in the parentheses (i.e. the multiplication of the two terms) is carried out for each technology (t) in the model, and then the resulting values are summed.

## Slide 38
38
4.9.4 UDC general equation
4.9 Reserve Margin in OSeMOSYS
To create and customise the UDC, the user chooses:
which variable the constraint applies to
New capacity,
Total capacity, or
Activity
whether the equation is an inequality () or an equality (=).
the value of the UDC constant
the value of the multiplier for each technology
Notes: The user can create as few or as many UDCs as they like. For each UDC created, the user must define the different elements of the UDC.
The user decides:
which variable the constraint applies to, i.e. either new capacity, total capacity, or activity;
the value of the multiplier for each technology in the model;
whether the equation is an inequality () or an equality (=);
and finally, the value of the UDC constant.
Multipliers and UDC constants are time-dependent, i.e. they are defined for each year of the model period.
The model results must abide by the resulting equation.
The user can create as few or as many UDCs as they like. For each UDC created, the user must define the different elements of the UDC.
The user decides:
which variable the constraint applies to, i.e. either new capacity, total capacity, or activity;
the value of the multiplier for each technology in the model;
whether the equation is an inequality (≤) or an equality (=);
and finally, the value of the UDC constant.
Multipliers and UDC constants are time-dependent, i.e. they are defined for each year of the model period.
The model results must abide by the resulting equation.
Let’s now look at some examples to better understand how the equation works in practice.

## Slide 39
39
4.9.5 Reserve Margin Representation Part 1
4.9 Reserve Margin in OSeMOSYS
Assuming a capacity factor of 1 for transmission technology, transmission capacity can serve as a proxy for the required total generation capacity.
Reorganizing to adhere to the standard format of UDC:
Notes: For the reserve margin, we need to determine a value in terms of capacity for total generation. In OSeMOSYS, this value is input through demand parameters (i.e., SpecifiedAnnualDemand and SpecifiedDemandProfile) in energy units, as previously studied. An alternative approach to link total generation with a capacity variable is through the transmission technology. Transmission is supplied by ELC001, representing electricity from power plants or total generation for our purposes.
However, to account for losses in the transmission stage, it is necessary to adjust the transmission capacity using the inverse of its efficiency. Note that we assume no installed overcapacity in transmission, as determined by the residual capacity, and the capacity factor for this technology is assumed to be 1.
The left side of the inequality therefore considers the product of transmission capacity, inverse of efficiency, and the planned reserve margin (expressed in decimal form). The right side of the inequality represents the contributions to the reserve margin from on-grid technologies, adjusted by their capacity credits. These contributions must be greater than the intended expected demand peak given by the reserve margin.
Finally, the inequality can be rewritten by moving the right-hand term to the left side, isolating a constant on the right-hand side. We will clarify the application of this concept with an example in the next slide.

## Slide 40
40
4.9.6 Reserve Margin Representation Part 2
4.9 Reserve Margin in OSeMOSYS
Let’s consider a scenario with a diesel power plant (PWRDSL), a solar power plant (PWRSOL), and a battery system (PWRBATT). The capacity credits are detailed in the accompanying table. Given a transmission technology (PWRTRN) efficiency of 95% and a reserve margin of 15%, the inequality would be as follows:
Technology | Capacity credit
Diesel PP | 90%
Solar PP | 9%
Battery system | 78%
Notes: In this illustrative example, we consider a basic system comprising a diesel power plant, a solar power plant, and a battery system. The technical parameters include a transmission efficiency of 95% and a reserve margin of 15%.
Using the equation described in the previous slide, we substitute the values accordingly. First, the transmission capacity, referred to as ‘PWRTRN Capacity,’ is multiplied by the inverse of the efficiency (1/0.95) and by the sum of 1 plus the reserve margin, which is 1 + 0.15. Note that all percentages are expressed in decimal form for these calculations.
Next, we compute the sum of the products of the capacities of the power plants and their respective capacity credits. The capacity credits may vary depending on the system, and the values provided here are indicative. Again, percentages are expressed in decimal form, and the naming conventions are summarized for each power plant.
During the hands-on exercise, we will practice building and incorporating these inequalities in MUIO.

## Slide 41
41
Lecture 4.9 References
1. Climate Compatible Growth. (2024). MUIO (Version v5.0.0). GitHub. https://github.com/ClimateCompatibleGrowth/MUIO

## Slide 42: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Fernando Plazas-Niño, Kane Alexander, Hannah Luscombe, Lucy Allington, Carla Cannone, Pooya Hoseinpoori, Alexander Kell, Adam Hawkes, Mark Howells