## Slide 1
Energy system modelling using OSeMOSYS
LECTURE 5
MODEL CALIBRATION

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO1: Understand the concept of model calibration.
ILO2: Learn the basic steps and parameters used to calibrate an OSeMOSYS model.

## Slide 3
5.1.1 What is model calibration about?
5.1 Introducing Model Calibration
Model calibration refers to the process of adjusting model parameters to ensure that outputs align with historical real-world data. The main thing to ensure is that you have at least calibrated the base year (first year in the model).
Chart: Final energy consumption 2021
| Biomass | Natural gas | Diesel | Gasoline | LPG | Electricity
Real data | 59 | 19 | 70 | 85 | 36 | 123
Model | 57 | 19 | 64 | 83 | 34 | 119
Chart: Primary energy production
| Biomass | Natural gas | Crude oil | Hydro | Solar | Wind
Real data | 59 | 19 | 241 | 89 | 23 | 11
Model | 58 | 20 | 239 | 87 | 25 | 9
Notes: Model calibration involves adjusting parameters to ensure that the model's outputs align with historical real-world data. In the case of OSeMOSYS, an optimization-based mathematical model, the goal is to produce an optimal solution rather than the most probable one. Calibration, in this context, focuses on replicating historical and realistic energy production and consumption patterns throughout the timeline. There are several aspects of the model that you can calibrate but the main one is ensuring the first year of your model matches the energy balance of that country for that year. You could alternatively calibrate the emissions of the model.
However, we typically calibrate energy production and capacity while conducting a sense-check on emissions, rather than primarily calibrating emissions. This is because emissions are a direct consequence of energy production and use, properly calibrating energy production and consumption should result in aligned emission levels. This is because fossil fuel combustion—and its associated emissions—is directly proportional to energy use.

## Slide 4
The main thing that modellers typically calibrate to is the input fuel use of each sub-sector.
However, you can also calibrate the output product of sectors if you have the data.
For example, if you have the amount of steel or aluminium produced as well as the fuel used in these sub-sectors you can calibrate the model for both.
Another potential thing to calibrate to is the emissions of each sub-sector. This is typically done by calculating an implied emissions intensity using annual total activity and total emissions data.
However, calibrating fuel use AND emissions can result in some problems….
5.1.2 What are you calibrating to?
5.1 Introducing Model Calibration
Notes: This slide elaborates on the concept of model calibration. Calibration typically involves aligning the model's behaviour with known historical data. Most commonly, this means adjusting the model so that input fuel use in each sub-sector matches historical records. However, calibration can also be applied to sub-sector outputs—such as the tons of steel or aluminium produced—if that data is available for the relevant years.
In many cases, particularly in the industry and transport sectors, the model can be calibrated using both input fuel use and output activity data to improve overall accuracy.
Additionally, calibration can include emissions data. In this approach, the model is aligned to match both fuel use and emissions by calculating an implied emissions intensity—that is, the amount of emissions released per unit of activity. To do this, you'll need annual data for both total activity and total emissions for the sector or area being modelled.
However, it's important to be cautious when calibrating to both fuel use and emissions. Consider a scenario where a country has underreported coal use, but a separate agency has overreported emissions from coal. This would result in an unrealistically high emissions intensity for coal. While this inconsistency might be acceptable if the goal is to preserve both the energy and emissions balances, it highlights the importance of cross-checking data sources.
Best practice is to first perform a bottom-up calculation—multiplying fuel use by the relevant IPCC emissions factors—then compare those results with the national emissions inventory. Depending on the level of discrepancy, you can then adjust your approach accordingly.

## Slide 5
5.2 Using an Energy Balance
5.2.1 How to calibrate using the Energy Balance
An essential resource often needed to calibrate energy use is the country’s energy balance.
Notes: The energy balance of a country is a comprehensive summary of all energy flows within its economy over a specific period, usually a year. It shows how energy is produced, imported, exported, transformed, and consumed across different sectors (e.g., industry, transport, households). The balance ensures that total energy inputs equal total outputs, accounting for losses and conversions—providing insights into energy dependency, efficiency, and sectoral demand.
Typically, you would need to find some energy balances to calibrate a model.

## Slide 6
Why is it important to calibrate the base year?
Ensures the model reflects real-world energy supply, demand, and performance.
Provides a reliable and realistic starting point using historical data.
Builds trust and credibility in the model’s results for stakeholders.
Improves accuracy of future energy projections and investment planning.
Identifies data gaps, errors, or inconsistencies early in the process.
Verifies technologies and system constraints function as expected in the model.
5.2.2 Calibrating the base year
5.2 Using an Energy Balance
Notes: Usually, we use the energy balance to calibrate the start year (base year) of the model.
There are several reasons for doing this. Calibrating your model:
Establishes a Realistic Starting Point The base year represents the most recent year with reliable data. Calibration ensures the model reflects actual historical energy supply, demand, and system performance. Without a good match to reality, future projections will be unreliable.
2. Builds Trust in the Model Calibration shows that the model can reproduce known outcomes. This increases confidence among stakeholders, especially decision-makers using the model for energy planning or policy development.
3. Improves Accuracy of Projections A well-calibrated model minimizes errors in cost assumptions, efficiencies, and capacities. This leads to more accurate simulations of future energy scenarios, emissions, and investment needs.
4. Helps Identify and Fix Data Issues The calibration process may reveal gaps, inconsistencies, or errors in input data. Catching these issues early ensures better quality throughout the modelling process.
5. Ensures Proper Functioning of Technologies and Constraints Calibration verifies that all modelled technologies operate as expected under real-world conditions. It also confirms that constraints such as capacity limits and fuel availability are set realistically.

## Slide 7
5.2 Using an Energy Balance
5.2.3 Example for Calibrating Using the Energy Balance
1. Convert to PJ: 1088 TJ/ 1000 = 1.088 PJ 2. Account for efficiency of technology: 1.088/1.266 = 0.859 PJ 3. Force this fuel use for the technology using lower and upper limits
Notes: Above is an example of how you would calibrate your model using an energy balance. In this example we are trying to calibrate the activity of an oil boiler for services heating. Using the energy balance, we note that the commercial and public services sector uses 1088 terajoules of oil. Let’s say the only technology using oil in the commercial sector are oil boilers. To calibrate the oil boiler to match the energy balance value in your base year (2021) you would first convert the energy balance value into petajoules since this is the unit we work with in OSeMOSYS. Next, you would divide this value by the efficiency (i.e. input activity ratio) of your services oil boiler technology to account for losses during the transformation of oil to heat. Lastly, you would force this calculated value in your model using a parameter called ‘Total Technology Annual Activity Lower Limit’. This parameter/constraint tells the model a clear lower restriction on the overall operation of a particular technology. It establishes a lower limit on the total activity within a year. Then, you want to set an upper bound, which would be 1% more than the lower limit value. This 1% is applied to give the model some wiggle room to avoid any issues when running the model. This upper bound is then applied to the ‘Total Technology Annual Activity Upper Limit’ parameter for the services oil boiler technology. This parameter tells the model there is a clear maximum restriction on the overall operation of a particular technology. It establishes an upper limit on the total activity within a year. Using these constraints forces the model to use the right amount of fuel for each technology in each sub-sector for the base year.

## Slide 8
5.2 Using an Energy Balance
5.2.4 Calculating Demand Using the Energy Balance
As described in the previous slide lower limits are calculated by dividing the energy balance values by the input activity ratios of the respective technologies.
The total housing heating demand for this year is then calculated by summing the lower limits of all the technologies.
Demand for HOU_HEAT = 46.158 + 90.360 + 312.889 + 0.426 = 449.834 PJ
Notes: If demand is not available through other sources, then it can be calculated using the calibrated lower limit values. Once you have calculated the calibrated lower limits for the relevant technologies that provide a particular service you can simply sum the lower limits to get the demand for that service. This is only one method to calculate the demand. As mentioned in the previous lecture, demands can also be taken from government reports, international databases etc.

## Slide 9
9
5.3.1 Residual capacity
5.3 Basics in Model Calibration
The existing installed capacity of a technology in the base year or historical years. It represents infrastructure that is already in place and available for use, without needing new investment.
Residual Capacity
There are two main categories of residual capacity:
Known vintage dates – this mainly applies to the power sector and occasionally large industrial facilities. It is based on actual data that you calculate a residual capacity profile for.
Unknown vintage dates – for everything else you would use model outputs to determine the residual capacity.
Notes: Residual Capacity refers to the existing installed capacity of a technology at the start of the model's time horizon, typically for the base year or historical years. It represents infrastructure that is already in place and available for use, without requiring new investment. In OSeMOSYS, this capacity is gradually declined in future years to reflect retirement or decommissioning of aging infrastructure. This gradual reduction ensures the model accurately captures the limited operational lifespan of existing assets and avoids overestimating available capacity in long-term projections. There are two main categories of residual capacity:
1. Known vintage dates: This applies mainly to the power sector (occasionally to large industrial facilities too). Based on actual data on commission dates, decommission dates, and operational lives you can calculate the residual capacity profile (capacity declining over time). For example, in the power sector, where individual power plants can be identified and decommissioning schedules are often available, estimating future residual capacity is straightforward. If the current capacity of a plant type is 600 MW in 2026 and a 50 MW plant is decommissioned in 2027, the residual capacity for 2027 would be 600 - 50 = 550 MW.
2. For unknown vintage capacity and dates – if you don’t have real capacity data, a sensible approach is to run the model with no residual capacity data and then use the model output capacity value for the base year as a starting point for your residual capacity for that technology. Since most models are calibrated to activity it is difficult to determine capacity without running the model first because there are typically multiple timeslices and therefore you do not know the capacity factor for each technology. To expand on this, say you had 1 time-slice and for example, your gas boiler activity was 100PJ and the capacity factor was 0.8. You would simply do capacity=100/31.526/0.8. When you have multiple time-slices though, not only does the CF differ by time-slice but the demand also differs by time-slice. While it is theoretically possible to calculate the annual average capacity factor, this is not only hard but also insufficient as it’s the peak time slice that determines the capacity needs, not the average. Long story short, it’s quite complicated to determine the residual capacity without running the model. Once you’ve run the model and got a capacity value for your base year you can treat part of this capacity as residual – for example you might assume 90% of the model output capacity in the base year for that technology is residual. Then you would apply a linear decline over time based on the operational life of the technology. The reason it is important to include residual capacities for technologies even if you do not have access to known vintage dates is because in reality if a country’s energy balance says it uses a particular fuel in a sector that means it must have existing capacity for it. If you do not account for this existing residual capacity in the model then the model will invest in a lot more capacity than is necessary in the base year, making it more unrealistic and expensive. Disclaimer: A linear decline over time is a rough approximation and can distort investment patterns since in reality historical capacity growth likely followed non-linear trends in response to growing demand rather than a linear decline. While imperfect, starting with a simple linear regression is a practical first step when detailed historical capacity data is unavailable.

## Slide 10
10
5.3.2 Residual capacity - Example
Projected
Historical
In the example below you have a capacity of 30 GW in the base year (2020) for a technology with a 5-year operational life and project residual capacity from 2020 onwards using a linear decline.
5.3 Basics in Model Calibration
Notes: The example above shows how you would calculate the residual capacity for future years by linearly decreasing the residual capacity in the base year (which is 2020 in this case) based on the operational life of the technology (which is 5 years in this example).

## Slide 11
11
5.3.3 Total Technology Annual Activity Lower Limit
Total minimum level of activity allowed for a technology in one year.
1)
2)
5.3 Basics in Model Calibration
Notes: As mentioned before calibration can be achieved through the Total Technology Annual Activity Lower Limit parameter. This parameter ensures that a technology produces at least a specified minimum amount of energy in a given year. For instance, if the biomass stove technology has a lower limit set to 20 PJ in 2023, the model will generate an activity where biomass stoves produce at least 20 PJ of cooking service in that year. While the technology may produce more than 20 PJ, the parameter guarantees a minimum production level without restricting maximum output. Typically, we use the ‘Total Technology Annual Activity Lower Limit’ parameter to calibrate only the base year using something like the energy balance, however, there are two common times this parameter is additionally used for calibration, this is:
To calibrate all historical years
To force technology use throughout the timeline
For calibrating all historical years:
If you get the economics right for your country, which is the eventual aim of any modelling exercise, you shouldn’t see abrupt early retirements of existing capacity. However, if there is no readily available data on economics for your country then there are situations where residual capacities can be entirely unused in the model because the model deems it more cost-effective to scrap existing capacity and invest in another technology. There can also be instances where a capacity is fully utilized in one year but abruptly becomes unused in the next year. These behaviours reflect the nature of OSeMOSYS as a cost optimization model. It aims to determine the least-cost solution for energy production and usage while neglecting certain practical realities of energy systems such as assuming a country would completely scrap existing capacity within one year. To avoid such unrealistic outcomes, we may need to calibrate energy production for each sector for historic years to match reality and build confidence in the model. Historical production data, such as electricity, heat, or other energy services, can be sourced from final energy balances or sector-specific reports for all historic years and not just the base year. Then the lower (and often upper limits) can be used to calibrate the historical years to ensure it matches reality. In example 1 of the slide above, only the historical years have been calibrated, and then future years are not.
For calibrating future years:
For certain technologies you may have to force activity throughout the timeline because technology use in the real-world is not based on economics but other factors such as convenience. This means the model wouldn’t choose to invest in this technology since it isn’t one of the most cost-effective options, but we know it will still be used due to societal behaviour. For example, resistive heaters are not the cheapest form of heating, but they are used in various places for numerous reasons such as a lack of heating infrastructure. It therefore makes sense to force a flat use of this technology throughout the modelling period, this can be seen in the slide Example 2 above.

## Slide 12
12
5.3.4 Total Annual Max Capacity Investment
Maximum new capacity allowed for a technology in one year.
The default value is 999,999, which represents no constraint on the new installed capacity for a technology.
By setting this parameter to zero during the calibration years, we deactivate technologies that are not part of the energy mix in the historical data.
Technology | Calibration years (known data) |  |  |  | Optimized modelling period |  |  |  | 
 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Coal power plant | 999999 | 999999 | 999999 | 999999 | 999999 | 999999 | 999999 | 999999 | 999999
Geothermal power plant | 0 | 0 | 0 | 0 | 999999 | 999999 | 999999 | 999999 | 999999
Example of how to parametrize a current technology in the mix (coal power plant) and a potential technology for the future (geothermal power plant)
5.3 Basics in Model Calibration
Notes: During the calibration years, we add all existing capacities and energy productions to replicate the expected historical behavior. At the same time, we ensure that technologies not included in the energy mix during those years are not installed.
To achieve this, we can use the parameter Total Annual Max Capacity Investment, which sets the maximum new capacity that can be installed for a technology per year. For example, if this parameter is set to 1 GW, the maximum new capacity installed in that year cannot exceed 1 GW. Setting the parameter to zero effectively deactivates any new capacity for that technology.
By setting Total Annual Max Capacity Investment to zero during the calibration years for all technologies that weren’t used in the historical years, we ensure the energy mix aligns with historical data. However, it’s crucial to restrict this parameter to the calibration years only; otherwise, these technologies will be unable to compete in future scenarios. It could also be advisable to set this parameter to zero for a few years beyond the last calibration year for technologies with long construction periods. For example, it is unlikely that an energy planner would propose a hydropower plant to be installed between 2024 and 2025, given that such plants typically require 5 to 10 years to build.

## Slide 13
13
Lecture 4.1 References
KTH. (2018). OSeMOSYS Documentation. https://osemosys.readthedocs.io/en/latest/index.html#
Plazas-Niño, F. (2024). Step-by-Step Guide to National Energy System Modelling with OSeMOSYS (v1.0). Zenodo. https://doi.org/10.5281/zenodo.13883416

## Slide 14: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Fernando Plazas-Niño, Trevor Barnes, Leigh Martindale