## Slide 1
Energy system modelling using OSeMOSYS
LECTURE 10
EMISSIONS

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO1 : Learn the importance of emissions accounting and the anthropogenic nature of climate change
ILO2: Learn how to represent emissions and how to constrain emission levels in OSeMOSYS in line with climate targets
ILO3: Learn how to add emissions to the OSeMOSYS model

## Slide 3
3
10.1.1 What is Climate Change?
10.1 Anthropogenic Causes of Climate Change
(Efbrazil, image, license: CC BY-SA 4.0)
(Concepts: Usher, W. (2021))
Notes: Climate change is most often thought of as the rise in global temperatures since the 20th century, shown on this figure. This global warming has multiple impacts that are also elements of climate change, including sea level rise, ice mass loss, ocean acidification, changes in animal and plant life, and extreme weather conditions. Whilst there has historically been natural climate variability, the changes since the 20th century cannot be explained by this alone and are attributed directly or indirectly to human activities which have altered the composition of the atmosphere, in addition to the natural climate variability. These human activities are known as anthropogenic causes of climate change, which we will discuss next.

## Slide 4
4
10.1.2 Global Warming and the Greenhouse Effect
10.1 Anthropogenic Causes of Climate Change
(Femke Nijsse & Eric Fisk, image, license: CC BY-SA 4.0)
(Concepts: Usher, W. (2021))
Notes: Human activities are thought to cause climate change through the greenhouse effect. This is where heat naturally radiating from the earth is trapped in the atmosphere due to the presence of greenhouse gases (GHGs). GHGs occur naturally. However, human activities have significantly increased their concentration in the atmosphere, hence amplifying the greenhouse effect and causing global warming. GHGs include carbon dioxide (CO2), methane (CH4), and nitrous oxides (NOx). The concentrations of all these gases have increased significantly since the pre-industrial era.
The capacity of a GHG or other agent to contribute to climate change is measured using the concept of radiative forcing. A positive radiative forcing indicates that the gas or agent increases global warming, with higher values signifying a greater effect. From this graph, we can see that all the GHGs mentioned above contribute to climate change. However, carbon dioxide is the focus of most analyses, because it has a large radiative forcing and it is the most emitted GHG by volume.
Next, we will look at which human activities emit GHGs.

## Slide 5
5
10.1.3 Introduction to Anthropogenic Causes of Climate Change
10.1 Anthropogenic Causes of Climate Change
(RCraig09, image, license: CC BY-SA 4.0)
(Concepts: Usher, W. (2021))
Notes: This slide introduces the links between human activities, global warming, and climate change effects. Several human activities, across multiple sectors, are responsible for emitting greenhouse gases. Most of these activities relate to the burning of fossil fuels, including electricity, heat production, cooking, and transportation. The retrieval, processing, and distribution of fossil fuels before they are used are also responsible for emitting greenhouse gases. Other activities creating significant levels of greenhouse gas emissions include industrial processes and agriculture, forestry, and land-use change.

## Slide 6
6
10.1.4 Carbon Dioxide Emissions by Country
10.1 Anthropogenic Causes of Climate Change
(Tomastvivlaren, image, license: CC BY-SA 4.0)
Notes: This chart shows that some countries emit more carbon dioxide than others. Emissions from China, the United States, and the European Union alone far outweigh those from all other countries combined. Developed countries are responsible for the majority of historical emissions, and it follows that they bear a large part of the responsibility for mitigating climate change. However, although many developing countries are taking steps to decarbonise their economies, the pace of progress is insufficient to avoid dangerous levels of global warming. Furthermore, climate change is a global issue with global impacts, and there are opportunities for all countries to play a part in its mitigation. It is often thought that developing countries must choose between economic development and protecting the environment, but there is the opportunity to avoid mistakes made by developed countries and instead pursue sustainable, low-carbon economic growth. Renewable energy technologies are rapidly declining in cost, so developing countries could support growth with affordable low-carbon energy systems. Importantly, small shares of fossil generation could play a role in developing countries to stabilize the system and allow incorporation of variable renewables, especially since developing countries have historically had low emissions. This can be pictured as an intermediate step, where small shares of fossil fuels are used to support the system whilst shares of renewables are increased, after which the system would ideally become 100% renewable to meet climate change goals. OSeMOSYS is helpful in assessing the cost and emissions implications of such scenarios to support policymaking.

## Slide 7
7
10.1.5 Effects of Climate Change
10.1 Anthropogenic Causes of Climate Change
(Our World in Data, image, license: CC BY 3.0)
Global temperature rise
Sea level rise
Ocean acidification
Extreme weather events
Reduced biodiversity
Human health impacts
Reduced agricultural yields
Economic consequences
(Concepts: Usher, W. (2021))
Notes: Climate change and sea level rise impact all human, animal, and plant life. Many of these effects are already measurable and will continue to worsen. They include:
uninhabitable areas, causing displacement of communities and mass migration;
reduced biodiversity, increased species extinctions rates, and changes in life ecosystems;
poorer human health, for example due to rising temperatures in cities or reduced agricultural yields that threaten food supplies;
higher frequency of extreme weather events such as floods and hurricanes, threatening lives and infrastructure;
Via these impacts, climate change will have enormous economic consequences, especially in the global south. For example, this graph shows that GDP in Africa, Asia, and South America is forecast to be up to 4% lower under a scenario with 2 degrees of warming relative to a scenario with no additional warming.
The negative effects of climate change are grounds for rapid and extensive action on climate change, with the transformation of global energy systems being a key step due to the emissions they currently produce.

## Slide 8
8
Lecture 10.1 References
Usher, William. (2021, March). Climate Change: Mitigation - Adaptation (Version 1). Zenodo. http://doi.org/10.5281/zenodo.4585597

## Slide 9
9
10.2.1 The Need for Emissions Representation in Energy System Models
10.2 Emissions Representation
(Our World in Data, image, license: CC BY 3.0)
Notes: In an effort to mitigate climate change and prevent the severe impacts mentioned previously, representatives from 195 nations at the 'COP' 21 in Paris agreed to a long-term goal of limiting the global average temperature rise to well below 2 degrees Celsius relative to pre-industrial levels. Achieving this goal will require a global transition to a low-carbon economy. The energy sector will play a crucial role, since it is responsible for a large share of total historical anthropogenic GHG emissions. In addition, it is important to reduce emissions of other pollutants such as nitrous oxides, which also have public health and environmental impacts.
Energy system modelling using tools like OSeMOSYS can support the transformation of energy systems by providing insights into the implications of different scenarios. In order to use modelling to support policymaking in line with climate change goals, it is crucial that we can represent emissions in OSeMOSYS.

## Slide 10
10
10.2.2 Introduction to Emissions Representation in Energy System Models
10.2 Emissions Representation
Fuel-Dependent Emissions:
Emissions that can be estimated fairly accurately based on the total amount of fuels combusted and the averaged carbon content of the fuels
E.g., Carbon Dioxide
Technology-Dependent Emissions
Emissions depend significantly on the combustion technology and operating conditions used, such as the specific type of power plant
E.g., Nitrous Oxides
Notes: In energy system models, emissions are represented either in fuels or in technologies. Carbon dioxide emissions are usually modelled in fuels, because emissions can be estimated fairly accurately based on the total amount of fuels combusted and the average carbon content of those fuels. In contrast, some pollutants such as nitrous oxides, are commonly represented in technologies. This is because these emissions depend on the combustion technology and its operating conditions.

## Slide 11
11
10.2.3 Representing Emissions in OSeMOSYS
10.2 Emissions Representation
Fuel-dependent emissions are accounted for in primary energy supply technologies
Technology-dependent emissions are accounted for in technologies using fuels e.g. power plants
Notes: As mentioned in the previous slide, different emissions are represented in different parts of the Reference Energy System.
Fuel-dependent emissions, such as carbon dioxide, can be accounted for by primary energy supply technologies, such as the coal extraction and imports technologies. Therefore, we do not need to add a carbon dioxide emissions factor to coal power plant technologies, as their emissions are already represented in the coal primary fuel technologies.
In contrast, technology-dependent emissions are accounted for by the emitting (i.e. fuel-burning) technologies. For example, to represent nitrous oxides emissions from power plants, we assign emissions factors to each power plant technology that produces nitrous oxides.
We will discuss emissions factors and the parameters used to represent emissions in OSeMOSYS in more detail next.

## Slide 12
12
10.2.4 Emission Activity Ratio
10.2 Emissions Representation
Emission Activity Ratio [Mt/PJ]: defines the rate of emission by each technology. We can estimate the emission activity ratio by dividing the input fuel emission factor by the technology efficiency.
Note that for primary technologies, the emission activity ratio is equivalent to the fuel emission factor.
Notes: In OSeMOSYS, all emissions are accounted for using the same parameter: the Emission Activity Ratio. This parameter defines the rate of emission of a pollutant by a technology in units million tonnes per petajoule or gigawatt hour of energy. The Emission Activity Ratio is defined for each combination of technology and pollutant in OSeMOSYS.
For example, the Emission Activity Ratio for carbon dioxide (the pollutant) for the coal extraction technology (the technology) would be equal to the amount of carbon dioxide released (in million tonnes) from burning 1 petajoule of coal.
For technology-dependent emissions, instead of requiring one emission ratio per fuel and pollutant, we ideally need emissions data for each technology which emits the pollutant. If this data is not available, we can estimate the emission activity ratio by dividing the average fuel emission factor by the technology efficiency. We will go through examples using these parameters in hands-on exercises.

## Slide 13
13
10.2.5 Example Emissions Factors
10.2 Emissions Representation
Fuel | Emission factor (kg/TJ) |  | 
 | CO2 | CH4 | N2O
Coal | 88136.0 | 10.0 | 1.5
Fuel oil | 80460.3 | 3.0 | 0.6
Diesel | 74233.4 | 3.9 | 3.9
Natural gas | 55539.1 | 92.0 | 3.0
Gasoline | 69323.7 | 33.0 | 3.2
LPG | 67185.1 | 5.0 | 0.1
Jet fuel-Kerosene | 73939.6 | 10.0 | 2.0
Source: IPCC (2006)
Notes: This slide shows some emissions factors for different fossil fuels and pollutants. These are the kind of data that we would use to define the Emission Activity Ratio in OSeMOSYS. In this case, we would use the emissions factors to define the Emission Activity Ratio for the technologies that produce the fuels listed, such as the coal extraction technology or coal imports technology. Looking at the data themselves, we can see that coal has the highest carbon dioxide emissions factor of the fuels listed, with oil products having slightly lower values and natural gas having the lowest. This is one of the reasons why coal power plants are often considered the most controversial in light of climate change goals, since coal has a very high carbon content.

## Slide 14
10.2 Emissions Representation
10.2.6 Adding Emission Activity Ratios to the Model
Notes: To assign emissions to a particular technology you would have to assign the relevant emissions to the ‘Emissions Activity Ratio’ column on the far right of the technologies tab in the ‘Model Configuration’ page of OSeMOSYS MUIO. Then you will you will be able to enter emissions activity ratio data for all years in the modelling horizon for that technology in the interface.

## Slide 15
Emission Constraints | Descriptions
Annual Emission Limit | Used to set an upper limit on emissions in a particular year. It will set a total maximum allowable cap on emissions that cannot be exceeded.
Emissions Penalty | Used to assign a cost to the release of an emission. It can represent an actual charge such as a tax or penalty, or an external cost that is not formally monetized. A negative value can be used to represent a credit or subsidy.
Model Period Emission Limit | Used to set a cumulative limit on emissions over the entire model horizon (i.e. all years).
10.2 Emissions Representation
10.2.7 Constraining Emissions
Notes: Constraining emissions is a key feature in OSeMOSYS that allows users to model the environmental impact of different energy system pathways. As countries adopt climate targets, such as net-zero commitments or emissions reduction pledges under the Paris Agreement, it becomes essential to incorporate emission limits and penalties into energy system planning models.
OSeMOSYS offers flexible tools to represent these constraints, helping users explore how different policy options—like carbon taxes or emission caps—can shape investment decisions and system operation.
The AnnualEmissionLimit parameter is used to set an upper limit on emissions in a particular year. It will set a total maximum allowable cap on emissions that cannot be exceeded. This parameter can for instance be used to model carbon mitigation scenarios. GHG mitigation goals are often specified as a target in a specific year (e.g. 30% reductions by 2030) and this parameter can be used to represent this.
The AnnualEmissionLimit parameter is defined for each emission and can be changed from year to year. It is specified in the applicable units of that emission.
The emissions penalty parameter is used to assign a cost to the release of an emission. It can represent an actual charge such as a tax or penalty, or an external cost that is not formally monetized. A negative value can be used to represent a credit or subsidy.
The AnnualEmissionLimit parameter is defined for each emission and can be changed from year to year. It is specified in currency units per unit of emission (e.g. $/Million tonnes). The parameter ModelPeriodEmissionLimit is used to set a cumulative limit on emissions over the entire model horizon (i.e. all years).
The parameter can for instance be used to model carbon mitigation scenarios. Since climate change impacts are ultimately determined by total cumulative greenhouse gas emission (GHG), reducing total emissions over time is more important than reaching an emission target for a given year. This parameter therefore lets users directly limit GHG impacts on climate, while allowing for the emission reduction pathway to be optimized.
The ModelPeriodEmissionLimit parameter is time-independent and defined for each emission. It is specified in the applicable units of that emission.

## Slide 16
16
16
Lecture 10.2 References
Taliotis, Constantinos, Gardumi, Francesco, Shivakumar, Abhishek, Sridharan, Vignesh, Ramos, Eunice, Beltramo, Agnese, … Howells, Mark. (2018, December). Emissions representation in OSeMOSYS. Zenodo. http://doi.org/10.5281/zenodo.4585676
IPCC (2006) Guidelines for National Greenhouse Gas Inventories, Volume 2: Energy, Table 1.3; available from: https://www.ipcc-nggip.iges.or.jp/EFDB/find_ef.php

## Slide 17: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Fernando Plazas-Niño, Emma Richardson, Lucy Allington, Carla Cannone, Pooya Hoseinpoori, Alexander Kell, Adam Hawkes, Mark Howells