## Slide 1
Energy system modelling using OSeMOSYS
LECTURE 12
MODELLING OF THE INDUSTRIAL SECTOR

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO1: Learn about the energy consumption in the industrial sector
ILO2: Understand different approaches to disaggregate the energy consumption in the industrial sector
ILO3: Understand how to model end-use technologies in the industrial sector using OSeMOSYS

## Slide 3
3
12.1.1 Introduction
12.1 Industrial sector
Chart: Final energy consumption worldwide in 2022, by sector
| Industry | Transport | Residential | Commercial and public services | Agriculture, forestry and fishing | Non-energy use | Non-specified
 | 128.29 | 117.33 | 85.63 | 33.72 | 34.04 | 40.68 | 6.58
Source: Statista (2024) - Link
The industrial sector encompasses a wide range of economic activities that transform raw materials into finished goods and intermediate products.
Notes: The industrial sector encompasses a wide range of economic activities that transform raw materials into finished goods and intermediate products. It includes energy-intensive industries such as steel, cement, and chemical production, as well as less energy-intensive sectors like food processing and textiles. This sector plays a critical role in supporting global economic growth, infrastructure development, and supply chains for various goods and services. However, it is also one of the largest consumers of energy, accounting for approximately 30% of global final energy use and contributing significantly to greenhouse gas emissions.
The industrial sector’s energy consumption is characterized by a reliance on both electricity and fossil fuels, with a significant share used for high-temperature heat and mechanical processes. Energy-intensive industries, such as iron and steel, cement, and petrochemicals, dominate the sector’s energy demand and carbon emissions due to their reliance on carbon-intensive fuels. Meanwhile, light industries like food and beverage processing typically have lower energy demands but still play a significant role in regional economies. As the demand for industrial goods rises in emerging markets, the sector’s energy use and emissions are projected to grow, underscoring the importance of innovation and policy measures to drive energy efficiency and decarbonisation.
Disclaimer: This lecture is not a resource to enable one to go from an energy balance to modelling the sector but rather provides an overview of the sector. Nevertheless, you would follow the same logic on calibration that was covered in Lecture 5.

## Slide 4
4
12.1.2 Subsectors
12.1 Industrial sector
The following subsectors are typically defined in the final energy balances:
Iron and steel
Chemical and petrochemical
Non-ferrous metals
Non-metallic minerals
Transport equipment
Construction
Machinery
Mining and quarrying
Food, beverages and tobacco
Paper, Pulp and printing
Wood and wood products
Textile and leather
Notes: The industrial sector can be categorized into various subsectors based on energy balances, reflecting differences in energy intensity and usage patterns. Energy-intensive industries, such as iron and steel, chemical and petrochemical, non-ferrous metals, and non-metallic minerals, dominate global industrial energy consumption. These industries require significant amounts of high-temperature heat and energy for processes like smelting, chemical synthesis, and cement production. For example, the iron and steel industry is one of the largest consumers of coal and electricity, while the chemical and petrochemical sector uses both energy and feedstocks, such as natural gas, to produce fertilizers, plastics, and other materials. The non-ferrous metals and non-metallic minerals industries also demand substantial energy for processes like aluminum smelting and cement kiln operation, making these subsectors critical areas for energy efficiency and decarbonization efforts.
Other industrial subsectors, such as transport equipment, machinery, mining and quarrying, and construction, are less energy-intensive but still significant in terms of total energy demand due to their scale and economic importance. For instance, transport equipment and machinery industries primarily consume electricity for manufacturing and assembly processes. Meanwhile, food and tobacco, paper, pulp and print, and wood and wood products rely on a mix of thermal and electrical energy for production. These subsectors often overlap with local and regional economic priorities, such as mining in resource-rich areas or food processing in agricultural regions. Lastly, sectors like textile and leather and construction are vital contributors to specific economies and consume energy for processes like fabric production or material manufacturing. Categorizing industries based on energy balances helps identify areas for improvement, enabling targeted interventions to optimize energy use and reduce emissions.

## Slide 5
5
12.1.3 Energy demands
12.1 Industrial sector
The most common energy demands modelled are:
Motive power
Process heat
Specific electricity uses
Notes: The industrial sector's energy demands are diverse, reflecting the wide range of processes and activities across different industries. The largest share of energy consumption comes from process heat, which is used in high-temperature applications such as steelmaking, cement production, and chemical manufacturing. These processes require temperatures ranging from several hundred to thousands of degrees Celsius, often relying on fossil fuels like coal, natural gas, and oil. Process heat also includes low-temperature applications for steam generation used in various processes. In addition, mechanical drive energy is critical for powering machinery, compressors, and pumps in industries like mining, manufacturing, and food processing. Specific electricity uses include lighting, motors, and increasingly advanced technologies such as robotics and automated production lines.
Energy demands vary significantly between subsectors. For example, the chemical and petrochemical industry consumes energy not only for heat but also as a feedstock for producing chemicals and plastics. The iron and steel industry is heavily reliant on coal for blast furnaces, while the non-ferrous metals sector, such as aluminum production, demands large amounts of electricity for electrolysis. Sectors like food processing and textile manufacturing primarily use energy for thermal applications such as drying, heating, and refrigeration. Across all subsectors, there is a growing trend toward electrification and the integration of renewable energy technologies to meet these demands sustainably.

## Slide 6
6
12.1.4 Key drivers and challenges in industrial energy use
12.1 Industrial sector
Drivers
Economic growth and industrialization
Population growth and urbanization
Challenges
Reliance on fossil fuels
Long asset lifecycles
Global supply chains and trade
High costs of emerging solutions
Technological advancement
Barriers in regulation and financing
Notes: Several factors drive energy use in the industrial sector. Economic growth and industrialization are among the most significant, particularly in emerging economies where manufacturing and construction activities are rapidly expanding. Population growth and urbanization further increase the demand for industrial products such as steel, cement, and chemicals. Technological advancements also drive energy use, as industries adopt more complex machinery and automation, which often require electricity and high-quality energy inputs. Global supply chains and trade also influence energy consumption, as manufacturing hubs concentrate in regions with cost advantages, leading to increased energy demands in those areas.
The industrial sector faces significant challenges in managing and reducing energy use. A major issue is the heavy reliance on fossil fuels for high-temperature processes, which lack cost-effective low-carbon alternatives at scale. The sector also grapples with long asset lifecycles, making it difficult to retrofit or replace existing infrastructure with more efficient or cleaner technologies. Another challenge is the variability in energy efficiency practices and technology adoption across industries and regions, often due to differing regulatory environments or access to financing. Additionally, decarbonization efforts can be hindered by the high costs and technical complexities of emerging solutions such as hydrogen, carbon capture, and electrification. Overcoming these challenges requires coordinated efforts among industry stakeholders, governments, and technology providers to foster innovation, policy support, and investments in sustainable industrial practices. This list is not exhaustive.

## Slide 7
7
Lecture 12.1 References
Manuel, S. D., Floris, T., Kira, W., Jos, S., & André, F. (2022). High technical and temporal resolution integrated energy system modelling of industrial decarbonisation. Advances in Applied Energy, 7. https://doi.org/10.1016/j.adapen.2022.100105

## Slide 8
8
12.2.1 Level of disaggregation
12.2 Approaches for modelling the industrial sector
Modeling the industrial sector is a challenging task due to the wide variety of subsectors and processes. A single subsector often encompasses multiple subindustries. Some examples are shown below.
Non-metallic minerals
Cement
Ceramics
Glass
Lime
Bricks
Non-ferrous metals
Copper
Aluminium
Lead and/or Tin
Nickel and/or Cobalt
Zinc and/or Cadmium
Notes: First, it is important to define which subsectors and industrial activities will be modelled. Not all subsectors are active in every country, and not all have the same level of energy consumption. The final energy balance should be the initial input to determine the advisable level of disaggregation in each case. For subsectors where there is no energy consumption of any fuel, we can immediately discard them unless there are known future plans to develop specific industries in the region.
Next, we should examine manufacturing or industrial reports to understand the types of industries included in each subsector for your region. For example, if there is energy consumption in the non-metallic minerals subsector, we might find three main activities: cement, ceramics, and glass production. Each of these industrial activities involves different energy processes and requires tailored modeling.
However, greater detail in disaggregation often results in increased model complexity, and the insights gained from this additional detail may not always be valuable. We will study three examples of modelling in the industrial sector to explore the differences and options in this area.

## Slide 9
9
12.2.2 The case of The Netherlands
12.2 Approaches for modelling the industrial sector
Four key subsectors were modelled and final demands were expressed in terms of tonnes of materials.
Subsectors
High-value chemicals (e.g., Naptha steam craker)
Hydrocarbons (e.g., traditional refining of crude oil)
Ammonia production (e.g., Haber-Bosh process)
Steel production (e.g., blast furnace)
Final demands
Tonnes of olefins
Tonnes of hydrocarbons
Tonnes of fertilizers
Tonnes of steel
Notes: In a study conducted by Sanchez Dieguez et al. (2022), an assessment of industrial decarbonization in the Netherlands was presented. Four key activities were included: high-value chemicals, hydrocarbons, ammonia, and steel production. The approach used to drive the system was to treat materials, rather than useful energy, as final demands. As shown in the figure, the final demands were defined in terms of tonnes of olefins, hydrocarbons, fertilizers, and steel.
Different technological alternatives were modeled within each subsector. For instance, in the steel industry, four processes for steel production were covered: blast furnace, smelting reduction, direct reduction, and electrolytic methods. For each method, several technologies were considered. For example, within blast furnace production, options included CCUS retrofits, top gas recirculation (TGR), or a combination of both.
Additionally, other subsectors were modeled in less detail to complete the industrial sector, including aluminum, urea, chlorine, glass, ceramics, and paper and board production. This study serves as an example of very detailed industrial sector modeling.

## Slide 10
10
12.2.3 The case of Costa Rica
12.2 Approaches for modelling the industrial sector
Seven industrial energy demands were modelled with corresponding technology options
Technologies
Boilers
Cement kilns
Glass furnaces
Heaters for food production
Lift trucks
On-site power generation
Other electricity uses
Final demands
Steam for all industries
Process heat for cement
Process heat for glass
Process heat for food
Lift-truck demand
On-site electricity demand
Other electricity demand
Notes: The Electric Power & Energy Research Laboratory at the University of Costa Rica developed a second version of the OSeMOSYS model for Costa Rica, incorporating the industrial sector. In this model, seven final energy demands were defined, representing the needs for heat, motive power, and electricity.
One initial simplification was aggregating the steam demand of all industries into a single demand. For steam generation, different boiler technologies were modeled (e.g., biomass, LPG, diesel, hydrogen, electricity). For heat demand, the three main industries in the country were specified: cement, glass, and food production. Similarly, various technological options for kilns, furnaces, and heaters were modeled for each energy demand.
The demand for moving lift trucks was also included, considering diesel, LPG, and electricity as input fuels. Finally, both on-site electricity generation and electricity supplied by the centralized grid were included.
Unlike the previous example, this model represents final demands as energy carriers instead of final end products. This case can be considered a medium-sized, disaggregated example that balances simplifications with a focus on key subsectors.

## Slide 11
11
12.2.4 The case of Colombia
12.2 Approaches for modelling the industrial sector
All industries are aggregated into three unified demands, representing the requirements for heat and electricity.
Technologies
Boilers
Furnaces
Electrical devices
Final demands
Indirect heat
Direct heat
Electricity demand
Notes: Plazas-Niño et al. (2023) modelled the Colombian energy system, including the industrial sector. Due to data unavailability, subsectors were not modelled; instead, energy demands for the entire industry were aggregated. Three final energy services were represented: direct heat, indirect heat, and electricity.
Direct heat is primarily used for high-temperature processes in energy-intensive industries such as steel, cement, petrochemicals, and paper. Indirect heat is mainly associated with steam generation and hot water, which are used in industries like food and beverage processing, textiles, and small-scale manufacturing. Finally, electricity is essential across all industries for various applications, with no explicit consideration of motive power demand.
For indirect heat, different boiler options (e.g., biomass, natural gas, hydrogen, electricity) were included, and for direct heat, an aggregated category of furnaces was represented. This example illustrates a highly simplified approach to modeling the industrial sector.

## Slide 12
12.2.5 General Rule
12.2 Approaches for modelling the industrial sector
Typically, in the Industry Sector you can simply calibrate the sector output activity to (e.g. Million tonnes of steel produced etc.) or input energy (e.g. fuel use through the energy balance) or both.
Notes: Typically, in the Industry Sector you can simply calibrate the sector output activity to (e.g. Million tonnes of steel produced etc.) or input energy (e.g. fuel use through the energy balance) or both.

## Slide 13
13
13
Lecture 12.2 References
EPERLab-UCR. (2021). OSeMOSYS-CR v2.0. Documentation. https://osemosys-cr-v2.readthedocs.io/en/latest/Overview.html
Manuel, S. D., Floris, T., Kira, W., Jos, S., & André, F. (2022). High technical and temporal resolution integrated energy system modelling of industrial decarbonisation. Advances in Applied Energy, 7. https://doi.org/10.1016/j.adapen.2022.100105
Plazas-Niño, F. A., Yeganyan, R., Cannone, C., Howells, M., & Quirós-Tortós, J. (2023). Informing sustainable energy policy in developing countries: An assessment of decarbonization pathways in Colombia using open energy system optimization modelling. Energy Strategy Reviews, 50, 101226. https://doi.org/10.1016/j.esr.2023.101226

## Slide 14
14
12.3.1 Technologies in the reference energy system
12.3 Modelling of industrial sector using OSeMOSYS
Coal furnace
Natural gas boiler
Diesel lift-truck
High heat demand
Coal
Natural gas
Diesel
Low heat demand
Lift-truck demand
DEMINDHHECOA
DEMINDLHENGS
DEMINDLIFDSL
INDHHE
COA
NGS
DSL
INDLHE
INDLIF
Notes: Similar to power plants, end-use technologies are represented as boxes in the reference energy systems. The input commodities can be either secondary energy carriers (e.g., diesel, electricity) or primary energy carriers (e.g., biomass, coal), depending on the technology, while the output commodity corresponds to the final energy demand (e.g., heat) or end product (e.g., tonnes of steel).
The examples shown on the slide illustrate three final energy demands previously described: high and low process heat, and motive power for lift trucks. Additional technological alternatives for meeting these final energy demands can be included, as we will explore in the next slide, to analyze future energy transition pathways. If you need a refresher on the naming conventions, refer to the material from Lecture 3.

## Slide 15
15
12.3.2 Fuel switching in the industrial sector
12.3 Modelling of industrial sector using OSeMOSYS
Coal furnace
Natural gas furnace
Hydrogen furnace
High heat demand
Coal
Natural gas
Hydrogen
Biomass boiler
LPG boiler
Electrical boiler
Low heat demand
Biomass
LPG
Electricity
High heat demand
High heat demand
Low heat demand
Low heat demand
Notes: Fuel switching plays a major role in modeling industrial technologies. However, efficiency improvement is closely linked to fuel switching, as cleaner fuels such as electricity or green hydrogen often require smaller quantities than fossil fuels. Additionally, since many manufacturing processes are already mature, technological efficiencies are unlikely to change significantly—meaning that efficiency gains are primarily achieved through fuel switching. In the examples on the slide, the same heat demands can be met by different fuels. Technologies like coal furnaces, natural gas furnaces, and hydrogen furnaces are commonly modeled to analyze transitions to cleaner energy sources. This approach enables the evaluation of how different fuels and technologies can supply process heat, which is critical for industries like steel, cement, and chemicals, as studied previously. For instance, replacing coal furnaces with natural gas furnaces can significantly reduce carbon emissions since natural gas burns more cleanly. Similarly, hydrogen furnaces provide a near-zero-emission alternative when hydrogen is produced from renewable energy, making them a compelling option in scenarios focused on deep decarbonization.

## Slide 16
16
12.3.3 Defining end-use technologies in OSeMOSYS
12.3 Modelling of industrial sector using OSeMOSYS
Key parameters for defining end-use technologies in the industrial sector:
Output Activity Ratio
Input Activity Ratio
Capital Cost
Fixed Cost
Capacity factor
Residual Capacity
Operational Life
Emissions Activity Ratio
Notes: For end-use technologies in the industrial sector, a few key parameters are sufficient to provide a good characterization.
Output and Input Activity Ratios: These are used to define the efficiency of the technology, as studied previously.
Capital Cost: This is the overnight cost per unit of installed capacity.
Fixed Cost: Operational and maintenance costs that are independent of the activity of technologies.
Residual Capacity: Represents the installed capacity of each technology.
Operational Life: Denotes the lifespan of each technology, usually provided by the manufacturer.
Capacity factor: Similar to power plants, industrial-grade equipment requires consideration of the percentage of actual available capacity used to produce energy during each timeslice.
Emissions Activity Ratio: Process emissions can be assigned to technologies in particular sectors. Process emissions in the industry sector are greenhouse gas emissions released directly from industrial processes, not from fuel combustion. They occur during chemical or physical transformations—for example, CO₂ released during cement production, steelmaking, or fertilizer manufacturing. These emissions are often hard to abate and require targeted technologies like carbon capture, process redesign, or material substitution to reduce. Therefore, it is important to represent these types of emissions in the industry sector.
In the next section, we will explore basic calculations to estimate some of these parameters when data is unavailable.

## Slide 17
17
12.3.4 Example of end-use technologies in OSeMOSYS
12.3 Modelling of industrial sector using OSeMOSYS
Output Activity Ratio: 1
Input Activity Ratio: 2.44
Capital Cost: 970 USD/kW
Fixed Cost: 1.6 USD/kW
Residual Capacity: 1.06 GW
Operational Life: 25 years
Capacity factor: 0.91
Biomass boiler
DEMINDLHEBIO
Low heat demand
Biomass
INDLHE
BIO
If the efficiency is 72% and the output activity ratio (INDLHE) is 1:
Input Activity Ratio = 1/0.72 = 1.39 (BIO)
Notes: This slide presents example data for a biomass boiler, sourced from a 2023 paper that used OSeMOSYS to model the Colombian energy system.
The capital cost is 970 USD per kW, while the fixed cost is 1.6 USD per kW. The residual capacity is provided in GW. The operational life is set at 25 years, which is very similar to biomass power plants.
This slide also includes an example calculation for the input activity ratio. The output fuel is low heat demand, and the output activity ratio is set to a default value of 1, as in previous examples. The input activity ratio can be calculated by dividing 1 by the efficiency. In this case, dividing 1 by 0.72 yields an input activity ratio of approximately 1.39. This value would be assigned to biomass, as it is the input fuel for a biomass boiler.

## Slide 18
18
Lecture 12.3 References
Plazas-Niño, F. A., Ortiz-Pimiento, N. R., & Quirós-Tortós, J. (2023). Supporting energy system modelling in developing countries: Techno-economic energy dataset for open modelling of decarbonization pathways in Colombia. Data in Brief, 48, 109268. https://doi.org/https://doi.org/10.1016/j.dib.2023.109268

## Slide 19
12.4
12.4 Calibrating the Industry Sector
Calibrate to Fuel Use Only | Calibrate to Output Activity Only | Calibrate to Both Input Fuel Use and Output Activity
Match historical energy balance and get the economics right |  | 

## Slide 20
12.4 Different Ways to Calibrate the Industry Sector
12.4 Calibrating the Industry Sector
Calibration Methodology | Positives | Negatives
Calibrate to fuel input only | Match historical energy balance which is critical and get the economics right | Might not have an actual representation of the recorded output which can be important
Calibrate to output only | Match historical production and get the economics right | No accurate historical fuel use which is not recommended.
Calibrate to both input and output | Match both historical energy balance and actual production | If the two come from disparate sources, it’s likely the efficiency can be significantly skewed.
Notes: There are several different ways to calibrate the industry sector.
The first possible way is calibrating only the fuel use. This is beneficial because you match the model to the country’s energy balance which is critical, and you can get the economics right. The main negative could be that you might not have actual representation of the recorded output which can be important in some cases (e.g. the client might want to know how many Mt of steel were produced). The second possible way is calibrating to output activity (e.g. Mtons of steel) only. The positives of this is that you match historical production values and you can also get the economics right. The main negative is that you don’t have an accurate historical fuel use, which is not recommended. This method should only be used if the fuel input is unknown.
The last common way is calibrating both input fuel use and output activity. This is beneficial because you can match the historical energy balance and actual historical production. The only potential issue with this is that if the two data points come from disparate sources it’s likely that the efficiency which is a result of the input fuel use and output activity, could be significantly skewed.

## Slide 21: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Fernando Plazas-Niño, Fynn Kiley