## Slide 1
Energy system modelling using OSeMOSYS
LECTURE 13
MODELLING OF THE TRANSPORT SECTOR

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO1: Learn about the energy consumption in the transport sector
ILO2: Understand basic concepts on the modelling of the transport sector
ILO3: Understand how to model end-use technologies in the transport sector using OSeMOSYS
ILO4: Perform basic calculations in the estimation of parameters for modelling end-use technologies in the transport sector using OSeMOSYS

## Slide 3
3
13.1.1 Introduction
13.1 Transport sector
Chart: Final energy consumption worldwide in 2022, by sector
| Industry | Transport | Residential | Commercial and public services | Agriculture, forestry and fishing | Non-energy use | Non-specified
 | 128.29 | 117.33 | 85.63 | 33.72 | 34.04 | 40.68 | 6.58
Source: Statista (2024) - Link
The transport sector encompasses all modes of transportation used to move people and goods, including road, rail, inland waterways, maritime, and aviation.
Notes: The transport sector encompasses all modes of transportation used to move people and goods, including road, rail, maritime, and aviation. This sector is a cornerstone of modern economies, facilitating trade, supply chains, and the movement of goods across local, national, and international markets. It also supports social connectivity by enabling commuting, leisure travel, and access to essential services such as education and healthcare. The increasing demand for transport is fueled by population growth, urbanization, and rising incomes, particularly in developing regions. As economies expand, the transport sector plays a critical role in bridging geographic distances and fostering economic integration.
However, the transport sector is also a major energy consumer and contributor to greenhouse gas (GHG) emissions. It accounts for approximately 26% of global CO₂ emissions, making it one of the largest sources of anthropogenic emissions. This is primarily due to its heavy reliance on fossil fuels, including gasoline, diesel, and jet fuel, which dominate the energy mix for road vehicles, airplanes, and ships. The combustion of these fuels releases significant amounts of carbon dioxide and other pollutants, exacerbating climate change and air quality issues. Without significant interventions, emissions from the transport sector are expected to continue rising, presenting a formidable challenge to achieving global sustainability goals.

## Slide 4
4
13.1.2 Subsectors
13.1 Transport sector
Transport
Passengers
Freight
Cars
Motorcycles
Taxis
Minibuses
Buses
Trains
Metro
Airplane
Boats
Ships
Trucks
Trains
Airplanes
Ships
Notes: Transport can be broadly categorized into two main types: passenger and freight. Passenger transport focuses on moving people, using modes such as personal vehicles, buses, trains, and airplanes for daily commutes, intercity travel, and leisure activities. Freight transport, on the other hand, involves the movement of goods through trucks, cargo ships, trains, and airplanes, supporting global trade and supply chains. Each mode within these categories plays a distinct role, shaped by factors such as travel distances, infrastructure availability, and economic demand. Passenger transport is often concentrated in urban and suburban areas, while freight transport serves both domestic markets and international trade, requiring integration across various transport networks.
Each transport mode has unique energy requirements and environmental impacts. Road transport, encompassing cars, trucks, and buses, is the largest energy consumer, accounting for approximately 75% of the sector’s total energy use. This dominance is due to the widespread reliance on internal combustion engines and the vast scale of personal vehicle ownership. In contrast, aviation and maritime transport, while smaller in terms of overall energy consumption, are essential for international connectivity and trade. These modes are highly energy-intensive, with aviation contributing disproportionately to CO₂ emissions per passenger or cargo unit, and maritime shipping relying heavily on bunker fuels with high carbon content. Understanding these distinctions is crucial for designing targeted policies and developing technologies that improve efficiency, reduce emissions, and support a sustainable transition across both passenger and freight transport systems.

## Slide 5
5
13.1.3 Fuel consumption – The example of Colombia
13.1 Transport sector
Chart: Energy consumption 2021
| Road passenger private | Road passenger public | Road freight | Air | River | Maritime | Rail
Natural gas | 5.173 | 10.49 | 3.14 | 0 | 0 | 0 | 0
Diesel | 28.703 | 80.48 | 134.681 | 0 | 0.247 | 5.224 | 0
Gasoline | 233.841 | 33.983 | 13.355 | 0.585 | 0.629 | 0 | 0
Electricity | 0 | 0 | 0 | 0 | 0 | 0 | 0.322
Jet Fuel | 0 | 0 | 0 | 37.793 | 0 | 0 | 0
Fuel Oil | 0 | 0 | 0 | 0 | 0 | 0.193 | 0
The transport sector is predominantly dependent on fossil fuels such as gasoline, diesel, jet fuel, and heavy fuel oil,
Notes: The transport sector is heavily reliant on fossil fuels, which account for the vast majority of its energy consumption. Gasoline and diesel dominate road transport, powering passenger vehicles, buses, and freight trucks. Jet fuel is the primary energy source for aviation, while maritime shipping relies on heavy fuel oil, also known as bunker fuel. Rail transport, depending on the region, uses either electricity or diesel as its main energy source. On the slide, you can see an example of the energy mix in the Colombian transport sector, reflecting the points discussed earlier.
In recent years, there has been a growing focus on diversifying the energy mix of the transport sector to meet climate targets. Electricity is emerging as a key energy carrier, especially for road transport, as electric vehicles (EV) adoption accelerates due to declining battery costs and supportive policies. Hydrogen, another promising alternative, is being explored for use in heavy-duty vehicles, shipping, and aviation, offering a zero-emission solution when produced from renewable sources. Biofuels, such as ethanol and biodiesel, provide transitional solutions by reducing lifecycle emissions while leveraging existing fuel infrastructure. Despite these advancements, challenges such as high costs, infrastructure requirements, and the scalability of alternative energy carriers need to be addressed to achieve a sustainable energy transformation in the transport sector.

## Slide 6
6
13.1.4 Key drivers and challenges in transport energy use
13.1 Transport sector
Drivers
Technological innovation
Policy frameworks
Challenges
High upfront costs
Reliance on fossil fuels
Urbanization
Behavioral and cultural barriers
Consumer preferences
Lack of infrastructure
Notes: The key drivers in the transport sector’s energy use and transformation are technological advancements, policy frameworks, and consumer preferences. Technological innovation, such as the development of electric vehicles (EVs), hydrogen-powered transport, and fuel-efficient engines, plays a pivotal role in reducing energy consumption and emissions across various modes. Government policies, including stricter emissions standards, low-emission zones, and subsidies for green technologies, are crucial in accelerating the adoption of cleaner transport solutions. Additionally, shifting consumer preferences toward more sustainable modes of transport, such as electric cars, shared mobility services, and public transit, are driving demand for cleaner alternatives. Urbanization and the growth of megacities also play a significant role in shaping transport demand and promoting efficient public transportation systems that are energy-efficient and reduce congestion.
Despite these positive drivers, the transport sector faces several significant challenges in its path toward decarbonization and energy efficiency. One of the primary obstacles is the high upfront cost of new, low-carbon technologies, such as electric vehicles and infrastructure (e.g., charging stations or hydrogen refueling networks), which can slow adoption rates, especially in developing regions. The existing reliance on fossil fuels, particularly in heavy-duty sectors like freight and aviation, adds complexity to transitioning to cleaner energy sources. Furthermore, the lack of global coordination on energy standards and the slow development of the necessary infrastructure for electric and hydrogen-powered transport hinder progress. Lastly, behavioral and cultural factors, such as the preference for personal vehicles in many countries and a lack of investment in public transportation, continue to pose challenges to widespread adoption of energy-efficient, shared, and public mobility solutions.
This list is not exhaustive.

## Slide 7
7
Lecture 13.1 References
Plazas-Niño, F. (2024, junio 17). Modelling the Road Transport Sector (Theory) | Advanced Energy System Modelling Using OSeMOSYS. Zenodo. https://doi.org/10.5281/zenodo.11882739

## Slide 8
8
13.2.1 Transport Calibration
13.2 Basic concepts on transport modelling
Calibration Methodology | Positives | Negatives
Calibrate to fuel input only | Match historical energy balance which is critical and get the economics right | Might not have an actual representation of the recorded output which can be important
Calibrate to output only | Match historical milelage and get the economics right | No accurate historical fuel use which is not recommended.
Calibrate to both input and output | Match both historical energy balance and actual mileage | If the two come from disparate sources, it’s likely the efficiency can be significantly skewed.
Notes: There are several different ways to calibrate the transport sector.
The first possible way is calibrating only the fuel use. This is beneficial because you match the model to the country’s energy balance which is critical, and you can get the economics right. The main negative could be that you might not have actual representation of the recorded output which can be important in some cases (e.g. the client might want to see actual vehicle mileage represented in the sector). The second possible way is calibrating to output activity (e.g. kilometre-metres travelled by each vehicle) only. The positives of this is that you match historical mileage values and you can also get the economics right. The main negative is that you don’t have an accurate historical fuel use, this is especially NOT recommended for the transport sector. This method should only be used if the fuel input is unknown. Getting the fuel use right for the transport sector is very critical so this should only be done as a last resort.
The last common way is calibrating both input fuel use and output mileage. This is beneficial because you can match the historical energy balance and actual historical mileage. The only potential issue with this is that if the two data points come from disparate sources it’s likely that the efficiency which is a result of the input fuel use and output mileage (i.e. activity), could be significantly skewed.

## Slide 9
9
13.2.2 Transport demand
13.2 Basic concepts on transport modelling
In the transport sector, final demands are expressed in units other than PJ. These demands can be categorized into two broad groups:
Passenger transport: Passenger-kilometer
A
B
30 km
100 passengers
Freight transport:
Tonne-kilometer
A
B
100 km
30 tonnes
Notes: The transport demand is quantified using different units compared to the previously studied demands and is divided into two main categories:
Passenger Transport: This refers to the movement of people between locations, such as a worker commuting from home to their workplace. It is measured in passenger-kilometres (pkm), which represent the total distance travelled multiplied by the number of passengers. For example, if 100 passengers travel 30 kilometers by train, the total passenger kilometers is 3,000.
Freight Transport: This involves the movement of goods between locations, such as transporting fruits from farms to supermarkets. It is measured in tonne-kilometres (tkm), which reflect the total distance travelled multiplied by the weight of the goods transported. or example, if a shipment of goods weighs 30 tons and is transported 100 kilometers, the total tonne kilometers is 3,000.

## Slide 10
10
13.2.3 Modes of transport as demands
13.2 Basic concepts on transport modelling
Road
Rail
River
Air
Cars
Motorcycles
Buses
Trucks
Trains
Metro
Ships
Airplanes
Boats
Maritime
Notes: Transport demand can be classified by mode of transportation, including cars, motorcycles, buses, trucks, and others. These categories can be further refined based on data resolution; for instance, cars may be subdivided into compact cars, full-size cars, SUVs, minivans, and pickups. Additionally, passenger transport can be categorized as either private or public, depending on the mode of travel—for example, cars represent private transport, while buses are part of public transport.
Where data is available, demand can also be disaggregated by travel distance, distinguishing between urban and intercity transport.
It is also essential to differentiate between modes of transport that serve both passenger and freight demands. For example, there may be separate demands for trains transporting passengers and trains carrying freight. In some cases, such as airplanes, both passenger and freight demands can be met simultaneously within the same flight.

## Slide 11
11
13.2.4 Efficiency in transport technologies
13.2 Basic concepts on transport modelling
Load factor: Average number of passengers or tonnes transported by each type of vehicle
Activity factor: Average number of kilometers traveled per year by each type of vehicle
Efficiency: Average number of passenger-kilometers or tonne-kilometers supplied per unit of energy (input fuel).
Notes: Before defining the efficiency of transport technologies, it is important to understand the concepts of load factor and activity factor. The load factor represents the average number of passengers or tonnes transported by each type of vehicle. The activity factor refers to the average number of kilometers traveled per year by each type of vehicle.
Efficiency, in this context, is defined as the average number of passenger-kilometers or tonne-kilometers supplied per unit of energy (input fuel). It is typically expressed in terms of Mpkm per PJ (million passenger-kilometers per petajoule) or Mtkm per PJ ( million tonne-kilometers per petajoule). Alternatively, efficiency data may also be expressed in kilometers per unit of energy.
The load factor can be used to calculate efficiency in passenger-kilometers per unit of energy or tonne-kilometers per unit of energy, depending on the type of transport mode. In other cases, if data is available for the activity factor and the amount of fuel consumed per vehicle, efficiency can first be estimated in kilometers per unit of energy. This can then be converted to passenger-kilometers or tonne-kilometers per unit of energy using the load factor. The equation on the slide illustrates how these concepts are interlinked.

## Slide 12
12
13.2.5 Fleet stock
13.2 Basic concepts on transport modelling
The number of vehicles is an important input in transport modeling for estimating fuel consumption and installed capacity.
Notes: The total number of vehicles, or fleet stock, is a common input in transport modelling. This data is often more disaggregated than energy consumption by vehicle type. The total number of vehicles can be expressed in Mv (million vehicles). If data on load factor, activity factor, efficiency, and fleet stock by technology type is available, it is possible to estimate the fuel consumption for each technology. The equation on the board illustrates how this calculation can be performed. We will revisit this concept in the final section of this lecture to practice these calculations.

## Slide 13
13
13
Lecture 13.2 References
Plazas-Niño, F. (2024, junio 17). Modelling the Road Transport Sector (Theory) | Advanced Energy System Modelling Using OSeMOSYS. Zenodo. https://doi.org/10.5281/zenodo.11882739

## Slide 14
14
13.3.1 Technologies in the reference energy system
13.3 Modelling of transport sector using OSeMOSYS
Gasoline car
Diesel truck
Electric motorcycle
Car transport demand
Gasoline
Diesel
Electricity
Truck transport demand
Motorcycle transport demand
DEMTRACARGSL
DEMTRATRKDSL
DEMTRAMCYELC
TRACAR
GSL
DSL
ELC
TRATRK
TRAMCY
Notes: Similar to power plants, end-use technologies are represented as boxes in the reference energy systems. The input commodities are mainly secondary fuels (e.g., gasoline, diesel, electricity), while the output commodity corresponds to the final transport demand (e.g., car transport demand, truck transport demand).
The examples shown on the slide illustrate three final transport demands by mode of transportation, as described previously: cars, trucks, and motorcycles. Additional technological alternatives for meeting these final energy demands can be included, as we will explore in the next slide, to analyze future energy transition pathways. If you need a refresher on the naming conventions, please refer to the material from Lecture 3.

## Slide 15
15
13.3.2 Fuel switching in the transport sector
13.3 Modelling of transport sector using OSeMOSYS
Gasoline car
CNG car
Electric car
Car transport demand
Gasoline
CNG
Electricity
Car transport demand
Diesel bus
Electric bus
Hydrogen bus
Bus transport demand
Diesel
Electricity
Hydrogen
Car transport demand
Bus transport demand
Bus transport demand
Notes: Similar to the industrial sector, fuel switching plays a significant role in modeling transport technologies. Efficiency improvement is closely linked to fuel switching, as cleaner fuels such as electricity or green hydrogen often require smaller quantities of energy compared to fossil fuels.
In the examples shown on the slide, the same transport demands can be met by different fuels. Technologies like battery electric vehicles, fuel cell electric vehicles, and compressed natural gas (CNG) vehicles are commonly modeled to analyze transitions to cleaner energy sources. This approach facilitates the evaluation of how various fuels and technologies can meet transport demands.
For instance, replacing gasoline vehicles with CNG vehicles can significantly reduce carbon emissions, as natural gas burns more cleanly. Similarly, hydrogen vehicles offer a near-zero-emission alternative when hydrogen is produced from renewable energy, making them a compelling option in scenarios focused on deep decarbonization.

## Slide 16
16
13.3.3 Defining end-use technologies in OSeMOSYS
13.3 Modelling of transport sector using OSeMOSYS
Key parameters for defining end-use technologies in the transport sector:
Output Activity Ratio
Input Activity Ratio
Capital Cost
Fixed Cost
Residual Capacity
Operational Life
Capacity to Activity Ratio
Notes: For end-use technologies in the transport sector, a few key parameters are sufficient to provide a good characterization.
Output and Input Activity Ratios: These are used to define the efficiency of the technology, as studied previously.
Capital Cost: This is critical as it reflects the commercial price of a vehicle. Capital cost is particularly significant from a behavioral perspective in this sector, as people often prioritize price over quality, efficiency, durability, or other features.
Fixed Cost: Operational and maintenance costs that are independent of the activity of a vehicle (e.g., taxes, insurance, annual maintenance).
Residual Capacity: Represents the installed capacity of each technology, typically based on the number of vehicles.
Operational Life: Denotes the lifespan of each technology, usually provided by the manufacturer.
Capacity to Activity Ratio: Controls the conversion of vehicle capacity (number of vehicles) into activity (vehicle-kilometres).
In the next section, we will explore some basic calculations to estimate these parameters.

## Slide 17
17
13.3.4 Example of end-use technologies in OSeMOSYS
13.3 Modelling of transport sector using OSeMOSYS
Output Activity Ratio: 1
Input Activity Ratio: 2 PJ/Gpkm
Capital Cost: 130 MUSD/Gpkm
Fixed Cost: 20 MUSD/Gpkm
Residual Capacity: 31.8 Gpkm
Operational Life: 20 years
Gasoline car
DEMTRACARGSL
Car transport demand
Gasoline
TRACAR
GSL
If the efficiency is 0.5 Gpkm/PJ and the output activity ratio (TRACAR) is 1:
Input Activity Ratio = 1/0.5 = 2 PJ/Gpkm (GSL)
Notes: This slide presents example data for a gasoline car, sourced from a 2023 study that used OSeMOSYS to model the Colombian energy system.
The capital cost is 130 million USD per Gpkm, while the fixed cost is 20 million USD per Gpkm. The residual capacity is provided in Gpkm; however, we will later see how this value directly correlates to the total number of cars, offering a more intuitive measure. The operational life is set at 20 years, which is relatively high for this type of technology but reflects the reality in Colombia, where vehicles are often used beyond the standard manufacturer lifespan.
The slide also includes an example calculation for the input activity ratio. The output fuel is car transport demand, with the output activity ratio set to a default value of 1, consistent with previous examples. Unlike prior technologies, the input activity ratio is not dimensionless. It is calculated by dividing 1 by the efficiency. In this case, dividing 1 by 0.5 yields an input activity ratio of approximately 2 PJ/Gpkm. This value is assigned to gasoline, the input fuel for a gasoline car, indicating that 2 PJ of gasoline is required to supply 1 Gpkm.

## Slide 18
18
Lecture 13.3 References
Plazas-Niño, F. (2024, junio 17). Modelling the Road Transport Sector (Theory) | Advanced Energy System Modelling Using OSeMOSYS. Zenodo. https://doi.org/10.5281/zenodo.11882739
Plazas-Niño, F. A., Ortiz-Pimiento, N. R., & Quirós-Tortós, J. (2023). Supporting energy system modelling in developing countries: Techno-economic energy dataset for open modelling of decarbonization pathways in Colombia. Data in Brief, 48, 109268. https://doi.org/https://doi.org/10.1016/j.dib.2023.109268

## Slide 19
19
13.4.1 Final transport demands
13.4 Practising modelling calculations
Transport demands can be estimated using the final energy balance and technology efficiencies.
Example: Fuel consumption for cars includes 6.5 PJ of gasoline, 2.4 PJ of diesel, and 0.8 PJ of electricity. Using the efficiencies provided in the table, calculate the total car transport demand.
Efficiency | Gasoline | Diesel | Electricity
Cars [Mpkm/PJ] | 500 | 530 | 2800
Notes: Using the final energy balance and vehicle technology efficiencies, we can estimate the total transport demand by mode of transportation. The equation shown on the slide calculates this by summing the product of fuel consumption and technology efficiency. Often, energy balance data is not fully disaggregated by vehicle type, requiring additional assumptions—for instance, estimating proportions based on fleet stock.
In the example on the slide, we have data on fuel consumption for cars and their respective efficiencies. By multiplying fuel consumption by efficiency, we obtain the transport demand in Gpkm for this case. Similar calculations can be applied to estimate transport demand for any mode of transportation.

## Slide 20
20
13.4.2 Capital cost
13.4 Practising modelling calculations
The capital cost of vehicles corresponds to the commercial cost of each technology.
Example: A diesel car has a commercial price equal to 35,000 USD. If the activity factor is 5,000 km per year and the load factor is 1.5 passengers per vehicle, what is the capital cost?
Notes: The capital cost of vehicles corresponds to the commercial cost of each technology. Initially measured in USD per vehicle, this cost can be converted to USD per passenger-kilometre (Mpkm) or USD per tonne-kilometre (Mtkm). This conversion involves dividing the unit cost of each vehicle type by the product of the activity factor and the load factor, as shown in the equation on the slide.
For example, consider a diesel car with a cost of 35,000 USD, an activity factor of 5,000 km per year, and a load factor of 1.5 passengers per vehicle. Using the formula, we calculate the capital cost as approximately 4.7 MUSD per Mpkm.
This method can be applied to calculate the capital cost or fixed cost for any transport technology, following the same logic.

## Slide 21
21
13.4.3 Residual capacity part 1
13.4 Practising modelling calculations
We can calculate the residual capacity based on fuel energy consumption or fleet stock.
Notes: Residual capacity refers to the installed capacity required to meet annual transport demand, equivalent to the fleet stock. Although it could be expressed in million vehicles (Mv) using a "Capacity to Activity Unit" parameter, which accounts for the activity factor multiplied by the load factor for each technology, it is often more practical to define residual capacity directly in terms of Mpkm/year or Mtkm/year. This capacity can be determined based on fuel energy consumption or fleet stock, as demonstrated by the equations on the slide. We will check an example on these calculations in the next slide.

## Slide 22
22
13.4.4 Residual capacity part 2
13.4 Practising modelling calculations
Example 1: Let’s consider that domestic airplanes for passenger transport consume 24 PJ of jet fuel per year. Assuming freight transport is negligible and the efficiency is 830 Mpkm per PJ, what is the residual capacity?
Example 2: There are a total of 45,000 trucks in a region. Considering that the activity factor is 60,000 km per year and the load factor is 20.1 tonnes per vehicle, what is the residual capacity
Notes: On this slide, we can see how to calculate residual capacities using the two approaches. In the first case, we use the fuel consumption per technology and its corresponding efficiency. Multiplying these values yields a residual capacity of 19920 Mpkm/year. Note that this approach assumes a capacity factor of 1, which is a common assumption for transport technologies.
In the second case, the fleet stock is directly known, making this a more accurate method for estimating residual capacity. By using the activity factor and the load factor, we calculate the residual capacity as 54270 Mtkm/year for the truck technology.

## Slide 23
23
Lecture 13.4 References
Plazas-Niño, F. (2024, junio 17). Modelling the Road Transport Sector (Theory) | Advanced Energy System Modelling Using OSeMOSYS. Zenodo. https://doi.org/10.5281/zenodo.11882739
Plazas-Niño, F. A., Ortiz-Pimiento, N. R., & Quirós-Tortós, J. (2023). Supporting energy system modelling in developing countries: Techno-economic energy dataset for open modelling of decarbonization pathways in Colombia. Data in Brief, 48, 109268. https://doi.org/https://doi.org/10.1016/j.dib.2023.109268

## Slide 24: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Fernando Plazas-Niño, Naomi Tan