## Slide 1
Energy system modelling using OSeMOSYS
LECTURE 14
SCENARIO VALIDATION AND DESIGN

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO1: Understand the concept of energy scenario. ILO2: Learn the basic concepts and parameters linked to scenario validation.
ILO2: Learn the basic steps to design energy scenarios.
ILO3: Learn how to model different energy scenarios using OSeMOSYS.

## Slide 3
14.1 Introduction to energy scenarios
14.1.1 What is an energy scenario?
Energy scenarios describe current and possible representations or developments of the energy system in terms of technical and organizational options (Grundwal et al., 2016)
In the case of OSeMOSYS, without imposed constraints, each run represents a baseline scenario of least-cost development of the system.
Notes: Energy scenarios are possible representations used to explore potential futures for energy systems. They provide representations of how technical, organizational, and policy decisions could shape the energy landscape over time. Scenarios help policymakers, researchers, and industry stakeholders understand the consequences of different decisions, such as remaining the same, choosing the most cost-effective options, adopting new technologies or implementing specific policies. As Grundwald et al. (2016) explain, scenarios are not predictions but structured explorations of possible pathways, making them crucial for strategic planning in energy transitions.
In the context of OSeMOSYS, an energy scenario is a run of how a least-cost energy system could evolve under specific conditions. Without additional constraints, OSeMOSYS optimizes the system to minimize costs, providing a "baseline" scenario of the most cost-efficient development. However, by imposing constraints—such as emissions targets, technology limits, or policy objectives—you can create alternative scenarios to study how different decisions impact costs, technology choices, and environmental outcomes. This flexibility makes OSeMOSYS a powerful tool for exploring diverse energy futures.

## Slide 4
 | Name | Description
Activity constraints | Total Technology Annual Activity Upper Limit | Total maximum level of activity allowed for a technology in one year.
 | Total Technology Annual Activity Lower Limit | Total minimum level of activity allowed for a technology in one year.
Capacity constraints | Total Annual Max Capacity | Total maximum existing (residual plus cumulatively installed) capacity allowed for a technology in a specified year.
 | Total Annual Min Capacity | Total minimum existing (residual plus cumulatively installed) capacity allowed for a technology in a specified year.
 | Total Annual Max Capacity Investment | Maximum capacity of a technology, expressed in power units.
 | Total Annual Min Capacity Investment | Minimum capacity of a technology, expressed in power units.
Emissions | Emissions Penalty (i.e., carbon price) | Penalty per unit of emission.
 | Annual Emission Limit | Annual upper limit for a specific emission generated in the whole modelled region.
14.2.1 Using Constraints in Scenarios
14.2 Introduction to energy scenarios
Notes: In OSeMOSYS we often use constraints to help us reflect reality, policies, and develop scenarios. Some of these constraints were already touched on in previous lectures but you can see them defined again in the slide above.
Let’s start with some examples of using constraints. For example, if the model doesn’t have country-specific techno-economic data perhaps you want to match the historical years model behaviour to reality by forcing the activity using ‘Total Technology Annual Activity Upper Limit’ and ‘Total Technology Annual Activity Lower Limit’ constraints as mentioned in the calibration Lecture 5. Another example could be that you want to represent a country’s NDCs which might say that they want to invest in 10 GW of solar by 2030. To do this you could apply an investment constraints using Total Annual Min Capacity to reflect the annual investment in solar required to meet the 2030 target.
Another example could be that a country has a Net Zero emissions target by 2053, then you could apply an annual emissions limit to get to net zero by 2053.
Consequently, constraints can be used for two main things: 1. To validate a scenario (least-cost scenario i.e. a scenario with little to no constraints other than those reflecting reality or calibration) 2. To build scenarios

## Slide 5
14.2 Scenario validation
There are many different types of validation, some examples include:
Compare model outputs to historical data (e.g. Energy mix, emissions, costs)
Check whether the least-cost scenario follows known trends
Implement constraints throughout the time frame to ensure the model is realistic for that country
14.2.1 Introduction to Scenario Validation
Validation doesn't mean we can perfectly predict the future—but it ensures our model behaves reasonably and that scenarios are grounded in reality. This is essential before using the results to inform policy or investment.
Notes: This slide introduces the concept of scenario validation in OSeMOSYS, emphasizing that while models can't predict the future, validation ensures scenarios are credible and grounded in reality. Validation helps confirm that the model behaves as expected and supports trustworthy decision-making.
Validation can involve:
Comparing outputs to historical data – this is typically for the base year which was covered in the calibration Lecture 5 but can also be for all historic years if you do not have country-specific techno-economics.
Checking whether low-cost pathways reflect known trends – ensuring the model is investing and using technologies that we know are the cheapest for the sector based on the input data we entered into the model. If an expensive or unexpected technology is appearing this may indicate an issue with the data entered or the way the model is set up. Another important thing here is ensuring the model does not abruptly change to another technology. The model could do this if it is cheaper overall to simply switch to another fuel type. Although this could be cheaper it is unrealistic for a country to completely switch to a different technology than it has historically been using within a year or a few years. Therefore, the modeller must add constraints to make the switch smoother and over time.
Applying realistic constraints to ensure the scenario remains relevant for a specific country context – if you know a country has limited resources for a particular technology then it validates the model to reflect this using constraints. This list is not exhaustive.

## Slide 6
6
14.2.3 Technology Penetration Rate
There are two methods to introduce a technology penetration rate:
Total Annual Max Capacity Investment: This parameter limits the maximum new capacity that can be installed each year.
Technology Activity Increase By Mode Limit: This parameter limits the maximum percentage increase in activity that a technology can achieve each year.
A penetration rate helps prevent abrupt jumps in technology utilization.
14.2 Scenario validation
Notes: Another common behavior observed in optimization results is the sudden jump in installed capacities from one year to the next when a technology becomes significantly cheaper than another in supplying an energy service. In reality, it is nearly impossible to decommission all installed capacity of one technology in a single year to make way for a new one.
To address this, we can incorporate a technology penetration rate using two approaches:
Total Annual Max Capacity Investment: This parameter sets a limit on the maximum new capacity that can be installed each year, based on historical data and market projections. For instance, if the power mix has been growing at an average rate of 1.2 GW per year, this value or a percentage of it could be used to regulate the penetration of new technologies in future years.
Technology Activity Increase By Mode Limit: This parameter limits the annual growth in activity levels for a technology to a specified percentage. For example, if a power plant generates 20 PJ in 2023 and the parameter is set to 0.1 (10%), the maximum generation in 2024 would be capped at 22 PJ (10% of 20 is 2, so 20 + 2 = 22). The percentage increase can be derived from historical trends or sectoral reports.
By applying these parameters, we can create a more realistic representation of technology transitions in energy systems.

## Slide 7
14.2.4 Total Technology Model Period Activity Upper Limit
14.2 Scenario validation
Total maximum level of activity allowed for a technology in the entire modelled period. It represents the total reserves of fossil fuels.
Crude oil
Natural gas
Coal
Nuclear fuels
Notes: Energy systems cannot produce energy infinitely. For fossil fuels, it is crucial to specify the reserves available for each type of fuel, including crude oil, natural gas, coal, and nuclear fuels. These reserve data are typically reported in weight or volume terms and must be converted into energy units. For example, 1 million barrels of oil is approximately 6 PJ.
To represent this in the model, we use the parameter Total Technology Annual Activity Upper Limit. This parameter sets a maximum limit on energy production for the entire modelling period.

## Slide 8
14.2.5 Total Technology Annual Activity Upper Limit
14.2 Scenario validation
Total maximum level of activity allowed for a technology in one year. It represents the technical potential of energy production of a technology.
Fossil fuels
Renewables
Controlled by depletion features in each reservoir or mine.
Controlled by natural conditions of each region
This parameter is defined for primary energy technologies such as MINCOA or MINBIO.
Notes: For fossil fuels, annual energy production cannot increase disproportionately from one year to the next. Oil reservoirs and coal mines have maximum production levels dictated by their depletion characteristics. However, detailed data on these limits is often unavailable, making it difficult to calculate an accurate average for an aggregated technology representing fuel extraction.
A simple approach is to use historical production data, taking the highest value as the default for the early years of the modeling period. This maximum can then increase linearly by a reasonable percentage over time. Adjustments can also be made if there is data on the development of new reservoirs or mines expected to become commercially viable in the future.
For renewables, the annual maximum potential is determined by the region or country’s natural conditions. For example, wind speed directly impacts the energy generated by wind power plants, typically referred to as the technical potential of the energy source.
In both cases—fossil fuels and renewables—the maximum annual energy production is defined using the Total Technology Annual Activity Upper Limit parameter. We add this parameter for primary energy source technologies (e.g., MINNGS, MINCOA, MINSOL, MINHYD)

## Slide 9
14.2.6 Total Annual Max Capacity
14.2 Scenario validation
Total maximum (residual plus cumulatively new installed) capacity allowed for a technology in a specified year. Specially used for renewable power plant technologies.
This parameter is defined for power plant technologies such as PWRSOL or PWRWND.
Solar
Wind
Hydro
Geothermal
Notes: For renewable energy sources, the technical potential may sometimes be expressed in capacity units (GW) rather than energy production (PJ). For example, reports may estimate a maximum installed capacity of 30 GW for photovoltaic solar power plants. This upper limit on total possible installed capacity can be used instead of the maximum energy production discussed on the previous slide.
In such cases, the parameter Total Annual Max Capacity is used. This parameter sets a maximum limit on the total installed capacity, including both residual (pre-existing) capacity and new cumulative capacity.
It is important to note that this parameter is applied to power plant technologies, not primary energy sources.

## Slide 10
10
Lecture 14.2 References
KTH. (2018). OSeMOSYS Documentation. https://osemosys.readthedocs.io/en/latest/index.html#
Plazas-Niño, F. (2024). Step-by-Step Guide to National Energy System Modelling with OSeMOSYS (v1.0). Zenodo. https://doi.org/10.5281/zenodo.13883416

## Slide 11
11
14.3.1 Example of energy scenarios
14.3 Introduction to scenario design
Source: IEA, 2023
STEPS: Stated Policies Scenario
APS: Announced Pledges Scenario
NZE: et Zero Emissions by 2050 Scenario
Notes: This slide illustrates the role of energy scenarios in understanding potential transitions in the global energy mix, based on the International Energy Agency's (IEA) World Energy Outlook 2023. It presents three scenarios—STEPS (Stated Policies Scenario), APS (Announced Pledges Scenario), and NZE (Net Zero Emissions by 2050 Scenario)—which reflect different trajectories for energy supply and demand based on varying policy commitments and climate goals. Each scenario shows projected shares of key energy sources from 2022 to 2050, emphasizing the shifts in the global energy landscape under different assumptions about government actions and technological advancements.
The STEPS scenario assumes current policies and commitments remain unchanged, leading to a gradual decline in the use of coal and oil, while natural gas, electricity, and modern renewables grow modestly. The APS scenario assumes the implementation of all announced pledges, resulting in a steeper decline in coal and oil, alongside more significant growth in electricity and modern renewables. Finally, the NZE scenario demonstrates an aggressive path to achieve net-zero emissions by 2050, showing a dramatic increase in modern renewables and hydrogen-based fuels, coupled with a sharp reduction in fossil fuels (oil, coal, and natural gas). This comparative approach helps policymakers and planners assess the implications of different levels of ambition in transitioning to a sustainable energy future.

## Slide 12
12
14.3.2 Scenario design process
Problem formulation / Policy question
Definition of storyline – Description of the general assumptions for the scenario
Quantification of specific parameters for modelling
Source: Adapted from Witt et al. (2020)
Decision-makers and stakeholders engagement
Iterative feedback and validation
14.3 Introduction to scenario design
Notes: The energy scenario design process is a structured framework that integrates various elements to develop meaningful and actionable scenarios for energy planning. It begins with problem formulation or policy questions, where the key challenges or objectives driving the scenario are clearly identified. This step is critical as it defines the focus of the scenario, such as reducing emissions, improving energy security, or achieving specific policy targets. Following this, the definition of the storyline takes place, where general assumptions about socioeconomic trends, policy commitments, technological developments, and other key drivers are established. This narrative provides the foundation for the scenario, offering a coherent vision of how the future might unfold under certain conditions. In OSeMOSYS, scenarios are used to explore how different assumptions and drivers shape the future of an energy system. A new scenario can designed based on a range of things, including existing or hypothetical policies such as emission targets, subsidies, or technology bans; technological developments like breakthroughs in storage or renewable energy; shifts in economic conditions, such as changes in fuel prices or GDP growth; and behavioural or structural changes, including demand patterns or trends toward electrification. These variations help users understand the implications of different future pathways and support more informed energy planning and decision-making.
The next stage involves the quantification of specific parameters for modeling, where the assumptions from the storyline are translated into concrete inputs for energy system models. These parameters include variables such as energy demand, technology costs, and resource availability, which are fed into computational tools to produce quantitative results. Throughout the process, engagement with decision-makers and stakeholders ensures that the scenarios are relevant, credible, and aligned with real-world needs. Additionally, iterative feedback and validation loops are essential, allowing for refinement and adjustments as new data, insights, or feedback emerge. This comprehensive approach ensures that the scenarios are robust and useful for guiding policy and strategic decisions.

## Slide 13
Problem formulation / Policy question
Definition of storyline – Description of the general assumptions for the scenario
Quantification of specific parameters for modelling
13
15.3.3 Example of scenario design
Eighty-five percent of the urban population has access to natural gas for cooking service. Domestic production of natural gas is declining quickly, and imports threaten affordability for most of the population. What alternatives are possible to address the risk of losing energy access for cooking and heating?
Under a constant depletion of natural gas reserves, urban residential cooking demand must progressively migrate to alternative fuels. This scenario analyzes the competition between three options: imported natural gas, LPG, and electricity, for supplying cooking demand in the next 25 years.
Natural gas reserves: 750 PJ
Annual LPG supply: 54 PJ
Unconstrained imports of natural gas (price 15.6 USD/GJ)
Domestic market prices for stoves
14.3 Introduction to scenario design
Notes: This slide illustrates a basic example of how the energy scenario design process can be applied to address a specific policy question. The problem formulation focuses on the risks associated with a declining domestic supply of natural gas, which currently serves 85% of the urban population for cooking. With imports becoming less affordable, the central question is: What alternatives are available to ensure continued access to energy for cooking and heating? This step establishes the context and identifies the key issue driving the scenario analysis.
The definition of the storyline assumes a constant depletion of natural gas reserves, requiring urban residential cooking demand to shift toward alternative fuels. This scenario explores three potential options—imported natural gas, liquefied petroleum gas (LPG), and electricity—as competing solutions for supplying cooking energy over the next 25 years. Quantification of specific parameters is then carried out, with specific inputs for modelling: natural gas reserves are set at 750 PJ, annual LPG supply at 54 PJ, and unconstrained imports priced at 15.6 USD/GJ. Domestic market prices for stoves are also included to assess affordability. It is important to note that this example is designed for teaching purposes and does not incorporate two critical aspects of real-world scenario design: stakeholder engagement to ensure relevance and iterative feedback to refine assumptions and validate results. Even the smallest change in model inputs—like a slight adjustment in fuel cost or technology efficiency—can create a new scenario with significantly different outcomes. When building just a few scenarios, they should be relevant, well-justified, and plausible, reflecting realistic futures. However, when running many scenarios, such as in a sensitivity analysis, the goal shifts to exploring a range of possible outcomes, helping to understand uncertainty and identify robust strategies.

## Slide 14
14
15.3.4 Modelling scenarios with OSeMOSYS
Depending on the scope of the OSeMOSYS model, multiple scenarios can be designed. The most common scenarios include:
Least-Cost Scenario
Business-as-Usual Scenario
Renewable Target Scenario
Emission Limit Scenario
Carbon Tax Scenario
Energy Efficiency Scenario
Electrification Target Scenario
14.3 Introduction to scenario design
Notes: OSeMOSYS is very flexible in designing a variety of energy scenarios. Depending on the scope and resolution of the model—whether temporal, geographical, or technological—different scenarios can be created to address specific policy questions and planning needs.
Some of the most common scenarios modelled with OSeMOSYS include the Least-Cost Scenario, which identifies the most cost-efficient way to meet energy demand; the Business-as-Usual Scenario, which projects future energy systems based on current policies and trends; and the Renewable Target Scenario, which simulates pathways to achieve specific renewable energy deployment goals. Other examples include the Emission Limit Scenario, which restricts greenhouse gas emissions, and the Carbon Tax Scenario, which incorporates the impact of carbon pricing. Scenarios like the Energy Efficiency Scenario and the Electrification Target Scenario explore the effects of improving energy efficiency and accelerating electrification, respectively. These scenarios enable decision-makers to evaluate trade-offs, compare outcomes, and design strategies that align with national or global energy goals. In next section, we will explore the main assumptions to model these scenarios.

## Slide 15
15
Lecture 14.3 References
Grunwald, A., Dieckhoff, C., Fischedick, M., Hoffler, F., Mayer, C., Weimer-Jehle, W. (2016). Consulting with energy scenarios: Requirements for scientific policy advice. Monograph Series on Science-based Policy Advice. acatech – Deutsche Akademie der Technikwissenschaften e. V., München.
IEA. (2023). World Energy Outlook 2023. https://www.iea.org/reports/world-energy-outlook-2023
Witt, T., Dumeier, M., & Geldermann, J. (2020). Combining scenario planning, energy system analysis, and multi-criteria analysis to develop and evaluate energy scenarios. Journal of Cleaner Production, 242. https://doi.org/10.1016/j.jclepro.2019.118414

## Slide 16
16
14.4.1 Least-cost scenario
14.4 Developing energy scenarios
This is the scenario we can run immediately after calibrating the model. It represents the least-cost pathway for developing the energy system.
No additional assumptions are made in the modelling of this scenario.
Notes: A Least-Cost Scenario represents the optimal development of the energy system from a purely economic perspective, identifying the cheapest way to meet energy demands over a specified time horizon. After calibrating the model with baseline data and ensuring all parameters are accurate, this scenario is run without imposing additional constraints, such as emission limits, renewable energy targets, or policy preferences. All available technologies compete freely based on their costs, including capital, operation, maintenance, and fuel costs. The model selects the most cost-effective mix of technologies and resources to satisfy energy demands, considering factors such as system efficiency and lifecycle costs. While this scenario provides insights into the most economical pathway, it does not account for externalities such as environmental impacts, social considerations, or policy objectives. As a result, it often serves as a benchmark to compare with more constrained or policy-driven scenarios, highlighting the trade-offs between cost and other priorities, such as sustainability or energy security.
No additional assumptions are made in the modelling of this scenario.

## Slide 17
17
14.4.2 Business-as-usual (BAU) scenario
14.4 Developing energy scenarios
A BAU scenario represents the future energy system based on existing trends, policies, and technologies without additional interventions.
The main assumption is that the current shares of the principal technologies are maintained throughout the modelling horizon. The parameter used is the Total Technology Annual Activity Lower Limit.
Example: Let’s assume that biomass supplies 60% of the cooking service in 2021 as the calibration year. We will set the Total Technology Annual Activity Lower Limit to 60% of the cooking demand for each year from 2022 to the end of the modeling horizon.
 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028
Lower Limit - Biomass stove | 60 | 66 | 72 | 78 | 84 | 90 | 96 | 102
Cooking demand | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170
Notes: A Business-as-Usual (BAU) Scenario represents a pathway of the future energy system based on current trends, policies, and technologies, without assuming any additional interventions or changes beyond those already in place. It serves as a reference scenario that reflects what would likely happen if no new policies, technological advancements, or behavioral shifts are introduced to address emerging challenges, such as climate change or energy security. The BAU scenario is useful for identifying potential gaps or issues in achieving long-term goals, as it highlights the consequences of maintaining the status quo. This scenario is usually used as a baseline scenario. By comparing the BAU scenario with alternative scenarios, such as those targeting emissions reductions or increased renewable energy deployment, policymakers can better understand the scale and urgency of actions needed to achieve desired outcomes.
In this scenario, the main assumption is that the current shares of the principal technologies are maintained throughout the modelling horizon. For example, if hydropower plants supply around 75% of electricity production in the calibration years, we can impose a lower activity limit for hydropower technology to ensure it produces at least 75% of electricity in subsequent years. Similarly, lower activity limits can be added for the most relevant technologies in each sector.

## Slide 18
18
14.4.3 Renewable target scenario
14.4 Developing energy scenarios
This scenario explores pathways to achieve specific renewable energy deployment goals within an energy system.
To set targets for renewable energy production, we use a User Defined Constraint (UDC). The general equation is as follows:
Example:
Notes: A Renewable Target Scenario explores pathways to achieve specific goals for renewable energy deployment within an energy system. This scenario assumes that policies, incentives, or mandates are implemented to increase the share of renewables—such as solar, wind, hydropower, or biomass—in the energy mix. The scenario typically models the investments, technological advancements, and infrastructure changes needed to meet predefined targets, such as generating 50% of electricity from renewables by a certain year. By examining the feasibility and impacts of achieving renewable energy targets, this scenario helps policymakers and stakeholders evaluate the measures required to transition to a cleaner and more sustainable energy system.
In this scenario, we represent the targets using a User Defined Constraint (UDC). Assuming that X% of electricity production must be supplied by renewable sources, we can formulate the equation shown on the slide. Note that the activity of transmission is converted into electricity from power plants by multiplying it by the input activity ratio. In the example, we include three renewable power plants, with the target set at 40%.

## Slide 19
19
14.4.4 Emission limit scenario
14.4 Developing energy scenarios
This scenario evaluates pathways for energy systems to meet specific GHG emission caps.
The Annual Emission Limit parameter is used to define the desired emission levels for a single year or across multiple years.
Example: Let’s assume the goal is to achieve carbon neutrality by 2040, with a gradually decreasing carbon budget starting from 2030. The Annual Emission Limit parameter would be defined as follows:
 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Annual Emission Limit | 999999 | 999999 | 999999 | 999999 | 999999 | 170 | 168 | 152 | 125 | 110 | 92 | 79 | 55 | 32 | 21 | 0
Notes: An Emission Limit Scenario models the development of an energy system under the constraint of a specific cap on greenhouse gas (GHG) emissions. This scenario explores how the energy mix and technology choices must adjust to meet a defined emissions reduction target, which could be based on national climate goals, international agreements (e.g., the Paris Agreement), or sector-specific policies. The emission limit acts as a binding constraint within the model, forcing the selection of low-carbon technologies, energy efficiency measures, and cleaner fuels, even if they are not the most cost-effective options in the absence of such constraints.
In this scenario, we set the emission limit using the Annual Emission Limit parameter. This can be applied to a specific year or across multiple years, effectively replicating the concept of a carbon budget. Additionally, this approach is useful for representing Net Zero Scenarios by setting the limit to zero for a particular year or series of years.

## Slide 20
20
14.4.5 Carbon tax scenario
14.4 Developing energy scenarios
This scenario examines pathways for energy systems constrained by carbon taxes.
The Emission Penalty parameter is used to define the carbon tax or price, applicable for a single year or across multiple years.
Example: Let’s assume a linear growth in carbon tax from US$12 per tCO2 in 2021 to US$30 per tCO2 by 2030. The Emission Penalty parameter would be defined as follows:
 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Emission Penalty | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30
Notes: A Carbon Tax Scenario models the impact of placing a price on greenhouse gas (GHG) emissions, effectively incentivizing a shift toward cleaner energy sources and technologies. In this scenario, a carbon tax is applied to each unit of emissions, typically measured in monetary terms per ton of CO₂ equivalent. This tax increases the costs of fossil fuel-based technologies and processes, encouraging the adoption of low-carbon alternatives such as renewables, energy efficiency measures, and electrification.
To incorporate this element into our scenario, we can use the Emission Penalty parameter. This parameter reflects the effect of a carbon price or tax by assigning a cost per unit of emissions per year.

## Slide 21
Final electricty use
Electricity after distribution (ELC003)
Final electricty use
21
14.4.6 Energy efficiency scenario
14.4 Developing energy scenarios
This scenario evaluates the evolution of the energy system with the implementation of energy efficiency measures.
The strategy involves creating new technologies that represent efficiency improvements through better input activity ratios but higher capital costs.
Example: One technology with standard efficiency will consume the expected amount of electricity but the second technology with higher efficiency will consume less electricity.
Standard efficiency appliances
IAR: 1 | Cost: 100 USD/kW
Standard efficiency appliances
IAR: 0.95 | Cost: 150 USD/kW
Electricity after distribution (ELC003)
100 PJ
100 PJ
95 PJ
100 PJ
Notes: An energy efficiency scenario refers to a modelled pathway that outlines how energy efficiency measures or improvements will be implemented and their impact on energy consumption, costs, and related environmental outcomes over time. It is typically used in energy planning and policy-making to assess how energy-saving technologies, behaviors, or policies can reduce overall energy demand.
In OSeMOSYS, energy measures can be represented in various ways. One key approach is to create additional technologies that meet energy demand while using less input fuel. For example, to address electricity demand, we can introduce virtual technologies that represent efficiency improvements by modifying the Input Activity Ratio (IAR). This could involve one technology with standard efficiency (i.e., IAR = 1) and another with improved efficiency (i.e., IAR = 0.95, representing an approximate 5% efficiency gain). It is important to define a capital cost for this efficiency improvement. Additionally, this can be disaggregated to account for specific energy demands, such as refrigerators or air conditioning, where efficiency plays a critical role.

## Slide 22
22
14.4.7 Electrification target scenario
14.4 Developing energy scenarios
This scenario explores pathways to achieve specific electrification goals within an energy system.
To set targets for electrification of energy demands, we use the Total Technology Annual Activity Lower Limit parameter.
Example: Let’s assume the goal is to achieve a 5% electrification of car transport demand by 2030. Given that the final transport demand is known, we will apply a progressive percentage of electrification to the service starting from 2021. The data would be as follows:
 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Lower Limit - Electric cars (Gpkm) | 0.205 | 0.45 | 0.705 | 0.98 | 1.4 | 1.74 | 2.135 | 2.6 | 3.15 | 3.65
Total car transport demand (Gpkm) | 41 | 45 | 47 | 49 | 56 | 58 | 61 | 65 | 70 | 73
Electrification percentage | 0.5% | 1.0% | 1.5% | 2.0% | 2.5% | 3.0% | 3.5% | 4.0% | 4.5% | 5.0%
Notes: An electrification target scenario explores pathways that outline the transition from fossil fuel-based energy sources to electricity as the primary energy source in various sectors of the economy, such as transportation, heating, and industry. This scenario typically sets specific targets for the amount of energy currently provided by non-electric sources (e.g., natural gas, oil, coal) to be replaced by electricity over a given period. This approach can also be applied to clean cooking targets.
Similar to the Business-as-Usual (BAU) scenario, we can use the Total Technology Annual Activity Lower Limit parameter. Based on the final energy demand and the target to be achieved, we can calculate the expected activity of electric technology for specific years. This desired activity level will then be set as the lower limit for the relevant technology. For example, if the low heat demand is 85 PJ in 2030, and the target is to electrify this service by 20% by 2030, we can establish that 85 × 0.2 = 17 PJ. Therefore, 17 PJ would be the Total Technology Annual Activity Lower Limit for electric boiler technology in 2030.

## Slide 23
23
Lecture 14.4 References
KTH. (2018). OSeMOSYS Documentation. https://osemosys.readthedocs.io/en/latest/index.html#

## Slide 24: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Fernando Plazas-Niño, Leigh Martindale