## Slide 1
Assessing power system flexibility with IRENA FlexTool
LECTURE 6
MODELLING FLEXIBILITY OPTIONS II

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO1: Understand how to model demand response measures.
ILO2: Understand how to model power to heat and heat network.
ILO3: Understand how to model power to hydrogen and hydrogen network.
ILO4: Understand how to model power to electric vehicles.

## Slide 3
3
6.1.1 Understanding demand-side flexibility
6.1 Demand response
How demand response works?
Step 1
Energy user signs up to voluntarily set up reduce energy usage in times of extreme demand.
Step 2
Electricity demand surges.
Step 3
User reduces its energy consumption based on the event received from aggregator.
Step 4
Reduced demand helps stabilize grid.
Step 5
Users are paid incentive for reducing the load.
Notes: Demand response (DR) plays a key role in power system flexibility by adjusting electricity consumption patterns in response to grid conditions, market prices, or system needs. Instead of only relying on generation to follow demand, DR allows demand to follow supply, which becomes increasingly important in systems with high shares of variable renewable energy (VRE).
From a flexibility perspective, DR can:
Reduce peak demand – Shifting or shedding loads during high-demand periods lowers the need for expensive peaking plants and reduces grid stress.
Absorb surplus generation – Increasing consumption when renewable output is high (e.g., running industrial processes or charging EVs during sunny/windy periods) prevents curtailment.
Provide fast balancing services – Certain DR resources can respond within seconds or minutes, offering frequency regulation, spinning reserve, and other ancillary services.

## Slide 4
4
6.1.2 Parameterization
6.1 Demand response
a) In FlexTool demand response is defined as a generator in the “unit_type” sheet:
Demand response increase: Generator with negative price, empty discharging efficiency and a charging efficiency
Demand response decrease: Generator with positive price, discharging efficiency and no charging efficiency
b) The Capacity of demand response should be defined in the “units” sheet:
Demand increase: negative capacity
Demand decrease: positive capacity
a
b
Notes: In FlexTool, demand response is defined as a generator. Therefore its characteristic should be defined in the “unit_type” sheet. Since demand response is modelled as a generator, it is moved to the other side of the demand-supply balance, and reverse signs should be used. Demand response increase is defined as a generator with a negative price, empty discharging efficiency and a charging efficiency. Demand response decrease is defined as a generator with a positive price, discharging efficiency and no charging efficiency. Demand can respond instantaneously to signals from the grid; therefore, the ramp-up and down rates can be set to 1.
Like other generator units, the demand response capacity should be defined in the “units” sheet with a negative value for demand increase and a positive value for demand reduction.

## Slide 5
5
Lecture 6.1 References
IRENA. 2019. IRENA FlexTool Modelling different flexibility options. International Renewable Energy Agency, Abu Dhabi. https://www.irena.org/-/media/Irena/Files/IRENA-flextool/IRENA_FlexTool_FlexibilityOptions.pdf

## Slide 6
6
6.2.1 Power to heat
6.2 Modelling power to heat
Heat grid
Power to heat devices, e.g., Heat pump, electric boiler:
Defined the same as a generator but in heat grid
Other heating devices, e.g., gas boiler or solar thermal:
Defined the same as a generator but in heat grid
Heat Demand
Thermal storage
Define the demand profile in “ts_energy” sheet
It represents heat demand in the system
Defined the same as electricity storage but in heat grid
Usually it has the property: “self-discharge loss”
Power grid
Natural gas, hydrogen grid, or renewable sources
Electric heat generator
Non- Electric heat
generator
Notes: In lecture two, it was discussed that a heating system composed of a heat pump and thermal storage could provide flexibility to the power system. This is done by generating heating when there is abundant renewable in the system and electricity prices are low. Power can be stored in the thermal storage and used at a later stage to cover heat demand when variable renewable generation is low or electricity prices are high. In this lecture, we discuss how to represent the power to heat flexibility option in FlexTool. In FlexTool every demand service is represented as a grid consisting of demand for that service, the heat generator units and thermal storage units. Therefore the first step in defining the power to heat flexibility option in FlexTool is to define a heat grid. Like the power grid, the heat grid is composed of heat demand, electric and non-electric thermal generating units, and thermal storage units.
First, you should add heat demand and define the heat grid. The power and heat sector coupling then takes place through electric heating units that convert power to heat. Heat generating units are defined in the same way as power generating units. The main difference is that their input grid is the power grid, and their output grid is the heat grid. In FlexTool the output heat is supplied to a heat grid which will either supply heat demand or is stored in thermal storage units. For non-electric heating units, the input grid can be a gas grid or renewable sources (set as fuel). The thermal storage units are also defined the same way as power storage units, but in this case, so their input and output are to the heat grid.

## Slide 7
7
6.2.2 Modelling heat demand
6.2 Modelling power to heat
To define a heat network:
The heat grid should be defined in the “gridNode” sheet. Please note that same as the power grid, the heat grid can be represented by a single node, multiple nodes, or only cover a certain region.
The heat node group can be defined in the “nodeGroup” on the heat grid to specify the network characteristics.
The temporal profile of heating demand should be added in the “ts_energy” sheet.
c
a
b
Notes: To define a heat network: First, you should define a heat grid in the “gridNode” sheet. Same as the power grid, the heat grid can be represented by a single node, multiple nodes, or only cover a certain region. Then you should specify the total demand at each node. As explained in the case of the power grid, if you use more than one node, the transmission link between the nodes should be specified in "nodeNode" sheet. You can also define a node group for heating in the “nodeGroup” sheet and use it to set parameters for the whole heat grid. Finally, you should add the temporal profile of heating demand in the “ts_energy” sheet.

## Slide 8
8
6.2.3 Modelling heat pumps
6.2 Modelling power to heat
b2.1
b2.2
b1
Defining heat pump is same as power generators with some differences:
a) In the “units” sheet electricity should be set as input grid and heat as output grid
b) In the “unit_type” sheet there are two ways to define heat pump efficiency:
  1. Static efficiency : Defined directly as “conversion eff”
  Or
  2. Dynamic efficiency :
  2.1 Activate option “use efficiency time series” in the “units” sheet
  2.2 Define efficiency time series in the “ts_unit” sheet
Notes: Defining heat pumps is the same as power generators, and the input parameters should be defined in both “unit_type” and “units” sheets. However, in the case of heat pumps, there are some differences. The first difference is that since a heat pump converts electricity to heat, in the “units” sheet, electricity should be set as input grid and heat as the output grid. The other point about a heat pump is that its efficiency varies with the outside temperature. Therefore, there are two ways to define heat pump efficiency. The first option is to use static efficiency. This can be easily defined by setting an average value for heat pump performance to “conversion eff”. The second option is to use dynamic efficiency by activating the option “use efficiency time series” in the “units” sheet and then specify efficiency time series in the “ts_unit” sheet.

## Slide 9
9
6.2.4 Modelling CHP units
6.2 Modelling power to heat
CHP
Electricity
Heat
Fuel
There is a relationship between heat () and electricity ( output of a CHP plants, being one of the outputs limiting the other. The relationship can be defined as:
Inequality constraints:
and
Equality constraint :
Notes: A combined heat and power (C.H.P.) unit is a generator that can produce both heat and electricity. Technical characteristics should be defined in the “unit_type” sheet as with any other generator. Then in the “units” sheet, you should define output one as electricity and output two as heat. There is typically a relationship between the heat and electricity output of a C.H.P. unit, as one output will limit the other. The relationship between the two outputs can be defined as equality or inequality constraints. The user-defined coefficients of these equations should be added to the "units" sheet as shown here.

## Slide 10
10
6.2.5 Modelling concentrated solar power
6.2 Modelling power to heat
CSP grid
Power grid
CSP generator
(Heat to power)
CSP Collector
CSP Storage
Solar availability time series in “ts_cf”
Same as solar PV generator but in CSP grid
Same as electricity storage but in CSP grid
Modelled same as a heat pump but heat is converted to electricity in this case
Concentrated solar power (CSP) units is defined as a single node grid with zero demand in “gridNode”.
Notes: To model concentrated solar power (C.S.P.), the same steps as the heat grid should be followed. The whole C.S.P. units are defined as a single node grid with zero demand in the “gridNode” sheet.
The C.S.P. grid consists of the following:
Solar as fuel and its availability which is set in the “ts_cf” sheet,
C.S.P. collector as a generator which defined in “unit” and “unit_type” sheets.C.S.P. storage which is the same as storage units in power and heat grids and is defined in the “unit” and “unit_type” sheet
And finally, C.S.P. generator that is modelled the same as a heat pump, but in this case, heat is converted to electricity; therefore, it is a power generator unit.

## Slide 11
11
11
Lecture 6.2 References
IRENA. 2019. IRENA FlexTool Modelling different flexibility options. International Renewable Energy Agency, Abu Dhabi. https://www.irena.org/-/media/Irena/Files/IRENA-flextool/IRENA_FlexTool_FlexibilityOptions.pdf

## Slide 12
12
6.3.1 Power to hydrogen
6.3 Modelling power to hydrogen
Hydrogen grid
Power to hydrogen units, Fuel cell and electrolyser:
Defined the same as a generator but in hydrogen grid
Other hydrogen generating units such as SMR:
Defined the same as a generator but in hydrogen grid
Hydrogen Demand
Hydrogen storage
Define the demand profile in the “ts_energy” sheet
It represents hydrogen demand in system
Defined the same as electricity storage but in hydrogen grid
In FlexTool a hydrogen network with different nodes could also be modelled
Power grid
Natural gas
Notes: As was mentioned in previous lectures, different end-use services are modelled as different grids in FlexTool. Therefore, in order to model the power to hydrogen flexibility option, first, you need to define a hydrogen grid. Like other power and heat networks, the hydrogen grid consists of hydrogen demand, hydrogen storage technologies, and hydrogen generation units. The demand for hydrogen can originate from different sectors such as industry, mobility, heating demand, aviation, etc. Like electricity, hydrogen is versatile in its production and can be produced from various resources. The interaction between the power grid and hydrogen grid takes place through two key technologies: electrolysers that absorb electricity and convert it to hydrogen; and Fuel Cells that absorb hydrogen and convert it back to electricity. One of the key benefits of hydrogen is that it can be stored at a large scale using cheap gas storage technologies such as underground caverns, which is currently much cheaper than storing power in batteries. Therefore the abundant renewable in the power grid can be converted to hydrogen and stored over a long period.

## Slide 13
13
6.3.2 Modelling hydrogen grid
6.3 Modelling power to hydrogen
a
b
c
To model a hydrogen grid:
Define a grid in the “gridNode”.
Add hydrogen to the “nodeGroup” .
Add hydrogen demand to the “ts_energy”.
To add hydrogen grid in more than one node, the connection between the nodes should be defined in the “nodeNode”.
Notes: The first step to model a hydrogen grid in FlexTool is to define a hydrogen grid in the “gridNode” sheet and specify the total demand and import-export if there is any. If the hydrogen grid is available in different nodes of a region, it should be defined for different nodes. Then a node group for hydrogen should be defined in the “nodeGroup” sheet. Finally, the hydrogen demand profile at each node should be added to the “ts_energy sheet”. Please note that if the hydrogen grid is available in more than one node, the connection between the nodes should be defined in the “nodeNode” sheet.

## Slide 14
14
6.3.3 Hydrogen generation and storage units
6.3 Modelling power to hydrogen
a
b
Add hydrogen generation/storage units in the “unit_type” and add the main characteristics.
  For hydrogen storage the inv.cost /kW should be set to zero.
Add the units to “unit” sheet and define the output grid as hydrogen.
  For electrolyser the input network should be set to electricity.
  For hydrogen storage the storage capacity should be specified.
0.7
Notes: Modelling hydrogen generation/storage units is the same as power generators. First, the units should be defined in the "unit_type" sheet, and their main characteristics, such as efficiency, investment cost, and so on, should be specified. One important point is that, with hydrogen storage, the investment cost per KW should be set to zero, and the "fixed KW over KWh ratio" does not need to be specified. All the units should then be added to the "unit" sheet, and their capacity should be defined. The storage capacity should also be specified for hydrogen storage units. For all the hydrogen/storage units, the output grid should be set as the hydrogen grid. For electrolyser, the input network should be set to electricity.

## Slide 15
15
Lecture 6.3 References
IRENA. 2019. IRENA FlexTool Modelling different flexibility options. International Renewable Energy Agency, Abu Dhabi. https://www.irena.org/-/media/Irena/Files/IRENA-flextool/IRENA_FlexTool_FlexibilityOptions.pdf

## Slide 16
16
6.4.1 Power to EV
6.4 Modelling power to EV
  EVs as predefined demand profiles that are added on top of the original demand curve.
  The three key EV charging scenarios are:
  Evening uncontrolled charging: EVs will charge at maximum power as soon as they are plugged into to the grid, mostly during evening hours.
  Night controlled charging: Charge is distributed during the night and coincides with wind availability and low power demand
  Day controlled charging: Charge coincides with the solar PV profile
a
b
c
Source: IRENA (2019)
Notes: The third sector coupling alternative is facilitated through the electrification of transport with electric vehicles. Electric vehicles can have different charging strategies. The simplest one is uncontrolled charging, in which an E.V. will charge at maximum power as soon as they are plugged into the grid, mostly during evening hours. However, uncontrolled charging is not flexible and can pose a challenge to the power system and increase flexibility requirements of the system if the number of connected electric vehicles is high.
On the other hand, when charged smartly, electric vehicles can provide demand-side flexibility to the system by optimising the charging process according to distribution and transmission grid constraints and local availability of renewable energy sources. Two of the key smart charging strategies are:
Night controlled charging, in which charge is distributed during the night and coincides with wind availability and low power demand.
Day controlled charging, in which charge coincides with the solar PV profile.
The demand for mobility in each strategy should be estimated, and the predefined demand profiles should be added in the “ts_energy” sheet in FlexTool.

## Slide 17
17
6.4.1 Modelling EV
6.4 Modelling power to EV
Electro-mobility grid
Demand
Reserve
Define the demand profile in the “ts_energy” sheet.
This demand represents discharge of battery for mobility.
This demand is estimated and projected over the planning horizon and should be added as input.
Defined reserve profile in the “ts_reserve” sheet.
This is used to represent the amount of EVs that are connected to grid in a time period.
Power grid
Discharge
Charge
Ancillary services
Simultaneity factor:represents the share of electric vehicles (EVs) that are simultaneously available and active for charging or discharging at a given time
Notes: Like other end-use services, to define power to E.V. in FlexTool, you should first define an Electro-mobility grid. An electro-mobility grid can be a single node or multiple node grid. The next step is to estimate and project demand for mobility and electric vehicles over the planning horizon in different nodes on the grid. You can use other software for this. Then you should define the demand for mobility in the “ts_energy” sheet. This demand represents the discharge of the battery for mobility. There are three options for defining electric vehicles in FlexTool. Option one is unidirectional charging based directly on demand for mobility. In this option, there is only one direction charge in which the charger converts grid electricity to electric vehicles. Option two is unidirectional charging with a flexible charging schedule. In this option, the charger converts grid electricity to electric vehicles, and the battery provides a temporal shift in the charging schedule. Option three is bidirectional charging with a flexible charging schedule. In this option, one charger converts grid electricity to electric vehicles. The battery provides a temporal shift in the charging schedule. In this case, there is also another charger that converts energy from the Electro-mobility grid (electric vehicles) back to the electricity grid. In the FlexTool package, an example case with electric vehicles is included in the input file named template-EVs. The users are encouraged to review how an E.V. grid is implemented in that case study.

## Slide 18
18
Lecture 6.4 References
IRENA. 2019. IRENA FlexTool Modelling different flexibility options. International Renewable Energy Agency, Abu Dhabi. https://www.irena.org/-/media/Irena/Files/IRENA-flextool/IRENA_FlexTool_FlexibilityOptions.pdf

## Slide 19: Thank you
www.climatecompatiblegrowth.com