## Slide 1: Saving energy and making your business more energy efficient:
10 easy steps for SMEs
Notes: Saving energy and making your business more energy efficient: 10 easy steps for SMEs
This project has received funding from the European Union’s Horizon Programme for Research and Innovation (2021-2027) under grant agreement No 101075596. Responsibility for this material’s content lies solely with the Every1 project and does not necessarily reflect the opinion of the European Union. The presentation is licensed CC BY-SA 4.0, unless otherwise stated.

## Slide 2: Introduction
Every business uses a range of equipment which needs electricity - whether it's lighting, computers, machinery, or AC systems. For small to medium enterprises (SMEs), electricity costs can represent a significant share of the operating budget, and inefficient consumption can negatively affect both profitability and resource management.
When you're managing an SME, you may wonder what kinds of technologies or activities might help you save energy. A key consideration will be cost and where to focus investment to make your business more efficient.
Notes: Every business uses a range of equipment which needs electricity - whether it's lighting, computers, machinery, or AC systems. For small to medium enterprises (SMEs), electricity costs can represent a significant share of the operating budget, and inefficient consumption can negatively affect both profitability and resource management.
When you're managing an SME, you may wonder what kinds of technologies or activities might help you save energy. A key consideration will be cost and where to focus investment to make your business more efficient.

## Slide 3: Contents
In this short presentation we'll explore:
How to better understand your energy consumption, and why this is important.
The benefits of making your business's energy consumption more efficient.
10 possible steps to save energy and make your business more efficient.
Each step begins with a reflective question. Take a moment to consider each question, before moving on.
Notes: In this short presentation we'll explore:
How to better understand your energy consumption, and why this is important.
The benefits of making your business's energy consumption more efficient.
10 possible steps to save energy and make your business more efficient.
Each step begins with a reflective question. Take a moment to consider each question, before moving on.

## Slide 4: 10 easy steps to save energy and make your business more energy efficient
Getting started: What do I need to know?
Getting started: What are the benefits of being more energy efficient?
Conduct an energy audit
Install a smart meter
Calculate appliance energy use
Explore more efficient energy use
Increase the energy efficiency of your equipment
Optimise your heating and cooling systems
Encourage energy saving practices amongst employees
Explore some further resources
Notes: 10 easy steps to save energy and make your business more energy efficient
Getting started: What do I need to know?
Getting started: What are the benefits of being more energy efficient?
Conduct an energy audit
Install a smart meter
Calculate appliance energy use
Explore more efficient energy use
Increase the energy efficiency of your equipment
Optimise your heating and cooling systems
Encourage energy saving practices amongst employees
Explore some further resources

## Slide 5: Step 1: Getting started: What do I need to know?
What do I need to know to get started?
Notes: Step 1: Getting started: What do I need to know?
What do I need to know to get started?

## Slide 6: Step 1: Getting started: What do I need to know about consuming energy?
It is important to understand how and when you are consuming energy. This enables you to:
Make informed decisions.
Identify patterns of how and when energy is being used.
Make changes to optimise your energy usage. This can improve energy efficiency, reduce costs, and contribute to sustainability efforts.
Understand what equipment uses the most energy and why. You can then prioritise improvements or upgrades for the most significant savings.
Notes: Step 1: Getting started: What do I need to know?
It is important to understand how and when you are consuming energy. This enables you to:
Make informed decisions.
Identify patterns of how and when energy is being used.
Make changes to optimise your energy usage. This can improve energy efficiency, reduce costs, and contribute to sustainability efforts.
Understand what equipment uses the most energy and why. You can then prioritise improvements or upgrades for the most significant savings.

## Slide 7: Step 1: Getting started: What do I need to know about electricity demand?
How do I understand how and when we’re consuming energy?
Identify your electricity demand patterns. Are you using:
  Energy-intensive equipment?
  Peak or off-peak electricity?
  Inefficient practices?
Read The Energy Trust’s A guide to energy efficiency in the workplace.
Notes: Step 1: Getting started: What do I need to know?
How do I understand how and when we’re consuming energy?
Identify your electricity demand patterns. Are you using:
  Energy-intensive equipment?
  Peak or off-peak electricity?
  Inefficient practices?
Read The Energy Trust’s A guide to energy efficiency in the workplace.
https://energysavingtrust.org.uk/a-guide-energy-efficiency-in-the-workplace/

## Slide 8: Step 1: Getting started: What do I need to know? What are my options?
Now that I understand how and when we’re consuming energy, what are my options?
Make small adjustments: like using high-energy equipment during off-peak hours, upgrading to energy-efficient appliances or optimising lighting.
Use smart digital tools and devices: to understand and manage energy consumption and costs.
Think longer-term: plan for switching to more energy-efficient infrastructure, machinery or building technology.
Explore tools and funding opportunities.
Notes: Step 1: Getting started: What do I need to know?
Now that I understand how and when we’re consuming energy, what are my options?
Make small adjustments: like using high-energy equipment during off-peak hours, upgrading to energy-efficient appliances or optimising lighting.
Use smart digital tools and devices: to understand and manage energy consumption and costs.
Think longer-term: plan for switching to more energy-efficient infrastructure, machinery or building technology.
Explore tools and funding opportunities.

## Slide 9: Step 2: Getting started: What are the benefits of being more energy efficient?
What are the benefits of being more energy efficient?
Notes: Step 2: Getting started: What are the benefits of being more energy efficient?
What are the benefits of being more energy efficient?

## Slide 10: Step 2: Getting started: The benefits of being more energy efficient
By using energy-saving approaches and technologies you can:
Save money through using less energy.
Reduce energy waste and lower bills.
Contribute to a more sustainable society and future.
Notes: Step 2: Getting started: What are the benefits of being more energy efficient?
By using energy-saving approaches and technologies you can:
Save money through using less energy
Reduce energy waste and lower bills
Contribute to a more sustainable society and future

## Slide 11: Step 3: Conduct an energy audit
How do I conduct an energy audit?
Notes: Step 3: Conduct an energy audit
How do I conduct an energy audit?

## Slide 12: Step 3: What is an energy audit
“Energy audits have been proven to provide potential average savings of 18% of total energy use.” (European Commission)
An energy audit is a comprehensive assessment of your SME’s energy usage.
Energy audits can be conducted internally or through an external service.
An energy audit identifies inefficient practices, energy-demanding equipment, and areas for improvement.
Auditors may also identify equipment requiring upgrade, inefficient operational practices or suggest energy-saving technologies.
Read more on Conducting an energy audit.
Notes: Step 3: Conduct an energy audit
“Energy audits have been proven to provide potential average savings of 18% of total energy use.” (European Commission)
An energy audit is a comprehensive assessment of your SME’s energy usage
Energy audits can be conducted internally or through an external service
An energy audit identifies inefficient practices, energy-demanding equipment, and areas for improvement
Auditors may also identify equipment requiring upgrade, inefficient operational practices or suggest energy-saving technologies
Read more on Conducting an energy audit.
https://energy.ec.europa.eu/topics/markets-and-consumers/actions-and-measures-energy-prices/coping-crisis_en
https://www.clustercollaboration.eu/content/conducting-energy-audit

## Slide 13: Step 4: Install a smart meter
What are the benefits of a smart meter?
Notes: Step 4: Install a smart meter
What are the benefits of a smart meter?

## Slide 14: Step 4: Installing a smart meter: what can they do?
“Smart Meters and controls, when used to identify and manage energy use, can lead to a reduction in energy use of up to 40%.”
(European Commission)
Smart meters give you real-time data on your electricity consumption, helping you identify trends and patterns in how and when you use electricity. This data helps to pinpoint areas where consumption spikes unexpectedly or where you could use appliances during off-peak hours to lower costs.
Notes: Step 4: Install a smart meter
“Smart Meters and controls, when used to identify and manage energy use, can lead to a reduction in energy use of up to 40%.”
(European Commission)
Smart meters give you real-time data on your electricity consumption, helping you identify trends and patterns in how and when you use electricity. This data helps to pinpoint areas where consumption spikes unexpectedly or where you could use appliances during off-peak hours to lower costs.
https://energy.ec.europa.eu/topics/markets-and-consumers/actions-and-measures-energy-prices/coping-crisis_en

## Slide 15: Step 4: Installing a smart meter: understanding their features
Many utility companies offer time-of-use pricing, where the cost of electricity varies depending on the time of day.
Peak hours come with higher rates due to increased demand, while off-peak hours have lower rates.
Understanding your SME’s energy consumption patterns during these hours can allow you to shift high-energy tasks (e.g. electric vehicle (EV) charging) to times when costs are lower.
Notes: Step 4: Install a smart meter
Many utility companies offer time-of-use pricing, where the cost of electricity varies depending on the time of day.
Peak hours come with higher rates due to increased demand, while off-peak hours have lower rates.
Understanding your SME’s energy consumption patterns during these hours can allow you to shift high-energy tasks (e.g. electric vehicle (EV) charging) to times when costs are lower.

## Slide 16: Step 5: Calculate appliance energy use
How do I calculate the amount of energy each appliance uses?
Notes: Step 5: Calculate appliance energy use
How do I calculate the amount of energy each appliance uses?

## Slide 17: Step 5: Calculate appliance energy use: how to approach it
If your SME involves production or manufacturing, energy use will be more concentrated on machines and tools.
An office-based SME might have higher energy consumption from lighting, heating/cooling, and electronic devices.
Differentiating between appliances can help focus efforts on areas with the highest potential for energy optimisation.
You can use (portable) plug-in energy consumption meters to monitor electricity consumption for each category of device.
Notes: Step 5: Calculate appliance energy use
If your SME involves production or manufacturing, energy use will be more concentrated on machines and tools.
An office-based SME might have higher energy consumption from lighting, heating/cooling, and electronic devices.
Differentiating between appliances can help focus efforts on areas with the highest potential for energy optimisation.
You can use (portable) plug-in energy consumption meters to monitor electricity consumption for each category of device.

## Slide 18: Step 6: Explore more efficient energy use
What practical steps can I take to use energy more efficiently?
Notes: Step 6: Explore more efficient energy use
What practical steps can I take to use energy more efficiently?

## Slide 19: Step 6: Explore more efficient energy use: saving money
“An average small business could reduce its energy bill by up to 30% by implementing good housekeeping and maintenance measures…” (European Commission)
LED lights use 80% less energy when compared to halogen bulbs, and last 20x longer (Source: Energy Saving Trust)
Improving motor-driven systems' energy efficiency, for every euro invested at least 7 euros will be saved over the equipment’s lifetime.
Energy efficient heat pumps can often replace traditional fossil fuel boilers, which can increase energy efficiency over 4 times.
Sources: European Commission
Notes: Step 6: Explore more efficient energy use
“An average small business could reduce its energy bill by up to 30% by implementing good housekeeping and maintenance measures…” (European Commission)
LED lights use 80% less energy when compared to halogen bulbs, and last 20X longer (Source: Energy Saving Trust)
Improving motor-driven systems' energy efficiency, for every euro invested at least 7 euros will be saved over the equipment’s lifetime.
Energy efficient heat pumps can often replace traditional fossil fuel boilers, which can increase energy efficiency over 4 times.
Sources: European Commission
https://energy.ec.europa.eu/topics/markets-and-consumers/actions-and-measures-energy-prices/coping-crisis_en
https://energysavingtrust.org.uk/advice/lighting/
https://energy.ec.europa.eu/topics/markets-and-consumers/actions-and-measures-energy-prices/coping-crisis_en

## Slide 20: Step 6: Explore more efficient energy use: saving energy
Heating costs increase by 8% for every 1 degree Celsius increase. Smart programmable thermostats can save between 5% and 15% on heating costs.
Lighting can be responsible for up to 40% of a building’s energy use. Using lighting controls reduces its energy use by over 1/3
Insulating pipework has been found to reduce energy losses by over 75%
The correct sizing of the compressor load and model selection of compressed air systems can reduce energy consumption by more than 1/3
Sources: European Commission
Notes: Step 6: Explore more efficient energy use
Heating costs increase by 8% for every 1 degree Celsius increase. Smart programmable thermostats can save between 5% and 15% on heating costs.
Lighting can be responsible for up to 40% of a building’s energy use. Using lighting controls reduces its energy use by over 1/3
Insulating pipework has been found to reduce energy losses by over 75%
The correct sizing of the compressor load and model selection of compressed air systems can reduce energy consumption by more than 1/3
Sources: European Commission
https://energy.ec.europa.eu/topics/markets-and-consumers/actions-and-measures-energy-prices/coping-crisis_en

## Slide 21: Step 7: Increase the energy efficiency of your equipment
How do I increase the energy efficiency of our equipment?
Notes: Step 7: Increase the energy efficiency of your equipment
How do I increase the energy efficiency of our equipment?

## Slide 22: Step 7: Increase the energy efficiency of your equipment: how to check
Identify outdated, energy-inefficient equipment. For example, older lighting systems, air conditioning units, and machinery may be consuming far more energy than newer, energy-efficient models.
Replace, repair, or upgrade to more efficient alternatives. For example, you could use motion detection for lighting or ensure that equipment uses its power saving mode after a certain time.
Use Topten.eu - The best products in Europe to compare your current equipment with other available solutions.
Notes: Step 7: Increase the energy efficiency of your equipment
Identify outdated, energy-inefficient equipment. For example, older lighting systems, air conditioning units, and machinery may be consuming far more energy than newer, energy-efficient models.
Replace, repair, or upgrade to more efficient alternatives. For example, you could use motion detection for lighting or ensure that equipment uses its power saving mode after a certain time.
Use Topten.eu - The best products in Europe to compare your current equipment with other available solutions.

## Slide 23: Step 8: Optimise your heating and cooling systems
How do I optimise our heating and cooling systems?
Notes: Step 8: Optimise your heating and cooling systems
How do I optimise our heating and cooling systems?

## Slide 24: Step 8: Optimise your heating and cooling systems: practical tips
Heating and cooling systems are among the largest energy consumers in most SMEs.
Installing programmable thermostats, ensuring regular maintenance, or using energy-efficient models can help reduce consumption.
Consider adjusting settings to ensure heating/cooling is only used when necessary. For example, turn off heating or air conditioning when employees aren’t around.
Notes: Step 8: Optimise your heating and cooling systems
Heating and cooling systems are among the largest energy consumers in most SMEs.
Installing programmable thermostats, ensuring regular maintenance, or using energy-efficient models can help reduce consumption.
Consider adjusting settings to ensure heating/cooling is only used when necessary. For example, turn off heating or air conditioning when employees aren’t around.

## Slide 25: Step 9: Encourage energy saving practices amongst employees
How do I encourage others to adopt energy saving practices?
Notes: Step 9: Encourage energy saving practices amongst employees
How do I encourage others to adopt energy saving practices?

## Slide 26: Step 9: Encourage energy saving practices amongst employees: some tips
A culture of energy mindfulness can lead to noticeable reductions in energy consumption.
Employee behavior can have a significant impact on energy consumption. Encourage employees to:
  Turn off lights.
  Unplug equipment when not in use.
  Use energy-efficient settings on computers and printers.
Read the International Energy Agency’s Behavioural Changes.
Notes: Step 9: Encourage energy saving practices amongst employees
A culture of energy mindfulness can lead to noticeable reductions in energy consumption.
Employee behavior can have a significant impact on energy consumption. Encourage employees to:
  Turn off lights
  Unplug equipment when not in use
  Use energy-efficient settings on computers and printers
Read the International Energy Agency’s Behavioural Changes.
https://www.iea.org/energy-system/energy-efficiency-and-demand/behavioural-changes

## Slide 27: Step 10: Explore some further resources
Where can I go to find out more?
Notes: Step 10: Explore some further resources
Where can I go to find out more?

## Slide 28: Next steps: Some further resources
Read the article Coping with the crisis: Increasing resilience in SMEs through energy efficiency.
Review Every1’s 30-minute Digital Energy Essentials course on Energy Use.
Read the article The benefits of energy efficiency improvements for businesses.
Review Every1’s 30-minute Digital Energy Essentials course Privacy, safety & security in the digital energy landscape.
If you want to find out more about energy efficiency, you may find the following resources useful:
Notes: Next Steps
If you want to find out more about energy efficiency, you may find the following resources useful:
Read the article Coping with the crisis: Increasing resilience in SMEs through energy efficiency.
Review Every1’s 30-minute Digital Energy Essentials course on Energy Use.
Read the article The benefits of energy efficiency improvements for businesses.
Review Every1’s 30-minute Digital Energy Essentials course Privacy, safety & security in the digital energy landscape.
https://www.open.edu/openlearncreate/course/view.php?id=12165

## Slide 29: Acknowledgements 1
Saving Energy and Making your Business more Energy Efficient: 10 Easy Steps includes adaptations in steps 3, 4, 5 and 6 of selected material from The European Commission’s Coping with the crisis: Increasing resilience in SMEs through energy efficiency (the ‘Original Work’) which is licensed CC BY 4.0.
This adaptation is made and published by the Every1 Project (the ‘Adapter’) and licensed CC BY-SA 4.0, unless otherwise stated.
The images used in this presentation are as follows:
Cover image: Electricity bills with lightbulb and calculator by Uswitch.com Images is licensed CC BY 2.0.
Introduction text image: Paper Beside Macbook by Lukas on Pexels.com
Step 1: Getting started: What do I need to know?: Black Plugs by Castorly Stock on Pexels.com
Step 2: Getting started: What are the costs and benefits of being more energy efficient?: Balancing by Scouse Smurf is licensed CC BY-ND 2.0.
Step 3: Conducting an Energy Audit: Energy audit by EE image database is licensed CC BY-NC 2.0.
Step 4: Installing a Smart Meter: British Gas Smart Meter by SlipStreamJC is licensed CC BY-NC 2.0.
Step 5: Identifying your electricity demand by device: Energy by Maria Eklind is licensed CC BY-SA 2.0.
Notes: Acknowledgements
Saving Energy and Making your Business more Energy Efficient: 10 Easy Steps includes adaptations in steps 3, 4, 5 and 6 of selected material from The European Commission’s Coping with the crisis: Increasing resilience in SMEs through energy efficiency (the ‘Original Work’) which is licensed CC BY 4.0.
This adaptation is made and published by the Every1 Project (the ‘Adapter’) and licensed CC BY-SA 4.0, unless otherwise stated.
The images used in this presentation are as follows:
Cover image: Electricity bills with lightbulb and calculator by Uswitch.com Images is licensed CC BY 2.0.
Introduction text image: Paper Beside Macbook by Lukas on Pexels.com
Step 1: Getting started: What do I need to know?: Black Plugs by Castorly Stock on Pexels.com
Step 2: Getting started: What are the costs and benefits of being more energy efficient?: Balancing by Scouse Smurf is licensed CC BY-ND 2.0.
Step 3: Conducting an Energy Audit: Energy audit by EE image database is licensed CC BY-NC 2.0.
Step 4: Installing a Smart Meter: British Gas Smart Meter by SlipStreamJC is licensed CC BY-NC 2.0.
Step 5: Identifying your electricity demand by device: Energy by Maria Eklind is licensed CC BY-SA 2.0.

## Slide 30: Acknowledgements 2
Step 6: Exploring possibilities to switch to more efficient energy use: Energy by Umberto Salvagnin is licensed CC BY 2.0.
Step 7: Increasing the energy efficiency of your equipment: Computer by eltpics is licensed CC BY-NC 2.0.
Step 8: Optimising your heating and cooling systems: Light Switch – 157/365 by Niklas Morberg is licensed CC BY-NC 2.0.
Step 9: Encourage energy saving practices amongst employees: @Work by Daphne is licensed CC BY 2.0.
The following resources were used to inform this presentation:
Energy Solutions Oxfordshire (n.d.) The benefits of energy efficiency improvements for businesses. https://www.energysolutionsoxfordshire.org/the-benefits-of-energy-efficiency-improvements-for-smes/
Torus (n.d.) What are the Cost & Benefits of Energy Efficiency? https://www.torus.co/learn/what-are-the-cost-benefits-of-energy-efficiency
Notes: Acknowledgements
Step 6: Exploring possibilities to switch to more efficient energy use: Energy by Umberto Salvagnin is licensed CC BY 2.0.
Step 7: Increasing the energy efficiency of your equipment: Computer by eltpics is licensed CC BY-NC 2.0.
Step 8: Optimising your heating and cooling systems: Light Switch – 157/365 by Niklas Morberg is licensed CC BY-NC 2.0.
Step 9: Encourage energy saving practices amongst employees: @Work by Daphne is licensed CC BY 2.0.
The following resources were used to inform this presentation:
Energy Solutions Oxfordshire (n.d.) The benefits of energy efficiency improvements for businesses. https://www.energysolutionsoxfordshire.org/the-benefits-of-energy-efficiency-improvements-for-smes/
Torus (n.d.) What are the Cost & Benefits of Energy Efficiency? https://www.torus.co/learn/what-are-the-cost-benefits-of-energy-efficiency

## Slide 31: Thank you!
Notes: Thank you!