## Slide 1: Lecture 5 Operational Requirements – Case Study
The Electricity Transition Playbook
Version 1.0
Supported by and in collaboration with CCG and Green Grids Initiative
Notes: The next four slides provide an overview of the some of the specific case studies for how Operability challenges have been addressed in a Great Britain context

## Slide 2: Case study 1: Dynamic Containment
    What is it?
    Participants
    Over 2022-23 FY, the market consisted of 30 active participants with executed volume of approx. 3TW and average clearing price of 10.2 £/MW/h for both DC High and Low services.
    At the moment, the primary technology participating in DC is battery energy storage due to flexibility and speed of response.
DC volumes: Jan 2021 - Dec 2022
NGESO Markets Roadmap
Operational limits of DC
1 second
to full delivery
100%
100%
49.5
49.8
50.2
50.5
Hz
Notes: Dynamic containment
What is it?
Dynamic Containment or DC is a service that is designed by to act rapidly when there is a fault on the system. Faults on the system cause the frequency to fluctuate drastically, DC counteracts this fluctuation.
There are 2 types of DC - ‘high’ and ‘low’ containment with ‘high’ containment dealing with when the frequency goes above 50Hz and ‘low’ dealing with when the frequency drops below 50Hz during a fault.
Maximum delivery time is 1 second and is capable of sustaining that delivery for 15 minutes.
DC being dynamic means that the any response is proportionate to the level of the fluctuation.
How does it mitigate operability challenges?
Increase in renewable generation on the system has resulted in an increase in both the frequency fluctuation pre-fault and rate of change of frequency post-fault.
DC service deals with this by detecting the fault within 0.5 seconds. This allows DC to deal with system faults faster to limit the negative effects that can occur when frequency deviates for too long.

## Slide 3: Case study 2: Constraint Management Pathfinder
    What is it?
Thermal constraint costs 2020-2022 in GB
NGESO Markets Roadmap
Notes: Constraint management pathfinder
What is it?
With the increase in wind generation around GB with the aim of 50GW by 2030, there will be significant constraints on the system. One area in particular being the England-Scotland border also called the ‘B6’ Boundary.
Constraint Management Pathfinder is designed to explore new short- and long-term solutions for Intertripping services. Intertripping is where generation may be reduced or disconnected following a fault.
Intertripping would allow more power over a boundary pre-fault as it enables the system operator to reduce the flow very rapidly in case of system faults.
How does it mitigate operability challenges?
It allows the system operator to run the system more efficiently allowing access to generation that has been moved to different areas such as B6 England-Scottish boundary.
The graph on the right shows the increasing financial impact of constraint costs
The initial requirements are 800MW of transmission-connected generation with the ability to be tripped off within 150micro seconds when armed and tripped by a fault.
Through the months of April 2022 to January 2023 National Grid ESO estimated that this service has saved consumers £80million that would otherwise have been used on constraint payments.

## Slide 4: Case study 3: Voltage Pathfinders and Reactive Market
Voltage Pathfinder 2 (Pennines Area) entrants by technology type
NGESO Markets Roadmap
Voltage Pathfinder 1 (Mersey Area) entrants by technology type
NGESO Markets Roadmap
Notes: Voltage Pathfinders and Reactive Market
What is it
The Voltage Pathfinders look for the most cost-effective ways to address high voltage system issues created by the need to absorb more reactive power on the transmission network due to a drop in both minimum demand and power consumption
They are long-term tender contracts and support the move to a 100% zero carbon by promoting the role of zero carbon assets to manage reactive power.
Whereas The Reactive Market design project has explored market design solutions to resolve the challenges for procuring reactive power, ensuring cost efficient solutions by maximising the participation of low carbon and flexible technologies.
This project looks at services across 3 timeframes; short-term looking at the day-head, medium-term looking at year-ahead contracts, and long-term market which covers over 4 years.
How does it mitigate operability challenges?
This is aimed to solve the loss of reactive power providers due to decommissioning of aging power plants.
decarbonisation means that these retired generators are not being replaced with similar assets. Confounding the issues as the new assets are further away from the locations where reactive services are needed.

## Slide 5: Case study 4: Stability Pathfinders and Market
*Live project as of May 2023.
Distribution of additional inertia requirement in 2030 in GB’s system
NGESO Operability Strategy Report
Stability
Pathfinder
Market
Notes: Stability Pathfinders and Market
The Stability Pathfinders look for the most cost-effective way to address stability issues created by the decline in system inertia caused by the loss of conventional generation that provided system stability as a by-product to generating energy
Three rounds of stability Pathfinder long-term tenders across different parts of GB in order to ensure National Grid ESO has access to enough system inertia and short circuit level to run the system reliably.
Whereas The Stability Market design project will consider the current GB stability arrangements and investigate the best options for an end to end market design.
The market will be designed to work across 3 timeframes; short-term looking at the day-head, medium-term looking at year-ahead contracts, and long-term market which covers 4+ years.
This allows the system operator a route to access stability services through an open, transparent, and competitive market.
It will promote the role of long-term investment signals for new assets such as synchronous condensers and also grid-forming capability in short-term market.
It is anticipated that the benefits of this market in 2030 would be approx. £58million
How does it mitigate operability challenges?
With the removal of carbon intensive assets there is a loss of inherent system stability, including system inertia, short circuit level and dynamic voltage.
As a result there will be a significant increase in the needs for inertia as highlighted by the graph
The stability Pathfinders and Stability Market are projects that work to mitigate the 40% loss of inertia over the last decade on GB’s system since the shift towards more renewable generation.
The total spend on three stability Pathfinders to date is over £1.6bn and they provide significant savings versus alternative options

## Slide 6: Case study 5: Demand Flexibility Service
Demand profile for Event 1: 16:30-18:30
Octopus Energy
Notes: Demand Flexibility Service
What is it?
The Demand Flexibility Service (DFS) is a service put in place by National Grid ESO across the winter of 2022/2023 and launched following the global energy crisis when the energy price increased sharply.
It is designed to reward both domestic and some commercial customers with smart meters, by offering incentives that will reduce their energy bills by using less power at certain peak points during the day.
The demonstration tests had a guaranteed minimum price of £3kWh, but could be more depending on the price in the Balancing mechanism
How does it mitigate operability challenges?
This helps to deal with a few of the operability challenges highlighted earlier by reducing energy usage during peak hours and cost of electricity down.
Energy Balancing - it helps to reduce the peak draw on the system reducing the need for redispatching generation to meet that demand.
System Adequacy – the service provides more flexibility when the output of renewable energy plants is low, during less windy/sunny days.

## Slide 7
Gregory, T., 2023. Lecture 5: Operational Requirements – Case Study.
The Electricity Transition Playbook. Release Version 1.0 [online presentation]. Climate Compatible Growth Programme, Green Grids Initiative
Supported by and in collaboration with CCG and Green Grids Initiative
Consolidated by Tim Gregory from CCG and Green Grids Initiative

## Slide 8
This document was updated on 11.10.2025