## Slide 1: Lecture 17: Integrating NbS with built infrastructure in different core infrastructure sectors
Yu Mo and Robyn Haggis, Oxford University

## Slide 2: Learning Outcomes
By the end of this lecture, you will:
Know how nature-based solutions (NbS) can be strategically integrated in different infrastructure sectors in order to deliver benefits for the sector as well as wider co-benefits for society, the economy and the environment
Have explored the sectors of water, solid waste, wastewater, energy, digital communications, transport and the urban environment
Have knowledge of the potential for NbS to substitute, complement or protect the services provided by different infrastructure sectors thanks to examples and case studies
Have the foundation for understanding how nature can be leveraged practically in different infrastructure sectors to achieve multiple benefits
2

## Slide 3: 17.1 Nature-based solutions (NbS) for water supply
Learning Objectives
To recall a range of nature-based solutions which can support the delivery of freshwater
To consider the ways in which nature-based solutions can enhance water quality
To recognise the value of integrating nature-based solutions with built infrastructure solutions for water supply
3

## Slide 4: 17.1 Nature-based solutions (NbS) for water supply
Introduction
Currently, one-third of people lack safe drinking water, and 5.7 billion may face water scarcity by 2050
Reliable freshwater supplies are essential for domestic needs, agriculture, health, and industry
While engineered water systems remain essential, NbS help regulate water flows, improve quality, and ensure sustainability by managing watersheds, underground aquifers, and ecosystems
Wetlands naturally filter contaminants, reducing reliance on water treatment plants while providing co-benefits like carbon sequestration, air purification, and ecotourism
NbS act as buffers against saline intrusion in coastal areas, enhance rainwater capture in urban settings, and prevent infrastructure damage from climate impacts like storm surges and flooding
4
(United Nations 2020; Gurria 2020; Bertule et al. 2014; Tremolet and Karres 2020; Browder et al. 2019; Blicharska et al. 2019; Silva et al. 2020; Kapos et al. 2019)

## Slide 5: 17.1 Nature-based solutions (NbS) for water supply
Introduction
5
Example nature-based solution | Example services
Protection of watersheds | Cities depend on surrounding rural areas for water supply. To protect the water sources, it often means investing in rural areas far beyond city boundaries
Restoration and protection of upstream forests | Regulation of peak flows, recharge of groundwater supplies
Restoration, protection and management of riparian vegetation along rivers, including wetlands and floodplains | Regulation of peak flows, recharge of groundwater supplies Reduced sedimentation and nutrient pollution in water courses (riparian buffers have efficiency of >70%)
Reconnecting rivers to floodplains | Regulation of peak flows, recharge of groundwater supplies Setting back or removing levees at the edge of river channels can help increase channel capacity and reduce exposure to floodwaters and erosion risk. Providing more room for meandering and healthy floodplains enables the creation of forest and wetland habitats that store water and decrease sedimentation
Creation of green roofs and rainwater harvesting systems in urban areas | Capture rainfall for domestic use. Regulate runoff and delay peak flows, preventing urban water supplies from being contaminated through sewer overflow
Creation of permeable pavements and green spaces in urban areas | Help water infiltration and recharge of water supplies during drought. Support water infiltration and mitigation of flooding and sewer overflow during flood events
Improved agricultural management practices | Land use within catchment areas has a major influence on determining whether watersheds are healthy and can deliver environmental services, and impacts erosion and associated sedimentation
Protection of coastal ecosystems such as oyster and coral reefs and mangroves | Coastal ecosystems can protect coastlines and water supplies from saline intrusion

## Slide 6: 17.1 Nature-based solutions (NbS) for water supply
Provision and regulation of freshwater flows
6
Location of the Atewa Forest, at the source of the Ayensu, Birim and Densu Rivers which together provide water for 5 million people. Protecting the forest provides co-benefits, including biodiversity (e.g., internationally recognised coastal wetlands which are fed by the rivers), carbon sequestration, and supporting local livelihoods (IUCN 2016).
NbS support infiltration, aquifer recharge, and wetland storage, ensuring a stable water supply
Forests and ecosystems regulate runoff, control peak flows, and reduce sedimentation, benefiting downstream communities
Atewa Forest in Ghana helps supply water to Accra by feeding the Densu River, Volta Reservoir, and Weija Dam
Seasonal flooding in north-east Ghana recharges wetlands and ponds, supporting livestock, food security, and local economies
Green roofs and rainwater harvesting capture stormwater, reduce sewer overflows, and provide water for domestic use, easing pressure on urban supplies
(Bertule et al. 2014; IUCN 2016; Mul et al. 2015; Enzi et al. 2017)

## Slide 7: 17.1 Nature-based solutions (NbS) for water supply
Regulation and maintenance of water quality, including reduced sedimentation
7
Water supplies are contaminated by agricultural runoff, industrial waste, landfill leaching, erosion, and sewer overflows, impacting human health, ecosystems, and economic activities
Healthy riparian vegetation, hill slope stabilization, and upstream ecosystem management prevent sediment from entering watercourses, reducing dredging costs and extending infrastructure lifespan
Improved grazing and agroforestry reduce soil erosion, which accounts for over two-thirds of soil loss in Europe
Wetlands and reed ponds trap sediments, heavy metals, and pollutants, purifying water supplies and preventing groundwater contamination
Green roofs, permeable pavements, and rainwater harvesting systems reduce stormwater runoff and prevent sewer overflows, safeguarding urban water quality
(Bertule et al. 2014; Browder et al. 2019; Tremolet and Karres 2020; Gopal 1999)

## Slide 8: 17.1 Nature-based solutions (NbS) for water supply
Water temperature control, biological control and turbidity control
8
Riparian vegetation can provide shade to waterways and help to reduce thermal pollution (left) (Bertule et al. 2014) The Thirlmere reservoir in the UK had such high turbidity in 2015 that it was put out of service (right) (Tremolet and Karres 2020).
Water supplies are contaminated by agricultural runoff, industrial waste, landfill leaching, erosion, and sewer overflows, impacting human health, ecosystems, and economic activities
Healthy riparian vegetation, hill slope stabilization, and upstream ecosystem management prevent sediment from entering watercourses, reducing dredging costs and extending infrastructure lifespan
Improved grazing and agroforestry reduce soil erosion, which accounts for over two-thirds of soil loss in Europe
Wetlands and reed ponds trap sediments, heavy metals, and pollutants, purifying water supplies and preventing groundwater contamination
Green roofs, permeable pavements, and rainwater harvesting systems reduce stormwater runoff and prevent sewer overflows, safeguarding urban water quality
(Bertule et al. 2014; Browder et al. 2019; Tremolet and Karres 2020; Honlah et al. 2019 )

## Slide 9: 17.1 Nature-based solutions (NbS) for water supply
Protecting water supplies from saline intrusion and being mindful of caveats for NbS implementation
9
Coastal ecosystems such as beaches and native vegetation can help to prevent terrestrial inundation of seawater and salination of water supplies
Rising sea levels, storm surges, and coastal flooding threaten freshwater supplies by increasing saltwater intrusion
Mangrove forests, dunes, salt marshes, and barrier reefs act as natural defenses, reducing erosion and preventing saltwater intrusion, similar to dykes and levees
NbS can be combined with engineered solutions to enhance water security, reducing the need for costly desalination
NbS should be planned at watershed or ridge-to-reef levels to prevent unintended impacts, such as affecting downstream biodiversity and water flow in areas like Ghana’s Densu Delta
(Bertule et al. 2014; Kapos et al. 2019; IUCN 2016, 2020; Cohen-Shacham et al. 2016; Shi et al. 2012)

## Slide 10: 17.1 Nature-based solutions (NbS) for water supply
Protecting water supplies from saline intrusion and being mindful of caveats for NbS implementation
10
Benefit type | Example
Net cost savings | Cost savings for water providers can offset the costs of implementing NbS. Watershed degradation impacts drinking water for more than 700 million people, and costs global cities US$5.4 billion in water treatment annually. Worldwide, annual costs to replace lost reservoir storage capacity due to sedimentation—in the form of constructing new or raising existing dams— are estimated at $10 - $20 billion.
Reduced operation and maintenance costs | Water service providers typically rely on grey infrastructure and costly water treatment processes in order to deliver safe water supplies. NbS can reduce water pollution and lead to lower maintenance requirements and associated costs by water treatment plants. The Nature Conservancy estimated that a 10% reduction in sediment can result in a reduction of 2.6% in operation and maintenance costs for water providers.
Energy cost savings | Many water treatment processes rely on large quantities of energy. By reducing water treatment requirements, water providers can save on energy costs.
Capital cost savings | NbS such as forest restoration can provide an alternative to engineered infrastructure. For example, New York City, which gets its water supply from 3 watersheds (75% forested and privately owned) invested in a working forests pollution prevention programme in addition to existing agricultural management best practices to address watercourse pollution. This provided an alternative to building a $US8-10 billion water treatment plant. NbS can reduce requirements for additional materials such as flocculants in water treatment processes. For example, to address increasing sedimentation of water courses, water providers need to use greater quantities of water filtration materials such as flocculants, which requires additional capital investment compared to NbS.
Reduced asset damage | Turbidity from sedimentation in water courses can damage dams and reservoirs. By implementing NbS, damage can be prevented, and additional cost savings incurred through reduced dredging needs.
Resilience | NbS can increase the resilience of urban and other water supplies in the face of climate change.
Co-benefits | NbS generate various co-benefits, including improved air quality, aesthetic value and carbon sequestration.
Integrating NbS can provide various benefits to water service providers. Examples are shown here (Tremolet and Karres 2020; Browder et al. 2019; Bertule et al. 2014).

## Slide 11: 17.1 Nature-based solutions (NbS) for water supply
Summary
Freshwater supplies originate in the broader watershed and are impacted by ecosystems and land use practices within the wider landscape context
Through implementing NbS, such as the restoration of riparian ecosystems and improved agricultural management practices, NbS can provide various benefits to water service providers. These include regulation of freshwater flows, maintenance of water quality, reduction of turbidity, and prevention of saline intrusion
NbS can support water delivery in inland, coastal and urban areas, and provide various economic benefits to service providers, including through reduced requirements for engineered infrastructure, reduced maintenance needs and extending the lifespan of built assets
11

## Slide 12: 17.1 Nature-based solutions (NbS) for water supply
Bibliography
Bertule, Maija, Gareth James Lloyd, Louise Korsgaard, James Dalton, Rebecca Welling, Stefano Barchiesi, Mark Smith, Jeff Opperman, Erin Gray, and Todd Gartner. 2014. “Nations Environment Programme Publication: Green Infrastructure Guide for Water Management: Ecosystem-based management approaches for water-related infrastructure projects.” http://www.medspring.eu/sites/default/files/Green-infrastructure-Guide-UNEP.pdf.
Blicharska, Malgorzata, Richard J. Smithers, Grzegorz Mikusiński, Patrik Rönnbäck, Paula A. Harrison, Måns Nilsson, and William J. Sutherland. 2019. “Biodiversity’s contributions to sustainable development.” Nature Research. https://doi.org/10.1038/s41893-019-0417-9.
Browder, Greg, Suzanne Ozment, Irene Rehberger Bescos, Todd Gartner, and Glenn-Marie Lange. 2019. “Integrating Green and Gray: Creating Next Generation Infrastructure.” WRI Publications, March. https://doi.org/10.46830/wrirpt.18.00028.
Cohen-Shacham, E., G. Walters, C. Janzen, and S. Maginnis. 2016. Nature-based solutions to address global societal challenges. https://doi.org/10.2305/iucn.ch.2016.13.en.
Enzi, Vera, Blanche Cameron, Péter Dezsényi, Dusty Gedge, Gunter Mann, and Ulrike Pitha. 2017. “Nature-Based Solutions and Buildings – The Power of Surfaces to Help Cities Adapt to Climate Change and to Deliver Biodiversity.” In Theory and Practice of Urban Sustainability Transitions, 159–83. Springer, Cham. https://doi.org/10.1007/978-3-319-56091-5_10.
Gopal, Brij. 1999. “Natural and constructed wetlands for wastewater treatment: Potentials and problems.” In Water Science and Technology, 40:27–35. 3. No longer published by Elsevier. https://doi.org/10.1016/S0273-1223(99)00468-0.
Gurria, Eva. 2020. “Nature for Life: The value of nature in achieving the Sustainable Development Goals | UNDP.” https://www.undp.org/content/undp/en/home/blog/2020/nature-for-life--the-value-of-nature-in-achieving-the-sustainabl.html.
Honlah, Emmanuel, Alexander Yao Segbefia, Divine Odame Appiah, Moses Mensah, and Peter Ofori Atakora. 2019. “Effects of water hyacinth invasion on the health of the communities, and the education of children along River Tano and Abby-Tano Lagoon in Ghana.” Edited by Albert Sabater. Cogent Social Sciences 5 (1): 1619652. https://doi.org/10.1080/23311886.2019.1619652.
IUCN. 2016. “The Economics of the Atewa Forest Range, Ghana,” 209. www.iucn.nl; Ghana.arocha.org.
———. 2020. IUCN Global Standard for Nature-based Solutions: a user-friendly framework for the verification, design and scaling up of NbS: first edition. IUCN, International Union for Conservation of Nature. https://doi.org/10.2305/iucn.ch.2020.08.en.#
Kapos, V., S. Wicander, T. Salvaterra, K. Dawkins, and C. Hicks. 2019. “The Role of the Natural Environment in Adaptation - Global Center on Adaptation.” https://gca.org/reports/the-role-of-the-natural-environment-in-adaptation/.
Mul, Marloes, Emmanuel Obuobie, Richard Appoh, Kwabena Kankam-Yeboah, Emmanuel Bekoe-Obeng, Barnabas Amisigo, Frederick Yaw Logah, Benjamin Ghansah, and Matthew McCartney. 2015. “Water resources assessment of the Volta River Basin.” IWMI Working Papers 166. https://doi.org/10.5337/2015.220.
Shi, Zhongjie, Daping Xu, Xiaohui Yang, Zhiqing Jia, Hao Guo, and Ningnan Zhang. 2012. “Ecohydrological impacts of eucalypt plantations: A review.” Journal of Food, Agriculture and Environment 10 (3-4): 1419–26. https://www.researchgate.net/publication/281138178{\_}Ecohydrological{\_}impacts{\_}of{\_}eucalypt{\_}plantations{\_}A{\_}review.
Silva, Mariana, Greg Watson, Amal Lee Amin, Graham Watkins, Amanda Rycerz, and John Firth. 2020. “Increasing Infrastructure Resilience with Nature-Based Solutions (NbS).” Washington, D.C.: Inter-American Development Bank. https://doi.org/10.18235/0002325.
Tremolet, S., and N. Karres. 2020. “Resilient European Cities: Nature-based Solutions for Clean Water.” The Nature Conservancy. https://www.nature.org/content/dam/tnc/nature/en/documents/TNC{\_}ResilientEuropeanCities{\_}NBSWater.pdf.
United Nations. 2020. “The United Nations world water development report 2016: water and jobs - UNESCO Digital Library.” https://unesdoc.unesco.org/ark:/48223/pf0000372985.locale=en.
Yao, Lei, Liding Chen, Wei Wei, and Ranhao Sun. 2015. “Potential reduction in urban runoff by green spaces in Beijing: A scenario analysis.” Urban Forestry and Urban Greening 14 (2): 300–308. https://doi.org/10.1016/j.ufug.2015.02.014.
12

## Slide 13: 17.2 Nature-based solutions for waste and wastewater treatment
Learning objectives
Recognise the value of nature-based solutions in waste management and wastewater treatment
Gain a basic understanding of the principles of designing nature-based solutions for waste management and wastewater treatment
13

## Slide 14: 17.2 Nature-based solutions for waste and wastewater treatment
Overview of the applications of nature-based solutions in waste and wastewater treatment
Population growth increases waste & wastewater generation
Low Treatment Rates:
Western Europe: 86%
North America: 67%
South Asia & Sub-Saharan Africa: 16%
Excess pollution surpasses nature’s self-regulation, harming ecosystems & human well-being
Engineering Solutions are crucial but not universally accessible
Nature-Based Solutions:
Cost-effective alternative/complement to engineering approaches
Treat certain contaminants efficiently
Provide co-benefits like ecosystem restoration
Vital for low-resource regions lacking expensive infrastructure
14
Services | Hard engineering options | Nature-based solution | Co-benefits
WASTE TREATMENT | Landfill Synthetic soil modifiers | Incorporation of natural and constructed wetlands in landfill leachate treatment Use of phytocapping to reduce water percolating into landfill Use of green manure, biochar, etc, to improve soil properties Use of hyper- accumulator ph- ytoremediation plants to remove contaminants from the soil, or to reduce their bio- availability Use of reconstructed grassland, heathland, and wetland to restore landfill sites | Carbon sequestration Habitat provision Biodiversity conservation Urban temperature control Aesthetics Mental health
WASTEWATER TREATMENT | Wastewater treatment plant | For urban and suburban source/point source: Green roof and rain garden to collect, store and clean rainwater before gradual release into water courses Constructed wetland for greywater treatment Constructed wetland for treating outflow from existing wastewater treatment plants Biodegradation and bioconversion to improve effluent from industrial and municipal treatment plants For non-point source: Growing perennial crops and winter crops to retain nutrients in soil Intercrop with legumes to enhance nutrient uptake Restoring water flow through wetlands Nature or constructed wetland to trap sediment and pollution runoff in farmed landscape Protecting and restoring intertidal habitat to reduce nutrient and other pollution in coastal water | Carbon sequestration Habitat provision Biodiversity conservation Urban temperature control Aesthetics Mental health
(Jones et al. 2021; Millennium ecosystem assessment 2005)

## Slide 15: 17.2 Nature-based solutions for waste and wastewater treatment
Incorporating nature-based solutions into landfill management
Constructed Wetlands & Leachate Treatment
Landfill leachate contains organic matter, nutrients, heavy metals, and salts
Effectiveness of Wetland Types:
  Hybrid Wetlands:
    Best for contaminant removal (BOD: 72.2%, COD: 56.2%, PO4: 61.0%, TKN: 64.9%, TN: 67.3%, NH3-N: 68.9%, TSS: 51.8%)
  Vertical Flow Wetlands:
    Best for heavy metal removal (Cd: 92.4%, Cr: 90.0%, Ni: 93.3%, Pb: 84.1%, Zn: 89.3%, Fe: 93.6%, Mn: 77.1%)
Landfill Restoration with Natural Habitats
Benefits:
Prevents water infiltration into the landfill
Stabilizes the site and reduces air pollution
Improves environmental quality & human health
Importance of Native Plants:
Self-sustaining, no need for fertilizers, pesticides, or irrigation
Enhances biodiversity by supporting native wildlife & pollinators
15
(Bakhshoodeh et al. 2020; Lamb et al. 2014; Simmons 1999; Geniole et al. 2016; Rubin 2006)

## Slide 16: 17.2 Nature-based solutions for waste and wastewater treatment
Case study: Constructed wetlands treating landfill leachates in Ibadan, Nigeria
16
Implementation and performance of a constructed wetland in treating leachate from a landfill site in Ibadan, Nigeria
Largest indigenous city in tropical Africa (3+ million people)
Landfills are the main waste disposal sites and leachate discharged untreated into the environment
Wetland Design:
Vertical subsurface-flow system
Filtration medium: 0.2m sand layer (coarse to medium) and 0.5m gravel layers (fine & coarse)
Plant used: Ipomoea aquatica (locally available plant)
Leachate flow by gravity
As a result, the final effluent met Nigeria's Federal Environmental Protection Agency standards for discharge into surface waters
(Aluko and Sridhar 2005)

## Slide 17: 17.2 Nature-based solutions for waste and wastewater treatment
Nature-based solutions for nutrient removal
17
Agriculture, untreated sewage, and wastewater effluents have significantly increased phosphorus and nitrogen in water systems, leading to water quality decline, algal blooms, and hypoxic zones. Most nutrient pollution comes from non-point sources, particularly fertilizer runoff from farmlands
Nature-Based Solutions (NBS):
Retention Strategies:
  Perennial crops (e.g., grasses) keep nitrogen in the soil, reducing groundwater contamination
  Winter cover crops (e.g., rye, clover) prevent nitrate leaching during winter and spring
Nutrient Removal:
  Wetland restoration & constructed wetlands intercept nutrient-rich water before reaching streams or rivers
  Ponds and wetlands filtering groundwater flows are effective nitrogen sinks, while those intercepting eroding sediments capture phosphorus
Challenges & Considerations: While wetlands effectively remove pollutants, they can release methane (CH₄) and nitrous oxide (N₂O) under anaerobic conditions. These gases have 84x and 298x the global warming potential of CO₂, making it essential to design solutions that minimize emissions while improving water quality
(Ongley, Xiaolan, and Tao 2010; Jones et al. 2021; Millennium ecosystem assessment 2005)

## Slide 18: 17.2 Nature-based solutions for waste and wastewater treatment
Case study: Floating wetlands treating urban wastewater in Pakistan
18
Wastewater stabilization ponds built in 1998 to treat 60% sewage, 40% industrial wastewater became overloaded as the city grew, reducing treatment efficiency
In 2014, a 1,858 m² Floating Treatment Wetlands system with 1,000 hydroponic rootmat units was installed, covering 3.5% of the pond surface and planted with helophytic grasses
Water quality improved significantly, with 79% COD removal, 88% BOD removal, and 65% TDS removal, along with a reduction in heavy metals
In 2015–2016, ~60 million m³ of wastewater per year was treated at a cost of $0.00026 per m³, with costs expected to decrease over time
It is a cost-effective, scalable solution for sewage and industrial wastewater treatment, particularly in regions with limited treatment infrastructure
(a) A schematic representation of a hydroponic rootmat, and (b-d) the growth of FTWs (adapted from Afzal et al. (2019))

## Slide 19: 17.2 Nature-based solutions for waste and wastewater treatment
Summary
Nature-based solutions provide cost-effective methods for waste and wastewater treatment
They can treat effluent from existing waste and wastewater treatment facilities, and are also critical for treating nutrient pollution
The case studies of using constructed wetlands to treat leachate from a landfill site in Nigeria and using floating treatment wetlands to treat urban wastewater in Pakistan have demonstrated how nature-based solutions can be used to improve the performance of engineering approaches
19

## Slide 20: 17.2 Nature-based solutions for waste and wastewater treatment
Bibliography
Afzal, Muhammad, Muhammad Arslan, Jochen A. Muller, Ghulam Shabir, Ejazul Islam, Razia Tahseen, Muhammad Anwar-ul-Haq, Amer J. Hashmat, Samina Iqbal, and Qaiser M. Khan. 2019. “Floating Treatment Wetlands as a Suitable Option for Large-Scale Wastewater Treatment.” Journal Article. Nature Sustainability 2 (9): 863–71. https://doi.org/10.1038/s41893-019-0350-y.
Aluko, Olufemi Oludare, and M. K. C. Sridhar. 2005. “Application of constructed wetlands to the treatment of leachates from a municipal solid waste landfill in Ibadan, Nigeria.” https://www.researchgate.net/profile/Olufemi-Aluko/publication/7751827{\_}Application{\_}of{\_}constructed{\_}wetlands{\_}to{\_}the{\_}treatment{\_}of{\_}leachates{\_}from{\_}a{\_}municipal{\_}solid{\_}waste{\_}landfill{\_}in{\_}Ibadan{\_}Nigeria/links/553526f30cf20ea35f0ffc21/Application-of-constructed-wetl.
Bakhshoodeh, Reza, Nadali Alavi, Carolyn Oldham, Rafael M. Santos, Ali Akbar Babaei, Jan Vymazal, and Pooya Paydary. 2020. “Constructed Wetlands for Landfill Leachate Treatment: A Review.” Journal Article. Ecological Engineering 146. https://doi.org/10.1016/j.ecoleng.2020.105725.
Geniole, Shawn N., Joacy P. F. David, Roseanne F. R. Euzibio, Beatriz Z. S. Toledo, Andrea I. M. Neves, and Cheryl M. McCormick. 2016. “Restoring Land and Mind: The Benefits of an Outdoor Walk on Mood Are Enhanced in a Naturalized Landfill Area Relative to Its Neighboring Urban Area.” Journal Article. Ecopsychology 8 (2): 107–20. https://doi.org/10.1089/eco.2016.0005.
Jones, Edward R., Michelle T. H. van Vliet, Manzoor Qadir, and Marc F. P. Bierkens. 2021. “Country-Level and Gridded Estimates of Wastewater Production, Collection, Treatment and Reuse.” Journal Article. Earth System Science Data 13 (2): 237–54.
Lamb, Dane T., Kartik Venkatraman, Nanthi Bolan, Nanjappa Ashwath, Girish Choppala, and Ravi Naidu. 2014. “Phytocapping: An Alternative Technology for the Sustainable Management of Landfill Sites.” Journal Article. Critical Reviews in Environmental Science and Technology 44 (6): 561–637.
Millennium ecosystem assessment, M. E. A. 2005. Ecosystems and Human Well-Being. Book. Vol. 5. Island Press Washington, DC.
Ongley, E. D., Z. Xiaolan, and Y. Tao. 2010. “Current Status of Agricultural and Rural Non-Point Source Pollution Assessment in China.” Journal Article. Environ Pollut 158 (5): 1159–68. https://doi.org/10.1016/j.envpol.2009.10.047.
Rubin, E. 2006. “Revegetating Landfills and Waste Containment Area Fact Sheet.” Journal Article. Environmental Protection Agency, United States.
Simmons, Elizabeth. 1999. “Restoration of Landfill Sites for Ecological Diversity.” Journal Article. Waste Management & Research 17 (6): 511–19. https://doi.org/10.1177/0734242X9901700617.
20

## Slide 21: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
Learning objectives
Consider how NbS can be integrated into transport networks for improved service delivery
Consider how NbS can be integrated into the energy sector for improved service delivery
Consider how NbS can be integrated into transmission line networks
21

## Slide 22: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
Integrating nature-based solutions in water transport networks - ports and harbours
22
Mangroves and other coastal and marine ecosystems can protect ports from climate impacts, support tranquillity of waters and increase navigability of shipping channels by reducing sedimentation and mitigating erosive forces from passing boats (Paalvast et al. 2012). Photograph Hijdra (2021).
Due to their low-lying nature and proximity to the coastal zone, ports and harbours are at risk of climate impacts including flooding and storm surges
Mangroves, seagrass, reefs (coral & oyster), and beaches act as natural barriers, enhancing port resilience against climate change
NbS mitigate boat wakes, prevent bank erosion, reduce sedimentation in shipping channels, and lowers dredging costs while extending harbour wall lifespans
NbS help maintain calm waters for navigation, and living harbour walls support infrastructure longevity while reducing port water pollution
(Hijdra 2021; Perkol-Finkel et al. 2018)

## Slide 23: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
Integrating nature-based solutions in water transport networks - rivers, canals and lakes
23
Service | Ports and harbours | Rivers, canals and lakes
Resilience to coastal hazards | Coastal NbS reduce wave energy and stabilise shorelines Restoration of mangroves forests and wetlands Restoration of reefs Creation of living breakwaters/quay walls Protection or restoration of salt marshes, coastal lagoons, coastal peatlands, sand dunes Beach restoration | Creation of buffer strips can mitigate flooding and erosion of navigation channels Restoration of riparian vegetation along navigation channels Reconnect rivers to floodplains
Tranquil waters for navigation | Coastal NbS provide services including wave dissipation and reduced sedimentation in harbours Wave collision and reflection can be minimised through porous revetements | Restoration of NbS to support biological control of invasive weeds. This can control floating aquatic plants that can clog navigation channels
Reduce sedimentation of navigation channels | Reef restoration and protection of terrestrial wetlands (e.g., mangroves) can contribute to shoreline stabilisation | Maintain riparian vegetation for services including sediment stabilisation
Reduction of erosive forces from boats | Restoration of mangroves, wetlands and reefs dissipate erosive forces from boat wakes Living break structures help to protect harbours from erosion Restoration of beaches can dampen wave action | Creation of buffer strips and banks along canals, rivers and lakes can dissipate erosive forces of boat wakes
Regulation of water supply in navigation channels |  | Improved management, e.g. removal of water-hungry species and restoration of native vegetation has been used in South Africa to keep water flowing during drought
Mitigation of pollution from water transport |  | Wetlands and ecosystems along watercourses can trap sediments and filter contaminants from boats Reeds can treat sewage that may be deposited
Hijdra 2021; Vital Ports n.d.; Perkol-Finkel et al. 2018; Paalvast et al. 2012; European Commission 2018; Madramootoo et al. 1994

## Slide 24: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
24
Integrating nature-based solutions into road and rail networks
NbS can protect road and rail infrastructure networks from climate impacts. Photograph from Browder et al. (2019).
Ecological underpasses and overpasses (Asian Development Bank 2019; European Commission, n.d.b)
With an estimated 25 million km of new roads by 2050, integrating natural-built transport networks can enhance resilience and efficiency
Vegetated slopes and verges along transport routes help mitigate flooding, prevent landslides, act as firebreaks, and provide temperature regulation, reducing maintenance costs and extending infrastructure lifespan
Ecological structures such as overpasses and underpasses allow wildlife movement and reduce vehicle collisions, improving transport sector resilience
Tree-lined roads improve driver focus, slow down traffic for pedestrian safety, and contribute to safer and more sustainable transport networks, with increasing adoption in projects like TRANSGREEN in Europe
(United Nations 2016; Kennedy et al. 2019; Kapos et al. 2019; Black, Tara, and Pakzad 2016; European Commission 2013; Interreg Danube n.d.; GMCA 2019)
Notes: There are now several open-source hazard products at global scales which are being used widely for vulnerability and risk analysis. A few resources include:
Global river and coastal flood maps: Historical and future hazard maps at different return periods (2, 5, 1, 25, 50, 10, 250, 500, 100 years). All data is available at a 30 arc-seconds resolution (~1km at equator) (Gassert et al. 2015).
Global hazard maps for earthquakes for different return periods (250, 475, 975, 1500, 2475 years) both Peak Ground Acceleration and spectral acceleration. Data is available at 0.072 degrees (~8km at equator).
Global dataset of 1,000 synthetic tropical cyclones paths with cyclone characteristics (e.g., wind speed, pressure) on a global scale. Wind speed probabilities are derived globally (1 metre, 1 minutes sustained speed) for different return periods (1 to 1,000 years) at 1km resolution (Bloemendaal et al. 2019).

## Slide 25: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
Integrating nature-based solutions into airports
Chicago O’Hare Airport has 338,000 ft² of green roofs across 12 buildings, retaining 90% of precipitation and saving $1.5 million in re-roofing costs by doubling roof lifespans
Chicago O’Hare and Portland International Airports use grazing programs instead of motorized mowing, cutting costs on fuel and equipment while improving air quality, reducing water contamination, and preventing soil erosion
NbS improves air quality, noise regulation, and microclimate control, reducing passenger stress and increasing airport appeal
Portland International Airport’s Terminal 4 green wall (20,000+ species) helps regulate temperature and purify air
Singapore’s Changi Airport integrates gardens and NbS features, enhancing its reputation as a world-class airport and reinforcing Singapore’s identity as a "City in a Garden"
25
Singapore’s Changi Airport includes multiple gardens and an open dome to allow rainfall to be captured by an indoor waterfall and forest, which provides cooling and energy savings to the airport, saving the airport money whilst supporting regulation of the indoor microclimate.
(Henderson 2017; Newman 2014; Airport Technology 2016; Trofimova 2020; Han, Lho, and Kim 2019)

## Slide 26: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
Integrating nature-based solutions into energy and digital transmission line networks
26
The LIFE ELIA project restored 130km of different ecosystems in ecological corridors under overhead electricity transmission networks (2011-2017). It delivered additional benefits including pollination, carbon storage, increased amenity value (European Commission 2013; Life Elia n.d.a)
Trees interfering with transmission lines require costly manual cutting and mulching
NbS, such as orchards or habitat restoration (peatlands, grasslands), help manage vegetation naturally while attracting pollinators and preserving rare species
Planting thorny woodlands along transmission line edges provides a natural barrier, enhancing safety and reducing unauthorized access
NbS can improve public acceptance of transmission projects by enhancing biodiversity, preserving landscapes, and offering ecological services
The LIFE ELIA project demonstrated that habitat restoration under power lines reduced maintenance costs, breaking even in 3–12 years and becoming 1.4–3.9 times cheaper than conventional methods over 30 years

## Slide 27: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
Integrating nature-based solutions into the energy sector - Services to hydropower
27
Restoring forests and riparian vegetation upstream of hydroelectric reservoirs helps regulate water flow, ensuring a stable water supply while reducing sedimentation, which minimizes dredging and maintenance costs
NbS prevents soil erosion and stabilizes sediments, reducing the amount of debris entering reservoirs, which can extend infrastructure lifespan and lower operational costs
By reducing turbidity, NbS decreases downtime for hydropower plants and prevents turbidity-related wear and tear on turbines and infrastructure
Healthy upstream ecosystems act as natural filters, protecting hydropower assets and improving overall energy service efficiency
NbS can increase the lifespan of built infrastructure through reducing erosion. Photograph from Browder et al. (2019).
(Arias et al. 2011; Stickler et al. 2013; Kaura et al. 2019; Guo et al. 2007; Browder et al. 2019)

## Slide 28: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
Integrating nature-based solutions into the energy sector - Services to solar power and fixed assets
28
Green roofs can anchor on green roofs, protect panels from weather impacts and support energy efficiency (Enzi et al. 2017).
Temperature Regulation & Efficiency: Maintaining wetlands around solar farms reduces ambient temperatures, improving solar panel efficiency
Green Roofs & Solar Panels: Green roofs anchor solar panels while increasing their efficiency by up to 20%, optimizing energy output
Infrastructure Protection: Restoring or managing ecosystems around solar farms protects grey infrastructure and ensures long-term service stability amid climate change

## Slide 29: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
Summary
Built infrastructure networks, such as transport (road, rail, water and air), energy and digital communications, typically rely on grey infrastructure assets for service delivery
However, there are several opportunities to leverage nature, through nature-based solutions, to enhance the delivery of sector services
By integrating nature into engineered networks, sectors can enhance service delivery, reduce maintenance requirements, benefit from cost savings, whilst delivering wider benefits for people, biodiversity and the environment
29

## Slide 30: 17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications
Bibliography
Airport Technology. 2016. “Airports go green through urban farming.” https://www.airport-technology.com/features/featureairports-go-green-through-urban-farming-4997195/.
Arias, Mauricio E., Thomas A. Cochrane, Keith S. Lawrence, Timothy J. Killeen, and Tracy A. Farrell. 2011. “Paying the forest for electricity: A modelling framework to market forest conservation as payment for ecosystem services benefiting hydropower generation.” Environmental Conservation 38 (4): 473–84. https://doi.org/10.1017/S0376892911000464.
Asian Development Bank. 2019. “ASIAN DEVELOPMENT BANK GREEN INFRASTRUCTURE DESIGN FOR TRANSPORT PROJECTS A ROAD MAP TO PROTECTING ASIA’S WILDLIFE BIODIVERSITY.” https://www.adb.org/publications/green-transport-projects-asia-wildlife.
Black, John, Kam Tara, and Parisa Pakzad. 2016. “Mainstreaming Green Infrastructure Elements into the Design of Public Road Reserves: Challenges for Road Authorities.” International Journal of Environmental Protection, January, 1–8. https://doi.org/10.5963/ijep0601001.
Browder, Greg, Suzanne Ozment, Irene Rehberger Bescos, Todd Gartner, and Glenn-Marie Lange. 2019. “Integrating Green and Gray: Creating Next Generation Infrastructure.” WRI Publications, March. https://doi.org/10.46830/wrirpt.18.00028.
Enzi, Vera, Blanche Cameron, Péter Dezsényi, Dusty Gedge, Gunter Mann, and Ulrike Pitha. 2017. “Nature-Based Solutions and Buildings – The Power of Surfaces to Help Cities Adapt to Climate Change and to Deliver Biodiversity.” In Theory and Practice of Urban Sustainability Transitions, 159–83. Springer, Cham. https://doi.org/10.1007/978-3-319-56091-5_10.
European Commission. 2013. “Guidance on a strategic framework for further supporting the deployment of EU-level green and blue infrastructure” 53 (9): 1689–99. https://ec.europa.eu/environment/nature/ecosystems/index{\_}en.htm.
———. 2018. Guidance document on Inland waterway transport and Natura 2000. Sustainable inland waterway development and management in the context of the EU Birds and Habitat Directives. https://doi.org/10.2779/779218.
———. n.d.a. “ELIA - Development of the beddings of the electricity transportation network as means of enhancing biodiversity.” Accessed March 30, 2021. https://ec.europa.eu/environment/life/project/Projects/index.cfm?fuseaction=search.dspPage{\&}n{\_}proj{\_}id=4077.
———. n.d.b. “Green Infrastructure and the Transport sector.” https://ec.europa.eu/environment/nature/ecosystems/pdf/Green Infrastructure/GI{\_}transport.pdf.
GMCA. 2019. “IGNITION - Greater Manchester Combined Authority.” https://www.greatermanchester-ca.gov.uk/what-we-do/environment/natural-environment/ignition/.
Guo, Zhongwei, Yiming Li, Xiangming Xiao, Lin Zhang, and Yaling Gan. 2007. “Hydroelectricity production and forest conservation in watersheds.” Ecological Applications 17 (6): 1557–62. https://doi.org/10.1890/06-0840.1.
Han, Heesup, Linda Heejung Lho, and Hyeon-Cheol Kim. 2019. “Airport Green Environment and Its Influence on Visitors’ Psychological Health and Behaviors.” Sustainability 11 (24): 7018. https://doi.org/10.3390/su11247018.
30

## Slide 31
Bibliography
Henderson, Joan C. 2017. “Airport roles: Pushing the boundaries at Singapore’s Changi Airport.” Asian Journal of Tourism Research 2 (3): 1–24. https://doi.org/10.12982/AJTR.2017.0015.
Hijdra, Arjan. 2021. “Ports and Nature-based Solutions: An Overview of 12+1 Financial Instruments – Water Science Policy.” https://www.watersciencepolicy.com/2021/01/31/ports-and-nature-based-solutions-an-overview-of-121-financial-instruments/ https://watersciencepolicy.com/article/ports-and-naturebased-solutions-an-overview-of-financial-instruments-a64149bd35be.
Interreg Danube. n.d. “Interreg Danube.” Accessed March 30, 2021. http://www.interreg-danube.eu/approved-projects/transgreen http://www.interreg-danube.eu/approved-projects/indeed.
Kapos, V., S. Wicander, T. Salvaterra, K. Dawkins, and C. Hicks. 2019. “The Role of the Natural Environment in Adaptation - Global Center on Adaptation.” https://gca.org/reports/the-role-of-the-natural-environment-in-adaptation/.
Kaura, Mohit, Mauricio E. Arias, Joshua A. Benjamin, Chantha Oeurng, and Thomas A. Cochrane. 2019. “Benefits of forest conservation on riverine sediment and hydropower in the Tonle Sap Basin, Cambodia.” Ecosystem Services 39 (October). https://doi.org/10.1016/j.ecoser.2019.101003.
Kennedy, Miriam, Lewis Fox-James, Sara Dethier, and Pasquale Capizzi. 2019. “Case Studies on Integrating Ecosystem Services and Climate Resilience in Infrastructure Development: Lessons for Advocacy,” 56. www.arup.com.
Life Elia. n.d.a. “Life Elia.” Accessed March 30, 2021. http://www.life-elia.eu/en/.
———. n.d.b. “Life Elia ⋅ Brochure n
2 - Cost_benefit analysis.” Accessed March 30, 2021. http://www.life-elia.eu/en/Brochure-n-2-Cost-benefit-analysis-118.
Madramootoo, C A, G T Dodds, C A Madramootool, and G T Doddsl. 1994. “Canadian Water Resources Journal ECOLOGICAL CONSIDERATIONS FOR RIVER DEVELOPMENT PROJECTS ECOLOGICAL CONSIDERATIONS FOR RIVER DEVELOPMENT PROJECTS R esearch Co ntri b uti ons/R ech erc h e s.” Canadian Water Resources Journal 19 (1). https://doi.org/10.4296/cwrj1901057.
Newman, Peter. 2014. “Biophilic urbanism: a case study on Singapore.” Australian Planner 51 (1): 47–65. https://doi.org/10.1080/07293682.2013.790832.
Paalvast, Peter, Bregje K. van Wesenbeeck, Gerard van der Velde, and Mindert B. de Vries. 2012. “Pole and pontoon hulas: An effective way of ecological engineering to increase productivity and biodiversity in the hard-substrate environment of the port of Rotterdam.” Ecological Engineering 44 (July): 199–209. https://doi.org/10.1016/j.ecoleng.2012.04.002.
Perkol-Finkel, Shimrit, Tomer Hadary, Andrew Rella, Raviv Shirazi, and Ido Sella. 2018. “Seascape architecture – incorporating ecological considerations in design of coastal and marine infrastructure.” Ecological Engineering 120 (September): 645–54. https://doi.org/10.1016/j.ecoleng.2017.06.051.
Semeraro, Teodoro, Roberta Aretano, Amilcare Barca, Alessandro Pomes, Cecilia Del Giudice, Elisa Gatto, Marcello Lenucci, et al. 2020. “A Conceptual Framework to Design Green Infrastructure: Ecosystem Services as an Opportunity for Creating Shared Value in Ground Photovoltaic Systems.” Land 9 (8): 238. https://doi.org/10.3390/land9080238.
Stickler, Claudia M., Michael T. Coe, Marcos H. Costa, Daniel C. Nepstad, David G. McGrath, Livia C. P. Dias, Hermann O. Rodrigues, and Britaldo S. Soares-Filho. 2013. “Dependence of hydropower energy generation on forests in the Amazon Basin at local and regional scales.” Proceedings of the National Academy of Sciences of the United States of America 110 (23): 9601–6. https://doi.org/10.1073/pnas.1215331110.
Trofimova, T E. 2020. “Greenspace Design for Airports.” In IOP Conference Series: Earth and Environmental Science. Vol. 459. 5. https://doi.org/10.1088/1755-1315/459/5/052033.
United Nations. 2016. “Mobilizing Sustainable Transport for Development.” Transport for Sustainable Development. https://sustainabledevelopment.un.org/content/documents/2375Mobilizing Sustainable Transport.pdf.
Vital Ports. n.d. “Home - Vital Ports.” Accessed March 30, 2021. https://www.vitalports.org/.
17.3 Designing integrated NbS-built infrastructure networks: transport, energy and digital communications

## Slide 32: 17.4 Integrating nature-based solutions (NbS) in the built environment
Learning objectives
Recall how NbS can be integrated to enhance building sector services
Recall how NbS can be integrated to promote positive outcomes in urban environments
Consider the ways in which NbS can benefit occupants across different sectors
32

## Slide 33: 17.4 Integrating nature-based solutions (NbS) in the built environment
Introduction to nature-based solutions in the built environment
33
Infrastructure Protection & Durability: Green roofs and walls shield buildings from climate impacts, enhancing lifespan and reducing maintenance costs
Sustainable Services & Water Management: Constructed wetlands aid wastewater treatment, while green roofs and rainwater harvesting systems enhance water resilience by capturing rainwater for reuse
Energy Efficiency & Cost Savings: Green roofs insulate buildings, reducing heating and cooling demands, while anchoring rooftop solar panels and increasing solar efficiency by up to 20%
Urban Integration & Global Adoption: Cities like New York, Berlin, Hong Kong, and Singapore incorporate NbS into buildings, airports, schools, and hospitals, supporting climate resilience and sustainability
(Blicharska et al. 2019; Enzi et al. 2017; Revitt, Worrall, and Brewer 2001; Stefanakis 2019)

## Slide 34: 17.4 Integrating nature-based solutions (NbS) in the built environment
Introduction to nature-based solutions in the built environment
34
Economic benefit | Description
Increased lifespan of engineered infrastructure | Green roofs can increase the lifespan of engineered roofs. For example, Liu and Baskaran (2003) report an increased lifespan of 44.4%, while Wong et al. (2003) find vegetative roofs can last three times longer. Fewer roof replacements required means reduced expenditure on replacement costs.
Reduced maintenance costs | The maintenance costs of green roofs are reported to be lower than those of grey infrastructure.
Increased property prices | Inclusion of NbS, such as street trees and urban parks, can lead to increased residential and commercial property prices. Incorporation of NbS can help to make sites and premises easier to sell or rent and help to retain occupants.
Additional economic opportunities | Green roofs can support income generation activities through increased demand for green building materials and urban farming opportunities.
Reduced wastewater treatment costs | Rain gardens and bioswales on buildings reduce stormwater runoff, minimising the amount of water requiring treatment. Cost savings arise from reducing energy cost expenditure due to reduced consumption needs for water treatment.
Reduced energy costs | Green walls and street trees can provide shading to buildings, while green roofs can promote thermal performance of roof membranes, enhancing evaporative cooling. This reduces cooling needs in summer and expenditure on ventilation. In winter, through seasonal leaf fall, the building can profit from warming sun energy, leading to reduced costs on heating. Studies show energy savings from green roofs in the range of 15-45% (for cool and white roofs up to 65%), through lower cooling needs. Karteris et al. (2016) found green roofs led to 16% reduction in energy used for cooling, and 5% for heating. In Singapore, the energy consumption of the KTP hospital is 30% less than comparable new hospitals, saving USD1million per year.
Reduced building expenditure | Green roofs have a reduced payback time and increased return on investment (ROI). Green roofs and walls act as buffers for extreme temperatures which can cause damage to building structures, leading to recurring maintenance costs.
Examples of economic benefits of integrating NbS into buildings (European Commission 2013; GMCA 2019)

## Slide 35: 17.4 Integrating nature-based solutions (NbS) in the built environment
Nature-based solutions in cities
Green roofs, parks, and urban vegetation regulate water flow, reduce stormwater runoff, and prevent sewer overflows, protecting urban water supplies
NbS attract investments, increase property values, and lower insurance premiums by mitigating climate risks like flooding and enhancing building durability
Urban greenery reduces the heat island effect, purifies air, and supports mental and physical health, lowering public health costs
Green spaces strengthen community cohesion, reduce urban violence, and improve road safety by enhancing driver focus and slowing vehicle speeds
Singapore mandates that new and refurbished buildings replace their footprint coverage with green space, ensuring integrated urban access to nature
35
Green roofs can reduce annual stormwater runoff by up to 50-90% for smaller storms (up to 25mm) and at least 30% for larger storms (GMCA 2019; Enzi et al. 2017).

## Slide 36: 17.4 Integrating nature-based solutions (NbS) in the built environment
Strategically integrating NbS to benefit offices, finance and retail
36
Studies show that employees with access to green spaces perform 10–25% better on memory tests and experience higher job satisfaction and productivity
Workers with a view of nature take fewer sick days (57 vs. 68 hours per year), potentially saving companies over $2,000 per employee annually
Green spaces enhance company reputation, attract investment, and increase retail rents while driving higher footfall in commercial areas
Well-maintained NbS boosts visitor spending, while degraded green spaces deter investment, recruitment, and retention
A green roof on top of a car park and rail yard in Illinois. The roof helps slow stormwater runoff and provides the surrounding offices with a view of nature (Browder et al. 2019)
(Green Infrastructure North West 2013; Elzeyadi 2011; GMCA 2019)

## Slide 37: 17.4 Integrating nature-based solutions (NbS) in the built environment
Strategically integrating NbS to benefit industrial sectors
37
Constructed wetlands and reed beds treat wastewater from industrial processes, reducing treatment costs and minimizing pollutant leaching into local water sources
NbS absorb pollutants, oxygenate air, and regulate indoor microclimates, reducing respiratory illnesses and improving employee well-being
Green spaces around factories reduce worker stress, enhance attention spans, and support a healthier, more productive workforce
Green roofs and living walls mitigate the urban heat island effect, benefiting both industrial facilities and surrounding communities
NbS could be integrated in and around factory buildings for various benefits including increasing the health, well-being and productivity of workers.
(Aluko and Sridhar 2005; Lamb et al. 2013; Langergraber 2013; Blicharska et al. 2019; GMCA 2019; Turhan and Gökçen Akkurt 2018)

## Slide 38: 17.4 Integrating nature-based solutions (NbS) in the built environment
Strategically integrating NbS to benefit health and education
38
Natural ecosystems provide various benefits which contribute to good health outcomes (WWF 2020)
NbS reduce stress, improve air quality, regulate temperatures, and provide spaces for exercise, enhancing overall quality of life
Studies show that hospital patients with views of trees recover faster, with lower blood pressure and heart rates, reducing healthcare costs
Green spaces boost cognitive function, attention spans, and provide hands-on learning about sustainability, biodiversity, and climate change
Green roofs and rainwater harvesting provide students with fresh food and water, reducing malnutrition and supporting education initiatives
(GMCA 2019; Green Infrastructure North West 2013; Blicharska et al. 2019; CNT 2010; Viray 2018; Newman 2014; Ulrich 1984)

## Slide 39: 17.4 Integrating nature-based solutions (NbS) in the built environment
Summary
This lecture has provided an overview of some of the ways in which nature-based solutions can be integrated into urban contexts
There are various options for integrating NbS, beyond green roofs, including therapeutic gardens, green balconies and greenspaces around factories
By investing in NbS in buildings, urban landscapes, and sectors including industry, retail, offices, health and education, cities and their occupants can benefit in multiple ways, including from improved economic productivity, improved environmental quality and health benefits
39

## Slide 40: 17.4 Integrating nature-based solutions (NbS) in the built environment
Bibliography
Aluko, Olufemi Oludare, and M. K. C. Sridhar. 2005. “Application of constructed wetlands to the treatment of leachates from a municipal solid waste landfill in Ibadan, Nigeria.” https://www.researchgate.net/profile/Olufemi-Aluko/publication/7751827{\_}Application{\_}of{\_}constructed{\_}wetlands{\_}to{\_}the{\_}treatment{\_}of{\_}leachates{\_}from{\_}a{\_}municipal{\_}solid{\_}waste{\_}landfill{\_}in{\_}Ibadan{\_}Nigeria/links/553526f30cf20ea35f0ffc21/Application-of-constructed-wetl.
Blicharska, Malgorzata, Richard J. Smithers, Grzegorz Mikusiński, Patrik Rönnbäck, Paula A. Harrison, Måns Nilsson, and William J. Sutherland. 2019. “Biodiversity’s contributions to sustainable development.” Nature Research. https://doi.org/10.1038/s41893-019-0417-9.
Bratman, Gregory N., Gretchen C. Daily, Benjamin J. Levy, and James J. Gross. 2015. “The benefits of nature experience: Improved affect and cognition.” Landscape and Urban Planning 138 (June): 41–50. https://doi.org/10.1016/j.landurbplan.2015.02.005.
Browder, Greg, Suzanne Ozment, Irene Rehberger Bescos, Todd Gartner, and Glenn-Marie Lange. 2019. “Integrating Green and Gray: Creating Next Generation Infrastructure.” WRI Publications, March. https://doi.org/10.46830/wrirpt.18.00028.
CNT. 2010. “COO The Value of Green Infrastructure A Guide to Recognizing Its Economic, Environmental and Social Benefits inside front cover intentionally lee blank.”
Elzeyadi, Ihab M. K. 2011. “Daylighting-Bias and Biophilia : Quantifying the Impact of Daylighting on Occupants Health.” https://www.semanticscholar.org/paper/Daylighting-Bias-and-Biophilia-{\%}3A-Quantifying-the-of-Elzeyadi/bfa52d19c047b0c109ee5db4b11d1c4dc0f3dc74.
Enzi, Vera, Blanche Cameron, Péter Dezsényi, Dusty Gedge, Gunter Mann, and Ulrike Pitha. 2017. “Nature-Based Solutions and Buildings – The Power of Surfaces to Help Cities Adapt to Climate Change and to Deliver Biodiversity.” In Theory and Practice of Urban Sustainability Transitions, 159–83. Springer, Cham. https://doi.org/10.1007/978-3-319-56091-5_10.
European Commission. 2013. “Building a Green Infrastructure for Europe.” https://doi.org/10.2779/54125.
GMCA. 2019. “IGNITION - Greater Manchester Combined Authority.” https://www.greatermanchester-ca.gov.uk/what-we-do/environment/natural-environment/ignition/.
Green Infrastructure North West. 2013. “Building natural value for sustainable economic development: The green infrastructure valuation toolkit user guide,” 83. www.bit.ly/givaluationtoolkit.
Kapos, V., S. Wicander, T. Salvaterra, K. Dawkins, and C. Hicks. 2019. “The Role of the Natural Environment in Adaptation - Global Center on Adaptation.” https://gca.org/reports/the-role-of-the-natural-environment-in-adaptation/.
40

## Slide 41: 17.4 Integrating nature-based solutions (NbS) in the built environment
Bibliography
Karteris, Marinos, Ifigeneia Theodoridou, Giorgos Mallinis, Emmanouel Tsiros, and Apostolos Karteris. 2016. “Towards a green sustainable strategy for Mediterranean cities: Assessing the benefits of large-scale green roofs implementation in Thessaloniki, Northern Greece, using environmental modelling, GIS and very high spatial resolution remote sensing data.” Elsevier Ltd. https://doi.org/10.1016/j.rser.2015.11.098.
Lamb, Dane T., Kartik Venkatraman, Nanthi Bolan, Nanjappa Ashwath, Girish Choppala, and Ravi Naidu. 2013. “Phytocapping: An alternative technology for the sustainable management of landfill sites.” Critical Reviews in Environmental Science and Technology 44 (6): 561–637. https://doi.org/10.1080/10643389.2012.728823.
Langergraber, Guenter. 2013. “Are constructed treatment wetlands sustainable sanitation solutions?” https://doi.org/10.2166/wst.2013.122.
Liu, Karen, and Bas Baskaran. 2003. “Thermal performance of green roofs through field evaluation.” Proceedings of the First Annual International Green Roofs Conference: Greening Rooftops for Sustainable Comunities., 10. https://www.researchgate.net/publication/44066600{\_}Thermal{\_}performance{\_}of{\_}green{\_}roofs{\_}through{\_}field{\_}evaluation http://archive.nrc-cnrc.gc.ca/obj/irc/doc/pubs/nrcc46412/nrcc46412.pdf.
Newman, Peter. 2014. “Biophilic urbanism: a case study on Singapore.” Australian Planner 51 (1): 47–65. https://doi.org/10.1080/07293682.2013.790832.
Revitt, D. M., P. Worrall, and D. Brewer. 2001. “The integration of constructed wetlands into a treatment system for airport runoff.” In Water Science and Technology, 44:469–76. 11-12. https://doi.org/10.2166/wst.2001.0868.
Stefanakis, Alexandros I. 2019. “The Role of ConstructedWetlands as Green Infrastructure for Sustainable Urban Water Management.” Sustainability (Switzerland) 11 (24): 6981. https://doi.org/10.3390/su11246981.
Stenfors, Cecilia U. D., Stephen C. Van Hedger, Kathryn E. Schertz, Francisco A. C. Meyer, Karen E. L. Smith, Greg J. Norman, Stefan C. Bourrier, et al. 2019. “Positive effects of nature on cognitive performance across multiple experiments: Test order but not affect modulates the cognitive effects.” Frontiers in Psychology 10 (JUL). https://doi.org/10.3389/fpsyg.2019.01413.
Turhan, Cihan, and Gülden Gökçen Akkurt. 2018. “Mitigation of urban heat island effect through nature-based solutions: H2020 urban GreenUP project.” IV. Uluslararası Katılımlı Anadolu Enerji Sempozyumu, no. April: 1–8. https://www.researchgate.net/publication/326441116{\_}MITIGATION{\_}OF{\_}URBAN{\_}HEAT{\_}ISLAND{\_}EFFECT{\_}THROUGH{\_}NATURE-BASED{\_}SOLUTIONS{\_}H2020{\_}URBAN{\_}GreenUP{\_}PROJECT https://www.researchgate.net/publication/326441116.
Ulrich, R. S. 1984. “View through a window may influence recovery from surgery.” Science 224 (4647): 420–21. https://doi.org/10.1126/science.6143402.
Viray, Arjun. 2018. “Current and Potential Uses of Green Roofs on Hospitals.” https://doi.org/10.15760/honors.661.
Wong, Nyuk Hien, Su Fen Tay, Raymond Wong, Chui Leng Ong, and Angelia Sia. 2003. “Life cycle cost analysis of rooftop gardens in Singapore.” Building and Environment 38 (3): 499–509. https://doi.org/10.1016/S0360-1323(02)00131-2.
WWF. 2020. Living Planet Report 2020 - Bending the curve of biodiversity loss. http://www.ecoguinea.org/papers-development.html.
41

## Slide 42: Thank you
www.climatecompatiblegrowth.com