## Slide 1: Lecture 18: Methods for integrating NbS in planning, implementation and governance
Yu Mo and Robyn Haggis, Oxford University

## Slide 2: Learning Outcomes
By the end of this lecture, you will:
Know methods and approaches to designing, implementing and governing nature-based solutions (NbS) in order to maximise potential benefits and ensure long-term project success
Understand decision-making approaches, data requirements, which stakeholders should be engaged, and the need for an adaptive management approach
Have a background to how NbS can be quantified and valued alongside engineered infrastructure solutions in the decision-making process
Understand importance of taking a landscape approach is highlighted, as well as the need for understanding the local context. The issue of timescale when working with NbS is also considered
2

## Slide 3: 18.1 Decision-making for nature-based solutions
Learning Objectives
Understand what the key considerations are when planning nature-based solutions
Learn how active adaptive management and evidenced-based decision-making can be applied when planning nature-based solutions
Obtain a basic understanding of how to account for uncertainty in the planning of nature-based solutions
3

## Slide 4: 18.1 Decision-making for nature-based solutions
Decision-making in nature-based solutions
Key Elements for Improving Decision-Making:
Use reliable data – Incorporate the best available information, including the value of ecosystem services
Ensure transparency & participation – Engage stakeholders at all levels for informed decision-making
Balance efficiency & fairness – Consider equity, long-term impacts, and trade-offs across ecosystem services
Maintain accountability – Implement monitoring, evaluation, and adaptive management
Barriers to Successful Implementation:
Institutional & Governance Issues – Corruption, weak regulation, and accountability
Market Failures – Economic incentives misaligned with sustainability goals
Lack of Representation – Failure to include marginalized communities (e.g., women, indigenous groups)
Underinvestment in Innovation – Insufficient funding for technology improving ecosystem service efficiency
Knowledge Gaps and lack of Information – Poor utilization of ecosystem management knowledge Limited data on nonmarketed ecosystem services and their link to human well-being
4
(Assessment 2005; Bauduceau et al. 2015)

## Slide 5: 18.1 Decision-making for nature-based solutions
Tools for better decision-making
Decision-Making Tools:
Deliberative Tools – Facilitate transparency and stakeholder participation (e.g., citizens’ juries, ecosystem service user forums)
Information-Gathering Tools – Collect data and opinions (e.g., environmental impact assessments, participatory rural appraisal)
Planning Tools – Evaluate policy options and trade-offs (e.g., cost-benefit analysis, multi-criteria analysis, visioning exercises)
Key Planning Tools for NbS:
Cost-Benefit Analysis – Identifies the most beneficial option while minimizing costs
Risk Assessment – Analyzes future risks and their tolerability
Multi-Criteria Analysis – Evaluates multiple conflicting factors in decision-making
Precautionary Principle – Accounts for potential negative impacts when scientific data is lacking
Vulnerability Analysis – Identifies and prioritizes weak points in a system
5
Method | Optimisation | Equity | Thresholds | Uncertainty
Cost-benefit analysis | + | + | - | +
Risk assessment | + | + | ++ | ++
Multi-criteria analysis | ++ | + | + | +
Precautionary principle | + | + | ++ | ++
Vulnerability analysis | + | + | ++ | +
Applicability of decision support methods and frameworks (Assessment 2005)
++: direct application of the method by design
+: possible application with modification or (in the case of uncertainty) the method has already been modified to handle uncertainty
–: weak but not impossible applicability with significant effort

## Slide 6: 18.1 Decision-making for nature-based solutions
The uncertainty of nature-based solutions
The integration of nature-based solutions in planning adds additional layers of uncertainty, including:
Resilience: NbS effectiveness evolves under climate change and uncertainty
Functional performance: Adaptive nature makes performance prediction less precise than grey infrastructure
Temporal factors: Benefits take time to materialize, and seasonal variations affect service delivery
Unforeseen consequences: Interconnected ecosystems may lead to unexpected impacts
Governance: Managing NbS is complex due to shifting socio-political and economic conditions
Active Adaptive Management helps reduce uncertainty by designing strategies that test ecosystem interactions and responses
This approach accelerates learning about complex socio-ecological systems, ensuring more informed decision-making.
6
(Assessment 2005)

## Slide 7: 18.1 Decision-making for nature-based solutions
Evidenced-based decision-making
7
Evidenced-based decision-making requires using evidence to answer three key issues:
Is the proposed measure effective in addressing the problem?
What are the most effective means of establishing and maintaining the green solution?
How does the effectiveness change with local conditions? Many will vary according to the climate, local ecology or societal variation
The evidence should be assessed within a four-staged process:
Collection of the possible interventions, with the objective of being as comprehensive as possible
Prioritization of interventions according to the likelihood of being implemented
Review of the published in a systematic and unbiased manner with the relevance and quality of the evidence assessed. Determination of the extent to which local environmental or social conditions modifies effectiveness
Synthesis and presentation of the results to practitioners in a manner that can be used readily by a wide range of individuals
(Bauduceau et al. 2015)

## Slide 8: 18.1 Decision-making for nature-based solutions
Case Study: Eco-safe roads in Nepal
Nepal’s rural roads are prone to landslides and erosion, often built without technical guidance, impacting economic development and increasing community vulnerability
Eco-roads established at three demonstration sites using bioengineering methods to stabilize landslide-prone roads
Vulnerability & Capacity Assessment – Geological assessments, remote sensing, and community interviews
Scientific Research – Studied erosion rates, rhizotrons, weather patterns, and cost-benefit comparisons
Capacity Building & Awareness – Training, field visits, workshops, and media outreach to promote eco-engineering
Cost-effective and locally adapted solution with strong community support
Local communities actively seeking funding for further implementation.
Significant policy influence, with Eco-Disaster Risk Reduction integrated into Nepal’s National Strategic Framework (2015-2030)
Scientific evidence strengthens policy advocacy
Community participation & livelihood integration are essential for success.
8
Demonstration site Gharelu before interventions (left) after interventions (right) (Monty et al. 2017)

## Slide 9: 18.1 Decision-making for nature-based solutions
Summary
This lecture introduces the process of decision-making when planning nature-based solutions and the common tools that can be used in the decision-making process
Particularly, this lecture discussed the uncertainly in implementing nature-based solutions, and how adaptive management and evidence-based decision-making can help to cope with that
A case study of constructing eco-roads in Nepal was presented to demonstrate the concepts
9

## Slide 10: 18.1 Decision-making for nature-based solutions
Bibliography
Assessment, Millennium ecosystem. 2005. Ecosystems and Human Well-Being: General Synthesis. Book. Vol. 5. Island Press Washington, DC.
Bauduceau, N., P. Berry, C. Cecchi, T. Elmqvist, M. Fernandez, T. Hartig, W. Krull, E. Mayerhofer, N. Sandra, and L. Noring. 2015. “Towards an EU Research and Innovation Policy Agenda for Nature-Based Solutions & Re-Naturing Cities: Final Report of the Horizon 2020 Expert Group on Nature-Based Solutions and Re-Naturing Cities.” Journal Article. Publications Office of the European Union: Brussels, Belgium.
Monty, F., R. Murti, S. Miththapala, and C. (eds) Buyck. 2017. “Ecosystems Protecting Infrastructure and Communities: Lessons Learned and Guidelines for Implementation.” Report.
10

## Slide 11: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Learning objectives
Describe the key data requirements for implementing NbS
Recall the importance of taking a system-wide landscape approach
Consider potential data sources for undertaking a baseline assessment
11

## Slide 12: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Landscape approach but rooted in the local ecological and socio-economic context
Why a Landscape Approach Matters
Ecosystem dependency – NbS success depends on wider environmental processes (e.g., hydrodynamics, sediment flux, human activity)
Interconnected impacts – Changes in one area affect biodiversity, water cycles, and climate in surrounding regions
Key Considerations
Assess interactions within and between ecosystems at scales like watersheds or forests
Balance ecological, economic, and socio-cultural factors in planning
Avoid unintended consequences by considering system-wide effects
Context-specific solutions – Evaluate local suitability for long-term success
12
(Seddon et al. 2021; Cohen-Shacham et al. 2019; Seddon et al. 2020; Cohen-Shacham et al. 2016; IUCN 2020b; IUCN 2020a)

## Slide 13: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Defining the societal challenge and understanding where NbS can help to meet service needs
NbS must address one of seven societal challenges (e.g., water security, climate resilience)
Needs assessment by NbS experts ensures solutions align with service requirements
Evidence-based approach helps define targets and measure effectiveness
Data requirements vary depending on environmental, social, and economic contexts
13
The 7 societal challenges that can be addressed by NbS. The societal challenge(s) identified should directly affect a specific group of people (e.g. a NbS to control coastal erosion endangering a specific municipality) or indirectly impact society as a whole (e.g. a NbS for mitigation) (IUCN 2020a)
(IUCN 2020a; Albert et al. 2020)

## Slide 14: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Ecological data
14
A baseline assessment helps determine the current state of ecosystems, their ability to provide services, and opportunities for improvement. It informs the design and implementation of effective NbS interventions:
Evaluate ecosystem condition & function
  Identify the extent of degradation and its impact on service delivery
  Assess ecosystem resilience to environmental and anthropogenic pressures
Determine vulnerabilities and future risks
  Understand how climate change, development, or land-use changes may affect NbS effectiveness
  Ensure selected NbS solutions remain viable over time
Identify societal needs and project objectives
  Define how NbS can address challenges such as water security, climate adaptation, or biodiversity loss
  Establish clear benchmarks for evaluating project success
Apply a landscape-scale perspective
  Recognize that relevant ecosystems extend beyond the immediate project area
  Consider upstream and downstream effects to maximize NbS benefits
Sources of Evidence for Assessment:
Scientific Research & Literature Review – Peer-reviewed studies and grey literature on ecosystem services
Local & Expert Knowledge – Stakeholder consultations, interviews, and participatory assessments
Field Surveys & Site Data Collection – Ecological measurements, biodiversity assessments, and water/soil quality analysis
Geospatial Data & Remote Sensing – Satellite imagery, GIS mapping, and historical land-use data
(IUCN 2020b; World Bank 2017)

## Slide 15: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Ecological data - Ecological data and information requirements
15
Ecological information | Description | Potential source of data
Ecosystem structure | Trophic dynamics Vegetation strata Spatial distribution and extent Degree of degradation | Geospatial ecosystem maps Government resources NGO datasets and reports Literature review NBS and local consultation
Species composition | Abundance of species from key taxonomic groups (e.g. plants, mammals, birds, soil microorganisms) | IUCN Red List
Key ecosystem functions / ecosystem services (see mini-lecture 15.2) | Provisioning services (e.g. rates of productivity) Regulating services (e.g. wave height attenuation, flow reduction rate) Supporting services (e.g. rare and endemic biodiversity) Cultural services (e.g. cultural and natural heritage, walking trails, ecotourism) | Literature review and NbS expert consultation for quantitative information on provisioning and regulating services IUCN Red List of threatened species (for information on rare biodiversity) UNESCO World Heritage Site for cultural / natural heritage
Key features of the natural environment | E.g. location of water bodies; nuance on water quantity/quality | Geospatial ecosystem maps Government resources NGO datasets and reports Literature review NbS and local consultation
Connectivity | Identifying existing or potential corridors of vegetation across the land or seascape that link prot ected/semi-protected areas, refugia for biodiversity and support genetic exchange | Geospatial ecosystem maps NGO datasets and reports Literature review
External threats to ecosystems | External threats may include development plans or climate change impacts Where possible this should be determined by the IUCN Red List of Threatened species and Red List of Ecosystems This should account for future external trends | IUCN Red list of Threatened Species Red List of Ecosystems
Existing or planned conservation interventions | Existing or ongoing conservation interventions in the target or adjacent landscape | Literature review Government reports
(IUCN 2020a)

## Slide 16: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Ecological data - Geospatial data sources
16
Data source | Description
World Terrestrial Ecosystems Map | Classifies the world into areas of similar climate, landform and landcover, which form the basic components of any terrestrial ecosystem structure. Provides a World Ecosystems Dataset which uses the ArcGIS Combine tool (Spatial Analyst) – this characterises ecosystems at a resolution of 250m and in 431 World Ecosystems Classes. Provides a layer that can be used in analysis at global and local regions. Has provided an ArcGIS Pro Package for large-scale spatial analysis. This contains original raster data with multiple table attributes. For simple mapping applications, there is a raster tile layer. Produced by adopting and modifying the IPCC approach on the definition of Terrestrial Ecosystems and development of standardised global climate regions. It can be accessed here.
World Protected Areas Database | The above layer can be combined with the World Protected Areas Database to assess the types of ecosystems that are protected, and progress towards meeting conservation goals. This layer updates monthly from the United Nations Environment Programme.
Protected Planet | Provides country level data. For example, for Ghana and for Jamaica. It also provides regional level data.
Nature Map | Nature map can be accessed here.
UN Biodiversity Map | Data is available from here.

## Slide 17: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Climate data
17
Solution identification needs to reflect how ecosystems change over time, taking into account the range of conditions that could occur
Climate data will be necessary to understand:
Potential risks to existing ecosystems and future NBS
Where a solution can leverage NbS to enhance resilience to potential climate impacts in or around the target location
Important to understand if there are factors that could undermine NbS and for identifying risk management solutions
Climate change impacts may result in shifting location, altitude or degradation of existing ecosystems and may also cause the loss of existing ecosystems, and so some options that are available today may not necessarily be present in the future
A climate impact assessment can be undertaken to identify climate change vulnerabilities and the extent to which ecosystem services are impacted
A landscape approach should be adopted, which explores risks to ecosystems, but also to ecosystems that impact the wider functioning of the target area
(IUCN 2020a; World Bank 2017; Kapos et al. 2019)

## Slide 18: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Socio-political data
18
Each NbS should be rooted in the local socio-economic and institutional context:
Stakeholder mapping
Identify ecosystem users & dependencies
Assess direct & indirect impacts on communities
Determine decision-makers & resource controllers
Evaluate local willingness & capacity for long-term involvement
Stakeholders: government and relevant government agencies, civil society organisations, local and indigenous communities, the private sector, women and youth
Review legal, regulatory, financial, and political influences
Align with national & regional development strategies
(IUCN, n.d.; Browder et al. 2019; Naumann et al. 2011; EC 2019)

## Slide 19: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Summary
Planning, designing and implementing NbS must start with a system-wide landscape approach
This is critical given the interconnectedness of nature with other aspects of the ecological and social system, both within and beyond the target area
In order to design an effective solution, it is necessary to undertake a needs assessment in order to understand the various service needs of the target area, and how nature may be leveraged to enhance service delivery
Solutions should be grounded in the local context, and therefore a baseline assessment should be conducted, to understand and map ecological and social aspects, and identify potential risks to the solution
19

## Slide 20: 18.2 Data Requirements for implementing nature-based solutions (NbS)
Bibliography
Albert, Christian, Mario Brillinger, Paulina Guerrero, Sarah Gottwald, Jennifer Henze, Stefan Schmidt, Edward Ott, and Barbara Schröter. 2020. “Planning nature-based solutions: Principles, steps, and insights.” Ambio, October, 1–16. https://doi.org/10.1007/s13280-020-01365-1.
Browder, Greg, Suzanne Ozment, Irene Rehberger Bescos, Todd Gartner, and Glenn-Marie Lange. 2019. “Integrating Green and Gray: Creating Next Generation Infrastructure.” WRI Publications, March. https://doi.org/10.46830/wrirpt.18.00028.
Cohen-Shacham, E., Angela Andrade, James Dalton, Nigel Dudley, Mike Jones, Chetan Kumar, Stewart Maginnis, et al. 2019. “Core principles for successfully implementing and upscaling Nature-based Solutions.” Elsevier Ltd. https://doi.org/10.1016/j.envsci.2019.04.014.
Cohen-Shacham, E., G. Walters, C. Janzen, and S. Maginnis. 2016. Nature-based solutions to address global societal challenges. https://doi.org/10.2305/iucn.ch.2016.13.en.
EC. 2019. “Commission staff working document. EU guidance on integrating ecosystems and their services into decision-making. Part 3/3.” https://ec.europa.eu/environment/nature/ecosystems/pdf/SWD_2019_305_F1_STAFF_WORKING_PAPER_EN_V2_P3_1042629.PDF.
IUCN. 2020a. Guidance for using the IUCN Global Standard for Nature-based Solutions. https://doi.org/10.2305/iucn.ch.2020.08.en.
———. 2020b. IUCN Global Standard for Nature-based Solutions: first editions. https://doi.org/10.2305/iucn.ch.2020.09.en.
———. n.d. “Ecosystems Protecting Infrastructure and Communities (EPIC) Technical brief.” https://www.iucn.org/sites/dev/files/content/documents/epic_technical_brief_final.pdf.
Kapos, Katherine, V Wicander, S Salvaterra, T Dawkins, and K Hicks. 2019. “The Role of the Natural Environment in Adaptation, Background Paper for the Global Commission on Adaptation.” 4. Vol. 26. https://gca.org/reports/the-role-of-the-natural-environment-in-adaptation/.
Naumann, Sandra, Matt Rayment, Paul Nolan, The Mersey Forest, Susannah Gill, Green Infrastructure, and Mersey Forest. 2011. “Design, implementation and cost elements of Green Infrastructure projects. Final Report,” no. 070307. https://ec.europa.eu/environment/enveco/biodiversity/pdf/GI_DICE_FinalReport.pdf.
Seddon, Nathalie, Alexandre Chausson, Pam Berry, Cécile A. J. Girardin, Alison Smith, and Beth Turner. 2020. “Understanding the value and limits of nature-based solutions to climate change and other global challenges.” Royal Society Publishing. https://doi.org/10.1098/rstb.2019.0120.
Seddon, Nathalie, Alison Smith, Pete Smith, Isabel Key, Alexandre Chausson, Cécile Girardin, Jo House, Shilpi Srivastava, and Beth Turner. 2021. “Getting the message right on nature-based solutions to climate change.” Global Change Biology 27 (8): 1518–46. https://doi.org/10.1111/gcb.15513.
World Bank. 2017.
20

## Slide 21: 18.3 Cost-benefit analysis for nature-based solutions
Learning objectives
Recognise that nature-based solutions are cost-effective in resolving many issues
Gain a general understanding of the common methods in estimating the monetary values of nature-based solutions
Perform cost-benefit analysis for nature-based solutions
21

## Slide 22: 18.3 Cost-benefit analysis for nature-based solutions
Nature-based solutions are cost-effective
22
NbS have economic advantages compared to traditional grey infrastructure due to
lower construction and maintenance costs
additional economic returns from co-benefits
Better understanding of the cost and benefit of nature-based solutions will inform better policy making through economic incentives:
Elimination of subsidies that promote excessive use of ecosystem services (and, where possible, transfer of these subsidies to payments for non-marketed ecosystem services)
Greater use of economic instruments and market-based approaches in the management of ecosystem services
Taxes or user fees for activities with “external” costs
Creation of markets, including through cap-and-trade systems
Payment for ecosystem services
Mechanisms to enable consumer preferences to be expressed through markets
(Assessment 2005)

## Slide 23: 18.3 Cost-benefit analysis for nature-based solutions
Methods for valuing the benefits of nature-based solutions
Nature based solutions provide different services, when estimating the value of these services, a distinction is usually made between “use or non-use,” “direct or indirect,” and “market and nonmarket”
Provisioning: Embodied in the products that are directly consumed, such as the fish produced by a fishery or a crop from agricultural land. These services are most often traded in markets. The value of these services can usually be estimated by their market price
Regulating services: Ecosystem functions that control biophysical cycles and levels, such as nutrient cycling, water filtration, or flood frequency and height. The value of these services can be estimated through the avoided cost method, the replacement cost method, and the expected damage function approach
Supporting: Underlying ecosystem processes, such as soil formation and oxygen production, which support the functioning of other ecosystem services
Cultural services: The intangible benefits ecosystems provide to people through emotional enjoyment, such as aesthetic experiences and recreation
The value of the supporting and culture service can be estimated by the property value method and the contingent valuation method
23
Method | Service | Nature-based solution | Value/ Economic returns | Source
Market price | Provisioning: fishery | Coral reefs and mangroves in American Samoa | USD0.75 million/year | (Polunin 2004)
Market price | Regulating services: Climate mitigation (carbon sequestration) | Planted mangroves in Northern Viet Nam | USD218 million | (Kapos et al. 2019)
Avoided damage | Regulating services: storm protection against hurricane Sandy (2012) | Coastal wetlands in the northeast USA | USD625 million | (Costanza et al. 2008)
Expected damage function | Regulating services: storm protection | Mangroves in Thailand | USD645,769 | (Barbier 2015)
Replacement cost | Regulating services: water filtration | Catskill watersheds | USD6-8 Billion | (Heal et al. 2005)
Value transfer + market value | Cultural service: tourism (diving/snorkeling) | Coral reefs in American Samoa | USD80,000 | (World Bank 2016)
Examples of methods for valuing nature-based solution services
(World Bank 2016)

## Slide 24: 18.3 Cost-benefit analysis for nature-based solutions
24
Cost comparison of nature-based solutions and grey infrastructure
Nature-based solutions are generally lower in cost compared to traditional grey infrastructure for climate hazard mitigation. For example coral reefs can reduce wave height similarly to tropical breakwaters but cost less than 10% of their construction cost (USD 1,290/m vs. USD 19,791/m)
Meta-study indicates nature-based defences can be 2 to 5 times less expensive than restoring natural systems compared to hard engineering.
Nature-based solutions offer increased cost effectiveness in deeper water due to rising breakwater construction costs
Hard infrastructure typically garners more confidence, necessitating careful cost-benefit analysis for nature-based options
Utilizing both nature-based solutions and grey infrastructure (hybrid approaches) can enhance project advantages
Nature-based solutions can buffer against climate change impacts, improve benefit-to-cost ratios, and provide additional co-benefits that increase over time as ecosystems mature
(Ferrario et al. 2014; Narayan et al. 2016)
Notes: There are now several open-source hazard products at global scales which are being used widely for vulnerability and risk analysis. A few resources include:
Global river and coastal flood maps: Historical and future hazard maps at different return periods (2, 5, 1, 25, 50, 10, 250, 500, 100 years). All data is available at a 30 arc-seconds resolution (~1km at equator) (Gassert et al. 2015).
Global hazard maps for earthquakes for different return periods (250, 475, 975, 1500, 2475 years) both Peak Ground Acceleration and spectral acceleration. Data is available at 0.072 degrees (~8km at equator).
Global dataset of 1,000 synthetic tropical cyclones paths with cyclone characteristics (e.g., wind speed, pressure) on a global scale. Wind speed probabilities are derived globally (1 metre, 1 minutes sustained speed) for different return periods (1 to 1,000 years) at 1km resolution (Bloemendaal et al. 2019).

## Slide 25: 18.3 Cost-benefit analysis for nature-based solutions
Case study: Cost-benefit analysis of mangrove plantation in Viet Nam
25
Cost | USD8.88 million
Benefits Dyke damage avoided Community risk avoided Aquaculture products CO2 sequestration | USD239.7 million USD295,000 USD15 million USD13.2 million* USD218 million
Benefit-cost ratio | 27
Northern Viet Nam, vulnerable coastal provinces
Project Duration: 1994 – 2010
Cost: USD 8.88 million
9,462 hectares of forest created (8,961 hectares mangroves)
Beneficiaries: 350,000 people across 166 communes
Objectives:
Reforest and afforest mangrove, casuarina, and bamboo forests
Enhance resilience against storms, flooding, sea-level rise, and drought
Economic Impact:
Estimated benefit-cost ratio: nearly 30
Excludes significant co-benefits (nutrient retention, biodiversity, flood control, etc.)
Improved co-benefit data could further enhance the benefit-cost ratio
Cost-benefit analysis of the Mangrove Plantation and Disaster Risk Reduction project (Cross 2012)

## Slide 26: 18.3 Cost-benefit analysis for nature-based solutions
Case study: Estimating the total economic value of Bermuda’s coral reefs
26
Bermuda’s known coral reef cover including hard and soft coral species (Sarkis et al. 2013)
Among the healthiest reefs in the Wider Caribbean; facing high risks due to nearby human population
Key Services:
Tourism
Fisheries
Real estate value
Coastal protection
Recreational/cultural value
Research/education
Economic Value estimated at USD722.4 million/year (Tourism 56%, Coastal Protection 37%)
Policy Recommendations:
Prioritize economically sound actions
Leverage cultural importance for management
Involve tourism in sustainability efforts
Balance reef use through strategic management
Ecosystem service | Method | Average value (million USD/year)
Tourism | The travel cost method, resulting in the “consumer surplus,” or the value of the coral reefs to tourist recreation from the visitor’s perspective The net factor income method, resulting in the “producer surplus,” or the value of coral reefs in the production of a marketed good generated through paid activities such as SCUBA diving and snorkeling The contingent valuation method, providing a ‘Willingness to Pay’ value for coral reef conservation, an additional measure of “consumer surplus” | 405.9
Coastal protection | Avoided damages | 265.9
Recreation and Cultural | ‘Willingness to Pay’ method by surveying local residents | 36.5
Fishery | Commercial fisheries Recreational fisheries | 4.9
Amenity | The hedonic pricing method, or the added value to residential properties | 6.8
Biodiversity research | Budgets of both governmental and non-governmental institutions in Bermuda | 2.3
Total | - | 722.4
The value of the six key services of Bermuda’s reef and the method used to estimate those values

## Slide 27: 18.3 Cost-benefit analysis for nature-based solutions
Summary
Nature-based solutions are effective and economically sensible
They offer higher benefit/cost ratio compared to traditional grey infrastructure by reducing construction cost and providing extra valuable co-benefits
This lecture introduces various methods for valuing services of nature-based solutions
Case studies of valuing the mangrove plantation in Viet Nam and the coral reefs in Bermuda demonstrates the application of these methods in practice
27

## Slide 28: 18.3 Cost-benefit analysis for nature-based solutions
Bibliography
Assessment, Millennium ecosystem. 2005. Ecosystems and Human Well-Being: General Synthesis. Book. Vol. 5. Island Press Washington, DC.
Barbier, Edward B. 2015. “Valuing the Storm Protection Service of Estuarine and Coastal Ecosystems.” Journal Article. Ecosystem Services 11: 32–38. https://doi.org/10.1016/j.ecoser.2014.06.010.
Costanza, Robert, Octavio Perez-Maqueo, M. Luisa Martinez, Paul Sutton, Sharolyn J. Anderson, and Kenneth Mulder. 2008. “The Value of Coastal Wetlands for Hurricane Protection.” Journal Article. AMBIO: A Journal of the Human Environment 37 (4): 241–48.
Cross, Red. 2012. “Mangrove Plantation in Viet Nam: Measuring Impact and Cost Benefit.” Journal Article. International Federation of Red Cross and Red Crescent Societies: Hanoi, Vietnam.
Ferrario, F., M. W. Beck, C. D. Storlazzi, F. Micheli, C. C. Shepard, and L. Airoldi. 2014. “The Effectiveness of Coral Reefs for Coastal Hazard Risk Reduction and Adaptation.” Journal Article. Nat Commun 5: 3794. https://doi.org/10.1038/ncomms4794.
Heal, G. M., E. B. Barbier, K. J. Boyle, A. P. Covich, S. P. Gloss, C. H. Hershner, J. P. Hoehn, C. M. Pringle, S. Polasky, and K. Segerson. 2005. “Valuing Ecosystem Services: Toward Better Environmental Decision Making Washington.” Report. DC: The National Academies Press.
Kapos, Katherine, V Wicander, S Salvaterra, T Dawkins, and K Hicks. 2019. “The Role of the Natural Environment in Adaptation, Background Paper for the Global Commission on Adaptation.” 4. Vol. 26. https://gca.org/reports/the-role-of-the-natural-environment-in-adaptation/.
Narayan, S., M. W. Beck, B. G. Reguero, I. J. Losada, B. van Wesenbeeck, N. Pontee, J. N. Sanchirico, J. C. Ingram, G. M. Lange, and K. A. Burks-Copes. 2016. “The Effectiveness, Costs and Coastal Protection Benefits of Natural and Nature-Based Defences.” Journal Article. PLoS One 11 (5): e0154735. https://doi.org/10.1371/journal.pone.0154735.
Polunin, N. 2004. “Economic Valuation of Coral Reefs and Adjacent Habitats in American Samoa Final Report.” Journal Article.
Sarkis, Samia, Pieter J. H. van Beukering, Emily McKenzie, Luke Brander, Sebastiaan Hess, Tadzio Bervoets, Lois Looijenstijn-van der Putten, and Mark Roelfsema. 2013. “Total Economic Value of Bermuda�s Coral Reefs: A Summary.” Book Section. In Coral Reefs of the United Kingdom Overseas Territories, 201–11. Springer.
World Bank. 2016. “Managing Coasts with Natural Solutions: Guidelines for Measuring and Valuing the Coastal Protection Services of Mangroves and Coral Reefs.” Report.
28

## Slide 29: 18.4 Implementing, monitoring and governing nature-based solutions (NbS) in infrastructure projects
Learning objectives
Recall why it is important to engage local and indigenous communities in NbS projects
Explain why an adaptive management approach is beneficial in NbS projects
Explain why NbS projects should include social safeguards
29

## Slide 30: 18.4 Implementing, monitoring and governing nature-based solutions (NbS) in infrastructure projects
Participatory approach - Local and indigenous communities
30
Integrating Nature-based Solutions (NbS) throughout the project lifecycle requires a participatory approach, actively engaging a diverse range of stakeholders, particularly local and indigenous communities and NbS experts
The success and sustainability of NbS projects hinge on social dimensions, including community willingness and commitment to the proposed solutions
Community involvement is crucial; without it, there is a risk of contributing to the decline of ecosystems and failing to recognize their value
Engaging local and indigenous communities is essential for aligning projects with the Sustainable Development Goals (SDGs) and ensuring that these communities benefit from the initiatives
Local and indigenous stakeholders should be involved in all phases of the project, and their feedback should be acknowledged and integrated into decision-making processes
(World Bank 2017 ; IUCN 2020b; Seddon et al. 2021; IUCN, n.d.)

## Slide 31: 18.4 Implementing, monitoring and governing nature-based solutions (NbS) in infrastructure projects
Participatory approach - Experts
31
Projects that aim to implement NbS must consider biophysical and socioeconomic processes at different spatial and temporal scales
This requires engagement with experts, from different disciplines such as climate, hydrology, engineering, ecology, economics and social sciences
(Seddon et al. 2021; Cohen-Shacham et al. 2019; World Bank 2017)
Stakeholder | Description
Local and indigenous communities | Local communities and indigenous people should be included at every stage
Experts | Experts are key to ensuring NbS are rooted in the local ecological context
Government agencies | Undertake proactive government engagement with governments at multiple levels, from political leaders to government ministries, for assistance with policies, laws, regulations, research and community outreach
Private sector | Private sector companies should be consulted where relevant to the project
Women | Including women can contribute to long-term impacts of NbS interventions whilst progressing gender equity
Youth | Incorporating youth supports sustainability, resilience and long-term impact of NbS interventions, educates them in the importance of NbS and addresses intergenerational equity
Bilateral aid agencies | These can offer more upstream, specialised expertise to help plan green-grey solutions
Civil society organisations | Can facilitate local community engagement
Development partners | To help develop and finance the project
Potential investors | Develop supportive partnerships with those who can bring financial resources (e.g. potential investors)

## Slide 32: 18.4 Implementing, monitoring and governing nature-based solutions (NbS) in infrastructure projects
Setting social and environmental safeguards
Decision-making on Nature-based Solutions (NbS) involves balancing conflicting beliefs, needs, and values among stakeholders, leading to social and environmental trade-offs
Identifying and reviewing trade-offs throughout the NbS project lifecycle is essential for ensuring project success and advancing development agendas
Social safeguards aim to protect disadvantaged groups from negative impacts of trade-offs, ensuring equitable access to benefits
Biodiversity safeguards are crucial for maintaining ecosystem services and may involve setting aside protected areas or regulating activities like fishing
Regular assessment of safeguards and trade-offs is necessary to adapt to changing circumstances, and resolution mechanisms should be in place to address grievances and conflicts
32
(IUCN 2020b, 2020a; Seddon et al. 2020, 2021 )

## Slide 33: 18.4 Implementing, monitoring and governing nature-based solutions (NbS) in infrastructure projects
The issue of timescale
33
It takes coral reefs at least 2-5 years to grow and reproduce, and longer before they reach suitable size and maturity to stabilise shorelines. By some estimates, it takes 4 decades for a restored tropical forest to fully recover its structure and ecosystem functionality (Browder et al. 2019).
Nature-based solutions (NbS) have varying timeframes for achieving full functionality and benefits, often requiring longer implementation periods than built solutions, especially for ecosystem restoration
The effectiveness of NbS can fluctuate seasonally, with varying service delivery depending on environmental conditions, yet not all projects need to reach maximum potential to meet service baseline requirements
Ecosystems evolve over time, leading to changes in the services that NbS can provide, necessitating a flexible approach to development and implementation
Successful NbS should consider the temporal dynamics of ecosystems and adopt long-term strategies (20-50 years) to ensure sustainability and resilience, while possibly integrating with built infrastructure during the transition period
(Cohen-Shacham et al. 2019; Browder et al. 2019; World Bank 2017; Seddon et al. 2021, 2020)

## Slide 34: 18.4 Implementing, monitoring and governing nature-based solutions (NbS) in infrastructure projects
Governing and managing NbS to ensure long-term success
34
Managing Nature-based Solutions (NbS) is challenging due to shifting social, economic, and environmental conditions, particularly when land rights are unclear, necessitating a balance between local needs and project goals to uphold Sustainable Development Goals (SDGs)
Community management is essential for the long-term success of NbS projects, with local and indigenous communities playing a crucial role in stewarding land and habitats
Successful NbS implementation requires collaboration with local communities and support from civil society organizations to ensure effective long-term maintenance and management
NbS are dynamic and can be affected by climate change and external factors, highlighting the need for an adaptive management approach where strategies are adjusted based on changing conditions and new information
Monitoring during and after NbS implementation is vital for assessing effectiveness, guiding necessary adjustments, and building a knowledge base to capture lessons learned
Monitoring/governing | Description
Identify new risks to the NbS | Understand new risks that may undermine the NbS and whether new actions are required to ensure NbS success.
Impacts of the NbS | Identify positive and negative social, environmental and economic consequences arising within and beyond the site. Understand if negative impacts require further mitigation.
Effectiveness | Monitor effectiveness of the NbS in addressing the societal challenge and other targets or objectives. If not, decide on follow-on actions.
Development of the NbS | Monitor how the NbS and associated service functions are progressing (if according to plan, etc.,), identify opportunities to improve performance, understand response under changing conditions.
Examples of aspects that should be monitored during NbS projects using an active management approach (IUCN 2020a)
(Seddon et al. 2020; Naumann et al. 2011; Cohen-Shacham et al. 2016; Albert et al. 2020; Cohen-Shacham et al. 2019; Spearman and Dave 2012)

## Slide 35: 18.4 Implementing, monitoring and governing nature-based solutions (NbS) in infrastructure projects
Implementing and scaling-up successful NbS
35
There is a need for more data and methods on Nature-based Solutions (NbS) to support their implementation and scaling, particularly regarding their effectiveness and cost-benefits in various scenarios, including extreme conditions
Project design and implementation should document lessons learned to help stakeholders replicate successful processes, alongside investigating appropriate methodologies
Development partners can bridge knowledge gaps by investing in performance monitoring and evaluations of NbS to enhance the evidence base and inform industry standards
Establishing open and transparent performance standards will facilitate the comparison of NbS with conventional engineering solutions, aiding in their uptake
Collaboration among investors, funders, and sectors is essential for building knowledge and awareness, while the IUCN Global Standard on NbS offers guidelines to support successful project planning and scalability
(IUCN 2020a,b; World Bank 2017)

## Slide 36: 18.4 Implementing, monitoring and governing nature-based solutions (NbS) in infrastructure projects
Summary
To ensure successful implementation and scaling-up of NbS projects, a participatory approach is required, with particular focus on engaging local and indigenous communities throughout the project lifecycle
Given that NbS are likely to involve numerous different stakeholders, trade-offs are likely, and so it is critical to develop robust social safeguards to avoid adverse unintended consequences
The NbS should be implemented and managed in line with the temporal dynamics of the ecosystem, and take an adaptive management approach, whereby actions are taken as the NbS develops to maintain long-term success
Lessons learned should be recorded and shared to support scaling-up
36

## Slide 37: 18.4 Implementing, monitoring and governing nature-based solutions (NbS) in infrastructure projects
Bibliography
Albert, Christian, Mario Brillinger, Paulina Guerrero, Sarah Gottwald, Jennifer Henze, Stefan Schmidt, Edward Ott, and Barbara Schröter. 2020. “Planning nature-based solutions: Principles, steps, and insights.” Ambio, October, 1–16. https://doi.org/10.1007/s13280-020-01365-1.
Browder, Greg, Suzanne Ozment, Irene Rehberger Bescos, Todd Gartner, and Glenn-Marie Lange. 2019. “Integrating Green and Gray: Creating Next Generation Infrastructure.” WRI Publications, March. https://doi.org/10.46830/wrirpt.18.00028.
Cohen-Shacham, E., Angela Andrade, James Dalton, Nigel Dudley, Mike Jones, Chetan Kumar, Stewart Maginnis, et al. 2019. “Core principles for successfully implementing and upscaling Nature-based Solutions.” Elsevier Ltd. https://doi.org/10.1016/j.envsci.2019.04.014.
Cohen-Shacham, E., G. Walters, C. Janzen, and S. Maginnis. 2016. Nature-based solutions to address global societal challenges. https://doi.org/10.2305/iucn.ch.2016.13.en.
IUCN. 2020a. Guidance for using the IUCN Global Standard for Nature-based Solutions. https://doi.org/10.2305/iucn.ch.2020.08.en.
———. 2020b. IUCN Global Standard for Nature-based Solutions: first editions. https://doi.org/10.2305/iucn.ch.2020.09.en.
———. n.d. “Ecosystems Protecting Infrastructure and Communities (EPIC) Technical brief.” https://www.iucn.org/sites/dev/files/content/documents/epic_technical_brief_final.pdf.
Naumann, Sandra, Matt Rayment, Paul Nolan, The Mersey Forest, Susannah Gill, Green Infrastructure, and Mersey Forest. 2011. “Design, implementation and cost elements of Green Infrastructure projects. Final Report,” no. 070307. https://ec.europa.eu/environment/enveco/biodiversity/pdf/GI_DICE_FinalReport.pdf.
Seddon, Nathalie, Alexandre Chausson, Pam Berry, Cécile A. J. Girardin, Alison Smith, and Beth Turner. 2020. “Understanding the value and limits of nature-based solutions to climate change and other global challenges.” Royal Society Publishing. https://doi.org/10.1098/rstb.2019.0120.
Seddon, Nathalie, Alison Smith, Pete Smith, Isabel Key, Alexandre Chausson, Cécile Girardin, Jo House, Shilpi Srivastava, and Beth Turner. 2021. “Getting the message right on nature-based solutions to climate change.” Global Change Biology 27 (8): 1518–46. https://doi.org/10.1111/gcb.15513.
Spearman, Margaret, and Radhika Dave. 2012. “A Review of Monitoring and Evaluation Approaches for Ecosystem-Based Adaptation,” 36. https://abcg.org/files/documents/2d63bd4f-0185-41e0-aa61-1e608f26abed.pdf.
World Bank. 2017.
37

## Slide 38: Thank you
www.climatecompatiblegrowth.com