## Slide 1: LECTURE 5 TRANSPORT MODELLING IN OSeMOSYS: BUILDING A MODEL
Transport Decarbonization and Data-to-Deal

## Slide 2: Learning Outcomes
By the end of this lecture, you will:
Understand the role of the transport sector in energy modelling.
Understand the Reference Energy System (RES) and its role in modelling.
Build your own Reference Energy System (RES)
Integrate the transport sector into an OSeMOSYS model.
Analyze and interpret transport scenarios in OSeMOSYS modelling.
Apply best practices for transport modelling.

## Slide 3: 1. The Role of Transport in Energy Modelling
3
Importance of Transport in Energy Systems
Transport is one of the hardest sectors to decarbonize and impacts other sectors like electricity and fuels (e.g., electric vehicles, biofuels).
Key contributor to energy demand
Transport accounts for ~30% of global energy use
Dependency on fossil fuels
95% of transport comes from fossil fuels
Source: UN, 2021
Large emitter of emissions
The transport sector is responsible for ~25% of greenhouse gas emissions
GHG
Notes: Transport is a significant player in global energy systems, accounting for about 30% of global energy use. This makes it one of the largest sectors in terms of energy consumption. The energy demand from transport comes from various modes such as road vehicles, aviation, shipping, and rail, all of which contribute to overall energy consumption in different ways. The sector’s energy consumption has been growing steadily, driven by population growth, urbanization, and increased demand for mobility, especially in developing countries. As economies grow, so does the demand for transport services, whether for people or goods.
A key challenge in the transport sector is its high dependency on fossil fuels. Approximately 95% of the energy consumed by the transport sector comes from fossil fuels, primarily gasoline, diesel, and jet fuel. This heavy reliance on fossil fuels has significant implications for both energy security and environmental sustainability. The transportation sector’s dependence on fossil fuels makes it vulnerable to price volatility, supply disruptions, and geopolitical risks associated with the global oil markets. Additionally, this dependence undermines efforts to transition to a low-carbon energy system and to achieve climate goals.
The transport sector is responsible for a substantial share of global greenhouse gas emissions, contributing around 25% of global emissions. This makes it a major source of carbon dioxide (CO₂) emissions, especially in urban areas where road transport and air travel are prevalent. In addition to CO₂, the sector also emits other pollutants, such as nitrogen oxides (NOx) and particulate matter, which contribute to air quality problems and health risks, especially in densely populated regions. Transport is one of the hardest sectors to decarbonize due to several factors. Unlike the electricity sector, where renewable energy sources such as solar and wind can be rapidly deployed, transport requires a much more complex shift in infrastructure, technology, and behavior.

## Slide 4: 1. The Role of Transport in Energy Modelling
4
Challenges of Decarbonizing Transport
High reliance on fossil fuels
Slow fleet turnover
Lack of charging infrastructure
High upfront costs of low-carbon techs
Energy system integration challenges
Difficult-to-decarbonize transport mode
Behavioural and cultural barriers
Policy and regulatory uncertainty
Supply chain and resource constraints
Global disparities in transport decarbonization
Notes: Decarbonizing transport presents several challenges due to the sector's heavy reliance on fossil fuels, infrastructure constraints, and behavioral factors. Here are key challenges:
1. High Reliance on Fossil Fuels.
The transport sector is still predominantly powered by petroleum-based fuels (gasoline, diesel, jet fuel).
Transitioning away from fossil fuels requires major investments in alternative fuels and vehicle technologies.
2. Slow Fleet Turnover.
Vehicles have long lifespans (10–30 years), meaning it takes time for cleaner technologies to replace older, polluting vehicles.
Policies must address both new vehicle adoption and retrofitting or phasing out existing fleets.
3. Lack of Charging and Refueling Infrastructure.
Scaling up infrastructure for electric vehicles (EVs), hydrogen fuel cells, and alternative fuels is expensive and complex.
Grid capacity and charging availability can be a barrier to EV adoption.
4. High Upfront Costs of Low-Carbon Technologies.
EVs, hydrogen trucks, and sustainable aviation fuels remain more expensive than conventional options.
Many consumers and businesses hesitate to invest due to the high initial cost.
5. Energy System Integration Challenges.
Decarbonizing transport must align with clean electricity and fuel production.
A surge in EV adoption increases electricity demand, requiring grid upgrades and renewable energy expansion.
6. Difficult-to-Decarbonize Transport Modes.
Aviation, shipping, and heavy-duty freight face technological and economic hurdles in adopting zero-carbon solutions.
Long-haul transport requires high energy density fuels, making electrification challenging.
7. Behavioral and Cultural Barriers.
Consumer preferences for larger, more powerful vehicles (e.g., SUVs) increase emissions.
Mode shift policies (e.g., encouraging public transport, cycling) require behavioral change and urban planning adjustments.
8. Policy and Regulatory Uncertainty.
Governments need stable, long-term policies (e.g., fuel standards, incentives, bans on combustion engine vehicles) to drive change.
Inconsistent policies and political shifts create uncertainty for investors and manufacturers.
9. Supply Chain and Resource Constraints.
EV batteries rely on critical minerals like lithium, cobalt, and nickel, which have supply chain and geopolitical risks.
Sustainable mining and recycling of materials need to be scaled up.
10. Global Disparities in Transport Decarbonization.
Low- and middle-income countries face additional barriers such as affordability, infrastructure gaps, and reliance on older vehicle imports.
Solutions must be tailored to different economic and geographic contexts.

## Slide 5: 1. The Role of Transport in Energy Modelling
5
Interactions Between Transport and Other Sectors – Power
The transport sector interacts deeply with the power sector (electricity generation & distribution)
1 Electrification of transport: EVs, electric buses, and railways increase electricity demand 2 Grid load and stability: Charging patterns affect peak demand and grid stability 3 Renewable integration: Smart charging and vehicle-to-grid (V2G) can support grid flexibility
Notes: The transport sector and power sector are increasingly interconnected, especially as the transition to clean energy accelerates. The growing electrification of transport and the integration of renewable energy sources are driving deeper interactions between these two sectors. Below are key points on how they interact:
Electrification of transport: As the transport sector moves towards electrification to reduce emissions and dependence on fossil fuels, new technologies such as electric vehicles (EVs), electric buses, and electric railways are becoming more widespread. This shift results in an increase in electricity demand.
Grid load and stability: As the number of electric vehicles (EVs) increases, charging patterns play a crucial role in determining how the additional load impacts the grid.
Renewable integration: The integration of renewable energy sources, such as solar and wind, with the electricity grid introduces variability and intermittency. In this context, smart charging and vehicle-to-grid (V2G) technologies can help balance supply and demand, supporting grid flexibility.

## Slide 6: 1. The Role of Transport in Energy Modelling
6
Interactions Between Transport and Other Sectors – Industry
The transport sector interacts deeply with the industry sector (manufacturing & supply chains)
1 Fuel demand: Heavy industry relies on transport for raw materials and product logistics 2 Vehicle manufacturing: Transition to EVs shifts industrial demand from oil refining to battery production 3 Freight & logistics: Efficient transport networks reduce industrial costs and emissions
Notes: The transport sector and industry sector are intricately linked, as the movement of goods, manufacturing processes, and fuel demand are all tightly interconnected. The transition to cleaner technologies and more efficient systems in both sectors can lead to cost savings, emission reductions, and greater operational synergies. Below are key points on how these sectors interact:
Fuel demand: The industrial sector, particularly heavy industries such as mining, steel, and cement production, relies heavily on the transport sector for raw materials and product logistics.
Vehicle manufacturing: As the world moves toward electric vehicles (EVs) to decarbonize the transport sector, the vehicle manufacturing process is undergoing a significant shift. This transition has important implications for the industry sector, especially in energy demand and material production.
Freight & logistics: The freight and logistics sector plays a crucial role in the wider industrial ecosystem by enabling the movement of goods between factories, warehouses, and distribution points

## Slide 7: 1. The Role of Transport in Energy Modelling
7
Interactions Between Transport and Other Sectors – Residential
The transport sector interacts deeply with the residential sector (housing & urban mobility)
1 Urban planning & transport access: Poor transport infrastructure limits access to jobs, healthcare, and education 2 Car ownership vs. public transport: Personal vehicles increase residential energy demand, while public transport reduces congestion and emissions 3 Fuel demand for heating & transport: Residential heating and private transport both impact fuel consumption patterns.
Notes: The interaction between the transport sector and the residential sector plays a crucial role in shaping urban mobility, energy demand, and emissions patterns. Urban design, the choice between car ownership and public transport, and the shared demand for fuels across heating and transport all link the two sectors closely. Below are key points on how they interact:
Urban planning & transport access: Urban planning directly impacts the accessibility of transport systems for residential areas. Poorly developed or insufficient transport infrastructure can limit access to essential services such as jobs, healthcare, and education, particularly in low-income or peripheral areas.
Car ownership vs. public transport: The decision between car ownership and public transport significantly affects residential energy demand. Personal vehicles increase the energy consumption of households, as private cars run on fossil fuels and are often less energy-efficient than public transport.
Fuel demand for heating & transport: Both residential heating and private transport have significant impacts on fuel consumption patterns. In colder climates, residential heating (especially using fossil fuels such as natural gas, coal, or oil) can be a major contributor to overall energy demand, while private transport is another major driver of fuel consumption.

## Slide 8: 1. The Role of Transport in Energy Modelling
8
Interactions Between Transport and Other Sectors – Services
The transport sector interacts deeply with the services sector (public services, retail, tourism)
1 Public transport: Supports workforce mobility and economic productivity 2 Freight & delivery services: E-commerce and logistics rely on efficient transport networks 3 Tourism & aviation: Hotels, restaurants, and cultural attractions depend on air and land transport
Notes: The transport sector has significant interactions with the services sector, encompassing public services, retail, and tourism. These relationships are essential to maintaining economic productivity, driving consumer behavior, and supporting cultural and social activities. Below are key points highlighting these interactions:
Public transport: Public transport plays a central role in enabling workforce mobility, which is crucial for economic productivity across various service sectors, including healthcare, education, and retail.
Freight & delivery services: The rise of e-commerce has placed increased demands on freight and delivery services, creating a need for efficient transport networks to ensure timely deliveries and smooth logistics.
Tourism & aviation: The tourism industry, including hotels, restaurants, and cultural attractions, is heavily reliant on air and land transport to bring visitors to destinations. Efficient transport systems are key enablers of the tourism economy, facilitating movement of tourists across regions and countries.

## Slide 9: 1. The Role of Transport in Energy Modelling
9
Interactions Between Transport and Other Sectors – Agriculture
The transport sector interacts deeply with the agriculture sector (food production & supply chains)
1 Farm machinery & transport: Tractors, harvesters, and irrigation pumps rely on diesel or electricity 2 Food supply chains: Transport affects cold storage, distribution, and food prices 3 Biofuels production: Agriculture provides feedstocks (e.g., corn, sugarcane) for biofuels, impacting land use
Notes: The transport sector plays a vital role in the agriculture sector, particularly in facilitating the movement of goods, providing energy for agricultural machinery, and supporting biofuels production. The synergy between transport and agriculture affects food production, supply chains, and land use. Below are key points on how these two sectors interact:
Farm machinery & transport: Agricultural machinery such as tractors, harvesters, and irrigation pumps often rely on either diesel or electricity to function, which ties them directly to the transport sector’s energy demand.
Food supply chains: Transport networks are central to ensuring the smooth operation of food supply chains, affecting everything from cold storage to distribution and ultimately, food prices.
Biofuels production: The agriculture sector provides the feedstocks (e.g., corn, sugarcane) required for biofuels production, which creates a direct link between agriculture and the transport sector.

## Slide 10: 1. The Role of Transport in Energy Modelling
10
Why Include Transport in Energy Modelling?
The transport sector:
Accounts for a large share of total energy demand, mainly from fossil fuels
Affects power demand (EVs), industry (vehicle manufacturing), agriculture (biofuels), and others
Thus, modelling the transport sector:
Helps assess pathways for electrification, biofuels, hydrogen, and efficiency improvements
Supports investment decisions for EV charging, fuel supply, and public transport expansion
Helps align transport policies with national climate commitments and net-zero targets
Enables testing of different policies, technology shifts, and behavioural changes
Including transport in energy modelling is essential for accurately assessing energy demand, emissions, infrastructure needs, and decarbonization pathways while ensuring alignment with climate and policy goals.
Notes: The transport sector accounts for a large share of total energy demand, mainly from fossil fuels, and affects power demand (EVs), industry (vehicle manufacturing), agriculture (biofuels), and other sectors.
Thus, modelling the transport sector:
Helps assess pathways for electrification, biofuels, hydrogen, and efficiency improvements
Supports investment decisions for EV charging, fuel supply, and public transport expansion
Helps align transport policies with national climate commitments and net-zero targets
Enables testing of different policies, technology shifts, and behavioural changes
Including transport in energy modelling is essential for accurately assessing energy demand, emissions, infrastructure needs, and decarbonization pathways while ensuring alignment with climate and policy goals.

## Slide 11: 1. The Role of Transport in Energy Modelling
11
Why Model Transport in OSeMOSYS?
OSeMOSYS (Open Source Energy Modelling System) is a free, open-source, and long-term energy system optimization model designed to support energy planning by identifying cost-optimal investment and operation strategies across multiple sectors.
Modelling the transport sector in OSeMOSYS allows for a cost-optimal assessment of energy demand, technology choices, and decarbonization pathways, while ensuring consistency with the broader energy system, including power generation, industry, and fuel supply.
Source: Howells et al., 2011
Notes: OSeMOSYS (Open Source Energy Modelling System) is a free, open-source, and long-term energy system optimization model designed to support energy planning by identifying cost-optimal investment and operation strategies across multiple sectors.
Modelling the transport sector in OSeMOSYS allows for a cost-optimal assessment of energy demand, technology choices, and decarbonization pathways, while ensuring consistency with the broader energy system, including power generation, industry, and fuel supply.

## Slide 12: 1. The Role of Transport in Energy Modelling
12
Benefits of Modelling Transport in OSeMOSYS
1 Integrated energy system approach Captures interactions between transport, power, and fuel supply
2 Cost-optimal pathways Identify least-cost technology and fuel choices for transport decarbonization
3 Flexible & open-source Allows scenario analysis with customizable assumptions and open data
4 Policy & investment insights Supports decision-making on EV adoption, biofuels, and infrastructure planning 5 Long-term scenario analysis Projects transport energy demand, emissions, and costs over decades 6 Technology representation Models different vehicle types, fuels, and efficiency improvements
Notes: There are numerous benefits of modelling transport in OSeMOSYS.
It has an Integrated Energy System Approach, which captures interactions between transport, power, and fuel supply systems, helping to understand how changes in one sector affect the others.
2. It includes Cost-Optimal Pathways, which identify least-cost technologies and fuel choices for decarbonizing transport, helping policymakers and businesses make cost-effective decisions.
3. It is Flexible & Open-Source, which enables scenario analysis with customizable assumptions and open data, making it adaptable to different contexts and accessible to a wide range of users.
4. It gives Policy & Investment Insights, which provides decision-support on policies and investments related to EV adoption, biofuels, and transport infrastructure planning.
5. It supports Long-Term Scenario Analysis, which projects future transport energy demand, emissions, and costs over decades, helping to plan for sustainable transport systems in the long run.
6. It allows Technology Representation, which models various vehicle types, fuels, and efficiency improvements, allowing for a thorough assessment of technology options for transport decarbonization.

## Slide 13: 1. The Role of Transport in Energy Modelling
13
Challenges of Modelling Transport in OSeMOSYS
1 Data gaps and uncertainty Lack of granular data and challenges in obtaining transport activity, vehicle stock, load factors, efficienciy data, and others, particularly for developing regions.
2 Complexity of transport systems
Capturing the diverse modes requires detailed parametrization, and interactions between transport demand, infrastructure and often simplified.
3 Dynamic behavioural changes Difficulty in modelling changes in consumer behaviour, such as shifts toward public transport or electric vehicles.
4 Scenario assumptions Scenarios often rely on assumptions about future trends (e.g., fuel prices) that are uncertain, which may lead to misleading outcomes if not validated.
Notes: There are also a few challenges, namely:
Data Gaps and Uncertainty: There is a scarcity of detailed data on transport activity, vehicle stock, load factors, efficiency, and other relevant variables, especially in developing regions. Missing or incomplete data creates uncertainty in modelling, affecting the accuracy of results and decision-making.
2. Complexity of Transport Systems: The transport system involves various modes (e.g., road, rail, air, maritime), each requiring different data and parameters.Transport demand, infrastructure, and operations are complex and often simplified in models, which can lead to oversights or inaccurate predictions.
3. Dynamic Behavioural Changes: Modelling changes in consumer behaviour, such as a shift to public transport or the adoption of electric vehicles (EVs), is difficult as it depends on socio-economic factors and policy influences. Predicting how behaviour will evolve over time adds an extra layer of complexity.
4. Scenario Assumptions: Many transport models depend on assumptions about future trends, such as fuel prices or technological advancements, which may not unfold as expected. If assumptions are not carefully validated, they can lead to misleading outcomes, impacting decision-making and policy advice.

## Slide 14: 2. Understand the Reference Energy System
14
What is a Reference Energy System?
A Reference Energy System (RES) is a visual/conceptual representation of an energy system that illustrates the flow of energy from primary sources (e.g., coal, oil, renewables) through various processes (e.g., conversion, transmission, distribution) to meet end-use demands (e.g., transport, residential, industrial, commercial).
Source: Babonneau et al., 2021
Notes: A Reference Energy System (RES) is a visual or conceptual representation of an energy system that illustrates the flow of energy from primary sources (e.g., coal, oil, renewables) through various processes (e.g., conversion, transmission, distribution) to meet end-use demands (e.g., transport, residential, industrial, commercial).
In this diagram, we can see that the sources, which are primary energy, on the left hand side. These include fossil, nuclear, renewables, as well as imports and exports. These are linked to conversion technologies, which are secondary energy, and include power plants, heat production, oil products, biofuels, synthetic fuels, hydrogen, liquified gas, imports and exports. Altogether, the sources and conversion technologies are part of ‘energy supply’.
From conversion technologies, the energy flows to technologies of demand, which cover the residential, commercial, agriculture, industry and transport sector. Technologies included are electric cars, diesel buses, charcoal cookstoves, and so on. This then flows to energy services, where the same sectors are represented as demands. Technologies of demand and energy services are grouped as ‘demands sectors’.

## Slide 15: 2. Understand the Reference Energy System
15
Components of a Reference Energy System
Primary energy resources: fossil fuels (coal, gas), renewables (solar, wind)
Energy conversion technologies: electricity generation (power plants), T&D
Energy carriers: coal/gas, solar/wind/hydro, electricity after power plants
End-use technologies: electric motorcycle, petrol motorcycle, petrol car
Energy service demands: motorcycle transport demand, car transport demand
Fossil
Renewables
Diesel imports
Electric motorcycle
Petrol motorcycle
Petrol car
Electric car
Diesel car
Motorcycle transport demand
Car transport demand
T&D
Electric charging
Electricity generation
Petrol
Diesel
Solar/Wind/Hydro
Coal/Gas
Electricity after power plants
Electricity for use
Resources
Conversion
End-use techs
Energy service demands
Notes: There are 5 main components of a reference energy system. Following the diagram below, these are:
Primary energy resources such as fossil fuels (coal, gas), renewables (solar, wind)
Energy conversion technologies: such as electricity generation (power plants), T&D
Energy carriers such as coal/gas, solar/wind/hydro, electricity after power plants
End-use technologies such as electric motorcycle, petrol motorcycle, petrol car
Energy service demands such as motorcycle transport demand, car transport demand
We can also see from the diagram that the RES starts from resources on the left, then conversion, then end-use technologies, finishing at energy service demands on the right.

## Slide 16: 2. Understand the Reference Energy System
16
Representation of Transport Modes in the Reference Energy System
Transport modes in the RES are modelled as energy-consuming technologies that convert fuels into mobility services (passenger-km or tonne-km).
Fossil
Renewables
Diesel imports
Electric motorcycle
Petrol motorcycle
Petrol car
Electric car
Diesel car
Motorcycle transport demand
Car transport demand
T&D
Electric charging
Electricity generation
Petrol
Diesel
Solar/Wind/Hydro
Coal/Gas
Electricity after power plants
Electricity for use
Resources
Conversion
End-use techs
Energy service demands
Passenger-km
PJ or MW
Passenger-km or 1000 vehicles
Notes: Transport modes in the RES are modelled as energy-consuming technologies that convert fuels into mobility services (passenger-km or tonne-km).
In this example for transport, we can see that the resource is in PJ or MW. The former for fuel types and the latter for solar and wind potential capacities. End-use technologies is normally represented in passenger-km, when measuring demand, or in 1,000 vehicles, when measuring capacity. End service demands, as mentioned earlier, will be in passenger-km for passenger transport, or freight-km for freight transport.

## Slide 17: 2. Understand the Reference Energy System
17
Representation of Transport Modes in the Reference Energy System
In the RES, transport modes (end-use techs) are categorized by mode and fuel type, with the level of detail depending on the desired model granularity.
Electric motorcycle
Petrol motorcycle
Petrol car
Electric car
Diesel car
Motorcycle transport demand
Car transport demand
End-use techs
Energy service demands
Diesel bus
Electric bus
CNG bus
Diesel rail
Electric rail
Diesel rail
Electric rail
LPG car
Bus transport demand
Rail passenger transport demand
Rail freight transport demand
Motorcycle
Car
Bus
Passenger rail
Freight
rail
End-use techs
Energy service demands
Notes: In the RES, transport modes (end-use techs) are categorized by mode and fuel type, with the level of detail depending on the desired model granularity.
In this example, we have 5 different modes – motorcycle, car, bus, passenger rail and freight rail. Hence we have 5 different energy service demands – motorcycle transport demand, car transport demand, bus transport demand, rail passenger transport demand, and rail freight transport demand.
We also have 5 different fuel types – electricity, petrol, diesel, liquified petroleum gas, and compressed natural gas.
Thus, the end-use techs for each demand are disaggregated by their fuel type. For the motorcycle demand, for example, we have electric motorcycle and petrol motorcycle.

## Slide 18: 2. Understand the Reference Energy System
18
Simplification
Provides a simplified yet comprehensive overview of the energy system for easier analysis.
Scenario Building
Serves as a baseline for modelling various scenarios, such as energy efficiency improvements, fuel switching, or renewable energy integration.
Decision Support
Helps policymakers, planners, and researchers understand the impacts of different energy policies and investments.
Flexibility
Can be adapted to include new technologies or shifts in energy demand.
18
Purpose of a Reference Energy System
Notes: The Purpose of a Reference Energy System comes down to four key points:
Simplification: Provides a simplified yet comprehensive overview of the energy system for easier analysis.
Scenario Building: Serves as a baseline for modeling various scenarios, such as energy efficiency improvements, fuel switching, or renewable energy integration.
Decision Support: Helps policymakers, planners, and researchers understand the impacts of different energy policies and investments.
Flexibility: Can be adapted to include new technologies or shifts in energy demand.

## Slide 19: 2. Understand the Reference Energy System
19
How does a Reference Energy System inform OSeMOSYS inputs?
Energy supply and conversion technologies The RES defines the available energy sources (e.g., coal, gas, renewables) and the technologies for converting those resources into usable energy (e.g., power plants, gas turbines, solar PV, wind turbines). These are used as input data for OSeMOSYS to simulate the supply and conversion sectors
Energy demand The RES specifies the energy demand across various sectors (e.g., residential, industrial, transportation). These demand profiles are used as inputs to OSeMOSYS, helping the model determine how to meet energy needs through different technologies and strategies
Infrastructure The RES outlines the infrastructure, such as grids, pipelines, and storage systems, that supports the transportation and storage of energy. This informs OSeMOSYS inputs related to capacity expansion, transmission, and storage systems
Notes: A RES is important to inform OSeMOSYS inputs.
The RES defines the available energy sources (e.g., coal, gas, renewables) and the technologies for converting those resources into usable energy (e.g., power plants, gas turbines, solar PV, wind turbines). These are used as input data for OSeMOSYS to simulate the supply and conversion sectors
The RES specifies the energy demand across various sectors (e.g., residential, industrial, transportation). These demand profiles are used as inputs to OSeMOSYS, helping the model determine how to meet energy needs through different technologies and strategies
The RES outlines the infrastructure, such as grids, pipelines, and storage systems, that supports the transportation and storage of energy. This informs OSeMOSYS inputs related to capacity expansion, transmission, and storage systems

## Slide 20: 3. Building a Reference Energy System
20
20
Building a Reference Energy System for the Transport Sector
Step 1: Define the system boundaries and scope
What is the region and time frame the RES will cover?
e.g. country / city
e.g. short-term / medium-term / long-term
What sectors will be included?
e.g. transportation / industrial / residential / agriculture
What components of the energy system will be represented?
e.g. electricity generation / energy storage / demand / transmission
Example: I want to model the Viet Nam transport and power sector on a country-scale and long-term. It will include electricity generation, storage, and transmission technologies, as well as transport demand.
Notes: To build a RES for the transport, we first have to define the system boundaries and scope.
The first question is what is the region and time frame the RES will cover? Will it be on a country or city scale? Will it cover the short, medium, or long-term?
The second question is what sectors will be included? Will it only focus on the transport sector? Or will it include the industrial, residential, and/or agriculture sectors?
The third question is what components of the energy system will be represented? Will it cover energy generation, storage, demand, and/or transmission?
As an example, I want to model the Viet Nam transport and power sector on a country-scale and long-term. It will include energy generation, storage, and transmission technologies, as well as transport demand.

## Slide 21: 3. Building a Reference Energy System
21
21
Building a Reference Energy System for the Transport Sector
Step 2: Identify and categorize energy sources List the available natural resources
e.g. coal, natural gas, oil, biomass, solar, wind, hydropower, uranium, etc.
Identify the technologies that convert primary energy into usable forms
e.g. coal-fired power plants, wind turbines, solar panels, nuclear power plant, etc.
Example:
I want to only include coal, oil, biomass, solar, wind, and hydropower in my model. I will also include coal, biomass, solar, wind and hydro power plants.
Notes: Step 2 is to identify and categorize the energy resources.
First, list the available natural resource that will be in your model. This could be coal, natural gas, oil, biomass, solar, wind, hydropower, uranium, and/or others.
Secondly, identify the technologies that convert primary energy into usable forms. This could be coal-fired power plants, wind turbines, solar panels, nuclear power plant, and/or others.
As an example, I want to only include coal, oil, biomass, solar, wind, and hydropower in my model. I will also include coal, biomass, solar, wind and hydro power plants.

## Slide 22: 3. Building a Reference Energy System
22
22
Building a Reference Energy System for the Transport Sector
Step 3: Identify any imports and exports
Identify if there are any imports and exports
e.g. diesel imports, fuel oil imports, electricity exports, biomass imports, coal exports, etc.
Example:
I want only to include coal, diesel, and electricity imports
Notes: Step 3 is to identify any imports and exports with your region. Are there any diesel imports, fuel oil imports, electricity exports, biomass imports, coal exports, and/or others?
For example, in my model, I want only to include coal, diesel, and electricity imports.

## Slide 23: 3. Building a Reference Energy System
23
23
Building a Reference Energy System for the Transport Sector
Step 4: Define end-use sectors, demands, and technologies
Determine the energy demand for different sectors and its granularity
e.g. transportation demand (motorcycle transport demand, car transport demand), heating demand, cooling demand, etc.
Determine the energy demand technologies and their granularity
e.g. motorcycle (petrol, electricity), car (petrol, diesel, electricity), bus (diesel, electricity), etc. Example:
I want to include motorcycles (petrol, electricity), car (petrol, diesel, electricity), bus (diesel, electricity), passenger and freight railway (diesel, electricity), and trucks (diesel, electricity)
Notes: Step 4 is to define end-use sectors, demands, and technologies.
Firstly, determine the energy demand for different sectors and its granularity. Will it have a transportation demand segregated into motorcycle transport demand and car transport demand and others, or will it just be transportation demand itself only? Will it include heating demand, cooling demand, and others, or no?
Secondly, determine the energy demand technologies and their granularity. Will it be motorcycle itself only, or will it be petrol motorcycle, electric motorcycle, petrol car, and so on?
As an example, I want to include motorcycles (petrol, electricity), car (petrol, diesel, electricity), bus (diesel, electricity), passenger and freight railway (diesel, electricity), and trucks (diesel, electricity)

## Slide 24: 3. Building a Reference Energy System
24
24
Building a Reference Energy System for the Transport Sector
Step 5: Map energy flows and interactions
Illustrate how energy flows from primary sources through to conversion processes
Coal mining
Biomass
Coal power plant
COA
Resources
Conversion
Oil
Solar
Wind
Hydropower
Biomass power plant
Solar power plant
Wind power plant
Hydro power plant
Coal imports
COA
BIO
SOL
WND
HYD
Notes: Step 5 is creating the visualization by mapping the energy flows and interactions. We will need to illustrate how energy flows from primary sources through to conversion processes.
In this example, with the scope noted in the earlier slides, my resources include coal mining, coal imports, oil, biomass, solar, wind, and hydropower. They are on the left side of the RES as this is the source. I will also include coal power plant, biomass power plant, solar power plant, wind power plant, and hydro power plant as they are the conversion technologies I want to include in my model. To link my the resources and conversion technologies, draw an arrow to show the energy flow. From coal mining and coal imports, there is an arrow each linking the resources to the coal power plant conversion. This is the same for biomass and biomass power plant, and so on.

## Slide 25: 3. Building a Reference Energy System
25
25
Building a Reference Energy System for the Transport Sector
Step 5: Map energy flows and interactions
Include refineries and distilleries, which is essential when modelling the transport sector
Coal mining
Biomass
Coal power plant
COA
Resources
Conversion
Oil
Solar
Wind
Hydropower
Biomass power plant
Solar power plant
Wind power plant
Hydro power plant
Coal imports
COA
BIO
SOL
WND
HYD
Oil refinery
Biomass plant / distillery
BIO
OIL
ELC
PETROL
DIESEL
ETHANOL
BIODIESEL
ELC
ELC
ELC
Notes: As I want to model the transport sector, fuel types such as petrol, diesel, ethanol and biodiesel will be important. To represent this, I will include refineries and distilleries. From the oil resource, I will draw an arrow to the oil refinery conversion technology. Outputs from these (as arrows) are petrol and diesel. Likewise, from the biomass resource, I will draw an additional arrow to the biomass plant / distillery conversion technology. Outputs from these (as arrows) are ethanol and biodiesel.

## Slide 26: 3. Building a Reference Energy System
Building a Reference Energy System for the Transport Sector
26
26
Step 5: Map energy flows and interactions
Ensure there is a technology to ‘blend’ the petrol & ethanol and diesel & biodiesel.
Coal mining
Biomass
Coal power plant
COA
Resources
Conversion
Oil
Solar
Wind
Hydropower
Biomass power plant
Solar power plant
Wind power plant
Hydro power plant
Coal imports
COA
BIO
SOL
WND
HYD
Oil refinery
Biomass plant / distillery
BIO
OIL
ELC
PETROL
DIESEL
ETHANOL
BIODIESEL
ELC
ELC
ELC
Blending petrol & ethanol
Blending diesel & biodiesel
PET + ETH
DIE + BIO
Notes: Now, with these fuel types, I need to ensure there is fuel blending for the biofuels. Thus, two new conversion technologies are introduced into the diagram. These are ‘blending petrol & ethanol’ and ‘blending diesel & biodiesel’. The energy carriers that go into ‘blending petrol & ethanol’ are petrol and ethanol, from the oil refinery and biomass plant / distillery conversion technologies. likewise, the energy carriers that go into ‘blending diesel & biodiesel’ are diesel and biodiesel, from the oil refinery and biomass plant / distillery conversion technologies. ‘

## Slide 27: 3. Building a Reference Energy System
27
27
Building a Reference Energy System for the Transport Sector
Step 5: Map energy flows and interactions
Include the systems that transport energy
Transmission
technology
Coal mining
Biomass
Coal power plant
COA
Resources
Conversion
Oil
Solar
Wind
Hydropower
Biomass power plant
Solar power plant
Wind power plant
Hydro power plant
Coal imports
COA
BIO
SOL
WND
HYD
Oil refinery
Biomass plant / distillery
BIO
OIL
ELC
PETROL
DIESEL
ETHANOL
BIODIESEL
ELC
ELC
Distribution
technology
ELC
ELC for EVs
EV charging
ELC for use
Electricity imports
Notes: Let’s include the systems that transport energy now. I have now added in the transmission conversion technology, with the electricity from power plants feeding into this. The electricity from transmission then feeds into a new conversion technology, the distribution technology. The electricity from distribution then feeds into EV charging technology, or it is electricity for use. This represents the transmission and distribution system, as well as charging stations for electric vehicles. Electricity imports are also included in this stage, feeding into transmission technology.

## Slide 28: 3. Building a Reference Energy System
28
28
Building a Reference Energy System for the Transport Sector
Step 5: Map energy flows and interactions
Represent storage technologies such as batteries if applicable
Transmission
technology
ELC
Distribution
technology
ELC for EVs
EV charging
ELC for use
Technology to storage
Technology from storage
Storage technology
Conversion
ELC
Electricity imports
Power plants
Notes: My model might want to have storage technologies, such as batteries. in this case, I will add 3 technologies: ‘technology to storage, storage technology, and technology from storage’ to the RES. These technologies are linked to each other, as well as the distribution technology.

## Slide 29: 3. Building a Reference Energy System
29
29
Building a Reference Energy System for the Transport Sector
Step 5: Map energy flows and interactions
Show how the energy is finally used in different sectors – motorcycles
ELC for EVs
EV charging
Conversion
Oil refinery
Biomass plant / distillery
PETROL
DIESEL
ETHANOL
BIODIESEL
Blending petrol & ethanol
Blending diesel & biodiesel
PET + ETH
DIE + BIO
Diesel imports
PETROL
DIESEL
Electric motorcycle
Petrol motorcycle
DIESEL
Motorcycle transport demand
End-use techs
Energy service demand
Notes: It is now time to finish the RES by including in end-use technologies and the energy service demand. In this example, I have electric motorcycle and petrol motorcycle as end-use technologies, which take in electricity from the EV charging technology, and petrol from the oil refinery, respectively. Both the electric motorcycle and petrol motorcycle feed into the motorcycle transport demand.

## Slide 30: 3. Building a Reference Energy System
30
30
Building a Reference Energy System for the Transport Sector
Step 5: Map energy flows and interactions
Show how the energy is finally used in different sectors – cars
ELC for EVs
EV charging
Conversion
Oil refinery
Biomass plant / distillery
PETROL
DIESEL
ETHANOL
BIODIESEL
Blending petrol & ethanol
Blending diesel & biodiesel
PET + ETH
DIE + BIO
Diesel imports
PETROL
DIESEL
Electric car
Petrol car
DIESEL
Car transport demand
Diesel car
End-use techs
Energy service demand
Notes: In this example, I have electric car and petrol car, which take in electricity from the EV charging technology, petrol from the oil refinery, respectively. I also have a diesel car, which I am also assuming takes in biofuel. Since a diesel car can take in pure diesel and blended diesel & biodiesel, there are links from the oil refinery, the ‘blending diesel & biodiesel’ technology, and diesel imports. All these cars, electric, petrol, and diesel, feed into the car transport demand.

## Slide 31: 3. Building a Reference Energy System
31
31
Building a Reference Energy System for the Transport Sector
Step 5: Map energy flows and interactions
Show how the energy is finally used in different sectors – buses
ELC for EVs
EV charging
Conversion
Oil refinery
Biomass plant / distillery
PETROL
DIESEL
ETHANOL
BIODIESEL
Blending petrol & ethanol
Blending diesel & biodiesel
PET + ETH
DIE + BIO
Diesel imports
PETROL
DIESEL
Electric bus
DIESEL
Bus transport demand
Diesel bus
End-use techs
Energy service demand
Notes: In this example, I have electric bus and diesel bus as end-use technologies, which take in electricity from the EV charging technology, and diesel from the oil refinery and imports, respectively. Both the electric bus and diesel bus feed into the bus transport demand.

## Slide 32: 3. Building a Reference Energy System
32
32
Building a Reference Energy System for the Transport Sector
Step 5: Map energy flows and interactions
Show how the energy is finally used in different sectors – railway
ELC for EVs
EV charging
Conversion
Oil refinery
Biomass plant / distillery
PETROL
DIESEL
ETHANOL
BIODIESEL
Blending petrol & ethanol
Blending diesel & biodiesel
PET + ETH
DIE + BIO
Diesel imports
PETROL
DIESEL
Electric passenger rail
DIESEL
Rail passenger transport demand
Diesel passenger rail
Electric freight rail
Diesel freight rail
ELC for EVs
Rail freight transport demand
End-use techs
Energy service demand
Notes: In this example, I have electric rail and diesel rail as end-use technologies, which take in electricity from the EV charging technology, and petrol from the oil refinery, respectively. However, note that there are 4 different end-use technologies for rail because 2 are for passenger and 2 are for freight. When there is a transport mode that serves both passenger and freight demand, it is important to model these separately, as the units and characteristics are different. The electric passenger rail and diesel passenger rail end-use technologies feed into the rail passenger transport demand, whilst the electric freight rail and diesel freight rail end-use technologies feed into the rail freight transport demand.

## Slide 33: 3. Building a Reference Energy System
33
33
Building a Reference Energy System for the Transport Sector
Step 5: Map energy flows and interactions
Show how the energy is finally used in different sectors – trucks
ELC for EVs
EV charging
Conversion
Oil refinery
Biomass plant / distillery
PETROL
DIESEL
ETHANOL
BIODIESEL
Blending petrol & ethanol
Blending diesel & biodiesel
PET + ETH
DIE + BIO
Diesel imports
PETROL
DIESEL
Electric truck
DIESEL
Truck transport demand
Diesel truck
End-use techs
Energy service demand
Notes: In this example, I have electric truck and diesel truck as end-use technologies, which take in electricity from the EV charging technology, and diesel from the oil refinery and imports, respectively. Both the electric truck and diesel truck feed into the bus transport demand.

## Slide 34: 3. Building a Reference Energy System
34
34
Building a Reference Energy System for the Transport Sector
Additional support:
Building a RES depends on multiple factors. As a guide and for a detailed transport RES, please see: https://zenodo.org/records/10948724
Notes: Building a RES depends on multiple factors. As a guide and for a detailed transport RES, please see: https://zenodo.org/records/10948724

## Slide 35: 4. Transport Modelling in OSeMOSYS
35
Key Data for Transport Modelling in OSeMOSYS
1 Accumulated Annual Demand
2 Capacity to Activity Unit
3 Output Activity Ratio
4 Input Activity Ratio
5 Residual Capacity
6 Operational Life
7 Capital Cost
8 Fixed Cost
9 Variable Cost
10 Emission Activity Ratio
Notes: There are 10 key data needed for transport modelling in OSeMOSYS.
Accumulated Annual Demand
Capacity to Activity Unit
Output Activity Ratio
Input Activity Ratio
Residual Capacity
Operational Life
Capital Cost
Fixed Cost
Variable Cost
Emission Activity Ratio

## Slide 36: 4. Transport Modelling in OSeMOSYS
36
Define the Scope and Boundaries
Time horizon: Choose the years you want to model (e.g., 2020-2050)
Geographical scope: National or regional level?
Transport modes: Road, rail, aviation, maritime, inland waterways
Vehicle types: Passenger cars, buses, trucks, motorcycles, trains, planes, ships, etc.
Energy carriers: Gasoline, diesel, electricity hydrogen, biofuels, etc.
Notes: When modelling transport in OSeMOSYS, it is essential to define the scope and boundaries clearly. This ensures that the model accurately represents transport demand, energy use, and emissions.
Time horizon: Choose the years to be modelled, such as 2020–2050. A longer horizon allows for assessing long-term transitions, while a shorter horizon focuses on near-term policy impacts.
Geographical scope: Define whether the model will represent a national, regional, or subnational transport system. The choice affects data availability, infrastructure considerations, and policy analysis.
Transport modes: Include different modes such as Road transport (cars, buses, trucks, motorcycles), Rail transport (passenger and freight trains), Aviation (domestic and international flights), Maritime transport (ships, ferries), Inland waterways (barges, river transport)
Vehicle types: Specify vehicle types within each mode such as Passenger vehicles (cars, buses, trains, planes), Freight transport (trucks, cargo ships, freight trains), Specialized vehicles (two-wheelers, electric buses, high-speed rail)
Energy carriers: Model the fuels and energy sources used in transport, such as Fossil fuels (gasoline, diesel), Electricity (for EVs, rail), Hydrogen (for fuel-cell vehicles), Biofuels (ethanol, biodiesel)

## Slide 37: 4. Transport Modelling in OSeMOSYS
37
Gather and Prepare Input Data
Demand projections: Passenger-km (pkm) and tonne-km (tkm)
Technology costs: Investment and fixed costs of transport technologies
Fuel costs: Import prices, local production costs
Load factors: Occupancy rates (passengers) and/or load (freight) for different vehicles
Energy intensities: Energy use per unit of activity (MJ/pkm or MJ/tkm)
Emission factors: CO2, NOX, PM, and other pollutants
Notes: To model transport in OSeMOSYS, it is crucial to gather and prepare high-quality input data. This ensures that the model accurately represents energy demand, technology costs, and emissions. This includes:
Demand projections in passenger-km and tonne-km
Technology costs including the investment costs and fixed costs of transport technologies
Fuel costs such as import prices, local production costs
Load factors like Occupancy rates (passengers) and/or load (freight) for different vehicles
Energy intensities including energy use per unit of activity (MJ/pkm or MJ/tkm)
Emission factors such as CO2, NOX, PM, and other pollutants

## Slide 38: 4. Transport Modelling in OSeMOSYS
38
Define Sets in OSeMOSYS
OSeMOSYS uses sets to define technologies and fuels
Define technologies:
Each vehicle type is modelled as a separate technology
Passenger transport: petrol car, diesel car, electric car, diesel bus, etc.
Freight transport: diesel truck, electric truck, heavy fuel oil ship, etc.
Define fuels (e.g., energy carriers):
Gasoline, diesel, electricity, hydrogen, natural gas, biofuels, etc.
Set up demand categories:
Passenger demand: motorcycle demand, car demand, rail passenger demand, etc.
Freight demand: truck demand, rail freight demand, maritime demand, etc.
Notes: OSeMOSYS uses sets to structure transport technologies, fuels, and demand categories, enabling flexible and detailed representation of energy use in the transport sector.
When defining technologies, each vehicle type is modelled as a separate technology such as petrol car, diesel car, electric car, diesel bus for passenger transport, and diesel truck, electric truck, heavy fuel oil ship for freight transport.
When defining fuels such as energy carriers, note that OSeMOSYS assigns specific fuels (energy carriers) to each transport technology, allowing analysis of fuel demand and shifts due to electrification or alternative fuels. Common transport fuels are gasoline, diesel, electricity, hydrogen, natural gas, biofuels.
When setting up demand categories, the transport demand is categorized into passenger and freight segments, enabling the model to reflect different mobility needs and vehicle utilization rates. Passenger demand include motorcycle demand, car demand, rail passenger demand. Freight demand include truck demand, rail freight demand, maritime demand.

## Slide 39: 4. Transport Modelling in OSeMOSYS
39
Define Parameters in OSeMOSYS
Key parameters are:
InputActivityRatio: Defines how much fuel is used per unit of transport demand
OutputActivityRatio: Ensures 1 unit of demand is met by 1 unit of activity
CapitalCost, FixedCost, VariableCost: Investment and operating costs of vehicles, as well as fuel costs
EmissionActivityRatio: Emission factors for each technology
CapacityToActivityUnit: Defines how much demand a unit of vehicle capacity serves
Notes: When modeling transport in OSeMOSYS, several key parameters define the relationship between energy use, costs, emissions, and transport activity. These parameters ensure an accurate representation of fuel consumption, costs, and emissions across different vehicle technologies.
InputActivityRatio: defines how much fuel is used per unit of transport demand
OutputActivityRatio: Ensures 1 unit of demand is met by 1 unit of activity
CapitalCost, FixedCost, VariableCost: Investment and operating costs of vehicles, as well as fuel costs
EmissionActivityRatio: Emission factors for each technology
CapacityToActivityUnit: Defines how much demand a unit of vehicle capacity serves

## Slide 40: 4. Transport Modelling in OSeMOSYS
40
Enhance a Model in OSeMOSYS
Extend the model by incorporating policy measures, mode shift, charging infrastructure, and behavioural changes to improve realism and assess the impact of different transport strategies
Include policy measures: EV subsidies, fuel taxes, CO₂ pricing
Integrate mode shifts: Shift demand between modes based on policy assumptions
Add charging infrastructure: For electric vehicles, hydrogen cell vehicles
Consider behavioural changes: Telecommuting, urban transport policies.
Notes: To improve the realism of transport modelling and assess the impact of different strategies, the model can be extended to include policy measures, mode shifts, infrastructure needs, and behavioral changes. These additions help capture the evolving dynamics of transport systems and their interactions with the energy sector.
Incorporating policy measures such as Reducing the upfront cost of electric vehicles to accelerate adoption, Increasing the cost of fossil fuels to encourage a shift to cleaner alternatives, and Applying carbon pricing mechanisms to internalize the environmental cost of transport emissions. These measures influence technology choices, fuel demand, and emissions trajectories in transport scenarios
Integrate mode shifts such as Policies encouraging a shift from private vehicles to buses, metro, and rail, Promoting walking and cycling infrastructure to reduce short-distance car trips, and Increasing rail and maritime transport for long-distance freight to reduce road transport emissions. Mode shifts can reduce energy consumption, emissions, and infrastructure strain while improving efficiency.
Add charging infrastructure like Expanding fast-charging stations for electric vehicles, Supporting fuel-cell vehicle adoption, and Ensuring the electricity system can handle increased demand from EVs. Without adequate infrastructure, electrification strategies may face adoption barriers and energy security risks
Consider behavioural changes like Reducing travel demand for commuting, Implementing congestion pricing, low-emission zones, and car-free areas, and Encouraging carpooling, ride-sharing, and micro-mobility solutions like e-scooters. Behavioral changes can significantly influence transport energy demand, congestion, and emissions.

## Slide 41: 5. Interpreting a Transport Model in OSeMOSYS
41
Energy consumption: Breakdown of fuel use by transport mode and energy carrier
Emissions: CO₂ and other pollutants from different transport technologies
Costs: Total system costs, investment costs, and operational expenses
Technology shares: Adoption of various vehicle types over time
Capacity utilization: Efficiency of vehicle use and infrastructure
Understanding Key Outputs in a Transport Model
Notes: Understanding the key outputs of a transport model in OSeMOSYS is essential for analyzing the sector’s energy demand, emissions, costs, and technology evolution. These outputs help assess the impact of different policy measures, technology shifts, and investment strategies.
Energy consumption, including Breakdown of fuel use by transport mode and energy carrier, Provides insights into fuel demand trends and helps plan for infrastructure needs (e.g., charging stations, fuel supply chains).
Emissions, such as CO₂ and other pollutants from different transport technologies, Supports climate policy alignment by assessing how different scenarios contribute to net-zero targets and air pollution reduction.
Costs, including Total system costs, investment costs, and operational expenses, Helps policymakers and investors compare cost-optimal pathways for transport decarbonization.
Technology shares, such as Adoption of various vehicle types over time, Helps evaluate the effectiveness of policies such as EV subsidies and fuel taxes in shifting transport technology.
Capacity utilization, including Efficiency of vehicle use and infrastructure, Ensures that transport infrastructure investments align with projected demand and technology adoption rates.

## Slide 42: 5. Interpreting a Transport Model in OSeMOSYS
42
A thorough analysis of the results ensures that the model provides meaningful insights into transport system performance, guiding policy and investment decisions for a sustainable and efficient future
Check Fuel Use: Does the energy consumption match expected values?
Compare Emissions: Are emissions reductions achieved under different scenarios?
Assess Costs: Which technologies are cost-optimal?
Scenario Analysis: Vary transport policies, fuel costs, and technology assumptions.
Run and Analyze Results
Notes: A thorough analysis of model results is essential for guiding policy and investment decisions toward a sustainable and efficient transport future. Key checks include evaluating energy use, emissions, costs, and scenario variations to ensure that the model provides realistic and actionable insights.
Checking fuel use Ensures the model accurately represents fuel use across different transport modes and identifies potential infrastructure needs (e.g., refueling stations, EV charging networks).
Comparing emissions Validates whether policy measures (e.g., EV adoption, fuel switching) effectively reduce transport-related emissions and contribute to net-zero goals.
Assessing costs helps policymakers and investors identify the most cost-effective pathways for transport decarbonization while considering affordability and feasibility.
Analyzing scenarios Enhances the model’s robustness by testing how sensitive results are to changes in key inputs, ensuring reliable decision-making under uncertainty.

## Slide 43: 6. Best Practices for Transport Modelling
43
When developing a transport modelling, thorough documentation and transparency are essential. This ensures clarity, reproducibility, and enables collaboration while fostering trust in the model’s results.
The U4RIA goals extend best practices and advances in transparency through a set of guidelines:
The U4RIA Goals
Source: Howells et al., 2021
Ubuntu – modelling should engage communities.
Retrievability – should be easy to find and access data.
Reusability – should be re-usable.
Repeatability - should be repeatable and user friendly.
Reconstructability – should include instructions to rebuild the energy modelling elements.
Interoperability – should allow for scenarios to be tested by other models or approaches and their compatibility to sub-sector or broader integration.
Auditability – should provide direct accountability to the funder of the energy modelling for policy support, as well as to society more broadly.
Notes: When developing a transport modelling, thorough documentation and transparency are essential. This ensures clarity, reproducibility, and enables collaboration while fostering trust in the model’s results.
The U4RIA goals extend best practices and advances in transparency through a set of guidelines:
Ubuntu. This is a concept borrowed from African philosophy regarding our shared humanity. Here this refers to the fact that communities should be involved with energy modelling.
Retrievability. It is often the case that it is difficult to find data. However, it should be the case that data are easily accessed and found.
Reusability. The model should be re-usable, no matter the amount of times the model is licensed.
Repeatability. The model should be repeatable and user friendly in a digital workflow.
Reconstructability. This extends the concept of repeatability to include the instructions for how to rebuild the energy modelling elements. For example, input data, model relations, and resulting scenarios.
Interoperability. This allows for scenarios to be tested by other models or approaches and integrate with other sub-sectors and more broadly in general.
Auditability. This means that there should be direct accountability to the internal or external funders of the energy modelling for policy support, as well as to society more broadly.

## Slide 44: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Naomi Tan
Imperial College London/Loughborough University