## Slide 1: LECTURE 6 TRANSPORT MODELLING IN OSeMOSYS: TRANSPORT DATA
Transport Decarbonization and Data-to-Deal

## Slide 2: Learning Outcomes
By the end of this lecture, you will:
Understand the data requirements for transport modelling in OSeMOSYS.
Learn how to source transport data for OSeMOSYS.
Address data gaps and uncertainty.
Explore practical approaches to transport data collection and validation.

## Slide 3: 1. Data for Transport Modelling in OSeMOSYS
3
Key Data Categories for Transport Modelling
Population and GDP
Drivers of transport demand
Passenger and freight activity
Key demand metrics
Vehicle stock
Number and types of vehicles
Load factor
Average capacity utilization of vehicles
Energy efficiency
Energy use per unit of demand
OSeMOSYS data inputs
Notes: Transport modelling in OSeMOSYS requires several key data inputs to effectively represent the relationship between transport demand, vehicle stock, and energy consumption. These inputs help define how transport services are delivered and how energy is used within the system.
The Key Data Categories for Transport Modelling are:
Population and GDP
  Population growth and economic development are fundamental drivers of transport demand.
  As population increases, the demand for passenger transport (e.g., commuting, public transport usage) rises.
  Higher GDP per capita is often associated with increased vehicle ownership, greater freight transport activity, and shifts in transport mode preferences.
Passenger and Freight Activity
  Passenger and freight movement are key metrics that define overall transport demand.
  Passenger activity is measured in passenger-kilometers (pkm), representing the total distance traveled by passengers.
  Freight activity is measured in tonne-kilometers (tkm), reflecting the volume of goods transported over a given distance.
Vehicle Stock
  The number and types of vehicles in the system influence energy demand and emissions.
  This includes different modes such as cars, buses, trucks, trains, and motorcycles, each with distinct energy consumption patterns.
  Vehicle stock also determines the potential for fuel switching (e.g., adoption of electric or hydrogen-powered vehicles).
Load Factor
  Load factor measures the average utilization of vehicle capacity.
  It indicates how efficiently vehicles are being used—whether they are typically full or operating below capacity.
  Higher load factors improve energy efficiency by reducing energy consumption per passenger or freight unit transported.
Energy Efficiency
  Energy efficiency defines how much energy is required per unit of transport demand.
  This varies by vehicle type, fuel type, and technology (e.g., internal combustion engine vs. electric vehicle).
  Improving energy efficiency is key to reducing overall fuel consumption and emissions.
Most of these data inputs serve as the foundation for transport modeling in OSeMOSYS. They allow for the assessment of future transport demand, fuel consumption, and emissions under different policy and technology scenarios. By incorporating these factors, the model can evaluate the impact of policy measures, efficiency improvements, and transitions to cleaner transport technologies.

## Slide 4: 1. Data for Transport Modelling in OSeMOSYS
4
1 Accumulated Annual Demand
2 Capacity to Activity Unit
3 Output Activity Ratio
4 Input Activity Ratio
5 Residual Capacity
6 Operational Life
7 Capital Cost
Key Data for Transport Modelling in OSeMOSYS
8 Fixed Cost
9 Variable Cost
10 Emission Activity Ratio
Notes: Transport modelling in OSeMOSYS relies on a structured set of data inputs that define the operation, costs, and emissions of transport technologies. These parameters are essential for capturing the dynamics of transport demand, infrastructure, and energy consumption over time.
The Key Data Categories for Transport Modelling in OSeMOSYS are:
Accumulated Annual Demand
  Represents the total transport demand over a given period (e.g., passenger-kilometers or tonne-kilometers).
  Used to ensure that the system meets expected transport service requirements.
Capacity to Activity Unit
  Defines the relationship between installed capacity and the level of transport activity that can be supported.
  For example, how many passenger-kilometers or tonne-kilometers a unit of vehicle capacity can provide.
Output Activity Ratio
  Determines the amount of useful transport service (e.g., pkm or tkm) generated per unit of activity from a transport technology.
  This is crucial for assessing the effectiveness of different transport modes.
Input Activity Ratio
  Specifies the energy or fuel required per unit of transport activity.
  Helps model energy consumption patterns for various transport technologies.
Residual Capacity
  Represents existing transport infrastructure or vehicle stock that continues to operate in future model years.
  Allows for a phased transition rather than assuming all vehicles are newly introduced.
Operational Life
  Defines the lifespan of transport technologies, including vehicles, infrastructure, and equipment.
  Ensures that replacements and decommissioning of assets are accounted for in long-term planning.
Capital Cost
  Represents the investment cost required to deploy transport technologies.
  Key factor in determining the feasibility of new infrastructure, vehicle fleets, and technology shifts.
Fixed Cost
  Captures the costs that do not vary with the level of transport activity, such as infrastructure maintenance.
  Important for evaluating long-term financial commitments in the transport sector.
Variable Cost
  Reflects costs that change with transport activity, such as fuel costs, operational expenses, and maintenance per kilometer traveled.
  Critical for assessing the economic competitiveness of different transport options.
Emission Activity Ratio
Defines the emissions generated per unit of transport activity.
Used to calculate total transport-sector emissions under different scenarios and to evaluate decarbonization strategies.

## Slide 5: 1. Data for Transport Modelling in OSeMOSYS
5
AccumulatedAnnualDemand[r,f,y]
Accumulated demand for a certain commodity in one specific year. It cannot be defined for a commodity if its SpecifiedAnnualDemand for the same year is already defined and vice versa.
Linking Data to OSeMOSYS Parameters – Accumulated Annual Demand
Passenger:
Freight:
Example:
The freight activity for light-duty vehicles was 800 million tonnes-km in 2020. Its Accumulated Annual Demand would be 0.8 billion tkm.
Notes: Accumulated Annual Demand is the accumulated demand for a certain commodity in one specific year. It cannot be defined for a commodity if its SpecifiedAnnualDemand for the same year is already defined and vice versa.
For passenger transport, it is expressed in billion passenger-kilometres (pkm) and it measures the total distance traveled by passengers across all transport modes.
For freight transport, it is expressed in billion tonne-kilometres (tkm) and represents the total weight of goods transported over a given distance.
As an example, suppose the freight activity for light-duty vehicles in 2020 was 800 million tonne-kilometers. Since 1 billion is equal to 1,000 million, the Accumulated Annual Demand would be 0.8 billion tkm

## Slide 6: 1. Data for Transport Modelling in OSeMOSYS
6
AccumulatedAnnualDemand[r,f,y]
Accumulated demand for a certain commodity in one specific year. It cannot be defined for a commodity if its SpecifiedAnnualDemand for the same year is already defined and vice versa.
Linking Data to OSeMOSYS Parameters – Accumulated Annual Demand
Passenger:
Freight:
Example:
The total distance travelled by car was 150,000 km. On average, there are 3 passengers in a car. The Accumulated Annual Demand is 150000 * 3 = 450000 pkm
We can calculate the demand based on the following equations:
Notes: We can calculate the Accumulated Annual demand based on these equations.
For passenger transport, the Accumulated Annual Demand is the distance travelled (in km) multiplied by the average load factor (in number of passengers).
For freight transport, the Accumulated Annual Demand is the distance travelled (in km) multiplied by the average load factor (in tonnes).
As an example, suppose the total distance travelled by car was 150,000 km. On average, there are 3 passengers in a car. The Accumulated Annual Demand is therefore 150,000 multiplied by 3, which is 450,000 passengers-km.

## Slide 7: 1. Data for Transport Modelling in OSeMOSYS
7
AccumulatedAnnualDemand[r,f,y]
Accumulated demand for a certain commodity in one specific year. It cannot be defined for a commodity if its SpecifiedAnnualDemand for the same year is already defined and vice versa.
Linking Data to OSeMOSYS Parameters – Accumulated Annual Demand
Passenger and Freight:
Example:
Fuel consumption for cars includes 6.5 PJ of petrol, 2.4 PJ of diesel, and 0.8 PJ of electricity. The efficiencies are 0.5 Bn pkm/PJ, 0.53 Bn pkm/PJ, and 2.8 Bn pkm/PJ for petrol, diesel, and electricity, respectively.
The Accumulated Annual Demand is (6.5 * 0.5) + (2.4 * 0.53) + (0.8 * 2.8) = 6.76 Bn pkm
We can also calculate the demand based on the following equation:
Notes: We can also calculate the Accumulated Annual demand based on another equation.
For passenger and freight transport, the Accumulated Annual Demand = energy consumption multiplied by technology efficiency for all technologies.
As an example, suppose the Fuel consumption for cars includes 6.5 PJ of petrol, 2.4 PJ of diesel, and 0.8 PJ of electricity. The efficiencies are 0.5 Bn pkm, 0.53 Bn pkm, and 2.8 Bn pkm for petrol, diesel, and electricity, respectively.
The demand for petrol technologies is 6.5 times 0.5 = 3.25
The demand for diesel technologies is 2.4 times 0.53 = 1.272
The demand for electric technologies is 0.8 times 2.8 = 2.24
The Accumulated Annual Demand is the total for these, so it is 3.25+1.272+2.24 = 6.76 Billion passenger-km

## Slide 8: 1. Data for Transport Modelling in OSeMOSYS
8
CapacityToActivityUnit[r,t]
Conversion factor relating the energy that would be produced when one unit of capacity is fully used in one year.
Linking Data to OSeMOSYS Parameters – Capacity to Activity Unit
Passenger:
Freight:
Example:
The activity for cars was 2.3 million pkm in 2020. There were 1.7 million cars. Its CTAU would be (2.3 / 1000) / (1.7 * 1000) = 0.00000135 = 1.35x10-6 Bn pkm / 1000 vehicles.
To convert from millions to billions
To convert to from million to thousands
Notes: The capacity to activity unit is the conversion factor relating to the energy that would be produced when one unit of capacity is fully used in one year.
For passenger transport, the capacity to activity unit is in billion passenger-km per 1,000 vehicles.
For freight transport, the capacity to activity unit is in billion tonne-km per 1,000 vehicles.
As an example, suppose the activity for cars was 2.3 million passenger-km in 2020. There were 1.7 million cars.
First, convert 2.3 million to billions by dividing by 1,000. This would give us 0.0023 billion passenger-km.
Next, convert 1.7 million cars to thousands by multiplying by 1,000. This would give us 1,700 thousand cars.
We now divide the activity by capacity, 0.0023 divided by 1,700. This will give us 0.00000135 billion passengers-km per 1,000 vehicles.

## Slide 9: 1. Data for Transport Modelling in OSeMOSYS
9
InputActivityRatio[r,t,f,m,y]
Rate of use of a commodity by a technology, as a ratio of the rate of activity.
Linking Data to OSeMOSYS Parameters – Input Activity Ratio
Passenger:
Example:
The fuel content of a petrol car is 34 MJ/L and its fuel economy is 7 L/100km.
The average number of people in the car is 2.
The IAR is (34 / 109) * (7 / 100) * (1 / (2 / 109)) = 1.19 PJ / billion pkm.
To convert from MJ to PJ
To convert to from L/100km to L/km
To ensure it is in billions
Notes: The input activity ratio is the rate of use of a commodity by a technology, as a ratio of the rate of activity.
For passenger transport, the input activity ratio is in petajoules of fuel per billion passenger-km. If data is scarce, the input activity ratio can also be calculated through an equation which multiplies the fuel content by fuel consumption and the inverse of the load factor.
Fuel content is in PJ per litre, fuel consumption is litre per km, and load factor is in billion passengers.
As an example, suppose The fuel content of a petrol car is 34 MJ per litre and its fuel economy is 7 Litres per 100km.
The average number of people in the car is 2.
First, convert megajoules to petajoules by dividing it by a billion.
Then, convert litre per 100km to litre per km by dividing the fuel consumption by 100.
Then, ensure the load factor is in billions by dividing 2 by a billion.
The input activity ratio should be 1.19 PJ per billion passenger-km.

## Slide 10: 1. Data for Transport Modelling in OSeMOSYS
InputActivityRatio[r,t,f,m,y]
Rate of use of a commodity by a technology, as a ratio of the rate of activity.
Linking Data to OSeMOSYS Parameters – Input Activity Ratio
10
Freight:
Example:
The energy intensity of diesel rail is 5.4 kgoe/ktkm.
The IAR is ((5.4 * 41.868) / 109) * 106 = 0.226 PJ / billion tkm.
To convert from kgoe to MJ
(1 kgoe = 41.868 MJ)
To convert to from MJ to PJ
To convert from kilo tkm to billion
Notes: The input activity ratio is the rate of use of a commodity by a technology, as a ratio of the rate of activity.
For freight transport, the input activity ratio is in petajoules of fuel per billion tonne-km. If data is scarce, the input activity ratio can also be calculated through an equation which multiplies the fuel content by fuel consumption and the inverse of the load factor.
Fuel content is in petajoules per litre, fuel consumption is litre per km, and load factor is in billion tonnes.
As an example, suppose the energy intensity of rail is 5.4 kilograms of oil equivalent per kilo tonne-km. Since we already have the energy intensity, we do not need to find the fuel content, fuel consumption or load factor. We only need to convert the units so that they comply with the OSeMOSYS model.
Thus, we need to convert kilograms oil equivalent to megajoules with the conversion of 1 kilograms oil equivalent is 41.868 megajoules. Then, ensure this is in petajoules by dividing by a billion. Finally, to convert kilo tonne-km to billion tonne-km, we need to multiply by a million. The answer should be 0.225 petajoules per billion tonne-km.

## Slide 11: 1. Data for Transport Modelling in OSeMOSYS
11
OutputActivityRatio[r,t,f,m,y]
Rate of commodity output from a technology, as a ratio of the rate of activity.
Linking Data to OSeMOSYS Parameters – Output Activity Ratio
In most cases, the Output Activity Ratio is set to 1 because the output is directly equal to the activity level
Petrol car
Diesel rail
Car transport demand
Rail (freight) transport demand
Petrol
Diesel
Example:
The OAR of a petrol car is 1.
The OAR of a diesel rail for freight is 1.
Notes: The output activity ratio is the Rate of commodity output from a technology, as a ratio of the rate of activity.
In most cases, the Output Activity Ratio is set to 1 because the output is directly equal to the activity level. This is visualized by a reference energy system on the right, where we can see that there is only one output (as indicated by the arrow) from the petrol car and diesel rail technologies that is meeting the demands. Thus, following this example, the output activity ratio of a petrol car is 1, and the output activity ratio of a diesel rail for freight is 1.

## Slide 12: 1. Data for Transport Modelling in OSeMOSYS
12
OutputActivityRatio[r,t,f,m,y]
Rate of commodity output from a technology, as a ratio of the rate of activity.
Linking Data to OSeMOSYS Parameters – Output Activity Ratio
However, this is not the case with refineries.
Oil refinery
Petrol
Crude oil extraction
Example:
A refinery’s yield for each fuel type is as follows:
Petrol: 30% of input crude oil  OAR is 0.3
Diesel: 25% of input crude oil  OAR is 0.25
Jet fuel: 20% of input crude oil  OAR is 0.20
Fuel oil: 15% of input crude oil  OAR is 0.15
LPG: 10% of input crude oil  OAR is 0.10
Crude oil imports
Diesel
Jet fuel
Fuel oil
LPG
Notes: However, this is not the case with refineries. It is unusual that the output activity ratio of refineries is 1. As illustrated in the reference energy system on the right, we can see that the oil refinery conversion technology has 5 different outputs – petrol, diesel, jet fuel, fuel oil , and liquified petroleum gas. The output activity ratio for this oil refinery will depend on the refinery’s yield for each of these fuel types.
As an example, suppose the refinery’s yield for petrol, diesel, jet fuel, fuel oil, and liquified petroleum gas is 30%, 25%, 20%, 15%, and 10% of the input of crude oil, respectively. Note that the input of crude oil includes the crude oil extraction and crude oil imports, as shown on the right. We then utilise these percentage ratios to calculate the output activity ratio. They will be proportional to the percentages we were given. So, the output activity ratio for petrol, diesel, jet fuel, fuel oil, and liquified petroleum gas is 0.3, 0.25, 0.20, 0.15, and 0.10, respectively

## Slide 13: 1. Data for Transport Modelling in OSeMOSYS
13
ResidualCapacity[r,t,y]
Remained capacity available from before the modelling period.
Linking Data to OSeMOSYS Parameters – Residual Capacity & Operational Life
Passenger and Freight:
OperationalLife[r,t]
Useful lifetime of a technology, expressed in years.
Passenger and Freight:
Notes: The residual capacity is the remained capacity available from before the modelling period. It is measured in 1,000 vehicles in OSeMOSYS.
The operational life is the useful lifetime of a technology, expressed in years.

## Slide 14: 1. Data for Transport Modelling in OSeMOSYS
14
CapitalCost[r,t,y]
Capital investment cost of a technology, per unit of capacity.
Linking Data to OSeMOSYS Parameters – Capital Cost
Passenger and Freight:
Example:
The cost of a car is 20,000 USD.
Thus, the Capital Cost is (20000 / 1000000) * 1000 = 20 M USD / 1000 vehicles.
The cost of an e-motorbike is 18 M VND. The currency exchange is 1 USD = 25,000 VND.
Thus, the Capital Cost is (18 / 0.025) * 1000 = 0.72 M USD / 1000 vehicles.
To convert to millions
To ensure it is for 1000 vehicles
To convert from VND to USD
To ensure it is for 1000 vehicles
Notes: The capital cost is the capital investment cost of a technology, per unit of capacity.
For passenger and freight transport, the capital cost is in million USD per 1,000 vehicles.
As an example, suppose the cost of a car is 20,000 USD. First, convert the cost to millions by dividing 20,000 by a million. Next, multiply this number by a thousand to ensure the cost is for 1,000 vehicles. This will give us a capital cost of 20 million USD per 1,000 vehicles.
Looking at another example, suppose the cost of an electric motorbike is 18 million Vietnamese Dong. First, convert the currency to USD with the exchange rate of 1 USD = 25,000 Vietnamese Dong. Then, multiply the number by 1,000 to ensure the cost is for 1,000 vehicles. This will give us a capital cost of 0.72 million USD per 1,000 vehicles.

## Slide 15: 1. Data for Transport Modelling in OSeMOSYS
15
FixedCost[r,t,y]
Fixed O&M cost of a technology, per unit of capacity.
Linking Data to OSeMOSYS Parameters – Fixed Cost
Example:
The maintenance cost for a CNG bus is 20,000 USD/year.
Its Fixed Cost would be (20000/1000000) * 1000 = 20 M USD / 1000 vehicles / year.
Passenger and Freight:
The maintenance cost for the metro is 50,000 USD/month.
Its Fixed Cost would be ((50000/1000000) * 12) * 1000 = 600 M USD / 1000 vehicles / year.
To convert to millions
To ensure it is for 1000 vehicles
To convert to millions
To ensure it is for 1000 vehicles
To convert from month to year
Notes: The fixed cost is the fixed operation and maintenance cost of a technology, per unit of capacity.
For passenger and freight transport, this is in million USD per 1,000 vehicles per year.
As an example, suppose the maintenance cost for a compressed natural gas bus is 20,000 USD per year. We first need to convert 20,000 to millions by dividing it by a million. Then, multiply by 1,000 to ensure it is for 1,000 vehicles. The fixed cost should be 20 million USD per 1,000 vehicles per year.
Looking at another example, suppose the maintenance cost for the metro is 50,000 USD per month. We need to to convert 50,000 to millions by dividing it by a million. As our number is by month, we need to multiply it by 12 to get it by year. Then, multiply by 1,000 to ensure it is for 1,000 vehicles. The fixed cost should be 600 million USD per 1,000 vehicles per year.

## Slide 16: 1. Data for Transport Modelling in OSeMOSYS
16
VariableCost[r,t,m,y]
Cost of a technology for a given mode of operation (Variable O&M cost), per unit of activity.
Linking Data to OSeMOSYS Parameters – Variable Cost
Passenger and Freight:
Example:
The cost of diesel was 20 USD/GJ in 2020.
Its Variable Cost would be (20 / 1000000) / 1000000 = 20 M USD / PJ.
To convert to millions
To convert from GJ to PJ
Notes: Variable cost is the cost of a technology for a given mode of operation per unit of activity.
For passenger and freight transport, the variable cost is in million USD per petajoule of fuel.
As an example, suppose the cost of diesel was 20 USD per gigajoule in 2020.
We first need to convert 20 USD to millions by dividing it by a million. Then, divide the number by another million to convert from gigajoule to petajoule. As the two millions cancel out, we will get a variable cost of 20 million USD per petajoule.

## Slide 17: 1. Data for Transport Modelling in OSeMOSYS
17
EmissionActivityRatio[r,t,e,m,y]
Emission factor of a technology per unit of activity, per mode of operation.
Linking Data to OSeMOSYS Parameters – Emission Activity Ratio
Passenger:
Freight:
Example:
Railway emissions are 54 g CO2 / pkm.
Its Emission Activity Ratio would be (54 / 1012 CO2) * (109) = 0.054 Mt CO2 / Bn pkm.
To convert from grams to millions tonnes
To ensure it is in billion pkm
Notes: The emission activity ratio is the emission factor of a technology per unit of activity, per mode of operation.
For passenger transport, the emission activity ratio is in million tonnes carbon dioxide per billion passenger-km.
For freight transport, the emission activity ratio is in million tonnes carbon dioxide per billion tonne-km.
As an example, suppose railway emissions are 54 grams of carbon dioxide per passenger-km. we first need to convert 54 grams to million tonnes by dividing 54 with 1,000,000,000,000. Then, multiply the value by a billion to ensure it is in billion passenger-km. Its emission activity ratio would therefore by 0.054 million tonnes carbon dioxide per billion passenger-km.

## Slide 18: 1. Data for Transport Modelling in OSeMOSYS
18
Geographic granularity
Is the model for domestic transport only, or does it include international?
Is the model split into urban, intercity, and rural?
Is the model representative of the whole country, or only a region?
Temporal scope
What is the modelling period? Short-term or long-term?
Will the model be based on annual or seasonal data?
Granularity and Temporal Considerations
Notes: When modelling transport in OSeMOSYS, considerations need to be made on the geographic granularity and temporal scope.
Geographic granularity defines the spatial resolution of the transport model, impacting the level of detail and applicability of results. Key questions include:
Domestic vs. International Transport
  Does the model focus only on domestic transport (movements within a country)?
  Does it include international transport, such as cross-border freight or aviation/maritime trade?
Urban, Intercity, and Rural Transport Segmentation
  Is the model disaggregated into urban (city-level transport, including public transit and private vehicles), intercity (longer-distance travel between cities), and rural (low-density areas with different transport needs)?
  This segmentation is important for analyzing different demand patterns and technology needs.
National vs. Regional Representation
  Does the model represent the entire country, or is it focused on specific regions?
  Some transport models might only cover major urban centers or key industrial corridors rather than a nationwide assessment.
Temporal scope determines the time horizon and frequency of data used in the model, affecting long-term planning and policy relevance.
Modeling Period: Short-Term vs. Long-Term
  Short-term models (e.g., 5–10 years) focus on immediate policy interventions, operational improvements, and near-future projections.
  Long-term models (e.g., 20–50 years) are essential for energy system planning, infrastructure investment, and decarbonization pathways.
Annual vs. Seasonal Data
  Annual models use aggregated yearly data, suitable for long-term energy and emissions forecasting.
  Seasonal models incorporate seasonal variations, which can be critical for transport demand changes due to weather, tourism, or agricultural cycles.

## Slide 19: 2. Sourcing Transport Data for Modelling in OSeMOSYS
19
Common Sources of Transport Data
National statistics offices
International organizations
Industry reports and academic studies
Survey data and stakeholder consultations
Notes: Transport data can be collected from a wide range of sources. 1. National Statistics Offices These offices provide a wide range of official data at the national level, often including detailed records on transportation infrastructure, vehicle fleets, traffic volumes, and fuel consumption.
2. International Organizations International bodies such as the World Bank, IEA, UNECE, and IATTC collect and publish cross-country data and provide comparative datasets for transport and energy sectors, often with a focus on policy and development goals.
3. Industry Reports and Academic Studies Reports from private-sector consultants, market research firms, and think tanks can provide valuable insights into transport sector trends, emerging technologies, and investment opportunities. Peer-reviewed studies and academic articles provide methodological insights, case studies, and in-depth analyses of transport behaviour, emissions, and system modelling.
4. Survey Data and Stakeholder Consultations Surveys and consultations with stakeholders, such as transport companies, government agencies, and local communities, provide qualitative and quantitative data on transport demand and behaviour.

## Slide 20: 2. Sourcing Transport Data for Modelling in OSeMOSYS
20
Open Data Resources for Transport Modelling
https://asiantransportobservatory.org/
Asian Transport Outlook, ADB
https://www.sciencedirect.com/science/article/pii/S2352340924009466
Transport Starter Data Kit, CCG, SLOCAT
Notes: Example sources include the Asian Transport Outlook from the Asian Development Bank (ADB) and the Transport Starter Data Kit from the Climate Compatible Growth programme (CCG) and the Partnership on Sustainable, Low Carbon Transport (SLOCAT).

## Slide 21: 2. Sourcing Transport Data for Modelling in OSeMOSYS
21
Open Data Resources for Transport Modelling
https://worldroadstatistics.org/
World Road Statistics,
IRF
https://portal.transport-data.org/
Transport Data Commons,
TDCI
Notes: Example sources include the Transport Data Commons from the Transport Data Commons Initiative (TDCI) and the World Road Statistics from the International Road Federation (IRF).

## Slide 22: 2. Sourcing Transport Data for Modelling in OSeMOSYS
22
Open Data Resources for Transport Modelling
DataBank,
WBG
https://data.worldbank.org/
https://uic-stats.uic.org/
Railisa,
UIC
Notes: Example sources include the DataBank from the World Bank Group (WBG) and Railisa from the International Union of Railways (UIC).

## Slide 23: 2. Sourcing Transport Data for Modelling in OSeMOSYS
23
Open Data Resources for Transport Modelling
Demand Technologies Data,
IEA-ETSAP
https://iea-etsap.org/index.php/energy-technology-data/energy-demand-technologies-data
https://data.europa.eu/en
European Data Portal,
EU
Notes: Example sources include the Demand Technologies Data from International Energy Agency Energy Technology Systems Analysis program (IEA-ETSAP) and European Data Portal from the European Union.

## Slide 24: 3. Addressing Data Gaps and Uncertainty
24
Data gaps refer to missing, incomplete, or insufficient information on datasets that prevent accurate analysis, decision-making, or modelling.
Data gaps can appear due to various reasons:
Limited data collection
Outdated models
Inaccessible sources
Lack of data standardization
Data gaps are common when modelling the
transport sector in OSeMOSYS – so don’t worry!
Identifying Data Gaps
(Source: AmCharts)
data gap
data gap
Notes: Data gaps refer to missing, incomplete, or insufficient information in datasets that prevent accurate analysis, decision-making, or modeling. Data gaps can affect the quality of results, leading to uncertainties in policy recommendations, energy planning, and infrastructure investments. Filling these gaps is crucial for enhancing the robustness of transport sector models and ensuring that outcomes are reflective of real-world conditions
Data gaps can appear due to various reasons:
Limited data collection: In many countries, especially those in the Global South, the availability of transport data may be limited due to gaps in national data collection systems or lack of consistent monitoring.
Outdated models: Models that are used to simulate transport systems may not always reflect the most current data or technologies, leading to outdated assumptions and projections.
Inaccessible sources: Some relevant data sources may be difficult to access due to legal, financial, or technological barriers, such as proprietary data or lack of public access to certain datasets.
Lack of data standardization: Data collected from different sources may not be standardized, making it difficult to combine or compare datasets across regions or time periods.
Data gaps are common when modeling the transport sector in OSeMOSYS, but don’t worry!

## Slide 25: 3. Addressing Data Gaps and Uncertainty
Calculation | Extrapolation or Interpolation | Proxy data | Expert judgement
Involves using available data and known formulas or relationships to compute a value Based on actual measurable factors that influence the outcome For examples, see slides 6, 7, 9 and 10 in this slide deck | Use mathematical methods to estimate missing values based on existing data points Extrapolation extends trends from known data to estimate missing values Interpolation estimates data points within a known range | Find related variables (proxies) to estimate missing data Assumes that the proxy behaves similarly to the missing data For example, using GDP per capita to estimate transport activity | Make informed assumptions based on expert judgement or literature review Clearly document your reasoning and how the assumptions may influence the results to build credibility and transparency
25
Desk-Based Methods to Address Data Gaps
Notes: There are four key main desk-based methods to address data gaps:
Calculation: Involves using available data and known formulas or relationships to compute a value based on actual, measurable factors that influence the outcome. Calculation is often the most straightforward method when you have complete data on the relevant variables.This method uses well-established relationships between variables. For example, fuel consumption can be calculated based on vehicle type, distance traveled, and fuel efficiency.
Extrapolation or interpolation: Extrapolation extends trends from known data points to estimate missing values beyond the observed range. This method is often used to predict future values or estimate missing data points outside the available range.It relies on the assumption that the trends observed in the data will continue into the future or extend to unknown data points. Interpolation estimates data points within a known range by using the existing data points on either side. This method is used when the data point falls within the range of observed values, and you want to estimate its value.It assumes that the data points follow a continuous pattern and that the trend will remain consistent.
Proxy data: Use related variables (proxies) to estimate missing data, assuming the proxy behaves similarly to the missing data. Proxy data can be used when direct data is unavailable or difficult to collect. The chosen proxy variable should have a strong correlation with the missing data.
Expert judgement: Make informed assumptions based on expert judgement or literature review. Clearly document your reasoning and how the assumptions may influence the results to build credibility and transparency. Expert judgment can be especially helpful when no data is available, or the available data is not sufficiently detailed.It involves making assumptions based on expertise, previous studies, or empirical evidence from similar regions or sectors.It’s critical to document the rationale behind any assumptions to ensure transparency and reproducibility.

## Slide 26: 3. Addressing Data Gaps and Uncertainty
26
When certain data points are missing, models will have to rely on assumptions and estimations, which can increase uncertainty.
Uncertainty is the lack of confidence in a piece of information, model, or prediction. It reflects the fact that data, models, or forecasts are rarely perfect and can be influenced by various factors.
Uncertainty in Transport Data
(Source: Monash University)
Notes: When certain data points are missing, models often rely on assumptions and estimations to fill the gaps. These assumptions can be based on expert judgement, previous studies, or mathematical methods like extrapolation or interpolation. While these methods are necessary for constructing a functioning model in the absence of complete data, they inherently introduce uncertainty. This is because the estimated values are not based on actual observed data but rather on approximations that may not perfectly reflect real-world conditions. The more data points are missing, or the more critical the missing data is to the model’s outcomes, the greater the uncertainty. In transport modeling, for example, missing information on vehicle stock, fuel consumption, or traffic patterns can significantly affect the results and lead to increased variability in the predictions.
Uncertainty itself refers to the lack of confidence in a piece of information, model, or prediction. It acknowledges that data, models, and forecasts are rarely perfect and that the systems being modeled—especially complex ones like transportation or energy—are influenced by numerous dynamic factors. No model can fully capture the complexity of real-world systems, and even with the best data collection and analytical techniques, imperfections remain. These imperfections can stem from various sources. Data uncertainty arises when datasets are incomplete, inaccurate, or unavailable, while model uncertainty reflects the simplifications or assumptions inherent in the model structure itself. Furthermore, forecast uncertainty emerges when models are used to predict future outcomes, as future developments—whether technological, economic, or political—are difficult to foresee with complete certainty.

## Slide 27: 3. Addressing Data Gaps and Uncertainty
27
Nonetheless, uncertainty can be managed!
Managing Uncertainty in Transport Data
Managing uncertainty
Scenario Analysis
Sensitivity Analysis
Testing model outcomes against data variability
Creating high/low estimates for uncertain parameters
Notes: Uncertainty can be managed through sensitivity analysis and scenario analysis. Sensitivity analysis is a technique used to determine how changes in the input variables of a model affect the model’s outputs. It helps identify which inputs have the most significant influence on the model’s results, allowing you to assess where uncertainties might be most impactful. Scenario analysis is a technique that explores different possible futures by altering assumptions about key variables or external factors. It is used to examine the implications of various scenarios—often incorporating a range of assumptions about factors such as technological developments, policy changes, or market trends.

## Slide 28: 3. Addressing Data Gaps and Uncertainty
28
Sensitivity analysis involves systematically changing input parameters (assumptions, coefficients, or data) within a specified range to see how these changes affect the model’s output.
The goal is to assess the degree of change in the outcome relative to the changes in the inputs.
By performing sensitivity analysis, you can:
Identify key drivers of uncertainty
Understand the robustness of your conclusions
Quantify how much the model’s outputs might vary given different assumptions or data variations
Make more informed decisions based on how sensitive the results are to specific inputs
Managing Uncertainty in Transport Data – Sensitivity Analysis
(Source: aprao)
Notes: Sensitivity analysis involves systematically changing input parameters (assumptions, coefficients, or data) within a specified range to see how these changes affect the model’s output. The goal of sensitivity analysis is to understand the robustness of a model’s results. By varying one or more input variables within a defined range, we can examine how much the model's outcome changes in response to these variations. It is particularly useful when dealing with uncertain or incomplete data, as it helps identify which assumptions or data points most affect the conclusions drawn from the model.
By performing sensitivity analysis, you can:
Identify key drivers of uncertainty
Understand the robustness of your conclusions
Quantify how much the model’s outputs might vary given different assumptions or data variations
Make more informed decisions based on how sensitive the results are to specific inputs

## Slide 29: 3. Addressing Data Gaps and Uncertainty
29
Scenario analysis is based on different assumptions about the future. Each scenario represents a plausible set of conditions (technological advancements, policy changes, or economic shifts) that could impact the model’s outcome.
The goal is to assess the range of possible results, helping to inform decision-making.
In scenario analysis:
Several distinct futures are defined
Each scenario includes multiple variables that evolve according to specific assumptions
Instead of focussing on a single forecast, you get a range of possible outcomes that can help you prepare for different situations
Managing Uncertainty in Transport Data – Scenario Analysis
(Source: Godínez-Zamore et al., 2020)
Notes: Scenario analysis is based on different assumptions about the future. Each scenario represents a plausible set of conditions (technological advancements, policy changes, or economic shifts) that could impact the model’s outcome.
The goal is to assess the range of possible results, helping to inform decision-making.
In scenario analysis:
Several distinct futures are defined
Each scenario includes multiple variables that evolve according to specific assumptions
Instead of focussing on a single forecast, you get a range of possible outcomes that can help you prepare for different situations

## Slide 30: 4. Approaches to Transport Data Collection and Validation
30
There are two common approaches to collect primary transport data:
Collecting Primary Data
1 Surveys and field studies:
Passenger surveys
Traffic counts
Benefits: provides detailed insights into individual behaviour and preferences, cost-effective and easy
Challenges: Response bias, recall bias, low response rates, time and resource-intensive, prone to human error
2 Stakeholder engagement:
Data sharing with transport agencies
One-on-one interviews or small group discussions
Benefits: broader perspective and enhanced data validation
Challenges: time and resource-intensive, potential bias, and data privacy
Notes: There are two common approaches to collect primary transport data:
Surveys and field studies, which can include passenger surveys and traffic counts. The benefits are that it provides detailed insights into individual behaviour and preferences, and is cost-effective and easy. However, there are challenges with response bias, recall bias, low response rates, time and resource-intensive, and prone to human error.
Stakeholder engagement, which can include data sharing with transport agencies and one-on-one interviews or small group discussions. The benefits are that it introduces a broader perspective on transport data and allows enhanced data validation. However, there are challenges with time and resource-intensive, potential bias, and data privacy

## Slide 31: 4. Approaches to Transport Data Collection and Validation
31
Validation Techniques
There are two common approaches to validate transport data:
1 Cross validation:
Compare with other data sources or methods to verify accuracy
2 Range/consistency check: Ensure the data falls within a valid range, benchmark against historical values
Notes: Two validate data, there are two common approaches.
Cross validation, which involves Comparing data with other data sources or methods to verify accuracy.
Range or consistency check, which involves ensuring the data falls within a valid range, and/or benchmarking the data against historical values.
These are important approaches to do when modelling the transport sector in OSeMOSYS with limited data and assumptions.

## Slide 32: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Naomi Tan
Imperial College London/Loughborough University