## Slide 1: Transport decarbonization and data-to-deal LECTURE 7: LEVERS AND VISUALISATION

## Slide 2: Lecture 7: Learning outcomes
By the end of this lecture, you will be able to:
Explain how multiple futures are considered in energy modelling using scenarios and lever
State relevant levers in transport modelling
Discuss the benefits and limitations of tools like the Pathways Calculator
Notes: By the end of this lecture, you will be able to:
Explain how multiple futures are considered in energy modelling using scenarios and lever
State relevant levers in transport modelling
Discuss the benefits and limitations of tools like the Pathways Calculator

## Slide 3: Considering multiple futures is integral to energy and transport modelling
A possible future is usually referred to as a ‘scenario’
  A scenario is a set of assumptions that reflect a particular narrative about the future.
Scenario assumptions usually concern policy decisions and uncertainties, e.g:
  Emissions targets
  Demand projections
  Technology costs
Scenario assumptions are reflected in input parameters.
The results can be compared in terms of costs, energy flow, infrastructure requirements, and emissions.
Notes: Modelling supports decision-making by providing information about different possible futures, allowing them to be compared
This comparison of different possible futures is an important part of what makes modelling useful.
A possible future is usually referred to as a ‘scenario’, which is a set of assumptions that reflect a particular narrative about the future.
Assumptions usually concern decisions policymakers could make or uncertainties about future. For optimisation models such as OSeMOSYS, assumptions could relate to Emissions targets, Demand projections, and technology costs.
Scenario assumptions are reflected in input parameters. The results can be compared in terms of costs, energy flow, infrastructure requirements, and emissions.

## Slide 4: Examples of the use of scenarios
The International Transport Forum’s Transport Outlook 2023
1. Current Ambition Scenario
2. High Ambition Scenario
The International Energy Agency’s Global Energy and Climate Model scenarios
1. Stated Policies Scenario
2. Announced Pledges Scenario
3. Net Zero Scenario
Notes: Some examples of the use of scenarios in modelling include, for instance, the International Transport Forum’s Transport Outlook 2023. The analysis explores two contrasting transport futures for the next 30 years using the ITF’s in-house transport models. The Current Ambition scenario reflects a continuation of existing decarbonisation policies, assessing their impact on transport demand, CO₂ emissions, and other factors. The High Ambition scenario examines the effects of more aggressive decarbonization policies.
The International Energy Agency’s Global Energy and Climate Model scenarios explores three scenarios for the future. The Stated Policies Scenario reflects current policies, highlighting the implementation gap in decarbonization. The Announced Pledges Scenario assumes full policy commitments, exposing the ambition gap to 1.5°C. The Net Zero Emissions by 2050 Scenario (NZE) outlines the necessary actions and timelines to achieve global net zero CO₂ emissions.
In these examples, each scenario reflects a different set of future policies. As is the case here, each modelling project typically includes a one reference scenario that reflects a future where no additional policies are implemented.

## Slide 5: Traditionally, a small number of scenarios are presented
It is traditional and convenient to present a small number of scenarios (e.g., 2-6) which may have been developed with input from stakeholders and experts
While useful, this format has some limitations:
  Alternative futures are missed
  Lengthy reports may be seen as less accessible
  Scenarios may be perceived as more final rather than subject to change
Notes: When disseminating modelling results and analysis, it is traditional and convenient to present a small number of scenarios (e.g., 2-6), as seen in the examples in the previous slides. There is a limit to how many charts and results can be included in a report. Furthermore, scenarios are often developed with input from stakeholders and experts, which help to ensure assumptions reflect stakeholder and expert views. With the accompanying written analysis, this format allows analysts to communicate key insights from the modelling.
While useful, this format has some limitations. By presenting a small number of futures, a large number of alternative futures representing different stakeholder views can be missed. Only stakeholders who have been in contact with the modelling team can provide input. Furthermore, static results are limited in their ability for readers to understand trade-offs in the system. Finally, scenarios may be perceived as more final, rather than subject to negotiation and continuous adjustment.

## Slide 6: More recently, interactive tools have allowed users to explore a wide range of scenarios
Examples:
2050 Calculator
The Global Electrical Platform
An interactive tool, has also been developed for OSeMOSYS: PathCalc.
Users adjust levers to create scenarios, and results are instantly updated
Levers represent intervention points or uncertainties
Each lever has four levels
The interface of the Laos PathCalc
Notes: More recently, interactive tools have allowed users to explore a wide range of scenarios. These tools can complement static modelling reports by addressing their limitations.
Examples of open-source, transparent visualisation tools include the 2050 Calculator and The Global Electrical Platform. These tools allow users to explore energy pathways, test policy impacts, and visualize trade-offs in a transparent and interactive way, helping stakeholders make informed decisions based on accessible, data-driven insights. Dozens of countries’ energy and electricity systems can be explored using these tools.
An interactive tool, Pathways Calculator, has also been developed for OSeMOSYS (PathCalc, for short). It is based on the 2050 Calculator concept.
To use the webtool, users adjust levers to change model input assumptions, and results are updated and visualised in real time.
Levers can represent intervention points or uncertainties which affect the system modelled.
Each lever has four levels to choose from, which collectively cover the range of possible values for the lever.
A scenario is defined by its combination of lever levels.

## Slide 7: Levers for the transport sector (1)
Transport levers in OSeMOSYS can include:
  Avoid, shift, improve levers
  Intervention points in other sectors which affect the transport sector indirectly
  Uncertainties
Notes: Levers which can be represented in OSeMOSYS and which affect the transport sector include:
  Intervention points that fall under the avoid, shift, improve framework for transport
  Intervention points in other sectors which affect the transport sector indirectly
  Uncertainties
These are unpacked in the next slide

## Slide 8: Levers for the transport sector (2)
Avoid | Total freight demand in tonne-km Total passenger demand in passenger-km
Shift | The modal profiles of passenger and freight transports Vehicle utilisation rates in km per vehicle per year Vehicle occupancies in tonne/vehicle or persons/vehicle
Improve | Vehicle fuel economy Vehicle technology mix
Notes: Avoid levers affect total freight and passenger demand. These demands are in terms of passenger-km and tonne-km, respectively. Passenger demand growth reduction can be the result of a variety of changes to people's transport environment. One potential driver is urban planning and land use policies which reduce the distance between home, work, and amenities, decreasing the need for long commutes.
Shift levers affect assumptions about:
The modal profiles of passenger and freight transport
Vehicle utilisation rates in km per vehicle per year. For constant transport demand, higher vehicle occupancy leads to lower energy demand.
Vehicle occupancies in tonne/vehicle or persons/vehicle. For constant transport demand, higher vehicle utilisation rate reduces the fleet size required.
Improve levers affect assumptions about the vehicle fuel economy and vehicle technology mix. Vehicle technology mix is changed through a transport decarbonisation constraint, which forces the model to reduce point-of-use emissions within transport. The model then chooses a least-cost basis which clean transport technologies to use.

## Slide 9: Levers for the transport sector (3)
Power and other sectors | Decarbonisation of the power sector Fuel blending and biofuels
Uncertainties | Capital, fixed, and variable costs Cost of capital
Note:
For practical modelling reasons, levers are often grouped.
Levers can be both intervention points and uncertainties
Notes: Levers from power and other sectors include the decarbonisation of the power sector, which is implemented through a decarbonisation constraint, allowing the model to choose least cost clean technology mix. Another lever is fuel blending and biofuels, which affect the share of biofuels in vehicle fuels.
Note that for practical modelling reasons, levers are often grouped in the webtool. For example, the user may be able to adjust an ‘Avoid’ lever which adjusts both freight and passenger demand together, but freight and passenger demands cannot be adjusted separately.
Furthremore, levers have been described here as either intervention points or uncertainties, but often, the distinction is not so clear-cut. Levers have varying degrees of influenceability. For instance, while some policies may affect transport demand, demand is also highly uncertain and dependent on factors which are difficult to influence.

## Slide 10: Ambition levels’ meanings
Level 1 | No effort
Level 2 | Requires moderate effort
Level 3 | Requires significant effort but is still achievable
Level 4 | Maximal possible value due to physical, engineering, or behavioural constraints
When levers are influenceable parts of the system rather than uncertainties, each lever level corresponds to a degree of effort required to achieve it:
Notes: When levers are influenceable parts of the system rather than uncertainties, each lever level corresponds to a degree of effort required to achieve it.
Level 1 assumes no effort, while Level 4 represents the maximum technically feasible outcome. Levels 2 and 3 show increasing ambition, balancing feasibility with impact.
Effort is constrained by geographic, behavioural, and engineering factors, influencing what is realistically achievable. Engaging experts from government, industry, and academia ensures credible level definitions. The approach allows users to explore trade-offs while ensuring the tool spans a wide range of opinions.
When levers are uncertainties, Levels 1 and 4 correspond to the uncertain value’s most extreme plausible values, and Levels 2 and 3 are intermediate values.

## Slide 11: Lever implementation in OSeMOSYS
Notes: For each lever, the OSeMOSYS base scenario defines ambition level 1 (no effort). Ambition levels 2, 3, and 4 are defined using three parameters similarly to the 2050 Calculator’s methodology.
Lever start year: the year in which the lever value begins deviating from the baseline value. For most levers, the start year was set to 2025.
Lever duration: the number of years it takes for the lever target value to be reached. This determines the end year. For most levers, duration was 25 years.
Lever target value: the value the lever achieves in the end year. These are detailed in the country modelling sections of this report.
These lever parameters are used to determine the lever value in each year, as shown in the figure. Prior to the start year, the lever’s trajectory follows baseline. Between the start and end years, the trajectory linearly deviates from baseline towards the target value. From the end year, the trajectory plateaus.

## Slide 12: Example PathCalc Intro
Let’s look at an example PathCalc.
The example PathCalc has five levers, each of which control a group of sub-levers.
Passenger and freight transport demand
Modal shift, vehicle utilisation rate, vehicle occupancy
Transport decarbonisation at point of use
Fuel blending, power system decarbonisation
Technology developments (capital and fixed costs)
Notes: Now, Let’s use an example PathCalc to illustrate how it can be used to support decision-making for long term planning in the transport sector.
The example PathCalc has five levers, each of which control a group of sub-levers.
The ‘Avoid’ lever controls passenger and freight transport demand.
The ‘Shift’ lever controls Mmdal shift, vehicle utilisation rate, and vehicle occupancy.
The ‘Improve’ lever controls transport decarbonisation at point of use.
The ‘Transform’ lever controls fuel blending and power system decarbonisation.
Finally, the ‘Costs’ lever controls capital and fixed costs trajectories for technologies which are expected to decrease in cost.

## Slide 13: PathCalc Example Energy savings from Avoid and Shift
Reference scenario
-20%
-40%
Together, Level 3 Avoid and Shift reduce annual fuel consumption by 60% by 2050.
Notes: Now, let’s use the levers. Starting from the reference scenario, where all levers are set to level 1, we adjust the Avoid lever to Level 3. If Avoid policies to reduce passenger and freight transport demands achieve Level 3 results, this alone reduces transport sector fuel consumption by 20% by 2050.
Next, if we adjust the Shift lever to Level 3, assuming that Shift policies also achieve Level 3 results, this reduces energy consumption by a further 40%.
Together, Level 3 Avoid and Shift reduce annual fuel consumption by 60% by 2050.

## Slide 14: PathCalc Example Takeaways
The high level of control of enables a deeper understanding of how different strategies contribute to overall outcomes.
It is important to note that the model shows only what may be achieved, not how to achieve it.
Notes: The example in the previous slide illustrates how the interactive web tool allows users to adjust assumptions for Avoid and Shift strategies separately and at different levels of ambition, rather than being limited to a few predefined scenarios. This fine level of control enables a deeper understanding of how different strategies contribute to overall outcomes. It also allows any user create a customised pathway and communicate their findings without needing to rely on the modelling team to run specific scenarios.
It is important to note that the model shows only what may be achieved, not how to achieve it. Planners would need to design policies to produce the behavioural and technological changes associated with Level 3 Avoid and Shift. There may be practical challenges and opportunities in doing so, which PathCalc does not provide insights on.

## Slide 15: PathCalc Example Cost of decarbonisation (1)
Without Avoid and Shift policies, the marginal cost of decarbonising the transport and power sectors is 100 million USD
+100 MUSD
Notes: Next, let’s investigate the cost of decarbonisation. Without Avoid and Shift policies, the marginal cost of decarbonising the transport and power sectors is 100 million USD.

## Slide 16: PathCalc Example Cost of decarbonisation (2)
With Avoid and Shift policies, the marginal cost of decarbonising the transport and power sectors becomes 30 million USD
Decarbonising is cheaper when Avoid and Shift strategies are in place.
+30 MUSD
Notes: When Avoid and Shift policies are set to Level 3, the marginal cost of decarbonising the transport and power sectors becomes 30 million USD. This decarbonised scenario costs 40% less than the reference scenario (shown in previous slide).
This shows that decarbonising is cheaper when Avoid and Shift strategies are in place.

## Slide 17: PathCalc Example Cost of decarbonisation (3)
The aggregate cost of a fully decarbonised scenario varies by 80 million USD, or nearly 20% of total transport-power system costs, depending on the cost assumptions used.
The cost of decarbonisation strategy is highly uncertain.
- 80 MUSD
Notes: The cost of decarbonisation can also be explored in relation to cost uncertainties. Here, we see that the aggregate cost of a fully decarbonised scenario varies by 80 million USD, or nearly 20% of total transport-power system costs, depending on the cost assumptions used.

## Slide 18: PathCalc Example Takeaways
The interactivity of the tool allows the user to understand how assumptions interact to produce outcomes.
The user can also identify the range of outcomes produced by a range of uncertain assumptions.
Notes: The example in the previous slides shows how various assumptions interact to significantly affect the cost of decarbonisation. The interactivity of the tool allows the user to understand how assumptions interact to produce outcomes.
The user can also identify the range of outcomes produced by a range of uncertain assumptions. For example, say a planner believes that Shift and Avoid can be influenced to fall between Levels 2 and 3, and the user also wants to consider the full range of cost trajectories. This planner can compare these scenarios to find the range of outcomes which result from this range of uncertain assumptions, allowing them to plan for this range of outcomes.

## Slide 19: PathCalc Example Impact of transport pathways on other sectors and ministries
To facilitate interministerial coordination, PathCalc includes charts with metrics of interest to different stakeholders:
Fuel costs for imported and domestic fuels
Capital and fixed costs for different sectors
Power generation and capacity
Transport fuel and technology mixes
Emissions and pollution
And more, if included in the model
Examples of graphs
Notes: A well-known challenge in many countries is siloed workflows across ministries, which can lead to contradictory or incoherent policies and plans across government.
To facilitate interministerial coordination, PathCalc includes charts with metrics of interest to different stakeholders:
Fuel costs for imported and domestic fuels
Capital and fixed costs for different sectors
Power generation and capacity
Transport fuel and technology mixes
Emissions and pollution
And more, if included in the model

## Slide 20: Summary: Benefits of interactive tools like PathCalc
The interactive, accessible, and transparent nature of tools like PathCalc have the potential to improve planning by supporting collaboration and a shared vision for the future.
User-friendliness promotes broad participation.
Instant feedback increases understanding of system being modelled.
More scenarios allows a wide range of perspectives to be considered.
Stakeholders can explore the impacts of different assumptions together, promoting consensus-building.
The shared interface promotes a common understanding between and shared ownership of the decision between ministries.
Notes: To summarise the benefits of interactive tools like PathCalc, The interactive, accessible, and transparent nature of tools like PathCalc have the potential to improve planning by supporting collaboration and a shared vision for the future.
The user-friendliness allows anyone to explore pathways regardless of modelling skills, promoting broad participation.
Unlike static reports, these tools provide instant feedback, allowing users to explore policy options and understand the effects of various assumptions and the interdependencies and trade-offs in system being modelled.
The high level of adjustability allows a wider range of perspectives to be considered with data, promoting inclusivity.
Instead of needing to agree on assumptions prior to modelling, stakeholders can explore the impacts of different assumptions together, promoting consensus-building.
The shared interface promotes a common understanding between and shared ownership of the decision between ministries. It also helps to ensure decisions are based on a consistent evidence base rather than siloed workflows. This promotes policy coherence in line with UN SDG goals.

## Slide 21: Creating new PathCalc webtools
A PathCalc can be created from an OSeMOSYS model and assumptions for each lever.
The levers included and the charts visualised can be customised.
Notes: In country teams can create their own version of PathCalc using the workflow developed. All that is required is a functioning OSeMOSYS model and assumptions for the four levels of each lever.
The levers to be included as well as the charts to be visualised can be customised.

## Slide 22: Limitations of Pathways Calculators
A key limitation of tools like the 2050 Calculator is that they allow users to explore only one scenario at a time.
This makes it difficult to compare multiple futures systematically.
The robust decision making approach addresses these limitations (next lecture).
Nevertheless, PathCalc can still play an important role.
Notes: A key limitation of tools like the 2050 Calculator is that they allow users to explore only one scenario at a time.
This makes it difficult to compare multiple futures systematically. Users must mentally track trade-offs rather than seeing patterns emerge across a broad set of scenarios.
The use of the robust decision making approach, which is covered in the next lecture, addresses these limitations
Nevertheless, because approaches like robust decision making are more complex, simpler approaches like in PathCalc can still play an important role. This is especially true in broad or early-stage discussions, where stakeholders need an accessible way to explore key assumptions and trade-offs

## Slide 23: Lecture summary
Considering multiple futures is a core aspect of modelling.
Traditional modelling projects typically produce a small number of scenarios which are analysed in reports.
In contrast, accessible, open, and interactive visualisation tools like PathCalc allow users to explore a wide range of possible futures.
The potential benefits of these tools include promoting better understanding of the system and trade-offs in planning, as well as facilitating interministerial coordination.
More complex scenario analysis approaches can address the limitations of tools PathCalc, but PathCalc’s simplicity and accessibility means it can still play an important role in decision support.
Notes: In summary, this lecture covered how considering multiple futures is a core aspect of modelling.
Traditional modelling projects typically produce a small number of scenarios which are analysed in reports.
In contrast, accessible, open, and interactive visualisation tools like PathCalc allow users to explore a wide range of possible futures.
The potential benefits of these tools include promoting better understanding of the system and trade-offs in planning, as well as facilitating interministerial coordination.
More complex scenario analysis approaches can address the limitations of tools PathCalc, but PathCalc’s simplicity and accessibility means it can still play an important role in decision support.

## Slide 24: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Emma Richardson
University College London
Emma.richardson.24@ucl.ac.uk