## Slide 1
Energy system modelling using OSeMOSYS
LECTURE 4
ENERGY DEMANDS AND THEIR REPRESENTATION

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO1: Learn about the characteristics of energy demands
ILO2: Learn the different types of energy demands
ILO3: Understand how energy demands are considered in energy models
ILO4: Learn how to represent energy demands in OSeMOSYS
Notes: Welcome to Lecture 4 of this course. This lecture focuses on several important concepts including:

## Slide 3
3
4.1.1 Energy Sectors
4.1 Energy Demand Characteristics
Industrial
Residential
Commercial
Transport
Agriculture
Notes: We all need energy, and we need it in different forms depending on the specific application. The demands for energy come from all sectors of society such as:
The residential sector (rural and urban) – for cooking, heating, cooling, lighting, and appliances
Industry – for chemical processes, steam production, and heating
Commerce – for lighting, heating, and cooling buildings or keeping products at low temperatures
Transport – for cars, trucks and buses, aviation, shipping, and trains
Agriculture – for tractors and machinery or pumping water
Because energy is used for different services in different sectors, the characteristics of energy demands vary by sector.

## Slide 4
4
4.1.2 Variations in Daily Energy Demand
4.1 Energy Demand Characteristics
(Taliotis et al. 2018, image, licensed under CC BY 4.0)
Notes: In lecture 3, we learnt that energy demands can vary on daily, weekly, and monthly timescales, mainly reflecting the schedule of consumers’ activities. In addition, this diagram also shows that energy demands vary by sector. We can see that the magnitude of demand varies by sector, with agricultural demand being significantly lower than residential and commercial demand in this example. This means that the commercial and residential sectors are consuming more electricity, perhaps because their activities are more energy intensive or on a larger scale. In addition, we see that the daily profile of demand varies by sector. For example, here, in the displayed graph, there is a clear evening peak in residential demand, while agricultural and industrial demands are quite consistent throughout the day. This is likely because agricultural and industrial machinery operates constantly, while energy use in homes peaks in the evening when consumers use more electricity for cooking, lighting, and appliances.

## Slide 5
5
4.1.3 Importance of Sector-Specific Demands
4.1 Energy Demand Characteristics
(Olaniyan et al. (2018), image, licensed under CC BY 4.0)
Notes: The differences between sectors discussed in the previous slide mean it can sometimes be important to model demands separately by sector, so that our models can consider the specific characteristics of each demand.
Additionally, within each of these sectors, the energy demand varies over time and across different classes of consumers. For example, within the residential sector, demands may differ between rural and urban households, as shown on this diagram, or between grid-connected and off-grid areas. Energy planners must make sure that the energy demand is met at any point in time for all classes of consumers. Thus, the key characteristics of demands must be represented in energy models.

## Slide 6
6
4.1.4 Long-Term Variations in Energy Demands
4.1 Energy Demand Characteristics
Notes: One of the key challenges in energy planning is that these energy demands change over time, for example, owing to population growth or the creation of new industries. On this diagram, we can see historical variations in energy demands which are likely correlated to changes in society. For example, increases in energy demand likely reflect increased industrial activity. In energy planning, it is important that we think about how energy demands are likely to change in the future. This is often done using forecasts of energy demand, such as the future projections shown in this figure. These forecasts can be created using estimates of the key influencers of energy demand, such as population growth and economic activity. Future projections are often also based on how energy demands have changed historically.
To project demand you can either: - Use existing demand projections - Project base year and historical demands using drivers such as population growth rate and/or GDP growth rate - Calculate an average of how demands have changed historically and use this as a projection growth rate
This list is not exhaustive.

## Slide 7
7
4.1.5 Capacity Expansion Planning
4.1 Energy Demand Characteristics
(Taliotis et al. 2018, image, licensed under CC BY 4.0)
Notes: The key purpose of modelling in OSeMOSYS is to plan capacity expansion. In order to do this, we need to consider these long-term changes in energy demands and use a projection of future demand, such as that shown by the green line in this diagram. An existing demand projection created from existing data, or using another tool, is used as input data for OSeMOSYS. In addition to a demand projection, we need data on the existing system capacity. Using the capacities and lifetimes of existing power plants, we can create a forecast of system capacity if there were no new capacity additions; this is represented by the blue line on the diagram, which shows gradually decreasing system capacity as power plants are retired. We can now see that there is a need for new capacity expansion in the future, as demand increases and existing system capacity decreases. There are losses in energy systems, and we always need capacity to be slightly higher than demand to account for this. Thus, the red line in this diagram shows the total system capacity requirements as demand increases. The gap between the red and blue lines therefore shows the required capacity expansion over time. OSeMOSYS can be used as a tool to plan such capacity expansion considering technical, economic, and environmental constraints.

## Slide 8
8
8
Lecture 4.1References
Taliotis, Constantinos, Gardumi, Francesco, Shivakumar, Abhishek, Sridharan, Vignesh, Ramos, Eunice, Beltramo, Agnese, … Howells, Mark. (2018, November). Defining final energy demands in OSeMOSYS. Zenodo. http://doi.org/10.5281/zenodo.4559206
Olaniyan K, McLellan B, Ogata S, Tezuka T. Estimating Residential Electricity Consumption in Nigeria to Support Energy Transitions. Sustainability [Internet]. 2018 May 5;10(5):1440. Available from: http://www.mdpi.com/2071-1050/10/5/1440

## Slide 9
9
4.2.1 Demands in Reference Energy Systems
4.2 Demands in Modelling
Notes: Demands are represented on the right-hand side of this simple Reference Energy System (RES), highlighted in green on this example RES.
As we can see in the diagram, there are several steps to get to the final demand split by sector. In this example there is:
The electricity from power plants, which represents the aggregated stream of electricity coming from all the power plants in the model;
Electricity after transmission, which accounts for the losses of the transmission lines;
Electricity for use or total electricity demand, which represents the electricity that arrives to final consumers after distribution.
Total demand can then be split by sector, for example in this RES we have the following demands:
  Industrial Electricity Demand
  Residential Electricity Demand
  Commercial Electricity Demand

## Slide 10
10
4.2.2 Generic Naming Convention for Demands
4.2 Demands in Modelling
Notes: Before we go any further, let’s quickly remind ourselves of the naming convention introduced in Lecture 3 and think about how this is relevant to defining our energy demands. This diagram is the same as the previous diagram; however, the names of commodities and technologies have been replaced by the codes specified in the naming convention. We can see that:
The electricity from power plants is named E.L.C.0 0 1
Electricity after transmission is named E.L.C.0 0 2
Electricity after distribution, or total electricity demand, is named E.L.C.0 0 3
Sector-specific electricity demands have the following names:
  Industrial Electricity Demand = I.N.D.E.L.C
  Residential Electricity Demand = R.E.S.E.L.C
  Commercial Electricity Demand = C.O.M.E.L.C

## Slide 11
11
4.2 Demands in Modelling
4.2.3 Understanding the logic – Part 1
Notes: When defining a demand, it is important to identify:
The carrier or service which the demand arises for: e.g., electricity, passenger transportation, or cooking.
The sector the demand arises from: e.g., residential (urban and/or rural, off- or on-grid), industrial, or commercial.
The average variability of such demand within a year, which is typically expressed using average demand profiles, explained in more detail later in this lecture.
The current and expected future annual average demand.
It is hard to predict future demands, and there is naturally uncertainty in our predictions. This is one reason why we model different scenarios.

## Slide 12
12
4.2 Demands in Modelling
4.2.4 Understanding the logic – Part 2
Notes: Let’s think about what we would need to identify when defining an example demand. In this example, we will think about the electricity consumed in urban homes. So, what do we need to identify based on the previous slide?
The energy carrier which the demand arises for: in this case this is electricity.
The sector the demand arises from: in this case this is the residential sector, or the urban residential sector if we want to be more specific.
The average variability of the demand over the year: here we would look at daily and yearly electricity load profiles for a residential urban area, which will tell us how the demand varies daily and in different seasons. From what we have learnt, we might expect this residential demand to be higher in the evening, and the seasonal variation would depend on the country’s climate.
The current and expected annual demand: here we would look at an energy balance (covered in more detail later) to get data for the current and historical residential electricity demand. We could use these data, potentially combined with an estimate of population growth, to create a future projection for the demand too.

## Slide 13
13
Lecture 4.2 References
Taliotis, Constantinos, Gardumi, Francesco, Shivakumar, Abhishek, Sridharan, Vignesh, Ramos, Eunice, Beltramo, Agnese, … Howells, Mark. (2018, November). Defining final energy demands in OSeMOSYS. Zenodo. http://doi.org/10.5281/zenodo.4585689
IEA (2023), World Energy Outlook 2023, IEA, Paris https://www.iea.org/reports/world-energy-outlook-2023, Licence: CC BY 4.0 (report); CC BY NC SA 4.0 (Annex A)

## Slide 14
14
4.3.1 Definitions
4.3 Demands in OSeMOSYS
Notes: There are several new parameters to introduce that are used to define final demands in OSeMOSYS:
Accumulated Annual Demand: This defines the total accumulated demand of a commodity that is constant throughout the year, for each modelled year.
Specified Annual Demand: This defines the total specified demand for each modelled year, linked to a specific ‘time of use’ during the year.
Specified Demand Profile: This defines the share of energy demand required in each time slice. For any demand that varies throughout the year it is crucial to use specified annual demand rather than accumulated annual demand because with accumulated annual demand the model could just choose to meet the entire demand in one time slice if it is cost-effective which would not be representative of how the demand needs to be met at specific amounts and specific times throughout the year.
It is important to note that one commodity demand cannot be defined using both Accumulated Annual Demand and Specified Annual Demand. Additionally, if a commodity demand is defined using Specified Annual Demand, data must also be entered for the Specified Demand Profile for that commodity demand because this describes how the demand entered to the ‘Specified Annual Demand’ is distributed throughout the year. Similarly, since accumulated demand means the model can literally satisfy it when it makes the most economic sense, you should only be use it when the allocation of that demand has zero effect on the economics of the entire system. For example, say you had an accumulated crop demand which would mean you’d also have an accumulated demand for agriculture motive power. The model can choose to fire up an electric sawmill in the night to balance out the load curve, which would be very unrealistic.
Additionally, always make sure you are entering demands in the correct units for OSeMOSYS, for several sectors the units are Petajoules (PJ), meaning we may need to change the units when taking demand data from other sources. For example, if we have an electricity demand profile in GWh, we would need to convert this to PJ, using a conversion factor of 1 GWh = 0.0036 PJ. Similarly, for industry we typically work in Million tonnes but you might have data in tonnes so you would have to change this.

## Slide 15
15
4.3.2 Backstop Technologies
4.3 Demands in OSeMOSYS
Notes: A Backstop technology is a fictitious technology that we model as an alarm bell. It is typically characterized by very high costs so that the model only chooses to use it if no other technology is available.
Whenever model results show that a Backstop technology comes into the system to produce electricity, this means that either:
The model is too constrained (i.e., there are not enough primary resources and conversion technologies in the system to produce enough electricity to satisfy the demand).
Or the model is not set up correctly (i.e., some technology parameters are defined in the wrong way).
It is useful to create one Backstop technology for each demand, as shown on the diagram above, so that we can quickly recognize where the problem is if we see that a Backstop technology is running.

## Slide 16
16
4.3.3 Backstop Technology Parameters
4.3 Demands in OSeMOSYS
Output Activity Ratio (for final electricity demand) = 1
Capital Cost [$/kW] = 999999
Variable Cost [$/GJ] = 999999
Operational Life [years] = 1
Notes: A Backstop technology is characterized by the key parameters shown on this slide. These parameters will be explained in more detail in later lectures; however, we can understand the logic behind these values. The Output Activity Ratio tells us which commodity a technology produces, and it usually has a value of 1 by default. Because the Output Activity Ratio for this Backstop technology is for final electricity demand, we know that this is the commodity produced by the backstop. We can see that both the capital and variable costs for the Backstop technology are very high; this is because OSeMOSYS will seek to find the solution with the lowest cost, so by assigning very high costs to the Backstop technology, we can be sure that the model will only use the Backstop when there is a problem with our model setup. The operational life is set to 1 year, which again ensures that the Backstop is less cost-effective than any other technologies in the model, providing the model is set up correctly. We will learn how to add a backstop technology to a model in the hands-on exercises.

## Slide 17
17
4.3.4 Sourcing Data for Energy Demands
4.3 Demands in OSeMOSYS
Providers of energy balance data and/or demand projections:
International Energy Agency [link]
International Renewable Energy Agency [link]
United Nations Statistics [link]
Asia-Pacific Economic Cooperation [link]
Notes: Energy demand data for use in energy models can come from several sources. Particularly useful sources include energy balances and Sankey diagrams. Energy balances tell us the amount of each commodity that is used by a country or region in a given year, usually broken down by sector. Sankey diagrams are a useful way of understanding the transformations between different energy commodities going from primary commodities to final consumption. Several organizations produce energy balance data that are publicly available, such as the International Energy Agency.

## Slide 18
18
Lecture 4.3 References
Pappis, I., Howells, M., Sridharan, V., Usher, W., Shivakumar, A., Gardumi, F. and Ramos, E., Energy projections for African countries, Hidalgo Gonzalez, I., Medarac, H., Gonzalez Sanchez, M. and Kougias, I., editor(s), EUR 29904 EN, Publications Office of the European Union, Luxembourg, 2019, ISBN 978-92-76-12391-0, doi:10.2760/678700, JRC118432

## Slide 19
Exogenous Demand: Demands that are set by the modeller, that must be met and do not change because of the model. For example, cement production per year, railway transport demand per year, crop demand per year. Exogenous demands can have real historical demands in historic years and then projected demands in future years.
Endogenous Demand: Demands that are not manually set by the modeller but emerge based on interactions within the model. For example, the demand for electricity in the power sector isn’t entered directly; it arises from the electricity needs of sectors such as industry, transport, and buildings. Similarly, the demand for hydrogen and ammonia is typically not set by the modeller but is driven by the demand for fertilizers and the ratios of hydrogen and ammonia needed to produce fertilizers or the use of hydrogen in vehicles.
4.4.1 Types of Demands
4.4 Demand Examples
Notes: Demands are incredibly important in OSeMOSYS as they are the driver for optimisation. The model needs demands in order to have something to optimise for. E.g. If you have demand for buildings heating, the model’s objective is to choose the cheapest technologies to meet that demand while also obeying any constraints that have been applied. There are two different types of demands: exogenous and endogenous. Exogenous demand is demand that is input into the model while endogenous demand is a result of the model’s internal interactions (input and output activity ratios) and is not a demand set by the modeller.

## Slide 20
4.4.2 Accumulated Annual Demand vs Specified Annual Demand
4.4 Demand Examples
We use the parameters Specified Annual Demand and Specified Annual Demand Profile when we want to consider the temporal variability of the demand within the year, e.g., electricity demand.
However, there are some demands that do not have specific temporal variability within the year. In this case, we use the parameter Accumulated Annual Demand, which allows us to specify the amount of demand for every model year, without specifying how that demand is spread throughout the year, e.g., passenger transport demand or cooking energy service.
Specified Annual Demand + Specified Annual Demand Profile
Accumulated Annual Demand
Do we need to consider demand variability within years?
Yes
No
Notes: We use the parameters Specified Annual Demand and Specified Annual Demand Profile when we want to consider the temporal variability of the demand within the year, e.g., electricity, cooking, and heating demand, since we know this varies relatively predictably across seasons and between day and night. However, there are some demands that do not have specific temporal variability within the year. In this case, we use the parameter Accumulated Annual Demand, which allows us to specify the amount of demand for every model year without specifying how that demand is spread throughout the year.
The demands for energy and fuels come from all sectors such as:
Buildings – for cooking, heating, cooling and appliances – units of activity typically in PJ
Transport – for cars, trucks and buses, aviation, shipping, and trains – units of activity typically in billion vehicle kilometres
Industry – for heating, iron and steel production, cement production, aluminum production, petrochemicals production, other chemicals production, fertilizers production and other industries – units of activity for heat is in PJ and for production quantities in Million tonnes (Mtons)
Agriculture – for tractors and machinery, processing and heating – units of activity in PJ
You may have noticed that demand units do not necessarily have to be energy units, for example, industry outputs can be the amount of product in Million tonnes and transport demands are typically in distance units such as Billion vehicle kilometres.

## Slide 21
4.4.3 Example Specified Annual Demand
4.4 Demand Examples
Notes: The Specified Annual Demand parameter is used to indicate the amount of demand in each year of the model period. We usually source the data for this parameter from existing demand forecasts, which may be based on key determinants of demand such as expected population growth. If we source demand data from existing sources, we must remember to convert the data into the right units for use in OSeMOSYS.

## Slide 22
22
4.4.4 Example Specified Demand Profile for OSeMOSYS
4.4 Demand Examples
Winter
Spring
Summer
Autumn
Night
Night
Night
Night
Night
Night
Night
Night
Day
Day
Day
Day
Notes: The Specified Annual Demand Profile parameter is used to indicate the proportion of the demand occurring in each time slice This chart shows an example specified demand profile for electricity in OSeMOSYS. There are 96 bars, 1 for each of the 96 time slices used in this OSeMOSYS model. In this example, we have four seasons (Winter, Spring, Summer, and Autumn), each represented by 24 time slices in OSeMOSYS, with 12 time slices for daytime and 12 time slices for nighttime. The Specified Demand Profile parameter is used to represent the proportion of demand occurring in each time slice. The specified demand profile values in each time slice must all add up to exactly 1.
From the chart we can see that the electricity demand in this example is highest in Winter Days, because the Winter Day time slices have the highest Specified Demand Profile values, while demand is lowest in Spring Nights. It is important to recognize that this is a simplification: in reality demand will vary within seasons and with each hour of the day. Our simplification means that we model one representative day of each season, and we assume equal demand within days and nights of those seasons. Although this is a simplification, it allows us to consider the variation in demand across seasons and day parts without having an incredibly complex model structure. Specified demand profiles can be unique such as the demand profile for electricity generation or the heating demand profile of a country. However, in most cases for modelling if country-specific data is not available we tend to keep the demand profile flat (e.g. in industry and transport sectors). Keeping a profile flat simply means making the demand profile exactly equal to the year split. This ensures that all the demand is not used up in one time slice but is distributed throughout the year, making it more realistic.

## Slide 23
4.4 Demand Examples
1 Petajoule (PJ) = 1000 Terajoules (TJ)
1 Petajoule (PJ) = 1,000,000 Gigajoules (GJ)
3.6 Petajoules (PJ) = 1 Terawatt hour (TWh)
0.0036 Petajoules (PJ) = 1 Gigawatt hour (GWh)
1 Giga-Watt (GW) = 1000 Mega-Watts (MW)
4.4.5 Reminder of Conversions
Notes: For anything energy related we typically use PJ in the MUIO for activity and GW for capacity, therefore it is important that you understand how to convert things into PJ and GW for model input. Therefore, please make a note of these conversions.

## Slide 24
24
Lecture 4.4 References
Taliotis, Constantinos, Gardumi, Francesco, Shivakumar, Abhishek, Sridharan, Vignesh, Ramos, Eunice, Beltramo, Agnese, … Howells, Mark. (2018, November). Defining final energy demands in OSeMOSYS. Zenodo. http://doi.org/10.5281/zenodo.4585689

## Slide 25: Thank you
www.climatecompatiblegrowth.com
Consolidated by:
Fernando Plazas-Niño, Kane Alexander, Hannah Luscombe, Lucy Allington, Carla Cannone, Pooya Hoseinpoori, Alexander Kell, Adam Hawkes, Mark Howells