## Slide 1
Energy system modelling using OSeMOSYS
LECTURE 6
FOSSIL POWER PLANTS, TRANSMISSION & DISTRIBUTION

## Slide 2
2
Learning Outcomes
By the end of this lecture, you will be able to:
ILO1: Understand the concepts of fossil power plants and fossil fuel supply chains
ILO2: Learn how to represent fossil power plants in OSeMOSYS
ILO3: Understand key characteristics and impacts of fossil power plants and their interactions with the wider energy system
ILO4: Understand key characteristics of transmission and distribution technologies and how to represent them in OSeMOSYS

## Slide 3
3
6.1.1 Introducing Fossil Power Plants
6.1 Introduction to Fossil Power Plants
Notes: In this lecture we will cover fossil power plants, namely coal, oil, and gas power plants which are highlighted in the RES diagram above. These are all types of thermal power plants. Note that biomass power plants are also thermal power plants; however, they will be covered separately in a later lecture. We will also touch on thermal combined heat and power plants (CHPs) briefly. We will first look at a basic overview of coal, diesel, and gas power plants and CHPs, then look at their technical characteristics and representation in OSeMOSYS, before finally exploring their impacts, both environmental and societal. In the last part of this lecture, we will learn more about Power Transmission and Distribution technologies, which are also highlighted on the RES diagram above.

## Slide 4
4
6.1.2 Fossil Fuel Power Plants – How do they Work?
6.1 Why is energy planning important?
4
Fuel is burned to produce heat
High pressure steam drives a turbine
Turbine drives a generator to produce electricity
Notes: Thermal power plants are power plants where thermal energy, generated by burning a fuel, is converted to electrical energy. This includes fossil power plants, where the fuel burnt is a fossil fuel, such as coal, natural gas, or oil. Although the fuel used can vary, these power plants are based around similar processes: the fuel is burnt to produce heat which generates steam. This steam then drives a turbine, which drives a generator to produce electricity. It is important to note that different fuels release different amounts of energy when burned. This is measured by the fuel's calorific value, which is the amount of energy released when 1kg of the fuel is burnt.

## Slide 5
6.1.3 Fossil Fuel Combined Heat and Power Plants – How do they Work?
6.1 Why is energy planning important?
Notes: Another alternative way of generating electricity using fossil fuels is through combined heat and power plants. A Combined Heat and Power (CHP) plant—also known as cogeneration—is a system that simultaneously generates electricity and useful thermal energy from the same fuel source. Rather than wasting heat from electricity production, CHP systems capture and use it for heating, industrial processes, or district heating networks. They are more expensive and generate less electricity for a unit of fuel than power plants but they generate a notable amount of heat. So, in some cases they are a desired choice.

## Slide 6
6
6.1.4 Fossil Power Plants in the Wider Energy System
6.1 Why is energy planning important?
Fossil Fuel Extraction or Imports
Fuel Processing
Fossil Power Plants and CHPs
Fuel Transport & Distribution
Power Transmission & Distribution
Electricity Demand
Fossil Fuel demands for:
- Transport
- Cooking & Lighting
- Heating
Notes: As we can see on this diagram, fossil power plants are just one part of the wider energy system, and several interactions with other technologies are needed in order to meet final energy demands. Firstly, we must understand the processes required to source the fossil fuels burned in these power plants: these fuels must either be extracted domestically or imported from other countries. It is important to remember that the supply of these fuels is associated with costs, as discussed in lecture 5. Additionally, it is important to remember that these fuels cannot be infinitely supplied since fossil fuels are non-renewable energy sources, with only a finite amount of reserves globally. The supply of these fuels also has environmental and social aspects, as discussed later in this lecture. In some cases the fuels also have to be further processed before they can be supplied to power plants, for example crude oil has to be refined at an oil refinery. In addition, once these fuels have been burned to generate electricity in fossil power plants, that electricity has to be transported to end-users via transmission and distribution networks. It is also important to remember that fossil fuels have several roles in the energy system, not just electricity generation, which are discussed in more detail in the next slide.

## Slide 7
7
6.1.5 Roles of Fossil Fuels
6.1 Why is energy planning important?
As well as for electricity generation, fossil fuels are used heavily in transport, cooking, heating, and lighting
Notes: Whilst we have so far discussed fossil fuels in relation to electricity generation, they have several other key roles in energy systems. Firstly, transport systems are often almost entirely based on fossil fuels, with cars, buses, and motorcycles in most countries being fuelled by oil products. Secondly, fossil fuels can be important for cooking and lighting, with many stoves and lamps being fuelled by kerosene, an oil products. Thirdly, fossil fuels often have a role in heating systems, with many countries having residential heating systems that rely on natural gas, and some industrial processes requiring high temperatures that can be difficult to achieve without burning fossil fuels. In developing countries, all of these demands are likely to grow as transport infrastructure evolves, populations increase, and industrial productivity grows. Together these factors mean that, even if we were to generate electricity with renewable technologies, energy systems could create increasingly large demands for fossil fuels in the future unless we switch to cleaner technologies in the transport, cooking, lighting, and heating sectors. This is a key element of the energy transition, which will be introduced next.

## Slide 8
8
6.1.6 Energy Transition
6.1 Why is energy planning important?
Example of the Energy Transition concept from Europe:
(Bartz/Stockmar, image licensed with CC BY 4.0)
Notes: The energy transition refers to the transformation of the energy sector from being reliant on fossil fuels to using low-carbon and renewable energy sources. There are several drivers of this transition, with greenhouse gas emissions and environmental impacts at the core. Burning fossil fuels releases greenhouse gases, which drive global warming, and creates harmful air pollution. Thus, there is a need to transition away from fossil fuels in order to mitigate climate change and protect the environment. Additionally, as discussed previously, fossil fuels are finite resources and will not last forever, meaning that a system reliant on these fuels in the long-term cannot be resilient or sustainable. Therefore, the energy transition calls for greater uptake of renewable energy technologies, which avoid some of the negative impacts of fossil power plants discussed in more detail later in this lecture. However, as we saw on the previous slide, fossil fuels are also used for transport, cooking, lighting, and heating. So, we must consider how we can transform these sectors to use renewable resources. For this reason, energy system models are often developed to allow us to study fuel switching, such as using electric vehicles. We will also cover this later in the course.

## Slide 9
9
Lecture 6.1 References
Taliotis, C., Gardumi, F., Shivakumar, A., Sridharan, V., Ramos, E., Beltramo, A., Rogner, H., Howells, M., 2018. Electricity supply system in OSeMOSYS I (Thermal power plants and T&D), KTH-Desa and OpTIMUS.community. Available at: https://zenodo.org/record/1942510#.YC5VjehKhPY. [18/02/2021] DOI: 10.5281/zenodo.1942510

## Slide 10
10
6.2.1 Fossil Power Plants in Reference Energy Systems
6.2 Fossil Power Plants in OSeMOSYS
Coal power plant
Diesel power plant
Combined cycle gas turbine
Electricity
Open cycle gas turbine
Coal
Diesel
Natural gas
Natural gas
Electricity
Electricity
Electricity
PWRCOA
PWRDSL
PWRNGS001
ELC001
PWRNGS002
COA
DSL
NGS
NGS
ELC001
ELC001
ELC001
Notes: Now we will look at how fossil power plants are represented in OSeMOSYS. Firstly, let's think about how they are represented in Reference Energy Systems. Fossil Power Plants are technologies and so are represented by boxes, as shown on this diagram. These power plants have both an input fuel, which is the specific fossil fuel they burn, and an output commodity, which is electricity. For example, we can see that the coal power plant has an input fuel of coal and produces electricity as its output. This diagram also shows an example of one of the generic code names used for all of these technologies and fuels, which we will use when building our own model in hands-on exercises. It is important to note that this diagram shows two types of gas power plant: Combined Cycle Gas Turbines and Open Cycle Gas Turbines. In a Combined Cycle Turbine, waste heat generated by burning the gas can be recycled, increasing the efficiency of the power plant compared to Open Cycle Gas Turbines. In this particular code naming convention, these types of power plants are named PWRNGS001 and PWRNGS002 respectively, in the other common naming convention the two different natural gas plants would be distinguished based on their names Country Code_POW_PP_NG and Country Code_POW_PP_NGCC respectively.

## Slide 11
6.2.2 Fossil Power Plants in Reference Energy Systems
6.2 Fossil Power Plants in OSeMOSYS
Coal combined heat and electricity plant
Oil combined heat and electricity plant
Natural gas combined heat and electricity plant
Electricity
Coal
Diesel
Natural gas
PWRCHPCOA
PWRCHPOIL
PWRCHPNGS
ELC001
COA
DSL
NGS
Heat
Electricity
Heat
Electricity
Heat
HEA001
ELC001
HEA001
ELC001
HEA001
Notes: Now we will look at how fossil combined heat and electricity plants are represented in OSeMOSYS. Firstly, let's think about how they are represented in Reference Energy Systems. Fossil Combined Heat and Power Plants are technologies and so are represented by boxes, as shown on this diagram. These power plants have both an input fuel, which is the specific fossil fuel they burn, and an output commodities, which are electricity and heat. For example, we can see that the coal combined heat and power plant has an input fuel of coal and produces electricity and heat as its output. This diagram also shows one of the examples of generic code names used for all of these technologies and fuels. Using the other generic naming convention you would have for example Country Code_POW_CHP_COAL, Country Code_POW_CHP_OIL, Country Code_POW_CHP_NG.

## Slide 12
12
6.2.3 Defining Fossil Plants in OSeMOSYS
6.2 Fossil Power Plants in OSeMOSYS
Key parameters for defining fossil power plants:
Output Activity Ratio
Input Activity Ratio
Capital, Fixed, and Variable Costs
Availability Factor
Capacity Factor
Operational Life
Emission Activity Ratio
Notes: In OSeMOSYS, fossil power plants are mainly characterized by the parameters shown on this slide. These are:
Output Activity Ratio: this is used to define the output fuel of the power plant, usually electricity (or, in the naming convention, E.L.C. 0 0 1) and has a value of 1 by default.
Input Activity Ratio: this is used to define the input fuel of the power plant and, since the Output Activity Ratio is set to 1 by default, defines the number of units of input fuel needed to produce 1 unit of electricity.
Capital, Variable, and Fixed Costs: these parameters are used to represent the costs of power plants.
Availability Factor: this is the maximum time a technology can run in the whole year, as a fraction of the year ranging from 0 to 1.
Capacity Factor: this defines how much energy is actually generated in a year over how much would be generated if the power plant operated at full capacity all year.
Operational Life: this is how many years the plant is expected to operate for.
We will look at these parameters in more detail in the following slides.
Emission Activity Ratio: how much Mtons of carbon dioxide equivalent are emitted per PJ of energy produced by the power plants. Disclaimer: you can either attribute the emissions of fuels at the point of extraction and importation of the fuel or at the point of combustion in power plants. If you have attributed, it at the point of extraction and imports then there is no need to assign an emissions activity ratio to the power plants.

## Slide 13
13
6.2.4 Input & Output Activity Ratios
6.2 Fossil Power Plants in OSeMOSYS
Notes: Let's explore the Output Activity Ratio and Input Activity Ratio parameters a little more. The Output Activity Ratio is the parameter used to define the output fuel produced by the power plant and is given a value of 1 by default. So, for the example on this slide, the output activity ratio for our coal power plant would be 1 for electricity. The Input Activity Ratio parameter is then used to define the input fuel and how many energy units of input fuel are needed to produce 1 energy unit of output fuel. So, in this case we want to define how many energy units of coal, the input fuel, are needed to produce 1 energy unit of electricity, the output fuel. In our example, we can see that 3 energy units of coal are needed to produce 1 energy unit of electricity, so the Input Activity Ratio for the coal power plant would be 3 for coal. It is also important to note that power plants can have more than one input or output fuel, for example some models are set up to consider the water consumption of power plants, meaning water would also have to be defined as an input fuel using Input Activity Ratio.

## Slide 14
14
6.2.5 Fossil Power Plant Costs
6.2 Fossil Power Plants in OSeMOSYS
Capital Costs ($/kW):
One-time costs of building the power plant
Variable Costs ($/GJ):
Costs incurred when the power plant runs, e.g., fuel costs
Fixed Costs ($/kW/yr):
Fixed annual costs, e.g., workers' salaries, taxes, and insurance
Notes: Fossil power plant costs are represented in OSeMOSYS using three parameters. Firstly, the Capital Cost parameter is used to define the one-time costs associated with building and setting up the power plant. This includes things like planning and design, construction and buying machinery, and commissioning and certification. Capital costs are defined using the unit $/kW, referring to the cost in dollars per kW of power plant capacity. The fixed costs parameter is used to consider regular costs occurring in every year that the power plant operates, including the costs of workers' salaries, taxes, insurance, and any fuel costs which are fixed every year. This is defined in $/kW/yr, referring to the cost in dollars per kW of power plant capacity per year. Finally, the variable costs parameter represents costs that are only incurred when the power plant runs to produce electricity. This is often mainly the cost of the input non-fuels or consumables that are needed for the power plant to run, such as chemicals. Variable costs are defined using the unit $/GJ, referring to the cost per GJ of energy produced.

## Slide 15
15
6.2.6 Availability Factor, Capacity Factor, and Operational Life
6.2 Fossil Power Plants in OSeMOSYS
Availability Factor: maximum time a technology can operate over the year, as a fraction of the year ranging from 0 to 1. This can account for planned power plant outages.
Capacity Factor: capacity available in each time slice expressed as a fraction of the total installed capacity ranging from 0 to 1. This accounts for unplanned power plant outages.
Operational Life: the useful lifetime of the power plant in years
Notes: Other key parameters for defining fossil power plants in OSeMOSYS include the availability factor, capacity factor, and operational life. This slide includes definitions for these parameters in relation to power plants. The availability factor represents the maximum time that a power plant is able to operate over the year, as a fraction of the whole year, ranging from 0 to 1. This value is set to 1 by default, meaning the power plant would be able to operate over the whole year; however, it can be adjusted to less than 1 to account for planned outages. For example, if we knew that a coal power plant would be out of operation for 10% of the year due to planned maintenance, we would give the technology an availability factor of 0.9. The capacity factor represents the power plant capacity available in each modelled time slice, as a fraction of the total installed capacity, ranging from 0 to 1. This parameter is used to account for unplanned outages. If 100% of a power plant's capacity could run to produce power 100% of the time, the power plant would have a capacity factor of 1. However this is not the case in reality as power plants do not always run at full capacity or all the time. For example, a coal power plant may have a capacity factor of 80%. Finally, the operational life parameter is the useful lifetime of the power plant in years. For example, a typical fossil power plant might have an expected life time of 25 years.

## Slide 16
16
6.2.7 Emission activity ratio
6.2 Fossil Power Plants in OSeMOSYS
It defines the relationship between the activity of a technology and its emissions, by indicating how many emission units are released for every unit of activity
Notes: The Emission Activity Ratio is used to define an emission factor for a technology. It describes the relationship between the activity of a technology and its associated emissions by indicating how many units of emissions are released per unit of activity.
For example, the combustion of 1 GJ of natural gas releases approximately 50.2 tonnes of CO₂ into the atmosphere. If a natural gas–fired power plant operates at an efficiency of 50%, then 2 GJ of natural gas are required to generate 1 GJ of electricity. In this case, the Emission Activity Ratio is calculated as the ratio of emissions (2 × 50.2 = 100.4 tonnes of CO₂) to activity (1 GJ of electricity generated), resulting in a value of 100.4 tCO₂/GJ.
The Emission Activity Ratio is both technology- and emission-specific and may vary across years and modes of operation. It is particularly important to define this parameter for each technology, especially when emissions are not accounted for at the primary production or import technology level. Doing so allows users to obtain emissions by technology and sector, rather than only total emissions by fuel.
When technology-specific emission factors are not available, the Emission Activity Ratio can be estimated using the formula shown in the slide. This ratio is equivalent to dividing the fuel emission factor by the corresponding technology efficiency.

## Slide 17
17
17
Lecture 6.2 References
Taliotis, C., Gardumi, F., Shivakumar, A., Sridharan, V., Ramos, E., Beltramo, A., Rogner, H., Howells, M., 2018. Electricity supply system in OSeMOSYS I (Thermal power plants and T&D), KTH-Desa and OpTIMUS.community. Available at: https://zenodo.org/record/1942510#.YC5VjehKhPY. [18/02/2021] DOI: 10.5281/zenodo.1942510

## Slide 18
18
6.3.1 Coal Supply Chain
6.3 Impacts of Fossil Power Plants
(Luo et al. 2017, image, licensed under CC BY 4.0)
Notes: The coal supply chain is made up of different stages, including:
Mining and preparation (underground or surface).
Transportation. this accounts for a large part of the total cost of the delivered product. It usually occurs via railways, large vessels through oceans, pipelines as a mixture of coal and water, and trucks (for short distances).
Combustion-based power plants. Two main technologies are used in coal power plants: Super-critical pulverized coal (or S. C. P. C.) and the Integrated Gasification Combined Cycle (or I. G. C. C.). Additionally, Carbon Capture and Storage (or C. C. S.) can be applied.
End-use of electricity in all sectors of society.
In many countries, coal is a source of energy security and jobs, as it is:
•Relatively inexpensive,
•Simple to extract and transport,
•Capable of providing baseload power generation,
•Located in politically stable regions and abundant in many countries.
However, there are challenges associated with coal, discussed next.

## Slide 19
19
6.3.2 Damaging impact of Coal
6.3 Impacts of Fossil Power Plants
Climate | Land-use | Water
CO2 emissions | Degradation of vegetation | River water alkalinity
SO2 – related acidification of ecosystems | Loss of wildlife habitats | Fly ash stored in impoundment ponds
Mercury emissions (concentration at higher levels of the food chain) | Damage due to mine collapses | Degradation of aquatic habitats
Acid rain | Loss of topsoil leads to infertile wastelands | Cooling water requirements
Notes: This slide shows some of the negative impacts of the coal supply chain and coal-fired power plants.
The continuing trend of year-on-year growth in coal-fired power needs to be reversed to meet ambitious carbon dioxide emissions targets. Indeed, the entire coal supply chain has negative impacts on:
Climate, due to Carbon Dioxide, Sulphur Dioxide, and mercury emissions which cause acidification and contribute to global warming.
Land-use, as mining activities degrade the vegetation, harm wildlife, and reduce crop fertility.
Water, though increased alkalinity, which degrades aquatic habitats.
We should bear in mind that Coal has strong advantages and disadvantages. We need to understand what drives governments to use it and what the trade-offs are in order to find feasible alternatives. Policy incentives such as carbon pricing and regulation are imperative to control pollution and limit generation from inefficient coal-fired power plants. A systems perspective may allow us to see non-obvious risks and opportunities of shifting away from coal or maintaining it.

## Slide 20
20
6.3.3 Oil and Gas Supply Chains
6.3 Impacts of Fossil Power Plants
(Katopodis et al. (2019), image, licensed under CC BY 4.0)
Notes: This time let's look at the oil and gas supply chains.
Oil and gas prices have been subject to oscillations, caused by geopolitical factors and related supply–demand balances. This raises questions of
energy supply security and import dependency for individual countries, but also of the resilience of the global economy to oil prices and vice versa.
The oil supply chain includes the following stages:
Extraction, using conventional wells, deep-water production, and enhanced oil recovery methods.
Transportation (using oil tankers, pipelines, trucks, and railways) and storage.
Refining, which is the industrial process that transforms crude oil into useful products such as petroleum naphtha, gasoline, and diesel fuel.
Combustion-based power plants.
Utility-scale power generation from oil products like heavy fuel oil or diesel has recently declined and is now responsible for only minor shares of generation in many regions. Small diesel generators are still used as backup (for example, in hospitals, factories, or households), especially in developing countries with unreliable electricity supply.
The gas supply chain includes:
Extraction, using conventional wells, deep-water production, or hydraulic fracturing.
Transportation (with pipelines and ships) and storage (underground storage or on-board Liquefied Natural Gas fleets).
Combustion-based power plants: Open Cycle Gas Turbines (O. C. G. Ts) and Combined Cycle Gas Turbines (C. C. G. Ts), the latter of which has a Heat Recovery Steam Generator (H. R. S. G.) to make use of waste heat, increasing efficiency.

## Slide 21
21
6.3.4 Environmental Impacts of Oil and Gas Power Plants
6.3 Impacts of Fossil Power Plants
Concerns about waste-water disposal, pollution of underground water, and increased seismic activity due to hydraulic fracking.
High number of oil spills due to accidents.
Methane (CH4) is a Greenhouse Gas with a warming effect 20 times stronger than Carbon Dioxide (however, methane is shorter lived in the atmosphere). Any direct emission of methane from leaks in the gas production chain contribute to global warming.
Combustion of oil & gas is responsible for emissions at local, regional, and global levels, including CO2, NOx, SOx and particulate matter.
The transport sector, which is based on oil products, accounts for a large share of global CO2 emissions
Notes: Oil and Gas have a negative impact on the environment at all the stages of the supply chain from production to transportation and final uses:
Hydraulic fracking, which consists of fracturing rocks with pressurized liquid to produce oil and gas, causes significant environmental concerns. These are related to waste-water disposal, pollution of underground water, and increased seismic activity.
After being extracted, oil is often transported using ships. Several oil spills in the sea have resulted in destruction of the ecosystem and loss of biodiversity, as well as pollution of the water.
If there are any leaks in the natural gas production chain, methane (CH4) is released, contributing to global warming. This greenhouse gas has a 20-times stronger warming effect than CO2, though it has a shorter lifespan in the atmosphere.
When the oil or the gas is finally burnt in power plants, emissions at local, regional, and global levels are released. These include CO2, NOx and particulate matter.
Oil products are the main fuels in the transport sector (cars, buses, trucks, motorbikes, and so on), which is responsible for a large share of global emissions.

## Slide 22
22
6.3.5 Social Impact of Oil & Gas power plants
6.3 Impacts of Fossil Power Plants
Oil, gas, and coal have long contributed to the development of economies and their security of supply. However, as well as environmental impacts, they have significant economic and social consequences:
Oil & gas are often produced in politically unstable regions
Reported cases of large displacement of local populations for oil extraction activities and harm to local societies and activities
Shifting away from oil and gas may have system impacts which need to be considered when supporting governments in decarbonization strategies:
We need models to quantify potential impacts of continuing current trends or shifting away from them. They can help us understand synergies and trade-offs between supply chains.
Notes: Demand for oil and especially gas is expected to increase if policies do not change drastically. This demand is driven by large and fast-growing economies. Technological solutions which could avert this are emerging, but they could have deep impacts on the system, which are not always known. There are also social factors that slow down the shift from oil and gas resources, including the need for fast growth (which can be easier to achieve using fossil fuels), the conservative trust in mature solutions, and the need for security.
Oil, gas, and coal have long contributed to the development of economies and their security of supply. However, they have important economic, social, and environmental consequences. Oil and gas are often produced in politically unstable regions, where sometimes wars, civil conflicts, or turmoil are related to control of the fossil fuel reserves. Moreover, there are many reported cases of large displacements of local populations for oil extraction activities, which can harm local societies.
From an environmental point of view, there is an urgent need to reduce global reliance on fossil fuels, but shifting away from these sources may have system impacts that need to be considered when supporting governments' decarbonization strategies. We need models to quantify potential impacts of continuing current trends or shifting away from them.

## Slide 23
23
Lecture 6.3 References
Gardumi, F. (2021, March). Oil, gas and coal: social, environmental, economic and system impacts (Version 1). Zenodo. http://doi.org/10.5281/zenodo.4585626

## Slide 24
24
6.4.1 Introducing Transmission and Distribution
6.4 Transmission and Distribution
Power is generated
Power is transmitted over large distances
Power is distributed to consumers
Notes: Once electricity has been produced by power generation technologies, it has to be transported to consumers for use. This process is done by power transmission and distribution technologies. Power transmission occurs over large distances and at high voltages, transporting electricity from the site of generation to areas where it is used, such as cities. Distribution occurs over much smaller distances and at lower voltages, taking power from the transmission system and distributing it to individual buildings.

## Slide 25
25
6.4.2 Balancing the Electricity System
6.4 Transmission and Distribution
Notes: At all times the electricity system has to be balanced. This means that generation has to equal consumption plus losses. Losses occur in energy systems for several reasons, for example power transmission technologies are not 100% efficient. This means that some energy is lost at several stages of the chain from electricity generation by power plants to electricity consumption by consumers. To ensure there is sufficient energy available, these losses must be considered in the balance of the system, meaning generation must equal the sum of consumption plus losses.
Because there is often no economically viable way to store very large quantities of electricity, it is important that this balance is maintained at all times, so in any one instance the total electricity generated should equal the sum of consumption plus losses. This has implications for the planning of energy supply, because some electricity generation technologies have limited flexibility, meaning they cannot be relied upon to produce electricity at all times. It is important that we model time variability so we can ensure that the system is balanced at all times.

## Slide 26
26
6.4.3 System Losses & Reliability
6.4 Transmission and Distribution
Notes: So, electricity systems are not completely efficient and contain several losses. This means that not all of the primary energy entering an electricity system is used by consumers. It is important to understand where these losses come from and consider them when modelling energy systems. The first source of losses is thermal energy losses in the generation of electricity; thermal electricity generation by power plants is not 100% efficient and some of the primary energy put in is lost as heat. These are usually the largest losses in the system. For example, not all of the energy in the coal burned at a coal power station is converted to electricity as a proportion of it is lost as heat. The concept of power plant efficiency is explored further in Lecture 4. A further source of energy losses is in the transmission and distribution of electricity, which again is not a 100% efficient process. Losses can be estimated as a percentage by calculating the difference between the output and input energies, then dividing this difference by the input energy, as illustrated in the equation on the slide.
Because of these system losses, electricity systems must always generate more electricity than is actually consumed to ensure demand is met. In some cases, electricity systems can fail to meet demand, for example because there is insufficient generation capacity. This has significant impacts on society.

## Slide 27
27
6.4.4 Transmission & Distribution in Reference Energy Systems
6.4 Transmission and Distribution
Notes: Now we understand a little more about transmission and distribution technologies, let's think about how we represent them in Reference Energy Systems and OSeMOSYS. On this diagram, the transmission and distribution technologies are highlighted. We can see that they are each modelled as a separate technology represented by a box on the reference energy system. We can also see what the input and output fuels for each of these technologies are. The input fuel for the transmission technology is the electricity from power plants, which is transported by the transmission technology to produce the output fuel of electricity after transmission. This electricity is then ready to be distributed to users, so it is taken in by the distribution technology as the input fuel. The distribution technology then produces the output electricity which is ready to be used – in this diagram this is named electricity after distribution. We will look at how these technologies are modelled in more detail in the following slides.

## Slide 28
28
6.4.5 Transmission and Distribution in OSeMOSYS Pt1
6.4 Transmission and Distribution
Electricity after distribution
Notes: Here we can see a close up of the power transmission and distribution technologies as they appear in Reference Energy System diagrams, as well as the generic naming convention used to name the technologies and their input and output fuels. We can see that power transmission is named PWRTRN., with an input fuel of ELC001, and an output fuel of ELC002, while power distribution is named PWRDIST, with an input fuel of ELC002, and an output fuel of ELC003. The first important parameters for defining power transmission and distribution technologies in OSeMOSYS are the input activity ratio and output activity ratio, with examples shown on this slide. As with previous examples, we will set the output activity ratio to 1 by default. For power transmission, the output activity ratio will therefore be 1 for ELC002, since this is the fuel produced by power transmission. With the output activity ratio set to 1, we can calculate the input activity ratio using the technology's efficiency, which in this case is 95% or 0.95 as a decimal. The input activity ratio is 1 divided by the efficiency as a decimal, so 1 divided by 0.95, giving us an input activity ratio of 1.05 for the power transmission technology, assigned to ELC001, since this is the input fuel for power transmission. The same method can be used to calculate the input activity ratio for power distribution, as shown on the slide.

## Slide 29
29
6.4.6 Transmission & Distribution in OSeMOSYS Pt2
6.4 Transmission and Distribution
Other important parameters for defining transmission and distribution in OSeMOSYS:
Capital Cost ($/kW)
Fixed Cost ($/kW/yr)
Variable Cost ($/GJ)
Operational Life (years)
Notes: Other important parameters for defining transmission and distribution technologies in OSeMOSYS are Capital, Fixed, and Variable Costs, and Operational Life. We discussed all of these parameters earlier in the lecture in relation to power plants, and we will now look at their meaning for power transmission and distribution technologies. The capital cost, in $/kW, defines the one-off investment costs of the power transmission or distribution technologies, mainly including the costs of the electrical equipment required. The fixed cost, in $/kW/yr, represents the fixed annual costs of operating and maintaining the transmission and distribution systems, for example the costs of workers' salaries. Thirdly, the variable cost, in $/GJ, represents costs that only occur when the transmission and distribution technologies actively transport electricity, defining the cost per GJ of electricity transmitted or distributed. Finally, the operational life refers to the lifetime of the power transmission or distribution technology in years. These technologies can have quite a long lifetime, for example 30 or 50 years. We will practice adding these technologies to our own model in the hands-on exercises.

## Slide 30
30
Lecture 6.4 References
Taliotis, C., Gardumi, F., Shivakumar, A., Sridharan, V., Ramos, E., Beltramo, A., Rogner, H., Howells, M., 2018. Electricity supply system in OSeMOSYS I (Thermal power plants and T&D), KTH-Desa and OpTIMUS.community. Available at: https://zenodo.org/record/1942510#.YC5VjehKhPY. [18/02/2021] DOI: 10.5281/zenodo.1942510

## Slide 31: Thank you
www.climatecompatiblegrowth.com
Consolidated by: Fernando Plazas-Niño, Kane Alexander, Rakia Bouallegui, Lucy Allington, Carla Cannone, Pooya Hoseinpoori, Alexander Kell, Adam Hawkes, Mark Howells