## Slide 1
CLEWs++ Modelling Course
LECTURE 1
Introduction to CLEWs++ Modelling Course

## Slide 2: First things first
2
Course prerequisite
Before taking the current course, the participant should first take the ‘Introduction to CLEWs’ course which can be accessed here: https://www.open.edu/openlearncreate/course/view.php?id=11715.
On top of that, the participant must have built at least one additional model (i.e. not as part of the first course) with minimal to zero help
Course objective and expectations
This course aims at helping the participant understand both the theoretical and practical principles around the CLEWs++ concept
Following the completion of the course, the participant will be able to build and analyse a full scale CLEWs++ model, using OSeMOSYS and templates provided
Course forum
For questions related to CLEWs++ modelling, please refer to the relevant forum https://forum.u4ria.org/c/clews/10

## Slide 3: Energy and other resource/economic systems are complex
Natural resources are finite
Money doesn’t grow on trees
Some situations are beyond our control…
Policy-making is complicated

## Slide 4: Quantifying the impossible
The use of mathematical models becomes imperative…

## Slide 5: From CLEWs to CLEWs++
CLEWs++ is an application of the CLEWs framework which features the following aspects:
The model is policy-relevant. This requires the following:
100% GHG emissions coverage. While this can definitely be the case with any CLEWs model, for CLEWs++ it’s a necessity. Therefore, waste sector and industrial process emissions (commonly omitted in other cases) must be included
Level of detail and quality is quite high
Model development has to follow a standardised and replicable method
Integrated assessment methodology for climate, land, energy and water security
Primary objective is to assess the role of technology choice and technology change
CLEWs
CLEWs ++

## Slide 6: The CLEWS++ Model Develops Integrated and Coherent Scenarios for Global GHG Emissions
CLEWs++ models the current and future energy-land-water-waste system through linear optimisation CLEWs++ uses linear optimisation to analyse how policymakers and markets will drive economic energy outcomes embeds socio-political and techno-economic feasibility into the scenarios As opposed to system simulation where the user forces the behaviour of the model, in optimisation, the model finds the least-cost solution, considering given constraints | CLEWs++ identifies least cost strategies for meeting energy/food/water demand security goal Capital costs Energy costs External costs While ensuring a high degree of feasibility and realism Socio-political preferences Most likely climate policies Public opinion on key technologies (e.g., carbon capture and storage) Technoeconomic feasibility Market and supply chain scale up (e.g., hydrogen) Resource availability (e.g., biomass)

## Slide 7: Integrated system analysis
The CLEWs++ whole-system approach not only incorporates all sectors, but also crucially considers the interactions between sectors. This is vital to ensuring scenario outcomes are realistic and coherent.
Let’s look at the energy system as an example.The energy system is comprised of numerous interacting systems, and the interactions within this system play a crucial role in determining the economics and outcomes of potential energy transitions.
2-way impact: demand affects supply and vice versa
Power generation
Hydrogen production
Transport
Buildings
Industry
Energy resources
Example Intra-System Interactions:
Decarbonisation of the power sector will increase power prices, raising the cost of power for electrified heat and transport
In turn, electrifying end-uses such as heat and transport will affect the economics of power generation and the resulting cost of power
Expansion of power and hydrogen demand could exhaust the cheapest renewables, and could require the exploitation of more expensive low-carbon resources
Power and hydrogen supply can interact through sector coupling or “Power-to-X”, reducing costs of both power and hydrogen and improving the economics of decarbonization and electrification
Takeaways
  Interactions between sectors will drive trends that cannot be predicted using exogenous cost assumptions
  These trends will accelerate or decelerate uptake of key technologies and have a profound effect on scenario outcomes
  Considering individual sectors in isolation will therefore give a distorted view of the future
  CLEWs++ co-solves across all key sector interactions, creating scenario outcomes that reflect the how these sectors will co-evolve

## Slide 8: CLEWS++ Represents all Major Conventional, Low-Carbon and Zero Emissions Technologies to meet demand in Future Energy Scenarios
Power
  Generation Coal | Oil | Gas | Biomass | Coal with CCS | Gas with CCS | Biomass with CCS | Nuclear | Hydro | Onshore wind | Offshore wind | Solar | Hydrogen
  Storage Battery storage | Power to gas
Hydrogen
  Coal gasification | Steam methane reformer | Coal gasification with CCS | Steam methane reformer with CCS | Electrolyzer
Liquid fuel production
  Petroleum-derived fuel | Biofuel | Synthetic fuel
Transport
  2-3 wheelers | Cars | Buses | Light commercial vehicles | Heavy commercial vehicles Liquid fuel ICE | Plug-in hybrid | Battery electric | Hydrogen fuel cell | Natural gas ICE
  Rail Liquid fuel | Electric
  Aviation Liquid fuel
  Shipping Liquid fuel | Ammonia
Industry
  Iron and steel Blast furnace-basic oxygen furnace (BF-BOF) | BF-BOF with CCS | Gas direct reduced iron with electric arc furnace (DRI-EAF) | Hydrogen DRI-EAF | Scrap steel with electric arc furnace
  Cement kilns Coal | Oil | Gas | Biomass | Coal with CCS | Gas with CCS | Biomass with CCS | Hydrogen
  Low-temp process heat Coal | Oil | Gas | Biomass | Hydrogen | Heat pump | District heat
  High-temp process heat Coal | Oil | Gas | Biomass | Coal with CCS | Gas with CCS | Biomass with CCS | Hydrogen
  High value chemicals Oil
Buildings
  Residential heat | Non-residential heat Coal boiler | Oil boiler | Gas boiler | Biomass boiler | District heat | Resistive heater | Heat pump
  Residential cooking Biomass stove | Coal stove | Gas stove | Oil stove | Electric stove
  Residential appliances | Non-residential appliances
Other sectors
  Agriculture Soils | Enteric fermentation | Manure management
  Land use change
  Waste Solid waste | Liquid waste
GHG removal
  Direct air capture
Note: This list is indicative, not exhaustive

## Slide 9: CLEWs++ coverage and interactions
Water
Waste
Climate
Energy
Land
In theory, all 5 systems may somehow interact with each other. Nevertheless, not all those interactions are significant enough or relevant for CLEWs++ and thus, they are usually omitted. For instance, the energy requirements for treating waste are -in the grand scheme of things- very small and therefore, this interactions is typically not covered.

## Slide 10: Example Reference Energy System
Production and Power Technologies
Fuel Transformation and Distribution Technologies
Transformation Technologies
End Use Technologies
Electrolyser
Biofuel Production
High Temp. Process Heat Techs. (w/ or w/o CCS)
Low Temp. Process Heat Techs.
Heat Technologies
Direct Air Capture
Motive Energy Technologies
Transport
Passenger:
Cars
2/3 Wheelers
Buses
Vans
Aviation
Rail
Freight:
Ships
Trucks
Factories
Cement
Chemicals (split into 3 sub-sectors)
Iron and Steel
Aluminum
Other
Housing Sector
Agricultural Units
Service Sector
Heat & Power Plants (w/ or w/o CCS)
Uranium
Biomass
Natural Gas
Coal
Oil
Low temp. process heat
Sectoral (district) heat
Sectoral electricity (post transmission)
Electricity (pre transmission)
Sectoral heat
Motive energy
Low temp. process heat
High temp. process heat
Hydrogen
Biofuels
Note: This diagram is indicative, not complete

## Slide 11: Disambiguation
Modelling scope
Refers to what aspects the model covers, e.g. whole energy system, CLEWs etc. This is independent from where the model is built. CLEWs++ will be the focus of this course
Modelling environment
Modelling environment or model generator refers to the platform/code used to build a model. For example, Excel can be the environment for a simple model. Various software can be also used. OSeMOSYS will be the focus of this course
Interface
OSeMOSYS can run using simple txt files (i.e. no interface) but various interfaces have been developed over time. The Model User Interface for OSeMOSYS (MUIO) will be the focus of this course
Templates
In order to prepare the input data for any model, the user usually relies on certain templates, depending on the scope of the model. The Model Development Infrastructure (MDI) will be the focus of this course

## Slide 12: Modelling scope
CLEWs++ model
CLEWs model
Whole energy system model
Simple power sector model
Power plants
Simple electricity demand
Industry
Buildings
Transport
Water
Land
Climate
Waste
Increased detail and policy-making relevance
Following standardised development approach

## Slide 13: Modelling environment
Any of the following can be used to build a CLEWs++ model. NB: the list is not exhaustive

## Slide 14: Interfaces for OSeMOSYS
MUIO is the most recently developed and advanced interface for using OSeMOSYS
MUIO can be downloaded here link
In the past, various OSeMOSYS interfaces have been developed. Most notably: MoManI, Otoole and Answer (not exclusive for OSeMOSYS use)

## Slide 15: Templates
Model Development Infrastructure (MDI)
Can be accessed here: https://zenodo.org/records/16875355
Various templates for building OSeMOSYS models have been developed over the years. Most notably, the Starter Data Kits (SDKs) and OSeMOSYS Global. Those templates differ both in terms of scope and usability.

## Slide 16: Thank you
www.climatecompatiblegrowth.com