## Slide 1
CLEWs++ Modelling Course
LECTURE 2
Main aspects of CLEWs++ model building

## Slide 2: Learning outcomes
2
Understand the main steps that should be taken when developing a CLEWs++ model
Look into the theory of those steps, so the learner can adapt the strategy as needed
1
2

## Slide 3: CLEWs++ model building process overview
NB: The following steps are not unique to CLEWs++ model development
Model scoping
Model calibration
Demand projections
Technology selection
Constraints
Scenario development
Data collection
Model QA and debugging
Key considerations
Data collection and model QA are process that happen at every stage.
Model QA and debugging is not covered in this lecture as there is a dedicated one on the topic.
While these processes can be all carried out by the same person, they require different skill–sets. Therefore, task allocation across team members can be done accordingly.
If more than one person is involved in the model development, tasks can be divided either horizontally or vertically.
  Horizontal split: each team member works on different processes, e.g. model calibration across all sectors
  Vertical split:each team members carries out all the processes for specific sectors

## Slide 4: Data collection
@Fra, others, is this covered in the first lecture? if so, pls mention so in the previous slide. If not, I’m sure we’ve got some material from courses etc that we could use?

## Slide 5: Model Scoping
  Defining the model scope is about a) setting the system boundaries and b) deciding on the level of detail
System boundaries
Level of detail
A CLEWs++ model features 100% GHG representation. As such, all sectors that emit GHG need to be represented.
Those emissions stem from the following sectors and thus, they all need to be included in the model:
Energy sector (combustion)
Industrial process emissions
Agriculture, Forestry, and Other Land Uses (AFOLU)
Waste
A CLEWs++ model needs to be policy-relevant. Hence, the level of detail needs to facilitate this objective.
The exact level of detail is case specific and requires an understanding of the facts on the ground in the country that is analysed. The breakdown of each sector can vary. For example, if the cement industry is not that significant in a certain country, cement doesn’t necessarily need to be represented explicitly. It can instead be lumped into the ‘other industry’.

## Slide 6: Model calibration
6
Model calibration is the process of systematically adjusting model parameters and input assumptions so that the model’s simulated outputs accurately reproduce observed system behaviour over one or more historical years, including alignment of initial conditions to ensure that the model’s starting state reflects the real-world conditions at the beginning of the modelling period.
It is important because those initial conditions will largely determine what happens during the first years of the modelling period, though their influence may extend beyond that. For example, suppose there are three types of cars: internal combustion engine (ICE), hybrid, and electric, and the hybrid is the cheapest option when considering lifetime ownership costs. If there were no existing cars, the model would simply invest in hybrids. However, if there are already some ICE or electric vehicles, the model would not scrap them before the end of their lifetimes, as doing so would not be economically viable.
The parameters used to calibrate the model are typically the Total Technology Annual Activity Lower Limit and Residual Capacity.
The sum of the activity of the technologies that meet a particular demand in a given year must be equal to that demand for the same year. In some cases, this is how demand is calculated. We start with fuel use (for example, for household space heating), which is converted into output activity through assumed efficiencies, and by summing these we obtain the total demand. In other cases, the demand may be given (for example, total cement production) and is then distributed across different technologies that serve the same demand, based on specific assumptions.
When calibrating a single technology, there are several possible approaches. In some cases, we begin with the input fuel, assume an efficiency, and calculate the resulting output activity. In others, we start with the output, assume an efficiency, and derive the input fuel. If both are available, we can calculate the efficiency directly, though this often requires sense-checking, as the input and output data may come from disparate sources, potentially leading to unrealistic efficiency values.
Model inputs
Calibration
Simulated data
Historical data
=

## Slide 7: Energy balances
7
Energy balances constitute the cornerstone for the calibration of a CLEWs++ model.
Energy balances are comprehensive accounting frameworks that track the flows of energy within an economy or system, showing how energy is produced, transformed, and consumed across different sectors and fuels. Each balance sheet maintains consistency between inputs and outputs, ensuring that the total supply equals total use of energy in physical or energy-equivalent units. These sheets provide a structured overview of energy efficiency, dependency, and transformation losses, forming the foundation for energy modelling, policy analysis, and emissions assessment.
While energy balances provide an excellent starting point, further analysis is required to disaggregate fuel use into the specific energy flows represented in the model. For example, within the housing sector, energy balances do not indicate the fuel share used for heating, cooking, lighting, and other end uses.
  Each of the sector-specific lectures will give practical examples on calibration

## Slide 8: Demand projections (1/3)
8
OSeMOSYS is a demand driven model. This practically means that a final service demand in a chain needs to be exogenously defined. The model will then choose the optimal technology mix to meet that demand, based on given costs and constraints
Below are some examples of final service demands used in a CLEWs++ model
Household electricity for appliances
Household water heating
Household space heating
V-km covered by cars
V-km covered by buses
V-km covered by trucks
Various crops
Mining output
Industrial heat

## Slide 9: Demand projections (2/3)
9
Base year demands are estimated using historical data
Demands for all other years are calculated and then fed into the model
While there are different methods for calculating demands, econometrics is the most common one
Econometrics is the application of statistical and mathematical methods to economic data in order to test hypotheses, forecast future trends, and estimate relationships between variables.
How it's used for calculating service demands:
Econometrics helps estimate the demand for services by analysing historical data (e.g., price, income, demographics, past usage patterns) and identifying how these factors influence demand. Common approaches include:
Regression analysis to model demand as a function of variables like price, income, or seasonality.
Time series models to forecast future demand based on past trends.
Panel data analysis when data spans across time and multiple locations or groups.
This allows businesses and policymakers to make informed decisions about resource allocation, pricing, staffing, and capacity planning.

## Slide 10: Demand projections (3/3)
10
An econometrics example
Year | Income (USD) | Urbanisation (%) | Electricity Price (USD/kWh) | Electricity Demand (kWh)
2015 | 30497 | 59.5 | 0.10733 | 119.8
2016 | 30973 | 60.6 | 0.10443 | 134.6
2017 | 32870 | 62.5 | 0.11145 | 129.1
2018 | 34856 | 61.4 | 0.10954 | 122.5
2019 | 34210 | 62.7 | 0.11950 | 133.8
2020 | 35321 | 65.0 | 0.12833 | 128.1
2021 | 38246 | 65.7 | 0.12758 | 137.4
2022 | 38545 | 68.1 | 0.14077 | 130.9
2023 | 38419 | 68.0 | 0.14144 | 133.8
2024 | 40543 | 68.6 | 0.14854 | 142.9
2025 | 41000 | 71 | 0.15500 | 140.0
2026 | 42250 | 72 | 0.15750 | 141.9
2027 | 43500 | 73 | 0.16000 | 143.8
2028 | 44750 | 74 | 0.16250 | 145.7
2029 | 46000 | 75 | 0.16500 | 147.5
Demand (kWh)=−67.47+0.00028⋅Income (USD)+2.16⋅Urbanisation (%)−40.98⋅Electricity Price (USD/kWh)

## Slide 11: Technology selection in each sub-sector or service
11
Represent All Historical Fuels
All historical fuels used within a sector should be represented in the model. Depending on the scope and objectives, fuels may be aggregated or disaggregated:
Aggregation example: Various oil sub-products can be grouped together under “oil”, and wood and other biomass types may be combined for simplicity.
Disaggregation example: In some cases, the same fuel should be represented by multiple technologies because their characteristics differ significantly. For instance, resistive heaters and heat pumps both use electricity to produce heat, but they behave very differently in terms of efficiency, cost, and flexibility.
Include Emerging or Future Technologies
In certain cases, technologies not yet widespread or even currently non-existent should be considered to reflect future innovation and policy pathways. Examples include:
Hydrogen vehicles
Power plants with Carbon Capture and Storage (CCS)
These technologies should be allowed to compete in future years even if they have no historical presence.
Technology Choice Driven by Cost and Constraints
Technology selection in OSeMOSYS is guided by two key principles:
Cost minimisation – The model seeks the least-cost combination of technologies to meet demand. This is assessed at the output level, expressed as the Levelised Cost of Output
(LCO-X), where X could represent electricity, heat, or hydrogen.LCO-X captures the total lifetime cost of producing one unit of output, including capital, operation and maintenance, and fuel costs.
By comparing LCO-X across technologies, the model identifies the most economically efficient mix.
2. Constraints – These limit or force the uptake of certain technologies to better reflect real-world conditions such as policy targets, resource availability, or behavioural preferences.
Techno-economic Data Sources
Techno-economic data (costs, efficiencies, lifetimes, etc.) should be drawn from local or regionally relevant sources whenever possible. If local data are unavailable, select sources that best approximate the regional context and document any assumptions clearly.

## Slide 12: Constraints
12
While OSeMOSYS seeks to achieve cost minimisation across sectors, the real world often does not operate under optimal conditions. To reflect this, constraints are introduced into the model. These constraints are typically of the following types:
Forcing a technology (in terms of activity or capacity) into the system, even when it is not the cost-optimal choice.
Capping the uptake of a technology, even if it would otherwise be the most economical option.
Regulating the rate of change at which a technology can enter or exit the system.
Controlling the share of a certain technology into the mix
A few examples of real-world factors that are translated into model constraints are shown below.
⛔
Hydropower may be the lowest-cost option for power generation, but it is naturally limited by resource availability.
✅
Heat pumps may not be the cheapest option for household heating, yet government incentives can lead to a degree of uptake.
👤
Electric vehicles might be the most cost-effective choice, but some people simply prefer petrol cars.
🏗️
Even when a technology is the lowest-cost option, its uptake may be restricted by manufacturing scale-up capacity or other practical limitations.

## Slide 13: Constraint examples
1
2
3
4
5
Constraint description
Parameter used
There’s a scheduled 1 GW nuclear plant installation for 2027 and we know that until 2030 there will be no more nuclear plants.
Hydropower capacity cannot exceed 600MW due to natural resource constraints.
Coal power plants cannot operate from 2035 and beyond
EV growth rate is 10% yoy.
There’s a target to produce at least 15PJ of biofuels from 2028 onwards
Total Annual Min Capacity Investment set to 1 for 2027 and 0 for the years before and after.
Also, Total Annual Max Capacity Investment same values as above until 2030. Default value (e.g. 9999) from 2031 onwards.
Total Annual Max Capacity set to 0.6 for all years.
Total Technology Annual Activity Upper Limit set to 0 from 2035 onwards.
Technology Activity Increase By Mode Limit set to 0.1 for ll years.
Total Technology Annual Activity Lower Limit set to 0 from until 2027 and 15 from 2028 onwards.

## Slide 14
Tool to create customized constraints. Flexible way to control and restrict OSeMOSYS models
Allows users to specify restrictions on relationships between variables.
Can be created for Activity, TotalCapacity and New Capacity variables
Can be equalities or inequalities
User-defined constraints (UDCs)
Examples
Set minimum shares (i.e. replicate targets such renewable electricity, fuel blending,
Apply constraints on activity, new capacity or total capacity of group of technologies
Set reserve margin constraints
… and many more

## Slide 15
UDC Constant: value to be respected in the defined constraint.
UDC Multiplier Activity: the factor by which the Total Technology Annual Activity of a Technology is multiplied by, as defined by the user.
UDC Multiplier Capacity: the factor by which the New Capacity and Total Capacity Annual are multiplied by, as defined by the user.
Parameters
TotalCapacityAnnual: Total capacity of a technology in a given year
NewCapacity: Capacity additions for a technology in a given year.
TotalTechnologyAnnualActivity: Total utilization of a technology in a given year
Variables
UDC Multiplier New Capacity: the factor by which the New Capacity and Total Capacity Annual are multiplied by, as defined by the user.
Variables and parameters

## Slide 16
Structure
Where i represents the technologies included in this specific UDC
UDCs are applied each year and both multipliers and constant values can change from year to year
Can be either inequalities or equalities
Any relationship that you can describe via this structure can be represented

## Slide 17: Example 1: Wind power investment
A model has 3 wind turbine technologies representing different wind classes: PWRWND001, PWRWND002 and PWRWND003
We want to limit the total investment in wind turbines to 2 GW in 2025 based on the perceived capacity of the domestic industry to install new turbines.
The regular Total Annual Max Capacity Investment parameter cannot capture this because it can only be applied to one technology at a time
However, we can create a UDC to do this

## Slide 18: Example1: Wind power investment continued
Steps:
Create a UDC (e.g. “WNDNEWCAP”) and assign the three WND technologies to it.
Enter the value 1 for UDC Multiplier New Techs for all three techs
Leave the values as 0 (default)for UDC Multiplier Capacity and UDC Multiplier Activity
Enter 2 as the value for UDC constants
For this constraint we want the sum of investment in the three technologies to be less than a given value. We can write that as:
UDC Multiplier Activity
UDC Constant

## Slide 19: Example 2: Land-use change

## Slide 20
Using User-Defined Constraints to set RE targets
UDC Constant
UDC Multiplier Activity
UDC inclusion
Let us say you want to create a target of 60% renewables (i.e. at least 60% of power
generation is renewable)
UDC Tag

## Slide 21: Scenario development (1/2)
21
Why do we need scenarios?
Reflect uncertainty
Answer “what if” type of questions
  A geopolitical incident
  A technological advancement
  Climate change
  Various policies
  Societal response
Help adjust political or business strategy
  Scenarios are modelled by tweaking one or more parameters in the base case
Before developing a new scenario, it’s critical to understand what you are trying to achieve. Scenario definitions can emerge through different approaches, but stakeholder engagement is usually catalytic

## Slide 22: Scenario development (2/2)
22
Scenario types
Dimension
Category
Description
Purpose
Temporal flow
Methodology
Forecasting
Backcasting
Projecting
Top-down
Bottom-up
Descriptive
Normative
From present trends to future
From future goal back to today
Hypothetical futures from assumptions
Start big-picture, refine down
Start from detailed assumptions, build up
What could happen
How to achieve a goal

## Slide 23: Thank you
www.climatecompatiblegrowth.com