## Slide 1
CLEWs++ Modelling Course
LECTURE 3
Buildings in the CLEWs++ concept

## Slide 2: Learning outcomes
2
Understand how buildings are modelled in the CLEWs++ concept
1
2
Go through some key considerations with regards to the main technologies used in buildings

## Slide 3
In the CLEWs++ model, the housing sector is divided into three key parts: cooking, heating, and other electricity, to reflect the distinct energy demands, technologies, and policy implications associated with each end-use.
Housing sector in the CLEWs++ model
Cooking
Heating
Other electricity
Cooking typically involves a wide range of fuels such as electricity, oil, and biomass, and is closely tied to household air pollution and health outcomes.
Heating encompasses both space and water heating, often with seasonal variations in which the specified demand profile is particularly important and with multiple technology options including electric heaters and gas boilers.
By modelling these categories separately, the framework allows for more accurate analysis of energy efficiency improvements, fuel-switching strategies, and emissions impacts.
Energy use for appliances, lighting, and cooling is currently grouped under “other electricity” for simplicity and due to data limitations. However, these components differ in their load profiles and efficiency potential and could be further disaggregated in future model iterations to enhance policy relevance and technical accuracy.

## Slide 4
Housing sector – Cooking flow diagram
The cooking sector represents a significant portion of household energy use, particularly in low- and middle-income countries where it can account for over 50% of residential energy consumption. It involves a variety of fuel sources—such as biomass, coal, natural gas, oil, and electricity—as reflected in the CLEWs++ model structure.
Globally, cooking is a major contributor to greenhouse gas emissions and indoor air pollution, especially when traditional biomass (wood, charcoal, dung) or coal is used in inefficient stoves. These fuels release high levels of carbon dioxide, methane, and black carbon, contributing not only to climate change but also to severe health impacts.
Transitioning to cleaner cooking fuels and technologies, such as electric or gas stoves, can therefore deliver both climate and public health benefits, making the cooking sector a key target for sustainable energy policies and interventions.
Housing cooking with biomass
Housing cooking with coal
Housing cooking with natural gas
Housing cooking with oil
Housing cooking with electricity
A
B
C
D
E
F
Commodity Key
A = Biomass
B = Coal
C = Natural gas
D = Oil
E = Electricity
F = Housing cooking

## Slide 5
Housing sector – Heating flow diagram
The heating sector is a major part of household energy use, especially in colder regions, where it often dominates residential energy demand. The CLEWs++ model captures this through various fuel and technology options, including biomass, coal, gas, oil, electricity, and district heating. It distinguishes between general electric heating and resistive electric heaters, which convert electricity directly into heat. Resistive heaters are low-cost devices and are typically less-efficient compared to other electricity-based alternatives like heat pumps. However, they are likely to be used for many years to come because of their convenience.
District heating systems are centralized heating systems that distribute heat to buildings through insulated pipes. They remain rare in low-income countries due to high infrastructure costs, lower heating demand, and less urban density.
As a result, decentralized and fuel-based heating options remain the norm in much of the developing world. However, these systems can offer high efficiency and lower emissions, especially when powered by renewable or waste heat sources, making them a valuable component of sustainable heating strategies globally.
Commodity Key
A = Biomass
B = Coal
C = Natural gas
D = Oil
E = Electricity
F = Power heat after district heating transmission
G = Housing heating
Housing heating with biomass
Housing heating with coal
Housing heating with natural gas
Housing heating with oil
Housing heating with electricity
A
B
C
D
E
G
Housing heating with resistive heater
District heating for housing
F

## Slide 6
Housing sector – Electricity flow diagram
This diagram illustrates how household electricity use is allocated in the CLEWs++ model. Electricity from the grid is directed to separate end-uses: cooking, heating, and all other uses represented in the housing unit technology. The housing unit captures electricity consumption not related to cooking or heating, including lighting, appliances (e.g., refrigerators, TVs), cooling (e.g., fans, air conditioners), and other uses. Capturing "other electricity" in the household sector is essential for accurately understanding and planning for total residential energy demand. As appliance ownership increases and cooling demand rises due to climate change and urbanization, this segment is expected to grow significantly.
Moreover, disaggregating this category in future model updates could support more precise interventions, such as promoting efficient lighting, appliance labeling programs, or sustainable cooling technologies, all of which are crucial for reducing peak electricity loads and achieving broader energy and climate goals.
Energy efficiency throughout the buildings sector is particularly important. For technologies modelled explicitly the efficiencies are directly tweaked but for other electricity we typically have to improve it exogenously (reduce other electricity demand) if we want to assume efficiency gains.
Housing cooking with electricity
Housing heating with electricity
Housing heating with resistive heater
Housing unit
A
C
B
D
Commodity Key
A = Electricity for housing
B = Housing cooking
C = Housing heating
D = Housing unit activities

## Slide 7
Commercial and public services sector in the CLEWs++ model
In the full-scale CLEWs++ model, the commercial and public services sector is divided into two key parts: heating and other electricity, to reflect the dominant energy uses and operational characteristics of this sector.
Heating
Other electricity
Capturing this end-use separately is essential for analysing efficiency improvements, fuel-switching options, and the integration of low-carbon heating technologies.
Heating includes both space and water heating across buildings such as offices, schools, and hospitals, with seasonal demand variations and a range of energy sources including electricity, oil, and district heating.
Other electricity encompasses a broad set of uses such as lighting, cooling, office equipment, IT infrastructure, and ventilation. These uses vary significantly in terms of load profiles and energy intensity depending on the type of service activity.
While grouped together for simplicity and to match available data, this category could be further disaggregated in future model versions to better capture the growing impact of digitalization, cooling demand, and energy efficiency measures within the services sector.

## Slide 8
Commercial and public services sector – Heating flow diagram
The structure of the services sector heating module in the CLEWs++ model reflects the diversity of fuels and technologies used to meet heating demand in commercial and public buildings. It includes biomass, coal, natural gas, oil, electricity (both heat pumps and resistive heating), and district heating, allowing for detailed analysis of energy flows and emissions.
Heating typically represents a significant share of energy-related emissions in the services sector—often accounting for over 40% in colder regions—but its contribution can vary widely depending on climate, building use, and fuel availability. Resistive heaters are commonly used where affordability and ease of installation take priority over efficiency, particularly in smaller or under-resourced facilities. District heating systems, while prevalent in high-density urban areas of some countries, are generally limited in regions with lower infrastructure investment or less centralized planning.
This disaggregated modelling approach enables more accurate assessments of decarbonization strategies, energy access planning, and technology deployment tailored to local conditions within the services sector.
Commodity Key
A = Biomass
B = Coal
C = Natural gas
D = Oil
E = Electricity
F = Power heat after district heating transmission
G = Services heating
Services heating with biomass
Services heating with coal
Services heating with natural gas
Services heating with oil
Services heating with electricity
A
B
C
D
E
G
Services heating with resistive heater
District heating for services
F

## Slide 9
Commercial and public services sector – Electricity flow diagram
The structure shown in this diagram highlights the allocation of electricity use within the commercial and public services sector in the CLEWs++ model, distinguishing between electricity used for heating (services heating with electricity and with resistive heater) and all other uses, captured under services unit. This separation is critical for accurately reflecting the diverse and often high electricity demand in service-sector buildings. The services unit branch includes electricity used for lighting, office equipment, cooling, ventilation, elevators, and other essential operations that keep public and commercial facilities running.
These uses can represent a significant portion of electricity consumption, particularly in urban areas and in facilities operating for extended hours, such as hospitals, government offices, and retail spaces.
Capturing this category explicitly enables the model to analyze trends in service-sector electrification, assess the impacts of efficiency improvements, and evaluate demand-side management strategies. While currently grouped for simplicity, future model updates could disaggregate services unit further to account for growing demands like digital infrastructure and cooling, especially in regions experiencing rapid development and urbanization.
Services heating with electricity
Services heating with resistive heater
Services unit
A
B
C
Commodity Key
A = Electricity for services
B = Services heating
C = Services unit activities

## Slide 10: Calibration and key aspects to consider
10
From energy balances to calibration
Energy balances typically report entire fuel use in households/service sector. Therefore, splitting this into heating, cooking etc. requires additional data mining/assumptions
Heating load profiles
For heating, load profiles are a combination the seasonal degree-day profile with the daily use profile. This typically gives a capacity factor of 20-30% for heating systems. In reality though, that should be 4-6% (and maybe twice as high for heat pumps) as they are designed for the coldest hour to ever be recorded and also tend to be oversized. This can be captured by adjusting the Capacity To Activity Unit
Costs in housing vs services
While a number of technologies (mainly heating and cooling) are the same across housing and services, their costs tend to differ. This is because in services, capacities tend to be higher which usually means that the per unit cost is lower
Energy efficiency
Energy efficiency in the form of supply is captured endogenously in a CLEWs++ model through the technoeconomic input of the end-use technologies. Demand side though (stemming mostly from either better insulation or more efficient user behaviour) needs to be analysed exogenously and proxied by reducing the final demand. When there is a cost associated with that (e.g. for insulation), that is usually not captured in the model and needs to be accounted for in result post-processing
Demand growth drivers
All housing related demands should grow with population, but that is not the whole story. As GDP per capita grows, energy consumption tends to also grow. There are limits, nevertheless. For example, demand for heating saturates as it wouldn’t be sensible to increase beyond a certain point. With services, while GDP is the main driver, things are not linear. Econometrics is the optimal way to project demand

## Slide 11: Main technologies and their characteristics – Heating (1/2)
11
Typically (and depending on the gas price) this is the lowest cost option when no emission constraints/price are considered. Its expansion may be limited by gas network availability, which can be considered through model constraints.
Gas boiler
Oil boiler
Coal boiler
Biomass boiler
In the vast majority of cases, this is a less cost-effective option than gas boilers. While vintage stock may be quite large in certain countries, new investments are less common and only an option if gas network is not available.
While fuel price is typically low, capex and maintenance cost are higher, and efficiency is lower than other boilers. Because of a) practical reasons with regards to usability and b) most importantly, indoor pollution, even if the economics favour this technology, it’s typically not selected. Therefore, besides vintage stock, new investments should be prevented in most cases.
Both price cost and actual technology cost tend to be high. When pure economics are considered, this technology is almost never selected. However, there’s a share of the population in many countries that still use that because they have free/low cost biomass available. To capture this, best practice is to force a share into the system.

## Slide 12: Main technologies and their characteristics – Heating (2/2)
12
A technology that can only kick in in a decarbonisation scenario. Heat pumps tend to be a more cost-effective option though, and therefore, the only driver for its uptake is the capped uptake of heat pumps (due to e.g. housing stock not being suitable).
Hydrogen boiler
Resistive heater
Heat pump
District heating
Based on pure economics, this is typically not a competitive option. It still used though by a certain share of the population because of convenience (low capex, zero maintenance cost and easy installation). It’s therefore good practice to force a share into the system. Expansion should be also capped though as the model may use it to balance out the electricity load profile (which is wrong).
This is typically the most cost-effective option in decarbonisation scenarios. In scenarios that consider pure economics, it may kick in in future years if certain conditions apply (i.e. expensive gas/oil and cheap electricity).
While this can be a low-cost option, expansion is typically limited by topological and other factors. On the other hand, it might be cheap in certain areas but not nationwide. For those reasons, it may be good practice to force a capped share into the system.

## Slide 13: Main technologies and their characteristics – Cooking
13
In cooking, the technological variation across different options is lower than that in heating. The two best fuels for cooking are typically:
Gas – When gas price is low, this is the most cost–effective option. Its expansion can be limited by gas network availability.
Electricity - Under certain (rare) conditions it can be cheaper than gas. In decarbonisation scenarios though, it’s typically the cost-optimal option.
Other fuels such as biomass, coal and various petroleum products are typically less favourable due to cost, indoor pollution, high GHG emissions and practical reasons with regards to usability. As long as either electricity and/or gas are available, those fuels are not expected to be selected.

## Slide 14: Practical Exercise
14
You are building the housing sector of a CLEWs++ model for the country of Genovia.
In 2020, Genovia’s energy use for the housing sector was as follows: Gas 15PJ, Oil: 9PJ, Biomass 4PJ and District heat 12PJ. We also know that the following shares of each fuel are used for cooking: Gas 35%, Oil 10% and Biomass 20%. The efficiency of all cooking technologies is 100% while for heating, values are as follows: Gas 90%, Oil 80% and Biomass 70%.
Which OSeMOSYS parameters would you use to ensure that the model represent Genovia’s housing heating sector historical conditions? You may ignore capacity
What value would you assign to these parameters in 2020?
Calibrating the housing heating sector

## Slide 15: Thank you
www.climatecompatiblegrowth.com

## Slide 16: Answers to the Practical Exercise
16
Calibrating the housing heating sector
To represent Genovia’s housing heating sector historical conditions Lower Annual Activity Limit (and equivalently the Upper Annual Activity Limit) should be applied to the heating and cooking technologies represented. Moreover, Specified Annual Demand should be used with an assigned profile.
The values for each activity limit should be calculated as follows:
Fuel use in the housing sector * Share used in heating * Technology Efficiency
The demand should be the sum of the activity of each technology
Activity
Gas: 15*(1-0.35)*0.9 = 8.775PJ
Oil: 9*(1-0.1)*0.8 = 6.48PJ
Biomass: 4*(1-0.2)*0.7 = 2.24PJ
District heat: 12PJ
Demand
8.775+6.48+2.24+12 = 29.495PJ