## Slide 1
CLEWs++ Modelling Course
LECTURE 4
Industry in the CLEWs++ concept

## Slide 2: Learning outcomes
2
Explain how transport is modelled in the CLEWs++ concept
1
2
Go through some key considerations with regards to the main technologies used in industry
3
Differentiate between top-down and bottom-up methods for defining industrial demand

## Slide 3
3
Industrial sector - Introduction
Chart: Final energy consumption worldwide in 2022, by sector
| Industry | Transport | Housing | Commercial and public services | Agriculture, forestry and fishing | Non-energy use | Non-specified
 | 128.29 | 117.33 | 85.63 | 33.72 | 34.04 | 40.68 | 6.58
Source: Statista (2024) - Link
The industrial sector encompasses a wide range of economic activities that transform raw materials into finished goods and intermediate products.

## Slide 4
4
Industrial sector - Subsectors
The following subsectors are typically defined in the final energy balances:
Iron and steel
Chemical and petrochemical
Non-ferrous metals
Non-metallic minerals (Cement etc.)
Mining and quarrying
Construction
Fertilisers
Machinery and Transport equipment
Food, beverages and tobacco
Paper, Pulp and printing
Wood and wood products
Textile and leather

## Slide 5
5
Industrial sector – Subsectors represented in CLEWs++
The following sub-sectors are typically represented explicitly in the CLEWs++ concept, while all others are aggregated under Other Industry. Additional sub-sectors can be included if required.
Iron and steel
Petrochemicals
Cement
Mining and quarrying
Hydrogen-based chemicals
Other industry

## Slide 6
6
Industrial sector – Energy demands
The most common energy demands modelled are:
Process heat
Electricity uses
The industrial sector's energy demands are diverse, reflecting the wide range of processes and activities across different industries. The largest share of energy consumption comes from process heat, which is used in high-temperature applications such as steelmaking, cement production, and chemical manufacturing and some low-temperature process heat applications such as drying and fermentation processes in the other chemicals and other industry sub-sectors.
These processes require temperatures ranging from several hundred to thousands of degrees Celsius, often relying on fossil fuels like coal, natural gas, and oil. Process heat also includes low-temperature applications for steam generation used in various processes.
Energy demands vary significantly between subsectors. For example, the chemical, petrochemical, and fertilisers industry consumes fuels not only for energy but also as a feedstock for producing chemicals and plastics.
Notes: .

## Slide 7
7
Industrial sector - Key drivers and challenges in industrial energy use
Drivers
Economic growth and industrialisation
Population growth and urbanisation
Challenges
Reliance on fossil fuels
Long asset lifecycles
Global supply chains and trade
High costs of emerging solutions
Technological advancement
Barriers in regulation and financing
Note: This list is not exhaustive.

## Slide 8
8
Approaches for modelling the industrial sector – Level of disaggregation
Modeling the industrial sector is a challenging task due to the wide variety of subsectors and processes. A single subsector often encompasses multiple subindustries. Some examples are shown below.
Not all subsectors are active in every country, and not all have the same level of energy consumption.
The energy balance table should be the initial input to determine the advisable level of disaggregation in each case. For subsectors where there is no energy consumption of any fuel, we can immediately discard them unless there are known future plans to develop specific industries in the region.
In the CLEWs++ concept, modelling usually covers up to the level described in the energy balances and nothing more detailed. Additional detail can be added if absolutely necessary as this would lead to increased complexity.
Non-metallic minerals
Cement
Ceramics
Glass
Lime
Bricks
Non-ferrous metals
Copper
Aluminium
Lead and/or Tin
Nickel and/or Cobalt
Zinc and/or Cadmium

## Slide 9
All industrial sectors currently represented in the MDI, with the exception of the cement sub-sector, include an input of high-temperature process heat (HPH). While the specific technology characteristics may differ by sectorfor example, one sector may rely on boilers while another uses furnaces—treating high-temperature process heat in a uniform way across sectors is a reasonable starting point. This does not imply that HPH is not represented at the sectoral level; rather, it means that the same techno-economic assumptions are applied across sectors.
The diagram illustrates the structure used to represent HPH generation within the industry sector under the CLEWs++ framework. It shows multiple energy carriers—biomass, coal, natural gas, oil and hydrogen—being converted into industrial high-temperature heat processes. Coal, natural gas and biomass also include carbon capture and storage (CCS) options. CCS plays an important role in reducing emissions in hard-to-abate sectors such as industry, where fossil fuels may remain necessary to achieve the required high temperatures.
Although multiple processes within a given sector may require high-temperature process heat, these are typically aggregated in the CLEWs++ concept.
High Temperature Process Heat
@Nadya, by X here we mean High temperature process heat for any industrial sector

## Slide 10
Low Temperature Process Heat
Low-temperature process heat (LPH) is typically associated with light industry. In the CLEWs++ concept, this currently includes the Other Chemicals and Other Industry sectors.
Similar to high-temperature process heat, LPH can be supplied using all three fossil fuels, biomass and hydrogen. In addition, industrial heat pumps (using electricity as an input) and the direct use of district heat are also available options. These latter three are low-carbon solutions, and as a result the application of carbon capture and storage (CCS) is less common for LPH.
@Nadya, X_LPH_ELE is industrial heat pumps

## Slide 11
Petrochemical sector
Petrochemicals constitute the largest chemical sub-sector in terms of both production volume and revenue. They include products such as ethylene, propylene and other intermediates used to manufacture plastics and a wide range of final goods. In the CLEWs++ concept, petrochemicals are typically modelled as a single sector.
The sector requires three main inputs: electricity, high-temperature process heat (HPH), and hydrocarbon feedstock. The feedstock can in principle be derived from any of the three fossil fuels; however, oil is by far the most commonly used. The technologies that convert fossil fuels into hydrocarbon feedstock are modelled as dummy technologies, included solely to facilitate system representation.
For technical and process-related reasons, oil is a significantly more suitable feedstock. As a result, while coal and gas may be cheaper, in the CLEWs++ concept they are generally treated as vintage fuels only, with all future investment requirements met using oil-based feedstock.
In the CLEWs++ framework, demand for petrochemicals is proxied through feedstock use, expressed in energy units (e.g. PJ). Energy balances typically report chemical energy and non-energy use together. To calibrate petrochemicals within CLEWs++, feedstock requirements must therefore be defined first. High-temperature process heat demand is then usually derived from feedstock needs using a standard ratio, while electricity demand is more case-specific and requires separate assessment.

## Slide 12
Hydrogen-based chemical sector
Hydrogen-based chemicals are primarily associated with fertiliser production, which is an essential component of most modern economies. In fertiliser manufacturing, hydrogen is typically converted into ammonia and then undergoes further processing.
To limit model detail to what is strictly necessary, the CLEWs++ concept represents this sector using hydrogen feedstock as the sole explicit input. Final demand for hydrogen-based chemicals is therefore proxied directly by hydrogen feedstock demand on a one-to-one basis. The remaining processes involved in fertiliser production (thermal, electrical, etc.) are effectively aggregated within the Other Chemicals sector (see next slide).
This represents the only endogenous demand for hydrogen in the model. In historical periods, hydrogen feedstock is supplied almost exclusively via grey hydrogen production, primarily from natural gas and, in some cases, coal. Under decarbonisation scenarios, this supply is expected to shift towards blue or green hydrogen.
@Nadya, instead of fertilisers, let’s use the term hydrogen-based chemicals.
Diagram needs redoing.
Input is hydrogen (nothing else)
Technology is hydrogen-based chemicals plant
Output is hydrogen-based chemicals

## Slide 13
Other chemicals sector
By Other Chemicals, we refer to all non-petrochemical and non-hydrogen-based chemical activities that are explicitly represented in the model. All energy use reported under the chemicals category in the energy balances that is not allocated to the other chemical sub-sectors is assigned here.
Inputs to this sector are high-temperature process heat (HPH), low-temperature process heat (LPH) and electricity. Fossil fuel use is split between HPH and LPH using user-defined shares, with a default split of 35% LPH and 65% HPH. District heat is assumed to be used entirely for LPH.
Sectoral demand is proxied using the combined use of HPH and LPH. The ratios of electricity, LPH and HPH inputs relative to this demand are then calculated and applied consistently across the entire modelling period (unless the user decides to adjust them).

## Slide 14
Iron & Steel sector
Iron & steel is the most complex industrial sector to model and analyse. In the CLEWs++ concept, it is divided into three main components.
1. Virgin iron and steel production
This component covers the conversion of iron ore to iron and subsequently to steel through integrated production routes. Demand is exogenous in the CLEWs++ framework, and four production routes are represented.
- In historical periods, the Blast Furnace–Basic Oxygen Furnace (BF–BOF) route is the most commonly used. Its main inputs are iron ore (not explicitly represented in CLEWs++), coal and coke. Coke is produced in coke ovens and is used almost exclusively in this sector. Consequently, when calibrating fuel input requirements for BF–BOF, energy use reported under both blast furnaces and coke ovens in the energy balances must be considered.
Output is measured in million tonnes (Mt) of steel and is typically available from statistics. Conversion efficiency is calculated as the ratio of total fuel input to steel output. In addition to combustion emissions, the process generates significant process emissions. Under purely economic scenarios, BF–BOF is often the cost-optimal route for virgin steel production.
- The BF–BOF route can also be combined with carbon capture and storage (CCS) to reduce both combustion and process emissions. This option involves higher capital costs and lower conversion efficiency than conventional BF–BOF.
- Direct Reduced Iron with Electric Arc Furnace (DRI–EAF) represents another full route from iron ore to steel. In some countries, this technology already operates using natural gas, leading to combustion emissions but significantly lower process emissions than BF–BOF.
- Hydrogen-based DRI–EAF is a key decarbonisation pathway for virgin steel production. In many cases, overall system economics favour this option over BF–BOF with CCS.
2. Secondary (recycled) steel production
Secondary steel is produced using Electric Arc Furnaces (EAF), with demand also treated as exogenous. Electricity demand is typically calculated by multiplying output production by a conversion efficiency obtained from the literature. This electricity demand is then deducted from the electricity reported under Iron & Steel in the energy balances, unless a separate figure is already available. In cases where such data exists, the conversion efficiency must be derived directly from reported inputs and outputs.
3. Preparation and finishing of steel products
This category represents downstream processing of steel products. Inputs include high-temperature process heat (HPH), derived from all fuels reported under the sector, and electricity, after deducting EAF requirements.
Demand is represented as a pseudo-flow proxied by the sum of virgin and recycled steel production. The ratios of HPH and electricity inputs relative to this demand are assumed to remain constant throughout the modelling period in the CLEWs++ concept.

## Slide 15
Cement sector
Cement is produced in kilns through the calcination process. In the CLEWs++ concept, all energy use reported under Non-metallic Minerals in the energy balances is initially attributed to cement. If further analysis shows that cement accounts for only a fraction of total non-metallic mineral energy use, only that share is allocated to cement, with the remainder assigned to Other Industry.
Cement production volumes are usually available from national statistics, allowing kiln conversion efficiencies to be calculated directly. If production data is unavailable, standard conversion efficiency values from the literature can be used to estimate output. Cement production also results in significant process emissions.
Cement kilns are among the most fuel-flexible industrial technologies. Most countries use a mix of fuels reflecting local economic conditions. Under purely economic assumptions, either coal or natural gas is typically the least-cost option, depending on the region. In decarbonisation scenarios, kilns may operate with carbon capture and storage (CCS) when using biomass, coal or gas, while hydrogen represents an alternative with zero combustion emissions. Any of these options may become dominant depending on system conditions.
Biomass with CCS, although more expensive in fuel terms, can deliver negative emissions, which are often valuable in deep decarbonisation pathways. For coal and gas, incomplete CO₂ capture means that even if coal is cheaper, a sufficiently high carbon price may favour gas. Hydrogen-based kilns still incur process emissions, and their competitiveness therefore depends on multiple interacting factors.
In the CLEWs++ framework, cement plants are represented using a dummy technology to capture electricity demand in the sector. Electricity use is defined based on energy balance data, and the ratio of electricity input to cement production is typically assumed to remain constant over the modelling period.
@Nadya, with the 2nd graph, pls ignore PLANT 2. There’s only one cement plant where inputs are cement and electricity and output is final cement products. Also, in the first diagram pls ignore biofuel kilns (the top technology)

## Slide 16
Mining sector
The mining sector covers the extraction of metals and other products from the ground. It relies on three main inputs: electricity (for ventilation, lighting, control systems, etc.), motive power for activities such as grinding and excavation, and low-temperature process heat (LPH), for example for drying ore concentrates.
In the CLEWs++ concept, motive power can typically be supplied by liquid fuels (petroleum products, biofuels or synthetic fuels) or by electricity.
Sectoral production is proxied through exogenous electricity demand. The corresponding ratios of motive power and LPH relative to this demand are calculated accordingly and are usually assumed to remain constant throughout the modelling period.
@Nadya, the 2nd input should be LPH, not HPH

## Slide 17
Other industry sector
Other Industry includes any industrial activities present in a country or region that are not explicitly modelled elsewhere and typically represents lighter industry in terms of energy intensity.
Energy inputs to this sector include high-temperature process heat (HPH), low-temperature process heat (LPH) and electricity. All fossil fuel use is split between HPH and LPH using user-defined shares, with a default split of 50% LPH and 50% HPH, while all district heat is assumed to supply LPH.
Sectoral demand is proxied through the combined use of HPH and LPH. The ratios of electricity, LPH and HPH inputs relative to this demand are typically assumed to remain constant throughout the modelling period.

## Slide 18: Key consideration in the power sector
18
Most industrial sectors tend to operate continuously with very high utilisation rates. While accurate data is often difficult to obtain, in the absence of better information it is reasonable to assume a flat operating profile (i.e. identical to the Year Split, corresponding to a 100% utilisation rate).
Industrial process emissions are critical to represent, as without them it is not possible to achieve full greenhouse gas emissions coverage. These emissions can be calculated using a top-down approach, if total sectoral emissions and production volumes are known, or a bottom-up approach using standard emission intensities where total emissions data is unavailable.
While motive power is an indispensable part of the industrial sector, it is in most cases not modelled separately, as it has largely been electrified and is therefore included within exogenous electricity demand. The mining sector is a notable exception.
Industrial demands can be calculated using a top-down approach when actual output is known but energy use is unknown, or a bottom-up approach when energy use is known but output is unknown. When both output and energy use are available, conversion efficiencies can be calculated directly. In such cases, calculated efficiencies must be sense-checked against values reported in the literature. If they fall outside reasonable ranges, this may unintentionally advantage or disadvantage competing future technologies whose efficiencies are taken directly from literature sources.
The plant technology shown in the previous slides is not strictly necessary; it is a dummy technology introduced to facilitate model functionality. Its main advantage is that it allows a single final demand to be defined, with fixed ratios used to represent all other inputs. In this way, any change in demand projections automatically drives all associated inputs. Without the plant technology, separate final demands would need to be defined for each input, increasing complexity and maintenance effort.
DEMAND PROFILE
PROCESS EMISSIONS
PLANT TECHNOLOGY
BOTTOM-UP VS TOP-DOWN DEMAND
MOTIVE POWER

## Slide 19: Practical Exercise
19
You are building the industrial sector of a CLEWs++ model for the country of Genovia.
The cement sector is required to decarbonise, and two technology options are available: coal-fired kilns with CCS and gas-fired kilns with CCS. Both technologies have a CO₂ capture rate of 90%, and all other techno-economic parameters are assumed to be identical. The cost of coal is 2.3 MUSD/PJ, while the cost of natural gas is 6.4 MUSD/PJ. The emission intensities are 0.092 Mt CO₂/PJ for coal and 0.056 Mt CO₂/PJ for natural gas, respectively.
You are asked to understand under what conditions gas-fired kilns will become more competitive than coal-fired kilns.
How can these conditions be implemented in the model?
Assessing technology choice in the cement sector under decarbonisation conditions

## Slide 20: Thank you
www.climatecompatiblegrowth.com

## Slide 21: Answers to the Practical Exercise
21
Assessing technology choice in the cement sector under decarbonisation conditions
Given that all other techno-economic parameters are identical, the factor that determines whether gas-fired kilns are more competitive than coal-fired kilns is the compound fuel price, defined as the sum of the actual fuel price and the carbon cost. Since the actual fuel prices are fixed, the determining variable is the carbon price. Gas-fired kilns become competitive when:
𝑃gas+(𝐸gas×C×(1−𝐶𝑅))×𝐶 ≤ 𝑃coal+(𝐸coal×C×(1−𝐶𝑅))×𝐶Pgas
Where:
P = fuel price (MUSD/PJ)
E = emission intensity (Mt CO₂/PJ)
CR = CO₂ capture rate (here 90%)
C = carbon price (MUSD/Mt CO₂)
6.4+(0.056*C*(1-0.9) ≤2.3+(0.092*C*(1-0.9)
C≥1138.9
B. This carbon price can be set up either explicitly using the Emissions Penalty parameter or implicitly by setting up an Annual Emission Limit or a Model Period Emission Limit.