## Slide 1
CLEWs++ Modelling Course
LECTURE 5
Transport in the CLEWs++ concept

## Slide 2: Learning outcomes
2
Understand how transport is modelled in the CLEWs++ concept
1
2
Go through some key considerations with regards to the main technologies used in transport

## Slide 3
3
6.2 Basic concepts on transport modelling
Road
Rail
Air
Cars
2/3 wheelers
Buses
Trucks (of various sizes)
Trains
Ships
Airplanes
Maritime
Notes: Transport demand can be classified by mode of transportation, including cars, motorcycles, buses, trucks, and others. These categories can be further refined based on data resolution; for instance, cars may be subdivided into compact cars, full-size cars, SUVs, minivans, and pickups. Additionally, passenger transport can be categorized as either private or public, depending on the mode of travel—for example, cars represent private transport, while buses are part of public transport.
Where data is available, demand can also be disaggregated by travel distance, distinguishing between urban and intercity transport.
It is also essential to differentiate between modes of transport that serve both passenger and freight demands. For example, there may be separate demands for trains transporting passengers and trains carrying freight. In some cases, such as airplanes, both passenger and freight demands can be met simultaneously within the same flight. In the full-scale CLEWs thesis we will look at cars, 2/3 wheelers (i.e. motorcycles, tuk tuks etc.), buses, vans, heavy trucks, light trucks, passenger railway, freight railway, shipping, and aviation.

## Slide 4
Structure in CLEWs Model – 2/3 wheelers
Two- and three-wheelers play a critical role in the transport systems of many low- and middle-income countries, where they often serve as the primary mode of motorized mobility for both passengers and small-scale freight.
The diagram shows how the CLEWs++ model represents different fuel types—electricity, liquid fuel, and natural gas—used by 2/3 wheelers to meet the demand for 2/3 wheelers.
These vehicles are especially prevalent in dense urban areas due to their affordability, manoeuvrability, and low operating costs. Their high share in the vehicle fleet makes them a key target for transport electrification and fuel-efficiency policies.
Properly modelling their energy demand and emissions impact is essential for planning clean mobility transitions in rapidly urbanizing regions.
2/3 wheelers using electricity
2/3 wheelers using liquid fuel
2/3 wheelers using natural gas
A
B
C
D
Commodity Key
A = Transport electricity
B = Liquid fuel
C = Natural gas
D = 2/3 wheelers activity (vehicle-kilometres)

## Slide 5
Structure in CLEWs Model - Cars
Cars are one of the most widely used modes of transport globally, with ownership steadily rising in low- and middle-income countries as incomes grow, infrastructure improves, and urbanization accelerates. The CLEWs++ model captures this evolution through multiple car technology pathways—electric, hydrogen, liquid fuel, natural gas, and plug-in hybrids—each contributing to overall car transport demand.
Plug-in hybrid electric vehicles (PHEVs) combine an internal combustion engine with a rechargeable battery, allowing them to operate on electricity for short distances and switch to fuel when needed, hence the input of both electricity and liquid fuels in the diagram above. This dual capability reduces fuel consumption and emissions compared to conventional vehicles while offering flexibility in areas with limited charging infrastructure.
As many developing countries experience a shift from public or informal transport to private car ownership, understanding the energy implications becomes increasingly important. Modelling these pathways helps assess the potential impacts of different policy choices—such as fuel taxation, electrification incentives, or urban planning—on emissions, energy demand, and sustainable mobility outcomes.
Cars using electricity
Cars using hydrogen
Cars using liquid fuel
Cars using natural gas
Cars using plug-in hybrids
A
B
C
D
A
E
Commodity Key
A = Transport electricity
B = Hydrogen
C = Liquid fuel
D = Natural gas
E = Car activity (vehicle-kilometres)
C

## Slide 6
Structure in CLEWs Model - Buses
Buses are a central component of public transport systems and are vital for moving large volumes of passengers efficiently, especially in urban and interurban settings. In the CLEWs++ model, buses are represented with multiple fuel pathways—electric, hydrogen, liquid fuels, natural gas, and plug-in hybrid electric buses to meet the demand for bus mobility.
Modelling the transition from diesel-dominated fleets toward cleaner alternatives like electric or hydrogen buses helps inform sustainable transport strategies and investment planning for expanding, modernizing, and greening public transport systems.
Buses using electricity
Buses using hydrogen
Buses using liquid fuel
Buses using natural gas
Buses using plug-in hybrids
A
B
C
D
A
E
Commodity Key
A = Transport electricity
B = Hydrogen
C = Liquid fuel
D = Natural gas
E = Bus activity (vehicle-kilometres)
C

## Slide 7
Structure in CLEWs Model – Heavy trucks
Heavy trucks are a critical component of freight transport systems, responsible for moving large volumes of goods over long distances and forming the backbone of logistics and supply chains worldwide. In the CLEWs++ model, heavy trucks are represented by multiple technology pathways—including electric, hydrogen, liquid fuels, natural gas, and plug-in hybrid electric trucks—all contributing to the heavy truck demand.
While diesel-powered trucks currently dominate the sector, alternative fuels are gaining traction due to growing pressure to reduce greenhouse gas emissions and improve urban air quality. Modelling these diverse pathways enables the evaluation of future technology transitions, fuel demand, and infrastructure needs for decarbonizing freight transport, especially as demand continues to rise in both industrialized and developing regions.
Heavy trucks using electricity
Heavy trucks using hydrogen
Heavy trucks using liquid fuel
Heavy trucks using natural gas
Heavy trucks using plug-in hybrids
A
B
C
D
A
E
Commodity Key
A = Transport electricity
B = Hydrogen
C = Liquid fuel
D = Natural gas
E = Heavy truck activity (vehicle-kilometres)
C

## Slide 8
Structure in CLEWs Model – Light trucks
Light trucks are widely used for local freight delivery, small business operations, and short- to medium-distance goods transport, especially in urban and peri-urban areas. In the CLEWs++ model, light trucks are represented across a range of fuel and technology options—including electric, hydrogen, liquid fuels, natural gas, and plug-in hybrids—all contributing to light truck demand.
As urban freight demand grows alongside e-commerce and population density, light trucks have become increasingly important in shaping energy use and emissions in cities.
Electrification of this segment offers strong potential for reducing local air pollution and fuel costs due to frequent stop-start driving cycles and shorter daily ranges. By modelling these pathways, the framework supports analysis of energy transitions and policy impacts for last-mile delivery and other light-duty freight services.
Light trucks using electricity
Light trucks using hydrogen
Light trucks using liquid fuel
Light trucks using natural gas
Light trucks using plug-in hybrids
A
B
C
D
A
E
Commodity Key
A = Transport electricity
B = Hydrogen
C = Liquid fuel
D = Natural gas
E = Light truck activity (vehicle-kilometres)
C

## Slide 9
Structure in CLEWs Model - Vans
Vans are a versatile transport mode, widely used for both passenger and light cargo transport, particularly in urban and peri-urban areas. In the CLEWs++ model, vans are represented through a variety of fuel and technology options—electric, hydrogen, liquid fuels, natural gas, and plug-in hybrids— all contributing towards the total van demand.
Vans serve a diverse range of purposes, from small business operations and ride-sharing services to institutional or municipal use. As cities push toward cleaner transport systems, the electrification of vans is gaining momentum, offering benefits such as lower operating costs, reduced urban air pollution, and compatibility with low-emission zones. Modelling these different pathways helps assess the potential impacts of vehicle technology shifts and informs policy planning for sustainable and flexible urban mobility.
Vans using electricity
Vans using hydrogen
Vans using liquid fuel
Vans using natural gas
Vans using plug-in hybrids
A
B
C
D
A
E
Commodity Key
A = Transport electricity
B = Hydrogen
C = Liquid fuel
D = Natural gas
E = Van activity (vehicle-kilometres)
C

## Slide 10
Structure in CLEWs Model - Railway
Railway networks often serve as essential infrastructure for both moving goods and enabling affordable public mobility. In the CLEWs++ model, railway transport is divided into two separate components: freight rail and passenger rail, each represented by distinct technology options. Freight railway includes electric, hydrogen, and liquid fuel technologies to meet the freight railway demand.
Passenger railway follows a similar structure with electric, hydrogen, and liquid fuel options to meet the passenger railway demand. Separating freight and passenger railway can be particularly useful when looking at decarbonisation strategies since passenger railway systems tend to electrify prior to freight railway.
The efficiencies, costs, and demands for both types of railways can also largely differ depending on the country. Capturing these dynamics in a CLEWs++ model allows for a better understanding of how rail transport interacts with national energy systems, fuel supply chains, and emissions, supporting more integrated and sustainable development planning.
Freight rail using electricity
Freight rail using hydrogen
Freight rail using liquid fuel
A
B
C
D
Passenger rail using electricity
Passenger rail using hydrogen
Passenger rail using liquid fuel
A
B
C
E
Commodity Key
A = Transport electricity
B = Hydrogen
C = Liquid fuel
D = Freight rail activity (vehicle-kilometres)
E = Passenger rail activity (vehicle-kilometres)

## Slide 11
Structure in CLEWs Model - Shipping
Shipping is a vital mode of passenger and freight transport, especially for international trade and coastal logistics, and plays a key role in the economic development of many low- and middle-income countries with growing import-export activity. In the CLEWs++ model, shipping is represented through two technology options: conventional-liquid fuels and ammonia-based fuels, which are gaining attention as a potential low-carbon alternative.
Both technologies contribute to the shipping demand. Modelling these options is crucial for understanding future energy demand and emissions from maritime transport, particularly as global regulations tighten on ship emissions and countries explore cleaner maritime strategies. This approach enables integrated planning of marine fuel supply chains and supports the evaluation of decarbonization pathways within national and regional development contexts.
Transport shipping using ammonia
Transport shipping using liquid fuel
A
B
C
Commodity Key
A = Ammonia
B = Liquid fuel
C = Shipping activity (vehicle-kilometres)

## Slide 12
Structure in CLEWs Model - Aviation
Aviation is a critical mode of long-distance passenger transport and a growing contributor to global emissions. In the CLEWs++ model, aviation is currently represented by a single technology pathway: liquid-fuel-powered aircraft, with output measured in passenger-kilometres by air.
The fuel input is modelled as a blend of oil-derived fuels, biofuels, and synthetic fuels. While jet-fuel oil continues to dominate aviation fuel use today, there is growing interest in decarbonization strategies that promote the uptake of sustainable aviation fuels (SAFs), such as advanced biofuels and synthetic (e-fuel) alternatives. These fuels have the potential to significantly reduce lifecycle emissions, but remain limited by high costs, supply constraints, and limited infrastructure.
By incorporating a flexible fuel blend in the model, future scenarios can explore how policy and technological advancements might shift the aviation sector toward lower-carbon fuels over time.
Aviation using liquid fuel
A
B
Commodity Key
A = Liquid fuel
B = Aviation activity (vehicle-kilometres)

## Slide 13: Main technologies in road transport and their characteristics (1/2)
13
Internal Combustion Engines (ICE)
This is the most established technology and the one still expected to dominate based on pure economics, up until the 2030s-2040s (depending on a few factors). While petroleum products (e.g. diesel/gasoline) are the most common ones, other fuels can be used:
Biofuels: while popular in certain parts of the world, they make economic sense only under decarbonisation conditions. Due to biomass availability limitations and other alternatives in road transport such s electric, a CLEWs++ model would usually allocate biomass elsewhere.
Hydrogen: this fuel can also make economic sense in decarbonisation scenarios. The most widely expected way to use hydrogen in transport though, is via fuel cells as opposed to ICEs. Therefore, this technology tends to be neglected in a CLEWs++ model.
Natural gas: an already competitive fuel in certain areas. It requires, however, modifications to the default setup of the vehicle. Moreover, not all re-fuelling stations provide natural gas. Therefore, capturing its uptake (which is not expected to be significant anyway) becomes a challenge. For this reason, a typical CLEWs++ model would only consider the vintage fleet of natural gas vehicles.
Synfuels: synthetic fuels are very expensive and only kick in in a decarbonisation scenario. Their presence in road transport is extremely rare and can only occur under certain conditions (i.e. lack of biofuels, expensive electricity and cheap gas which can be converted into blue hydrogen and then into synfuels).
Mild hybrids: unlike plug-in hybrids, mild hybrids only use diesel/petrol as an input and the electricity is generated within the technology. Therefore, modelling mild hybrids separately is not different from modelling high-efficiency ICE vehicles. Typically, models of this kind are not ideal for comparing various technology options with the same input fuel but varying levels of efficiency and thus, in a CLEWs++ model this is typically avoided.

## Slide 14: Main technologies in road transport and their characteristics (2/2)
14
Electric
Electric vehicles (EVs) are the most prominent, future technology. While decarbonisation incentives (explicit or implicit) can help boost their uptake, they are expected to dominate new sales anyway in the 2030s-2040s, depending on the region. Electric-vehicle charging stations (EVCIs) availability can be a limiting factor. While the load profile doesn’t matter when it comes to vehicles doesn’t matter (as they store the fuel), with EVs it has system-wide implications (because of the charging). Therefore, in a CLEWs++ model, the user has to specify a profile for road transport demand.
Hydrogen (fuel cell)
The fuel cell is a promising technology under decarbonisation conditions. It broadly favours larger vehicles such as busses and trucks. Therefore, it’s rarer to kick in in e.g. cars as opposed to trucks. Even with larger vehicles though, if electricity is cheap and annual mileage is relatively high, electric vehicles may still get the edge.
Plug-in hybrid
This type of vehicle uses both an ICE and a battery-powered, electric motor. While it can help lower emissions, it cannot contribute to the complete decarbonisation of the sector. Moreover, relying on two input fuels makes its accurate simulation more complicated. Given the complexity in combination with the less significant system benefits, in a typical CLEWs++ model, only the vintage fleet is considered.

## Slide 15: Practical Exercise
15
You are building the transport sector of a CLEWs++ model for the country of Genovia.
In 2020, Genovia’s energy use for the road transport sector was as follows: Petroleum products 8PJ, and Biofuels 2PJ. We also know that the following shares of each fuel are used for cars: Petroleum products 70% and Biofuels 90%. Finally, in Genovia that year there were 13,700,000 registered, internal combustion engine cars that covered a total distance of 820 billion-vkm.
Calculate the efficiency of internal combustion engine cars in 2020. Which parameter(s) would you use to express it?
Calculate the capacity to activity unit of internal combustion engine cars in 2020
Calibrating the housing heating sector

## Slide 16: Thank you
www.climatecompatiblegrowth.com

## Slide 17: Answers to the Practical Exercise
17
Calibrating the road transport sector
To calculate the efficiency of internal combustion engine cars in 2020, the total fuel use needs to be divided by the activity. The total fuel use is as follows:
8PJ*0.7+2*0.9 = 7.4PJ
Efficiency = 7.4PJ/820billion-vkm = 0.009PJ/820 billion-vkm
To express this in the model, the Input Activity Ratio should be 0.009 while the Output Activity Ratio should be 1
Capacity to Activity Unit = 820/13.7 = 59.9 billion-vkm/million cars