## Slide 1
CLEWs++ Modelling Course
LECTURE 8
Agriculture

## Slide 2: Learning outcomes
2
Assessing which crops to represent in your CLEWs model
1
2
Structuring and Representing Crops in your CLEWs Model
3
Calibrating Crop Yields
4
Implementing Techno-Economic Crop Data

## Slide 3: Why Agriculture is Unique:
High Variability & Complexity:
Multiple crop types with distinct characteristics
Different management intensities (irrigated/rainfed, high/low input)
Seasonal patterns and rotation cycles
Diverse productivity levels and resource requirements
Critical Nexus Interactions:
Water: Largest consumer of freshwater resources (irrigation, rainfall)
Energy: Significant user of fuels (machinery, pumping) and fertilisers
Food Security: Direct link to nutrition and livelihoods
Climate: Major source of emissions (fertilizers, machinery) and potential carbon sink
Policy Sensitivity:
Agriculture is heavily influenced by, and responsive to, policy interventions:
Subsidies and price supports
Irrigation infrastructure investments
Technology adoption programs
Trade policies and market access
Economic Significance:
In many developing countries, agriculture accounts for:
20-40% of GDP
50-70% of employment
Majority of rural livelihoods
Agricultural land represents the most dynamic and policy-relevant component of the land system

## Slide 4
Key Challenge: Balancing model complexity with comprehensive coverage
The Problem:
Too many crops → Overly complex, unmanageable model
Too few crops → Incomplete picture of agricultural land use
Example Scenarios:
If 2 crops = 50% coverage → Insufficient detail
If 2 crops = 90% coverage (remaining 10% highly fragmented) → Potentially adequate
Bottom Line: Need a systematic threshold method for crop selection
1. Determining Crop Inclusion in CLEWs Models

## Slide 5: Three Selection Approaches
1. Percentage-Based Threshold
Include crops accounting for X% of total harvested area (e.g., 80%)
✓ Captures majority of land use
✗ May require excessive detail in diverse agricultural systems
2. Fixed Number Threshold
Include top N crops (e.g., top 5 or 10)
✓ Simple and uniform across countries
✗ May miss important crops in diverse agricultural profiles
3. Hybrid Approach Recommended
Combine both methods for optimal balance
Example: Top 5 crops PLUS additional crops until 80% threshold reached
Crop selection also driven by the purpose of your model

## Slide 6: Beyond Land Area: Ensuring Economic Relevance
Critical Consideration: Land area alone doesn't tell the whole story
High-value crops may occupy small land areas but be critical to:
  National economy and GDP
  Export revenues
  Food security
  Employment and livelihoods
Real-World Example: A specialty crop like saffron, coffee, or cocoa might represent:
<5% of harvested area
BUT 20%+ of agricultural export value
Recommendation for Crop Selection: When applying the three approaches, cross-reference with:
Economic value metrics (GDP contribution, export value)
Strategic importance (food security, employment)
Policy priorities (government agricultural strategies)
Crop selection also driven by the purpose of your model

## Slide 7: Determining Crop Inclusion in CLEWs Models
Complete Hands-on 7a to learn this skill

## Slide 8: 2. Crop Representation in CLEWs Models
Each Selected Crop Modelled in Four Categories:
Water Source:
Irrigated - Uses irrigation systems
Rainfed - Relies on natural precipitation
Input Intensity:
High Input - Modern inputs (fertilizers, pesticides, machinery, improved seeds)
Low Input - Traditional/subsistence farming with minimal external inputs
Why This Matters:
Different water requirements and availability
Different yield potentials
Different costs and resource needs
Different climate vulnerability profiles
LAND
↓
├── AGRICULTURAL LAND
│ ↓
│ └── CROPLAND
│ ↓
│ ├── CROP 01 (irrigated, high input)
│ ├── CROP 01 (rainfed, high input)
│ ├── CROP 01 (irrigated, low input)
│ ├── CROP 01 (rainfed, low input)
│ │
│ ├── CROP 02 (irrigated, high input)
│ ├── CROP 02 (rainfed, high input)
│ └── ... [pattern repeats for all crops]
│
├── FOREST
├── BUILT-UP LAND
└── OTHER LAND

## Slide 9: Why Four Categories? Balancing Detail and Practicality
Not Too Simple:
A single representation per crop would mask critical differences in:
  Water resource requirements and constraints
  Productivity and yield variations
  Climate vulnerability and adaptation strategies
  Investment and cost structures
Not Too Complex:
Further disaggregation (e.g., by soil type, slope, farm size, specific crop varieties) would:
  Exponentially increase data requirements
  Create model complexity that's difficult to calibrate and validate
  Produce outputs that are harder to interpret for policy decisions
  Require granular data often unavailable in many countries
The "Sweet Spot": This four-way classification captures the most policy-relevant distinctions while remaining:
Manageable in terms of data collection
Computationally feasible
Aligned with available agricultural statistics (FAO, national agencies)
Actionable for decision-makers

## Slide 10
Inputs
Outputs
Resource Requirements per hectare:
Land: Cropland area allocated
Water: Irrigation water and precipitation
Energy: Diesel and gasoline for machinery/pumping
Products & Environmental Flows per hectare:
Primary Product: Crop yield (e.g., sugarcane)
Water Flows: Evapotranspiration, surface runoff, groundwater recharge
Land Use: Occupied agricultural land
Each of the 4 crop categories (irrigated/rainfed × high/low input) has unique input-output coefficients reflecting different farming practices and yields.

## Slide 11: Naming Conventions

## Slide 12: 3. Crop Calibration: harvested area
The problem: it is not always possible (e.g due to a lack of data available) to know how much harvested area we should allocate for each crop and farming type.
In order to have a consistency between the model and the reality, it is important that the total harvested area corresponds to the total national harvested area, respecting the land-use constraints.
This has to be done for the reference year to ensure consistency – how?

## Slide 13: 3. Crop Calibration: Yield
Once you know how much harvested area to allocate for each crop-type, it is important to calibrate the crop-yiel.
In literature or national reports, it is possible to find theoretical data. However, they can differ from real data depending on the assumptions/conditions used for calulating them.
Same as for the harvested area, it is important that the total production is consistent with national statistics. A mismatch, could cause problems in land-covers (e.g if the yield is lower, than in the reference year we need to allocate more land for increasing the crop production).
How do we do that?

## Slide 14: 3. Crop Calibration: Hands on exercise
1 – Go on Zenodo and download the Land calibration tool
2 – Read the instructions
3 - Add the crops in the ”User Setting” with the following data
You have to calibrate the harvested area and the crop yield for 3 regions in your country and two main crops: cereals and maize. The rest of the harvested area will be considered as ”other” crops
Number | Name
Crop 1 | Cereals
Crop 2 | Maize
 | Value in Hectares (ha)
Total irrigated area | 50000
Harvested area (total) | 
 | Value in Hectares (ha)
Total harvested area | 200000
Crop 1 | 50000
Crop 2 | 120000
Crop 3 | 0
Crop 4 | 0
Crop 5 | 0
Crop 6 | 0
Other crops | 30000

## Slide 15: 3. Crop Calibration: Hands on exercise
1 – Go on Zenodo and download the Land calibration tool
2 – Read the instructions
3 - Add the crops in the ”User Setting” with the following data
You have to calibrate the harvested area and the crop yield for 3 regions in your country and two main crops: cereals and maize. The rest of the harvested area will be considered as ”other” crops
Share of harvested area | 
Name | Share (%)
Area 1 | 30.0%
Area 2 | 60.0%
Area 3 | 10.0%
Area 4 | 0.0%
Production | 
Annual Production for the reference year | Value in Mton
Crop 1 | 1
Crop 2 | 3
Crop 3 | 0
Crop 4 | 0
Crop 5 | 0
Crop 6 | 0
Other crops | 0.5

## Slide 16: 3. Crop Calibration: Hands on exercise
1 – Go on Zenodo and download the Land calibration tool
2 – Read the instructions
3 - Add the crops in the ”User Setting” with the following data
You have to calibrate the harvested area and the crop yield for 3 regions in your country and two main crops: cereals and maize. The rest of the harvested area will be considered as ”other” crops
Area 1 |  |  |  | Area 2 |  |  |  | Area 3 |  |  | 
LR1 | HR1 | LI1 | HI1 | LR2 | HR2 | LI2 | HI2 | LR3 | HR3 | LI3 | HI3
YIELD | YIELD | YIELD | YIELD | YIELD | YIELD | YIELD | YIELD | YIELD | YIELD | YIELD | YIELD
0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1 | 1.2 | 1.3 | 1.4
0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5
Average Other crops |  | 
Area 1 | Area 2 | Area 3
0.1 | 0.2 | 0.3

## Slide 17: 4. Adding Techno-Economic Data
Residual capacity
Costs (hands on activity)
Crop imports?

## Slide 18: Thank you
www.climatecompatiblegrowth.com