## Slide 1
CLEWs++ Modelling Course
LECTURE 9 Water

## Slide 2: Learning outcomes
1
2
2
Learn how to pre-process water system’s data.
3
Be able to represent seasonal variability and crop growing stages.
4
Use the principles learnt to design and model the water sector and the implications of and on the CLEWs++ concept.
Know how to represent the water system and its interlinkages in the CLEWs++ concept.
5
Be able to interpret final results.

## Slide 3: The water system - recap
3
Photo Source: Igor Shiklamonov, 1993, "Water in Crisis: A Guide to the World's Freshwater Resources"
Where is the water?
97% in the oceans (salt water).
The majority of the fresh water is stored in glaciers and ice caps.
Other sources of fresh water: surface and groundwater.
Notes: General overview and recap from CLEWs (theoretical) – recap from the open learn course CLEWs

## Slide 4: The water system - recap
4
Photo Source: ”The Water Cycle” by AIRS is licensed under CC BY 2.0.
The water cycle is the continuous movement of water through evaporation, condensation, precipitation, and runoff. It involves the processes of water turning into vapor, forming clouds, falling as rain or snow, and returning to bodies of water, ultimately sustaining ecosystems and regulating climate.
For the purposes of CLEWs analysis we focus on the processes of:
Precipitation
Evapotranspiration
Runoff
Ground water infiltration
Water balance
Precipitation (P)
Evapotranspiration (Et)
Run-off (R)
Groundwater recharge (GWT)
P = ET + R + GWT
Notes: General overview and recap from CLEWs (theoretical) – recap from the open learn course CLEWs

## Slide 5: Representing the water sector in CLEWs - recap
5
The sum of the water balance outputs must be equal to the input (for the technologies that do not have additional water input, e.g., irrigation).
Interlinkages and demand
The water balance
Surface run-off (WTRSUR)
Water - land
Water - energy
Water –public demand
P + (IW) = ET + R + GWT
Notes: Recap from CLEWs (modelling part)

## Slide 6: The water reference system - recap
6

## Slide 7: The importance of data gathering and pre-processing the data: water interlinkages and techno-economic data
7
What type of data do you need?
Power sector: - Water for cooling power plants
Demand: - Municipal - Industrial
Costs: - Capital, variable and fixed costs for the water system infrastructure
Water balance: - Precipitation - Evapotranspiration - Groundwater recharge - Surface Water run-off - Water for Irrigation
Data gathering and data pre-processing are essential for building your CLEWs model

## Slide 8: The importance of data gathering and pre-processing the data: Power sector and demand
8
Model input
Unit
Suggested references
Reference 1 Reference 2
AQUASTAT

## Slide 9: The importance of data gathering and pre-processing the data: Water balance
9
P + (IW) = ET + R + GWT
Groundwater recharge (GWR)
Sugarcane plantation
Land resource
/ cultivated area
Sugar
/ cultivated area
Precipitation (P)
Runoff (R)
Evapotranspiration (ET)
/ cultivated area
/ cultivated area
/ cultivated area
/ cultivated area
Irrigation water (IW)
/ cultivated area
Notes: The problem: correlation and casual effect (to be explored more in the scenario section)
The water balance : how to do it  maybe hands on example

## Slide 10: The importance of data gathering and pre-processing the data: Water balance
10
The problem: in CLEWs models there is no causual-effect between water input and output.
The water balance has to be done before inputting the data in your CLEWs model.
In literature, it is often possible to find the share of groundwater percolation and plant evapotranspiration. The difference between the input and the output is the run off water.
Typical values are: - Evapotranspiration: 40-50% of the input - Groundwater percolation: 1-2% of the input
P + (IW) = ET + R + GWT
Be careful: these values vary depending on land-cover type, crop-type, country and region (depending on the soil characteristics.)
Notes: The problem: correlation and casual effect (to be explored more in the scenario section)
The water balance : how to do it  maybe hands on example

## Slide 11: The importance of data gathering and pre-processing the data: Water balance - methods
11
Input activity ratio – Precipitation
Find the average annual precipitation in volume (Bm3)
Divide the value by the total land in 1000sq.Km
Find the Bm3/1000sq.Km
2
Output activity ratio – Evapotranspiration
For each land-cover type (Lecture 07), and for each crop-type (Lecture 08), find how much is the evapotranspiration in volume or as share of the input.
P + (IW) = ET + R + GWT
Input activity ratio – Irrigation (only for irrigated crops)
Output activity ratio –Groundwater
For each land-cover type and for each crop-type find how much is the water percolation (usually expressed as a share of precipitation).
Output activity ratio – Run-off
Calculate it as the difference of the other values you have found to close the balance:
R = P + (IW) – ET - GWT
1
3
4
5
Remember to be always consistent with the unit of measures!
Notes: The problem: correlation and casual effect (to be explored more in the scenario section)
The water balance : how to do it  maybe hands on example

## Slide 12: Hands-on Exercise
12
You are building the water balance for your CLEWs model.
Start from your CLEWs model and try to look at some data for precipitation, evapotranspiration and groundwater recharge. You can try to ask also ChatGpt and get some preliminary data. Then, on a separate Excel sheet, try to do the balance on your own and find the remining variable for the balance: the run-off water. Remember to always check if the balance is respected (input = output).
1
How much do the results differ across land-cover types?
Is there any difference across crop-types?
Which land-cover type is the one with the highest evapotranspiration?
Reflect on these questions:

## Slide 13: Modelling seasonal varibility and crop-growing stages
13
The problem: in CLEWs models there is no causual-effect between water input and output
What if I want to represent a drier season?
What if in the future the precipitations will increase/decrease?
What if the crops are forecasted to require more/less water?
What if there is a variation in evapotranspiration?
Photo Source: ”Observed seasonal cycle” by Climate Change Knowledge Portal
Notes: The problem (put some examples)
Interactive question (e.g reflection if it is a good idea to work with capacity factors with technologies etc.
Go back to pre-processing

## Slide 14: Modelling seasonal varibility and crop-growing stages Aim and objectives
14
Types of vegetation:
Regenerates naturally ( forest, grassland, water bodies)
Does not regenerate naturally (cropland)
Water requirements can be simplified with yearly averages.
Water requirements have intra-annual variability
Photo Source: ”Crop coefficient curve” taken from FAO – Irrigation and Drainage paper 56.
Kc - crop coefficient
Determines crop-specific evapotranspiration.
Directly proportional to crops’ water requirements.
Crop water requirements can be three times more if we are in the growing stage (Mid-season) than the harvested phase (Late-season).
What if during the growing stage there is a lack of renewable available water?

## Slide 15: Modelling seasonal varibility and crop-growing stages Methods
15
Define the seasons
Season 1 = growing
Season 2 = Harvesting
The seasons have to be taken into account when modelling the time-slices of your CLEWs model (!)
1
2
Create one ”dummy” technology for each season
3
Create one ”dummy” commodity for each season
S1
S2
Notes: We decided to divide the overall growing curve into two main phases: growing and harvesting stage (respectively mid and late season). For each season we then created a new dummy technology, called Season 1 and Season 2

## Slide 16: Modelling seasonal varibility and crop-growing stages Methods
16
Increase the modes of operation for each modelled season.
4
5
Output activity ratio
S1 and S2 for both dummy technologies
6
Input activity ratio
S1 and S2 for all crop land
Each mode of operation (MoO) is associated to a season. If MoO 1 refers to Season 1 and MoO 2 to Season 2, this set-up has to be consistent for modelling all the water cycle.
7
Each mode of operation represents a separate water balance (refer to slides on data pre-processing)
Notes: For each modelled season, we increased the modes of operations. Since in this case they were two, we will show the model set-up with two modes of operations. Note that it is possible to increase the number of modelled seasons and modes, but this will lead also to increased model complexity and computational requirements.
To each season-technology is associated a commodity, called S1 and S2. These commodities go into cropland uses, but the value of the input activity ratio varies according to the mode of operation. Each mode of operation (MoO) is associated with a season: in this case MoO 1 refers to Season 1 and MoO 2 to Season 2. This set-up has to be consistent for modelling all the water cycle. Another key factor of the modelling consists in associating a capacity factor to each season-technology. The capacity factor has to be 1 for the time slice that represents the season and 0 for the other one. This will force the land technology to switch between Season 1 and 2 changing water requirements and water outputs accordingly.

## Slide 17: Modelling seasonal varibility and crop-growing stages Methods – consistency across seasons
17
For this type of modelling you will have to work with ”Activity” paramenters instead of ”capacity” for modelling cropland.
Working with the activity instead of the capacity, allows you to constrain and calibrate land for each mode, ensuring consistency across the seasons (modes).
Consistency across seasons is very important!

## Slide 18: Modelling seasonal varibility and crop-growing stages Methods - consistency across seasons
18
Change the residual capacity for cropland to ”Total Technology Annual Activity Lower Limit”.
Set the ”Operational Life” to 1 for all the crop land.
Put 0 to Capital costs (assuming there is no difference in buying land across crop-types).
Use the same Acrivity decrease/increase limits for each mode for calibrating land.
Use the same variable costs for each mode.
Input the same output acrivity ratio for crops in the additional mode(s).
Use the ”Capacity Factor” for the dummy season technologies: set 1 in the Timeslice corresponding to Season 1 and 0 for the other (do the opposite for the other season)

## Slide 19: Hands-on Exercise
19
You are modelling crop growing stages and seasonal variability.
Start from your CLEWs model and model 2 seasons: growing and harvesting. For each season input the following values.
Parameter | Technology | Commodity | Mode of operation | Value
Output activity ratio | MINLND | LND | 1 | 1
Output activity ratio | MINPRC | WTRPRC | 1 | 1
Output activity ratio | Season1 | S1 | 1 | 1
Output activity ratio | Season2 | S2 | 2 | 1
Output activity ratio | LNDCRP | EVP | 1 | Evapotranspiration associated to season 1
Output activity ratio | LNDCRP | EVP | 2 | Evapotranspiration associated to season 2
Output activity ratio | LNDCRP | GWT | 1 | Groundwater recharge associated to season 1
Output activity ratio | LNDCRP | GWT | 2 | Groundwater recharge associated to season 2
Output activity ratio | LNDCRP | SUR | 1 | Surface water associated to season 1
Output activity ratio | LNDCRP | SUR | 2 | Surface water associated to season 2

## Slide 20: Hands-on Exercise
20
You are modelling crop growing stages and seasonal variability.
Start from your CLEWs model and model 2 seasons: growing and harvesting. For each season input the following values.
Parameter | Technology | Commodity | Mode of operation | Value
Output activity ratio | LNDCRP | CRP | 1 | Yield
Output activity ratio | LNDCRP | CRP | 2 | Yield
Input activity ratio | LNDCRP | LND |  | 1
Input activity ratio | LNDCRP | LND |  | 1
Input activity ratio | LNDCRP | WTRPRC | 1 | Precipitation associated to season 1
Input activity ratio | LNDCRP | WTRPRC | 2 | Precipitation associated to season 2
Input activity ratio | LNDCRP | S1 | 1 | 1
Input activity ratio | LNDCRP | S2 | 2 | 1
Capacity Factor | Season1 | - | - | 1 in the Timeslice corresponding to Season 1 and 0 for the other
Capacity Factor | Season2 | - | - | 1 in the Timeslice corresponding to Season 2 and 0 for the other

## Slide 21: Hands-on Exercise
21
Techno-economic parameters and constraints
Parameter | Technology | Mode of operation | Value
Total Annual Max Capacity | LNDCRP | - | Calibrated value only for the reference year
Total Technology Annual Activity Lower Limit | LNDCRP | - | Calibrated value only for the reference year
Total Technology Annual Activity Upper Limit | LNDCRP | - | Calibrated value only for the reference year
Technology Activity Decrease By Mode Limit | LNDCRP | 1 | Same value as mode 2
Technology Activity Decrease By Mode Limit | LNDCRP | 2 | Same value as mode 1
Technology Activity Increase By Mode Limit | LNDCRP | 1 | Same value as mode 2
Technology Activity Increase By Mode Limit | LNDCRP | 2 | Same value as mode 1
Fixed Cost | LNDCRP | - | 
Variable Cost | LNDCRP | 1 | Same value as mode 2
Variable Cost | LNDCRP | 2 | Same value as mode 1

## Slide 22: Interpreting results
22
Rate Of Activity filtered by croplands (Tech Group), and by modes of operation (Mo Id) in the rows.
All the figure have been created using the MUIO v.5.3 user interface
What can you see?

## Slide 23: Interpreting results
23
Production by technology by mode filtered by croplands (Tech Group), and by modes of operation (Mo Id) in the rows.
All the figure have been created using the MUIO v.5.3 user interface
What can you see?
Is the water recharge the same?

## Slide 24: Examples and case studies
24
By post-processing the results you can explore the impact on resources, for example water stress
Photo Source: ”Average annual water stress” taken from ”Open-access models for case study countries-Update” by IAM compact Horizon Europe research project.
Case study: Ethiopia
Aim: assesment of resource stress due to irrigation expantion.

## Slide 25: Examples and case studies
25
By downscaling climate data, you can investigate the effect of climate change on the use of resources.
Photo Source: ” A clustering approach to improve spatial representation in water-energy-food models” by Abhishek Shivakumar etal 2021 Environ.Res.Lett. 16 114027.
Case study: Vietnam
Aim: improvement of spatial representation in water-energy-food models.
You can ensure consistency with IPCC climate data.

## Slide 26: Key Considerations
26
Water Data
Water variability
Climate change and seasonal variability
Once you know how the rainfall patter will vary (e.g due to climate change), you can re-create the water balance for each crop/land-use.
When dealing with water it is crucial to pre-process water data and esure that the balance is respected.
It is possible to increase the varibility of rainfall patters and water demand increasing modes of operation and using dummy technologies.

## Slide 27: Thank you
www.climatecompatiblegrowth.com