## Slide 1
CLEWs++ Modelling Course
LECTURE 10
Waste in the CLEWs++ concept

## Slide 2: Learning outcomes
1
2
Understand how solid and liquid waste are represented in the CLEWs++ concept
2
Recognise the main solid and liquid waste disposal and treatment technologies, and compare their associated benefits and trade-offs
3
Learn how to calibrate the solid and liquid waste sectors to a region-specific context
4
Use the principles from the waste sector to design and calibrate a sector that is not explicitly included in the CLEWs++ concept

## Slide 3: Representing Solid and Liquid Waste in CLEWs++
3
In CLEWs++, the waste sector is split into solid waste and liquid waste, reflecting how waste is generated, managed, and regulated in real-world systems.
These two waste types follow fundamentally different treatment pathways, rely on different infrastructure, and are associated with distinct environmental pressures, so they must be represented separately in the model. This distinction is important because waste management choices have wide-ranging impacts on greenhouse gas emissions, air and water pollution, public health, and overall system sustainability, and these impacts vary significantly across countries and regions.
This includes household, commercial, and industrial solid materials. Solid waste generation is measured by the mass generated (e.g. million tonnes per year). Emissions mainly arise from decomposition and combustion processes.
This includes wastewater from households, industry, and sanitation systems. Liquid waste disposal is quantified as the pollution load, typically measured using BOD*. Wider impacts are driven by the treatment efficiency and discharge to water bodies.
* This is explained on Slide 22.
Solid
Waste
Liquid
Waste

## Slide 4: Solid Waste

## Slide 5: Solid Waste Generation in CLEWs++
5
The solid waste sector represents the generation, collection, and treatment of all non-liquid waste produced by households, industry, and other sources. This includes everyday items like paper, food scraps, and plastics, as well as larger items like furniture, packaging, and construction debris.
Waste management has important implications for environmental quality, public health, and climate outcomes. Poorly managed waste can lead to uncontrolled methane emissions, air pollution from open burning, and soil and water contamination from dumping. Conversely, effective management through collection, recycling, composting, digestion, incineration, and controlled landfilling can reduce emissions, recover energy or materials, and improve overall resource efficiency.
In CLEWs++, solid waste pathways are divided into uncollected and collected waste.
Uncollected waste refers to material that is left unmanaged, such as waste that is openly burned or dumped.
Collected waste is material that is gathered and sent for treatment or processing.
This distinction helps the model capture how different disposal methods affect emissions and environmental outcomes.

## Slide 6: Solid Waste Disposal and Treatment Options
6
The following solid waste disposal and treatment options should be represented as separate technologies in a CLEWs++ model. Open burning and dumping fall under the category of uncollected waste. All other technologies are classified under collected waste.
Waste is burned openly on site. This has a very low cost but generates high air pollution and greenhouse gas emissions.
Waste is disposed of in uncontrolled sites. Minimal cost, but this causes land and water contamination, odours, and long-term environmental degradation.
Organic waste is biologically decomposed into nutrient-rich compost. It reduces emissions and can provide agricultural benefits.
Organic waste is treated anaerobically, producing biogas and digestate. Requires capital investment but reduces methane emissions if the waste is diverted from landfills.
Open Burning
Dumping
Composting
Digestors

## Slide 7: Solid Waste Disposal and Treatment Options (Continued)
7
Waste is separated and processed into reusable materials. In CLEWs++, recycling is modelled as four distinct technologies for metal, paper, plastics, and glass. Requires collection and processing infrastructure.
Specialised treatment for toxic or dangerous waste. Protects human health and the environment, typically high cost and strict regulatory oversight.
Controlled thermal treatment of waste. Reduces waste volume and requires proper emission management. Tends to have a moderate to high cost.
At a low to moderate cost, residual or general waste is buried in a controlled site with varying levels of gas and leachate management. In CLEWs++, the landfill technology can be linked to a landfill gas power plant, which converts methane to electricity.
Recycling
Hazardous Waste Disposal
Incineration
Landfill

## Slide 8: Overview of the Solid Waste Sector in CLEWs++
8
Dumping
Open Burning
Collected Waste
Solid Waste Generation
Unseparated Waste
Separated Waste
Organic Separation
Incineration
Landfill (General)
Landfill (Residual)
Digestors
Composting
Metal Recycling
Paper Recycling
Plastics Recycling
Glass Recycling
Hazardous Waste Disposal
Landfill Gas Power Plant
A
B
C
D
E
F
G
H
I
J
K
Commodity Key
A = All Solid Waste
B = Collected Waste
C = General Waste
D = Organic Waste
E = Residual Waste
F = Glass
G = Metal
H = Paper
I = Plastics
J = Hazardous Waste
K = Electricity
L = Biogas
L

## Slide 9: Overview of the Solid Waste Sector: Part 1
9
Dumping
Open Burning
Collected Waste
Solid Waste Generation
Unseparated Waste
Separated Waste
Organic Separation
A
B
Commodity Key
A = All Solid Waste
B = Collected Waste
Collection and Sorting Structure
All solid waste enters the model as a single generated waste commodity, which can either be collected or remain uncollected.
Uncollected waste represents unmanaged disposal pathways, such as dumping and open burning, which are modelled explicitly.
Collected waste can be directed towards unseparated waste or processed through waste separation pathways.
Separation distinguishes organic waste from other material streams and identifies waste that is suitable for downstream recycling or treatment.
This structure allows independent calibration of collection rates, separation levels, and waste composition.

## Slide 10: Overview of the Solid Waste Sector: Part 2
10
Treatment and Recovery Pathways
Unseparated waste can be sent to landfill or incineration, representing disposal options with different emissions and energy characteristics.
Separated waste enables material specific recycling, including glass, metals, paper, plastics, and hazardous waste streams.
Organic waste can be treated through composting or anaerobic digestion, producing stabilised material and biogas.
Residual waste can be sent to controlled landfill, where landfill gas recovery enables electricity generation.
This downstream structure allows the model to explore trade offs between disposal, recycling, biological treatment, and energy recovery.
10
Unseparated Waste
Separated Waste
Organic Separation
Incineration
Landfill (General)
Landfill (Residual)
Digestors
Composting
Metal Recycling
Paper Recycling
Plastics Recycling
Glass Recycling
Hazardous Waste Disposal
Landfill Gas Power Plant
C
D
E
F
G
H
I
J
K
L
Commodity Key
C = General Waste H = Paper
D = Organic Waste I = Plastics
E = Residual Waste J = Hazardous Waste
F = Glass K = Electricity
G = Metal L = Biogas

## Slide 11: Key Considerations in the Solid Waste Sector
11
1
Solid Waste is Activity Driven rather than Demand Driven
In most CLEWs++ sectors, system behaviour is demand-driven. For example, the modeller will input the demand for household heating, and the model determines which technologies operate to meet it, along with the associated costs and emissions.
The waste sector operates differently. Solid waste generation is not a choice made by the system and cannot be optimised away through alternative technologies. It is imposed on the model rather than solved for. Therefore, total solid waste generation is represented as an activity that must occur.
2
Technology Characteristics and Regional Context
While efficiencies and emissions factors for solid waste technologies tend to vary less across countries than other sectors, income level often matters. Recognising whether the region is low-, middle-, or high-income informs assumptions about typical technology performance and environmental impact.
3
Generation, Collection and Disposal Data is key
The starting point is to know the total solid waste generated in the region. Then, evidence on the share of waste that is collected versus left uncontrolled strongly affects the environmental and cost outcomes. Knowing how collected waste is treated helps to define realistic flows in the model.

## Slide 12: How to Calibrate the Solid Waste Sector
12
The total amount of solid waste generated is imposed on the model using the lower and upper annual activity limit parameters on the waste generation technology. These limits are typically based on historical national waste data and projected forwards using appropriate drivers such as population growth or income trends.
User defined constraints (UDCs) are required to ensure solid waste is collected and treated in a logical manner. Without any constraints, the model optimisation would send all waste to the cheapest and most efficient disposal option, which rarely is an accurate reflection of a real-world waste management system.
As a reminder, UDCs can be created as either equalities or inequalities, and consist of a constant and a set of multipliers for different variables. UDCs follow this equation, where t represents the technology:
SUM(UDC Multiplier New Capacityt * New Capacityt + UDC Multiplier Total Capacityt * Total Capacityt + UDC Multiplier Activityt * Activityt ) <= UDC Constant
1
Force Total Solid Waste Generation
2
Force Collection and Treatment Pathways

## Slide 13: How to Calibrate the Solid Waste Sector (Continued)
13
The following UDCs are recommended when setting up solid waste as part of the CLEWs++ concept.
1
The purpose of this UDC is to set a minimum share of total solid waste that is collected. This reflects the fact that, in most regions, only a proportion of generated solid waste enters the formal waste management system.
The logic of this constraint is to require activity in the waste collection technology to exceed a specified share of total waste generation.
Technologies included: Waste generation, Waste Collection
Constraint Type: Inequality
UDC Constant: 0
UDC Multiplier activity:
Waste Generation: Equal to the proportion of solid waste that is collected
Waste Collection: -1
Enforcing Waste Collection
For example:
If 25% of a region’s solid waste is collected, the UDC Multiplier Activity for Waste Generation would be 0.25. This may vary across time to reflect how waste collection behaviours are expected to change.

## Slide 14: How to Calibrate the Solid Waste Sector (Continued)
14
The following UDCs are recommended when setting up solid waste as part of the CLEWs++ concept.
2
The purpose of this UDC is to ensure consistency between waste collection and downstream disposal options. Any waste that is collected must be treated or disposed of, rather than remaining unallocated or implicitly dumped.
The logic behind this constraint is to balance total solid waste collection with the sum of all disposal and treatment options.
Technologies included: Waste Collection, open burning, dumping, digestors, composting, all recycling technologies, hazardous waste disposal, waste incineration, landfill
Constraint Type: Equality
UDC Constant: 0
UDC Multiplier activity:
Waste Collection: -1
All disposal and treatment technologies: 1
Balancing Waste Collection and Disposal

## Slide 15: How to Calibrate the Solid Waste Sector (Continued)
15
The following UDCs are recommended when setting up solid waste as part of the CLEWs++ concept.
3
The purpose of this UDC is to ensure that the organic waste disposal does not exceed the actual amount of organic waste content of the collected solid waste.
Composting and digestor technologies can only process the biodegradable component of the waste stream. In reality, these technologies are limited by the physical composition of waste, rather than by cost or technical efficiency alone. Without an explicit constraint, the model may allocate more waste to organic treatment pathways than is physically available as organic material.
Technologies included: Waste collection, digestors, composting
Constraint Type: Inequality
UDC Constant: 0
UDC Multiplier activity:
Waste Collection: Equal to the organic content of collected waste
Digestors and Composting: 1
Balancing Organic Waste Content
For example:
According to the IPCC, in middle income countries the average organic waste content of collected waste (by weight) is 53%. Therefore, the UDC multiplier activity for the Waste Collection technology would be 0.53.

## Slide 16: Practical Exercise
16
You are building the solid waste sector of a CLEWs++ model for the country of Genovia.
In 2020, Genovia’s total solid waste generation was 2.3 million tonnes. By 2030, total solid waste generation is expected to have increased by 6% relative to its 2020 level. Across the period, 62% of total solid waste generation is collected through the formal waste management system.
1
Which OSeMOSYS parameter would you use to ensure that the model represents Genovia’s total solid waste generation as an externally imposed quantity?
What value would you assign to this parameter in 2020?
What value would you assign in 2030, given the expected increase in waste generation?
Forcing Total Solid Waste Generation
2
Write out the user defined constraint (UDC) needed to ensure that 62% of Genovia’s total solid waste generation is always collected. Specify:
The technologies included in the constraint
Whether the constraint is an equality or an inequality,
The value of the UDC constant, and
The UDC multiplier activity for each technology.
Forcing the Waste Collection Share

## Slide 17: Liquid Waste

## Slide 18: Liquid Waste Generation in CLEWs++
18
The liquid waste sector represents the generation, collection, and treatment of all wastewater produced by households, industry, and other sources. This includes greywater from kitchens and bathrooms, blackwater containing human waste, and liquid waste from industrial processes.
Managing liquid waste is critical for protecting water quality, human health, and ecosystems. Untreated or poorly treated wastewater can degrade rivers, lakes, and groundwater, leading to waterborne diseases and environmental damage. Effective treatment through technologies such as septic tanks, latrines, anaerobic lagoons, and centralised or advanced aerobic treatment can remove organic pollutants, reduce biochemical oxygen demand (BOD), and prevent harmful discharges to the environment.
In CLEWs++, liquid waste pathways are classified according to the type of treatment they receive. This allows the model to capture how different treatment technologies reduce pollution loads and influence environmental outcomes:
On-site and decentralised systems include latrines, septic tanks, and anaerobic lagoons, where wastewater is treated close to its source.
Sewer-based treatment includes centralised and advanced aerobic treatment plants, where wastewater is collected via sewers and treated in larger facilities.

## Slide 19: Liquid Waste Treatment Options
19
The following liquid waste treatment options should be represented as separate technologies in a CLEWs++ model. On-site systems such as septic tanks, anaerobic lagoons, and latrines are decentralised treatments, while centralised aerobic and advanced aerobic treatments are sewer-based.
Wastewater is treated in conventional plants using oxygen-based biological processes. Removes most organic pollutants, moderate cost, requires energy and infrastructure.
Enhanced treatment for higher pollutant removal efficiency. Very effective at protecting water quality, but higher capital and operational costs.
Centralised Aerobic Treatment
Advanced Aerobic Treatment

## Slide 20: Liquid Waste Treatment Options (Continued)
20
On-site tanks that partially treat wastewater before infiltration. Low cost, commonly used in low-density areas, but efficiency depends on proper maintenance.
Simple sanitation systems for basic waste containment. They require minimal treatment and are low cost, making them suitable for rural or informal settlement. Limited pollution control.
Large ponds where wastewater undergoes anaerobic decomposition. Suitable for warm climates and large land areas, produces biogas, moderate removal of BOD, relatively low cost but requires space.
Septic Tanks
Latrines
Anaerobic Lagoons

## Slide 21: Overview of the Liquid Waste Sector in CLEWs++
21
Septic Tanks
Anaerobic Lagoons
Latrines
Liquid Waste Generation
Sewers
Centralised Aerobic Treatment
A
B
Commodity Key
A = All Liquid Waste
B = Collected Waste
Advanced Aerobic Treatment
Liquid waste generation produces a single aggregate wastewater commodity, representing all liquid waste entering the sanitation system.
This commodity can follow multiple pathways depending on sanitation access, either through decentralised on-site treatment or collection via sewer networks for centralised treatment.
Decentralised pathways include latrines, septic tanks, and anaerobic lagoons, representing non sewered sanitation systems where wastewater is managed locally.
Sewer based collection converts total liquid waste into a collected wastewater commodity, which can then be allocated across different centralised treatment technologies.
The separation between total liquid waste and collected waste enables independent calibration of sanitation coverage and treatment choice, supporting scenarios that explore expanded sewer access and improved treatment standards.

## Slide 22: Key Considerations in the Liquid Waste Sector
22
1
Liquid Waste is Activity Driven rather than Demand Driven
As with solid waste, the liquid waste sector is activity-driven, rather than demand-driven. The model does not optimise total wastewater production; instead, total generation is represented as a mandatory activity that must occur in each time period.
2
Key Data: BOD per Capita
To set up the liquid waste sector, the average biochemical oxygen demand (BOD) per person provides a critical baseline. BOD measures the amount of organic matter in wastewater that can be biologically decomposed and therefore reflects the pollution load. Combining per capita BOD with population data allows the model to estimate total BOD entering the treatment system.
3
Generation, Collection and Disposal Data is key
Treatment efficiencies, emissions factors, and energy use differ across technologies such as septic tanks, primary sedimentation, or advanced biological treatment. Knowing the types of treatment used and their relative shares in the region informs how BOD is reduced and helps ensure the model reflects realistic flows and environmental outcomes.

## Slide 23: How to Calibrate the Liquid Waste Sector
23
The total liquid waste generated is imposed on the model using the lower and upper annual activity limit parameters on the liquid waste generation technology, based on historical national waste data and projected forwards using appropriate drivers. The activity limit should be equal to the total liquid waste generation.
Just one user defined constraint (UDC) is required for this sector. This ensures that a minimum share of total liquid waste is collected. The logic behind this is that the activity of the sewer technology exceeds a given share of total liquid waste generation.
Technologies included: Waste generation, Waste Collection
Constraint Type: Inequality
UDC Constant: 0
UDC Multiplier activity:
Waste Generation: Equal to the proportion of liquid waste that is collected (can change over time)
Waste Collection: -1
1
Force Total Liquid Waste Generation
2
    Force Liquid Waste Collection

## Slide 24: Modelling Sectors not included in the CLEWs++ Concept

## Slide 25: Key Considerations when Modelling New Sectors
25
Understand the Core Processes
Identify the main processes within the sector from a systems perspective. This is crucial as the CLEWs++ concept considers the energy, land, and water use within a sector, as well as the emissions produced. Clarifying each process ensures accurate representation of resource demands, the costs, and the varying environmental impacts.
Decide what to Model Explicitly
Consider the differences in efficiency, costs, and emissions, as well as the relative importance of sub-sectors within the regional context before deciding what to model explicitly. Likewise, consider the divergent growth patterns of certain sub-sectors. Group minor processes when appropriate, but separate significant processes that strongly influence results.
Include Alternative Technologies for Transition Scenarios
When modelling decarbonisation or energy transition scenarios, incorporate technologies that enable these changes, even if they are not currently present. This allows CLEWs++ to explore potential future pathways, such as integrating renewable energy options in traditionally fossil-fuel-dominated sectors.

## Slide 26: Thank you
www.climatecompatiblegrowth.com

## Slide 27: Answers to the Practical Exercise
27
1. Forcing Total Solid Waste Generation
To represent total solid waste generation as an externally imposed quantity, the Lower Annual Activity Limit (and equivalently the Upper Annual Activity Limit) should be applied to the Waste Generation technology (WSTGEN).
In 2020, the value should reflect observed total solid waste generation. So, in 2020, the lower annual activity limit = 2.3 million tonnes.
By 2030, total solid waste generation is expected to increase by 6% relative to 2020:
      2030 waste generation = 2.3 * 1.06 = 2.438 million tonnes
      Lower annual activity limit (WSTGEN, 2030) = 2.438 million tonnes
2. Forcing the Waste Collection Share
Technologies included: Waste generation (WSTGEN), Waste collection (WSTCOL)
Constraint type: Inequality
UDC Constant: 0
UDC Multiplier activity:
WSTGEN: 0.62
WSTCOL: -1
This constraint requires activity in the waste collection technology to be at least 62% of total solid waste generation in every model year, preventing the model from underrepresenting waste collection.