## Slide 1
CLEWs++ Modelling Course
LECTURE 10
Introduction to Model Development Infrastructure (MDI)

## Slide 2: Learning outcomes
2
Get an overview of the concept of the Model Development Infrastructure (MDI)
Go through the first MDI files
1
2

## Slide 3: The MDI concept
3
Standardising model-building practices can increase efficiency, save time, and reduce errors. The MDI aims to standardise CLEWs++ model development. Although there have been other efforts in the past to support this goal, the MDI stands out due to the following key aspects.
Source: https://www.cambridge.org/engage/coe/article-details/689db738728bf9025e622637
MDI folder: https://zenodo.org/records/16875355
Broader scope
Earlier initiatives have primarily focused on the power sector or, at best, selected areas within the energy system. In contrast, the MDI enables the development of comprehensive CLEWs models and also incorporates waste and industrial process emissions; elements not previously included in standard CLEWs models. This extended coverage, achieving 100% representation of greenhouse gas (GHG) emissions, is referred to as CLEWs++.
Adjustable scope
While the MDI allows for the construction of a detailed CLEWs++ model across multiple sectors, it also supports flexibility in model scope. Users may exclude certain sectors (e.g. such as waste) if not relevant to their analysis. Similarly, sectoral detail can be customised. For instance, the industrial sector can be disaggregated into sub-sectors; if a user opts not to model aluminium production explicitly, it can be grouped under a general ‘other industry’ category.
Ease of use
The MDI is based on a series of Excel files and requires no coding skills. Users populate these files in sequence, following clear, step-by-step instructions. This design minimises the likelihood of errors and lowers the barrier to entry for non-programmers.
Modular and maintainable
Instead of relying on a single master file, the MDI consists of multiple interlinked files. This modularity ensures that updates or improvements to one component do not disrupt the entire workflow, enhancing both usability and long-term maintainability.

## Slide 4: The MDI structure and the broader model development flowchart
4
01_Tool - Calibration
02_Tool - Technoeconomics
03_Tool - Demand Projections
04_Tool - Residual Capacity Power
05_Tool - Year Split & Load Profiles
06_Tool - Renewables CFs
07_Tool - Constraints
08_Tool - Residual Capacity Others
User
collected data
Model Input Data
00 - Technology Database
Model conceptualisation & scoping
MDI
Result analysis & debugging
It’s worth noting that the MDI is no replacement for in-depth knowledge of energy modelling, but a supporting set of tools
In the MDI folder, there are some generic instructions, as well as file-specific ones within each file

## Slide 5: 00 - Technology Database (1/2)
CCG technology directory
Easy to navigate
Smooth update process
Standardised naming convention
Facilitates model development
One coherent directory, listing technoeconomic data for all technologies included in CLEWs++
Technoeconomic data is country-specific and thus, the user is encouraged to search for relevant data and store it in the database.
However, the database is pre-populated with global data, so that a basic CLEWs++ model can be developed even with minimal to zero data collection
Populated with a comprehensive list

## Slide 6: 00 - Technology Database (2/2)
Milestone year values
The Technology Database should only include milestone year values, e.g. 2020, 2030 and so on
Users (not always modellers) are usually interested in the above values only
Intermediate values are usually interpolated . In the MDI, the interpolation occurs in the Technoeconomics Tool
#
Tech ID
A unique combination of all 5 filters leads to a unique tech name and a unique Tech ID (e.g. 1, 2…. 257)
If more than one data source is used for a specific technology, a Source identifier is also used (e.g. a, b…. k)

## Slide 7: 01_Tool - Calibration
7
This tool forms the backbone of the MDI.
Its purpose is to provide the initial conditions for a reference year, using historical data.
It is pre-populated with energy balances and power generation by source for all countries.
Building on the energy balances, the tool generates the necessary data to describe each sub-sector included in the MDI.
While the energy balances are the most critical input, additional user-sourced data can improve the quality of the calibration. If such data are unavailable, default values can be applied.

## Slide 8: 02_Tool - Technoeconomics
8
This tool draws primarily on data from the Technology Database and reformats it into a structure suitable for modelling. For example, while the Technology Database provides capital cost data for milestone years only (e.g. 2030 and 2040), modelling requires values for all intermediate years.
The Technoeconomics tool addresses this by applying linear interpolation to generate the necessary annual data points.
The tool focuses on compiling all key techno-economic parameters required to model a technology in OSeMOSYS. Most of the necessary data are sourced directly from the Technology Database, meaning that only minimal additional inputs are needed at this stage.
The main supplementary input concerns emission intensities, for which users may either provide their own values or utilise the default data included in the tool.

## Slide 9: 03_Tool - Demand Projections
9
This tool uses the base-year demand values calculated in 01_Tool – Calibration as the starting point. For each future year, it projects demand by multiplying the base-year value by the specified growth rate, thereby producing annual demand estimates for each demand category.
The tool is pre-populated with growth rates for most demand types and countries. These default values are derived from a simplified techno-economic analysis that uses GDP and population trends as key drivers. Users are encouraged to revise these growth rates where more accurate or context-specific data are available.
An additional function of this tool is to allow the user to define whether each demand is categorised as Accumulated Annual or Specified Annual - a distinction that is essential in later modelling stages.

## Slide 10: 04_Tool - Residual Capacity Power
10
This tool uses the commissioning date and installed capacity of each type of (combined heat &) power plant to aggregate this data and generate a vintage capacity profile for each technology type. This enables the model to represent the remaining operational capacity of existing plants over time in a realistic manner.
Where such commissioning data are unavailable, this tool may be omitted. In such cases, the vintage capacity profile for power plants can instead be calculated using the same method applied to most end-use technologies (see 08_Tool – Residual Capacity Others).

## Slide 11: 05_Tool - Year Split & Load Profiles
11
This tool calculates two key input parameters for the model.
Year Split – This represents the share of each time slice within a year. At the time of writing, the tool provides a fixed year split for 30 predefined time slices. Future versions are expected to allow users to define custom time slices and year splits.
Demand Profiles – These profiles apply to the demands identified as Specified Annual in the previous tool (03_Tool – Demand Projections). A demand profile expresses the distribution of demand occurrence throughout the year as a share of the total. To generate these profiles, the tool requires both the year split and an hourly demand profile for each demand type. Hourly profiles for a selection of key demands are preloaded in the MDI and can be accessed in the Profiles folder.

## Slide 12: 06_Tool - Renewables CFs
12
This tool calculates the capacity factor for wind and solar technologies for each time slice.
Similar to 05_Tool – Year Split and Demand Profiles, it uses the predefined year split in combination with hourly capacity factor data to produce the final time-slice-specific values.
Pre-loaded capacity factor profiles, disaggregated by country and by technology (wind and solar), are included in the MDI and can be accessed in the Profiles folder.

## Slide 13: 07_Tool - Constraints
13
This tool assists the user in defining constraints that influence the behaviour of the model.
A set of predefined constraints is included; however, it is at the user’s discretion to determine which of these are relevant to their case study and to specify their parameter values accordingly.
In addition to the default options, the user may introduce custom constraints to address specific modelling requirements or policy considerations.

## Slide 14: 08_Tool - Residual Capacity Others
14
This tool calculates the vintage capacity profile for all technologies that have an associated capital cost.
For technologies without capital costs, residual capacity is not applicable.
To generate these profiles, the user first runs a scenario in which no residual capacity is specified.
This allows the model to determine the capacity required in the base year, given the predefined technology activity.
A linear decline in capacity is then assumed, based on the operational lifetime of the relevant technology.

## Slide 15: Model Input Data
15
This file is not a tool in the conventional sense, as it performs no calculations.
Instead, it compiles the outputs from all preceding tools and organises the data into a structure that is ready for direct use in building a model within the Model User Interface for OSeMOSYS (MUIO).

## Slide 16: Thank you
www.climatecompatiblegrowth.com