## Slide 1
CLEWs++ Modelling Course
LECTURE 12
Model QA & Debugging

## Slide 2: Learning outcomes
2
Go through best practices for model QA
Provide tips for model debugging
1
2

## Slide 3: Introduction to model QA
3
Just because a model runs, it doesn’t mean it’s correct…
VS
Infeasible solution
If the model is not able to solve, then there’s 100% a mistake. Fixing the mistake and getting the model to run should be a priority
Feasible solution
When a model does run, it means it’s mathematically correct. It doesn’t necessarily mean it’s accurate though. QA over the model output should be always performed
Some basic QA principles
What does the market/real world think about this?
Does the model behave according to expectations?
Do we believe our scenarios?

## Slide 4: Check - Supply doesn’t exceed demand
4
Supply should not exceed demand unless it’s linked to system cost reductions which is rare (e.g. electricity exports)
Chart: 
| 2020 | 2025 | 2030 | 2035 | 2040
Heat demand | 140 | 152 | 166 | 174 | 196
Chart: Heat supply
| 2020 | 2025 | 2030 | 2035 | 2040
Gas boilers | 80 | 100 | 120 | 140 | 160
Oil boilers | 42 | 30 | 15 | 10 | 5
Biomass boilers | 18 | 22 | 31 | 24 | 31
Chart: 
| 2020 | 2025 | 2030 | 2035 | 2040
Heat demand | 140 | 152 | 166 | 174 | 196
Chart: Heat supply
| 2020 | 2025 | 2030 | 2035 | 2040
Gas boilers | 88 | 110 | 132 | 154 | 176
Oil boilers | 46.2 | 33 | 16.5 | 11 | 5.5
Biomass boilers | 19.8 | 24.2 | 34.1 | 26.4 | 34.1
✓
X
Solution
If supply exceeds demand, the most likely causes are:
Some constraints are forcing the model to overproduce. Those could be:
      Absolute constraints such as forced activity
      A minimum utilisation rate on certain technologies
      A wrongly set UDC
      A relative constraint such as a decrease rate which doesn’t allow the activity of a certain technology to reduce enough
      There’s some other indirect demand further downstream, driving supply

## Slide 5: Check - Constraints are respected
5
When constraints are used in the model, it’s critical to verify that they are respected
In some cases, the check is straightforward. For example, when a Total Technology Annual Activity Lower Limit is used for a technology, it will be respected if entered correctly
Things get more complicated when a parameter is used to constraint the model, but the impact is expected somewhere else in the model. For example, capacity might be forced in transport, expecting to see a certain activity (either due to a minimum utilisation rate or pure economics). If the output is not according to expectations, it’s likely that the off-model calculations need reviewing

## Slide 6: Check - Technology choice makes sense
6
Understanding what technology mix is sensible is not always straightforward though. It requires an understanding of the (current and future) economics of the technologies included in the model, as well as market intuition
If the technologies that kick in are not in line with expectations, it could be down to either constraints preventing the expansion of a technology/forcing a competitor or wrongly inserted technoeconomic parameters
Capital cost [M$/GW] | 667 | 667 | 1497 | 1497
Fixed O&M cost [MW/GW/y] | 22 | 22 | 42 | 42
Fuel cost [M$/PJ] | 5 | 5 | 0 | 0
Lifetime [y] | 25 | 25 | 25 | 25
Efficiency [%] | 60 | 60 | 100 | 100
Capacity factor [%] | 80 | 50 | 35 | 20
LCOE [$/MWh] | 36.9 | 41.1 | 33.2 | 58.2
When in doubt regarding the technology choice in the model, checking the economics off-model is the best way forward.
Below is an example of a levelised cost of electricity calculation for gas power plants and a wind turbines under different capacity factor values and 0% discount rate.
Some cases are more complicated than others. For example, when emissions are limited, one needs to take into account the shadow carbon price.
Chart: Power generation in BAU [TWh]
| 2020 | 2025 | 2030 | 2035 | 2040
Hydropwer | 200 | 200 | 200 | 200 | 200
Gas CCGT | 30 | 40 | 50 | 60 | 70
Coal with CCS | 0 | 0 | 5 | 20 | 50
Can you spot the mistake?... CCS should never kick in BAU (i.e assuming no cabron emission limits or price)

## Slide 7: Check - Smooth graphs
7
Chart: Million cars
| 2020 | 2025 | 2030 | 2035 | 2040
ICE cars | 240 | 260 | 283 | 333 | 410
Electric cars | 10 | 32 | 56 | 118 | 193
Chart: Million cars
| 2020 | 2025 | 2030 | 2035 | 2040
ICE cars | 240 | 210 | 283 | 250 | 410
Electric cars | 10 | 32 | 56 | 118 | 193
✓
X
It’s important that all output trends appear smooth, i.e. without fluctuations
When certain shifts in trajectories appear to be abrupt, they can be usually fixed with activity increase/decrease rates
If actual fluctuations appear (i.e. the activity/capacity of a certain technology going up and down), it requires a deeper dive into how the model is set up, and in many cases taking a few steps back

## Slide 8: Implement model changes gradually
8
Implementing model changes in stages, as opposed to all at once, helps with both understanding the impact of each change and with knowing which exact intervention might cause a bug
On occasion, certain model changes can be grouped together and applied in one go. This depends on a) the complexity and anticipated impact of the changes and b) the level of experience of the user
It’s important to differentiate between changes pertaining to the actual development of the model and changes made purely for diagnostic purposes
Apply change 1
Actual development
Diagnostics
Assess impact of change 1
Apply change 2
Assess impact of change 2
Apply change 1
Assess impact of change 1
Apply change 2
Assess impact of change 2
Retract change 1

## Slide 9: Some common bugs (and what to do…)
9
Note: The above list is not exhaustive
Over-constrained model
Missing technology input
Wrong name/input value
Problem description
Solution
The user added a constraint which clashes which clashes with another one upstream/downstream or even at the same level
Look thoroughly into the flow the constraint was added to and try to figure out where the issue might be. Potentially remove all model constraints and re-introduce gradually.
A new flow was added that has to kick in but was not connected properly.
Check the Model diagram in MUIO and ensure a) there’s no flow that starts with a commodity as opposed to a technology and b) all flows are accurately connected
Examples:
A technology name is using a character that is not recognised
Operational Life input value is not an integer
Any input value is using a comma
Retract recent changes and check all names/input values thoroughly
Does MUIO take care of this one? Let’s mention it in this case but maybe still good to describe the problem for non MUIO OSeMOSYS users

## Slide 10: But what can you do when an entire model is broken?
10
Ideally one shouldn’t get to this point because changes should be applied gradually. Nevertheless, in case the user either applies many changes in one go or inherits a broken model from another user, below are some tips on how to resolve
1
2
3
4
Create a copy of the model. Delete all input data but keep Model configuration inputs (e.g. Technology/Commodity declaration)
Pick one very simple flow and re-introduce the data after checking it carefully. That data would be:
The Year Split
One final demand (if it’s a Specified Annual Demand, the relevant Specified Demand profile is also needed)
The Output Activity Ratio of one technology that can meet that demand
Try to run the model and move to the next step
Gradually connect all technologies by using the Input/Output Activity Ratios. Once all technologies are connected, re-introduce non-constraint related data gradually (start with demands, then technoeconomic inputs)
Finally, re-introduce all model constraints gradually

## Slide 11: Exercises
@Fra, could you paste the KTH debugging exercises here

## Slide 12: Thank you
www.climatecompatiblegrowth.com