## Slide 1: Modelling for Fossil Fuel Retirement : Fossil Fuel Retirement Model
Lecture 4:
Applying FFRM to inform fossil fuel retirement strategies

## Slide 2
Lecture Outline
Modelling for Fossil Fuel Decommissioning: FFRM
Part 1 | Structure of FFRM
Part 2 | FFRM Calibration

## Slide 3: Learning Objectives
By the end of this lecture, participants will be able to:
The structure of the FFRM (key parameters, variables and regimes) and interpret how the core equations represent net revenue, generation targets, and retirement
Explain the key inputs used to calibrate FFRM (e.g., capacity, start year, PLF, efficiency, OPEX) and how they link to the model equations

## Slide 4: Modelling for Fossil Fuel Retirement : Fossil Fuel Retirement Model
Part 1:
Structure of FFRM

## Slide 5: Overview of FFRM
The structure of the FFRM comprises eight core mathematical equations used to determine the foregone net revenue of fossil fuel fleets.
The core objective function assess foregone revenue under:
The PPA regime, which is based on commercially negotiated power purchase agreements
The market-based regime, which reflects projected hourly spot prices that are determined exogenously.
Notes: This slide explains the basic structure of the FFRM. At its heart, the model is built around eight core mathematical equations. Together, these equations quantify foregone net revenue for fossil fuel fleets is essentially, what operators lose when plants run less or retire earlier than they otherwise would. The model’s objective function is set up to evaluate foregone revenue under two different revenue regimes. First is the PPA regime, where revenue is governed by commercially negotiated power purchase agreements, so the price and payment structure are contract-based. Second is the market-based regime, where revenue is driven by projected hourly spot prices. Those spot prices are treated as exogenous inputs to the model.

## Slide 6: The Structure of FFRM - Net Revenue (NR) Objective Function
The first part of the equation represents revenue minus variable cost. Electricity price in year (y), price scenario (p), and time (t) is net of the generator’s variable cost in year (y), and this margin is multiplied by electricity generated.
The second part represents fixed costs applied to remaining (non-retired) capacity and is subtracted from the first part. The difference in systemwide net revenue between the business-as-usual and decarbonisation scenarios is used to calculate foregone revenue. Foregone revenue associated with retired capacity is then used to estimate stranded cost.
Notes: This equation estimates net revenue for each generator. The first term is the operating margin: electricity price (by year y, price case p, and time t) minus variable cost (in year y), multiplied by generation.The second term is fixed cost × retired capacity, which we subtract from the operating net revenue. To get foregone revenue, we take the difference in system-wide net revenue between the BAU and decarbonisation scenarios. That foregone revenue is then used as a proxy for stranded cost associated with retired capacity.

## Slide 7: The Structure of FFRM - Foregone Revenue Constraint
This equation is a fraction that limits how far a power plant unit’s net revenue can deviate from the business-as-usual scenario. It represents the proportional loss in net revenue: net revenue under decarbonisation is subtracted from BAU in the numerator, and BAU net revenue is in the denominator. Alpha (α) is a user-defined threshold, and the model constrains the net revenue loss so it cannot exceed α.
Notes: This fraction caps how much a unit’s net revenue can drop compared to business-as-usual (BAU). The numerator is the change in net revenue: decarbonisation minus BAU. Dividing by BAU net revenue turns it into a proportional loss, which is reflected as a percentage. α is a user-defined threshold, and the model constrains the loss so it cannot exceed α.

## Slide 8: The Structure of FFRM - Fleetwide Generation Target Constraint
This equation constrains fleetwide generation to match a user-defined trajectory. It requires total generation across all units and time blocks to equal the system generation target for each year and scenario. Under a decarbonisation trajectory, fossil generation declines over time, reducing net revenue relative to the business-as-usual scenario.
Notes: This equation shows the constraint pins total fleet generation to a user-defined target each year and scenario. We sum generation across units and time blocks and weight by (H[t]) to get total energy. In decarbonisation, fossil output falls over time, so net revenue is lower than BAU.

## Slide 9: The Structure of FFRM - Minimum Generation Constraint
This equation shows a constraint whereby the electricity generated per generator (g), in year (y), time period (t),scenario (s) and price regime (p), multiplied by the number of hours in that period should be equal to or be greater than minimum generation of that generator (g).
Notes: This equation shows a constraint whereby the electricity generated per generator (g), in year (y), time period (t),scenario (s) and price regime (p), multiplied by the number of hours in that period should be equal to or be greater than minimum generation of that generator (g).
The second equation shows is similar to the equation reference above. However it represents the upper bound whereby the total electricity generation by a generator (g) over time (t), scenario (s), price regime (p) multiplied by the number of hours in a time period does not exceed the specified maximum allowed generation for a generator (g).

## Slide 10: The Structure of FFRM - Maximum Generation Constraint
This constraint sets an upper bound on generation. It ensures that total electricity produced by unit across all time blocks does not exceed the maximum allowed generation for that unit​. This prevents the model from dispatching a unit beyond feasible annual output given capacity, availability, and any operational limits.

## Slide 11: The Structure of FFRM - Capacity Balance Equation
This equation tracks generation capacity over time decreasing capacity when units a retired. Therefore the available capacity is equal to the capacity from the previous year minus any capacity that is retired in year (y).
Notes: This equation tracks generation capacity over time decreasing capacity when units a retired. Therefore the available capacity is equal to the capacity from the previous year minus any capacity that is retired in year (y).

## Slide 12: The Structure of FFRM - Capacity Requirement Constraint
This equation illustrates the minimum level of fleetwide capacity that needs to be maintained. It shows the total available generation capacity must be equal or greater than the target value. It specifies that there must be enough capacity in the system to meet the target.
Notes: The first equation shows the minimum level of fleetwide capacity that needs to be maintained. It shows the total available generation capacity must be equal or greater than the target value. It specifies that there must be enough capacity in the system to meet the target.

## Slide 13: The Structure of FFRM: Cumulative Retirement Equation
Finally, this equation defines the cumulative retirement in each year. It provides a running total of retirements.
For each plant, it adds up all the years the plant has been retired up to that year, so the model knows whether and how long the plant has already been retired.
Notes: The final equation shows finally, this equation defines the cumulative retirement in each year.

## Slide 14: Modelling for Fossil Fuel Retirement : Fossil Fuel Retirement Model
Part 2:
FFRM Calibration

## Slide 15: FFRM Calibration - Plant Data
The first stage of calibrating the FFRM requires plant-level information on costs, capacity, and start year.
It is essential to ensure that the total capacities of the plants in your list are equal to or higher than the "residual capacity" of the technology in OSeMOSYS at the beginning of the modelling period; otherwise, the model will fail. Plant capacity information should be referenced in the OSeMOSYS documentation.

## Slide 16: FFRM Calibration - Plant Data
Plant-specific variable costs (operational, maintenance, and fuel costs) in $/MWh.

## Slide 17: FFRM Calibration - Plant Data
Plant-specific fixed costs in $/MWh. Plant-specific fixed costs ($/MWh) refer to the fixed costs required to keep a specific plant available and operational. This is only used to calculate PPA cost, if you have PPA information you don’t need to complete this column.

## Slide 18: FFRM Calibration - Plant Data
Plant-specific PPA costs are calculated as COST + FIXED COST. If you already have PPA cost information, you may overwrite the formula and enter your values directly. Otherwise, the FFRM will calculate this value automatically.

## Slide 19: FFRM Calibration - Plant Data
Market price ($/MWh) is the wholesale electricity price for the relevant region and time period. If open-source price data are not available, you can use the dual value (shadow price) from an electricity balance constraint in a capacity expansion model (e.g., OSeMOSYS) as a proxy.

## Slide 20: FFRM Calibration - Plant Data
Capacity (MW) refers to each plant’s installed generating capacity, reflecting the maximum electrical output it can produce under normal operating conditions and expressed in megawatts.

## Slide 21: FFRM Calibration - Plant Data
The start year of a power plant; the year when the plant is connected to the grid and starts generating electricity.

## Slide 22: FFRM Calibration - Plant Data
Plant Type defines the fossil fuel technology
PWRCOA001: Coal power plant
PWROHC001: Light fuel oil power plant
PWROHC002 : Oil fired gas turbine - SCGT
PWRNGS001: Natural gas power plant - CCGT
PWRNGS002: Natural gas power plant - SCGT
PWROHC003: Light fuel oil standalone generator (1kW)

## Slide 23: FFRM Calibration - Plant Data
Pricing regime refers to the basis on which a plant’s electricity price (and resulting revenue) is determined. It indicates whether the plant is priced under a PPA regime (contracted price) or a market regime (wholesale market price). The FFRM Read the Docs has a Electricity Market Structure Map which shows the potential pricing regimes that exist within the country, which can be found here.

## Slide 24: FFRM Calibration - Plant Data
The Contracted Price refers to a capacity payment, which unit of measurement is USD per MW. This can be applied to any regime and appears as a separate revenue stream from the energy price. If data is not publicly available, this column should be zero.

## Slide 25: FFRM Calibration - PPA Years
The next sheet, "FC_PPA," is calibrated based on the data collected in the previous sheet.
The values here represent the PPA fixed cost at 85% of the plant load factor, expressed in $/MW/year.
The values should be displayed for the years during which the PPA is still active.

## Slide 26: FFRM Calibration - PPA Years
These values represent the PPA fixed cost (availability payment) at an 85% plant load factor (PLF), expressed in $/MW/year.
FFRM is profit-maximising and plants decide operation and retirement based on profits, the PPA regime must include a fixed annual $/MW revenue stream (plus any energy payment).
Values should be shown only for the years in which the PPA remains active
58.33 x 0.85 x 8760 = 434,325
8760 is the number of hours in a year

## Slide 27: FFRM Calibration - Fossil Fuel Generation Projection
Here, we impose constraints on the model according to the generation limits (TWh) obtained from long term capacity expansion models, such as OSeMOSYS. This constraint can be applied across different types of fossil fuel technologies, such as coal (PWRCOA001), gas (PWRNGS001) and oil (PWROHC001).
Exercise caution regarding the following:
If the generation target trajectory increases year-on-year, the model may become infeasible if units have already been retired.
The units specified are in TWh. However, ensure conversion from the units provided by OSeMOSYS before finalising this document.

## Slide 28: FFRM Results
The findings include plant retirement schedules and discounted net revenue under regimes across scenarios such as least cost and net zero.
Stranded costs for each decarbonization scenario is calculated relative to the baseline or least cost, representing the reduction in discounted revenue.
Retirements are determined by both the age and cost of stations, with fixed costs being the primary factor in the PPA regime, while variable costs drive decisions in the market price regime.

## Slide 29: FFRM Results - Stranded Costs
In this instance, the total cost requiring compensation for prematurely retiring plants amounts to $81 billion USD. A published study applying the FFRM examined coal retirement pathways in India. More information can be found here.
 | Scenario 1 (Least Cost) | Scenario 2 (Net Zero)
Total Discounted Revenue (Billion US$) | 207 | 126
Stranded Cost Compensation (Billion US$) | - | 81

## Slide 30: Part 4: References
Suski, A., Hong, L. and Chattopadhyay, D. (2022) ‘Modeling coal plant stranded costs for decarbonization pathway analyses’, Energy for Sustainable Development, 71, pp. 480–489. doi: 10.1016/j.esd.2022.10.02
Liu, Z., Osei-Owusu, S. and Luscombe, H. (2025) ‘Structure overview: Equations’, FFRM 1.0 documentation. Available at: https://ffrm-python.readthedocs.io/en/latest/equations.html (Accessed: 6 February 2026).