## Slide 1
CLEWs++ Modelling Course
LECTURE 12
From MDI to MUIO
RECOMMENDED CITATION: Avgerinopoulos, G., Gardumi, F., and Flint-Smith, A. (2026). 'Lecture 12: From MDI to MUIO'. Climate Compatible Growth programme OpenLearn Collection [Powerpoint Lecture]. [Online]. Available at: https://www.open.edu/openlearncreate/course/view.php?id=18048

## Slide 2: Learning outcomes
‹#›
Complete model development moving from the MDI to MUIO.
Use two alternative approaches for inputing data into MUIO and explain their respective advantages and disadvantages.
1
2

## Slide 3: Using the MDI to develop a model
‹#›
The previous lecture explained how the Model Development Infrastructure (MDI) tool works to collect the necessary data inputs to build a model. This lecture covers how to translate the collected data from the MDI into the Model User Interface (MUIO) on OSeMOSYS.
Before building a first version of your model, it is important to have downloaded the MDI and followed the accompanying instructions from start to finish. Upon completion, the MDI produces the Model Input Data file, which contains all the information required to build a first version of the model.
Once the data has been produced, there are two ways to input it into MUIO:
  Sector by sector → less prone to errors, but time-consuming. Strongly recommended for beginners
  All data in one go → generally faster, but more prone to errors and therefore requires a higher level of experience and confidence.
The coming slides describe each method and outline their respective advantages and disadvantages.

## Slide 4: Using the MDI to develop a model
‹#›
The MDI is preloaded with a set of model features (e.g. sets, technologies, commodities) that can be used flexibly, depending on the scope of the specific model.
In most cases, there will inevitably be features that the modeller wants to include, which are not covered by the MDI (e.g. specific technologies or commodities, or UDCs for specific policy targets). These can often be defined after an initial version of the model has been developed, as the user engages with stakeholders.
Such features can be incorporated either by modifying the existing MDI files or by creating additional input files, depending on user preference.

## Slide 5: Input approach 1: Sector by Sector
‹#›
In this approach, the user builds the model one sector at a time, running, debugging, and carrying out quality assurance (QA) before moving on to the next sector.
Demand-side energy sectors – buildings, industry, and transport – should be prioritised over the power sector and other supply-side components, because it is easier to calibrate the latter once the demands are all defined. OSeMOSYS is a demand-driven model and as such, if there is no exogenous demand defined, the model will not produce any credible results. Water, land, waste, and agriculture should be addressed afterwards.
The following sequence is recommended for entering input parameters. It is best practice to run the model after each step and to add the next parameter only once the model runs successfully:
5. Define operational life
6. Set capacity-to-activity units
7. Apply capacity factors, where relevant
8. Set Total Technology Annual Activity Lower Limits
9. Set Total Technology Annual Activity Upper Limits
Create and connect technologies, commodities, and emissions in the Configure model panel
Define Input and Output Activity Ratios
Enter demands and demand profiles
Specify capital and fixed costs

## Slide 6: Input approach 1: Sector by Sector (continued)
‹#›
The residual capacity can typically be added safely for all sectors at the end in a single step.
If the input data for a specific parameter causes the model to fail, it is recommended to roll back those changes and then re-enter the data incrementally (technology by technology, or at least in smaller groups) until the source of the error is identified.
Using this method, it may be the case that the results of intermediate steps are not sensible because key parameters driving the optimisation have not yet been entered. Still, it is good practice that the user checks the results and sees if they meet the expectations.
E.g. it is important to note that the costs of some technologies are determined further upstream in the system. For example, the cost of electricity used in households is derived from the power sector. To avoid technologies that rely on electricity appearing to have near-zero costs during intermediate runs, a temporary variable cost can be assigned, with the reminder to remove it once the upstream sectors are fully implemented.

## Slide 7: Input approach 2: All Data in One Go
‹#›
In this approach, the user builds all model sectors simultaneously. The order in which parameters are entered is identical to that of the previous approach.
Note: Even if the model runs successfully, quality assurance of the results must still be carried out on a sector-by-sector basis.

## Slide 8: Thank you
www.climatecompatiblegrowth.com