## Slide 1: Sustainable healthcare: Action for environmental protection
Launch the course

## Slide 2: The life cycle of a pharmaceutical product
Freshwater
Manufacturing plant
Hospital
Pharmacy
This module will describe the major sources of environmental impacts and risks to human health and the environment in the life cycle of a pharmaceutical, from manufacture to disposal.
There are four environments to explore: factory, hospital, pharmacy and freshwater.

## Slide 3: The life cycle of a pharmaceutical product
Navigate the slides using the arrows in the bottom corner.
Interact with the infographics to reveal information about the environmental impact caused by the production, use, and disposal of pharmaceuticals.
Continue onto the next slide to start at the manufacturing plant, or use the Menu button in the bottom right to return to the homepage at any time.
Sources are provided at the end of the file and at the end of each section.
Menu

## Slide 4: Interactive manufacturing plant
Actions for environmental sustainability
Go back
Let’s go!

## Slide 5: Pharmaceutical manufacturing
The manufacturing process of pharmaceuticals requires a lot of resources.
Energy and water are consumed in the making of pharmaceuticals, but perhaps most significantly, the quantity of waste created by the pharmaceutical industry is extremely high compared to other industries. Hundreds of times more waste than products are formed!
Pharmaceuticals are made from hazardous chemicals, meaning that safety precautions are needed to protect workers and avoid leaks into the environment (known as fugitive emissions).
Modern pharmaceutical production is performed to high health and safety standards.
Good Manufacturing Practice (GMP) is a legal code of practice to ensure medicines are high quality, safe and effective.
As well as minimising exposure to hazardous chemicals, new scientific techniques can be used to reduce the amount of chemicals needed and replace them with safer alternatives.
We shall now explore some of the actions being taken by pharmaceutical companies to protect workers and the environment.
R. A. Sheldon, Green Chem., 2023, 25, 1704-1728.
European Medicines Agency
Menu

## Slide 6: Explore the picture for information
There are 8 features to explore
Menu

## Slide 7: Explore the picture for information
Menu
Automation
There are 8 features to explore

## Slide 8
Menu
Automation
Automation replaces human workers with robotic apparatus. This can eliminate exposure to hazardous chemicals and speed up repetitive procedures.
Click to close

## Slide 9: Explore the picture for information
Menu
Flow chemistry
There are 8 features to explore

## Slide 10
Menu
Flow chemistry
‘Flow chemistry’ is an alternative to the standard ‘batch chemistry’. The ingredients are dissolved and mixed in tubes, passing over surfaces that accelerate the reaction (known as catalysts). The process is very efficient using the minimum amount of chemicals. The process can be increased in size by adding more or longer tubes!
Flow chemistry has met some resistance in the pharmaceutical industry because of the initial investment required and because it is more difficult to designate separate batches for quality control in case a medicine needs to be recalled.
Click to close

## Slide 11: Explore the picture for information
Menu
Batch reactor
There are 8 features to explore

## Slide 12
Menu
Batch reactor
A batch reactor is the standard way of performing large scale chemical reactions. All the ingredients are combined and stirred. The temperature is carefully controlled to maximise production.
Because the pharmaceutical ingredient is produced in batches, labelling and quality control is easy to monitor. Any batch found to contain impurities, or be associated with adverse patient effects, can be recalled and disposed of.
Batch reactors use a lot of energy and are not very efficient at mixing, resulting in slow reactions.
Click to close
The standard batch reactor uses heat to initiate reactions. This has been the standard approach since the alchemists of antiquity. There are modern alternatives including electrochemistry (where electrodes generate reactive ions) and mechanochemistry (using mechanical force to promote reactions) but neither have been adapted to mainstream medicinal chemistry.
Click to close

## Slide 13: Explore the picture for information
Menu
Storage
There are 8 features to explore

## Slide 14
Menu
Storage
Ideally the most hazardous substances can be replaced, but on balance, other factors such as cost, risk, and product purity need to be considered to have an optimised process. Hazardous chemicals must be stored safely to reduce the risk of exposure. Certain chemicals must not be stored in close proximity in case they react explosively with each other. Sealed cabinets are used to prevent the spread of fire.
Click to close

## Slide 15: Explore the picture for information
Menu
PPE
There are 8 features to explore

## Slide 16
Menu
PPE
Chemical ingredients present a risk to human health. Many pharmaceutical precursors are poisonous or have chronic health effects. Liquids can be split onto skin or into the eyes, while powders and vapours can be inhaled. The use of hazardous chemicals must be preceded by a risk assessment. It may be determined that some chemicals can be handled safely with gloves only, while others might need workers to use eye protection, respirators, or full hazmat suits. These are all examples of personal protective equipment (PPE).
Click to close

## Slide 17: Explore the picture for information
Menu
Online monitoring
There are 8 features to explore

## Slide 18
Menu
Online monitoring
Designing a safe process requires an expert knowledge of the chemicals and equipment involved. Maintaining the safety of an operational chemical process requires ‘Process Analytical Technology’ (PAT) because observation by eye does not always reveal very much. For example, sensors are used to monitor temperatures in case of a ‘runaway reaction’, where an unexpected spike in temperature accelerates the chemical reaction and risks a build up of energy, resulting in an explosion.
Click to close
Process Analytical Technology.

## Slide 19: Explore the picture for information
Menu
Transport
There are 8 features to explore

## Slide 20
Menu
Transport
Goods are routinely transported around the world. There are greenhouse gas emissions associated with transport, especially heavy freight. The impact is higher for medicines requiring cold storage. However, the climate change impact of the pharmaceutical manufacturing process is much higher, so much higher in fact that impact of transport is negligible!
Click to close
Climate change impact of an API by source.

## Slide 21: Explore the picture for information
Menu
Waste
There are 8 features to explore

## Slide 22
Menu
Waste
After the pharmaceutical product has been made, there is a significant amount of waste. This waste is likely to be hazardous and can only be legally disposed of by specialist waste management operators. This is an extra expense. More efficient manufacturing processes can minimise waste and reduce the amount of materials needed.
Click to close
The 12 principles of Green Chemistry promote waste reduction, energy reduction, and risk reduction. The biggest contributors to waste in pharmaceutical manufacturing are solvents – inert liquids used to mix and separate other chemicals. A lot of research is dedicated to finding safer, more sustainable solvents.
Click to close
12 Principles of Green Chemistry.
Safer solvents.

## Slide 23: Pharmaceutical manufacturing
Chemical manufacturing is catching up with other sectors (e.g. the automotive sector) with the introduction of more remote control and automation. Closed systems to minimise exposure to hazards and a stronger emphasis on how efficiency and waste correspond to costs is driving pharmaceutical manufacturing towards safer and more sustainable practices.
Additional reading:
  Green Chemistry The 12 principles of Green Chemistry
  Flow chemistry The Hitchhiker’s Guide to Flow Chemistry
  Electrochemistry Electrochemistry basics
  Mechanochemistry Fundamental Principles and Applications
  Safe and Sustainable by Design policy Commission Recommendation
  Runaway reactions Causes of accidents
  Automation in the chemical industry The smart factories of the future
  Greenhouse gas emissions Companies Products and packaging Transport and storage
  Waste Solvents E-factor (waste measurement)
  Energy Green technology
Menu

## Slide 24: Interactive hospital
Actions for environmental sustainability
Go back
Let’s go!

## Slide 25: Hospital
The day-to-day running of a hospital and other medical institutions has inherent impacts on the environment due to the size and location of the facility. The necessity for heating, electricity sourcing and use, number of staff and patients, and transport accessibility are all contributing to the overall environmental impact.
In-patient care utilises diverse treatments, each with benefits and disadvantages in terms of patient well-being, cost effectiveness, and environmental impact.
A fundamental principle in sustainable healthcare is not to compromise patient outcomes in order to reduce environmental impact. Human health remains the top priority, and sustainability targets balance environmental and socioeconomic factors.
The environmental impact of a hospital can be reduced in surprising ways without a negative effect on patients. Various interventions are summarised in the following infographic.
Menu

## Slide 26: Click on a room
Menu

## Slide 27: Reception and waiting area
Return
Lights on
Generic energy and impact reducing practices that apply to offices and other businesses are also applicable to hospitals.
In public areas (waiting room, café, shop) the recycling of waste, reusable items such as cutlery, careful stock taking of perishable items, choice of low impact food (e.g. vegetarian), heating and ventilation controls can all have a considerable effect.

## Slide 28: Reception and waiting area
Return
Lights off
Lighting is an example of electricity use. Modern lighting is energy efficient. Heating is a much greater consumer of energy.
Electricity can be acquired from different sources, depending on location. Renewable energy options are generally available, and large buildings can supplement energy grid supply with solar panels and wind turbines.

## Slide 29: Surgery theatre
Return
Anaesthetic gases can have an extremely high ‘global warming potential’, meaning their contribution to climate change is ranked much greater than carbon dioxide. Some anaesthesiologists are adapting their procedures in an attempt to reduce their carbon footprint. However, some experts maintain that the quantities of anaesthetic gases are too small to have a significant impact and their atmospheric chemistry is different to carbon dioxide making standard comparisons (with global warming potential) misleading.
Reusable equipment that can be safely sterilised reduces waste.
Some surgeries can be re-evaluated to local anaesthetic which also reduces costs.

## Slide 30: Patient ward
Return
Deprescribing is a good practice for some patients that have accumulated conditions and medicines. Review of prescriptions can lead to simplified treatment and lower consumption of pharmaceuticals.
Community support networks for earliest possible patient discharge reduces cases of prolonged hospital care.
Basic practices such as providing tablets in reusable cups instead of paper cups can have long term financial savings and reduce waste.
Some patients benefit from outdoor activities such as walking which can accelerate recovery and reduce the quantity (and impact) of pharmaceutical use.

## Slide 31: Waste and sterilisation area
Return
Certain tools and equipment can be sterilised and used again. The choice of materials the equipment is made from is clearly important; rather than being made for the lowest cost and then disposed, high quality, corrosion-resistant metal is needed for tools. Budgeting departments need to have long term planning for a circular economy at the heart of their procurement policies. Reusable equipment can be x50 more expensive than single-use items which represents a saving in the long run but that might not be clear in an annual budget.
Hospital waste is diverse and often hazardous. Clear disposal instructions and the provision of specialised waste bins can facilitate the safe disposal of hazardous waste and the recycling (or perhaps even reuse) of other items.

## Slide 32: Hospital
The Dutch healthcare system is responsible for the equivalent of 18 million tonnes of carbon dioxide emissions each year. The British healthcare system emits 25 million tonnes per year. Hospitals are at the heart of healthcare provision and account for a quarter of those healthcare emissions, while the necessary medicines and equipment account for a further third of emissions (UK data). Big policy changes are needed to make substantial reductions to the environmental impact of hospital infrastructure and in-patient care.
Additional reading:
  Dutch healthcare impact The environmental impact of the Dutch healthcare sector
  UK healthcare impact A carbon footprint assessment of the NHS
  Anaesthetic gases Science of climate change Climate impact
  Circular economy Strategies for sustainable healthcare
  Sustainable Quality Improvement Healthcare case studies
  Sustainable healthcare Book
  Hospital wastewater emissions Hospital emission sources for pharmaceuticals in municipal wastewater
Menu

## Slide 33: Interactive pharmacy
Actions for environmental sustainability
Go back
Let’s go!

## Slide 34: Pharmacy
Outpatient care often involves the prescription of medicine.
Doctors and pharmacists can be informed about the environmental impact of certain pharmaceuticals and told of low-impact alternatives through their professional training programs.
The information passed to patients about the environmental impact of medicines could also be better communicated in the same way health risks (e.g. side-effects) are.
A pharmacy also has sources of its own waste and carbon emissions, many of which are summarised in other online resources.
Online interactive pharmacy
Menu

## Slide 35: Click on a room for information
Menu

## Slide 36: Dispensary and shop front
Return
There are many options to make the shop front more sustainable. The choice of lights, climate control methods and settings, materials for shopping bags and displays all make a difference.
Staff can be encouraged to cycle or take public transport to work through a variety of subsidy schemes.

## Slide 37: Waste collection
Return
Hazardous waste can only be collected and processed by registered hazardous waste management companies. Incorrect labelling of waste has legal consequences.
Much of the packaging for supplies can be recycled. There has been a recent drive to minimise the auxiliary packaging of many products but there is a minimum safe level of packaging required for pharmaceuticals, although some medicines may have a few possible packaging options. European tablet medicines have gradually changed from being dispensed in bottles that could be recycled (either glass or a single plastic material) to blister packets that are a combination of foil and plastic and are not routinely recyclable. Novel recycling strategies are required for multiplayer packaging which may not be economically feasible.

## Slide 38: Chemical storage and preparation
Return
Secure and safe storage of medicines is very important to avoid theft but also to manage potential leaks and spillages that might consequently contaminate the water supply.
Well maintained stock records and cooperation between pharmacies and care homes etc. can help distribute medicines to avoid overstocking and risk exceeding use-by dates.

## Slide 39: Private consultation area
Return
In Sweden, there is a requirement for pharmacies to explain the environmental consequences of certain medicines (specifically diclofenac).This is typically achieved with signs and labels. Sweden also has priority list of medicines with the best ratio of price to environmental impact for treatments to common aliments.
Patients routinely have unused medicines at home that will need to be disposed of safely. Information on the risks to the environment of putting pharmaceutical products in the general waste can be communicated when being prescribed or collecting medicines. Company or government collections can be organised as part of ‘extended consumer responsibility’ obligations or for the safe recovery of syringes for example. The patient has an obligation to return or recycle packaging and unused medication.

## Slide 40: Bathroom
Return
Although carbon emissions from energy use (and waste reduction to a lesser extend) tends to dominate sustainability discussions, freshwater is a vital resource threatened by unsustainable practices.
The use of pharmaceutical products inevitably leads to the contamination of water, either by excretion of metabolites or from topical (skin) treatments being washed off. The influx of synthetic bioactive substances into freshwater has the potential for far reaching negative consequences on he environment. (This is explored in the final section.)
Leaks and dripping taps waste water. Prompt maintenance helps preserve clean water reserves.

## Slide 41: Storeroom/ staff room
Return
As with any office space, there is good practice that can be followed to save energy and water and prevent waste. A key facet to implementing environmentally sound practices is communication. Staff must be aware (and trained in some instances) about correct waste disposal and other sustainable workplace etiquette. Correct up to date signage is useful, and employee-led initiatives by motivated staff members can create a productive and supportive work environment with tangible cost benefits from reducing waste or saving energy.

## Slide 42: Pharmacy
The pharmacy, along with the doctors office, presents an opportunity to communicate the impact of pharmaceuticals to patients and encourage informed discussion about the available choices between prescribed medicines and their relative health benefits, but also their negative consequences. As a business premises, a pharmacy also has the opportunity to reduce its environmental impact through its choice of energy, waste management schemes, and other policies.
Additional reading:
  OECD guidance Pharmaceutical household waste Pharmaceutical residues in freshwater
  Take-back schemes Finnish Environment Institute
  Interactive pharmacy Online resource
  Sustainable pharmacy Medicines and the environment: challenges and solutions for sustainable pharmacy
  Packaging Shukla et al., The Journal of the Minerals, Metals and Materials Society, 2022, 74, 612.
Menu

## Slide 43: Pharmaceuticals in the environment
Actions for environmental sustainability
Go back
Let’s go!

## Slide 44: How do pharmaceuticals enter the environment?
It is a natural consequence that our bodies eliminate foreign (xenobiotic) substances via urine and faeces, including pharmaceuticals, most of which are bio-transformed into a range of metabolites before being excreted. This introduces chemicals into the environment via wastewater.
Incorrectly disposed medicines may also result in environmental contamination.
There are high profile examples of disastrous consequences for animals arising from pharmaceuticals in the environment.
Typically, the presence of pharmaceuticals in the environment is low enough not to be harmful to humans. However, the long-term effects of persistent exposure is not definitively known.
Water regulations are being updated as a response to pharmaceuticals detected in the environment, but at present there is no single speciality wastewater treatment to deal with this issue completely.
The environmental biodegradability of pharmaceuticals is also impacted by their molecular design.
A combination of innovations, information, and greater responsibility from stakeholders is required.
Menu

## Slide 45: Environment
Menu
There are 10 features to explore

## Slide 46: Environment
Menu
Industrial air emissions
There are 10 features to explore

## Slide 47: Factory
Menu
Energy and chemicals have associated emissions. Carbon dioxide contributes to climate change. Volatile organic compounds (VOCs) are frequently used in the chemical industries and if released into the atmosphere can cause smog and other forms of air pollution.
Click to close
Manufacturing plant

## Slide 48: Environment
Menu
Manufacturing
There are 10 features to explore

## Slide 49: Factory
Menu
Direct emissions of pharmaceuticals from a manufacturing plant are small. The primary concern in drug discovery and development is efficacy and safety but the development of biodegradable substances is becoming a more significant consideration. For example, ifosfamide is poorly biodegradable cytostatic drug. Further research discovered an analogue glufosfamide based on sugar molecules that is not only more biodegradable but is also more easily absorbed by the intestine.
Click to close
Manufacturing plant

## Slide 50: Environment
Menu
Hospital
There are 10 features to explore

## Slide 51: Hospital
Menu
Some medicine is consumed in hospitals (estimates vary from 1% to 20%) but the majority of medicines are consumed at home. Household waste water is the major source of pharmaceuticals in the environment.
Click to close
Hospital

## Slide 52: Environment
Menu
There are 10 features to explore
Crop protection

## Slide 53: Farm
Menu
Aquatic environments are also contaminated by chemicals originating from agriculture. These include fertiliser and pest control treatments.
Click to close
Farm

## Slide 54: Environment
Menu
Agriculture
There are 10 features to explore

## Slide 55: Farm
Menu
Diclofenac is a nonsteroidal anti-inflammatory drug approved for humans and animals. It is one of the most studied pharmaceuticals in the environment. Diclofenac is toxic to fish and reduces the thickness of bird shells. Vulture populations in South Asia were decimated by fatal diclofenac poisoning: cattle treated with diclofenac died and were scavenged by vultures who then suffered liver failure. Now alternatives to diclofenac are often prescribed, and in Sweden, pharmacies are obliged to show signs warning of the environmental damage of diclofenac. Aquaculture (e.g. fish farming) can be very damaging to the environment if medicine (via feed) is directly supplied to the water.
Click to close
Farm

## Slide 56: Environment
Menu
Direct industrial effluent
There are 10 features to explore

## Slide 57: River
Menu
In Europe, some industrial waste water is permitted to be discharged into rivers but pharmaceutical production waste is generally incinerated which destroys any chemicals. Losses of active pharmaceutical ingredients from manufacturing plant to the environment are minimal. In other regions, the quantity of pharmaceuticals entering the environment via industrial wastewater can be more significant.
Many pharmaceuticals and the protective coatings on manufacturing equipment meet the definition of ‘polyfluoroalkyl substances’ (PFAS, fluorine containing organic molecules). PFAS are persistent and mobile in the environment, causing widespread contamination.
Click to close
River

## Slide 58: Environment
Menu
Municipal effluent
There are 10 features to explore

## Slide 59: River
Menu
The waste water from households is the primary source of pharmaceuticals in the environment. The constant flow of chemicals in our waste water maintains low concentrations of bioactive substances in freshwater. The effects of many APIs and their metabolites when present at persistently low concentrations are not fully known, but reduced growth and behaviour changes to fish have been reported. Endocrine active substances are known to cause hormone disruption to aquatic organisms (including fish and frogs). As of 2020, traces of 992 APIs have been found in 89 countries. This is projected to increase by 20% in the next 20 years. Contrast agents and psychotropic drugs are amongst the most common APIs found in drinking water (not metabolised or degraded).
Click to close
River

## Slide 60: Environment
Menu
Wastewater treatment
There are 10 features to explore

## Slide 61: Water treatment
Menu
Most pharmaceuticals entering the environment do so by passing through a wastewater treatment plant. Typical municipal waste water treatment is not designed to remove the diversity and low concentration of chemicals arising from medicine use. On average about a third of a given API passes through the treatment plant and into the environment (but some chemicals like the antibiotic trimethoprim are virtually unaffected). The pharmaceuticals that are captured (e.g. in sewage sludge) may also get introduced into the environment. Sewage sludge may be spread onto agricultural land as a fertiliser, or sent to landfill. New regulatory proposals are introducing requirements to remove pharmaceuticals from wastewater, to be paid for by the manufacturers. Specialist treatments include activated carbon filtration and ozone to degrade chemical pollutants.
Click to close
Wastewater treatment plant

## Slide 62: Environment
Menu
Household medicine use
There are 10 features to explore

## Slide 63: Home
Menu
Active pharmaceutical ingredients (APIs) are metabolised in the body and excreted. This is a common source of chemicals in the environment entering via our wastewater systems. In addition, a large quantity of medicines go unused and are put into household waste. It was estimated to be over 17 million kilograms a year in France alone. Sweden, Portugal and Netherlands have high rates of returning unused medicines to pharmacies, but most often across Europe they are put into the household waste. If this waste is landfilled then pharmaceuticals can leech into the environment.
Click to close
Domestic residence

## Slide 64: Environment
Menu
Veterinary medicine
There are 10 features to explore

## Slide 65: Home
Menu
Veterinary medicines (e.g. endectocides such as worming treatments and wash off lice treatments), and their metabolites, also enter the environment via similar routes to human medicine. Our understanding of their ecological impact is limited by a lack of monitoring and toxicological data (especially for metabolites) but it is generally thought that pets are a minor source of pharmaceuticals in the environment.
Click to close
Domestic residence

## Slide 66: Positive actions
Collection points and take back schemes would reduce the quantity of APIs entering the environment.
A sustainable pharmacy supply chain also requires new innovative and readily biodegradable APIs, innovative low-impact dosage forms, deprescribing where appropriate and alternative therapies to pharmacological interventions (e.g. diet, exercise).
Specialised wastewater treatments help process and degrade APIs before they enter the environment. The Urban Wastewater Directive of 2024 requires that wastewater treatments will be mostly paid for by the companies that caused the pollution.
Additional reading:
  Climate change Sustainable Healthcare (book)
  Household waste Pharmaceutical household waste
  OECD guidance Pharmaceutical residues in freshwater
  Veterinary medicines Environmental risks
  Medicines in the environment 1. Umweltaspekte von Humanarzneimitteln in der medizinischen und pharmazeutischen Praxis (German)
              2. Arzneimittelwirkstoffe im Wasserkreislauf (German)
              3. Geneesmiddelen en milieu (Dutch)
              4. Medicines and the environment: challenges and solutions for sustainable pharmacy (book)
Menu

## Slide 67: Credits
Go back
Let’s go!

## Slide 68: Sources
Specific references are given on the corresponding slides.
All the images and diagrams in this file are original artwork created with Microsoft templates and models.
Manufacturing references:
  Green Chemistry The 12 principles of Green Chemistry
  Flow chemistry The Hitchhiker’s Guide to Flow Chemistry
  Electrochemistry Electrochemistry basics
  Mechanochemistry Fundamental Principles and Applications
  Safe and Sustainable by Design policy Commission Recommendation
  Runaway reactions Causes of accidents
  Automation in the chemical industry The smart factories of the future
  Greenhouse gas emissions Companies Products and packaging Transport and storage
  Waste Solvents E-factor (waste measurement)
  Energy Green technology
Menu

## Slide 69: Sources
Hospital references:
  Dutch healthcare impact The environmental impact of the Dutch healthcare sector
  UK healthcare impact A carbon footprint assessment of the NHS
  Anaesthetic gases Science of climate change Climate impact
  Circular economy Strategies for sustainable healthcare
  Sustainable Quality Improvement Healthcare case studies
  Sustainable healthcare Book
  Hospital wastewater emissions Hospital emission sources for pharmaceuticals in municipal wastewater
Pharmacy references:
  OEDC guidance Pharmaceutical household waste Pharmaceutical residues in freshwater
  Interactive pharmacy Online resource
  Take-back schemes Finnish Environment Institute
  Sustainable pharmacy Medicines and the environment: challenges and solutions for sustainable pharmacy
  Packaging Shukla et al., The Journal of the Minerals, Metals and Materials Society, 2022, 74, 612.
Menu

## Slide 70: Sources
Environment references:
  Climate change Sustainable Healthcare (book)
  Household waste Pharmaceutical household waste
  OECD guidance Pharmaceutical residues in freshwater
  Circular economy Pharmaceutical value chain
  Packaging Recyclable packaging
  Veterinary medicines Environmental risks
  Medicines in the environment 1. Umweltaspekte von Humanarzneimitteln in der medizinischen und pharmazeutischen Praxis (German)
              2. Arzneimittelwirkstoffe im Wasserkreislauf (German)
              3. Geneesmiddelen en milieu (Dutch)
              Regulation:
                Pharmaceuticals in the environment European Union Strategic Approach to Pharmaceuticals in the Environment
                Pharmaceutical strategy for Europe European Commission
Menu

## Slide 71: Acknowledgements
This educational resource was produced by the scientists, researchers and policy advisors in the TRANSPHARM consortium.
Menu

## Slide 72: Instructor guidance
The normal slideshow functions have been disabled. The default navigation options are the buttons in the bottom right. In some infographics a map can be clicked to navigate back to the sub-section menu.
To use this powerpoint in presenter mode:
‘Slide show’ > ‘Set up slide show’ > click to change ‘Show type’ to ‘Presented by a speaker’
However, the slide deck is not easily navigated in the conventional manner because of the way the infographics are designed from multiple slides.
You are free to share, use, and adapt this content as you see fit with appropriate attribution without other restriction. Suggested credit:
This content has been supplied by TRANSPHARM. TRANSPHARM has received funding from the European Union’s Horizon Europe research and innovation program under grant agreement N° 101057816. https://transforming-pharma.eu/
Menu

## Slide 73: We hope you enjoyed this resource. Have you seen our other content?
Relaunch this course