## Slide 1
SELF-PACED PRE-COURSE · MODULE 2
Geospatial Fundamentals
for Energy Access
Vector, raster, coordinate reference systems, file formats, and data sources are the vocabulary every energy access dataset maps onto.
Geospatial Data Management for Energy Access, Planning and Modelling
Commissioned by SEforALL · Maintained & updated by Kartoza · Hosted by CCG
ESTIMATED TIME
60 minutes

## Slide 2
MODULE 2 · GEOSPATIAL FUNDAMENTALS
How This Module Is Organised
Seven units build the vocabulary you need before Week 1. Work through them in order; each one assumes the last.
1
Why Geospatial Data Matters for Energy Access
Connecting spatial data to real electrification decisions
8 min
2
Vector and Raster Data Models
The two fundamental ways spatial data is structured
10 min
3
File Formats You Will Encounter
GeoPackage, GeoTIFF, COG, Shapefile, GeoJSON, CSV
8 min
4
Coordinate Reference Systems
Why CRS mismatches are GIS's most common error
9 min
5
Key Data Sources for Energy Access Planning
Where population, grid, resource and boundary data come from
9 min
6
The Core GIS Workflow
From raw data to a decision, in five governed steps
8 min
7
Common Data Governance Challenges
The problems your governance plan will need to solve
8 min
Each unit closes with a reference slide, five or more sources you can return to while writing your governance plan.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
2

## Slide 3
1
SECTION 1
Why Geospatial Data Matters for Energy Access
Every electrification decision is a spatial decision. This unit shows you why.
Module 2: Geospatial Fundamentals

## Slide 4
UNIT 1 · APPLIED FOUNDATIONS
The Energy Access Data Challenge
Closing the electrification gap depends on knowing exactly where the gap is.
685M
people still without access to electricity worldwide (2022)
91%
of the global population had access to electricity in 2022
2030
The SDG7 deadline for universal, affordable, reliable energy
300+
Geospatial datasets are typically needed per national electrification plan
Geospatial data sits at the centre of every decision in the electrification planning process, from identifying unserved communities to sizing grid extensions and modelling off-grid solar potential. The quality of that data, and the systems used to manage it, directly determine whether plans succeed or fail in the field.
Source: IEA, IRENA, UNSD, World Bank, and WHO (2025) Tracking SDG7: The Energy Progress Report 2025.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
4

## Slide 5
UNIT 1 · APPLIED FOUNDATIONS
Four Ways Geospatial Data Drives Energy Decisions
You covered pieces of this in earlier reading. Here is how they connect.
🏘
Locating people
Population data (WorldPop, census) shows where people live and how many lack access to electricity, but only at a specific location. Without coordinates, a demand estimate cannot be mapped to a community.
⚡
Mapping infrastructure
Transmission lines, substations, and distribution networks are spatial objects with exact geometry. You cannot plan grid extension, estimate connection cost, or identify the nearest feeder without them.
☀
Assessing resource
Solar irradiance, wind speed and hydro potential vary continuously across space. Raster datasets capture that variation, cell by cell, at the resolution your analysis needs.
🎯
Targeting investment
Least-cost electrification models (e.g., OnSSET) calculate where grid, mini-grid, and solar home systems are most cost-effective, a purely spatial optimisation across millions of raster cells.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
5

## Slide 6
SECTION 1 · REFERENCES
Unit 1 Reference List
1
IEA, IRENA, UNSD, World Bank and WHO (2025) Tracking SDG7: The Energy Progress Report 2025. Washington, DC: World Bank.
2
Mentis, D., Howells, M., Rogner, H., Korkovelos, A., Arderne, C., Zepeda, E., Siyal, S.H., Taliotis, C., Bazilian, M., De Roo, A., Tanvez, Y., Oudalov, A. and Scholtz, E. (2017) 'Lighting the world: the first application of an open source, spatial electrification tool (OnSSET) on Sub-Saharan Africa', Environmental Research Letters, 12(8), 085003.
3
Sustainable Energy for All (2024) Energy Access Explorer: A Geospatial Planning Platform. Vienna: SEforALL. Available at: https://www.energyaccessexplorer.org (Accessed: 14 July 2026).
4
Arderne, C., Zorn, C., Nicolas, C. and Koks, E.E. (2020) 'Predictive mapping of the global power system using open data', Scientific Data, 7, article 19.
5
World Bank / ESMAP (2023) Global Electrification Platform: Geospatial Least-Cost Electrification Planning. Washington, DC: World Bank. Available at: https://electrifynow.energydata.info (Accessed: 14 July 2026).
6
United Nations (2015) Transforming Our World: The 2030 Agenda for Sustainable Development, A/RES/70/1. New York: United Nations General Assembly.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
6

## Slide 7
2
SECTION 2
Vector and Raster Data Models
The two fundamental ways spatial data is structured, and when each one applies.
Module 2: Geospatial Fundamentals

## Slide 8
UNIT 2 · DATA MODELS
Vector Data - Points, Lines, Polygons
Discrete geographic features with exact geometry and an attribute table row per feature.
Point
A single coordinate pair (x, y). One row per feature.
Energy examples: Village and settlement locations, substations, transformers, solar panel installations, survey collection points.
Line (LineString)
A connected sequence of coordinates forming a linear feature. The hardest geometry to keep topologically clean.
Energy examples: Transmission lines, distribution feeders, road networks, river channels.
Polygon
A closed shape defining an area. Must not overlap or leave gaps when representing a complete partition.
Energy examples: Administrative boundaries, mini-grid service areas, electrified districts, solar farm footprints.
GEOMETRY TYPES
Point
Line
Polygon
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
8

## Slide 9
UNIT 2 · DATA MODELS
Raster Data - A Grid of Cells
A regular grid of pixels, each storing a numeric value. Extent is defined by origin, cell size and row/column count.
Resolution
The size of one cell on the ground. WorldPop: 100m. Global Solar Atlas GHI: 1km. Sentinel-2: 10m. Higher resolution = smaller cells = larger files.
Band
A single layer of values. A population raster typically has one band (count). A satellite image has several (red, green, blue, near-infrared).
Nodata value
A sentinel value (often -9999) marking a cell with no valid data. Treating nodata as zero is a common, dangerous analysis error.
Resampling
Reprojecting a raster changes cell alignment and values. Use Nearest Neighbour for categorical data; Bilinear or Cubic for continuous data.
A CONTINUOUS SURFACE, ONE VALUE PER CELL - e.g., population density
100m × 100m
245 people
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
9

## Slide 10
UNIT 2 · DATA MODELS
Choosing Vector or Raster - and Moving Between Them
The same real-world phenomenon can sometimes be modelled either way. The right choice depends on the question you are asking.
Choose VECTOR when…
• Features have distinct, countable boundaries (a substation, a district)
• You need exact topology, shared boundaries, connectivity, and network routing
• Attribute-rich queries matter ("show all feeders installed after 2019")
• Precise area or length measurement is required for individual features
Choose RASTER when…
• The phenomenon varies continuously across space (irradiance, elevation)
• You are running cell-by-cell modelling (least-cost paths, suitability surfaces)
• The source is imagery or a sensor product (satellite bands, DEMs)
• You need fast map algebra across a large area rather than per-feature detail
In practice, electrification planning uses both together. A raster least-cost surface is generated, then converted to vector polygons to report results by administrative area.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
10

## Slide 11
SECTION 2 · REFERENCES
Unit 2 Reference List
1
Longley, P.A., Goodchild, M.F., Maguire, D.J. and Rhind, D.W. (2015) Geographic Information Science and Systems. 4th edn. Hoboken, NJ: Wiley.
2
Open Geospatial Consortium (2011) OGC Simple Feature Access - Part 1: Common Architecture, version 1.2.1. Wayland, MA: OGC.
3
Zanaga, D., Van De Kerchove, R., De Keersmaecker, W., Souverijns, N., Brockmann, C., Quast, R., Wevers, J., Grosu, A., Paccini, A., Vergnaud, S., Cartus, O., Santoro, M., Fritz, S., Georgieva, I., Lesiv, M., Carter, S., Herold, M., Li, L., Tsendbazar, N.E., Ramoino, F. and Arino, O. (2021) ESA WorldCover 10 m 2020 v100. European Space Agency.
4
Lloyd, C.T., Sorichetta, A. and Tatem, A.J. (2017) 'High resolution global gridded data for use in population studies', Scientific Data, 4, 170001.
5
QGIS.org (2026) QGIS Desktop User Guide - Working with Vector and Raster Data. QGIS Documentation. Available at: https://docs.qgis.org (Accessed: 14 July 2026).
6
NASA Jet Propulsion Laboratory / ESA Copernicus Programme (2021) Copernicus DEM: Global Digital Elevation Model. Available at: https://spacedata.copernicus.eu (Accessed: 14 July 2026).
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
11

## Slide 12
3
SECTION 3
File Formats You Will Encounter
Format choice is a governance decision; it determines who can use your data and what gets lost along the way.
Module 2: Geospatial Fundamentals

## Slide 13
UNIT 3 · FILE FORMATS
Knowing the Landscape
Six formats cover almost everything you will receive, create, or share in this programme.
PREFERRED
GeoPackage (.gpkg)
An SQLite container holding multiple vector and raster layers. The modern standard for sharing and storing spatial datasets. Use this as your default.
STANDARD
GeoTIFF (.tif)
Raster format with georeferencing embedded in the file. Works with every GIS tool. Use for elevation, solar resource, and satellite imagery.
MODERN
Cloud Optimised GeoTIFF (COG)
A GeoTIFF structured for HTTP range requests, so QGIS can stream it without a full download. Increasingly the default on major data platforms.
LEGACY
Shapefile (.shp + companions)
Still common but outdated: 10-character field name limit, no datetime type, 3-6 companion files required. Accept from others; never create new ones.
WEB USE
GeoJSON (.geojson)
Text-based vector format, good for web maps and APIs. Not suited to large datasets. Often the format returned directly by online APIs.
COMMON
CSV with coordinates (.csv)
Tabular data with lat/lon columns. Widely used for survey data. Import into QGIS and export to GeoPackage before any spatial analysis.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
13

## Slide 14
UNIT 3 · FILE FORMATS
The Format Decision Tree
Apply this decision logic to every dataset you receive or create (when working with QGIS) from the pre-course exercises onward.
?
Receiving vector data?
Save as a GeoPackage layer immediately. Archive the shapefile. Keep the GeoPackage as your working copy.
?
Receiving raster data?
Accept GeoTIFF or COG. Avoid ERDAS .img or ESRI Grid convert on receipt. Note resolution and CRS in your data inventory.
?
Sharing data externally?
For partners: GeoPackage or GeoTIFF. For web maps: GeoJSON (small) or OGC WFS/WMS. Never share shapefiles if avoidable.
?
Survey or tabular data?
Import CSV via 'Add Delimited Text Layer'. Verify CRS (usually EPSG:4326). Export to GeoPackage; discard the original CSV.
RULE
One .gpkg file per exercise. All layers inside. Nothing else in the project folder except the .qgs project file.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
14

## Slide 15
SECTION 3 · REFERENCES
Unit 3 Reference List
1
Open Geospatial Consortium (2022) OGC GeoPackage Encoding Standard, version 1.3.1. Wayland, MA: OGC.
2
Cloud Native Geospatial Foundation (2023) Cloud Optimized GeoTIFF Specification. Available at: https://cogeo.org (Accessed: 14 July 2026).
3
Butler, H., Daly, M., Doyle, A., Gillies, S., Hagen, S. and Schaub, T. (2016) The GeoJSON Format, RFC 7946. Fremont, CA: Internet Engineering Task Force.
4
Environmental Systems Research Institute (1998) ESRI Shapefile Technical Description, white paper J-7855. Redlands, CA: Esri.
5
FlatGeobuf Contributors (2024) FlatGeobuf Format Specification. Available at: https://flatgeobuf.org (Accessed: 14 July 2026).
6
Radiant Earth Foundation (2023) SpatioTemporal Asset Catalog (STAC) Specification, version 1.0.0. Available at: https://stacspec.org (Accessed: 14 July 2026).
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
15

## Slide 16
4
SECTION 4
Coordinate Reference Systems
Mismatched CRS is the single most common source of incorrect spatial analysis, and it is almost always invisible until the result is wrong.
Module 2: Geospatial Fundamentals

## Slide 17
UNIT 4 · COORDINATE REFERENCE SYSTEMS
From a Curved Earth to a Flat Map
A CRS defines how positions on the Earth's curved surface become flat coordinates you can measure.
Geographic CRS
degrees (lat / lon)
PROJECTION
Projected CRS
metres (UTM zones)
The rule this programme follows: store in EPSG:4326, analyse in your regional UTM zone.
EPSG:4326
WGS84 Geographic
Degrees. Every GPS device outputs this. Use for data exchange, storage of global datasets, and web services. Do not use for measuring distances or areas.
UTM Zones
Projected
Metres. Use for area, distance, and buffer calculations. Choose the correct zone for your country - e.g., UTM Zone 36S for South Africa, 35S for Zambia, 37S for Kenya.
EPSG:3857
Web Mercator
Used by Google Maps and OpenStreetMap tiles. Do not use for analysis area distortion is extreme away from the equator. Only use for display against web basemaps.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
17

## Slide 18
UNIT 4 · COORDINATE REFERENCE SYSTEMS
Finding the Right UTM Zone for Your Country
Each UTM zone covers 6° of longitude. The zone number plus hemisphere (N or S) together define the EPSG code.
Zone 34
Zone 35
Zambia
Zone 36
South Africa · Tanzania
Zone 37
Kenya · Ethiopia
Zone 38
6° of longitude per zone, numbered west to east - 'S' or 'N' marks the hemisphere
Country
EPSG code
Zone
South Africa (eastern)
EPSG:32736
WGS 84 / UTM Zone 36S
Kenya
EPSG:32637
WGS 84 / UTM Zone 37S (or 37N north of equator)
Zambia
EPSG:32735
WGS 84 / UTM Zone 35S
Ethiopia
EPSG:32637
WGS 84 / UTM Zone 37N
Tanzania
EPSG:32736
WGS 84 / UTM Zone 36S (most of country)
Ghana
EPSG:32630
WGS 84 / UTM Zone 30N
Find yours: spatialreference.org or epsg.io search your country name. Ask: is my study area east or west of the prime meridian? Above or below the equator?
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
18

## Slide 19
SECTION 4 · REFERENCES
Unit 4 Reference List
1
Snyder, J.P. (1987) Map Projections: A Working Manual, USGS Professional Paper 1395. Washington, DC: United States Geological Survey.
2
International Association of Oil & Gas Producers (2026) EPSG Geodetic Parameter Dataset. Available at: https://epsg.org (Accessed: 14 July 2026).
3
International Organization for Standardization (2019) ISO 19111:2019 Geographic Information - Referencing by Coordinates. Geneva: ISO.
4
National Geospatial-Intelligence Agency (2014) The Universal Grids and the Transverse Mercator and Polar Stereographic Map Projections, NGA.SIG.0012_2.0.0. Springfield, VA: NGA.
5
QGIS.org (2026) QGIS Desktop User Guide - Coordinate Reference Systems. QGIS Documentation. Available at: https://docs.qgis.org (Accessed: 14 July 2026).
6
Kartoza (2023) Working with Coordinate Reference Systems in QGIS: A Practical Guide. Cape Town: Kartoza GIS Academy.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
19

## Slide 20
5
SECTION 5
Key Data Sources for Energy Access Planning
Understanding where data comes from helps you assess its quality and fitness for use.
Module 2: Geospatial Fundamentals

## Slide 21
UNIT 5 · DATA SOURCES
The Data Source Directory
Six categories cover most datasets you will work with across this programme.
🏘
Population & settlements
WorldPop (100m raster), GHSL, national census, HRSL (Meta AI / CIESIN)
⚡
Grid infrastructure
OpenStreetMap, gridfinder (satellite-derived), national utility shapefiles, USAID/KfW project data
☀
Solar & energy resource
Global Solar Atlas (ESMAP/Solargis), NASA POWER, PVGIS, GHI/DNI rasters
▢
Administrative boundaries
GADM, geoBoundaries, national mapping agencies, OCHA COD boundaries
🌍
Land cover & terrain
ESA WorldCover, SRTM/Copernicus DEM, MODIS, Sentinel satellite data
📊
Socioeconomic & demand
DHS surveys, World Bank Open Data, IMF, national household surveys
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
21

## Slide 22
UNIT 5 · DATA SOURCES
Assessing Source Quality and Fitness for Use
Not every dataset that fits your study area is fit for your purpose. Ask these six questions before you rely on any source.
1
Currency
When was it last updated? A 2015 settlement layer may miss five years of electrification and urban growth.
2
Resolution
Does the spatial detail match your decision? A 1km solar raster cannot site an individual mini-grid.
3
Lineage
Is the collection and processing method documented? Undocumented data cannot be trusted or reproduced.
4
Completeness
Are there gaps, and are they random or systematic? OSM coverage is often thinner in rural areas.
5
Accuracy
Has it been validated against ground truth? Look for a stated confidence interval or accuracy statement.
6
Licence
Can you legally use, adapt, and redistribute it? Check CC BY, ODbL, and government open-data terms.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
22

## Slide 23
SECTION 5 · REFERENCES
Unit 5 Reference List
1
WorldPop (2020) Global High Resolution Population Denominators Project. Southampton: University of Southampton. Available at: https://www.worldpop.org (Accessed: 14 July 2026).
2
Runfola, D., Anderson, A., Baier, H., Crittenden, M., Dowker, E., Fuhrig, S. et al. (2020) 'geoBoundaries: A global database of political administrative boundaries', PLOS ONE, 15(4), e0231866.
3
GADM (2022) GADM Database of Global Administrative Areas, version 4.1. Available at: https://gadm.org (Accessed: 14 July 2026).
4
Solargis / World Bank Group - ESMAP (2024) Global Solar Atlas 2.0. Washington, DC: World Bank. Available at: https://globalsolaratlas.info (Accessed: 14 July 2026).
5
Arderne, C., Zorn, C., Nicolas, C. and Koks, E.E. (2020) 'Predictive mapping of the global power system using open data', Scientific Data, 7, article 19.
6
UN Office for the Coordination of Humanitarian Affairs (2026) Humanitarian Data Exchange (HDX) Data Catalogue. Geneva: UN OCHA. Available at: https://data.humdata.org (Accessed: 14 July 2026).
7
ICF / The DHS Program (2026) Demographic and Health Surveys: Spatial Data Repository. Rockville, MD: USAID. Available at: https://spatialdata.dhsprogram.com (Accessed: 14 July 2026).
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
23

## Slide 24
6
SECTION 6
The Core GIS Workflow
Every geospatial project follows a similar sequence. Seeing the whole flow shows you where governance fits.
Module 2: Geospatial Fundamentals

## Slide 25
UNIT 6 · THE GIS WORKFLOW
Five Steps, From Raw Data to Decision
Data governance applies at every stage of this workflow, ensuring the right data is collected, stored, and processed correctly, every time.
1
Acquire
Download, receive, or collect raw datasets from sources identified in your data inventory.
2
Clean & Validate
Fix topology errors, fill gaps, standardise field names, and check geometry accuracy.
3
Transform
Reproject to a consistent CRS, convert formats, and join attribute tables.
4
Integrate
Load all cleaned layers into a single database GeoPackage or PostGIS.
5
Analyse
Run spatial queries, overlays, buffers, zonal statistics, and electrification models.
Where governance lives: your Data Governance Plan documents roles for each step above who acquires, who validates, who owns the integrated database, and what quality standard analysis must meet before it informs a decision.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
25

## Slide 26
SECTION 6 · REFERENCES
Unit 6 Reference List
1
Longley, P.A., Goodchild, M.F., Maguire, D.J. and Rhind, D.W. (2015) Geographic Information Science and Systems. 4th edn. Hoboken, NJ: Wiley.
2
Wilkinson, M.D., Dumontier, M., Aalbersberg, I.J., Appleton, G., Axton, M., Baak, A. et al. (2016) 'The FAIR Guiding Principles for scientific data management and stewardship', Scientific Data, 3, 160018.
3
International Organization for Standardization (2013) ISO 19157:2013 Geographic Information - Data Quality. Geneva: ISO.
4
QGIS.org (2026) QGIS Desktop User Guide - Processing Toolbox. QGIS Documentation. Available at: https://docs.qgis.org (Accessed: 14 July 2026).
5
Kartoza (2024) GIS Academy: The GeoPackage-First Database Strategy. Cape Town: Kartoza. Available at: https://kartoza.com (Accessed: 14 July 2026).
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access — Pre-Course
26

## Slide 27
7
SECTION 7
Common Data Governance Challenges
Understanding these challenges now will help you frame the governance work ahead.
Module 2: Geospatial Fundamentals

## Slide 28
UNIT 7 · DATA GOVERNANCE
Eight Recurring Challenges in Energy Access Data
Every one of these is a data governance problem solvable with clear policies, roles, and documented processes.
1
Inconsistent coordinate systems across datasets from different government agencies
2
Outdated grid infrastructure data that does not reflect recent electrification projects
3
Population rasters at a different spatial resolution than your survey data
4
Village shapefiles digitised from paper maps, with unknown positional accuracy
5
Solar resource rasters without documentation of sensor, date, or processing method
6
Duplicate datasets circulating within an organisation under different filenames
7
Datasets locked in proprietary formats ArcGIS personal geodatabases, .mdb files
8
No clear owner for nationally important layers nobody updates the grid shapefile
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
28

## Slide 29
UNIT 7 · DATA GOVERNANCE
From Challenge to Governance Plan
Every challenge on the previous slide maps to a section of the Data Governance Plan you will build across this programme.
Inconsistent CRS · duplicate datasets
Data Inventory
No clear data owner
Roles & RACI
Undocumented accuracy · unknown lineage
Quality Standards
Proprietary formats · no catalogue
Metadata & SDI
Outdated infrastructure layers
Roadmap
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
29

## Slide 30
SECTION 7 · REFERENCES
Unit 7 Reference List
1
International Organization for Standardization (2014) ISO 19115-1:2014 Geographic Information - Metadata - Part 1: Fundamentals. Geneva: ISO.
2
Wilkinson, M.D., Dumontier, M., Aalbersberg, I.J., Appleton, G., Axton, M., Baak, A. et al. (2016) 'The FAIR Guiding Principles for scientific data management and stewardship', Scientific Data, 3, 160018.
3
Republic of South Africa (2013) Protection of Personal Information Act, No. 4 of 2013. Pretoria: Government Gazette.
4
World Resources Institute (2022) Open Data for Energy Access: A Governance Framework for Practitioners. Washington, DC: WRI.
5
Group on Earth Observations (2023) Spatial Data Infrastructure Principles for Sustainable Development. Geneva: GEO Secretariat.
6
European Union (2007) Directive 2007/2/EC (INSPIRE): Establishing an Infrastructure for Spatial Information in the European Community. Brussels: Official Journal of the European Union.
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
30

## Slide 31
MODULE 2
Key Takeaways
You should now be able to:
✓
Explain the difference between vector (point, line, polygon) and raster data, with energy examples
✓
Identify recommended file formats for vector and raster data: GeoPackage, GeoTIFF, COG
✓
Explain why coordinate reference systems matter, and when to use geographic vs projected CRS
✓
Name at least five key data sources used in energy access planning, by category
✓
Describe the five-step GIS workflow from acquisition to analysis, and where governance fits
✓
Articulate at least three common data quality challenges in energy access contexts
Next: Module 3 - Data Aggregators, Platforms & Data Quality · Geospatial Data Management for Energy Access - Pre-Course
Module 2 complete · Geospatial Data Management for Energy Access
31

## Slide 32
CREDITS & ATTRIBUTION
How This Material Came Together
This module is part of an open educational programme. The organisations below hold distinct roles in its creation, maintenance, and delivery.
COMMISSIONED BY
Sustainable Energy for All - commissioning body.
MAINTAINED & UPDATED BY
Kartoza - open-source geospatial solutions; content updates and delivery.
HOSTED BY
Climate Compatible Growth - hosting and platform delivery.
Geospatial Data Management for Energy Access · Pre-Course · Module 2
Module 2: Geospatial Fundamentals · Geospatial Data Management for Energy Access - Pre-Course
32