## Slide 1
Lesson 1: Introduction to Geo-X
Geo-X training course
Notes: Welcome to the Geo-X training course. This is Lesson 1: Introduction to Geo-X, the first of six lessons in this course. The Geo-X tool has been developed under the Strategic Hydrogen Integration for Effective Low-carbon Development (SHIELD) project, and this course has been made available through the Open University as part of the Climate Compatible Growth course collection. By the end of this lesson, you will have a clear understanding of what Geo-X is, the types of questions it can help you answer, and how it fits within the broader landscape of energy modelling tools. In later lessons, you will learn how to install and run the tool yourself. For now, let us begin with the big picture.

## Slide 2: Learning outcomes
By the end of this lesson, you will:
Understand what Geo-X is and how it differs from other modelling tools.
Describe the main applications of Geo-X.
Identify the key research and policy questions that Geo-X can address.
2
Notes: By the end of this lesson, you will be able to explain what Geo-X is and how it differs from other modelling tools you may already be familiar with. You will be able to describe the main commodities and analyses supported by Geo-X, and identify the research and policy questions it can help address. These three outcomes will guide the structure of everything that follows.

## Slide 3
Table of contents
The policy problem
Why does geography matter for green commodities?
How does Geo-X differ from other tools?
Introduction to Geo-X
What Geo-X is not
What you will learn in this course
What is Geo-X
Notes: Here is an overview of the topics we will cover in this lesson. Let’s begin with the policy problem: why geography matters when thinking about green commodities, and then we will introduce Geo-X and explain how it compares to more systemic modelling tools.

## Slide 4
Why does geography matter for green commodities?
Demand location
Renewable resources
Demand locations are often determined by existing industrial facilities or strategic export ambitions.
Green commodities are produced using technologies that generate no direct CO₂ emissions.
Modern energy systems integrate:
  Solar photovoltaics (PV)
  Wind turbines (onshore/offshore)
  Geothermal
  Hydropower
A key trade-off: renewable-resource availability versus distance to demand.
Ukraine example:
Notes: The starting point for understanding Geo-X is a simple but important observation: where you produce a green commodity matters enormously. Green commodities – such as green hydrogen and green ammonia – are produced using renewable energy sources like solar, wind, geothermal, and hydropower. These resources are not evenly distributed. Some regions have high solar irradiation; others have strong and consistent wind. At the same time, demand centres are often located far from where the best renewable resources exist – either because of legacy industrial infrastructure or because a country wants to produce for export. This creates a fundamental trade-off: the best production sites may not be the closest to demand. Geo-X is designed precisely to navigate that trade-off, by estimating the full cost of production and delivery across an entire territory.
Map note: the map shows the baseline levelised cost of hydrogen (LCOH), in EUR per kg, for Ukraine.
P95 = 95th percentile. The colour scale is capped at P95, so the most expensive 5% of locations are all drawn in the same darkest shade. This prevents a small number of extreme outliers from flattening the colour contrast across the rest of the country.
LCOH = levelised cost of hydrogen: the discounted lifetime cost of production and delivery divided by the discounted lifetime volume of hydrogen delivered.

## Slide 5
What is Geo-X?
Geo-X is an open-source geospatial modelling framework for estimating the cost of producing and delivering low-carbon commodities, such as green hydrogen and green ammonia, from potential production sites to specified demand locations.
Geolocation
Optimised technology mix
Levelised cost
PHOTO: NASA/Unsplash
LCOH =
NPV of lifetime costs
NPV of lifetime output (kg H₂ or kg NH₃)
PHOTO: Andreas Gücklhorn/Unsplash
Notes: So what exactly is Geo-X? At its core, Geo-X is an open-source geospatial modelling framework that estimates the cost of producing and delivering low-carbon commodities – from every possible production location in a territory to one or more specified demand centres. The framework integrates three key dimensions. First, geolocation: it uses spatial data to characterise each point in the territory – its renewable resource potential, its distance to roads or water sources, and land availability constraints. Second, the optimised technology mix: it optimises the combination of generation, storage, and conversion technologies at each location. Third, it calculates levelised costs: the full cost per kilogram of commodity delivered, allowing direct comparison across locations and scenarios. The result is a spatially explicit picture of where production is competitive and where it is not.

## Slide 6
How does Geo-X differ from other tools?
Geo-X analyses commodity production, with particular emphasis on:
The geospatial location of production and consumption.
Land availability, considering limitations for installing energy infrastructure, e.g. slope constraints and the exclusion of nature reserves and other protected areas.
Typical energy-system modelling tools emphasise:
The system-level impact of including generation and consumption agents, e.g. the impact of large-scale H₂ deployment on power systems.
Interactions among multiple energy carriers across the wider energy system.
Geo-X does not replace other tools;
instead, it complements them.
Notes: A question that often comes up is: how does Geo-X differ from other energy modelling tools? The key distinction lies in the level of analysis. Geo-X is a plant-level, location-specific tool. It asks: given a specific site, what would it cost to build and operate a production facility there and deliver the commodity to a given demand point? It pays close attention to land availability constraints – for example, excluding areas with steep slopes or protected reservoirs – and to the spatial relationship between production and demand. By contrast, typical energy system models, such as PyPSA-Europe or OSeMOSYS, focus on the system level. They model how generators, grids, and consumers interact across a whole network and capture system-wide operational effects like the impact of large-scale hydrogen deployment on power system operation. These are genuinely different questions, and they require different tools. Geo-X does not replace system models – it complements them. A common workflow is to use Geo-X to identify competitive production zones and then feed those insights into a system model for broader integration analysis.

## Slide 7
Table of contents
The policy problem
Introduction to Geo-X
What Geo-X is not
What you will learn in this course
How Geo-X works: three optimisations
Commodities supported by Geo-X: hydrogen modelling
Outputs
Real applications
Commodities supported by Geo-X: ammonia modelling
Notes: This slide marks a transition in the lesson. Having introduced the policy motivation and the positioning of Geo-X relative to other tools, we now go deeper into what Geo-X actually does and produces. We will look at the three components of its optimisation framework, the commodities it currently supports, the outputs it generates, and some concrete examples of where it has been applied. This is the technical heart of the lesson.

## Slide 8
Geo-X is a mathematical-optimisation tool built on the PyPSA framework. Three aspects are optimised: production, transport, and supply-demand balancing.
Production optimisation
Transport optimisation
Supply–demand balancing
Geo-X minimises production costs based on the CAPEX and OPEX invested across different production segments:
Mix of available power technologies, e.g. solar photovoltaic, wind turbines, hydropower.
Links between energy carriers, e.g. electrolysers, Haber–Bosch synthesis, fuel cells.
Storage facilities, e.g. Li-ion batteries, compressed hydrogen.
Geo-X minimises transport costs based on the CAPEX and OPEX of different transport strategies:
Transport alternatives, e.g. trucking, pipelines.
Conversion costs, e.g. conversion of hydrogen to ammonia.
Geo-X meets demand while considering:
Time-step resolution, e.g. hourly or 4-hour intervals.
Demand flexibility – certain degree of flexibility can be considered depending on the characteristics of the demand.
How Geo-X works: three optimisations
Notes: Let us now look more closely at the mathematical engine behind Geo-X. The framework is built on PyPSA – an open-source energy system modelling library – and it optimises three interconnected aspects of commodity production. The first is production optimisation: for each location, Geo-X finds the lowest-cost combination of power generation technologies, such as solar, wind, or hydropower, together with storage and conversion equipment like electrolysers or Haber-Bosch synthesis units. It minimises the total capital and operating expenditure of this production system. The second is transport optimisation: once production costs are known, Geo-X finds the cheapest way to move the commodity from the production site to the demand centre, choosing between options such as trucking and pipelines, and accounting for any conversion steps along the way. For instance, converting hydrogen into ammonia to reduce transport costs. The third aspect is supply-demand balancing: the model meets a specified annual demand, with a defined time resolution, typically hourly, and can accommodate a degree of demand flexibility where the end use allows it. Together, these three components give you the full levelised cost of delivering the commodity to the demand point. The three blocks are solved together, not sequentially - production, transport and supply-demand balancing are all part of the same cost-minimisation problem.
Acronyms on this slide: PyPSA = Python for Power System Analysis (the open-source framework Geo-X is built on); CAPEX = capital expenditure (up-front investment); OPEX = operating expenditure (running costs); NPV = net present value.

## Slide 9
Commodities supported by Geo-X: hydrogen modelling
The current version of Geo-X considers hydrogen and ammonia as the primary commodities integrated into the model. Critical minerals such as copper are handled by Geo-MinX, a companion spatial techno-economic framework built on Geo-X.
The diagram below illustrates a typical hydrogen supply chain model:
Notes: Geo-X currently supports three commodities. The first two, green hydrogen and green ammonia, are the most developed in the tool, and the focus of this course. The diagram on this slide illustrates the typical modelling chain for hydrogen: renewable electricity is generated, used to power an electrolyser to produce hydrogen, which is then compressed or converted and transported to the demand centre. Each step in this chain contributes to the final levelised cost, and Geo-X optimises the entire chain simultaneously for every location in the territory. Copper production is also supported, through a related tool called Geo-MinX, which applies the same geospatial framework to mining and processing, including off-grid, hybrid, and grid-connected electricity supply scenarios. This extensibility is a key design feature of Geo-X: the codebase is modular, making it possible to add new commodities in the future.
Geo-MinX belongs to a class of purpose-built modeling tools that merge location-based data with economic analysis, with the goal of streamlining how minerals are processed and moved through supply chains. Its main uses include estimating how much renewable energy a project will need and pinpointing the most cost-effective locations to process critical minerals—copper being a key example. As part of a larger ecosystem, Geo-MinX sits within the Geo-X GitHub repository, a project that leverages the Snakemake workflow system to automatically generate levelised cost (LC) estimates across different commodities.
Acronyms on this slide: PPA = power purchase agreement

## Slide 10
Commodities supported by Geo-X: ammonia modelling
The diagram below shows a typical model for the ammonia supply chain:
Notes: For ammonia, the modelling chain extends the hydrogen pathway. Green hydrogen is produced via electrolysis, and then synthesised into ammonia using the Haber-Bosch process, which requires nitrogen from an air separation unit and additional electricity. The resulting ammonia can be transported as a liquid at moderate pressure, which is often cheaper than transporting compressed hydrogen over long distances. At the demand end, ammonia can either be used directly, for example, as a fertiliser feedstock or as a shipping fuel, or cracked back into hydrogen if the end user requires hydrogen. Geo-X models all of these steps, allowing you to compare the full delivered cost of ammonia versus hydrogen for a given demand centre and geography.

## Slide 11
Outputs
The commodity production architecture is applied across the entire study area, identifying the production cost and technological mix.
modelling architecture (e.g. hydrogen)
geospatial cost of production
technological mix per location
Notes: The key output of Geo-X is a set of spatially explicit cost maps. Once the optimisation has been run for every hexagonal cell in the territory – each one representing a potential production site – the results are assembled into two main forms. The first is a geospatial heatmap showing the levelised cost of production and delivery across the entire territory. This allows you to immediately identify where production is cheapest and how costs vary with distance to demand or renewable resource quality. The second is a breakdown of the cost components – energy, storage, conversion, transport – which tells you which factors are driving costs in different regions. These outputs are designed to be directly useful for policy analysis: they can inform infrastructure prioritisation, competitiveness assessments, and scenario comparisons.
The stacked bars show which cost components (generation, electrolysis, storage, water, transport) make up the LCOH at each location, so the dominant cost driver can be read off directly.

## Slide 12
Real applications
Suited to policy analysis, academic research, and applied decision-making:
  Production siting; supply scenarios; regional competitiveness comparisons; identification of low-cost production corridors
Policy questions it can support:
Where should infrastructure be prioritised?
How does the region compare with international benchmarks?
How do cost assumptions affect industrial strategy?
How can financial instruments affect production costs?
Where are the best locations for green industrial hubs?
Research questions it can answer:
Where is production cheapest?
Which cost component dominates?
How sensitive are costs to demand location?
How sensitive are results to technology cost assumptions?
Which transport option is most cost-effective?
Notes: Geo-X has already been applied in a range of policy and research contexts. On the policy side, it is well-suited to questions like: where should infrastructure investment be prioritised? How does a country's production potential compare to international benchmarks? How sensitive is the business case to changes in cost assumptions or financing conditions? Where are the most promising locations for green industrial hubs? On the research side, Geo-X helps answer questions about which cost components dominate in a given context, how sensitive results are to the location of demand centres, and which transport option – trucking or pipeline – is economically optimal at different scales. Published applications include case studies in Namibia for hydrogen and ammonia, Zambia for copper, and Ukraine for green hydrogen and ammonia production under different financing scenarios. The Ukraine case study is particularly relevant to this course, as it draws directly on the methods you will be learning here.

## Slide 13
Table of contents
The policy problem
Introduction to Geo-X
What Geo-X is not
What you will learn in this course
Scope and limitations of the tool
Notes: We now turn to an equally important part of understanding any modelling tool: its limitations. Knowing what a tool does not do is essential for interpreting results correctly and avoiding misuse. The next slide describes the key scope boundaries of Geo-X.

## Slide 14
Scope and limitations of the tool
Geo-X emphasises the modelling of locational aspects:
It does not consider system integration: power generation does not interact with the existing power system, so there are no sales of excess electricity and no purchases during periods of scarcity.
There is no explicit modelling of existing energy networks.
Results are sensitive to the input data and cost assumptions used.
Notes: Geo-X is designed with a clear and deliberate scope, and it is important to understand what lies outside it. First, Geo-X focuses on the localised cost of commodity production, it does not model system integration. This means it does not capture how large-scale hydrogen production might affect the broader power system, or how existing generation assets might interact with new green commodity plants. Second, there is no explicit modelling of existing electricity networks. Power generation in Geo-X is treated as newly built, off-grid infrastructure for most commodities – any excess electricity is assumed to be curtailed rather than exported. Third, results are sensitive to the input assumptions you provide – cost projections, technology parameters, interest rates, and demand locations all affect the outputs significantly. This is not a weakness unique to Geo-X, but it means that scenario analysis and sensitivity testing are essential parts of any credible application. Taken together, these boundaries mean that Geo-X is best understood as a screening and siting tool – a way of identifying where production is likely to be competitive – rather than a tool for detailed system planning.

## Slide 15
Table of contents
The policy problem
Introduction to Geo-X
What Geo-X is not
What you will learn in this course
Course roadmap
Quizzes and hands-on exercises
Notes: Before we close this lesson, let’s look ahead at the full course. You have just completed Lesson 1, which gave you the conceptual foundation for everything that follows. The remaining five lessons will take you from installation all the way to advanced applications.

## Slide 16
Course roadmap
This course consists of six lessons. The remaining lessons are:
Lesson 2: Software setup
Lesson 3: Data inputs
Lesson 4: Running the model
Lesson 5: Interpreting the results
Lesson 6: Advanced options
Notes: Here is the full course roadmap. Lesson 2 covers software setup: you will clone the repository, configure your environment, and run a basic verification example. Lesson 3 introduces data inputs: you will learn about the spatial hexagon files, the techno-economic parameter spreadsheets, and the configuration file that controls the model runs. Lesson 4 takes you through running the model: executing the Snakemake workflow, troubleshooting common issues, and designing scenarios. Lesson 5 focuses on interpreting results: reading the heatmaps, understanding cost breakdowns, and constructing supply curves. And Lesson 6 introduces advanced options, including incorporating new technologies and applying the framework to other commodities. Each lesson builds on the previous one, so we recommend working through them in order.

## Slide 17
Quizzes and hands-on exercises
Enjoy the course.
After each lesson, you will complete a quiz of 6 to 10 questions to check your understanding of the key points.
From Lesson 2 onwards, each lesson also includes a hands-on exercise.
Note: Figures and graphics throughout this course were produced by the authors, generated either through custom Python code or with the assistance of Claude AI.
Notes: At the end of this lesson, and each lesson that follows, you will find a short quiz of six to ten questions. These are designed to help you check your understanding before moving on. From Lesson 2 onwards, there is also a hands-on exercise – a set of practical challenges – that will take your Geo-X skills beyond the slides and into real modelling work. We hope you find the course both useful and engaging. If you have any questions as you work through the material, please use the course discussion forum. Good luck and enjoy the course.

## Slide 18: Thank you
www.climatecompatiblegrowth.com
Notes: Thank you for completing Lesson 1 of the Geo-X training course. You now have a solid conceptual understanding of what Geo-X is, how it works, and where it fits in the landscape of energy modelling tools. In Lesson 2, we will get practical: you will set up the software environment and run your first example. We look forward to seeing you there.